BOREAS AFM-04 Twin Otter Aircraft Flux Data

Summary

The BOREAS AFM-04 team used the NRC Twin Otter aircraft in 1994 and 1996 to make measurements in the boundary layer of the fluxes of sensible and latent heat, momentum, ozone, methane, and carbon dioxide, plus supporting meteorological parameters such as temperature, humidity, and wind speed and direction.  Aircraft position, heading, and altitude were also recorded, as were several radiometric observations for use in interpretation of the data (greenness index, surface temperature, incoming and reflected radiation).  Data were collected at both the NSA and SSA during the three 1994 IFCs and in July and August of 1996.  These data are stored in tabular ASCII files.

Table of Contents

*  1 Data Set Overview

*  2 Investigator(s)

*  3 Theory of Measurements

*  4 Equipment

*  5 Data Acquisition Methods

*  6 Observations

*  7 Data Description

*  8 Data Organization

*  9 Data Manipulations

*  10 Errors

*  11 Notes

*  12 Application of the Data Set

*  13 Future Modifications and Plans

*  14 Software

*  15 Data Access

*  16 Output Products and Availability

*  17 References

*  18 Glossary of Terms

*  19 List of Acronyms

*  20 Document Information

1. Data Set Overview

1.1 Data Set Identification

BOREAS AFM-04 Twin Otter 1994 Aircraft Flux Data

1.2 Data Set Introduction

The BOReal Ecosystem-Atmosphere Study (BOREAS) Airborne Fluxes and Meteorology (AFM)-04 team used the National Research Council (NRC) Twin Otter aircraft in 1994 and 1996 to make measurements in the boundary layer of the fluxes of sensible and latent heat, momentum, ozone, methane, and carbon dioxide, plus supporting meteorological parameters such as temperature, humidity, and wind speed and direction.  Aircraft position, heading, and altitude were also recorded, as were several radiometric observations for use in interpretation of the data (greenness index, surface temperature, incoming and reflected radiation).  Data were collected at both the Northern Study Area (NSA) and Southern Study Area (SSA) during the three 1994 IFCs and in July and August of 1996.  These data are stored in tabular American Standard Code for Information Interchange (ASCII) files.

1.3 Objective/Purpose

The Twin Otter was one of four flux aircraft operated in BOREAS.  The purpose of its flights was to make measurements in the boundary layer of the fluxes of sensible and latent heat, momentum, ozone, methane, and carbon dioxide, plus supporting meteorological parameters such as temperature, humidity, and wind speed and direction.  Aircraft position, heading, and altitude were also recorded, as were several radiometric observations for use in interpretation of the data (greenness index, surface temperature, incoming and reflected radiation).  These data will be used to attempt to relate boundary layer processes (atmosphere/vegetation exchanges) to radiometric data available from satellites, i.e., ground truthing of satellite data.  Through this research, it is hoped that techniques can be developed to utilize satellite data for global monitoring of climate change.

1.4 Summary of Parameters

Temperature, Dewpoint Temperature, Pressure, Downwelling Radiation, Upwelling Radiation, Greenness Index, Three Orthogonal Components of the Wind Velocity, Along-Wind Component, Across Wind Component, H2O Mixing Ratio, CO2 Mixing Ratio, Ozone Concentration, Methane, Sensible Heat Flux, Latent Heat Flux, Momentum Flux, Carbon Dioxide Flux, Ozone Flux, Methane Flux, Aircraft Position, Heading, Altitude (Radar and Pressure), Surface Temperature, Satellite Simulator

1.5 Discussion

The Twin Otter operated in all three Intensive Field Campaign (IFCs) in 1994.  In 1994 the aircraft made 57 flights, including 1100 flux runs. In 1996, a total of 27 project flights were made.  The recorded data rate was increased from 16 Hz (as in 1994) to 32 Hz (for 1996), improving the resolution of the data contributing to the flux estimates.  The archived data were collected on straight and level flux runs over the BOREAS site and on regional runs between Prince Albert and Thompson and in each project area.  A variety of flight profiles are possible (grids, L- patterns, profiling stacks, soundings), which are described in Section 7.3.  The archive data include run-averaged data, focusing on the fluxes and the supporting meteorological, radiometric, and aircraft positional data.  No attempt was made to archive the high-rate (16-Hz or 32-Hz) data, which can be acquired from NRC directly, if required.

There was a significant difference in the instrumentation configuration on the Twin Otter for 1996 when compared with the 1994 campaign.  It carried additional cloud physics and aerosol instruments belonging to the Atmospheric Environment Service (AES).  These additional data are not included in this data set.  Please consult MacPherson (1996) and MacPherson and Bastian (1997) for detailed information about the instrument configurations in 1994 and 1996.

1.6 Related Data Sets

BOREAS AFM-01 NOAA/ATDD Long-EZ 1994 Aircraft Flux Data over the SSA

BOREAS AFM-02 Wyoming King Air 1994 Aircraft Flux and Moving Window Data

BOREAS AFM-03 NCAR Electra 1994 Aircraft Flux Data

BOREAS AFM-03 NCAR Electra 1994 Aircraft Moving Window Data

BOREAS AFM-04 NRC Twin Otter Aircraft Sounding Data

BOREAS AFM-05 Level-1 Upper Air Network Data

BOREAS AFM-05 Level-2 Upper Air Network Standard Pressure Level Data

2. Investigator(s)

2.1 Investigator(s) Name and Title

J. Ian MacPherson

Flight Research Laboratory

Institute for Aerospace Research

National Research Council of Canada

Ottawa, Ontario

Canada

Raymond L. Desjardins

Centre for Land and Biological Resources Research

Agriculture Canada

Central Experimental Farm

Ottawa, Ontario

Canada

2.2 Title of Investigation

Atmospheric Boundary Layer Analyses from Canadian Twin Otter Aircraft

2.3 Contact Information

Contact 1

----------

J. Ian MacPherson

National Research Council

Ottawa, Ontario

Canada

(613) 998-3014

(613) 952-1704 (fax)

jim@u614ji.iar.nrc.ca

Contact 2

----------

David Knapp

Raytheon ITSS

NASA GSFC

Greenbelt, MD

(301) 286-1424

(301) 286-0239 (fax)

David.Knapp@gsfc.nasa.gov

3. Theory of Measurements

A series of reports addressing the theory and practice of measuring atmospheric variables from a moving, aircraft platform may be found in MacPherson (1981, 1988, 1990a, 1990b, 1992, 1996) and MacPherson and Bastian (1997).

A basic requirement for measuring gas fluxes from a moving aircraft is to account for the motion of the air relative to the motion of the aircraft.  The true air motion is derived from the vector difference between the air velocity relative to the aircraft velocity relative to the ground.

Air motion relative to the aircraft is measured by a nose-mounted gust boom incorporating a Rosemount 858AJ28 5-hole probe.  This device and the associated pressure transducers measure static pressure (altitude), dynamic pressure (airspeed) and the angles of attack and sideslip.  These instruments in combination with a global positioning system (GPS) and an inertial reference system (IRS) are used to derive the flux measurements.

4. Equipment

4.1 Sensor/Instrument Description

The Twin Otter atmospheric research aircraft is a highly instrumented platform for research on the atmospheric boundary layer, air pollution, etc.  Descriptions of the aircraft and its instrumentation and software are given in detail in MacPherson (1981, 1988, 1990a, 1990b, 1996) and MacPherson and Bastian (1997).

The instruments used to make these measurements included:

Parameter              Instrument

Sensible Heat         Rosemount fast response 102DJ1CG

Incident Solar Rad.   Kipp and Zonen CM-11 pyranometer (305-2800 nm range)

Reflected Solar Rad.  Eppley pyranometer

Greenness Index       Skye Industries Vegetation Greenness Indicator

Surface Temperature   Barnes PRT-5 infrared radiometer

Satellite Simulation  Exotech 100BX Satellite Simulator

CO2, H2O               LI-COR LI-6262 CO2/H2O analyzer (these CO2 data reported to

BORIS)

ESRI (developed by Agriculture Canada)

Dew Point             E, G, and G Model 137-S10 Cambridge dew point sensor

Ozone                 TECO Ozone Analyzer Model 49 (these O3 data reported to

BORIS)

GFAS (unit borrowed from German Aerospace Research

Establishment)

Scintrex LOZ-3 ozone detector

Momentum              Wind Components

Inertial Velocity     Litton LTN-90-100 Inertial Reference System

Position              Trimble Model TNL-7880SR GPS/VLF/Omega

Altitude (AGL)        Sperry AA-200 Radio Altimeter (1994 and 1996)

Riegl LD-90-3 Laser Altimeter (1996 only)

4.1.1 Collection Environment

The data were collected from the aircraft, flying at various altitudes.

4.1.2 Source/Platform

Twin Otter DHC-6-200 twin turboprop utility transport.

Maximum gross takeoff weight 11,579 lb. Service ceiling 20,000 ft. Endurance 3 to 4 hours, depending on instrumentation and weather.

4.1.3 Source/Platform Mission Objectives

The primary objective was to measure the vertical flux of sensible and latent heat, CO2, ozone, methane, and momentum for scaling up surface-based measurements to regional scales.  The ultimate objective is to develop algorithms to relate boundary layer processes to satellite-derived data.

4.1.4 Key Variables

Temperature, Dewpoint Temperature, Pressure, Downwelling Radiation, Upwelling Radiation, Greenness Index, Three Orthogonal Components of the Wind Velocity, Along-Wind Component, Across Wind Component, H2O Mixing Ratio, CO2 Mixing Ratio, Ozone Concentration, Methane, Sensible Heat Flux, Latent Heat Flux, Momentum Flux, Carbon Dioxide Flux, Ozone Flux, Methane Flux, Aircraft Position, Heading, Altitude (Radar and Pressure), Surface Temperature, Satellite Simulator

4.1.5 Principles of Operation

A basic requirement for measuring gas fluxes from a moving aircraft is to account for the motion of the air relative to the motion of the aircraft.  The true air motion is derived from the vector difference between the air velocity relative to the aircraft velocity relative to the ground.

Air motion relative to the aircraft is measured by a nose-mounted gust boom incorporating a Rosemount 858AJ28 5-hole probe.  This device and the associated pressure transducers measure static pressure (altitude), dynamic pressure (airspeed) and the angles of attack and sideslip.  These instruments in combination with a global positioning system (GPS) and an inertial reference system (IRS) are used to derive the flux measurements.

The principles of operation of the aircraft and its other instrumentation and software are given in detail in MacPherson (1981, 1988, 1990a, 1990b, 1996) and MacPherson and Bastian (1997).

4.1.6 Sensor/Instrument Measurement Geometry

See MacPherson (1988, 1990a, 1990b, 1996) and MacPherson and Bastian (1997).

4.1.7 Manufacturer of Sensor/Instrument

See Sections 4.1 and 6, and MacPherson (1988, 1990a, 1996) and MacPherson and Bastian (1997).

4.2 Calibration

Instruments on the aircraft were calibrated prior to each IFC.  Key instruments (such as temperature probes) were calibrated two or three times during each IFC.

4.2.1 Specifications

Not available.

4.2.1.1 Tolerance

Not available.

4.2.2 Frequency of Calibration

All instruments were calibrated at least once per IFC.

4.2.3 Other Calibration Information

See MacPherson (1988, 1990a, 1990b, 1996) and MacPherson and Bastian (1997).

5. Data Acquisition Methods

There were several types of flight profiles.  These are described in MacPherson (1988, 1990a, 1996) and MacPherson and Bastian (1997).  Plotted flight tracks are shown for every flight.  One hundred and twenty-eight channels of data are recorded digitally in 16-bit words at 16 samples per second (1994) or 32 samples per second (1996) on a Digital Archive Tape (DAT) Drive.  Most signals are low-pass filtered with a breakpoint of 5 Hz to prevent aliasing.

Fluxes are calculated using the procedures detailed in MacPherson (1990b, 1996, 1997).  It should be noted that in the final submission to the BOREAS Information System (BORIS), three sets of flux and root mean square (RMS) data were submitted.  The first used untreated time histories in the derivation of fluxes using the eddy correlation technique, the second used linearly detrended data, and the third used time histories that were high-pass filtered with a third-order algorithm with a break point set at 0.012 Hz (5 km wavelength).  It is felt that most scientists working with these data would prefer to use the linearly detrended data.  Data from the National Center for Atmospheric Research (NCAR) and University of Wyoming King Air aircraft were archived with the identical formats.

6. Observations

6.1 Data Notes

None.

6.2 Field Notes

Note: 128 channels of data are recorded digitally in 16-bit words at 16

samples per second on a DAT drive.  Signals are low-pass filtered with a breakpoint of 5 Hz to prevent aliasing.

The following table lists the 128 recorded signals.  Not all of these are archived to BORIS (see Section 8), but many contribute to calculated quantities such as true airspeed, wind velocity, fluxes, etc.

**Note:***  This is basically the recorder buffer to be used in the site visit in May 1993.  Additional parameters were recorded in BOREAS (e.g., satellite simulator).  A Trimble global positioning system (GPS) replaced or augmented the Loran-C in 1994.

Channel Number Variable Name Units  Recorded   Instrument   Description

Resolution (per bit)

__________________________________________________________________________

1 FILEHR HRS 1 NAE CLOCK COMBINED WORD, TAPE FILE AND GMT HOURS.

2 MINSEC  MIN/SEC      1      NAE CLOCK             COMBINED WORD,

GMT MINUTES/ SECONDS.

3 EVENT       -        1      EVENT MARKER         MULTI LEVEL

EVENT MARKER

4 LTD DEG 1 ARNAV LORAN-C | LATITUDE DEGREES

5 LTM MIN 0.01 MODEL 40-AVA-100 | LATITUDE MINUTES

6 LGD DEG 1 "" | LONGITUDE DEGREES

7 LGM MIN 0.01 "" | LONGITUDE MINUTES

8 LTML MIN 0.01 LITTON INERTIAL REF | LATITUDE MINUTES

9 LGML MIN 0.01 SYSTEM, LTN-90-100 | LONGITUDE MINUTES

10 HDGT DEG 0.1 SPERRY C-12 GYRO TRUE HEADING

(MAGNETIC HEADING CORRECTED TO TRUE HEADING USING MAG VARIATION OUTPUT

FROM LORAN-C)

11 HDGTL        DEC      0.1     LITTON 90 IRS      TRUE HEADING, LITTON

12 WDTI           DEG      0.1      * DERIVED*        WIND DIRECTION     FROM   DOPPLER/ INERTIAL SYSTEM, DEGREES TRUE ( NOTE 1)

13 WDTL      DEG      0.1      * DERIVED*          FROM LITTON SYSTEM

(SEE NOTE 2)

14 WSMI M/S 0.01 * DERIVED* WIND SPEED FROM DOPPLER INERTIAL SYSTEM ( NOTE 1)

15 WSML      M/S     0.01      * DERIVED*          FROM LITTON SYSTEM

(SEE NOTE 2)

16 UGE M/S 0.01 * DERIVED* NORTH/SOUTH WIND COMPONENT FROM DOPPLER/INERTIAL

SYSTEM, + FROM N

17 VGE     M/S       0.0             * DERIVED*     EAST/WEST, + FROM EAST

18 WGE     M/S       0.0             * DERIVED*     VERTICAL WIND, + UP

19 LWN     M/S       0.0             * DERIVED*

NORTH/SOUTH WIND COMPONENT FROM LITTON SYSTEM, (NOTE 2), + FROM N

20 LWE     M/S       0.01            * DERIVED*          EAST/WEST WIND

COMPONENT, + FROM E

21 WEP     M/S       0.01            * DERIVED* VERTICAL WIND COMPONENT

22 TSNBC DEG C 0.01 * DERIVED* STATIC TEMPERATURE, DERIVED FROM TAS &

TOTAL TEMP (SEE CH 48) NOSE STARBOARD TEMPERATURE PROBE

23 DEWPTC     DEG C   0.01     EGG MODEL 137          DEW POINT

24 SDCTC      DEG C   0.01      * DERIVED*       STATIC TEMPERATURE     IN C02 ANALYZER DUCT, DERIVED FROM DUCT TAS & DUCT TOTAL TEMP; ROSEMOUNT

102 PROBE

25 PRT5C         DEG C   0.01      BARNES PRT-5         SURFACE TEMPERATURE

26 RADUP        W/M2     0.1       KIPP & ZONEN CM-11   UPWARD FACING     RADIOMETER, MEASURES INCIDENT RADIATION (SEE ALSO NOTE 3)

27 RADOWN    W/M2     0.1     EPPLEY PYRANOMETER-2 DOWNWARD FACING

RADIOMETER, MEASURES REFLECTED RADIATION.

28 C02N02    MG/M3    0.1     AGRICULTURE CANADA    CARBON DIOXIDE CONC

ESRI C02/H20 ANALYZER 20 HZ RESPONSE, LOW PASS FILTERED AT 5.5 HZ FOR

ANTI-ALIASING

29 H20       G/M3            0.01      C02/H20 ANALYZER     WATER VAPOR

CONC, ESRI

30 RALT       M  0.1         SPERRY AA-200 RADIO  HEIGHT ABOVE GROUND ALTIMETER

31 TASFK KTS 0.1 * DERIVED* TRUE AIRSPEED, FUSELAGE PROBES.

32 TASNBK KTS 0.1 * DERIVED* TRUE AIRSPEED, NOSEBOOM PROBES.

33 TASDCT KTS 0.1 * DERIVED* TRUE AIRSPEED IN C02/H20 ANALYZER DUCT.

34 PSDUCT     MB      0.1     A.I.R. AIR-DB-2C    STATIC PRESSURE IN DUCT.

35 PSNBC MB 0.1 PAROSCIENTIFIC STATIC PRESSURE 215L-AW-012     NOSEBOOM,

CORRECTED FOR POSITION ERROR

36 TSFC    DEG C     0.01      * DERIVED*         STATIC TEMPERATURE,

DERIVED FROM TAS AND TOTAL TEMP MEASURED BY FUSELAGE PORT ROSEMOUNT PROBE

(SEE CHANNEL 47)

37 GRNRAT      -    0.001     SKYE INDUSTRIES    GREENNESS RATIO, 730

SKR-100            NM SIGNAL/660 NM SIGNAL.

38 VDTM      M/S      0.1     DECCA DOPPLER      GROUND SPEED, TOTAL

RADAR-72         VECTOR FROM DOPPLER RADAR.

39 GSL       KTS      0.1     LITTON 90 IRS      GROUND SPEED, TOTAL

VECTOR FROM LITTON

40 LCC02 MV 1.0 LICOR 6262 C02 CONCENTRATION, RECORDED AS MILLIVOLTS,

CONVERTED TO PPM

41 LCTSC    DEG C    0.01     LICOR 6262         TEMPERATURE IN LICOR

ANALYZER TEST CELL

42 UGEIL M/S 0.01 * DERIVED* NORTH/SOUTH WIND COMPONENT FROM DOPPLER/LITTON

SYSTEM, + FROM N.

43 VGEIL          M/S      0.01        * DERIVED*     EAST/WEST, + FROM E.

44 WGEIL         M/S      0.01        * DERIVED*     VERTICAL WIND, + UP

45 LCH20     MV       1.0      LICOR 6262          H20 CONCENTRATION

RECORED AS MILLIVOLTS, CONVERTED TO PPT

46 WFIL      M/S     0.01      *DERIVED*         HIGH-PASS FILTERED

VERTICAL WIND FOR EDDY ACCUMULATION SYSTEM

47 TTF      DEG K    0.01     ROSEMOUNT 102DJ1CG   TOTAL TEMPERATURE,

FAST RESPONSE, PORT FUSELAGE PROBE

48 TTNB     DEG K    0.01     ROSEMOUNT 102DJ1CG   TOTAL TEMPERATURE,

FAST RESPONSE, STAR'B FUSELAGE PROBE

49 PSFC      MB       0.1     ROSEMOUNT 1201F1B4A1B  STATIC PRESSURE,

FUSELAGE PORTS, CORRECTED FOR POSITION ERROR.

50 METHAN    PPB      1.0     UNISEARCH TDL         METHANE CONCENTRATION

METHANE ANALYZER

51 -- --- NOT USED

52 TECO PPB 0.1 TECO-49 OZONE OZONE CONCENTRATION ANALYZER SLOW RESPONSE  FOR MEAN CONCENTRATIONS

53 OZD       PPB      0.1     GERMAN OZONE ANALYZER  OZONE CONCENTRATION

GFAS OS-G-2 FAST RESPONSE (>10 HZ)

54 DOZD PPB 0.01 "" HI-SENSITIVITY OZONE FLUCTUATIONS FROM START OF FLUX RUN

55 UCO2N2   MG/M3    0.1     AGRICULTURE CANADA     RAW C02 UNFILTERED

SIGNAL C02/H20 ANALYZER

56 UH20N2 G/M3 0.01 AGRICULTURE CANADA RAW H20 UNFILTERED SIGNAL C02/H20

ANALYZER

57 THETAL DEG 0.01 LITTON-90 IRS PITCH ATTITUDE + NOSE UP

58 PHIL DEG 0.01 LITTON-90 IRS ROLL ATTITUDE + RIGHT WING DOWN

59 VXMLTN M/S 1/128 DECCA DOPPLER RADAR-72 ALONG-HEADING COMPONENT OF GROUND

SPEED, POSITIVE FORWARD.

60 VYMLTN    M/S    1/256    DECCA DOPPLER RADAR-72   ACROSS-HEADING

COMPONENT OF GROUND SPEED, POSITIVE STARBOARD

61 VZMLTN    M/S    1/512    DECCA DOPPLER RADAR-72  VERTICAL COMPONENT

OF AIRCRAFT VELOCITY REL TO GROUND, + DOWN. (ABOVE 3 CORRECTED TO POSITION

OF LITTON-90 IRS).

62 ULN       M/S     0.01    LITTON-90 IRS         NORTH/SOUTH INERTIAL

VELOCITY, + TO NORTH.

63 VLE      M/S     0.0         LITTON-90 IRS EAST/WEST, + TO EAST

64 WZL      M/S     0.0         LITTON-90 IRS  VERTICAL, + DOWN

65 PDF      MB      0.01        ROSEMOUNT TRANSDUCER    DYNAMIC PRESSURE     1221F-2VL7A1A  FUSELAGE PITOT UNCORRECTED FOR P.E.

66 PDNB      MB      0.01    ROSEMOUNT TRANSDUCER  DYNAMIC PRESSURE

1221F-1V7A1B   NOSEBOOM PITOT UNCORRECTED FOR P.E.

67 PSF       MB      0.10    ROSEMOUNT TRANSDUCER  STATIC PRESSURE,

1201F-1B4A1B    FUSELAGE PORTS, UNCORRECTED FOR P.E.

68 PSNBLR    MB      0.10    PAROSCIENTIFIC         STATIC PRESSURE

215L-AW-012     NOSEBOOM, CORRECTED TO LAB STANDARD, UNCORRECTED FOR P.E.

69 PD        MB      0.01    *DERIVED*             DYNAMIC PRESSURE USED

(PDNB OR PDF) IN REAL TIME SOFTWARE SELECTED BY FUNCTION SWITCH

70 PDFNB     MB      0.01    *DERIVED*             DYNAMIC PRESSURE FROM

FUSELAGE PORT CORRECTED TO NOSEBOOM POSITION, USED AS PDNB BACKUP

71 EACONT    BITS     1.0    *DERIVED*             SIGNAL THAT CONTROLS

EDDY ACCUMULATION SYSTEM,1000 WHEN WFIL IS UP -1000 WHEN WFIL IS DOWN ZERO

IN DEAD ZONE

72 TS        DEGC    0.01	*DERIVED*             STATIC TEMP USED IN REAL

(TSFC OR TSNBC)         TIME SOFTWARE, SELECTED BY FUNCTION SWITCH

73 GRN660 - 0.01 SKYE INDUSTRIES 660 NM SIGNAL FROM SKR-100 GREENNESS DEVICE

74 GRN730 - 0.01 SKYE INDUSTRIES 730 NM SIGNAL FROM SKR-100 GREENNESS DEVICE

75 TSPARO DEGF 0.01 PAROSCIENTIFIC TRANSDUCER TEMPERATURE 215L-AW-012

USED TO CORRECT STATIC PRESSURE SIGNAL

76 WGAI       M/S     0.01     *DERIVED*             VERTICAL WIND, DOPPLER

SYSTEM, A/C AXES

77 LALT FT 1.0 LITTON 90/100 IRS ABSOLUTE HEIGHT

78 PALT FT 1.0 *DERIVED* PRESSURE HEIGHT, USES PSNBC

79 LTDL DEG 1.0 LITTON 90/100 IRS LITTON LATITUDE, DEG ONLY

80 LTDL DEG 1.0 "" LITTON LONGITUDE, DEG ONLY

81 PDFC MB 0.01 ROSEMOUNT TRANSDUCER DYNAMIC PRESSURE 1221F-2VL7A1A

FUSELAGE PITOT CORRECTED FOR P.E.

82 PDNBC       MB     0.01   ROSEMOUNT TRANSDUCER  DYNAMIC PRESSURE

1221F-1V7A1B   NOSEBOOM PITOT CORRECTED FOR P.E.

83 VX       KNOTS   0.10  DECCA DOPPLER RADAR-72  GROUND SPEED, X COMPONENT

A/C AXES, + FORWARD

84 VY KNOTS 0.10 "" GROUND SPEED, Y COMPONENT A/C AXES, + TO STARBOARD

85 VX KNOTS 0.10 "" GROUND SPEED, Z COMPONENT A/C AXES, + DOWN

86 THETA DEG 0.01 KEARFOTT ATTITUDE PITCH ATTITUDE GYRO, T2109 + NOSE UP

87 PHI DEG 0.01 KEARFOTT ATTITUDE ROLL ATTITUDE GYRO, T2109 + RIGHT WIND DOWN

88 AZL M/S2 0.01 LITTON 90/100 IRS VERTICAL ACCELERATION, A/C AXES,+ A/C DOWN

89 EAZL M/S2 0.01 "" VERTICAL ACCELERATION EARTH AXES, +A/C DOWN

90 UAIRN     M/S    1/128      *DERIVED*            NORTH COMPONENT OF TRUE

AIRSPEED (TAS) VECTOR

91 VAIRE M/S 1/128 *DERIVED* EAST COMPONENT OF TRUE AIRSPEED VECTOR

92 WAIRZ M/S 1/128 *DERIVED* VERTICAL COMPONENT OF TRUE AIRSPEED VECTOR,+ A/C

DOWN

93 UAIR     M/S       1/128     *DERIVED*    X-AXIS TAS      COMPONENT

94 VAIR     M/S       1/128     *DERIVED*    Y-AXIS TAS      COMPONENT

95 WAIR     M/S       1/128     *DERIVED*    Z-AXIS TAS      COMPONENT

96 UANAE    M/S       1/128     *DERIVED*    X-AXIS TAS      COMPONENT,     CORRECTED TO NAE ACCELEROMETER LOCATION

97 VANAE     M/S    1/128      *DERIVED*            Y-AXIS TAS COMPONENT,

CORRECTED TO NAE ACCELEROMETER LOCATION

98 WANAE     M/S    1/128      *DERIVED*            Z-AXIS TAS COMPONENT,

CORRECTED TO NAE ACCELEROMETER LOCATION

99 UALTN     M/S    1/128      *DERIVED*            X-AXIS TAS COMPONENT,

CORRECTED TO LITTON IRS LOCATION

100 VALTN     M/S    1/128      *DERIVED*            Y-AXIS TAS COMPONENT,

CORRECTED TO LITTON IRS LOCATION

101 WALTN     M/S    1/128      *DERIVED*            Z-AXIS TAS COMPONENT,

CORRECTED TO LITTON IRS LOCATION

102 UMIX7     M/S    1/128      *DERIVED*       X INERTIAL VELOCITY COMPONENT

FROM NAE/DOP SYSTEM

103 VMIX7 M/S 1/128 *DERIVED* Y INERTIAL VELOCITY COMPONENT FROM NAE/DOP

SYSTEM

104 WMIX7 M/S 1/128 *DERIVED* Z INERTIAL VELOCITY COMPONENT FROM NAE/DOP

SYSTEM

105 PDDUCT MB 0.01 ROSEMOUNT TRANSDUCER DYNAMIC PRESSURE IN C02 1221F-2VL7A1A

MEASUREMENT DUCT

106 ALPHA    DEG      0.01     ROSEMOUNT 858AJ28      ANGLE OF ATTACK PROBE &

12211F1VL5A1  MEASURED BY 5 TRANSDUCER   HOLE PROBE ON NOSEBOOM

107 BETA     DEG      0.01     ROSEMOUNT 858AJ28        ANGLE OF SIDE-PROBE &

12211F1VL5A1  SLIP MEASURED TRANSDUCER   BY 5 HOLE PROBE  ON NOSEBOOM.

108 UDOTN    M/S2    1/128      *DERIVED*            DERIVATIVE OF X INERTIAL

VELOCITY FROM NAE/DOP SYSTEM

109 VDOTN    M/S2    1/128      *DERIVED*            DERIVATIVE OF Y INERTIAL

VELOCITY FROM NAE/DOP SYSTEM

110 WDOTN    M/S2    1/128      *DERIVED*            DERIVATIVE OF Z INERTIAL

VELOCITY FROM NAE/DOP SYSTEM

111 UGAI      M/S     0.01       *DERIVED*         LONGITUDINAL WIND, DOPPLER

SYSTEM, A/C AXES

112 VGAI M/S 0.01 *DERIVED* LATERAL WIND, DOPPLER SYSTEM, A/C AXES

113 PALFNB MB 0.01 ROSEMOUNT TRANSDUCER DIFFERENTIAL PRESSURE 1221-1F1VL5A1

R-858 ANGLE OF ATTACK PORTS

114 UGAIL      M/S    0.01       *DERIVED*         LONGITUDINAL WIND, LIT/DOP

SYSTEM, A/C AXES

115 VGAIL M/S 0.01 *DERIVED* LATERAL WIND, LIT/DOP SYSTEM, A/C AXES

116 WGAIL M/S 0.01 *DERIVED* VERTICAL WIND, LIT/DOP SYSTEM, A/C AXES

117 AXL M/S2 0.01 LITTON 90/100 IRS LONGITUDINAL ACCELERATION, A/C AXES,

+ A/C FWD

118 AYL M/S2 0.01 LITTON 90/100 IRS LATERAL ACCELERATION, A/C AXES, + A/C

STARB

119 PBETNB MB 0.01 ROSEMOUNT TRANSDUCER DIFFERENTIAL PRESSURE 1221-1F1VL5A1

R-858 ANGLE OF SIDESLIP PORTS

120  AX       M/S2    0.01     SYSTRON DONNER 4211  LONGITUDINAL ACCELERATION,

A/C AXES, BACKUP SYSTEM

121 AY M/S2 0.01 SYSTRON DONNER 4211 LATERAL ACCELERATION, A/C AXES

122 AX M/S2 0.01 SYSTRON DONNER 4211 VERTICAL ACCELERATION, A/C AXES

123 PRATEL DEG/S 0.01 LITTON 90/100 IRS ROLL RATE, + RIGHT WING D

124 QRATEL DEG/S 0.01 "" PITCH RATE, + NOSE UP

125 RRATEL DEG/S 0.01 "" YAW RATE, + NOSE RIGHT

126 PRATE DEG/S 0.01 SMITHS GYROS 402-RGA ROLL RATE, + RIGHT WING D

127 QRATE DEG/S 0.01 "" PITCH RATE, + NOSE UP

128 RRATE DEG/S 0.01 "" YAW RATE, + NOSE RIGHT

---------------------------------------------------------------------------

NOTE 1:  This is the backup, or alternative, wind measuring system in case the Litton 90/100 inertial reference system (IRS) should fail.  Calculation of wind components is described in reports by  MacPherson (1988, 1990a, 1990b, 1996) and MacPherson and Bastian (1997).  The air velocity relative to the aircraft is measured by the true air speed (TAS) and noseboom angles of attack and sideslip.  The aircraft inertial velocity relative to Earth is measured in aircraft axes by a system incorporating complementary filtering in real time on the aircraft microprocessor.  A system of accelerometers and rate gyros provides the high-frequency components to this filter; the Decca 3-axis Doppler radar provides the low-frequency components.  The resulting calculated velocity components in a/c axes are subtracted from the TAS components to get the three components of winds in a/c axes.  These are then resolved into Earth axes using the pitch and roll attitude and the aircraft heading to get uge, vge, and wge (channels 16-18).

NOTE 2: The primary wind system uses a Litton 90/100 IRS to measure the aircraft inertial velocity components in 3 Earth axes.  The IRS is similar to an INS (Inertial Navigation System), but measures the velocities, accelerations and rates in aircraft axes as well as Earth axes.  This is also used to derive wind given in channels 11, 13, 15, 19, 20, 21, 42, 43, and 44 above.  Numerous tests have been done to compare flux data derived with these two different wind measuring systems on the Twin Otter.  Some of this appears in MacPherson (1990a, 1996).  These studies reveal that fluxes derived with the older Doppler-based system appear to be underestimated by 10-15 percent.  The Litton based wind should be used whenever possible (channels 19, 20, 21, 13, and 15).

Note 3:  MacPherson (1988, 1990b, 1996) gives a description of a routine used to correct the radup reading for aircraft attitude changes.

In 1996, AFM-04 submitted the following table describing the instrumentation status.

1996 Flights

There may be some steps in some of the analog channels;  Most obvious in high-altitude inputs and tests; Required further investigation.

It appears that the ESRI and LICOR are slightly motion dependent, producing small additional downward C02 flux for ESRI, upward for LICOR.

There is a sawtooth on the WAIRZ that originates from the basic resolution of the digiquartz transducers, PALPHA, PBETA and PDNB.  The PDNB is quite steppy when compared with the Rosemount for PDF.  The range of the PDNB is too high (0-12 psi, which good for about 700 knots!).  It should be replaced with one that does no more than 0-1 psi, or at least that of the PALPHA and PBETA transducers.

Satellite simulator

_ in MSS mode, 1 deg field of view for Flights 58-62,

in SPOT 15-deg field of view for Flights 63-69

in MSS mode, 15 deg field of view, Flights 70-83

NOTE:  In flux re-analysis with Kalman filtering and ground-calculated winds, the TASNB used in most flights was low by about 0.3 mps.  When TASF was used for Flight 65, it was low by 1.3 mps; For Flights 66-   when TASF used, then correction factor of 1.3 was applied in airborne program, so no additional adjustment would be required except when working right from pressure data (recalculated in TASFUSE)

Bias required to beta of +0.35 for all flights except Flt 75, in which it should be 0.54

TASF will be low by 1.3 mps until Flight 66, for which a bias was added to the airborne program

TASNB will be low by 0.3 mps until Flight 67, for which a bias was added to the airborne program

TASNB low by 1.10 mps on Flight 67, possibly due to loose connection on transducer

For Flight 68 -  TAS bias removed from airborne program, but biases added to PDNB of 0.4 mb, and to PDF of 1.2 mb:  PDNB bias changed to +0.2 for Flight 69 and subsequent flights

Temperatures start to diverge about Flight 72, with TSPort greater than starboard, increasing to 1.0 deg by Flight 78.

NOTE:  BOREAS airborne program was inadvertently using old noseboom PE values, not new ones derived on May 16 test flights:  In recalculation, run PLOTPOK96_new with correct PE's, then re-run the reciprocal wind checks to get new biases for TAS and Beta.  Data suggests that old PE's may be the more accurate.  Need to do verification of May 16 PE's on another flight.

NOTE:  Also have noticed that the PDFNB is using the new PE's (0.904*PDFC);  To match the old PE's used in the other calculations, 0.936 should be used.  Airborne program changed to 0.936 on August 1 before Flight 78

RADUP reads -6 while in hangar; add bias in REDEF programs

GPS has lag of several seconds; must adjust in  ARCPOK96_new

TECO possibly reads 3 ppb high;  Must check all zeros for each individual flight prior to final archive round of flux calculations.

NOTE:  Greenness index is not necessarily associated with healthy plants and good C02 uptake on Ag run, for Canola indicates a greenness index of 1.9, when it is at least as developed as wheat fields giving 3.2-3.5

LICOR spikes caused by spikes in PSLICOR; affects C02 more than H20.

The following table indicates instrument status during the flights in 1996.

Date  Flight #

Instrument Status

Jul 09   58

- GPS quit twice, first enroute from YPA to W to start Ag run, second in last run of first grid (approx 1755 GMT).  Returned to normal at 1808.

- LOZ3 ozone analyzer u/s most of flight, turned off for part of flight

- NO/N02 analyzer reads high throughout flight, although recorded reading is perhaps only a tenth of what was shown on face of unit.

- ESRI C02/H20 analyzer intermittent, but H20 OK after Run 14; C02 signal looks OK except for Runs 13 and 14 when unit turned off

- Reciprocal runs suggest TAS low by 0.5 mps; apply this bias in re-calc

- DLR ozone analyzer has spikes and poor correlation with TECO;   Not useable

- Laser altimeter drops to below zero in several spikes, perhaps an indication of a signal or error level.

Jul 09   59

- NO/N02 analyzer possibly u/s throughout flight

- LOZ3 recycled off/on in sounding (Run 01), but then OK rest of flight; use 1.0 slope when doing fluxes from regression against TECO

- Reciprocal runs suggest TASNB low by 0.45 mps

Jul 10   60

- GPS quit at 1754 Z for about 4 minutes.  Caused abort of Run 13 at OJP

- TASNB appears to be low by 0.4 mps

- ESRI H20 signal unusable for Run 09; spikes

- NO/N02 analyzer not correct, drifting downwards through flight from 20 ppb

- Time lost 20 sec at start-up, so IAR time behind AES and cameras by about 20 seconds

Jul 11   61

- GPS quit at 1751 for a few minutes

- NO/N02 analyzer u/s

- Time 20 seconds behind cameras, but synchronized with AES DAS

- TASNB appears low by about 0.3 mps

- Note:  C02 and H20 analyzers calibrated prior to this flight

- LICOR C02 has some spikes and seems noisy and poorly correlated with the ESRI during the OBS runs late in the flight.

Jul 12   62

- GPS problem, recycled Off/On at 1745 GMT; Problem identified as poor satellite configuration

- DLR ozone analyzer turned off at 1743 due to rain on Run 04

- LOZ3 power supply failed, so unit operated on battery but failed at 1853 Z in Run 11

- ESRI C02 should be distrusted on several runs when rain encountered.

- NO/NO2 analyzer removed from aircraft

Jul 14    63

- Satellite Simulator changed to SPOT Mode, Gains set at B=5, C=25, and D=5:  D is limiting at about 42 W/m2 only over Ag Run

- Flew into rain on Run 10; DLR selected OFF at 1740

- DLR signal alive for first 9 runs, but biased off to near zero concentration for unknown reason

- AES DAS quit at 1649 GMT

- GPS outage again most of time between 1725 and 1740 GMT

- New routine to hold Laser_alt constant when signal drops below zero.  Unit does not work over water

- Note:  Runs 5-11 across Candle Lake include 2 n miles of forest before and after the lake surface, thus the flux calculated over the whole event will not be accurate;  Runs must be subdivided to get fluxes for water only.

Date  Flight

Instrument Status

July 14 (cont)

- Good agreement between the ESRI and LICOR C02 fluxes, but the LICOR H20 fluxes quite a bit smaller than the ESRI.

- NO/NO2 analyzer removed from aircraft

- Reciprocal Ag runs suggest TASNB too low, as in previous flights.

Jul 15    64

- ABORT Flight due to failure of P_Alpha pressure transducer, therefore no vertical gust capability

- NO/NO2 analyzer removed from aircraft

Jul 15    65

- TEST Flight;  Temporary pressure transducer configuration:

_ P_beta transducer (0-3 PSID) moved to P_alpha position

_ Noseboom PD transducer (0-12 PSID) moved to P-beta position

_ NO PDNB or TASNB recorded

_ Winds and static temperature use TAS_F (i.e., F/S 2 ON)

_ Alpha and Beta use PDFNB (i.e., F/S 3 ON)

- TAS_F reads 1.3 mps low

- Beta bias of -0.4 deg:  Add 0.4 deg to beta (which already has an additional 0.35 deg)

- Greenness Index sensors not turned on

- NO/NO2 analyzer removed from aircraft

- DLR ozone analyzer reads near zero throughout flight

- Magnetic heading mis-set until 1910.

- PSNBC incorrect; not corrected for Position Error

Jul 19    66

- Pressure transducers back in usual configuration

- Beta bias again to add 0.35, and TASNB add 0.3 mps

- DLR instrument not flown

- NO/NO2 analyzer removed from aircraft

- GPS out at 1715 at end of Run 06 and through Run 07

- First flight with bias of 1.3 mps added to TASF

- First flight with Laser altimeter updating at 50 Hz

Jul 20    67

- First flight with bias of 0.3 mps added to TASNB

- TASNB was low by 1.1 mps, possibly due to loose connection on transducer

- Also discovered that airborne program was using old noseboom PE's, rather than new ones derived on May 16 test flight.  Will leave that way until end of program

- PSduct appears to be 3 mb high.

- NO/N02 analyzer on aircraft, but N02 signal seems highly correlated with altitude.

Jul 20    68

- For this flight (and subsequent ones), the TAS bias was removed and instead, a bias was added to PDNB (0.4 mb) and PDF (1.2 mb) to bring them to zero while at zero airspeed in the hangar.

- Reciprocal data from each grid gives the same TAS error;  0.37 mps should be subtracted from TASNB.  Beta bias less than 0.1 deg.

- Run 12 was wrong line (FR-FP instead of FR-FQ);  Was repeated

- GPS locked up on last run of first grid (Run 11);  run may have been extended a bit too far east.

- GPS out between grids; Poor satellite configuration

- PDNBC has little steps that are not identical to PDNB, even on ramp.

- Care with fluxes:  There are trends and discontinuities in some of the runs for C02 and H20, perhaps due to large clouds just west of grid.

Date  Flight

Instrument Status

Jul 23   69

- ABORT flight; generator out, then brake fire

- PDNB bias set to +0.2 this and subsequent flights; PDF bias remains at +1.2

Jul 25  T-11

- GPS not turned on, and heater circuit breakers pulled

- Generator failure on takeoff; abort rest of flight

- No DAT tape

Jul 25  T-12

- Generator test: GPS not used; no DAT tape

Jul 26   70

- GPS from Convair 580 installed after Flight 69; first project use this flight

- GPS intentionally left OFF until after takeoff in case there was a generator problem; selected ON at about 1942Z, a minute after takeoff

- Satellite Simulator in MSS Mode, 15 deg, gains 5,5,5,1

- DLR ozone analyzer not installed this flight

- PSDUCT checked and found 3 mb high on landing.

- Event marker off too short time between Runs 01 and 02:  Flux program groups them together, so need to re-run by event time

- LICOR H20  plotted vs ESRI had slope of about 0.85, and resulted in low fluxes compared to ESRI.  Prior to this flight, a major calibration was performed on LICOR with many test gases to answer 480 vs 422 problem.  No problem was found, but now slope seems low compared to ESRI.

Jul 27   71

- GPS intentionally left OFF until after takeoff in case there was a generator problem; selected ON at about 1655Z, a minute after takeoff

- DLR ozone analyzer not flown

- Runs 20 and 21 through rain shower, may affect ESRI C02/H20 fluxes

- Time 20 seconds behind cameras, but aligned with AES DAS

- GPS into Standby for about a minute after Ag Run 01

- NB:  LICOR H20 fluxes seemed low compared to ESRI, and even compared to those from DewPt:  LICOR H20 cospectrum has funny shape, with peak at wavelength different from either LICOR C02 or ESRI H20.

- Spikes and/or dropouts in ESRI H20 signal on at least one run; Must check all runs for H20 spikes, especially since there is concern about its comparison with the LICOR H20

Jul 29   72

- GPS intentionally left OFF until after takeoff in case there was a generator problem; selected ON at about 1513Z, a minute after takeoff

- First flight with difference in static pressures; PSNBC greater than PSFC by 1.8 mb;  PSFC later proven to be the errant one- Time 20 seconds behind cameras, but synchronized with AES DAS

- LICOR H20 could be low on first 3 or 4 runs

- Cospectra indicate that LICOR calibration too low, or ESRI too high

- GPS went into Standby at 1720Z at end of Run 18; selected OFF then ON

- Spikes in ESRI H20 signal

Jul 29   73

- Time 20 seconds behind the cameras, but synchronized with AES DAS

- Static pressure difference; PSFC about 2.5 mb too low

Jul 30   74

- Time 20 seconds behind the cameras, but synchronized with AES DAS

- There is a 2.5 mb difference in PSFC and PSNBC (PSFC probably too low)

- GPS went into Standby enroute to 'A'

Date  Flight

Instrument Status

Jul 30   75

- Time 20 seconds behind the cameras, but synchronized with AES DAS

- There is a 2.5 mb difference in PSFC and PSNBC (PSFC probably too low)

- NO/N02 device off scale high

Jul 31   76

- Time 20 seconds behind the cameras, but synchronized with AES DAS

- There is a 2.5 mb difference in PSFC and PSNBC.  Ground check August 01 indicate PSFC is errant transducer

- NO/N02 device off scale high

- Standard deviation of ESRI C02 signal was high relative to LICOR on several runs, (eg., Run 22); Large spikes in ESRI occasionally, H20 and C02 (Run 5

- LICOR C02 signal suspect.  seems to lack high frequency, like the H20 signal of Flight 71.  Also, see notes on Flight 77 re: the LICOR C02 lag

LICOR span also found low on August 01 calibration

- For some reason, the TAS bias has dropped to zero

Jul 31   77

- Time 20 seconds behind the cameras, but synchronized with AES DAS

- There is a 2.5 mb difference in PSFC and PSNBC

- NO/N02 device off scale high

- The difference between the LICOR and ESRI C02 fluxes seems larger than usual; check cospectra;  LICOR C02 has many spikes.  Also, Run 02 has positive LICOR C02 flux when ESRI negative.  Data compared with Harry McCaughey at YJP, LE's agreed, but his C02 fluxes agreed well with ESRI (his -0.23, ours ESRI -0.215), and NOT the LICOR (-0.04)

- Cospectra show that LICOR C02 very suspect (see Run 6);  Also, the LICOR C02 signal seems to require a different lag than the H20, which is very unusual.  The C02 signal looks like it should have only been lagged 8 time slices, rather than 19 like the H20: Found out August 4 that this is due to pressure used in conversion from ppm to concentration.  Mixing ratio lags OK

- Data archived using ESRI for C02 flux, but LICOR for H20

- When calibrated Aug. 1, the span was low on the LICOR C02 by approximately 10 percent.

- LICOR Ser. 649 removed from aircraft after this flight and replaced by LICOR Ser. 703

- For some reason, the TAS bias has dropped to zero

Aug 01   78

- First flight with LICOR Ser. 703

- LICOR C02 fluxes larger, but still well below ESRI

- Also, LICOR H20 fluxes low, particularly on 100' runs;  Low at all frequencies, suggesting calibration has low span

- Data archived using ESRI for H20 flux, but LICOR for C02

- GPS total failure at 1847Z prior to first run

- No AES data recorded this flight

- There is a 2.5 mb difference in PSFC and PSNBC

- PDFNB factor changed to old values of 0.936 PSFC

- PSFC less than PDNBC

- Port temperature greater than Starboard

Date  Flight

Instrument Status

Aug 02   79

- LICOR fluxes very low compared to ESRI: regression of 32-Hz data suggest calibration sensitivity too low when compared with ESRI

On some runs at YJP, LICOR C02 trace very different than ESRI

LICOR C02 trace trails ESRI by about 1/2 second, while H20 is OK.

- PSFC less than PDNBC

- Port temperature greater than Starboard by about 2 deg C.

- Time 20 seconds behind the cameras, but synchronized with AES DAS

- Turned ESRI instrument OFF at 1751 after sounding since nitrogen was getting low

- DLR ozone analyzer has some large excursions that are not duplicated by LOZ3 or TECO

Aug 03   80

- First Flight with LICOR Ser. # 176 (same unit flown in 1994, still using Dec. 1993 calibration constants)

- LICOR C02 fluxes still well below those of ESRI, and became near zero at end of flight, as in Flight 79

- LICOR H20 span adjusted in flight right after takeoff; set to approximate data from aircraft dew point sensor.  Was reading about 5 gm/Kg high until then (approx. 1610 Z)

- PSFC still about 2 mb less than PSNBC

- Temperature probes cleaned and recalibrated prior to this flight.

- Time 20 seconds behind the cameras, but synchronized with AES DAS

- Evidence of steps in most analog channels, most clearly seen in high altitude runs where signals are clean (see pitches)

Aug 05   81

- LICOR calibrated before flight;  also filter and filter line replaced;  old unit had possible small leak at connector

- PSFC less than PSNBC by about 2 mb

- DLR ozone device matched LOZ3 in flight for first time in quite some time; CWT cleaned unit after last flight

- Airborne LICOR subroutine changed before this flight:  The C02 and H20 concentrations in mg/m3 and gm/m3 respectively are now calculated using the PS_LICOR and LC_TEMP instead of the noseboom pressure and temperature.

- Evidence of steps in most analog channels, most clearly seen in high altitude runs where signals are clean (see pitches)

Aug 06  T-13

- TEST FLIGHT with ESRI dust closed and 'bagged';  LICOR still plumbed to duct

- PSFC lower than PSNBC by about 2 mb

- DLR ozone analyzer not installed

Aug 07   82

- PSFC lower than PSNBC by about 2 mb

- DLR ozone analyzer turned OFF at 1545 Z due to rain

- Time about 20 seconds behind camera, but synchronized with AES DAS

Aug 08   83

- PSFC lower than PSNBC by about 2 mb

- DLR ozone analyzer not flown this flight

Time about 20 seconds behind camera, but synchronized with AES DAS

Summary of 1996 Fluxes

SSA

Date

| DoY/Flt | Site |
| --- | --- |

GMT

|  | Runs1 |
| --- | --- |

Wind

d/mps

Temp

degC

H

W/m2

LE3

| W/m2 | BR |
| --- | --- |

C024

mg/m2/s

Oz

ug/m2/s

NetR

W/m2

Jul 09

191

58

Grid

Grid

1730

1845

9

9

197/5.0

198/5.0

19.4

20.0

190

222

208

212

0.91

1.05

-0.39

| -0.30 |  |
| --- | --- |

679

712

Jul 09

191

| 59 | OA | 2130 | 6 | 182/5.5 | 20.3 | 104 | 270 | 0.39 | -0.73 | -0.32 | 506 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Jul 10

192

60

OBS

OJP

1715

1800

8

7

133/6.0

119/5.2

21.3

22.3

183

224

193

214

0.95

1.05

-0.24

-0.28

-0.31

-0.37

616

644

Jul 11

193

61

OA

OBS

1715

1845

9

6

012/2.4

036/3.9

20.7

22.3

74

168

313

180

0.23

0.93

-0.81

-0.19

-0.44

-0.10

573

583

Jul 14

196

63

Ag

Lake

1815

1730

7

7

256/3.8

231/2.5

21.4

20.6

42

1

339

25

0.12

0.06

-0.88

0.00

-0.25

0.00

616

-

Jul 19

201

| 66 | OA | 1700 | 6 | 202/5.6 | 17.4 | 120 | 268 | 0.45 | -0.79 | -0.59 | 615 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Jul 20

202

| 67 | Lake | 1145 | 6 | 124/2.0 | 13.7 | 7 | 59 | 0.12 | +0.14 | -0.04 | - |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Jul 20

202

68

Grid

Grid

1630

1745

9

9

158/3.2

187/2.6

17.5

19.3

152

199

153

247

0.99

0.81

-0.38

-0.39

-0.17

-0.17

557

693

Jul 26

208

| 70 | OA | 2045 | 6 | 165/2.1 | 18.0 | 84 | 215 | 0.39 | -0.82 | -0.35 | 381 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Jul 27

209

71

Grid

Grid

OBS

1745

1845

1915

9

9

2

131/3.9

155/4.5

166/4.9

16.9

17.2

17.1

47

42

33

121 5

125

50

0.39

0.34

0.65

-0.49 6

-0.43

-0.21

-0.34

-0.34

-0.17

311 6

245

64

Jul 29

211

72

OBS

Grid

Grid

1600

1700

1745

8

9

9

174/1.8

148/1.5

152/1.8

18.6

19.4

20.5

130

134

149

160

187

227

0.82

0.71

0.66

-0.33

-0.37

-0.40

-0.26

-0.24

-0.26

500

578

621

Jul 29

211

| 73 | OA | 2015 | 7 | 177/2.5 | 22.3 | 23 | 173 | 0.13 | -0.43 | -0.17 | 212 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

1 - Only nominal 100' runs     3- From LICOR   4- From LICOR

5 - LICOR H20 suspiciously low this day   6- Overcast this day

7 - Clouds over; decreasing radiation study

Note : Fluxes computed with linearly detrended data with Kalman-corrected winds, as archived

NSA

Date

| DoY/Flt | Site |
| --- | --- |

GMT

|  | Runs |
| --- | --- |

Wind

| d/mps | Temp |
| --- | --- |

H

W/m2

LE

| W/m2 | BR |
| --- | --- |

C02

mg/m2/s

Oz

ug/m2/s

NetR

W/m2

July 31

213

76

Grid

Grid

OBS

OJP

1515

1615

1700

1730

9

9

5

8

203/3.6

219/4.3

222/3.9

218/4.3

23.3

24.3

25.0

25.3

92

132

196

237

150

190

135

96

0.61

0.70

1.45

2.46

-0.23

-0.22

-0.19

-0.09

-0.03

-0.09

0.01

0.00

450

527

586

609

July 31

213

77

Burn

YJP

Burn

1915

1945

2000

4

8

5

216/5.4

222/5.0

212/5.5

26.1

26.5

26.3

81

175

90

171

75

211

0.47

2.32

0.43

-0.27 8

-0.22

-0.34

-0.20

-0.03

-0.25

439

368

479

Aug 01

214

| 78 | Burn | 1900 | 4 | 200/6.4 | 24.3 | 64 | 185 9 | 0.35 | -0.29 | -0.16 | 317 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Aug 02

215

79

Grid

Grid

OBS

OJP

YJP

1500

1600

1645

1715

1745

9

9

5

8

6

225/4.6

235/5.4

233/5.7

228/6.1

230/7.5

23.6

24.8

25.7

26.1

26.4

62

106

148

200

206

172

150

170

83

124

0.36

0.71

0.87

2.41

1.66

-0.22

-0.16

-0.19

-0.07

-0.09

-0.18

-0.16

-0.16

-0.12

-0.10

431

515

599

554

575

Aug 03

216

80

Grid

Grid

OBS

YJP

1630

1730

1815

1845

9

9

6

5

100/3.5

115/3.2

127/3.5

104/3.4

25.1

25.9

26.7

27.0

135

162

205

174

167

145

159

67

0.81

1.12

1.28

2.60

-0.26

-0.17

-0.18

-0.02

-0.15

-0.16

-0.18

-0.05

509

554

591

418

Aug 05

218

81

OJP

Grid

Grid

OJP

1600

1645

1745

1815

6

9

9

6

201/3.6

195/3.9

196/4.3

203/4.4

21.6

22.2

23.1

23.1

141

138

129

68

148

222

180

101

0.95

0.62

0.62

0.67

-0.13

-0.27

-0.31

-0.11

-0.21

-0.30

-0.17

-0.16

510

538

462

182

Aug 07

220

82

OBS2

OBS2

Burn

1500

1545

1645

4

4

6

295/4.6

280/4.6

295/6.5

12.9

13.5

13.6

48

87

61

143

190

135

0.33

0.46

0.45

-0.29

-0.36

-0.34

-0.31

-0.33

-0.17

283

296

20710

Aug 08

221

83

Grid

Grid

OBS

1515

1615

1700

9

9

6

004/4.1

009/4.0

014/3.7

9.2

10.1

11.1

88

144

183

88

116

136

1.00

1.24

1.35

-0.43

-0.51

-0.50

-0.17

-0.22

-0.19

272

400

482

2 - Flux divergence or advection study, only 30 m runs shown

8 - ESRI C02 fluxes used Flt 77   9 - ESRI LE fluxes used Flt 78

10 - Increasing cloud

Note : Fluxes computed with linearly detrended data using Kalman-corrected winds:  as archived

7. Data Description

7.1 Spatial Characteristics

7.1.1 Spatial Coverage

Grid flight patterns consisted of twin sets (one in the NSA and one in the SSA) of nine parallel lines flown at 100 feet above ground level (AGL) at a 2-km spacing covering a 16- by 16-km area. For each of these grids, two flight plans were stored in the aircraft’s GPS system; one with the east/west lines, and one with the north/south lines.  On a given day, the wind direction was measured and the flight pattern was chosen that was closest to cross wind.  Since turbulent eddies are elongated in the direction of the wind, crosswind tracks encounter more eddies; thus, the determination of the flux is statistically more reliable.  On each grid flight, the grid pattern was flown twice, with the repeated pass flown in the opposite direction to the first.  In this way, each pair of runs on a given line can be examined for possible biases in wind measurement or other variables.  The double grid pattern took nearly 2 hours to fly.  Some regional runs were also flown, for example, from Prince Albert to Nipawin, Saskatchewan.  Very long regional runs were flown (at approximately 500 feet) on the transit flights between Prince Albert (near the SSA) and Thompson (in the NSA).

The two 16-km grids fall within the NSA and SSA.

The North American Datum of 1983 (NAD83) corner points for these grid patterns are:

SSA

Latitude     Longitude

--------     ---------

Northeast    53.930° N     104.565° W

Northwest    53.930° N     104.810° W

Southwest    53.787° N     104.810° W

Southeast    53.787° N     104.565° W

NSA

Latitude     Longitude

--------     ---------

Northeast    55.947° N      98.397° W

Northwest    55.947° N      98.653° W

Southwest    55.803° N      98.653° W

Southeast    55.803° N      98.397° W

In their 1996 report, AFM-04 reported the following waypoints for non-grid runs.

|  | Waypoint | 1 | Waypoint | 2 |
| --- | --- | --- | --- | --- |
|  | Site | Lat. | Long. | Lat. | Long. | Comments |
| OA - SSA | 53 34.9 | -106 16.8 | 53 38.4 | -106 09.6 | About 11 km, homogeneous vegetation |
| OBS - SSA | 53 59.0 | -105 08.2 | 53 57.8 | -104 56.0 | 14.5 km, mostly spruce, tower near west end |
| OJP - SSA | 53 53.6 | -104 44.2 | 53 56.0 | -104 39.5 | Only 6 km homog., so marginal for TS |
| Agricultural Run | 53 21.0 | -105 28.8 | 53 31.0 | -105 28.9 | 18.5 km, pasture, canola and wheat |
| Extended Ag to forest | 53 31.0 | -105 28.9 | 53 41.0 | -105 29.0 | 18.5 km interface from Ag to forest |
| Full Candle Lake Run | 53 34.7 | -106 23.8 | 53 59.0 | -104 47.2 | 115 km, Heterogeneous, 3 lakes |

Candle Lake Run for

| morning Flight 67 | 53 49.8 | -105 27.9 | 53 51.6 | -105 12.9 | 14 km run across Candle lake |
| --- | --- | --- | --- | --- | --- |
| OBS - NSA | 55 52.5 | -98 22.5 | 55 52.4 | -98 34.0 | 12 km good sfc. |
| OJP - NSA | 55 55.6 | -98 37.7 | 55 56.6 | -98 36.2 | 3 km homog. veg, marginal for TN |
| Burn - NSA | 55 49.7 | -98 19.4 | 55 51.6 | -98 30.0 | 11 km all burned; used for almost all runs in 1994 |
| YJP - NSA | 55 53.8 | -98 16.4 | 55 54.2 | -98 18.8 | < 3km, marginal for flux |

Flux runs were also made over Candle Lake over a length of 115 km.  These runs were made to cover a heterogeneous track across the study area in order to see how flux varies over different land cover types.

En route from the Prince Albert Airport to the area of the flux towers in the boreal forest, an agricultural area was overflown consisting mostly of pasture, rapeseed, and wheat.  To collect data to monitor fluxes over the whole growing season in an agricultural area, a 20-km north/south track was selected in this area.  This was flown by the Twin Otter at a 30-m altitude on 40 occasions during the three IFCs in 1994.

On 08-Sept-1994, a 500-km flux run was made along the transect between the NSA and SSA from 1640 to 2040 Greenwich Mean Time (GMT).

7.1.2 Spatial Coverage Map

None.

7.1.3 Spatial Resolution

The spatial resolution of the original data used in the flux computations is a function of the aircraft speed (approximately 55 m/s) and the digital recording rate (16 Hz in 1994, 32 Hz in 1996) and the anti-alias filtering applied to the data prior to recording (5.5 Hz).  This translates to a basic sampling resolution of approximately 12 m (1994) and 6 m (1996) for the Twin Otter.

7.1.4 Projection

None. These data were collected at point locations.

7.1.5 Grid Description

The data were collected at point locations, primarily in a regular grid pattern.  The grid spacing was approximately 2 km.

7.2 Temporal Characteristics

7.2.1 Temporal Coverage

In 1994, data were collected on the following dates:

IFC-1:  25-May-1994 to 27-May-1994

29-May-1994

31-May-1994 to 01-Jun-1994

04-Jun-1994

06-Jun-1994 to 11-Jun-1994

13-Jun-1994

IFC-2:  20-Jul-1994 to 29-Jul-1994

01-Aug-1994 to 02-Aug-1994

04-Aug-1994

08-Aug-1994

IFC-3:  31-Aug-1994 to 03-Sep-1994

06-Sep-1994

08-Sep-1994

11-Sep-1994 to 19-Sep-1994

In 1996, data were collected on the following dates:

06-Jul-1996 to 07-Jul-1996

09-Jul-1996 to 12-Jul-1996

14-Jul-1996 to 15-Jul-1996

19-Jul-1996 to 20-Jul-1996

23-Jul-1996

25-Jul-1996 to 27-Jul-1996

29-Jul-1996 to 31-Jul-1996

01-Aug-1996 to 03-Aug-1996

05-Aug-1996 to 10-Aug-1996

SSA   * number of runs of each type

| Date | Fl | Ag | Intf | CL | Grid |  | SS |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Bud | TRS | Other | Snd |
| 1996 |
| W-X | X-Y |
|  | OA | BS | JP | Fen |
| Jul 09 | 58 | 2 | 2 |
| 18 |
| 2 |
| Jul 09 | 59 |  |
| 6 |
|  | 1 |
| Jul 10 | 60 | 2 | 2 |  |
|  | 8 | 7 |
|  | 1 |
| Jul 11 | 61 | 1 | 1 | 1 |
| 9 | 6 |
| 1 |
| Jul 12 | 62 | 2 | 2 |
|  | 11 |
|  | 1 |
| Jul 14 | 63 | 8 | 2 |
|  | 7 | 2 |
| Jul 15 | 65 | 2 |
|  | Jul 19 | 66 |  |
| 6 |
|  | 1 |
| Jul 20 | 67 |  |
|  | 2 |
|  | 16 | 3 |
| Jul 20 | 68 | 2 |
|  | 18 |  |
|  | 1 |
| Jul 26 | 70 | 1 |  | 1 |
| 6 |
| 1 | 1 |
| Jul 27 | 71 | 1 |
|  | 18 |
| 2 |
| 1 |
| Jul 29 | 72 | 2 |
|  | 18 |
| 8 |
| 2 |
| Jul 29 | 73 | 1 |
|  |  | 7 |
| 8 | 1 |
| Jul 30 | 74 |  |
| 1 |
|  | 1 |
| 2 |
|  | 17 | 24 | 9 | 3 | 72 | 34 | 26 | 7 |
| 11 | 1 | 32 | 20 |

NSA

Date

|  | Fl | Grd |
| --- | --- | --- |
| SS |
|  | M-O | TRS | Other | Snd |
| 1996 |
|  | burn | BS | OJP | YJP |
| Jul 30 | 75 |
|  | 6 |
|  | 1 | 1 |
| 1 |
| Jul 31 | 76 | 18 |  | 5 | 8 |  |
|  | 2 | 2 |
| Jul 31 | 77 |
| 9 |
|  | 8 |
| 1 |
| Aug 01 | 78 |
| 8* |
|  | Aug 02 | 79 | 18 |  | 5 | 8 | 6 |  |
|  | 2 |
| Aug 03 | 80 | 18 |  | 6 |  | 5 |
|  | 4 | 1 |
| Aug 05 | 81 | 18 |
|  | 12 |
| 6 | 3 |
| Aug 07 | 82 |
| 6 | 12 |
|  | 4 | 2 |
| Aug 08 | 83 | 18 |
| 6 |
| 1 |
|  | 09 | 90 | 23 | 40 | 28 | 19 | 1 | 1 | 16 | 13 |

CL: 62 nm Candle Lake     Snd: Sounding    Bud:  Flux Budget

TRS - transect PA/Flin Flon (SSA) Flin Flon/Thompson (NSA)    SS:  Site-specific (towers)

*  4 runs at 100', 4 at 500'

7.2.2 Temporal Coverage Map

None.

7.2.3 Temporal Resolution

The aircraft data were recorded at a basic rate of 16 Hz (1994) or 32 Hz (1996).  Flight durations were typically 3 to 3.5 hours.  On several occasions there were two flights per day.

7.3 Data Characteristics

Data characteristics are defined in the companion data definition file (afm4tofx.def).

7.4 Sample Data Record

Sample data format shown in the companion data definition file (afm4tofx.def).

8. Data Organization

8.1 Data Granularity

All of the AFM-04 Twin Otter Aircraft Flux Data are contained in one data set.

8.2 Data Format(s)

The data files contain numerical and character fields of varying length separated by commas.  The character fields are enclosed with single apostrophe marks.  There are no spaces between the fields. Sample data records are shown in the companion data definition file (afm4tofx.def).

9. Data Manipulations

9.1 Formulae

The principal equations used to compute wind components and fluxes from the Twin Otter data are given in MacPherson (1990b, 1992, 1996).

9.1.1 Derivation Techniques and Algorithms

See MacPherson (1990b, 1992, 1996) and MacPherson and Bastian (1997).

9.2 Data Processing Sequence

9.2.1 Processing Steps

1.  AFM-04 processed the data and sent them to BORIS.

2.  BORIS staff received the data, made necessary conversions to standard units, and loaded the data into the data base.

3.  BORIS staff documented the data set and compiled basic statistics about the data.

See MacPherson (1988, 1990a, 1990b, 1996) and MacPherson and Bastian (1997) for more detailed information about the processing that AFM-04 did to its data before submitting the data to BORIS.

9.2.2 Processing Changes

There are quite a number of selectable options in the playback program for the Twin Otter data.  These include the option to use the alternative (backup) wind computations in case of a problem with the Litton 90/100 IRS.

9.3 Calculations

9.3.1 Special Corrections/Adjustments

1. Calculation of wind components is described in MacPherson (1981, 1990b, 1996) and MacPherson and Bastian (1997).  The air velocity relative to the aircraft is measured by the true air speed (TAS) and noseboom angles of attack and sideslip.  The TAS vector is then resolved into Earth axes (north, east, and vertical components).  Subtracted from these are the aircraft inertial velocity components measured by a Litton 90/100 IRS, to get the three components of the wind velocity in Earth-fixed axes.

An alternative, or backup, wind system is employed on the Twin Otter in case the Litton 90 is unserviceable (rare).  For this system, known as the NAE/DOP winds, the aircraft inertial velocity relative to Earth is measured in aircraft axes by a system incorporating complementary filtering in real time on the aircraft microprocessor.  A system of accelerometers and rate gyros provides the high- frequency components to this filter; the Decca 3-axis Doppler radar provides the low-frequency components.  The resulting calculated velocity components in A/C axes are subtracted from the TAS components to get the three components of wind in A/C axes.  These are then resolved into Earth axes using the pitch, roll, attitude, and aircraft heading.

2. For each flight, the ground speed for all runs is averaged.  The high-pass filtered breakpoint is then selected as the average ground speed divided by 5,000 m.  This gives a breakpoint of about 0.012 Hz for high-pass filtered flux estimates.

3. Three sets of fluxes were derived, one using 'raw' data, one using linearly detrended time histories, and one using high-pass filtered data.  All are included in the archive, as well as correlation coefficients and RMS values of parameters contributing to the flux estimates.

9.3.2 Calculated Variables

There was no direct measurement of net radiation made on the Twin Otter in BOREAS.  Rather, it was calculated at each interval using incident and reflected solar radiation (RADUP and RADOWN), with longwave contributions derived from PRT-5 surface temperature (Ts in deg K) and air temperature (Ta in deg K) in the following equation:

NETRAD = RADUP - RADOWN + [1.20*s*Ta4 - 171.0] - [0.98*s*Ts4]

where the last two terms represent the incident and reflected longwave components, using the Stephan-Boltzmann Constant s = 5.6924*10-8 and a surface emissivity of 0.98.  This computed value of net radiation has agreed quite well with tower measurements.

9.4 Graphs and Plots

None.

10. Errors

10.1 Sources of Error

Errors can result from a number of different sources.  The flux measurements are subject to possible errors relating to the measurements from the IRS.

A problem was detected with the ESRI CO2 analyzer.  Possible reasons for this problem are listed in MacPherson (1996).  As a result of this problem with the ESRI, data from the LI-COR were reported for the CO2 and H2O fluxes.

10.2 Quality Assessment

10.2.1 Data Validation by Source

Great care has been taken in the collection and analysis of the Twin Otter data.  The wind measuring system is continually monitored for accuracy using techniques such as wind boxes, control input cases, and intercomparisons with other aircraft (Dobosy et al., 1997).  Cospectral plots have been used to check the flux contributions at all wavelengths to ensure that they were not contaminated by inadequate compensation for aircraft motion.

Aircraft data were compared at various BOREAS workshops.  This led to the decision to include all three sets of fluxes (i.e., from raw, detrended, and HP-filtered time histories) in the database.

10.2.2 Confidence Level/Accuracy Judgment

See Section 10.2.1.

10.2.3 Measurement Error for Parameters

Not available at this revision.

10.2.4 Additional Quality Assessments

See Dobosy et al. (1997) for a comparison of fluxes from various aircraft.

AFM-04 submitted the following comparison table based on 1996 data.

COMPARISON BETWEEN TWIN OTTER AND FLUX TOWERS

BOREAS 1996

a) Old Aspen - SSA

Date

1996

Time1

| GMT | # runs | Alt5 | Temp |
| --- | --- | --- | --- |

H

W m-2

LE3

W m-2

C024 Flux

mg m-2 s-1

July 09

Flt 59

2130

2200

2120-2148

6

42

20.92

20.80

20.34

141

85

104

230

252

268 301

-0.61

-0.59

-0.71 -0.89

July 11

Flt 61

1730

1703-1730

6

36

21.60

20.59

100

75

338

306 350

-0.81

-0.78 -0.88

July 19

Flt 66

1730

1700-1720

4

46

17.86

17.40

204

138

285

266 280

-0.79

-0.80 -0.95

July 26

Flt 70

2100

2038-2103

6

32

18.95

17.95

157

84

171

214 260

-0.61

-0.81 -0.95

July 29

Flt 73

2030

2001-2025

6

34

23.23

22.19

7

10

93

154 186

-0.15

-0.36 -0.40

1 - Lines with single time are for tower; lines with time range are for aircraft

For Aspen tower, time is for the end of the half hour period.

b) Old Black Spruce - SSA

Date

1996

Time1

| GMT | # runs | Alt5 |
| --- | --- | --- |

Net Rad

W m-2

H

W m-2

LE3

W m-2

C024 Flux

mg m-2 s-1

U*

m s-1

July 10

Flt 60

1722

1702-1730

5

43

545

613

349

183

134

173 179

-0.25

-0.22 -0.44

0.87

0.78

July 11

Flt 61

1900

1830-1902

6

38

727

583

475

168

336

180 179

-0.29

-0.19 -0.39

0.61

0.62

July 20

Flt 67

1100

1044-1047

1

35

-33

-69

-4

-6

3

2 2

+0.04

+0.06 +0.06

0.07

0.00

Jul 29

Flt 72

1630

1558-1626

5

35

483

515

227

134

120

174 199

-0.37

-0.34 -0.53

0.30

0.33

1  For tower, time is for end time of 1/2-hour period         3, 4    Left From LI-COR data, right - ESRI

5  From radar altimeter, generally above canopy     7  Only runs used within tower half-hour

c) Old Jackpine - NSA

Date

1996

Time1

| GMT | # runs | Alt5 | Temp8 |
| --- | --- | --- | --- |

Wind

degT/mps

H

W m-2

LE3

W m-2

C024 Flux

mg m-2 s-1

U*

m s-1

July 31

Flt 76

1700

1715-1732

8

29

25.25

287/5.4

210/4.2

287

236

46

99 81

-0.19

-0.09 -0.40

0.93

0.71

Aug 02

Flt 79

1707-1727

8

32

26.03

287/7.2

227/5.6

364

197

95

90 109

-0.105

-0.07 -0.31

1.49

0.89

Aug 05

Flt 81

1558-1611

1811-1823

6

6

32

31

21.62

23.11

201/4.0

203/4.2

141

67

144   145

99 99

-0.13   -0.37

-0.11 -0.21

0.53

0.67

1  For tower, time is for start of 1/2-hour period         3, 4    Left From LI-COR data, right - ESRI

5  From radar altimeter, generally above canopy     7  Only runs used within tower half-hour

8  Tower temperature at 30 m

d) Old Black Spruce - NSA

Date

1996

Time1

| GMT | # runs | Alt5 | Temp8 |
| --- | --- | --- | --- |

Wind

degT/mps

H

W m-2

LE3

W m-2

C024 Flux

mg m-2 s-1

U*

m s-1

July 30

Flt 75

2030

2017-2048

6

33

27.06

27.25

214/2.9

220/2.4

370

176

113

167 173

-0.017

-0.12 -0.31

0.29

0.42

Jul 31

Flt 76

1700

1650-1713

5

34

24.89

24.97

216/4.3

215/3.8

501

194

206

137 143

-0.22

-0.18 -0.40

0.80

0.63

Aug 02

Flt 79

1700

1642-1704

5

33

25.49

25.63

227/6.4

237/5.6

294

145

176

184 232

-0.26

-0.19 -0.35

0.91

0.83

Aug 03

Flt 80

1800

1830

1806-1834

6

32

26.35

26.76

26.66

123/3.7

135/2.8

116/3.2

420

335

203

82

195

158 171

-0.21

-0.23

-0.18 -0.39

0.56

0.61

0.54

Aug 07

Flt 82

1500

1530

1456-1514

1532-1549

4

4

31

34

12.16

12.66

12.88

13.48

285/3.7

283/4.1

294/4.9

289/4.3

94

84

47

86

142

103

143   181

191 209

-0.27

-0.24

-0.29   -0.50

-0.36 -0.52

0.63

0.58

0.58

0.63

Aug 08

Flt 83

1700

1645-1714

6

32

10.73

11.04

002/2.9

018/4.3

233

182

75

136 138

-0.30

-0.50 -0.76

0.51

0.63

1  For tower, time is for mid time of 1/2-hour period

10.2.5 Data Verification by Data Center

Data were examined for general consistency and clarity.

11. Notes

11.1 Limitations of the Data

None given.

11.2 Known Problems with the Data

Despite careful study by Agriculture Canada technicians and some modifications to the ESRI instrument, data from 1996 suggest that the problems with the ESRI analyzer persisted.

11.3 Usage Guidance

Note that although there are fewer than 100 records in any data file, there are over 170 columns of data.  Most spreadsheet software should be able to handle up to 256 columns of data.

11.4 Other Relevant Information

None.

12. Application of the Data Set

These data can be used to obtain study area and regional scale estimates of the various fluxes.

13. Future Modifications and Plans

None given.

14. Software

14.1 Software Description

The program used to generate the flux estimates for 1994 and output numerous summary files was called ARCPOK94, which was run on a Micro-VAX Alpha computer used in the field and in the lab.

The program used to generate the flux estimates for 1996 and output numerous summary files for archive purposes was called ARCPOK96_NEW, which was run on the MicroVax-alpha computer used in the field and at the Flight Research Laboratory (FRL) in Ottawa.  The principal equations used to compute wind components and fluxes from Twin Otter data are given in MacPherson (1996) and MacPherson and Bastian (1997).

Contact Ian MacPherson for more information.

14.2 Software Access

None given.

15.   Data Access

15.1  Contact for Data Center/Data Access Information

These BOREAS data are available from the Earth Observing System Data and Information System (EOS-DIS) Oak Ridge National Laboratory (ORNL) Distributed Active Archive Center (DAAC). The BOREAS contact at ORNL is:

ORNL DAAC User Services

Oak Ridge National Laboratory

(865) 241-3952

ornldaac@ornl.gov

ornl@eos.nasa.gov

15.2  Procedures for Obtaining Data

BOREAS data may be obtained through the ORNL DAAC World Wide Web site at http://www-eosdis.ornl.gov/ or users may place requests for data by telephone, electronic mail, or fax.

15.3  Output Products and Availability

Requested data can be provided electronically on the ORNL DAAC's anonymous FTP site or on various media including, CD-ROMs, 8-MM tapes, or diskettes.

The complete set of BOREAS data CD-ROMs, entitled "Collected Data of the Boreal Ecosystem-Atmosphere Study", edited by Newcomer, J., et al., NASA, 1999, are also available.

16. Output Products and Availability

16.1 Tape Products

Not applicable.

16.2 Film Products

Not applicable.

16.3 Other Products

These data are available on the BOREAS CD-ROM series.

17. References

17.1 Platform/Sensor/Instrument/Data Processing Documentation

The Twin Otter Atmospheric Research Aircraft and its instrumentation have been described in the following reports available from the National Research Council of Canada:

MacPherson, J.I. 1988. NAE Twin Otter Operations in FIFE. National Research Council Canada Report LTR-FR-104.

MacPherson, J.I. 1989. NAE Twin Otter Operations in the 1988 Eulerian Model Evaluation Field Study. National Research Council Canada Report LTR-FR-107.

MacPherson, J.I. 1990a. NAE Twin Otter Operations in FIFE 1989. National Research Council Report LTR-FR-113.

MacPherson, J.I. 1990b. Wind and Flux Calculations on the NAE Twin Otter. NAE Laboratory Technical Report LTR-FR-109. National Research Council. January 1990.

MacPherson, J.I. 1992. NRC Twin Otter Operations in the 1991 California Ozone Deposition Experiment.  National Research Council of Canada Report LTR-FR-118. May 1992.

MacPherson, J.I. 1996. NRC Twin Otter Operations in BOREAS 1994. Laboratory Technical Report LTR-FR-129. National Research Council Canada. April 1996.

MacPherson, J.I. and M. Bastian. 1997. NRC Twin Otter Operations in BOREAS 1996. Laboratory Technical Report LTR-FR-134.  National Research Council of Canada. November 1997.

MacPherson, J.I. and J.M. Morgan. 1981. The N.A.E. Twin Otter Atmospheric Research Aircraft. National Research Council Report LTR-FR-80.

MacPherson, J.I. and S.W. Baillie. 1986. The N.A.E. Atmospheric Research Aircraft. National Research Council Report, NAE Misc 62.

MacPherson, J.I., R.J. Grossman, and R.D. Kelly. 1992. Intercomparison Results for FIFE Flux Aircraft. Journal of Geophysical Research 97(D17):18,499-18,514.

17.2 Journal Articles and Study Reports

Barr, A.G., A.K. Betts, R.L. Desjardins, and J.I. MacPherson. 1997. Comparison of regional surface fluxes from boundary-layer budgets and aircraft measurements above boreal forest. Journal of Geophysical Research 102(D24): 29,213-29,218.

Desjardins, R.L., J.I. MacPherson, L. Mahrt, P. Schuepp, E. Pattey, H. Neumann, D. Baldocchi, S. Wofsy, D. Fitzjarrald, H. McCaughey, and D.W. Joiner. 1997. Scaling up flux measurements for the boreal forest using aircraft-tower combinations. Journal of Geophysical Research 102(D24): 29,125-29,133.

Dobosy, R.J., T.L. Crawford, J.I. MacPherson, R.L. Desjardins, R.D. Kelly, S.P. Oncley, and D.H. Lenschow. 1997. Intercomparison among four flux aircraft at BOREAS in 1994.  Journal of Geophysical Research 102(D24):29,101-29,111.

Ogunjemiyo, S., P.H. Schuepp, J.I. MacPherson, and R.L. Desjardins. 1997. Analysis of flux maps versus surface characteristics from Twin Otter grid flights in BOREAS 1994.  Journal of Geophysical Research 102(D24): 29,135-29,145.

MacPherson, J.I. and A.K. Betts. 1997. Aircraft encounters with strong coherent vortices over the boreal forest. Journal of Geophysical Research 102(D24): 29,231-29,234.

MacPherson, J.I. and R.L. Desjardins. 1991. Airborne Tests of Flux Measurement by the Relaxed Eddy Accumulation Technique. Proceedings of the Seventh Symposium on Meteorological Observations and Instrumentation.  American Meteorological Society. New Orleans. January, 1991.

Sellers, P. and F. Hall. 1994. Boreal Ecosystem-Atmosphere Study: Experiment Plan. Version 1994-3.0, NASA BOREAS Report (EXPLAN 94).

Sellers, P. and F. Hall. 1996. Boreal Ecosystem-Atmosphere Study: Experiment Plan. Version 1996-2.0, NASA BOREAS Report (EXPLAN 96).

Sellers, P., F. Hall, and K.F. Huemmrich. 1996. Boreal Ecosystem-Atmosphere Study: 1994 Operations. NASA BOREAS Report (OPS DOC 94).

Sellers, P., F. Hall, and K.F. Huemmrich. 1997. Boreal Ecosystem-Atmosphere Study: 1996 Operations. NASA BOREAS Report (OPS DOC 96).

Sellers, P., F. Hall, H. Margolis, B. Kelly, D. Baldocchi, G. den Hartog, J. Cihlar, M.G. Ryan, B. Goodison, P. Crill, K.J. Ranson, D. Lettenmaier, and D.E. Wickland. 1995. The boreal ecosystem-atmosphere study (BOREAS): an overview and early results from the 1994 field year. Bulletin of the American Meteorological Society. 76(9):1549-1577.

Sellers, P.J., F.G. Hall, R.D. Kelly, A. Black, D. Baldocchi, J. Berry, M. Ryan, K.J. Ranson, P.M. Crill, D.P. Lettenmaier, H. Margolis, J. Cihlar, J.

Newcomer, D. Fitzjarrald, P.G. Jarvis, S.T. Gower, D. Halliwell, D. Williams, B. Goodison, D.E. Wickland, and F.E. Guertin. 1997. BOREAS in 1997:

Experiment Overview, Scientific Results and Future Directions. Journal of Geophysical Research 102(D24): 28,731-28,770.

17.3 Archive/DBMS Usage Documentation

None.

18. Glossary of Terms

None.

19. List of Acronyms

AES     - Atmospheric Environment Service

AFM     - Airborne Fluxes and Meteorology

AGL     - Above Ground Level

ASCII   - American Standard Code for Information Interchange

BOREAS  - BOReal Ecosystem-Atmosphere Study

BORIS   - BOREAS Information System

CD-ROM  - Compact Disk-Read-Only Memory

DAAC    - Distributed Active Archive Center

DAT     - Digital Archive Tape

EOS     - Earth Observing System

EOSDIS  - EOS Data and Information System

FIFE    - First ISLSCP Field Experiment

FIS     - FIFE Information System

FRL     - Flight Research Laboratory

GMT     - Greenwich Mean Time

GSFC    - Goddard Space Flight Center

HP      - high pass

HTML    - HyperText Markup Language

IAR     - Institute for Aerospace Research

IFC     - Intensive Field Campaign

INS     - Inertial Navigation System

IRS     - Inertial Reference System

ISLSCP  - International Satellite Land Surface Climatology Project

MSL     - Mean Sea Level

NAE     - National Aeronautical Establishment

NASA    - National Aeronautics and Space Administration

NCAR    - National Center for Atmospheric Research

NRC     - National Research Council, Canada

NSA     - Northern Study Area

ORNL    - Oak Ridge National Laboratory

PANP    - Prince Albert National Park

RMS     - Root Mean Square

SSA     - Southern Study Area

TAS     - True Air Speed

URL     - Uniform Resource Locator

20. Document Information

20.1 Document Revision Date

Written: 01-Jan-1993

Revision Date: 10-Aug-1999

20.2 Document Review Date(s)

BORIS Review:  30-Jun-1999

Science Review:

20.3 Document ID

20.4 Citation

These data were measured by the Twin Otter Atmospheric Research Aircraft operated by the National Research Council of Canada. J.I. MacPherson of NRC was the Principal Investigator responsible for the operation of the aircraft in BOREAS and the processing of the data. Other scientists on the Twin Otter project team were Ray Desjardins of Agriculture Canada and Peter Schuepp of McGill University. Funding for the Twin Otter participation in BOREAS was provided by Agriculture Canada, NSERC and the National Research Council of Canada.

20.5 Document Curator

20.6 Document URL

KEYWORDS

--------

CARBON DIOXIDE FLUX

OZONE

GREENNESS

MIXING RATIO

TEMPERATURE