Boreas Data Documentor Appendix 2 - Campbell Scientific Sample Programs for each of the 10 Sites.  This is in WordPerfect 6.1 format.

Appendix 1 - Programs for the Automatic Meteorological Stations Data - Mesocale Network

Program: Boreas  La Ronge, SK  August 11/94

Flag Usage:

Input Channel Usage:

Excitation Channel Usage:

Continuous Analog Output Usage:

Control Port Usage:

Pulse Input Channel Usage:

Output Array Definitions:

*     1       Table 1 Programs

01: 5       Sec. Execution Interval

01:  P18      Time                 Beginning of Program Time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 43      Loc [:FirstTime]

02:  P18      Time                 Time used for counting minutes

01: 1       Minutes into current day (maximum 1440)

02: 60      Mod/by

03: 64      Loc [:Minutes  ]

03:  P10      Battery Voltage            Battery Voltage

01: 25      Loc [:Battery V]

04:  P2       Volt (DIFF)                PAR Sensor         KJ/m*m

01: 1       Rep

02: 2       15 mV slow Range

03: 1       IN Chan

04: 1       Loc [:Par KJ/m2]

05: .5      Mult

06: 0       Offset

05:  P2       Volt (DIFF)                Net Radiometer    KJ/m*m

01: 1       Rep

02: 4       500 mV slow Range

03: 2       IN Chan

04: 2       Loc [:Net KJ/m2]

05: .0700   Mult

06: 0       Offset

06:  P2       Volt (DIFF)                Albedometer Up    KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 3       IN Chan

04: 3       Loc [:AlU KJ/m2]

05: .59453  Mult

06: 0       Offset

07:  P2       Volt (DIFF)                Albedometer Down   KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 4       IN Chan

04: 4       Loc [:AlD KJ/m2]

05: .56948  Mult

06: 0       Offset

08:  P30      Z=F                 Beginning of IR Sensor  deg C

01: 0       F

02: 29      Z Loc [:OV  Pw   ]

09:  P30      Z=F

01: 5000    F

02: 30      Z Loc [:5V  Pw   ]

10:  P21      Analog Out Set CAO channel 1 to 5000 mV

01: 1       CAO Chan

02: 30      mV Loc 5V  Pw

11:  P4       Excite,Delay,Volt(SE) Measures Ed and Erel

01: 1       Rep

02: 5       5000 mV slow Range

03: 9       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 100     Delay (units .01sec)

06: 1200    mV Excitation

07: 31      Loc [:Ed Volts ]

08: .001    Mult

09: 0       Offset

12:  P4       Excite,Delay,Volt(SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 10      IN Chan

04: 2       Excite all reps w/EXchan 2

05: 100     Delay (units .01sec)

06: 5000--  mV Excitation

07: 32      Loc [:Erel Volt]

08: .001    Mult

09: 0       Offset

13:  P89      If X<=>F

01: 31      X Loc Ed Volts

02: 3       >=

03: .42315  F

04: 30      Then Do

14:  P55      Polynomial

01: 1       Rep

02: 31      X Loc Ed Volts

03: 33      F(X) Loc [:Td C     ]

04: 48.653  C0

05: -302.29 C1

06: 658.31  C2

07: -911.19 C3

08: 660.33  C4

09: -201.44 C5

15:  P94      Else

16:  P89      If X<=>F

01: 31      X Loc Ed Volts

02: 3       >=

03: .03125  F

04: 30      Then Do

17:  P37      Z=X*F

01: 31      X Loc Ed Volts

02: 10      F

03: 34      Z Loc [:Temporary]

18:  P55      Polynomial

01: 1       Rep

02: 34      X Loc Temporary

03: 33      F(X) Loc [:Td C     ]

04: 88.341  C0

05: -140.82 C1

06: 131.86  C2

07: -74.476 C3

08: 23.529  C4

09: -3.8390 C5

19:  P30      Z=F

01: 6       F

02: 35      Z Loc [:Six      ]

20:  P47      Z=X^Y

01: 34      X Loc Temporary

02: 35      Y Loc Six

03: 34      Z Loc [:Temporary]

21:  P37      Z=X*F

01: 34      X Loc Temporary

02: .25131  F

03: 34      Z Loc [:Temporary]

22:  P33      Z=X+Y

01: 34      X Loc Temporary

02: 33      Y Loc Td C

03: 33      Z Loc [:Td C     ]

23:  P94      Else

24:  P37      Z=X*F

01: 31      X Loc Ed Volts

02: 100     F

03: 34      Z Loc [:Temporary]

25:  P55      Polynomial

01: 1       Rep

02: 34      X Loc Temporary

03: 33      F(X) Loc [:Td C     ]

04: 164.35  C0

05: -134.14 C1

06: 80.230  C2

07: -23.831 C3

08: 2.6569  C4

09: 0       C5

26:  P95      End

27:  P95      End

28:  P37      Z=X*F

01: 32      X Loc Erel Volt

02: 1       F

03: 32      Z Loc [:Erel Volt]

29:  P37      Z=X*F

01: 33      X Loc Td C

02: -.00224 F

03: 36      Z Loc [:Erel Mult]

30:  P34      Z=X+F

01: 36      X Loc Erel Mult

02: 1.0589  F

03: 36      Z Loc [:Erel Mult]

31:  P36      Z=X*Y

01: 32      X Loc Erel Volt

02: 36      Y Loc Erel Mult

03: 37      Z Loc [:Ecrel V  ]

32:  P55      Polynomial

01: 1       Rep

02: 37      X Loc Ecrel V

03: 38      F(X) Loc [:Trel C   ]

04: .0836   C0

05: 122     C1

06: -65.5   C2

07: 126.4   C3

08: -223.2  C4

09: 140.3   C5

33:  P33      Z=X+Y                    End of IR Sensor

01: 33      X Loc Td C

02: 38      Y Loc Trel C

03: 12      Z Loc [:IRSensorC]

34:  P21      Analog Out

01: 1       CAO Chan

02: 29      mV Loc OV  Pw

35:  P4       Excite,Delay,Volt(SE)    Wind Direction  degrees true

01: 1       Rep

02: 5       5000 mV slow Range

03: 11      IN Chan

04: 3       Excite all reps w/EXchan 3

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 13      Loc [:WindDdegT]

08: .071    Mult

09: 0       Offset

36:  P3       Pulse                     Wind Speed    metres/sec

01: 1       Rep

02: 2       Pulse Input Chan

03: 21      Low level AC; Output Hz.

04: 14      Loc [:WindS m/s]

05: .0980   Mult

06: 0       Offset

37:  P3       Pulse                    Tipping Bucket     mm

01: 1       Rep

02: 1       Pulse Input Chan

03: 2       Switch closure

04: 18      Loc [:TipBuc mm]

05: .03     Mult

06: 0       Offset

38:  P89      If X<=>F       On the 50th minute skip the multiplexer

01: 64      X Loc Minutes  and execute soil moisture in Table 2

02: 2       <>

03: 50      F

04: 30      Then Do

39:  P20      Set Port                  Start of Multiplexer

01: 1       Set high

02: 1       Port Number

40:  P20      Set Port

01: 1       Set high

02: 2       Port Number

41:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

42:  P20      Set Port

01: 0       Set low

02: 2       Port Number

43:  P8       Excite,Delay,Volt(DIFF)     Setra Pressure Sensor KPa

01: 1       Rep

02: 4       500 mV slow Range

03: 8       IN Chan

04: 1       Excite all reps w/EXchan 1

05: 1       Delay (units=.01sec)

06: 2500    mV Excitation

07: 11      Loc [:Press KPa]

08: .12     Mult

09: 80      Offset

44:  P20      Set Port

01: 1       Set high

02: 2       Port Number

45:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

46:  P20      Set Port

01: 0       Set low

02: 2       Port Number

47:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

48:  P20      Set Port

01: 1       Set high

02: 2       Port Number

49:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

50:  P20      Set Port

01: 0       Set low

02: 2       Port Number

51:  P11      Temp 107 Probe          Temperature at 10 cm    deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 7       Loc [:Soil 10cm]

05: 1       Mult

06: 0       Offset

52:  P20      Set Port

01: 1       Set high

02: 2       Port Number

53:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

54:  P20      Set Port

01: 0       Set low

02: 2       Port Number

55:  P11      Temp 107 Probe           Temperature at 20 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 8       Loc [:Soil 20cm]

05: 1       Mult

06: 0       Offset

56:  P20      Set Port

01: 1       Set high

02: 2       Port Number

57:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

58:  P20      Set Port

01: 0       Set low

02: 2       Port Number

59:  P11      Temp 107 Probe          Temperature at 50 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 9       Loc [:Soil 50cm]

05: 1       Mult

06: 0       Offset

60:  P20      Set Port

01: 1       Set high

02: 2       Port Number

61:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

62:  P20      Set Port

01: 0       Set low

02: 2       Port Number

63:  P4       Excite,Delay,Volt(SE)   107F Temperature LC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 26      Loc [:LC Store ]

08: .001    Mult

09: 0       Offset

64:  P55      Polynomial

01: 1       Rep

02: 26      X Loc LC Store

03: 6       F(X) Loc [:Temp LC C]

04: -74.159 C0              Coefficients for 35 foot cable -

05: 645.87  C1              lower canopy

06: -3844.6 C2

07: 16081   C3

08: -34152  C4

09: 29933   C5

65:  P34      Z=X+F

01: 6       X Loc Temp LC C

02: 273.15  F

03: 28      Z Loc [:Temp LC K]

66:  P20      Set Port

01: 1       Set high

02: 2       Port Number

67:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

68:  P20      Set Port

01: 0       Set low

02: 2       Port Number

69:  P4       Excite,Delay,Volt(SE)  HMP35CF Temperature UC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 27      Loc [:UC Store ]

08: .001    Mult

09: 0       Offset

70:  P55      Polynomial

01: 1       Rep

02: 27      X Loc UC Store

03: 5       F(X) Loc [:Temp UC C]

04: -74.168 C0              Coefficients for 50 foot cable -

05: 646.22  C1               upper canopy

06: -3848.9 C2

07: 16107   C3

08: -34225  C4

09: 30009   C5

71:  P20      Set Port

01: 1       Set high

02: 2       Port Number

72:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

73:  P20      Set Port

01: 0       Set low

02: 2       Port Number

74:  P4       Excite,Delay,Volt(SE)   HMP35CF Relative Humidity %RH

01: 1       Rep

02: 5       5000 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 15      Delay (units .01sec)

06: 5000    mV Excitation

07: 10      Loc [:Humid %RH]

08: .1      Mult

09: 0       Offset

75:  P20      Set Port

01: 0       Set low

02: 1       Port Number

76:  P30      Z=F               Beginning of Dewpoint Calculations

01: 9.5     F

02: 48      Z Loc [:a        ]

77:  P30      Z=F

01: 265.5   F

02: 49      Z Loc [:b        ]

78:  P37      Z=X*F

01: 5       X Loc Temp UC C

02: 9.5     F

03: 50      Z Loc [:a*T      ]

79:  P34      Z=X+F

01: 5       X Loc Temp UC C

02: 265.5   F

03: 51      Z Loc [:b+T      ]

80:  P38      Z=X/Y

01: 50      X Loc a*T

02: 51      Y Loc b+T

03: 52      Z Loc [:aT/b+T   ]

81:  P34      Z=X+F

01: 52      X Loc aT/b+T

02: -2      F

03: 53      Z Loc [:aT/b+T-2 ]

82:  P40      Z=LN(X)

01: 10      X Loc Humid %RH

02: 54      Z Loc [:ln(RH)   ]

83:  P30      Z=F

01: 2.303   F

02: 55      Z Loc [:ln/log   ]

84:  P38      Z=X/Y

01: 54      X Loc ln(RH)

02: 55      Y Loc ln/log

03: 56      Z Loc [:log (RH) ]

85:  P33      Z=X+Y

01: 56      X Loc log (RH)

02: 53      Y Loc aT/b+T-2

03: 57      Z Loc [:log +aT/b]

86:  P38      Z=X/Y

01: 48      X Loc a

02: 57      Y Loc log +aT/b

03: 58      Z Loc [:a/logRH  ]

87:  P38      Z=X/Y

01: 49      X Loc b

02: 58      Y Loc a/logRH

03: 22      Z Loc [:Dewpoint ]       End of Dewpoint Calculations

88:  P95      End

89:  P92      If time is

01: 0       minutes into a

02: 1       minute interval

03: 30      Then Do

90:  P89      If X<=>F

01: 64      X Loc Minutes

02: 3       >=

03: 55      F

04: 30      Then Do

91:  P4       Excite,Delay,Volt(SE)     Belfort Weighing Gauge

01: 1       Rep

02: 5       5000 mV slow Range

03: 12      IN Chan

04: 4       Excite all reps w/EXchan 4

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 19      Loc [:Belfortmm]

08: .07826  Mult

09: 0       Offset

92:  P20      Set Port                   Begin Snow Depth Sensor

01: 1       Set high

02: 6       Port Number

93:  P20      Set Port

01: 0       Set low

02: 4       Port Number

94:  P20      Set Port

01: 1       Set high

02: 5       Port Number

95:  P20      Set Port

01: 0       Set low

02: 5       Port Number

96:  P20      Set Port

01: 1       Set high

02: 4       Port Number

97:  P20      Set Port

01: 1       Set high

02: 5       Port Number

98:  P20      Set Port

01: 0       Set low

02: 5       Port Number

99:  P20      Set Port

01: 0       Set low

02: 4       Port Number

100: P87      Beginning of Loop

01: 0       Delay

02: 6       Loop Count

101: P20      Set Port

01: 1       Set high

02: 5       Port Number

102: P20      Set Port

01: 0       Set low

02: 5       Port Number

103: P95      End

104: P20      Set Port

01: 1       Set high

02: 5       Port Number

105: P22      Excitation with Delay

01: 1       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

106: P20      Set Port

01: 0       Set low

02: 6       Port Number

107: P20      Set Port

01: 1       Set high

02: 6       Port Number

108: P22      Excitation with Delay

01: 1       EX Chan

02: 8       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

109: P20      Set Port

01: 0       Set low

02: 5       Port Number

110: P30      Z=F

01: 1       F

02: 39      Z Loc [:Snow Calc]

111: P30      Z=F

01: 0       F

02: 42      Z Loc [:Snow # Pu]

112: P87      Beginning of Loop

01: 0       Delay

02: 16      Loop Count

113: P20      Set Port

01: 1       Set high

02: 5       Port Number

114: P20      Set Port

01: 0       Set low

02: 5       Port Number

115: P1       Volt (SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 13      IN Chan

04: 40      Loc [:Snow Data]

05: 1       Mult

06: 0       Offset

116: P89      If X<=>F

01: 40      X Loc Snow Data

02: 3       >=

03: 3000    F

04: 30      Then Do

117: P33      Z=X+Y

01: 39      X Loc Snow Calc

02: 42      Y Loc Snow # Pu

03: 42      Z Loc [:Snow # Pu]

118: P95      End

119: P37      Z=X*F

01: 39      X Loc Snow Calc

02: 2       F

03: 39      Z Loc [:Snow Calc]

120: P95      End

121: P30      Z=F

01: 291     F

02: 41      Z Loc [:T2 291 K ]

122: P38      Z=X/Y

01: 28      X Loc Temp LC K

02: 41      Y Loc T2 291 K

03: 20      Z Loc [:Snow D mm]

123: P39      Z=SQRT(X)

01: 20      X Loc Snow D mm

02: 20      Z Loc [:Snow D mm]

124: P36      Z=X*Y

01: 42      X Loc Snow # Pu

02: 20      Y Loc Snow D mm

03: 20      Z Loc [:Snow D mm]

125: P37      Z=X*F

01: 20      X Loc Snow D mm

02: .52176  F

03: 20      Z Loc [:Snow D mm]

126: P34      Z=X+F

01: 20      X Loc Snow D mm

02: -39     F

03: 20      Z Loc [:Snow D mm]

127: P20      Set Port

01: 0       Set low

02: 4       Port Number

128: P20      Set Port

01: 0       Set low

02: 5       Port Number

129: P20      Set Port                 End of Snow Depth

01: 0       Set low

02: 6       Port Number

130: P89      If X<=>F           Five Minute Average at the top of

01: 64      X Loc Minutes   the hour for Belfort and Snow Depth

02: 1       =

03: 59      F

04: 10      Set high Flag 0 (output)

131: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 15      Array ID or location

132: P71      Average

01: 2       Reps

02: 19      Loc Belfortmm

133: P95      End

134: P95      End

135: P92      If time is

01: 0       minutes into a

02: 60      minute interval

03: 30      Then Do

136: P35      Z=X-Y

01: 15      X Loc Av Belfor

02: 59      Y Loc Prev Belf

03: 60      Z Loc [:Belf Diff]

137: P31      Z=X

01: 15      X Loc Av Belfor

02: 59      Z Loc [:Prev Belf]

138: P95      End

139: P89      If X<=>F          Two minute average of Wind Speed

01: 64      X Loc Minutes     and Direction at top of the hour

02: 3       >=

03: 58      F

04: 10      Set high Flag 0 (output)

140: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 23      Array ID or location

141: P69      Wind Vector

01: 1       Rep

02: 0       Samples per sub-interval

03: 1       Polar Sensor/(S, D1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

142: P92      If time is

01: 59      minutes into a

02: 60      minute interval

03: 10      Set high Flag 0 (output)

143: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 61      Array ID or location

144: P71      Average          One minute average of Pressure

01: 1       Rep              at top of the hour

02: 11      Loc Press KPa

145: P71      Average          One minute average of Temperature

01: 1       Rep              at top of the hour

02: 5       Loc Temp UC C

146: P71      Average            Average Dewpoint for the hour

01: 1       Rep

02: 22      Loc Dewpoint

147: P92      If time is            Begin writing to the array -

01: 0       minutes into a        15 minute interval

02: 15      minute interval

03: 10      Set high Flag 0 (output)

148: P80      Set Active Storage Area

01: 1       Final Storage Area

02: 1       Array ID or location

149: P70      Sample                     Sample Battery

01: 1       Rep

02: 25      Loc Battery V

150: P77      Real Time                  Year, Day, Time

01: 1110    Year,Day,Hour-Minute

151: P78      Resolution

01: 1       High Resolution

152: P72      Totalize           Totalize Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Loc Par KJ/m2

153: P78      Resolution

01: 0       Low Resolution

154: P82      Standard Deviation Std Dev Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Sample Loc Par KJ/m2

155: P71      Average           Average TempUC, TempLC, Temp10

01: 6       Reps              Temp20, Temp50, RelHum

02: 5       Loc Temp UC C

156: P78      Resolution

01: 1       High Resolution

157: P71      Average           Average Pressure

01: 1       Rep

02: 11      Loc Press KPa

158: P78      Resolution

01: 0       Low Resolution

159: P71      Average           Average IRSensor

01: 1       Rep

02: 12      Loc IRSensorC

160: P82      Standard Deviation Std Dev Temp UC, TempLC, Temp10

01: 8       Reps               Temp20, Temp50, RelHum, Pressure

02: 5       Sample Loc Temp UC C IRSensor

161: P69      Wind Vector      Average Wind Speed, Wind Direction

01: 1       Rep                   and Std Dev Wind Direction

02: 0       Samples per sub-interval

03: 0       Polar Sensor/(S, D1, SD1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

162: P82      Standard Deviation      Std Dev Wind Speed

01: 1       Rep

02: 14      Sample Loc WindS m/s

163: P70      Sample                Sample Belfort, Snow Depth

01: 2       Reps                  Average of last 5 minutes

02: 15      Loc Av Belfor         of the hour

164: P72      Totalize                Totalize Tip Bucket

01: 1       Rep

02: 18      Loc TipBuc mm

165: P33      Z=X+Y

01: 18      X Loc TipBuc mm

02: 65      Y Loc Total Tip

03: 65      Z Loc [:Total Tip]

166: P70      Sample                     Sample Soil Moisture

01: 1       Rep                       Average of minute 50

02: 17      Loc Av Soil M             of the hour

167: P78      Resolution

01: 1       High Resolution

168: P70      Sample           Sample Pressure for GTS

01: 1       Rep

02: 61      Loc Press 1hr

169: P78      Resolution

01: 0       Low Resolution

170: P70      Sample      Sample TempUC, Dewpoint for GTS

01: 2       Reps

02: 62      Loc Temp  1hr

171: P70      Sample           Sample Wind Dir for GTS

01: 1       Rep

02: 24      Loc WindD 1hr

172: P70      Sample         Sample Wind Speed for GTS

01: 1       Rep

02: 23      Loc WindS 1hr

173: P70      Sample           Sample Belfort difference from

01: 1       Rep              previous hour

02: 60      Loc Belf Diff

174: P70      Sample          Sample Total Tipping Bucket for season

01: 1       Rep

02: 65      Loc Total Tip

175: P70      Sample

01: 2       Reps

02: 73      Loc ThC 1sec

176: P96      Serial Output

01: 30      SM192/SM716/CSM1

177: P18      Time                Store end of Program time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 45      Loc [:LastTime ]

178: P35      Z=X-Y                Program Execution Time

01: 45      X Loc LastTime

02: 43      Y Loc FirstTime

03: 44      Z Loc [:Prog Time]

179: P        End Table 1

*     2       Table 2 Programs

01: 60      Sec. Execution Interval

01:  P92      If time is

01: 50      minutes into a

02: 60      minute interval

03: 30      Then Do

02:  P89      If X<=>F

01: 43      X Loc FirstTime

02: 4       <

03: 200     F

04: 30      Then Do

03:  P86      Do

01: 10      Set high Flag 0 (output)

04:  P30      Z=F

01: 0       F

02: 29      Z Loc [:OV  Pw   ]

05:  P30      Z=F

01: 2000    F

02: 66      Z Loc [:2V  Pw   ]

06:  P17      Panel Temperature

01: 67      Loc [:PanelTemp]

07:  P20      Set Port

01: 1       Set high

02: 1       Port Number

08:  P87      Beginning of Loop

01: 0       Delay

02: 2       Loop Count

09:  P20      Set Port

01: 1       Set high

02: 2       Port Number

10:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

11:  P20      Set Port

01: 0       Set low

02: 2       Port Number

12:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0.0000  mV Excitation

13:  P95      End

14:  P21      Analog Out

01: 2       CAO Chan

02: 66      mV Loc 2V  Pw

15:  P22      Excitation with Delay

01: 4       EX Chan

02: 100     Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

16:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 46      Loc [:ThC 1 sec]

07: 1       Mult

08: 0       Offset

17:  P22      Excitation with Delay

01: 4       EX Chan

02: 2000    Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

18:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 47      Loc [:ThC 21sec]

07: 1       Mult

08: 0       Offset

19:  P21      Analog Out

01: 2       CAO Chan

02: 29      mV Loc OV  Pw

20:  P20      Set Port

01: 0       Set low

02: 1       Port Number

21:  P35      Z=X-Y                   End of Soil Moisture

01: 47      X Loc ThC 21sec

02: 46      Y Loc ThC 1 sec

03: 68      Z Loc [:Soil Diff]

22:  P37      Z=X*F

01: 68      X Loc Soil Diff

02: 4.89    F

03: 69      Z Loc [:Soil Mult]

23:  P30      Z=F

01: 10      F

02: 70      Z Loc [:Soil Ten ]

24:  P47      Z=X^Y

01: 70      X Loc Soil Ten

02: 69      Y Loc Soil Mult

03: 71      Z Loc [:Soil Sub ]

25:  P37      Z=X*F

01: 71      X Loc Soil Sub

02: .00026  F

03: 72      Z Loc [:Soil Res ]

26:  P37      Z=X*F

01: 72      X Loc Soil Res

02: .1      F

03: 21      Z Loc [:Soil MPa ]

27:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 17      Array ID or location

28:  P70      Sample

01: 1       Rep

02: 21      Loc Soil MPa

29:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 73      Array ID or location

30:  P70      Sample

01: 2       Reps

02: 46      Loc ThC 1 sec

31:  P95      End

32:  P95      End

33:  P        End Table 2

*     3       Table 3 Subroutines

01:  P        End Table 3

*     4       Mode 4 Output Options

01: 0       (Tape OFF) (Printer OFF)

02: 0       Printer 300 Baud

*     A       Mode 10 Memory Allocation

01: 76      Input Locations

02: 130     Intermediate Locations

*     C       Mode 12 Security (OSX-0)

01: 00      Security Option

02: 0000    Security Code

Key:

T=Table Number

E=Entry Number

L=Location Number

T:  E:  L:

1:  4:  1:  Loc [:Par KJ/m2]

1:  5:  2:  Loc [:Net KJ/m2]

1:  6:  3:  Loc [:AlU KJ/m2]

1:  7:  4:  Loc [:AlD KJ/m2]

1: 70:  5:  F(X) Loc [:Temp UC C]

1: 64:  6:  F(X) Loc [:Temp LC C]

1: 51:  7:  Loc [:Soil 10cm]

1: 55:  8:  Loc [:Soil 20cm]

1: 59:  9:  Loc [:Soil 50cm]

1: 74: 10:  Loc [:Humid %RH]

1: 43: 11:  Loc [:Press KPa]

1: 33: 12:  Z Loc [:IRSensorC]

1: 35: 13:  Loc [:WindDdegT]

1: 36: 14:  Loc [:WindS m/s]

1: 37: 18:  Loc [:TipBuc mm]

1: 91: 19:  Loc [:Belfortmm]

1:122: 20:  Z Loc [:Snow D mm]

1:123: 20:  Z Loc [:Snow D mm]

1:124: 20:  Z Loc [:Snow D mm]

1:125: 20:  Z Loc [:Snow D mm]

1:126: 20:  Z Loc [:Snow D mm]

2: 26: 21:  Z Loc [:Soil MPa ]

1: 87: 22:  Z Loc [:Dewpoint ]       End of Dewpoint Calculations

1:  3: 25:  Loc [:Battery V]

1: 63: 26:  Loc [:LC Store ]

1: 69: 27:  Loc [:UC Store ]

1: 65: 28:  Z Loc [:Temp LC K]

1:  8: 29:  Z Loc [:OV  Pw   ]

2:  4: 29:  Z Loc [:OV  Pw   ]

1:  9: 30:  Z Loc [:5V  Pw   ]

1: 11: 31:  Loc [:Ed Volts ]

1: 12: 32:  Loc [:Erel Volt]

1: 28: 32:  Z Loc [:Erel Volt]

1: 14: 33:  F(X) Loc [:Td C     ]

1: 18: 33:  F(X) Loc [:Td C     ]

1: 22: 33:  Z Loc [:Td C     ]

1: 25: 33:  F(X) Loc [:Td C     ]

1: 17: 34:  Z Loc [:Temporary]

1: 20: 34:  Z Loc [:Temporary]

1: 21: 34:  Z Loc [:Temporary]

1: 24: 34:  Z Loc [:Temporary]

1: 19: 35:  Z Loc [:Six      ]

1: 29: 36:  Z Loc [:Erel Mult]

1: 30: 36:  Z Loc [:Erel Mult]

1: 31: 37:  Z Loc [:Ecrel V  ]

1: 32: 38:  F(X) Loc [:Trel C   ]

1:110: 39:  Z Loc [:Snow Calc]

1:119: 39:  Z Loc [:Snow Calc]

1:115: 40:  Loc [:Snow Data]

1:121: 41:  Z Loc [:T2 291 K ]

1:111: 42:  Z Loc [:Snow # Pu]

1:117: 42:  Z Loc [:Snow # Pu]

1:  1: 43:  Loc [:FirstTime]

1:178: 44:  Z Loc [:Prog Time]

1:177: 45:  Loc [:LastTime ]

2: 16: 46:  Loc [:ThC 1 sec]

2: 18: 47:  Loc [:ThC 21sec]

1: 76: 48:  Z Loc [:a        ]

1: 77: 49:  Z Loc [:b        ]

1: 78: 50:  Z Loc [:a*T      ]

1: 79: 51:  Z Loc [:b+T      ]

1: 80: 52:  Z Loc [:aT/b+T   ]

1: 81: 53:  Z Loc [:aT/b+T-2 ]

1: 82: 54:  Z Loc [:ln(RH)   ]

1: 83: 55:  Z Loc [:ln/log   ]

1: 84: 56:  Z Loc [:log (RH) ]

1: 85: 57:  Z Loc [:log +aT/b]

1: 86: 58:  Z Loc [:a/logRH  ]

1:137: 59:  Z Loc [:Prev Belf]

1:136: 60:  Z Loc [:Belf Diff]

1:  2: 64:  Loc [:Minutes  ]

1:165: 65:  Z Loc [:Total Tip]

2:  5: 66:  Z Loc [:2V  Pw   ]

2:  6: 67:  Loc [:PanelTemp]

2: 21: 68:  Z Loc [:Soil Diff]

2: 22: 69:  Z Loc [:Soil Mult]

2: 23: 70:  Z Loc [:Soil Ten ]

2: 24: 71:  Z Loc [:Soil Sub ]

2: 25: 72:  Z Loc [:Soil Res ]

Page 24    Input Location Labels:

1:Par KJ/m2    20:Snow D mm    39:Snow Calc    58:a/logRH

2:Net KJ/m2    21:Soil MPa     40:Snow Data    59:Prev Belf

3:AlU KJ/m2    22:Dewpoint     41:T2 291 K     60:Belf Diff

4:AlD KJ/m2    23:WindS 1hr    42:Snow # Pu    61:Press 1hr

5:Temp UC C    24:WindD 1hr    43:FirstTime    62:Temp  1hr

6:Temp LC C    25:Battery V    44:Prog Time    63:Dewpt 1hr

7:Soil 10cm    26:LC Store     45:LastTime     64:Minutes

8:Soil 20cm    27:UC Store     46:ThC 1 sec    65:Total Tip

9:Soil 50cm    28:Temp LC K    47:ThC 21sec    66:2V  Pw

10:Humid %RH    29:OV  Pw       48:a            67:PanelTemp

11:Press KPa    30:5V  Pw       49:b            68:Soil Diff

12:IRSensorC    31:Ed Volts     50:a*T          69:Soil Mult

13:WindDdegT    32:Erel Volt    51:b+T          70:Soil Ten

14:WindS m/s    33:Td C         52:aT/b+T       71:Soil Sub

15:Av Belfor    34:Temporary    53:aT/b+T-2     72:Soil Res

16:Av Snow D    35:Six          54:ln(RH)       73:ThC 1sec

17:Av Soil M    36:Erel Mult    55:ln/log       74:ThC 21sec

18:TipBuc mm    37:Ecrel V      56:log (RH)     75:_________

19:Belfortmm    38:Trel C       57:log +aT/b    76:_________

Program: Boreas  Meadow Lake, SK  Aug 31/95

Flag Usage:

Input Channel Usage:

Excitation Channel Usage:

Continuous Analog Output Usage:

Control Port Usage:

Pulse Input Channel Usage:

Output Array Definitions:

*     1       Table 1 Programs

01: 5       Sec. Execution Interval

01:  P18      Time                 Beginning of Program Time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 43      Loc [:FirstTime]

02:  P18      Time                 Time used for counting minutes

01: 1       Minutes into current day (maximum 1440)

02: 60      Mod/by

03: 64      Loc [:Minutes  ]

03:  P10      Battery Voltage            Battery Voltage

01: 25      Loc [:Battery V]

04:  P2       Volt (DIFF)                PAR Sensor         KJ/m*m

01: 1       Rep

02: 2       15 mV slow Range

03: 1       IN Chan

04: 1       Loc [:Par KJ/m2]

05: .5      Mult

06: 0       Offset

05:  P2       Volt (DIFF)                Net Radiometer    KJ/m*m

01: 1       Rep

02: 4       500 mV slow Range

03: 2       IN Chan

04: 2       Loc [:Net KJ/m2]

05: .065    Mult

06: 0       Offset

06:  P2       Volt (DIFF)                Albedometer Up    KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 3       IN Chan

04: 3       Loc [:AlU KJ/m2]

05: .63939  Mult

06: 0       Offset

07:  P2       Volt (DIFF)                Albedometer Down   KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 4       IN Chan

04: 4       Loc [:AlD KJ/m2]

05: .60459  Mult

06: 0       Offset

08:  P30      Z=F                 No IR Sensor at this site

01: -999    F

02: 12      Z Loc [:IRSensorC]

09:  P4       Excite,Delay,Volt(SE)    Wind Direction  degrees true

01: 1       Rep

02: 5       5000 mV slow Range

03: 11      IN Chan

04: 3       Excite all reps w/EXchan 3

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 13      Loc [:WindDdegT]

08: .071    Mult

09: 0       Offset

10:  P3       Pulse                     Wind Speed    metres/sec

01: 1       Rep

02: 2       Pulse Input Chan

03: 21      Low level AC; Output Hz.

04: 14      Loc [:WindS m/s]

05: .0980   Mult

06: 0       Offset

11:  P3       Pulse                    Tipping Bucket     mm

01: 1       Rep

02: 1       Pulse Input Chan

03: 2       Switch closure

04: 18      Loc [:TipBuc mm]

05: .025    Mult

06: 0       Offset

12:  P89      If X<=>F      On the 50th minute skip the multiplexer

01: 64      X Loc Minutes and execute soil moisture in Table 2

02: 2       <>

03: 50      F

04: 30      Then Do

13:  P20      Set Port                  Start of multiplexer

01: 1       Set high

02: 1       Port Number

14:  P22      Excitation with Delay

01: 2       EX Chan

02: 2       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

15:  P8       Excite,Delay,Volt(DIFF)     Setra Pressure Sensor KPa

01: 1       Rep

02: 4       500 mV slow Range

03: 8       IN Chan

04: 1       Excite all reps w/EXchan 1

05: 1       Delay (units=.01sec)

06: 2500    mV Excitation

07: 11      Loc [:Press KPa]

08: .12     Mult

09: 80      Offset

16:  P22      Excitation with Delay

01: 2       EX Chan

02: 2       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

17:  P22      Excitation with Delay

01: 2       EX Chan

02: 2       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

18:  P11      Temp 107 Probe          Temperature at 10 cm    deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 7       Loc [:Soil 10cm]

05: 1       Mult

06: 0       Offset

19:  P22      Excitation with Delay

01: 2       EX Chan

02: 2       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

20:  P11      Temp 107 Probe           Temperature at 20 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 8       Loc [:Soil 20cm]

05: 1       Mult

06: 0       Offset

21:  P22      Excitation with Delay

01: 2       EX Chan

02: 2       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

22:  P11      Temp 107 Probe          Temperature at 50 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 9       Loc [:Soil 50cm]

05: 1       Mult

06: 0       Offset

23:  P22      Excitation with Delay

01: 2       EX Chan

02: 2       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

24:  P30      Z=F                 No 107F Temperature at this site

01: -999    F

02: 6       Z Loc [:Temp LC C]

25:  P22      Excitation with Delay

01: 2       EX Chan

02: 2       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

26:  P4       Excite,Delay,Volt(SE)  HMP35CF Temperature UC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 27      Loc [:UC Store ]

08: .001    Mult

09: 0       Offset

27:  P55      Polynomial

01: 1       Rep

02: 27      X Loc UC Store

03: 5       F(X) Loc [:Temp in C]

04: -74.221 C0              Coefficients for 140 foot cable

05: 648.34  C1

06: -3875.8 C2

07: 16274   C3

08: -34691  C4

09: 30508   C5

28:  P34      Z=X+F

01: 5       X Loc Temp in C

02: 273.15  F

03: 28      Z Loc [:Temp in K]

29:  P22      Excitation with Delay

01: 2       EX Chan

02: 2       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

30:  P4       Excite,Delay,Volt(SE)   HMP35CF Relative Humidity %RH

01: 1       Rep

02: 5       5000 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 15      Delay (units .01sec)

06: 5000    mV Excitation

07: 10      Loc [:Humid %RH]

08: .1      Mult

09: 0       Offset

31:  P20      Set Port                 End of Multiplexer

01: 0       Set low

02: 1       Port Number

32:  P30      Z=F               Beginning of Dewpoint Calculations

01: 9.5     F

02: 48      Z Loc [:a        ]

33:  P30      Z=F

01: 265.5   F

02: 49      Z Loc [:b        ]

34:  P37      Z=X*F

01: 5       X Loc Temp in C

02: 9.5     F

03: 50      Z Loc [:a*T      ]

35:  P34      Z=X+F

01: 5       X Loc Temp in C

02: 265.5   F

03: 51      Z Loc [:b+T      ]

36:  P38      Z=X/Y

01: 50      X Loc a*T

02: 51      Y Loc b+T

03: 52      Z Loc [:aT/b+T   ]

37:  P34      Z=X+F

01: 52      X Loc aT/b+T

02: -2      F

03: 53      Z Loc [:aT/b+T-2 ]

38:  P40      Z=LN(X)

01: 10      X Loc Humid %RH

02: 54      Z Loc [:ln(RH)   ]

39:  P30      Z=F

01: 2.303   F

02: 55      Z Loc [:ln/log   ]

40:  P38      Z=X/Y

01: 54      X Loc ln(RH)

02: 55      Y Loc ln/log

03: 56      Z Loc [:log (RH) ]

41:  P33      Z=X+Y

01: 56      X Loc log (RH)

02: 53      Y Loc aT/b+T-2

03: 57      Z Loc [:log +aT/b]

42:  P38      Z=X/Y

01: 48      X Loc a

02: 57      Y Loc log +aT/b

03: 58      Z Loc [:a/logRH  ]

43:  P38      Z=X/Y

01: 49      X Loc b

02: 58      Y Loc a/logRH

03: 22      Z Loc [:Dewpoint ]       End of Dewpoint Calculations

44:  P95      End

45:  P92      If time is

01: 0       minutes into a

02: 1       minute interval

03: 30      Then Do

46:  P89      If X<=>F

01: 64      X Loc Minutes

02: 3       >=

03: 55      F

04: 30      Then Do

47:  P20      Set Port             Belfort Weighing Gauge mm

01: 1       Set high

02: 3       Port Number

48:  P20      Set Port

01: 1       Set high

02: 2       Port Number

49:  P22      Excitation with Delay

01: 2       EX Chan

02: 20      Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

50:  P20      Set Port

01: 0       Set low

02: 3       Port Number

51:  P20      Set Port

01: 1       Set high

02: 3       Port Number

52:  P20      Set Port

01: 0       Set low

02: 2       Port Number

53:  P30      Z=F

01: 0       F

02: 19      Z Loc [:Belfortmm]

54:  P30      Z=F

01: 1       F

02: 31      Z Loc [:Weightx10]

55:  P87      Beginning of Loop

01: 0       Delay

02: 3       Loop Count

56:  P30      Z=F

01: 1       F

02: 32      Z Loc [:Weightx2 ]

57:  P30      Z=F

01: 0       F

02: 33      Z Loc [:Subtotal ]

58:  P87      Beginning of Loop

01: 0       Delay

02: 4       Loop Count

59:  P1       Volt (SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 12      IN Chan

04: 34      Loc [:HI or LO ]

05: 1       Mult

06: 0       Offset

60:  P89      If X<=>F

01: 34      X Loc HI or LO

02: 3       >=

03: 3000    F

04: 30      Then Do

61:  P33      Z=X+Y

01: 32      X Loc Weightx2

02: 33      Y Loc Subtotal

03: 33      Z Loc [:Subtotal ]

62:  P95      End

63:  P20      Set Port

01: 1       Set high

02: 2       Port Number

64:  P20      Set Port

01: 0       Set low

02: 2       Port Number

65:  P37      Z=X*F

01: 32      X Loc Weightx2

02: 2       F

03: 32      Z Loc [:Weightx2 ]

66:  P95      End

67:  P36      Z=X*Y

01: 33      X Loc Subtotal

02: 31      Y Loc Weightx10

03: 33      Z Loc [:Subtotal ]

68:  P33      Z=X+Y

01: 33      X Loc Subtotal

02: 19      Y Loc Belfortmm

03: 19      Z Loc [:Belfortmm]

69:  P37      Z=X*F

01: 31      X Loc Weightx10

02: 10      F

03: 31      Z Loc [:Weightx10]

70:  P95      End

71:  P20      Set Port

01: 0       Set low

02: 3       Port Number

72:  P20      Set Port

01: 0       Set low

02: 2       Port Number

73:  P20      Set Port                   Begin Snow Depth Sensor

01: 1       Set high

02: 6       Port Number

74:  P20      Set Port

01: 0       Set low

02: 4       Port Number

75:  P20      Set Port

01: 1       Set high

02: 5       Port Number

76:  P20      Set Port

01: 0       Set low

02: 5       Port Number

77:  P20      Set Port

01: 1       Set high

02: 4       Port Number

78:  P20      Set Port

01: 1       Set high

02: 5       Port Number

79:  P20      Set Port

01: 0       Set low

02: 5       Port Number

80:  P20      Set Port

01: 0       Set low

02: 4       Port Number

81:  P87      Beginning of Loop

01: 0       Delay

02: 6       Loop Count

82:  P20      Set Port

01: 1       Set high

02: 5       Port Number

83:  P20      Set Port

01: 0       Set low

02: 5       Port Number

84:  P95      End

85:  P20      Set Port

01: 1       Set high

02: 5       Port Number

86:  P22      Excitation with Delay

01: 1       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

87:  P20      Set Port

01: 0       Set low

02: 6       Port Number

88:  P20      Set Port

01: 1       Set high

02: 6       Port Number

89:  P22      Excitation with Delay

01: 1       EX Chan

02: 8       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

90:  P20      Set Port

01: 0       Set low

02: 5       Port Number

91:  P30      Z=F

01: 1       F

02: 39      Z Loc [:Snow Calc]

92:  P30      Z=F

01: 0       F

02: 42      Z Loc [:Snow # Pu]

93:  P87      Beginning of Loop

01: 0       Delay

02: 16      Loop Count

94:  P20      Set Port

01: 1       Set high

02: 5       Port Number

95:  P20      Set Port

01: 0       Set low

02: 5       Port Number

96:  P1       Volt (SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 13      IN Chan

04: 40      Loc [:Snow Data]

05: 1       Mult

06: 0       Offset

97:  P89      If X<=>F

01: 40      X Loc Snow Data

02: 3       >=

03: 3000    F

04: 30      Then Do

98:  P33      Z=X+Y

01: 39      X Loc Snow Calc

02: 42      Y Loc Snow # Pu

03: 42      Z Loc [:Snow # Pu]

99:  P95      End

100: P37      Z=X*F

01: 39      X Loc Snow Calc

02: 2       F

03: 39      Z Loc [:Snow Calc]

101: P95      End

102: P30      Z=F

01: 291     F

02: 41      Z Loc [:T2 291 K ]

103: P38      Z=X/Y

01: 28      X Loc Temp in K

02: 41      Y Loc T2 291 K

03: 20      Z Loc [:Snow D mm]

104: P39      Z=SQRT(X)

01: 20      X Loc Snow D mm

02: 20      Z Loc [:Snow D mm]

105: P36      Z=X*Y

01: 42      X Loc Snow # Pu

02: 20      Y Loc Snow D mm

03: 20      Z Loc [:Snow D mm]

106: P37      Z=X*F

01: 20      X Loc Snow D mm

02: .52176  F

03: 20      Z Loc [:Snow D mm]

107: P34      Z=X+F

01: 20      X Loc Snow D mm

02: -39     F

03: 20      Z Loc [:Snow D mm]

108: P20      Set Port

01: 0       Set low

02: 4       Port Number

109: P20      Set Port

01: 0       Set low

02: 5       Port Number

110: P20      Set Port                 End of Snow Depth

01: 0       Set low

02: 6       Port Number

111: P89      If X<=>F          Five Minute Average at the top of

01: 64      X Loc Minutes    the hour for Belfort and Snow Depth

02: 1       =

03: 59      F

04: 10      Set high Flag 0 (output)

112: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 15      Array ID or location

113: P71      Average

01: 2       Reps

02: 19      Loc Belfortmm

114: P95      End

115: P95      End

116: P92      If time is             Calculate the Belfort change

01: 0       minutes into a         from the previous hour

02: 60      minute interval

03: 30      Then Do

117: P35      Z=X-Y

01: 15      X Loc Av Belfor

02: 59      Y Loc Prev Belf

03: 60      Z Loc [:Belf Diff]

118: P31      Z=X

01: 15      X Loc Av Belfor

02: 59      Z Loc [:Prev Belf]

119: P95      End

120: P89      If X<=>F           Two minute average of Wind Speed

01: 64      X Loc Minutes      and Direction at top of the hour

02: 3       >=

03: 58      F

04: 10      Set high Flag 0 (output)

121: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 23      Array ID or location

122: P69      Wind Vector

01: 1       Rep

02: 0       Samples per sub-interval

03: 1       Polar Sensor/(S, D1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

123: P92      If time is

01: 59      minutes into a

02: 60      minute interval

03: 10      Set high Flag 0 (output)

124: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 61      Array ID or location

125: P71      Average            One minute average of Pressure

01: 1       Rep                at top of the hour

02: 11      Loc Press KPa

126: P71      Average            One minute average of Temperature

01: 1       Rep                at top of the hour

02: 5       Loc Temp in C

127: P71      Average            One minute average of Dewpoint

01: 1       Rep                at top of the hour

02: 22      Loc Dewpoint

128: P92      If time is            Begin writing to the array -

01: 0       minutes into a        15 minute interval

02: 15      minute interval

03: 10      Set high Flag 0 (output)

129: P80      Set Active Storage Area

01: 1       Final Storage Area

02: 2       Array ID or location

130: P70      Sample                     Sample Battery

01: 1       Rep

02: 25      Loc Battery V

131: P77      Real Time                  Year, Day, Time

01: 1110    Year,Day,Hour-Minute

132: P78      Resolution

01: 1       High Resolution

133: P72      Totalize           Totalize Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Loc Par KJ/m2

134: P78      Resolution

01: 0       Low Resolution

135: P82      Standard Deviation Std Dev Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Sample Loc Par KJ/m2

136: P71      Average           Average TempUC, TempLC, Temp10

01: 6       Reps              Temp20, Temp50, RelHum

02: 5       Loc Temp in C

137: P78      Resolution

01: 1       High Resolution

138: P71      Average                Average Pressure

01: 1       Rep

02: 11      Loc Press KPa

139: P78      Resolution

01: 0       Low Resolution

140: P71      Average                Average IRSensor

01: 1       Rep

02: 12      Loc IRSensorC

141: P82      Standard Deviation Std Dev Temp UC, TempLC, Temp10

01: 8       Reps               Temp20, Temp50, RelHum, Pressure

02: 5       Sample Loc Temp in CIRSensor

142: P69      Wind Vector      Average Wind Speed, Wind Direction

01: 1       Rep                   and Std Dev Wind Direction

02: 0       Samples per sub-interval

03: 0       Polar Sensor/(S, D1, SD1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

143: P82      Standard Deviation      Std Dev Wind Speed

01: 1       Rep

02: 14      Sample Loc WindS m/s

144: P70      Sample                Sample Belfort, Snow Depth

01: 2       Reps                  Average of last 5 minutes

02: 15      Loc Av Belfor         of the hour

145: P72      Totalize                Totalize Tip Bucket

01: 1       Rep

02: 18      Loc TipBuc mm

146: P33      Z=X+Y

01: 18      X Loc TipBuc mm

02: 65      Y Loc Total Tip

03: 65      Z Loc [:Total Tip]

147: P70      Sample                     Sample Soil Moisture

01: 1       Rep                       Average of minute 50

02: 17      Loc Av Soil M             of the hour

148: P78      Resolution

01: 1       High Resolution

149: P70      Sample          Sample Pressure for GTS

01: 1       Rep

02: 61      Loc Press 1hr

150: P78      Resolution

01: 0       Low Resolution

151: P70      Sample           Sample TempUC, Dewpoint for GTS

01: 2       Reps

02: 62      Loc Temp  1hr

152: P70      Sample           Sample Wind Dir for GTS

01: 1       Rep

02: 24      Loc WindD 1hr

153: P70      Sample         Sample Wind Speed for GTS

01: 1       Rep

02: 23      Loc WindS 1hr

154: P70      Sample          Sample Belfort difference from

01: 1       Rep             previous hour

02: 60      Loc Belf Diff

155: P70      Sample         Sample Total Tipping Bucket for season

01: 1       Rep

02: 65      Loc Total Tip

156: P70      Sample

01: 2       Reps

02: 73      Loc ThC 1 sec

157: P96      Serial Output

01: 30      SM192/SM716/CSM1

158: P18      Time                Store end of Program time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 45      Loc [:LastTime ]

159: P35      Z=X-Y                Program Execution Time

01: 45      X Loc LastTime

02: 43      Y Loc FirstTime

03: 44      Z Loc [:Prog Time]

160: P        End Table 1

*     2       Table 2 Programs

01: 30      Sec. Execution Interval

01:  P92      If time is

01: 50      minutes into a

02: 60      minute interval

03: 30      Then Do

02:  P89      If X<=>F

01: 43      X Loc FirstTime

02: 4       <

03: 200     F

04: 30      Then Do

03:  P86      Do

01: 10      Set high Flag 0 (output)

04:  P30      Z=F

01: 0       F

02: 29      Z Loc [:0V  Pw   ]

05:  P30      Z=F

01: 2000    F

02: 66      Z Loc [:2V  Pw   ]

06:  P17      Panel Temperature

01: 67      Loc [:PanelTemp]

07:  P20      Set Port

01: 1       Set high

02: 1       Port Number

08:  P87      Beginning of Loop

01: 0       Delay

02: 2       Loop Count

09:  P22      Excitation with Delay

01: 2       EX Chan

02: 2       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

10:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0.0000  mV Excitation

11:  P95      End

12:  P21      Analog Out

01: 2       CAO Chan

02: 66      mV Loc 2V  Pw

13:  P22      Excitation with Delay

01: 4       EX Chan

02: 100     Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

14:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 46      Loc [:ThC 1 sec]

07: 1       Mult

08: 0       Offset

15:  P22      Excitation with Delay

01: 4       EX Chan

02: 2000    Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

16:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 47      Loc [:ThC 21sec]

07: 1       Mult

08: 0       Offset

17:  P21      Analog Out

01: 2       CAO Chan

02: 29      mV Loc 0V  Pw

18:  P20      Set Port

01: 0       Set low

02: 1       Port Number

19:  P35      Z=X-Y                   End of Soil Moisture

01: 47      X Loc ThC 21sec

02: 46      Y Loc ThC 1 sec

03: 68      Z Loc [:Soil Diff]

20:  P37      Z=X*F

01: 68      X Loc Soil Diff

02: 4.89    F

03: 69      Z Loc [:Soil Mult]

21:  P30      Z=F

01: 10      F

02: 70      Z Loc [:Soil Ten ]

22:  P47      Z=X^Y

01: 70      X Loc Soil Ten

02: 69      Y Loc Soil Mult

03: 71      Z Loc [:Soil Sub ]

23:  P37      Z=X*F

01: 71      X Loc Soil Sub

02: .00026  F

03: 72      Z Loc [:Soil Res ]

24:  P37      Z=X*F

01: 72      X Loc Soil Res

02: .1      F

03: 21      Z Loc [:Soil MPa ]

25:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 17      Array ID or location

26:  P70      Sample

01: 1       Rep

02: 21      Loc Soil MPa

27:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 73      Array ID or location

28:  P70      Sample

01: 2       Reps

02: 46      Loc ThC 1 sec

29:  P95      End

30:  P95      End

31:  P        End Table 2

*     3       Table 3 Subroutines

01:  P        End Table 3

*     4       Mode 4 Output Options

01: 0       (Tape OFF) (Printer OFF)

02: 0       Printer 300 Baud

*     A       Mode 10 Memory Allocation

01: 76      Input Locations

02: 135     Intermediate Locations

*     C       Mode 12 Security (OSX-0)

01: 00      Security Option

02: 0000    Security Code

Key:

T=Table Number

E=Entry Number

L=Location Number

T:  E:  L:

1:  4:  1:  Loc [:Par KJ/m2]

1:  5:  2:  Loc [:Net KJ/m2]

1:  6:  3:  Loc [:AlU KJ/m2]

1:  7:  4:  Loc [:AlD KJ/m2]

1: 27:  5:  F(X) Loc [:Temp in C]

1: 24:  6:  Z Loc [:Temp LC C]

1: 18:  7:  Loc [:Soil 10cm]

1: 20:  8:  Loc [:Soil 20cm]

1: 22:  9:  Loc [:Soil 50cm]

1: 30: 10:  Loc [:Humid %RH]

1: 15: 11:  Loc [:Press KPa]

1:  8: 12:  Z Loc [:IRSensorC]

1:  9: 13:  Loc [:WindDdegT]

1: 10: 14:  Loc [:WindS m/s]

1: 11: 18:  Loc [:TipBuc mm]

1: 53: 19:  Z Loc [:Belfortmm]

1: 68: 19:  Z Loc [:Belfortmm]

1:103: 20:  Z Loc [:Snow D mm]

1:104: 20:  Z Loc [:Snow D mm]

1:105: 20:  Z Loc [:Snow D mm]

1:106: 20:  Z Loc [:Snow D mm]

1:107: 20:  Z Loc [:Snow D mm]

2: 24: 21:  Z Loc [:Soil MPa ]

1: 43: 22:  Z Loc [:Dewpoint ]       End of Dewpoint Calculations

1:  3: 25:  Loc [:Battery V]

1: 26: 27:  Loc [:UC Store ]

1: 28: 28:  Z Loc [:Temp in K]

2:  4: 29:  Z Loc [:0V  Pw   ]

1: 54: 31:  Z Loc [:Weightx10]

1: 69: 31:  Z Loc [:Weightx10]

1: 56: 32:  Z Loc [:Weightx2 ]

1: 65: 32:  Z Loc [:Weightx2 ]

1: 57: 33:  Z Loc [:Subtotal ]

1: 61: 33:  Z Loc [:Subtotal ]

1: 67: 33:  Z Loc [:Subtotal ]

1: 59: 34:  Loc [:HI or LO ]

1: 91: 39:  Z Loc [:Snow Calc]

1:100: 39:  Z Loc [:Snow Calc]

1: 96: 40:  Loc [:Snow Data]

1:102: 41:  Z Loc [:T2 291 K ]

1: 92: 42:  Z Loc [:Snow # Pu]

1: 98: 42:  Z Loc [:Snow # Pu]

1:  1: 43:  Loc [:FirstTime]

1:159: 44:  Z Loc [:Prog Time]

1:158: 45:  Loc [:LastTime ]

2: 14: 46:  Loc [:ThC 1 sec]

2: 16: 47:  Loc [:ThC 21sec]

1: 32: 48:  Z Loc [:a        ]

1: 33: 49:  Z Loc [:b        ]

1: 34: 50:  Z Loc [:a*T      ]

1: 35: 51:  Z Loc [:b+T      ]

1: 36: 52:  Z Loc [:aT/b+T   ]

1: 37: 53:  Z Loc [:aT/b+T-2 ]

1: 38: 54:  Z Loc [:ln(RH)   ]

1: 39: 55:  Z Loc [:ln/log   ]

1: 40: 56:  Z Loc [:log (RH) ]

1: 41: 57:  Z Loc [:log +aT/b]

1: 42: 58:  Z Loc [:a/logRH  ]

1:118: 59:  Z Loc [:Prev Belf]

1:117: 60:  Z Loc [:Belf Diff]

1:  2: 64:  Loc [:Minutes  ]

1:146: 65:  Z Loc [:Total Tip]

2:  5: 66:  Z Loc [:2V  Pw   ]

2:  6: 67:  Loc [:PanelTemp]

2: 19: 68:  Z Loc [:Soil Diff]

2: 20: 69:  Z Loc [:Soil Mult]

2: 21: 70:  Z Loc [:Soil Ten ]

2: 22: 71:  Z Loc [:Soil Sub ]

2: 23: 72:  Z Loc [:Soil Res ]

Page 21    Input Location Labels:

1:Par KJ/m2    20:Snow D mm    39:Snow Calc    58:a/logRH

2:Net KJ/m2    21:Soil MPa     40:Snow Data    59:Prev Belf

3:AlU KJ/m2    22:Dewpoint     41:T2 291 K     60:Belf Diff

4:AlD KJ/m2    23:WindS 1hr    42:Snow # Pu    61:Press 1hr

5:Temp in C    24:WindD 1hr    43:FirstTime    62:Temp  1hr

6:Temp LC C    25:Battery V    44:Prog Time    63:Dewpt 1hr

7:Soil 10cm    26:LC Store     45:LastTime     64:Minutes

8:Soil 20cm    27:UC Store     46:ThC 1 sec    65:Total Tip

9:Soil 50cm    28:Temp in K    47:ThC 21sec    66:2V  Pw

10:Humid %RH    29:0V  Pw       48:a            67:PanelTemp

11:Press KPa    30:5V  Pw       49:b            68:Soil Diff

12:IRSensorC    31:Weightx10    50:a*T          69:Soil Mult

13:WindDdegT    32:Weightx2     51:b+T          70:Soil Ten

14:WindS m/s    33:Subtotal     52:aT/b+T       71:Soil Sub

15:Av Belfor    34:HI or LO     53:aT/b+T-2     72:Soil Res

16:Av Snow D    35:             54:ln(RH)       73:ThC 1 sec

17:Av Soil M    36:             55:ln/log       74:ThC 21 Se

18:TipBuc mm    37:             56:log (RH)     75:_________

19:Belfortmm    38:             57:log +aT/b    76:_________

Program: Boreas  Prince Albert, SK  September 1/94

Flag Usage:

Input Channel Usage:

Excitation Channel Usage:

Continuous Analog Output Usage:

Control Port Usage:

Pulse Input Channel Usage:

Output Array Definitions:

*     1       Table 1 Programs

01: 5       Sec. Execution Interval

01:  P18      Time                 Beginning of Program Time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 43      Loc [:FirstTime]

02:  P18      Time                 Time used for counting minutes

01: 1       Minutes into current day (maximum 1440)

02: 60      Mod/by

03: 64      Loc [:Minutes  ]

03:  P10      Battery Voltage            Battery Voltage

01: 25      Loc [:Battery V]

04:  P2       Volt (DIFF)                PAR Sensor         KJ/m*m

01: 1       Rep

02: 2       15 mV slow Range

03: 1       IN Chan

04: 1       Loc [:Par KJ/m2]

05: .5      Mult

06: 0       Offset

05:  P2       Volt (DIFF)                Net Radiometer    KJ/m*m

01: 1       Rep

02: 4       500 mV slow Range

03: 2       IN Chan

04: 2       Loc [:Net KJ/m2]

05: .0665   Mult

06: 0       Offset

06:  P2       Volt (DIFF)                Albedometer Up    KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 3       IN Chan

04: 3       Loc [:AlU KJ/m2]

05: .56243  Mult

06: 0       Offset

07:  P2       Volt (DIFF)                Albedometer Down   KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 4       IN Chan

04: 4       Loc [:AlD KJ/m2]

05: .60459  Mult

06: 0       Offset

08:  P30      Z=F                 Beginning of IR Sensor  deg C

01: 0       F

02: 29      Z Loc [:OV  Pw   ]

09:  P30      Z=F

01: 5000    F

02: 30      Z Loc [:5V  Pw   ]

10:  P21      Analog Out Set CAO channel 1 to 5000 mV

01: 1       CAO Chan

02: 30      mV Loc 5V  Pw

11:  P4       Excite,Delay,Volt(SE) Measures Ed and Erel

01: 1       Rep

02: 5       5000 mV slow Range

03: 9       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 100     Delay (units .01sec)

06: 1200    mV Excitation

07: 31      Loc [:Ed Volts ]

08: .001    Mult

09: 0       Offset

12:  P4       Excite,Delay,Volt(SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 10      IN Chan

04: 2       Excite all reps w/EXchan 2

05: 100     Delay (units .01sec)

06: 5000--  mV Excitation

07: 32      Loc [:Erel Volt]

08: .001    Mult

09: 0       Offset

13:  P89      If X<=>F

01: 31      X Loc Ed Volts

02: 3       >=

03: .42315  F

04: 30      Then Do

14:  P55      Polynomial

01: 1       Rep

02: 31      X Loc Ed Volts

03: 33      F(X) Loc [:Td C     ]

04: 48.653  C0

05: -302.29 C1

06: 658.31  C2

07: -911.19 C3

08: 660.33  C4

09: -201.44 C5

15:  P94      Else

16:  P89      If X<=>F

01: 31      X Loc Ed Volts

02: 3       >=

03: .03125  F

04: 30      Then Do

17:  P37      Z=X*F

01: 31      X Loc Ed Volts

02: 10      F

03: 34      Z Loc [:Temporary]

18:  P55      Polynomial

01: 1       Rep

02: 34      X Loc Temporary

03: 33      F(X) Loc [:Td C     ]

04: 88.341  C0

05: -140.82 C1

06: 131.86  C2

07: -74.476 C3

08: 23.529  C4

09: -3.8390 C5

19:  P30      Z=F

01: 6       F

02: 35      Z Loc [:Six      ]

20:  P47      Z=X^Y

01: 34      X Loc Temporary

02: 35      Y Loc Six

03: 34      Z Loc [:Temporary]

21:  P37      Z=X*F

01: 34      X Loc Temporary

02: .25131  F

03: 34      Z Loc [:Temporary]

22:  P33      Z=X+Y

01: 34      X Loc Temporary

02: 33      Y Loc Td C

03: 33      Z Loc [:Td C     ]

23:  P94      Else

24:  P37      Z=X*F

01: 31      X Loc Ed Volts

02: 100     F

03: 34      Z Loc [:Temporary]

25:  P55      Polynomial

01: 1       Rep

02: 34      X Loc Temporary

03: 33      F(X) Loc [:Td C     ]

04: 164.35  C0

05: -134.14 C1

06: 80.230  C2

07: -23.831 C3

08: 2.6569  C4

09: 0       C5

26:  P95      End

27:  P95      End

28:  P37      Z=X*F

01: 32      X Loc Erel Volt

02: 1       F

03: 32      Z Loc [:Erel Volt]

29:  P37      Z=X*F

01: 33      X Loc Td C

02: -.00224 F

03: 36      Z Loc [:Erel Mult]

30:  P34      Z=X+F

01: 36      X Loc Erel Mult

02: 1.0589  F

03: 36      Z Loc [:Erel Mult]

31:  P36      Z=X*Y

01: 32      X Loc Erel Volt

02: 36      Y Loc Erel Mult

03: 37      Z Loc [:Ecrel V  ]

32:  P55      Polynomial

01: 1       Rep

02: 37      X Loc Ecrel V

03: 38      F(X) Loc [:Trel C   ]

04: .0836   C0

05: 122     C1

06: -65.5   C2

07: 126.4   C3

08: -223.2  C4

09: 140.3   C5

33:  P33      Z=X+Y                    End of IR Sensor

01: 33      X Loc Td C

02: 38      Y Loc Trel C

03: 12      Z Loc [:IRSensorC]

34:  P21      Analog Out

01: 1       CAO Chan

02: 29      mV Loc OV  Pw

35:  P4       Excite,Delay,Volt(SE)    Wind Direction  degrees true

01: 1       Rep

02: 5       5000 mV slow Range

03: 11      IN Chan

04: 3       Excite all reps w/EXchan 3

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 13      Loc [:WindDdegT]

08: .071    Mult

09: 0       Offset

36:  P3       Pulse                     Wind Speed    metres/sec

01: 1       Rep

02: 2       Pulse Input Chan

03: 21      Low level AC; Output Hz.

04: 14      Loc [:WindS m/s]

05: .0980   Mult

06: 0       Offset

37:  P3       Pulse                    Tipping Bucket     mm

01: 1       Rep

02: 1       Pulse Input Chan

03: 2       Switch closure

04: 18      Loc [:TipBuc mm]

05: .024    Mult

06: 0       Offset

38:  P89      If X<=>F     On the 50th minute skip the multiplexer

01: 64      X Loc Minutes and execute soil moisture in Table 2

02: 2       <>

03: 50      F

04: 30      Then Do

39:  P20      Set Port                  Start of Multiplexer

01: 1       Set high

02: 1       Port Number

40:  P20      Set Port

01: 1       Set high

02: 2       Port Number

41:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

42:  P20      Set Port

01: 0       Set low

02: 2       Port Number

43:  P8       Excite,Delay,Volt(DIFF)     Setra Pressure Sensor KPa

01: 1       Rep

02: 4       500 mV slow Range

03: 8       IN Chan

04: 1       Excite all reps w/EXchan 1

05: 1       Delay (units=.01sec)

06: 2500    mV Excitation

07: 11      Loc [:Press KPa]

08: .12     Mult

09: 80      Offset

44:  P20      Set Port

01: 1       Set high

02: 2       Port Number

45:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

46:  P20      Set Port

01: 0       Set low

02: 2       Port Number

47:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

48:  P20      Set Port

01: 1       Set high

02: 2       Port Number

49:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

50:  P20      Set Port

01: 0       Set low

02: 2       Port Number

51:  P11      Temp 107 Probe          Temperature at 10 cm    deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 7       Loc [:Soil 10cm]

05: 1       Mult

06: 0       Offset

52:  P20      Set Port

01: 1       Set high

02: 2       Port Number

53:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

54:  P20      Set Port

01: 0       Set low

02: 2       Port Number

55:  P11      Temp 107 Probe           Temperature at 20 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 8       Loc [:Soil 20cm]

05: 1       Mult

06: 0       Offset

56:  P20      Set Port

01: 1       Set high

02: 2       Port Number

57:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

58:  P20      Set Port

01: 0       Set low

02: 2       Port Number

59:  P11      Temp 107 Probe          Temperature at 50 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 9       Loc [:Soil 50cm]

05: 1       Mult

06: 0       Offset

60:  P20      Set Port

01: 1       Set high

02: 2       Port Number

61:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

62:  P20      Set Port

01: 0       Set low

02: 2       Port Number

63:  P4       Excite,Delay,Volt(SE)   107F Temperature LC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 26      Loc [:LC Store ]

08: .001    Mult

09: 0       Offset

64:  P55      Polynomial

01: 1       Rep

02: 26      X Loc LC Store

03: 6       F(X) Loc [:Temp LC C]

04: -74.159 C0              Coefficients for 35 foot cable -

05: 645.87  C1              lower canopy

06: -3844.6 C2

07: 16081   C3

08: -34152  C4

09: 29933   C5

65:  P34      Z=X+F

01: 6       X Loc Temp LC C

02: 273.15  F

03: 28      Z Loc [:Temp LC K]

66:  P20      Set Port

01: 1       Set high

02: 2       Port Number

67:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

68:  P20      Set Port

01: 0       Set low

02: 2       Port Number

69:  P4       Excite,Delay,Volt(SE)  HMP35CF Temperature UC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 27      Loc [:UC Store ]

08: .001    Mult

09: 0       Offset

70:  P55      Polynomial

01: 1       Rep

02: 27      X Loc UC Store

03: 5       F(X) Loc [:Temp UC C]

04: -74.221 C0              Coefficients for 150 foot cable -

05: 648.34  C1               upper canopy

06: -3875.8 C2

07: 16274   C3

08: -34691  C4

09: 30508   C5

71:  P20      Set Port

01: 1       Set high

02: 2       Port Number

72:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

73:  P20      Set Port

01: 0       Set low

02: 2       Port Number

74:  P4       Excite,Delay,Volt(SE)   HMP35CF Relative Humidity %RH

01: 1       Rep

02: 5       5000 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 15      Delay (units .01sec)

06: 5000    mV Excitation

07: 10      Loc [:Humid %RH]

08: .1      Mult

09: 0       Offset

75:  P20      Set Port

01: 0       Set low

02: 1       Port Number

76:  P30      Z=F               Beginning of Dewpoint Calculations

01: 9.5     F

02: 48      Z Loc [:a        ]

77:  P30      Z=F

01: 265.5   F

02: 49      Z Loc [:b        ]

78:  P37      Z=X*F

01: 5       X Loc Temp UC C

02: 9.5     F

03: 50      Z Loc [:a*T      ]

79:  P34      Z=X+F

01: 5       X Loc Temp UC C

02: 265.5   F

03: 51      Z Loc [:b+T      ]

80:  P38      Z=X/Y

01: 50      X Loc a*T

02: 51      Y Loc b+T

03: 52      Z Loc [:aT/b+T   ]

81:  P34      Z=X+F

01: 52      X Loc aT/b+T

02: -2      F

03: 53      Z Loc [:aT/b+T-2 ]

82:  P40      Z=LN(X)

01: 10      X Loc Humid %RH

02: 54      Z Loc [:ln(RH)   ]

83:  P30      Z=F

01: 2.303   F

02: 55      Z Loc [:ln/log   ]

84:  P38      Z=X/Y

01: 54      X Loc ln(RH)

02: 55      Y Loc ln/log

03: 56      Z Loc [:log (RH) ]

85:  P33      Z=X+Y

01: 56      X Loc log (RH)

02: 53      Y Loc aT/b+T-2

03: 57      Z Loc [:log +aT/b]

86:  P38      Z=X/Y

01: 48      X Loc a

02: 57      Y Loc log +aT/b

03: 58      Z Loc [:a/logRH  ]

87:  P38      Z=X/Y

01: 49      X Loc b

02: 58      Y Loc a/logRH

03: 22      Z Loc [:Dewpoint ]       End of Dewpoint Calculations

88:  P95      End

89:  P92      If time is

01: 0       minutes into a

02: 1       minute interval

03: 30      Then Do

90:  P89      If X<=>F

01: 64      X Loc Minutes

02: 3       >=

03: 55      F

04: 30      Then Do

91:  P4       Excite,Delay,Volt(SE)     Belfort Weighing Gauge

01: 1       Rep

02: 5       5000 mV slow Range

03: 12      IN Chan

04: 4       Excite all reps w/EXchan 4

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 19      Loc [:Belfortmm]

08: .07386  Mult

09: 0       Offset

92:  P20      Set Port                   Begin Snow Depth Sensor

01: 1       Set high

02: 6       Port Number

93:  P20      Set Port

01: 0       Set low

02: 4       Port Number

94:  P20      Set Port

01: 1       Set high

02: 5       Port Number

95:  P20      Set Port

01: 0       Set low

02: 5       Port Number

96:  P20      Set Port

01: 1       Set high

02: 4       Port Number

97:  P20      Set Port

01: 1       Set high

02: 5       Port Number

98:  P20      Set Port

01: 0       Set low

02: 5       Port Number

99:  P20      Set Port

01: 0       Set low

02: 4       Port Number

100: P87      Beginning of Loop

01: 0       Delay

02: 6       Loop Count

101: P20      Set Port

01: 1       Set high

02: 5       Port Number

102: P20      Set Port

01: 0       Set low

02: 5       Port Number

103: P95      End

104: P20      Set Port

01: 1       Set high

02: 5       Port Number

105: P22      Excitation with Delay

01: 1       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

106: P20      Set Port

01: 0       Set low

02: 6       Port Number

107: P20      Set Port

01: 1       Set high

02: 6       Port Number

108: P22      Excitation with Delay

01: 1       EX Chan

02: 8       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

109: P20      Set Port

01: 0       Set low

02: 5       Port Number

110: P30      Z=F

01: 1       F

02: 39      Z Loc [:Snow Calc]

111: P30      Z=F

01: 0       F

02: 42      Z Loc [:Snow # Pu]

112: P87      Beginning of Loop

01: 0       Delay

02: 16      Loop Count

113: P20      Set Port

01: 1       Set high

02: 5       Port Number

114: P20      Set Port

01: 0       Set low

02: 5       Port Number

115: P1       Volt (SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 13      IN Chan

04: 40      Loc [:Snow Data]

05: 1       Mult

06: 0       Offset

116: P89      If X<=>F

01: 40      X Loc Snow Data

02: 3       >=

03: 3000    F

04: 30      Then Do

117: P33      Z=X+Y

01: 39      X Loc Snow Calc

02: 42      Y Loc Snow # Pu

03: 42      Z Loc [:Snow # Pu]

118: P95      End

119: P37      Z=X*F

01: 39      X Loc Snow Calc

02: 2       F

03: 39      Z Loc [:Snow Calc]

120: P95      End

121: P30      Z=F

01: 291     F

02: 41      Z Loc [:T2 291 K ]

122: P38      Z=X/Y

01: 28      X Loc Temp LC K

02: 41      Y Loc T2 291 K

03: 20      Z Loc [:Snow D mm]

123: P39      Z=SQRT(X)

01: 20      X Loc Snow D mm

02: 20      Z Loc [:Snow D mm]

124: P36      Z=X*Y

01: 42      X Loc Snow # Pu

02: 20      Y Loc Snow D mm

03: 20      Z Loc [:Snow D mm]

125: P37      Z=X*F

01: 20      X Loc Snow D mm

02: .52176  F

03: 20      Z Loc [:Snow D mm]

126: P34      Z=X+F

01: 20      X Loc Snow D mm

02: -39     F

03: 20      Z Loc [:Snow D mm]

127: P20      Set Port

01: 0       Set low

02: 4       Port Number

128: P20      Set Port

01: 0       Set low

02: 5       Port Number

129: P20      Set Port                 End of Snow Depth

01: 0       Set low

02: 6       Port Number

130: P89      If X<=>F           Five Minute Average at the top of

01: 64      X Loc Minutes    the hour for Belfort and Snow Depth

02: 1       =

03: 59      F

04: 10      Set high Flag 0 (output)

131: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 15      Array ID or location

132: P71      Average

01: 2       Reps

02: 19      Loc Belfortmm

133: P95      End

134: P95      End

135: P92      If time is

01: 0       minutes into a

02: 60      minute interval

03: 30      Then Do

136: P35      Z=X-Y

01: 15      X Loc Av Belfor

02: 59      Y Loc Prev Belf

03: 60      Z Loc [:Belf Diff]

137: P31      Z=X

01: 15      X Loc Av Belfor

02: 59      Z Loc [:Prev Belf]

138: P95      End

139: P89      If X<=>F           Two minute average of Wind Speed

01: 64      X Loc Minutes      and Direction at top of the hour

02: 3       >=

03: 58      F

04: 10      Set high Flag 0 (output)

140: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 23      Array ID or location

141: P69      Wind Vector

01: 1       Rep

02: 0       Samples per sub-interval

03: 1       Polar Sensor/(S, D1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

142: P92      If time is

01: 59      minutes into a

02: 60      minute interval

03: 10      Set high Flag 0 (output)

143: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 61      Array ID or location

144: P71      Average             One minute average of Pressure

01: 1       Rep                 at top of the hour

02: 11      Loc Press KPa

145: P71      Average             One minute average of Temperature

01: 1       Rep                 at top of the hour

02: 5       Loc Temp UC C

146: P71      Average             One minute average of Dewpoint

01: 1       Rep                 at top of the hour

02: 22      Loc Dewpoint

147: P92      If time is            Begin writing to the array -

01: 0       minutes into a        15 minute interval

02: 15      minute interval

03: 10      Set high Flag 0 (output)

148: P80      Set Active Storage Area

01: 1       Final Storage Area

02: 3       Array ID or location

149: P70      Sample                     Sample Battery

01: 1       Rep

02: 25      Loc Battery V

150: P77      Real Time                  Year, Day, Time

01: 1110    Year,Day,Hour-Minute

151: P78      Resolution

01: 1       High Resolution

152: P72      Totalize           Totalize Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Loc Par KJ/m2

153: P78      Resolution

01: 0       Low Resolution

154: P82      Standard Deviation Std Dev Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Sample Loc Par KJ/m2

155: P71      Average           Average TempUC, TempLC, Temp10

01: 6       Reps              Temp20, Temp50, RelHum

02: 5       Loc Temp UC C

156: P78      Resolution

01: 1       High Resolution

157: P71      Average            Average Pressure

01: 1       Rep

02: 11      Loc Press KPa

158: P78      Resolution

01: 0       Low Resolution

159: P71      Average            Average IRSensor

01: 1       Rep

02: 12      Loc IRSensorC

160: P82      Standard Deviation Std Dev Temp UC, TempLC, Temp10

01: 8       Reps               Temp20, Temp50, RelHum, Pressure

02: 5       Sample Loc Temp UC C IRSensor

161: P69      Wind Vector      Average Wind Speed, Wind Direction

01: 1       Rep                   and Std Dev Wind Direction

02: 0       Samples per sub-interval

03: 0       Polar Sensor/(S, D1, SD1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

162: P82      Standard Deviation      Std Dev Wind Speed

01: 1       Rep

02: 14      Sample Loc WindS m/s

163: P70      Sample                Sample Belfort, Snow Depth

01: 2       Reps                  Average of last 5 minutes

02: 15      Loc Av Belfor         of the hour

164: P72      Totalize                Totalize Tip Bucket

01: 1       Rep

02: 18      Loc TipBuc mm

165: P33      Z=X+Y

01: 18      X Loc TipBuc mm

02: 65      Y Loc Total Tip

03: 65      Z Loc [:Total Tip]

166: P70      Sample                    Sample Soil Moisture

01: 1       Rep                       Average of minute 50

02: 17      Loc Av Soil M             of the hour

167: P78      Resolution

01: 1       High Resolution

168: P70      Sample        Sample Pressure for GTS

01: 1       Rep

02: 61      Loc Press 1hr

169: P78      Resolution

01: 0       Low Resolution

170: P70      Sample   Sample TempUC, Dewpoint for GTS

01: 2       Reps

02: 62      Loc Temp  1hr

171: P70      Sample           Sample Wind Dir for GTS

01: 1       Rep

02: 24      Loc WindD 1hr

172: P70      Sample           Sample Wind Speed for GTS

01: 1       Rep

02: 23      Loc WindS 1hr

173: P70      Sample           Sample Belfort difference from

01: 1       Rep              previous hour

02: 60      Loc Belf Diff

174: P70      Sample      Sample Total Tipping Bucket for season

01: 1       Rep

02: 65      Loc Total Tip

175: P70      Sample

01: 2       Reps

02: 73      Loc ThC 1sec

176: P96      Serial Output

01: 30      SM192/SM716/CSM1

177: P18      Time                Store end of Program time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 45      Loc [:LastTime ]

178: P35      Z=X-Y                Program Execution Time

01: 45      X Loc LastTime

02: 43      Y Loc FirstTime

03: 44      Z Loc [:Prog Time]

179: P        End Table 1

*     2       Table 2 Programs

01: 60      Sec. Execution Interval

01:  P92      If time is

01: 50      minutes into a

02: 60      minute interval

03: 30      Then Do

02:  P89      If X<=>F

01: 43      X Loc FirstTime

02: 4       <

03: 200     F

04: 30      Then Do

03:  P86      Do

01: 10      Set high Flag 0 (output)

04:  P30      Z=F

01: 0       F

02: 29      Z Loc [:OV  Pw   ]

05:  P30      Z=F

01: 2000    F

02: 66      Z Loc [:2V  Pw   ]

06:  P17      Panel Temperature

01: 67      Loc [:PanelTemp]

07:  P20      Set Port

01: 1       Set high

02: 1       Port Number

08:  P87      Beginning of Loop

01: 0       Delay

02: 2       Loop Count

09:  P20      Set Port

01: 1       Set high

02: 2       Port Number

10:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

11:  P20      Set Port

01: 0       Set low

02: 2       Port Number

12:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0.0000  mV Excitation

13:  P95      End

14:  P21      Analog Out

01: 2       CAO Chan

02: 66      mV Loc 2V  Pw

15:  P22      Excitation with Delay

01: 4       EX Chan

02: 100     Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

16:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 46      Loc [:ThC 1 sec]

07: 1       Mult

08: 0       Offset

17:  P22      Excitation with Delay

01: 4       EX Chan

02: 2000    Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

18:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 47      Loc [:ThC 21sec]

07: 1       Mult

08: 0       Offset

19:  P21      Analog Out

01: 2       CAO Chan

02: 29      mV Loc OV  Pw

20:  P20      Set Port

01: 0       Set low

02: 1       Port Number

21:  P35      Z=X-Y                   End of Soil Moisture

01: 47      X Loc ThC 21sec

02: 46      Y Loc ThC 1 sec

03: 68      Z Loc [:Soil Diff]

22:  P37      Z=X*F

01: 68      X Loc Soil Diff

02: 4.89    F

03: 69      Z Loc [:Soil Mult]

23:  P30      Z=F

01: 10      F

02: 70      Z Loc [:Soil Ten ]

24:  P47      Z=X^Y

01: 70      X Loc Soil Ten

02: 69      Y Loc Soil Mult

03: 71      Z Loc [:Soil Sub ]

25:  P37      Z=X*F

01: 71      X Loc Soil Sub

02: .00026  F

03: 72      Z Loc [:Soil Res ]

26:  P37      Z=X*F

01: 72      X Loc Soil Res

02: .1      F

03: 21      Z Loc [:Soil MPa ]

27:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 17      Array ID or location

28:  P70      Sample

01: 1       Rep

02: 21      Loc Soil MPa

29:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 73      Array ID or location

30:  P70      Sample

01: 2       Reps

02: 46      Loc ThC 1 sec

31:  P95      End

32:  P95      End

33:  P        End Table 2

*     3       Table 3 Subroutines

01:  P        End Table 3

*     4       Mode 4 Output Options

01: 0       (Tape OFF) (Printer OFF)

02: 0       Printer 300 Baud

*     A       Mode 10 Memory Allocation

01: 76      Input Locations

02: 130     Intermediate Locations

*     C       Mode 12 Security (OSX-0)

01: 00      Security Option

02: 0000    Security Code

Key:

T=Table Number

E=Entry Number

L=Location Number

T:  E:  L:

1:  4:  1:  Loc [:Par KJ/m2]

1:  5:  2:  Loc [:Net KJ/m2]

1:  6:  3:  Loc [:AlU KJ/m2]

1:  7:  4:  Loc [:AlD KJ/m2]

1: 70:  5:  F(X) Loc [:Temp UC C]

1: 64:  6:  F(X) Loc [:Temp LC C]

1: 51:  7:  Loc [:Soil 10cm]

1: 55:  8:  Loc [:Soil 20cm]

1: 59:  9:  Loc [:Soil 50cm]

1: 74: 10:  Loc [:Humid %RH]

1: 43: 11:  Loc [:Press KPa]

1: 33: 12:  Z Loc [:IRSensorC]

1: 35: 13:  Loc [:WindDdegT]

1: 36: 14:  Loc [:WindS m/s]

1: 37: 18:  Loc [:TipBuc mm]

1: 91: 19:  Loc [:Belfortmm]

1:122: 20:  Z Loc [:Snow D mm]

1:123: 20:  Z Loc [:Snow D mm]

1:124: 20:  Z Loc [:Snow D mm]

1:125: 20:  Z Loc [:Snow D mm]

1:126: 20:  Z Loc [:Snow D mm]

2: 26: 21:  Z Loc [:Soil MPa ]

1: 87: 22:  Z Loc [:Dewpoint ]       End of Dewpoint Calculations

1:  3: 25:  Loc [:Battery V]

1: 63: 26:  Loc [:LC Store ]

1: 69: 27:  Loc [:UC Store ]

1: 65: 28:  Z Loc [:Temp LC K]

1:  8: 29:  Z Loc [:OV  Pw   ]

2:  4: 29:  Z Loc [:OV  Pw   ]

1:  9: 30:  Z Loc [:5V  Pw   ]

1: 11: 31:  Loc [:Ed Volts ]

1: 12: 32:  Loc [:Erel Volt]

1: 28: 32:  Z Loc [:Erel Volt]

1: 14: 33:  F(X) Loc [:Td C     ]

1: 18: 33:  F(X) Loc [:Td C     ]

1: 22: 33:  Z Loc [:Td C     ]

1: 25: 33:  F(X) Loc [:Td C     ]

1: 17: 34:  Z Loc [:Temporary]

1: 20: 34:  Z Loc [:Temporary]

1: 21: 34:  Z Loc [:Temporary]

1: 24: 34:  Z Loc [:Temporary]

1: 19: 35:  Z Loc [:Six      ]

1: 29: 36:  Z Loc [:Erel Mult]

1: 30: 36:  Z Loc [:Erel Mult]

1: 31: 37:  Z Loc [:Ecrel V  ]

1: 32: 38:  F(X) Loc [:Trel C   ]

1:110: 39:  Z Loc [:Snow Calc]

1:119: 39:  Z Loc [:Snow Calc]

1:115: 40:  Loc [:Snow Data]

1:121: 41:  Z Loc [:T2 291 K ]

1:111: 42:  Z Loc [:Snow # Pu]

1:117: 42:  Z Loc [:Snow # Pu]

1:  1: 43:  Loc [:FirstTime]

1:178: 44:  Z Loc [:Prog Time]

1:177: 45:  Loc [:LastTime ]

2: 16: 46:  Loc [:ThC 1 sec]

2: 18: 47:  Loc [:ThC 21sec]

1: 76: 48:  Z Loc [:a        ]

1: 77: 49:  Z Loc [:b        ]

1: 78: 50:  Z Loc [:a*T      ]

1: 79: 51:  Z Loc [:b+T      ]

1: 80: 52:  Z Loc [:aT/b+T   ]

1: 81: 53:  Z Loc [:aT/b+T-2 ]

1: 82: 54:  Z Loc [:ln(RH)   ]

1: 83: 55:  Z Loc [:ln/log   ]

1: 84: 56:  Z Loc [:log (RH) ]

1: 85: 57:  Z Loc [:log +aT/b]

1: 86: 58:  Z Loc [:a/logRH  ]

1:137: 59:  Z Loc [:Prev Belf]

1:136: 60:  Z Loc [:Belf Diff]

1:  2: 64:  Loc [:Minutes  ]

1:165: 65:  Z Loc [:Total Tip]

2:  5: 66:  Z Loc [:2V  Pw   ]

2:  6: 67:  Loc [:PanelTemp]

2: 21: 68:  Z Loc [:Soil Diff]

2: 22: 69:  Z Loc [:Soil Mult]

2: 23: 70:  Z Loc [:Soil Ten ]

2: 24: 71:  Z Loc [:Soil Sub ]

2: 25: 72:  Z Loc [:Soil Res ]

Program: Boreas Suite B Prince Albert Apr 08/94

Flag Usage:

Input Channel Usage:

Excitation Channel Usage:

Continous Analog Output Usage:

Control Port Usage:

Pulse Input Channel Usage:

Output Array Definitions:

*     1       Table 1 Programs

01: 5       Sec. Execution Interval

01:  P22      Excitation with Delay                Signal Light

01: 3       EX Chan

02: 25      Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 2500    mV Excitation

02:  P2       Volt (DIFF)                         Pyranometer

01: 1       Rep

02: 23      25 mV 60 Hz rejection Range

03: 1       IN Chan

04: 1       Loc [:PSP kJ/m2]

05: .55991  Mult

06: 0.0000  Offset

03:  P2       Volt (DIFF)                        Pyrgeometer

01: 1       Rep

02: 23      25 mV 60 Hz rejection Range

03: 2       IN Chan

04: 2       Loc [:PIR kJ/m2]

05: 1.5152  Mult

06: 0.0000  Offset

04:  P2       Volt (DIFF)

01: 1       Rep

02: 21      2.5 mV 60 Hz rejection Range

03: 3       IN Chan

04: 3       Loc [:ThPile mV]

05: 1       Mult

06: 0.0000  Offset

05:  P89      If X<=>F

01: 1       X Loc PSP kJ/m2

02: 4       <

03: 0.0000  F

04: 30      Then Do

06:  P30      Z=F

01: 0.0000  F

02: 00      Exponent of 10

03: 1       Z Loc [:PSP kJ/m2]

07:  P95      End

08:  P89      If X<=>F

01: 2       X Loc PIR kJ/m2

02: 4       <

03: 0.0000  F

04: 30      Then Do

09:  P30      Z=F

01: 0.0000  F

02: 00      Exponent of 10

03: 2       Z Loc [:PIR kJ/m2]

10:  P95      End

YSI 44031 Thermistor Measurement

11:  P4       Excite,Delay,Volt(SE)

01: 2       Reps

02: 24      250 mV 60 Hz rejection Range

03: 9       IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0000    Delay (units .01sec)

06: 1700    mV Excitation

07: 4       Loc [:Tcase C  ]

08: .01     Mult

09: 0       Offset

YSI 44031 Linearization

12:  P87      Beginning of Loop

01: 0000    Delay

02: 2       Loop Count

13:  P89      If X<=>F

01: 4--     X Loc Tcase C

02: 4       <

03: .5      F

04: 30      Then Do

14:  P55      Polynomial

01: 1       Rep

02: 4--     X Loc Tcase C

03: 4--     F(X) Loc [:Tcase C  ]

04: -64.140 C0

05: 472.02  C1

06: -2304.8 C2

07: 7037.4  C3

08: -11140  C4

09: 7001.6  C5

15:  P94      Else

16:  P55      Polynomial

01: 1       Rep

02: 4--     X Loc Tcase C

03: 4--     F(X) Loc [:Tcase C  ]

04: -32.981 C0

05: 85.859  C1

06: -62.706 C2

07: 30.782  C3

08: -8.1108 C4

09: .87158  C5

17:  P95      End

18:  P95      End

19:  P92      If time is

01: 0       minutes into a

02: 15      minute interval

03: 10      Set high Flag 0 (output)

20:  P80      Set Active Storage Area

01: 1       Final Storage Area 1

02: 3       Array ID or location

21:  P77      Real Time

01: 1220    Year,Day,Hour-Minute

22:  P78      Resolution

01: 1       High Resolution

23:  P72      Totalize                Totalize PSP, PIR, ThPile

01: 3       Reps

02: 1       Loc PSP kJ/m2

24:  P78      Resolution

01: 0       Low Resolution

25:  P71      Average                Average Tcase, Themisph

01: 2       Reps

02: 4       Loc Tcase C

26:  P82      Standard Deviation     Std Dev PSP, PIR, ThPile

01: 5       Reps                           Tcase, Themisph

02: 1       Sample Loc PSP kJ/m2

27:  P96      Serial Output

01: 71      SM192/SM716/CSM1

28:  P        End Table 1

*     2       Table 2 Programs

01: 0.0000  Sec. Execution Interval

01:  P        End Table 2

*     3       Table 3 Subroutines

01:  P        End Table 3

*     A       Mode 10 Memory Allocation

01: 28      Input Locations

02: 64      Intermediate Locations

03: 0.0000  Final Storage Area 2

*     C       Mode 12 Security

01: 0000    LOCK 1

02: 0000    LOCK 2

03: 0000    LOCK 3

Key:

T=Table Number

E=Entry Number

L=Location Number

T:  E:  L:

1:  2:  1:  Loc [:PSP kJ/m2]

1:  6:  1:  Z Loc [:PSP kJ/m2]

1:  3:  2:  Loc [:PIR kJ/m2]

1:  9:  2:  Z Loc [:PIR kJ/m2]

1:  4:  3:  Loc [:ThPile mV]

1: 11:  4:  Loc [:Tcase C  ]

1: 14:  4:  F(X) Loc [:Tcase C  ]

1: 16:  4:  F(X) Loc [:Tcase C  ]

Program: Boreas  Nipawin, SK   August 30/94

Flag Usage:

Input Channel Usage:

Excitation Channel Usage:

Continuous Analog Output Usage:

Control Port Usage:

Pulse Input Channel Usage:

Output Array Definitions:

*     1       Table 1 Programs

01: 5       Sec. Execution Interval

01:  P18      Time                 Beginning of Program Time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 43      Loc [:FirstTime]

02:  P18      Time                 Time used for counting minutes

01: 1       Minutes into current day (maximum 1440)

02: 60      Mod/by

03: 64      Loc [:Minutes  ]

03:  P10      Battery Voltage            Battery Voltage

01: 25      Loc [:Battery V]

04:  P2       Volt (DIFF)                PAR Sensor         KJ/m*m

01: 1       Rep

02: 2       15 mV slow Range

03: 1       IN Chan

04: 1       Loc [:Par KJ/m2]

05: .5      Mult

06: 0       Offset

05:  P2       Volt (DIFF)                Net Radiometer    KJ/m*m

01: 1       Rep

02: 4       500 mV slow Range

03: 2       IN Chan

04: 2       Loc [:Net KJ/m2]

05: .06900  Mult

06: 0       Offset

06:  P2       Volt (DIFF)                Albedometer Up    KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 3       IN Chan

04: 3       Loc [:AlU KJ/m2]

05: .58617  Mult

06: 0       Offset

07:  P2       Volt (DIFF)                Albedometer Down   KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 4       IN Chan

04: 4       Loc [:AlD KJ/m2]

05: .57013  Mult

06: 0       Offset

08:  P30      Z=F                 Beginning of IR Sensor  deg C

01: 0       F

02: 29      Z Loc [:OV  Pw   ]

09:  P30      Z=F

01: 5000    F

02: 30      Z Loc [:5V  Pw   ]

10:  P21      Analog Out Set CAO channel 1 to 5000 mV

01: 1       CAO Chan

02: 30      mV Loc 5V  Pw

11:  P4       Excite,Delay,Volt(SE) Measures Ed and Erel

01: 1       Rep

02: 5       5000 mV slow Range

03: 9       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 100     Delay (units .01sec)

06: 1200    mV Excitation

07: 31      Loc [:Ed Volts ]

08: .001    Mult

09: 0       Offset

12:  P4       Excite,Delay,Volt(SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 10      IN Chan

04: 2       Excite all reps w/EXchan 2

05: 100     Delay (units .01sec)

06: 5000--  mV Excitation

07: 32      Loc [:Erel Volt]

08: .001    Mult

09: 0       Offset

13:  P89      If X<=>F

01: 31      X Loc Ed Volts

02: 3       >=

03: .42315  F

04: 30      Then Do

14:  P55      Polynomial

01: 1       Rep

02: 31      X Loc Ed Volts

03: 33      F(X) Loc [:Td C     ]

04: 48.653  C0

05: -302.29 C1

06: 658.31  C2

07: -911.19 C3

08: 660.33  C4

09: -201.44 C5

15:  P94      Else

16:  P89      If X<=>F

01: 31      X Loc Ed Volts

02: 3       >=

03: .03125  F

04: 30      Then Do

17:  P37      Z=X*F

01: 31      X Loc Ed Volts

02: 10      F

03: 34      Z Loc [:Temporary]

18:  P55      Polynomial

01: 1       Rep

02: 34      X Loc Temporary

03: 33      F(X) Loc [:Td C     ]

04: 88.341  C0

05: -140.82 C1

06: 131.86  C2

07: -74.476 C3

08: 23.529  C4

09: -3.8390 C5

19:  P30      Z=F

01: 6       F

02: 35      Z Loc [:Six      ]

20:  P47      Z=X^Y

01: 34      X Loc Temporary

02: 35      Y Loc Six

03: 34      Z Loc [:Temporary]

21:  P37      Z=X*F

01: 34      X Loc Temporary

02: .25131  F

03: 34      Z Loc [:Temporary]

22:  P33      Z=X+Y

01: 34      X Loc Temporary

02: 33      Y Loc Td C

03: 33      Z Loc [:Td C     ]

23:  P94      Else

24:  P37      Z=X*F

01: 31      X Loc Ed Volts

02: 100     F

03: 34      Z Loc [:Temporary]

25:  P55      Polynomial

01: 1       Rep

02: 34      X Loc Temporary

03: 33      F(X) Loc [:Td C     ]

04: 164.35  C0

05: -134.14 C1

06: 80.230  C2

07: -23.831 C3

08: 2.6569  C4

09: 0       C5

26:  P95      End

27:  P95      End

28:  P37      Z=X*F

01: 32      X Loc Erel Volt

02: 1       F

03: 32      Z Loc [:Erel Volt]

29:  P37      Z=X*F

01: 33      X Loc Td C

02: -.00224 F

03: 36      Z Loc [:Erel Mult]

30:  P34      Z=X+F

01: 36      X Loc Erel Mult

02: 1.0589  F

03: 36      Z Loc [:Erel Mult]

31:  P36      Z=X*Y

01: 32      X Loc Erel Volt

02: 36      Y Loc Erel Mult

03: 37      Z Loc [:Ecrel V  ]

32:  P55      Polynomial

01: 1       Rep

02: 37      X Loc Ecrel V

03: 38      F(X) Loc [:Trel C   ]

04: .0836   C0

05: 122     C1

06: -65.5   C2

07: 126.4   C3

08: -223.2  C4

09: 140.3   C5

33:  P33      Z=X+Y                    End of IR Sensor

01: 33      X Loc Td C

02: 38      Y Loc Trel C

03: 12      Z Loc [:IRSensorC]

34:  P21      Analog Out

01: 1       CAO Chan

02: 29      mV Loc OV  Pw

35:  P4       Excite,Delay,Volt(SE)    Wind Direction  degrees true

01: 1       Rep

02: 5       5000 mV slow Range

03: 11      IN Chan

04: 3       Excite all reps w/EXchan 3

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 13      Loc [:WindDdegT]

08: .071    Mult

09: 0       Offset

36:  P3       Pulse                     Wind Speed    metres/sec

01: 1       Rep

02: 2       Pulse Input Chan

03: 21      Low level AC; Output Hz.

04: 14      Loc [:WindS m/s]

05: .0980   Mult

06: 0       Offset

37:  P3       Pulse                    Tipping Bucket     mm

01: 1       Rep

02: 1       Pulse Input Chan

03: 2       Switch closure

04: 18      Loc [:TipBuc mm]

05: .025    Mult

06: 0       Offset

38:  P89      If X<=>F      On the 50th minute skip the multiplexer

01: 64      X Loc Minutes and execute soil moisture in Table 2

02: 2       <>

03: 50      F

04: 30      Then Do

39:  P20      Set Port                  Start of Multiplexer

01: 1       Set high

02: 1       Port Number

40:  P20      Set Port

01: 1       Set high

02: 2       Port Number

41:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

42:  P20      Set Port

01: 0       Set low

02: 2       Port Number

43:  P8       Excite,Delay,Volt(DIFF)     Setra Pressure Sensor KPa

01: 1       Rep

02: 4       500 mV slow Range

03: 8       IN Chan

04: 1       Excite all reps w/EXchan 1

05: 1       Delay (units=.01sec)

06: 2500    mV Excitation

07: 11      Loc [:Press KPa]

08: .12     Mult

09: 80      Offset

44:  P20      Set Port

01: 1       Set high

02: 2       Port Number

45:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

46:  P20      Set Port

01: 0       Set low

02: 2       Port Number

47:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

48:  P20      Set Port

01: 1       Set high

02: 2       Port Number

49:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

50:  P20      Set Port

01: 0       Set low

02: 2       Port Number

51:  P11      Temp 107 Probe          Temperature at 10 cm    deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 7       Loc [:Soil 10cm]

05: 1       Mult

06: 0       Offset

52:  P20      Set Port

01: 1       Set high

02: 2       Port Number

53:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

54:  P20      Set Port

01: 0       Set low

02: 2       Port Number

55:  P11      Temp 107 Probe           Temperature at 20 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 8       Loc [:Soil 20cm]

05: 1       Mult

06: 0       Offset

56:  P20      Set Port

01: 1       Set high

02: 2       Port Number

57:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

58:  P20      Set Port

01: 0       Set low

02: 2       Port Number

59:  P11      Temp 107 Probe          Temperature at 50 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 9       Loc [:Soil 50cm]

05: 1       Mult

06: 0       Offset

60:  P20      Set Port

01: 1       Set high

02: 2       Port Number

61:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

62:  P20      Set Port

01: 0       Set low

02: 2       Port Number

63:  P4       Excite,Delay,Volt(SE)   107F Temperature LC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 26      Loc [:LC Store ]

08: .001    Mult

09: 0       Offset

64:  P55      Polynomial

01: 1       Rep

02: 26      X Loc LC Store

03: 6       F(X) Loc [:Temp LC C]

04: -74.159 C0              Coefficients for 35 foot cable -

05: 645.87  C1              lower canopy

06: -3844.6 C2

07: 16081   C3

08: -34152  C4

09: 29933   C5

65:  P34      Z=X+F

01: 6       X Loc Temp LC C

02: 273.15  F

03: 28      Z Loc [:Temp LC K]

66:  P20      Set Port

01: 1       Set high

02: 2       Port Number

67:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

68:  P20      Set Port

01: 0       Set low

02: 2       Port Number

69:  P4       Excite,Delay,Volt(SE)  HMP35CF Temperature UC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 27      Loc [:UC Store ]

08: .001    Mult

09: 0       Offset

70:  P55      Polynomial

01: 1       Rep

02: 27      X Loc UC Store

03: 5       F(X) Loc [:Temp UC C]

04: -74.181 C0              Coefficients for 75 foot cable -

05: 646.76  C1               upper canopy

06: -3855.7 C2

07: 16149   C3

08: -34341  C4

09: 30134   C5

71:  P20      Set Port

01: 1       Set high

02: 2       Port Number

72:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

73:  P20      Set Port

01: 0       Set low

02: 2       Port Number

74:  P4       Excite,Delay,Volt(SE)   HMP35CF Relative Humidity %RH

01: 1       Rep

02: 5       5000 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 15      Delay (units .01sec)

06: 5000    mV Excitation

07: 10      Loc [:Humid %RH]

08: .1      Mult

09: 0       Offset

75:  P20      Set Port

01: 0       Set low

02: 1       Port Number

76:  P30      Z=F               Beginning of Dewpoint Calculations

01: 9.5     F

02: 48      Z Loc [:a        ]

77:  P30      Z=F

01: 265.5   F

02: 49      Z Loc [:b        ]

78:  P37      Z=X*F

01: 5       X Loc Temp UC C

02: 9.5     F

03: 50      Z Loc [:a*T      ]

79:  P34      Z=X+F

01: 5       X Loc Temp UC C

02: 265.5   F

03: 51      Z Loc [:b+T      ]

80:  P38      Z=X/Y

01: 50      X Loc a*T

02: 51      Y Loc b+T

03: 52      Z Loc [:aT/b+T   ]

81:  P34      Z=X+F

01: 52      X Loc aT/b+T

02: -2      F

03: 53      Z Loc [:aT/b+T-2 ]

82:  P40      Z=LN(X)

01: 10      X Loc Humid %RH

02: 54      Z Loc [:ln(RH)   ]

83:  P30      Z=F

01: 2.303   F

02: 55      Z Loc [:ln/log   ]

84:  P38      Z=X/Y

01: 54      X Loc ln(RH)

02: 55      Y Loc ln/log

03: 56      Z Loc [:log (RH) ]

85:  P33      Z=X+Y

01: 56      X Loc log (RH)

02: 53      Y Loc aT/b+T-2

03: 57      Z Loc [:log +aT/b]

86:  P38      Z=X/Y

01: 48      X Loc a

02: 57      Y Loc log +aT/b

03: 58      Z Loc [:a/logRH  ]

87:  P38      Z=X/Y

01: 49      X Loc b

02: 58      Y Loc a/logRH

03: 22      Z Loc [:Dewpoint ]       End of Dewpoint Calculations

88:  P95      End

89:  P92      If time is

01: 0       minutes into a

02: 1       minute interval

03: 30      Then Do

90:  P89      If X<=>F

01: 64      X Loc Minutes

02: 3       >=

03: 55      F

04: 30      Then Do

91:  P4       Excite,Delay,Volt(SE)     Belfort Weighing Gauge

01: 1       Rep

02: 5       5000 mV slow Range

03: 12      IN Chan

04: 4       Excite all reps w/EXchan 4

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 19      Loc [:Belfortmm]

08: .07824  Mult

09: 0       Offset

92:  P20      Set Port                   Begin Snow Depth Sensor

01: 1       Set high

02: 6       Port Number

93:  P20      Set Port

01: 0       Set low

02: 4       Port Number

94:  P20      Set Port

01: 1       Set high

02: 5       Port Number

95:  P20      Set Port

01: 0       Set low

02: 5       Port Number

96:  P20      Set Port

01: 1       Set high

02: 4       Port Number

97:  P20      Set Port

01: 1       Set high

02: 5       Port Number

98:  P20      Set Port

01: 0       Set low

02: 5       Port Number

99:  P20      Set Port

01: 0       Set low

02: 4       Port Number

100: P87      Beginning of Loop

01: 0       Delay

02: 6       Loop Count

101: P20      Set Port

01: 1       Set high

02: 5       Port Number

102: P20      Set Port

01: 0       Set low

02: 5       Port Number

103: P95      End

104: P20      Set Port

01: 1       Set high

02: 5       Port Number

105: P22      Excitation with Delay

01: 1       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

106: P20      Set Port

01: 0       Set low

02: 6       Port Number

107: P20      Set Port

01: 1       Set high

02: 6       Port Number

108: P22      Excitation with Delay

01: 1       EX Chan

02: 8       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

109: P20      Set Port

01: 0       Set low

02: 5       Port Number

110: P30      Z=F

01: 1       F

02: 39      Z Loc [:Snow Calc]

111: P30      Z=F

01: 0       F

02: 42      Z Loc [:Snow # Pu]

112: P87      Beginning of Loop

01: 0       Delay

02: 16      Loop Count

113: P20      Set Port

01: 1       Set high

02: 5       Port Number

114: P20      Set Port

01: 0       Set low

02: 5       Port Number

115: P1       Volt (SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 13      IN Chan

04: 40      Loc [:Snow Data]

05: 1       Mult

06: 0       Offset

116: P89      If X<=>F

01: 40      X Loc Snow Data

02: 3       >=

03: 3000    F

04: 30      Then Do

117: P33      Z=X+Y

01: 39      X Loc Snow Calc

02: 42      Y Loc Snow # Pu

03: 42      Z Loc [:Snow # Pu]

118: P95      End

119: P37      Z=X*F

01: 39      X Loc Snow Calc

02: 2       F

03: 39      Z Loc [:Snow Calc]

120: P95      End

121: P30      Z=F

01: 291     F

02: 41      Z Loc [:T2 291 K ]

122: P38      Z=X/Y

01: 28      X Loc Temp LC K

02: 41      Y Loc T2 291 K

03: 20      Z Loc [:Snow D mm]

123: P39      Z=SQRT(X)

01: 20      X Loc Snow D mm

02: 20      Z Loc [:Snow D mm]

124: P36      Z=X*Y

01: 42      X Loc Snow # Pu

02: 20      Y Loc Snow D mm

03: 20      Z Loc [:Snow D mm]

125: P37      Z=X*F

01: 20      X Loc Snow D mm

02: .52176  F

03: 20      Z Loc [:Snow D mm]

126: P34      Z=X+F

01: 20      X Loc Snow D mm

02: -39     F

03: 20      Z Loc [:Snow D mm]

127: P20      Set Port

01: 0       Set low

02: 4       Port Number

128: P20      Set Port

01: 0       Set low

02: 5       Port Number

129: P20      Set Port                 End of Snow Depth

01: 0       Set low

02: 6       Port Number

130: P89      If X<=>F           Five Minute Average at the top of

01: 64      X Loc Minutes    the hour for Belfort and Snow Depth

02: 1       =

03: 59      F

04: 10      Set high Flag 0 (output)

131: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 15      Array ID or location

132: P71      Average

01: 2       Reps

02: 19      Loc Belfortmm

133: P95      End

134: P95      End

135: P92      If time is

01: 0       minutes into a

02: 60      minute interval

03: 30      Then Do

136: P35      Z=X-Y

01: 15      X Loc Av Belfor

02: 59      Y Loc Prev Belf

03: 60      Z Loc [:Belf Diff]

137: P31      Z=X

01: 15      X Loc Av Belfor

02: 59      Z Loc [:Prev Belf]

138: P95      End

139: P89      If X<=>F           Two minute average of Wind Speed

01: 64      X Loc Minutes      and Direction at top of the hour

02: 3       >=

03: 58      F

04: 10      Set high Flag 0 (output)

140: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 23      Array ID or location

141: P69      Wind Vector

01: 1       Rep

02: 0       Samples per sub-interval

03: 1       Polar Sensor/(S, D1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

142: P92      If time is

01: 59      minutes into a

02: 60      minute interval

03: 10      Set high Flag 0 (output)

143: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 61      Array ID or location

144: P71      Average           One minute average of Pressure

01: 1       Rep               at top of the hour

02: 11      Loc Press KPa

145: P71      Average           One minute average of Temperature

01: 1       Rep               at top of the hour

02: 5       Loc Temp UC C

146: P71      Average           One minute average of Dewpoint

01: 1       Rep               at top of the hour

02: 22      Loc Dewpoint

147: P92      If time is            Begin writing to the array -

01: 0       minutes into a        15 minute interval

02: 15      minute interval

03: 10      Set high Flag 0 (output)

148: P80      Set Active Storage Area

01: 1       Final Storage Area

02: 4       Array ID or location

149: P70      Sample                     Sample Battery

01: 1       Rep

02: 25      Loc Battery V

150: P77      Real Time                  Year, Day, Time

01: 1110    Year,Day,Hour-Minute

151: P78      Resolution

01: 1       High Resolution

152: P72      Totalize           Totalize Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Loc Par KJ/m2

153: P78      Resolution

01: 0       Low Resolution

154: P82      Standard Deviation Std Dev Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Sample Loc Par KJ/m2

155: P71      Average           Average TempUC, TempLC, Temp10

01: 6       Reps              Temp20, Temp50, RelHum

02: 5       Loc Temp UC C

156: P78      Resolution

01: 1       High Resolution

157: P71      Average           Average Pressure

01: 1       Rep

02: 11      Loc Press KPa

158: P78      Resolution

01: 0       Low Resolution

159: P71      Average           Average IRSensor

01: 1       Rep

02: 12      Loc IRSensorC

160: P82      Standard Deviation Std Dev Temp UC, TempLC, Temp10

01: 8       Reps               Temp20, Temp50, RelHum, Pressure

02: 5       Sample Loc Temp UC C IRSensor

161: P69      Wind Vector      Average Wind Speed, Wind Direction

01: 1       Rep                   and Std Dev Wind Direction

02: 0       Samples per sub-interval

03: 0       Polar Sensor/(S, D1, SD1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

162: P82      Standard Deviation      Std Dev Wind Speed

01: 1       Rep

02: 14      Sample Loc WindS m/s

163: P70      Sample                Sample Belfort, Snow Depth

01: 2       Reps                  Average of last 5 minutes

02: 15      Loc Av Belfor         of the hour

164: P72      Totalize                Totalize Tip Bucket

01: 1       Rep

02: 18      Loc TipBuc mm

165: P33      Z=X+Y

01: 18      X Loc TipBuc mm

02: 65      Y Loc Total Tip

03: 65      Z Loc [:Total Tip]

166: P70      Sample                     Sample Soil Moisture

01: 1       Rep                       Average of minute 50

02: 17      Loc Av Soil M             of the hour

167: P78      Resolution

01: 1       High Resolution

168: P70      Sample           Sample Pressure for GTS

01: 1       Rep

02: 61      Loc Press 1hr

169: P78      Resolution

01: 0       Low Resolution

170: P70      Sample   Sample TempUC, Dewpoint for GTS

01: 2       Reps

02: 62      Loc Temp  1hr

171: P70      Sample           Sample Wind Dir for GTS

01: 1       Rep

02: 24      Loc WindD 1hr

172: P70      Sample         Sample Wind Speed for GTS

01: 1       Rep

02: 23      Loc WindS 1hr

173: P70      Sample      Sample Belfort difference from

01: 1       Rep           previous hour

02: 60      Loc Belf Diff

174: P70      Sample      Sample Total Tipping Bucket for season

01: 1       Rep

02: 65      Loc Total Tip

175: P70      Sample

01: 2       Reps

02: 73      Loc ThC 1sec

176: P96      Serial Output

01: 30      SM192/SM716/CSM1

177: P18      Time                Store end of Program time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 45      Loc [:LastTime ]

178: P35      Z=X-Y                Program Execution Time

01: 45      X Loc LastTime

02: 43      Y Loc FirstTime

03: 44      Z Loc [:Prog Time]

179: P        End Table 1

*     2       Table 2 Programs

01: 60      Sec. Execution Interval

01:  P92      If time is

01: 50      minutes into a

02: 60      minute interval

03: 30      Then Do

02:  P89      If X<=>F

01: 43      X Loc FirstTime

02: 4       <

03: 200     F

04: 30      Then Do

03:  P86      Do

01: 10      Set high Flag 0 (output)

04:  P30      Z=F

01: 0       F

02: 29      Z Loc [:OV  Pw   ]

05:  P30      Z=F

01: 2000    F

02: 66      Z Loc [:2V  Pw   ]

06:  P17      Panel Temperature

01: 67      Loc [:PanelTemp]

07:  P20      Set Port

01: 1       Set high

02: 1       Port Number

08:  P87      Beginning of Loop

01: 0       Delay

02: 2       Loop Count

09:  P20      Set Port

01: 1       Set high

02: 2       Port Number

10:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

11:  P20      Set Port

01: 0       Set low

02: 2       Port Number

12:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0.0000  mV Excitation

13:  P95      End

14:  P21      Analog Out

01: 2       CAO Chan

02: 66      mV Loc 2V  Pw

15:  P22      Excitation with Delay

01: 4       EX Chan

02: 100     Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

16:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 46      Loc [:ThC 1 sec]

07: 1       Mult

08: 0       Offset

17:  P22      Excitation with Delay

01: 4       EX Chan

02: 2000    Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

18:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 47      Loc [:ThC 21sec]

07: 1       Mult

08: 0       Offset

19:  P21      Analog Out

01: 2       CAO Chan

02: 29      mV Loc OV  Pw

20:  P20      Set Port

01: 0       Set low

02: 1       Port Number

21:  P35      Z=X-Y                   End of Soil Moisture

01: 47      X Loc ThC 21sec

02: 46      Y Loc ThC 1 sec

03: 68      Z Loc [:Soil Diff]

22:  P37      Z=X*F

01: 68      X Loc Soil Diff

02: 4.89    F

03: 69      Z Loc [:Soil Mult]

23:  P30      Z=F

01: 10      F

02: 70      Z Loc [:Soil Ten ]

24:  P47      Z=X^Y

01: 70      X Loc Soil Ten

02: 69      Y Loc Soil Mult

03: 71      Z Loc [:Soil Sub ]

25:  P37      Z=X*F

01: 71      X Loc Soil Sub

02: .00026  F

03: 72      Z Loc [:Soil Res ]

26:  P37      Z=X*F

01: 72      X Loc Soil Res

02: .1      F

03: 21      Z Loc [:Soil MPa ]

27:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 17      Array ID or location

28:  P70      Sample

01: 1       Rep

02: 21      Loc Soil MPa

29:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 73      Array ID or location

30:  P70      Sample

01: 2       Reps

02: 46      Loc ThC 1 sec

31:  P95      End

32:  P95      End

33:  P        End Table 2

*     3       Table 3 Subroutines

01:  P        End Table 3

*     4       Mode 4 Output Options

01: 0       (Tape OFF) (Printer OFF)

02: 0       Printer 300 Baud

*     A       Mode 10 Memory Allocation

01: 76      Input Locations

02: 130     Intermediate Locations

*     C       Mode 12 Security (OSX-0)

01: 00      Security Option

02: 0000    Security Code

Input Location Assignments (with comments):

Key:

T=Table Number

E=Entry Number

L=Location Number

T:  E:  L:

1:  4:  1:  Loc [:Par KJ/m2]

1:  5:  2:  Loc [:Net KJ/m2]

1:  6:  3:  Loc [:AlU KJ/m2]

1:  7:  4:  Loc [:AlD KJ/m2]

1: 70:  5:  F(X) Loc [:Temp UC C]

1: 64:  6:  F(X) Loc [:Temp LC C]

1: 51:  7:  Loc [:Soil 10cm]

1: 55:  8:  Loc [:Soil 20cm]

1: 59:  9:  Loc [:Soil 50cm]

1: 74: 10:  Loc [:Humid %RH]

1: 43: 11:  Loc [:Press KPa]

1: 33: 12:  Z Loc [:IRSensorC]

1: 35: 13:  Loc [:WindDdegT]

1: 36: 14:  Loc [:WindS m/s]

1: 37: 18:  Loc [:TipBuc mm]

1: 91: 19:  Loc [:Belfortmm]

1:122: 20:  Z Loc [:Snow D mm]

1:123: 20:  Z Loc [:Snow D mm]

1:124: 20:  Z Loc [:Snow D mm]

1:125: 20:  Z Loc [:Snow D mm]

1:126: 20:  Z Loc [:Snow D mm]

2: 26: 21:  Z Loc [:Soil MPa ]

1: 87: 22:  Z Loc [:Dewpoint ]       End of Dewpoint Calculations

1:  3: 25:  Loc [:Battery V]

1: 63: 26:  Loc [:LC Store ]

1: 69: 27:  Loc [:UC Store ]

1: 65: 28:  Z Loc [:Temp LC K]

1:  8: 29:  Z Loc [:OV  Pw   ]

2:  4: 29:  Z Loc [:OV  Pw   ]

1:  9: 30:  Z Loc [:5V  Pw   ]

1: 11: 31:  Loc [:Ed Volts ]

1: 12: 32:  Loc [:Erel Volt]

1: 28: 32:  Z Loc [:Erel Volt]

1: 14: 33:  F(X) Loc [:Td C     ]

1: 18: 33:  F(X) Loc [:Td C     ]

1: 22: 33:  Z Loc [:Td C     ]

1: 25: 33:  F(X) Loc [:Td C     ]

1: 17: 34:  Z Loc [:Temporary]

1: 20: 34:  Z Loc [:Temporary]

1: 21: 34:  Z Loc [:Temporary]

1: 24: 34:  Z Loc [:Temporary]

1: 19: 35:  Z Loc [:Six      ]

1: 29: 36:  Z Loc [:Erel Mult]

1: 30: 36:  Z Loc [:Erel Mult]

1: 31: 37:  Z Loc [:Ecrel V  ]

1: 32: 38:  F(X) Loc [:Trel C   ]

1:110: 39:  Z Loc [:Snow Calc]

1:119: 39:  Z Loc [:Snow Calc]

1:115: 40:  Loc [:Snow Data]

1:121: 41:  Z Loc [:T2 291 K ]

1:111: 42:  Z Loc [:Snow # Pu]

1:117: 42:  Z Loc [:Snow # Pu]

1:  1: 43:  Loc [:FirstTime]

1:178: 44:  Z Loc [:Prog Time]

1:177: 45:  Loc [:LastTime ]

2: 16: 46:  Loc [:ThC 1 sec]

2: 18: 47:  Loc [:ThC 21sec]

1: 76: 48:  Z Loc [:a        ]

1: 77: 49:  Z Loc [:b        ]

1: 78: 50:  Z Loc [:a*T      ]

1: 79: 51:  Z Loc [:b+T      ]

1: 80: 52:  Z Loc [:aT/b+T   ]

1: 81: 53:  Z Loc [:aT/b+T-2 ]

1: 82: 54:  Z Loc [:ln(RH)   ]

1: 83: 55:  Z Loc [:ln/log   ]

1: 84: 56:  Z Loc [:log (RH) ]

1: 85: 57:  Z Loc [:log +aT/b]

1: 86: 58:  Z Loc [:a/logRH  ]

1:137: 59:  Z Loc [:Prev Belf]

1:136: 60:  Z Loc [:Belf Diff]

1:  2: 64:  Loc [:Minutes  ]

1:165: 65:  Z Loc [:Total Tip]

2:  5: 66:  Z Loc [:2V  Pw   ]

2:  6: 67:  Loc [:PanelTemp]

2: 21: 68:  Z Loc [:Soil Diff]

2: 22: 69:  Z Loc [:Soil Mult]

2: 23: 70:  Z Loc [:Soil Ten ]

2: 24: 71:  Z Loc [:Soil Sub ]

2: 25: 72:  Z Loc [:Soil Res ]

Input Location Labels:

1:Par KJ/m2    20:Snow D mm    39:Snow Calc    58:a/logRH

2:Net KJ/m2    21:Soil MPa     40:Snow Data    59:Prev Belf

3:AlU KJ/m2    22:Dewpoint     41:T2 291 K     60:Belf Diff

4:AlD KJ/m2    23:WindS 1hr    42:Snow # Pu    61:Press 1hr

5:Temp UC C    24:WindD 1hr    43:FirstTime    62:Temp  1hr

6:Temp LC C    25:Battery V    44:Prog Time    63:Dewpt 1hr

7:Soil 10cm    26:LC Store     45:LastTime     64:Minutes

8:Soil 20cm    27:UC Store     46:ThC 1 sec    65:Total Tip

9:Soil 50cm    28:Temp LC K    47:ThC 21sec    66:2V  Pw

10:Humid %RH    29:OV  Pw       48:a            67:PanelTemp

11:Press KPa    30:5V  Pw       49:b            68:Soil Diff

12:IRSensorC    31:Ed Volts     50:a*T          69:Soil Mult

13:WindDdegT    32:Erel Volt    51:b+T          70:Soil Ten

14:WindS m/s    33:Td C         52:aT/b+T       71:Soil Sub

15:Av Belfor    34:Temporary    53:aT/b+T-2     72:Soil Res

16:Av Snow D    35:Six          54:ln(RH)       73:ThC 1sec

17:Av Soil M    36:Erel Mult    55:ln/log       74:ThC 21sec

18:TipBuc mm    37:Ecrel V      56:log (RH)     75:_________

19:Belfortmm    38:Trel C       57:log +aT/b    76:_________

Program: Boreas Suite B Nipawin Mar 28/94

Flag Usage:

Input Channel Usage:

Excitation Channel Usage:

Continous Analog Output Usage:

Control Port Usage:

Pulse Input Channel Usage:

Output Array Definitions:

*     1       Table 1 Programs

01: 5       Sec. Execution Interval

01:  P22      Excitation with Delay               Signal Light

01: 3       EX Chan

02: 25      Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 2500    mV Excitation

02:  P2       Volt (DIFF)                         Pyranometer

01: 1       Rep

02: 23      25 mV 60 Hz rejection Range

03: 1       IN Chan

04: 1       Loc [:PSP kJ/m2]

05: .57013  Mult

06: 0.0000  Offset

03:  P2       Volt (DIFF)                        Pyrgeometer

01: 1       Rep

02: 23      25 mV 60 Hz rejection Range

03: 2       IN Chan

04: 2       Loc [:PIR kJ/m2]

05: 1.3298  Mult

06: 0.0000  Offset

04:  P2       Volt (DIFF)

01: 1       Rep

02: 21      2.5 mV 60 Hz rejection Range

03: 3       IN Chan

04: 3       Loc [:ThPile mV]

05: 1       Mult

06: 0.0000  Offset

05:  P89      If X<=>F

01: 1       X Loc PSP kJ/m2

02: 4       <

03: 0.0000  F

04: 30      Then Do

06:  P30      Z=F

01: 0.0000  F

02: 00      Exponent of 10

03: 1       Z Loc [:PSP kJ/m2]

07:  P95      End

08:  P89      If X<=>F

01: 2       X Loc PIR kJ/m2

02: 4       <

03: 0.0000  F

04: 30      Then Do

09:  P30      Z=F

01: 0.0000  F

02: 00      Exponent of 10

03: 2       Z Loc [:PIR kJ/m2]

10:  P95      End

YSI 44031 Thermistor Measurement

11:  P4       Excite,Delay,Volt(SE)

01: 2       Reps

02: 24      250 mV 60 Hz rejection Range

03: 7       IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0000    Delay (units .01sec)

06: 1700    mV Excitation

07: 4       Loc [:Tcase C  ]

08: .01     Mult

09: 0       Offset

YSI 44031 Linearization

12:  P87      Beginning of Loop

01: 0000    Delay

02: 2       Loop Count

13:  P89      If X<=>F

01: 4--     X Loc Tcase C

02: 4       <

03: .5      F

04: 30      Then Do

14:  P55      Polynomial

01: 1       Rep

02: 4--     X Loc Tcase C

03: 4--     F(X) Loc [:Tcase C  ]

04: -64.140 C0

05: 472.02  C1

06: -2304.8 C2

07: 7037.4  C3

08: -11140  C4

09: 7001.6  C5

15:  P94      Else

16:  P55      Polynomial

01: 1       Rep

02: 4--     X Loc Tcase C

03: 4--     F(X) Loc [:Tcase C  ]

04: -32.981 C0

05: 85.859  C1

06: -62.706 C2

07: 30.782  C3

08: -8.1108 C4

09: .87158  C5

17:  P95      End

18:  P95      End

19:  P92      If time is

01: 0       minutes into a

02: 15      minute interval

03: 10      Set high Flag 0 (output)

20:  P80      Set Active Storage Area

01: 1       Final Storage Area 1

02: 4       Array ID or location

21:  P77      Real Time

01: 1220    Year,Day,Hour-Minute

22:  P78      Resolution

01: 1       High Resolution

23:  P72      Totalize             Totalize PSP, PIR, ThPile

01: 3       Reps

02: 1       Loc PSP kJ/m2

24:  P78      Resolution

01: 0       Low Resolution

25:  P71      Average            Average Tcase, Themisph

01: 2       Reps

02: 4       Loc Tcase C

26:  P82      Standard Deviation   Std Dev PSP, PIR, ThPile,

01: 5       Reps                         Tcase, Themisph

02: 1       Sample Loc PSP kJ/m2

27:  P96      Serial Output

01: 71      SM192/SM716/CSM1

28:  P        End Table 1

*     2       Table 2 Programs

01: 0.0000  Sec. Execution Interval

01:  P        End Table 2

*     3       Table 3 Subroutines

01:  P        End Table 3

*     A       Mode 10 Memory Allocation

01: 28      Input Locations

02: 64      Intermediate Locations

03: 0.0000  Final Storage Area 2

*     C       Mode 12 Security

01: 0000    LOCK 1

02: 0000    LOCK 2

03: 0000    LOCK 3

Input Location Assignments (with comments):

Key:

T=Table Number

E=Entry Number

L=Location Number

T:  E:  L:

1:  2:  1:  Loc [:PSP kJ/m2]

1:  6:  1:  Z Loc [:PSP kJ/m2]

1:  3:  2:  Loc [:PIR kJ/m2]

1:  9:  2:  Z Loc [:PIR kJ/m2]

1:  4:  3:  Loc [:ThPile mV]

1: 11:  4:  Loc [:Tcase C  ]

1: 14:  4:  F(X) Loc [:Tcase C  ]

1: 16:  4:  F(X) Loc [:Tcase C  ]

Program:   Boreas   Saskatoon, SK  November 24, 1995

Flag Usage:

Input Channel Usage:

Excitation Channel Usage:

Continuous Analog Output Usage:

Control Port Usage:

Pulse Input Channel Usage:

Output Array Definitions:

*     1       Table 1 Programs

01: 10      Sec. Execution Interval

01:  P30      Z=F      Spacer for instruments not used

01: -999    F

02: 46      Z Loc [:Spacer   ]

02:  P18      Time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 37      Loc [:FirstTime]

03:  P18      Time

01: 1       Minutes into current day (maximum 1440)

02: 60      Mod/by

03: 64      Loc [:Minutes  ]

04:  P17      Panel Temperature      Interior bunker temperature

01: 32      Loc [:Bunker C ]

05:  P3       Pulse               RM Young Wind Speed

01: 1       Rep

02: 3       Pulse Input Chan

03: 21      Low level AC; Output Hz.

04: 20      Loc [:WindS m/s]

05: .098    Mult

06: 0       Offset

06:  P4       Excite,Delay,Volt(SE)      Wind Direction

01: 1       Rep

02: 5       5000 mV slow Range

03: 8       IN Chan

04: 3       Excite all reps w/EXchan 3

05: 3       Delay (units .01sec)

06: 5000    mV Excitation

07: 21      Loc [:WindDdegT]

08: .071    Mult

09: 0       Offset

07:  P3       Pulse                Tipping Bucket

01: 1       Rep                  .2 mm/tip

02: 2       Pulse Input Chan

03: 2       Switch closure

04: 16      Loc [:TipBuc mm]

05: .2      Mult

06: 0       Offset

08:  P3       Pulse                Bright Sunshine

01: 1       Rep                  .1 hours/pulse

02: 1       Pulse Input Chan

03: 2       Switch closure

04: 47      Loc [:BrightSun]

05: .1      Mult

06: 0       Offset

09:  P92      If time is

01: 0       minutes into a

02: 1       minute interval

03: 30      Then Do

10:  P89      If X<=>F

01: 64      X Loc Minutes

02: 3       >=

03: 55      F

04: 30      Then Do

11:  P20      Set Port           Belfort Precipitation

01: 1       Set high

02: 3       Port Number

12:  P20      Set Port

01: 1       Set high

02: 2       Port Number

13:  P22      Excitation with Delay

01: 1       EX Chan

02: 20      Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

14:  P20      Set Port

01: 0       Set low

02: 3       Port Number

15:  P20      Set Port

01: 1       Set high

02: 3       Port Number

16:  P20      Set Port

01: 0       Set low

02: 2       Port Number

17:  P30      Z=F

01: 0       F

02: 17      Z Loc [:Belfortmm]

18:  P30      Z=F

01: 1       F

02: 40      Z Loc [:Weightx10]

19:  P87      Beginning of Loop

01: 0       Delay

02: 3       Loop Count

20:  P30      Z=F

01: 1       F

02: 41      Z Loc [:Weightx2 ]

21:  P30      Z=F

01: 0       F

02: 42      Z Loc [:Subtotal ]

22:  P87      Beginning of Loop

01: 0       Delay

02: 4       Loop Count

23:  P1       Volt (SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 3       IN Chan

04: 43      Loc [:HI or LO ]

05: 1       Mult

06: 0       Offset

24:  P89      If X<=>F

01: 43      X Loc HI or LO

02: 3       >=

03: 3000    F

04: 30      Then Do

25:  P33      Z=X+Y

01: 41      X Loc Weightx2

02: 42      Y Loc Subtotal

03: 42      Z Loc [:Subtotal ]

26:  P95      End

27:  P20      Set Port

01: 1       Set high

02: 2       Port Number

28:  P20      Set Port

01: 0       Set low

02: 2       Port Number

29:  P37      Z=X*F

01: 41      X Loc Weightx2

02: 2       F

03: 41      Z Loc [:Weightx2 ]

30:  P95      End

31:  P36      Z=X*Y

01: 42      X Loc Subtotal

02: 40      Y Loc Weightx10

03: 42      Z Loc [:Subtotal ]

32:  P33      Z=X+Y

01: 42      X Loc Subtotal

02: 17      Y Loc Belfortmm

03: 17      Z Loc [:Belfortmm]

33:  P37      Z=X*F

01: 40      X Loc Weightx10

02: 10      F

03: 40      Z Loc [:Weightx10]

34:  P95      End

35:  P20      Set Port

01: 0       Set low

02: 3       Port Number

36:  P20      Set Port                End of Belfort

01: 0       Set low

02: 2       Port Number

37:  P20      Set Port                Snow Depth Sensor

01: 1       Set high

02: 6       Port Number

38:  P20      Set Port

01: 0       Set low

02: 4       Port Number

39:  P20      Set Port

01: 1       Set high

02: 5       Port Number

40:  P20      Set Port

01: 0       Set low

02: 5       Port Number

41:  P20      Set Port

01: 1       Set high

02: 4       Port Number

42:  P20      Set Port

01: 1       Set high

02: 5       Port Number

43:  P20      Set Port

01: 0       Set low

02: 5       Port Number

44:  P20      Set Port

01: 0       Set low

02: 4       Port Number

45:  P87      Beginning of Loop

01: 0       Delay

02: 6       Loop Count

46:  P20      Set Port

01: 1       Set high

02: 5       Port Number

47:  P20      Set Port

01: 0       Set low

02: 5       Port Number

48:  P95      End

49:  P20      Set Port

01: 1       Set high

02: 5       Port Number

50:  P22      Excitation with Delay

01: 1       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

51:  P20      Set Port

01: 0       Set low

02: 6       Port Number

52:  P20      Set Port

01: 1       Set high

02: 6       Port Number

53:  P22      Excitation with Delay

01: 1       EX Chan

02: 8       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

54:  P20      Set Port

01: 0       Set low

02: 5       Port Number

55:  P30      Z=F

01: 1       F

02: 33      Z Loc [:Snow Calc]

56:  P30      Z=F

01: 0       F

02: 36      Z Loc [:Snow # Pu]

57:  P87      Beginning of Loop

01: 0       Delay

02: 16      Loop Count

58:  P20      Set Port

01: 1       Set high

02: 5       Port Number

59:  P20      Set Port

01: 0       Set low

02: 5       Port Number

60:  P1       Volt (SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 4       IN Chan

04: 34      Loc [:Snow Data]

05: 1       Mult

06: 0       Offset

61:  P89      If X<=>F

01: 34      X Loc Snow Data

02: 3       >=

03: 3000    F

04: 30      Then Do

62:  P33      Z=X+Y

01: 33      X Loc Snow Calc

02: 36      Y Loc Snow # Pu

03: 36      Z Loc [:Snow # Pu]

63:  P95      End

64:  P37      Z=X*F

01: 33      X Loc Snow Calc

02: 2       F

03: 33      Z Loc [:Snow Calc]

65:  P95      End

66:  P30      Z=F

01: 291     F

02: 35      Z Loc [:T2 291K  ]

67:  P38      Z=X/Y

01: 44      X Loc Temp LC K

02: 35      Y Loc T2 291K

03: 18      Z Loc [:Snow D mm]

68:  P39      Z=SQRT(X)

01: 18      X Loc Snow D mm

02: 18      Z Loc [:Snow D mm]

69:  P36      Z=X*Y

01: 36      X Loc Snow # Pu

02: 18      Y Loc Snow D mm

03: 18      Z Loc [:Snow D mm]

70:  P37      Z=X*F

01: 18      X Loc Snow D mm

02: .52176  F

03: 18      Z Loc [:Snow D mm]

71:  P34      Z=X+F

01: 18      X Loc Snow D mm

02: -39     F

03: 18      Z Loc [:Snow D mm]

72:  P20      Set Port

01: 0       Set low

02: 4       Port Number

73:  P20      Set Port

01: 0       Set low

02: 5       Port Number

74:  P20      Set Port                End of Snow Depth

01: 0       Set low

02: 6       Port Number

75:  P89      If X<=>F           Five minute average at the top of

01: 64      X Loc Minutes      the hour for Belfort and Snow Depth

02: 1       =

03: 59      F

04: 10      Set high Flag 0 (output)

76:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 28      Array ID or location

77:  P71      Average

01: 2       Reps

02: 17      Loc Belfortmm

78:  P95      End

79:  P95      End

80:  P10      Battery Voltage           Battery Voltage

01: 31      Loc [:Battery V]

81:  P20      Set Port                Start the multiplexer

01: 1       Set high

02: 1       Port Number

82:  P22      Excitation with Delay

01: 1       EX Chan

02: 10      Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

83:  P7       3 Wire Half Bridge      Soil Temperature - 5 cm

01: 1       Rep

02: 4       500 mV slow Range

03: 1       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 4300    mV Excitation

06: 5       Loc [:Soil  5cm]

07: 100.93  Mult

08: 0       Offset

84:  P16      Temperature RTD

01: 1       Rep

02: 5       R/Ro Loc Soil  5cm

03: 5       Loc [:Soil  5cm]

04: 1       Mult

05: 0       Offset

85:  P22      Excitation with Delay

01: 1       EX Chan

02: 10      Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

86:  P7       3 Wire Half Bridge           Soil Temperature - 10 cm

01: 1       Rep

02: 4       500 mV slow Range

03: 1       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 4300    mV Excitation

06: 6       Loc [:Soil 10cm]

07: 100.93  Mult

08: 0       Offset

87:  P16      Temperature RTD

01: 1       Rep

02: 6       R/Ro Loc Soil 10cm

03: 6       Loc [:Soil 10cm]

04: 1       Mult

05: 0       Offset

88:  P22      Excitation with Delay

01: 1       EX Chan

02: 10      Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

89:  P7       3 Wire Half Bridge           Soil Temperature - 20 cm

01: 1       Rep

02: 4       500 mV slow Range

03: 1       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 4300    mV Excitation

06: 7       Loc [:Soil 20cm]

07: 100.93  Mult

08: 0       Offset

90:  P16      Temperature RTD

01: 1       Rep

02: 7       R/Ro Loc Soil 20cm

03: 7       Loc [:Soil 20cm]

04: 1       Mult

05: 0       Offset

91:  P22      Excitation with Delay

01: 1       EX Chan

02: 10      Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

92:  P7       3 Wire Half Bridge           Soil Temperature - 50 cm

01: 1       Rep

02: 4       500 mV slow Range

03: 1       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 4300    mV Excitation

06: 8       Loc [:Soil 50cm]

07: 100.93  Mult

08: 0       Offset

93:  P16      Temperature RTD

01: 1       Rep

02: 8       R/Ro Loc Soil 50cm

03: 8       Loc [:Soil 50cm]

04: 1       Mult

05: 0       Offset

94:  P22      Excitation with Delay

01: 1       EX Chan

02: 10      Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

95:  P7       3 Wire Half Bridge      Soil Temperature - 100 cm

01: 1       Rep

02: 4       500 mV slow Range

03: 1       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 4300    mV Excitation

06: 9       Loc [:Soil100cm]

07: 100.93  Mult

08: 0       Offset

96:  P16      Temperature RTD

01: 1       Rep

02: 9       R/Ro Loc Soil100cm

03: 9       Loc [:Soil100cm]

04: 1       Mult

05: 0       Offset

97:  P22      Excitation with Delay

01: 1       EX Chan

02: 10      Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

98:  P7       3 Wire Half Bridge           Soil Temperature - 150 cm

01: 1       Rep

02: 4       500 mV slow Range

03: 1       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 4300    mV Excitation

06: 10      Loc [:Soil150cm]

07: 100.93  Mult

08: 0       Offset

99:  P16      Temperature RTD

01: 1       Rep

02: 10      R/Ro Loc Soil150cm

03: 10      Loc [:Soil150cm]

04: 1       Mult

05: 0       Offset

100: P22      Excitation with Delay

01: 1       EX Chan

02: 10      Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

101: P7       3 Wire Half Bridge           Soil Temperature - 300 cm

01: 1       Rep

02: 4       500 mV slow Range

03: 1       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 4300    mV Excitation

06: 11      Loc [:Soil300cm]

07: 100.93  Mult

08: 0       Offset

102: P16      Temperature RTD

01: 1       Rep

02: 11      R/Ro Loc Soil300cm

03: 11      Loc [:Soil300cm]

04: 1       Mult

05: 0       Offset

103: P22      Excitation with Delay

01: 1       EX Chan

02: 10      Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

104: P7       3 Wire Half Bridge     Grass Temperature from RTD

01: 1       Rep                    Located in Stevenson Screen

02: 4       500 mV slow Range

03: 1       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 4300    mV Excitation

06: 48      Loc [:GrassTemp]

07: 89.845  Mult

08: 0       Offset

105: P16      Temperature RTD

01: 1       Rep

02: 48      R/Ro Loc GrassTemp

03: 48      Loc [:GrassTemp]

04: .87363  Mult

05: 0       Offset

106: P22      Excitation with Delay

01: 1       EX Chan

02: 10      Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

107: P4       Excite,Delay,Volt(SE)           HMP35C Temperature

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 2       Excite all reps w/EXchan 2

05: 10      Delay (units .01sec)

06: 500     mV Excitation

07: 12      Loc [:Temp    C]

08: .001    Mult

09: 0       Offset

108: P55      Polynomial

01: 1       Rep

02: 12      X Loc Temp    C

03: 12      F(X) Loc [:Temp    C]

04: -74.261 C0

05: 649.94  C1

06: -3896.3 C2

07: 16401   C3

08: -35045  C4

09: 30889   C5

109: P34      Z=X+F

01: 12      X Loc Temp    C

02: 273.15  F

03: 44      Z Loc [:Temp LC K]

110: P22      Excitation with Delay

01: 1       EX Chan

02: 10      Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

111: P4       Excite,Delay,Volt(SE)   HMP35C Relative Humidity

01: 1       Rep

02: 5       5000 mV slow Range

03: 14      IN Chan

04: 2       Excite all reps w/EXchan 2

05: 15      Delay (units .01sec)

06: 5000    mV Excitation

07: 14      Loc [:Humid %RH]

08: .1      Mult

09: 0       Offset

112: P30      Z=F                Beginning of Dewpoint Calculations

01: 9.5     F

02: 51      Z Loc [:a        ]

113: P30      Z=F

01: 265.5   F

02: 52      Z Loc [:b        ]

114: P37      Z=X*F

01: 12      X Loc Temp    C

02: 9.5     F

03: 53      Z Loc [:a*T      ]

115: P34      Z=X+F

01: 12      X Loc Temp    C

02: 265.5   F

03: 54      Z Loc [:b+T      ]

116: P38      Z=X/Y

01: 53      X Loc a*T

02: 54      Y Loc b+T

03: 55      Z Loc [:aT/b+T   ]

117: P34      Z=X+F

01: 55      X Loc aT/b+T

02: -2      F

03: 56      Z Loc [:aT/b+T-2 ]

118: P40      Z=LN(X)

01: 14      X Loc Humid %RH

02: 57      Z Loc [:ln(RH)   ]

119: P30      Z=F

01: 2.303   F

02: 58      Z Loc [:ln/log   ]

120: P38      Z=X/Y

01: 57      X Loc ln(RH)

02: 58      Y Loc ln/log

03: 59      Z Loc [:log (RH) ]

121: P33      Z=X+Y

01: 59      X Loc log (RH)

02: 56      Y Loc aT/b+T-2

03: 60      Z Loc [:log +aT/b]

122: P38      Z=X/Y

01: 51      X Loc a

02: 60      Y Loc log +aT/b

03: 61      Z Loc [:a/logRH  ]

123: P38      Z=X/Y

01: 52      X Loc b

02: 61      Y Loc a/logRH

03: 13      Z Loc [:DewPoint ]      End of Dewpoint Calculations

124: P22      Excitation with Delay

01: 1       EX Chan

02: 10      Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

125: P22      Excitation with Delay

01: 2       EX Chan

02: 100     Delay w/EX (units=.01sec)

03: 10      Delay after EX (units=.01sec)

04: 0       mV Excitation

126: P22      Excitation with Delay

01: 1       EX Chan

02: 10      Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

127: P2       Volt (DIFF)                Par Radiation

01: 1       Rep

02: 2       15 mV slow Range

03: 1       IN Chan

04: 1       Loc [:Par KJ/m2]

05: 1       Mult

06: 0       Offset

128: P22      Excitation with Delay

01: 1       EX Chan

02: 10      Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

129: P2       Volt (DIFF)                Albedometer Up

01: 1       Rep

02: 3       50 mV slow Range

03: 1       IN Chan

04: 3       Loc [:AlU kJ/m2]

05: 1.1891  Mult

06: 0       Offset

130: P22      Excitation with Delay

01: 1       EX Chan

02: 10      Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

131: P2       Volt (DIFF)                Albedometer Down

01: 1       Rep

02: 3       50 mV slow Range

03: 1       IN Chan

04: 4       Loc [:AlD KJ/m2]

05: 1.1416  Mult

06: 0       Offset

132: P22      Excitation with Delay

01: 1       EX Chan

02: 10      Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

133: P2       Volt (DIFF)                Net Radiometer

01: 1       Rep

02: 4       500 mV slow Range

03: 1       IN Chan

04: 2       Loc [:Net KJ/m2]

05: .128    Mult

06: 0       Offset

134: P22      Excitation with Delay

01: 1       EX Chan

02: 10      Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 5000    mV Excitation

135: P8       Excite,Delay,Volt(DIFF)      Setra Pressure

01: 1       Rep

02: 4       500 mV slow Range

03: 1       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 1       Delay (units=.01sec)

06: 2500    mV Excitation

07: 15      Loc [:Press KPa]

08: .12     Mult

09: 80      Offset

136: P20      Set Port

01: 0       Set low

02: 1       Port Number

137: P92      If time is           Calculate the Belfort change

01: 0       minutes into a       at the top of the hour

02: 60      minute interval

03: 30      Then Do

138: P35      Z=X-Y

01: 28      X Loc AvBelfort

02: 65      Y Loc Prev Belf

03: 66      Z Loc [:Belf Diff]

139: P31      Z=X

01: 28      X Loc AvBelfort

02: 65      Z Loc [:Prev Belf]

140: P95      End

141: P89      If X<=>F           Two minute average of Wind Speed

01: 64      X Loc Minutes      and Direction at top of the hour

02: 3       >=

03: 58      F

04: 10      Set high Flag 0 (output)

142: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 23      Array ID or location

143: P69      Wind Vector

01: 1       Rep

02: 0       Samples per sub-interval

03: 1       Polar Sensor/(S, D1)

04: 20      Wind Speed/East Loc WindS m/s

05: 21      Wind Direction/North Loc WindDdegT

144: P92      If time is

01: 59      minutes into a

02: 60      minute interval

03: 10      Set high Flag 0 (output)

145: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 25      Array ID or location

146: P71      Average           One minute average of Pressure

01: 1       Rep               at top of the hour

02: 15      Loc Press KPa

147: P71      Average           One minute average of Temperature

01: 2       Reps               and DewPoint at top of the hour

02: 12      Loc Temp    C

148: P92      If time is

01: 0       minutes into a

02: 60      minute interval

03: 10      Set high Flag 0 (output)

149: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 45      Array ID or location

150: P72      Totalize          Totalize Bright Sun for the hour

01: 1       Rep

02: 47      Loc BrightSun

151: P92      If time is

01: 0       minutes into a

02: 15      minute interval

03: 10      Set high Flag 0 (output)

152: P80      Set Active Storage Area

01: 1       Final Storage Area

02: 5       Array ID or location

153: P70      Sample             Sample Battery

01: 1       Rep

02: 31      Loc Battery V

154: P77      Real Time                Year, Day, Time

01: 1110    Year,Day,Hour-Minute

155: P78      Resolution

01: 1       High Resolution

156: P72      Totalize      Totalize Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Loc Par KJ/m2

157: P78      Resolution

01: 0       Low Resolution

158: P82      Standard Deviation  Std Dev Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Sample Loc Par KJ/m2

159: P71      Average           Average Air Temp

01: 1       Rep

02: 12      Loc Temp    C

160: P70      Sample           Space for other Air Temp

01: 1       Rep

02: 46      Loc Spacer

161: P71      Average           Average Soil10, Soil20, Soil50

01: 3       Reps

02: 6       Loc Soil 10cm

162: P71      Average           Average RelHum

01: 1       Rep

02: 14      Loc Humid %RH

163: P78      Resolution

01: 1       High Resolution

164: P71      Average           Average Pressure

01: 1       Rep

02: 15      Loc Press KPa

165: P78      Resolution

01: 0       Low Resolution

166: P70      Sample           Space for IR Sensor

01: 1       Rep

02: 46      Loc Spacer

167: P82      Standard Deviation     Std Dev Temperature

01: 1       Rep

02: 12      Sample Loc Temp    C

168: P70      Sample           Space for Std Dev other Temperature

01: 1       Rep

02: 46      Loc Spacer

169: P82      Standard Deviation    Std Dev Soil10, Soil20, Soil50

01: 3       Reps

02: 6       Sample Loc Soil 10cm

170: P82      Standard Deviation   Std Dev RelHum and Pressure

01: 2       Reps

02: 14      Sample Loc Humid %RH

171: P70      Sample           Space for Std Dev IR Sensor

01: 1       Rep

02: 46      Loc Spacer

172: P69      Wind Vector       Average Wind Speed, Wind Direction

01: 1       Rep               and Std Dev Wind Direction

02: 180     Samples per sub-interval

03: 0       Polar Sensor/(S, D1, SD1)

04: 20      Wind Speed/East Loc WindS m/s

05: 21      Wind Direction/North Loc WindDdegT

173: P82      Standard Deviation      Std Dev Wind Speed

01: 1       Rep

02: 20      Sample Loc WindS m/s

174: P70      Sample           Sample Average Belfort, Snow Depth

01: 2       Reps             Average of last 5 minutes of hour

02: 28      Loc AvBelfort

175: P72      Totalize           Totalize Tipping Bucket

01: 1       Rep

02: 16      Loc TipBuc mm

176: P33      Z=X+Y

01: 16      X Loc TipBuc mm

02: 75      Y Loc Total Tip

03: 75      Z Loc [:Total Tip]

177: P70      Sample           Sample Soil Moisture

01: 1       Rep              Average of minute 50

02: 30      Loc Av Soil M              of the hour

178: P78      Resolution

01: 1       High Resolution

179: P70      Sample           Sample Pressure for GTS

01: 1       Rep

02: 25      Loc Press 1hr

180: P78      Resolution

01: 0       Low Resolution

181: P70      Sample          Sample Temperature, Dewpoint for GTS

01: 2       Reps

02: 26      Loc Temp  1hr

182: P70      Sample           Sample Wind Direction for GTS

01: 1       Rep

02: 24      Loc WindD 1hr

183: P70      Sample           Sample Wind Speed for GTS

01: 1       Rep

02: 23      Loc WindS 1hr

184: P70      Sample           Sample Belfort Difference from

01: 1       Rep              previous hour

02: 66      Loc Belf Diff

185: P70      Sample      Sample Total Tipping Bucket for season

01: 1       Rep

02: 75      Loc Total Tip

186: P71      Average           Average Soil5

01: 1       Rep

02: 5       Loc Soil  5cm

187: P71      Average           Average Soil100, Soil150, Soil300

01: 3       Reps

02: 9       Loc Soil100cm

188: P72      Totalize           Totalize Bright Sun

01: 1       Rep

02: 47      Loc BrightSun

189: P71      Average           Average Grass Temp

01: 1       Rep

02: 48      Loc GrassTemp

190: P71      Average           Average Bunker Temp

01: 1       Rep

02: 32      Loc Bunker C

191: P70      Sample           Sample hourly Bright Sun

01: 1       Rep

02: 45      Loc BrSun Hr

192: P70      Sample            Sample the daily values

01: 8       Reps

02: 67      Loc BrSun Day

193: P92      If time is

01: 1437    minutes into a

02: 1440    minute interval

03: 10      Set high Flag 0 (output)

194: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 67      Array ID or location

195: P72      Totalize        Total Bright Sun for the day

01: 1       Rep

02: 47      Loc BrightSun

196: P73      Maximize           Maximum Temp for the day

01: 1       Rep

02: 10      Value with Hr-Min

03: 12      Loc Temp    C

197: P74      Minimize           Minimum Temp for the day

01: 1       Rep

02: 10      Value with Hr-Min

03: 12      Loc Temp    C

198: P73      Maximize           Maximum Wind Speed for the day

01: 1       Rep

02: 10      Value with Hr-Min

03: 20      Loc WindS m/s

199: P79      Sample on Max or Min  Wind Direction at Max Wind Speed

01: 1       Rep

02: 21      Loc WindDdegT

200: P18      Time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 39      Loc [:LastTime ]

201: P35      Z=X-Y

01: 39      X Loc LastTime

02: 37      Y Loc FirstTime

03: 38      Z Loc [:ProgTime ]

202: P        End Table 1

*     2       Table 2 Programs

01: 0       Sec. Execution Interval

01:  P        End Table 2

*     3       Table 3 Subroutines

01:  P        End Table 3

*     4       Mode 4 Output Options

01: 0       (Tape OFF) (Printer OFF)

02: 0       Printer 300 Baud

*     A       Mode 10 Memory Allocation

01: 86      Input Locations

02: 300     Intermediate Locations

*     C       Mode 12 Security (OSX-0)

01: 00      Security Option

02: 0000    Security Code

Input Location Assignments (with comments):

Key:

T=Table Number

E=Entry Number

L=Location Number

T:  E:  L:

1:127:  1:  Loc [:Par KJ/m2]

1:133:  2:  Loc [:Net KJ/m2]

1:129:  3:  Loc [:AlU kJ/m2]

1:131:  4:  Loc [:AlD KJ/m2]

1: 83:  5:  Loc [:Soil  5cm]

1: 84:  5:  Loc [:Soil  5cm]

1: 86:  6:  Loc [:Soil 10cm]

1: 87:  6:  Loc [:Soil 10cm]

1: 89:  7:  Loc [:Soil 20cm]

1: 90:  7:  Loc [:Soil 20cm]

1: 92:  8:  Loc [:Soil 50cm]

1: 93:  8:  Loc [:Soil 50cm]

1: 95:  9:  Loc [:Soil100cm]

1: 96:  9:  Loc [:Soil100cm]

1: 98: 10:  Loc [:Soil150cm]

1: 99: 10:  Loc [:Soil150cm]

1:101: 11:  Loc [:Soil300cm]

1:102: 11:  Loc [:Soil300cm]

1:107: 12:  Loc [:Temp    C]

1:108: 12:  F(X) Loc [:Temp    C]

1:123: 13:  Z Loc [:DewPoint ]      End of Dewpoint Calculations

1:111: 14:  Loc [:Humid %RH]

1:135: 15:  Loc [:Press KPa]

1:  7: 16:  Loc [:TipBuc mm]

1: 17: 17:  Z Loc [:Belfortmm]

1: 32: 17:  Z Loc [:Belfortmm]

1: 67: 18:  Z Loc [:Snow D mm]

1: 68: 18:  Z Loc [:Snow D mm]

1: 69: 18:  Z Loc [:Snow D mm]

1: 70: 18:  Z Loc [:Snow D mm]

1: 71: 18:  Z Loc [:Snow D mm]

1:  5: 20:  Loc [:WindS m/s]

1:  6: 21:  Loc [:WindDdegT]

1: 80: 31:  Loc [:Battery V]

1:  4: 32:  Loc [:Bunker C ]

1: 55: 33:  Z Loc [:Snow Calc]

1: 64: 33:  Z Loc [:Snow Calc]

1: 60: 34:  Loc [:Snow Data]

1: 66: 35:  Z Loc [:T2 291K  ]

1: 56: 36:  Z Loc [:Snow # Pu]

1: 62: 36:  Z Loc [:Snow # Pu]

1:  2: 37:  Loc [:FirstTime]

1:201: 38:  Z Loc [:ProgTime ]

1:200: 39:  Loc [:LastTime ]

1: 18: 40:  Z Loc [:Weightx10]

1: 33: 40:  Z Loc [:Weightx10]

1: 20: 41:  Z Loc [:Weightx2 ]

1: 29: 41:  Z Loc [:Weightx2 ]

1: 21: 42:  Z Loc [:Subtotal ]

1: 25: 42:  Z Loc [:Subtotal ]

1: 31: 42:  Z Loc [:Subtotal ]

1: 23: 43:  Loc [:HI or LO ]

1:109: 44:  Z Loc [:Temp LC K]

1:  1: 46:  Z Loc [:Spacer   ]

1:  8: 47:  Loc [:BrightSun]

1:104: 48:  Loc [:GrassTemp]

1:105: 48:  Loc [:GrassTemp]

1:112: 51:  Z Loc [:a        ]

1:113: 52:  Z Loc [:b        ]

1:114: 53:  Z Loc [:a*T      ]

1:115: 54:  Z Loc [:b+T      ]

1:116: 55:  Z Loc [:aT/b+T   ]

1:117: 56:  Z Loc [:aT/b+T-2 ]

1:118: 57:  Z Loc [:ln(RH)   ]

1:119: 58:  Z Loc [:ln/log   ]

1:120: 59:  Z Loc [:log (RH) ]

1:121: 60:  Z Loc [:log +aT/b]

1:122: 61:  Z Loc [:a/logRH  ]

1:  3: 64:  Loc [:Minutes  ]

1:139: 65:  Z Loc [:Prev Belf]

1:138: 66:  Z Loc [:Belf Diff]

1:176: 75:  Z Loc [:Total Tip]

Program:   Boreas Suite B Saskatoon  June 1/94

Flag Usage:

Input Channel Usage:

Excitation Channel Usage:

Continuous Analog Output Usage:

Control Port Usage:

Pulse Input Channel Usage:

Output Array Definitions:

*     1       Table 1 Programs

01: 5       Sec. Execution Interval

01:  P18      Time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 15      Loc [:FirsTime ]

02:  P1       Volt (SE)                Pyranometer

01: 1       Rep

02: 3       50 mV slow Range

03: 7       IN Chan

04: 1       Loc [:PSP kJ/m2]

05: .6120   Mult

06: 0       Offset

03:  P2       Volt (DIFF)              Pyrgeometer

01: 1       Rep

02: 1       5 mV slow Range

03: 1       IN Chan

04: 2       Loc [:PIR kJ/m2]

05: 1.2346  Mult

06: 0       Offset

04:  P2       Volt (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 3       IN Chan

04: 3       Loc [:ThPile mV]

05: 1       Mult

06: 0       Offset

05:  P4       Excite,Delay,Volt(SE)

01: 1       Rep

02: 4       500 mV slow Range

03: 3       IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 1700    mV Excitation

07: 5       Loc [:ThemisphC]

08: .01     Mult

09: 0       Offset

06:  P4       Excite,Delay,Volt(SE)

01: 1       Rep

02: 4       500 mV slow Range

03: 4       IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 1700    mV Excitation

07: 4       Loc [:Tcase C  ]

08: .01     Mult

09: 0       Offset

07:  P17      Panel Temperature

01: 8       Loc [:PanelTemp]

08:  P87      Beginning of Loop

01: 0       Delay

02: 2       Loop Count

09:  P89      If X<=>F

01: 4--     X Loc Tcase C

02: 4       <

03: .5      F

04: 30      Then Do

10:  P55      Polynomial

01: 1       Rep

02: 4--     X Loc Tcase C

03: 4--     F(X) Loc [:Tcase C  ]

04: -64.140 C0

05: 472.02  C1

06: -2304.8 C2

07: 7037.4  C3

08: -11140  C4

09: 7001.6  C5

11:  P94      Else

12:  P55      Polynomial

01: 1       Rep

02: 4--     X Loc Tcase C

03: 4--     F(X) Loc [:Tcase C  ]

04: -32.981 C0

05: 85.859  C1

06: -62.706 C2

07: 30.782  C3

08: -8.1108 C4

09: .87158  C5

13:  P95      End

14:  P95      End

15:  P92      If time is

01: 0       minutes into a

02: 15      minute interval

03: 10      Set high Flag 0 (output)

16:  P80      Set Active Storage Area

01: 1       Final Storage Area

02: 5       Array ID or location

17:  P77      Real Time

01: 1110    Year,Day,Hour-Minute

18:  P78      Resolution

01: 1       High Resolution

19:  P72      Totalize                Totalize PSP, PIR, ThPile

01: 3       Reps

02: 1       Loc PSP kJ/m2

20:  P78      Resolution

01: 0       Low Resolution

21:  P71      Average                  Average Tcase, Themisph

01: 2       Reps

02: 4       Loc Tcase C

22:  P82      Standard Deviation      Std Dev PSP, PIR, ThPile

01: 5       Reps                            Tcase, Themisph

02: 1       Sample Loc PSP kJ/m2

23:  P70      Sample

01: 2       Reps

02: 13      Loc ThC 1 Sec

24:  P96      Serial Output

01: 30      SM192/SM716/CSM1

25:  P        End Table 1

*     2       Table 2 Programs

01: 60      Sec. Execution Interval

01:  P92      If time is

01: 50      minutes into a

02: 60      minute interval

03: 30      Then Do

02:  P89      If X<=>F

01: 15      X Loc FirsTime

02: 4       <

03: 200     F

04: 30      Then Do

03:  P86      Do

01: 10      Set high Flag 0 (output)

04:  P30      Z=F

01: 0       F

02: 6       Z Loc [:0V Pw    ]

05:  P30      Z=F

01: 2000    F

02: 7       Z Loc [:2V Pw    ]

06:  P17      Panel Temperature

01: 8       Loc [:PanelTemp]

07:  P21      Analog Out

01: 2       CAO Chan

02: 7       mV Loc 2V Pw

08:  P22      Excitation with Delay

01: 4       EX Chan

02: 100     Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

09:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 8       Ref Temp Loc PanelTemp

06: 9       Loc [:ThC 1 Sec]

07: 1       Mult

08: 0       Offset

10:  P22      Excitation with Delay

01: 4       EX Chan

02: 2000    Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

11:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 8       Ref Temp Loc PanelTemp

06: 10      Loc [:ThC 21Sec]

07: 1       Mult

08: 0       Offset

12:  P21      Analog Out

01: 2       CAO Chan

02: 6       mV Loc 0V Pw

13:  P35      Z=X-Y                   End of Soil Moisture

01: 10      X Loc ThC 21Sec

02: 9       Y Loc ThC 1 Sec

03: 11      Z Loc [:Soil Diff]

14:  P37      Z=X*F

01: 11      X Loc Soil Diff

02: 4.89    F

03: 12      Z Loc [:Soil Mult]

15:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 13      Array ID or location

16:  P70      Sample

01: 2       Reps

02: 9       Loc ThC 1 Sec

17:  P95      End

18:  P95      End

19:  P        End Table 2

*     3       Table 3 Subroutines

01:  P        End Table 3

*     4       Mode 4 Output Options

01: 00      Tape/Printer Option

02: 00      Printer Baud Option

*     A       Mode 10 Memory Allocation

01: 33      Input Locations

02: 64      Intermediate Locations

*     C       Mode 12 Security (OSX-0)

01: 00      Security Option

02: 0000    Security Code

Key:

T=Table Number

E=Entry Number

L=Location Number

T:  E:  L:

1:  2:  1:  Loc [:PSP kJ/m2]

1:  3:  2:  Loc [:PIR kJ/m2]

1:  4:  3:  Loc [:ThPile mV]

1:  6:  4:  Loc [:Tcase C  ]

1: 10:  4:  F(X) Loc [:Tcase C  ]

1: 12:  4:  F(X) Loc [:Tcase C  ]

1:  5:  5:  Loc [:ThemisphC]

2:  4:  6:  Z Loc [:0V Pw    ]

2:  5:  7:  Z Loc [:2V Pw    ]

1:  7:  8:  Loc [:PanelTemp]

2:  6:  8:  Loc [:PanelTemp]

2:  9:  9:  Loc [:ThC 1 Sec]

2: 11: 10:  Loc [:ThC 21Sec]

2: 13: 11:  Z Loc [:Soil Diff]

2: 14: 12:  Z Loc [:Soil Mult]

1:  1: 15:  Loc [:FirsTime ]

Program: Boreas  Lynn Lake, MB  June 14/94

Flag Usage:

Input Channel Usage:

Excitation Channel Usage:

Continuous Analog Output Usage:

Control Port Usage:

Pulse Input Channel Usage:

Output Array Definitions:

*     1       Table 1 Programs

01: 5       Sec. Execution Interval

01:  P18      Time                 Beginning of Program Time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 43      Loc [:FirstTime]

02:  P18      Time                 Time used for counting minutes

01: 1       Minutes into current day (maximum 1440)

02: 60      Mod/by

03: 64      Loc [:Minutes  ]

03:  P10      Battery Voltage            Battery Voltage

01: 25      Loc [:Battery V]

04:  P2       Volt (DIFF)                PAR Sensor         KJ/m*m

01: 1       Rep

02: 2       15 mV slow Range

03: 1       IN Chan

04: 1       Loc [:Par KJ/m2]

05: .5      Mult

06: 0       Offset

05:  P2       Volt (DIFF)                Net Radiometer    KJ/m*m

01: 1       Rep

02: 4       500 mV slow Range

03: 2       IN Chan

04: 2       Loc [:Net KJ/m2]

05: .0660   Mult

06: 0       Offset

06:  P2       Volt (DIFF)                Albedometer Up    KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 3       IN Chan

04: 3       Loc [:AlU KJ/m2]

05: .60533  Mult

06: 0       Offset

07:  P2       Volt (DIFF)                Albedometer Down   KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 4       IN Chan

04: 4       Loc [:AlD KJ/m2]

05: .59312  Mult

06: 0       Offset

08:  P30      Z=F                 Beginning of IR Sensor  deg C

01: 0       F

02: 29      Z Loc [:OV  Pw   ]

09:  P30      Z=F

01: 5000    F

02: 30      Z Loc [:5V  Pw   ]

10:  P21      Analog Out Set CAO channel 1 to 5000 mV

01: 1       CAO Chan

02: 30      mV Loc 5V  Pw

11:  P4       Excite,Delay,Volt(SE) Measures Ed and Erel

01: 1       Rep

02: 5       5000 mV slow Range          Note that Channel 9 and 10

03: 10      IN Chan                     have been reversed here as

04: 2       Excite all reps w/EXchan 2  they were wired opposite

05: 100     Delay (units .01sec)

06: 1200    mV Excitation

07: 31      Loc [:Ed Volts ]

08: .001    Mult

09: 0       Offset

12:  P4       Excite,Delay,Volt(SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 9       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 100     Delay (units .01sec)

06: 5000--  mV Excitation

07: 32      Loc [:Erel Volt]

08: .001    Mult

09: 0       Offset

13:  P89      If X<=>F

01: 31      X Loc Ed Volts

02: 3       >=

03: .42315  F

04: 30      Then Do

14:  P55      Polynomial

01: 1       Rep

02: 31      X Loc Ed Volts

03: 33      F(X) Loc [:Td C     ]

04: 48.653  C0

05: -302.29 C1

06: 658.31  C2

07: -911.19 C3

08: 660.33  C4

09: -201.44 C5

15:  P94      Else

16:  P89      If X<=>F

01: 31      X Loc Ed Volts

02: 3       >=

03: .03125  F

04: 30      Then Do

17:  P37      Z=X*F

01: 31      X Loc Ed Volts

02: 10      F

03: 34      Z Loc [:Temporary]

18:  P55      Polynomial

01: 1       Rep

02: 34      X Loc Temporary

03: 33      F(X) Loc [:Td C     ]

04: 88.341  C0

05: -140.82 C1

06: 131.86  C2

07: -74.476 C3

08: 23.529  C4

09: -3.8390 C5

19:  P30      Z=F

01: 6       F

02: 35      Z Loc [:Six      ]

20:  P47      Z=X^Y

01: 34      X Loc Temporary

02: 35      Y Loc Six

03: 34      Z Loc [:Temporary]

21:  P37      Z=X*F

01: 34      X Loc Temporary

02: .25131  F

03: 34      Z Loc [:Temporary]

22:  P33      Z=X+Y

01: 34      X Loc Temporary

02: 33      Y Loc Td C

03: 33      Z Loc [:Td C     ]

23:  P94      Else

24:  P37      Z=X*F

01: 31      X Loc Ed Volts

02: 100     F

03: 34      Z Loc [:Temporary]

25:  P55      Polynomial

01: 1       Rep

02: 34      X Loc Temporary

03: 33      F(X) Loc [:Td C     ]

04: 164.35  C0

05: -134.14 C1

06: 80.230  C2

07: -23.831 C3

08: 2.6569  C4

09: 0       C5

26:  P95      End

27:  P95      End

28:  P37      Z=X*F

01: 32      X Loc Erel Volt

02: 1       F

03: 32      Z Loc [:Erel Volt]

29:  P37      Z=X*F

01: 33      X Loc Td C

02: -.00224 F

03: 36      Z Loc [:Erel Mult]

30:  P34      Z=X+F

01: 36      X Loc Erel Mult

02: 1.0589  F

03: 36      Z Loc [:Erel Mult]

31:  P36      Z=X*Y

01: 32      X Loc Erel Volt

02: 36      Y Loc Erel Mult

03: 37      Z Loc [:Ecrel V  ]

32:  P55      Polynomial

01: 1       Rep

02: 37      X Loc Ecrel V

03: 38      F(X) Loc [:Trel C   ]

04: .0836   C0

05: 122     C1

06: -65.5   C2

07: 126.4   C3

08: -223.2  C4

09: 140.3   C5

33:  P33      Z=X+Y                    End of IR Sensor

01: 33      X Loc Td C

02: 38      Y Loc Trel C

03: 12      Z Loc [:IRSensorC]

34:  P21      Analog Out

01: 1       CAO Chan

02: 29      mV Loc OV  Pw

35:  P4       Excite,Delay,Volt(SE)    Wind Direction  degrees true

01: 1       Rep

02: 5       5000 mV slow Range

03: 11      IN Chan

04: 3       Excite all reps w/EXchan 3

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 13      Loc [:WindDdegT]

08: .071    Mult

09: 0       Offset

36:  P3       Pulse                     Wind Speed    metres/sec

01: 1       Rep

02: 2       Pulse Input Chan

03: 21      Low level AC; Output Hz.

04: 14      Loc [:WindS m/s]

05: .0980   Mult

06: 0       Offset

37:  P3       Pulse                    Tipping Bucket     mm

01: 1       Rep

02: 1       Pulse Input Chan

03: 2       Switch closure

04: 18      Loc [:TipBuc mm]

05: .025    Mult

06: 0       Offset

38:  P89      If X<=>F      On the 50th minute skip the multiplexer

01: 64      X Loc Minutes and execute soil moisture in Table 2

02: 2       <>

03: 50      F

04: 30      Then Do

39:  P20      Set Port                  Start of Multiplexer

01: 1       Set high

02: 1       Port Number

40:  P20      Set Port

01: 1       Set high

02: 2       Port Number

41:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

42:  P20      Set Port

01: 0       Set low

02: 2       Port Number

43:  P8       Excite,Delay,Volt(DIFF)     Setra Pressure Sensor KPa

01: 1       Rep

02: 4       500 mV slow Range

03: 8       IN Chan

04: 1       Excite all reps w/EXchan 1

05: 1       Delay (units=.01sec)

06: 2500    mV Excitation

07: 11      Loc [:Press KPa]

08: .12     Mult

09: 80      Offset

44:  P20      Set Port

01: 1       Set high

02: 2       Port Number

45:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

46:  P20      Set Port

01: 0       Set low

02: 2       Port Number

47:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

48:  P20      Set Port

01: 1       Set high

02: 2       Port Number

49:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

50:  P20      Set Port

01: 0       Set low

02: 2       Port Number

51:  P11      Temp 107 Probe          Temperature at 10 cm    deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 7       Loc [:Soil 10cm]

05: 1       Mult

06: 0       Offset

52:  P20      Set Port

01: 1       Set high

02: 2       Port Number

53:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

54:  P20      Set Port

01: 0       Set low

02: 2       Port Number

55:  P11      Temp 107 Probe           Temperature at 20 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 8       Loc [:Soil 20cm]

05: 1       Mult

06: 0       Offset

56:  P20      Set Port

01: 1       Set high

02: 2       Port Number

57:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

58:  P20      Set Port

01: 0       Set low

02: 2       Port Number

59:  P11      Temp 107 Probe          Temperature at 50 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 9       Loc [:Soil 50cm]

05: 1       Mult

06: 0       Offset

60:  P20      Set Port

01: 1       Set high

02: 2       Port Number

61:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

62:  P20      Set Port

01: 0       Set low

02: 2       Port Number

63:  P4       Excite,Delay,Volt(SE)   107F Temperature LC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 26      Loc [:LC Store ]

08: .001    Mult

09: 0       Offset

64:  P55      Polynomial

01: 1       Rep

02: 26      X Loc LC Store

03: 6       F(X) Loc [:Temp LC C]

04: -74.159 C0              Coefficients for 35 foot cable -

05: 645.87  C1              lower canopy

06: -3844.6 C2

07: 16081   C3

08: -34152  C4

09: 29933   C5

65:  P34      Z=X+F

01: 6       X Loc Temp LC C

02: 273.15  F

03: 28      Z Loc [:Temp LC K]

66:  P20      Set Port

01: 1       Set high

02: 2       Port Number

67:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

68:  P20      Set Port

01: 0       Set low

02: 2       Port Number

69:  P4       Excite,Delay,Volt(SE)  HMP35CF Temperature UC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 27      Loc [:UC Store ]

08: .001    Mult

09: 0       Offset

70:  P55      Polynomial

01: 1       Rep

02: 27      X Loc UC Store

03: 5       F(X) Loc [:Temp UC C]

04: -74.181 C0              Coefficients for 75 foot cable -

05: 646.76  C1               upper canopy

06: -3855.7 C2

07: 16149   C3

08: -34341  C4

09: 30134   C5

71:  P20      Set Port

01: 1       Set high

02: 2       Port Number

72:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

73:  P20      Set Port

01: 0       Set low

02: 2       Port Number

74:  P4       Excite,Delay,Volt(SE)   HMP35CF Relative Humidity %RH

01: 1       Rep

02: 5       5000 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 15      Delay (units .01sec)

06: 5000    mV Excitation

07: 10      Loc [:Humid %RH]

08: .1      Mult

09: 0       Offset

75:  P20      Set Port

01: 0       Set low

02: 1       Port Number

76:  P30      Z=F               Beginning of Dewpoint Calculations

01: 9.5     F

02: 48      Z Loc [:a        ]

77:  P30      Z=F

01: 265.5   F

02: 49      Z Loc [:b        ]

78:  P37      Z=X*F

01: 5       X Loc Temp UC C

02: 9.5     F

03: 50      Z Loc [:a*T      ]

79:  P34      Z=X+F

01: 5       X Loc Temp UC C

02: 265.5   F

03: 51      Z Loc [:b+T      ]

80:  P38      Z=X/Y

01: 50      X Loc a*T

02: 51      Y Loc b+T

03: 52      Z Loc [:aT/b+T   ]

81:  P34      Z=X+F

01: 52      X Loc aT/b+T

02: -2      F

03: 53      Z Loc [:aT/b+T-2 ]

82:  P40      Z=LN(X)

01: 10      X Loc Humid %RH

02: 54      Z Loc [:ln(RH)   ]

83:  P30      Z=F

01: 2.303   F

02: 55      Z Loc [:ln/log   ]

84:  P38      Z=X/Y

01: 54      X Loc ln(RH)

02: 55      Y Loc ln/log

03: 56      Z Loc [:log (RH) ]

85:  P33      Z=X+Y

01: 56      X Loc log (RH)

02: 53      Y Loc aT/b+T-2

03: 57      Z Loc [:log +aT/b]

86:  P38      Z=X/Y

01: 48      X Loc a

02: 57      Y Loc log +aT/b

03: 58      Z Loc [:a/logRH  ]

87:  P38      Z=X/Y

01: 49      X Loc b

02: 58      Y Loc a/logRH

03: 22      Z Loc [:Dewpoint ]       End of Dewpoint Calculations

88:  P95      End

89:  P92      If time is

01: 0       minutes into a

02: 1       minute interval

03: 30      Then Do

90:  P89      If X<=>F

01: 64      X Loc Minutes

02: 3       >=

03: 55      F

04: 30      Then Do

91:  P4       Excite,Delay,Volt(SE)     Belfort Weighing Gauge

01: 1       Rep

02: 5       5000 mV slow Range

03: 12      IN Chan

04: 4       Excite all reps w/EXchan 4

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 19      Loc [:Belfortmm]

08: .07181  Mult

09: 0       Offset

92:  P20      Set Port                   Begin Snow Depth Sensor

01: 1       Set high

02: 6       Port Number

93:  P20      Set Port

01: 0       Set low

02: 4       Port Number

94:  P20      Set Port

01: 1       Set high

02: 5       Port Number

95:  P20      Set Port

01: 0       Set low

02: 5       Port Number

96:  P20      Set Port

01: 1       Set high

02: 4       Port Number

97:  P20      Set Port

01: 1       Set high

02: 5       Port Number

98:  P20      Set Port

01: 0       Set low

02: 5       Port Number

99:  P20      Set Port

01: 0       Set low

02: 4       Port Number

100: P87      Beginning of Loop

01: 0       Delay

02: 6       Loop Count

101: P20      Set Port

01: 1       Set high

02: 5       Port Number

102: P20      Set Port

01: 0       Set low

02: 5       Port Number

103: P95      End

104: P20      Set Port

01: 1       Set high

02: 5       Port Number

105: P22      Excitation with Delay

01: 1       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

106: P20      Set Port

01: 0       Set low

02: 6       Port Number

107: P20      Set Port

01: 1       Set high

02: 6       Port Number

108: P22      Excitation with Delay

01: 1       EX Chan

02: 8       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

109: P20      Set Port

01: 0       Set low

02: 5       Port Number

110: P30      Z=F

01: 1       F

02: 39      Z Loc [:Snow Calc]

111: P30      Z=F

01: 0       F

02: 42      Z Loc [:Snow # Pu]

112: P87      Beginning of Loop

01: 0       Delay

02: 16      Loop Count

113: P20      Set Port

01: 1       Set high

02: 5       Port Number

114: P20      Set Port

01: 0       Set low

02: 5       Port Number

115: P1       Volt (SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 13      IN Chan

04: 40      Loc [:Snow Data]

05: 1       Mult

06: 0       Offset

116: P89      If X<=>F

01: 40      X Loc Snow Data

02: 3       >=

03: 3000    F

04: 30      Then Do

117: P33      Z=X+Y

01: 39      X Loc Snow Calc

02: 42      Y Loc Snow # Pu

03: 42      Z Loc [:Snow # Pu]

118: P95      End

119: P37      Z=X*F

01: 39      X Loc Snow Calc

02: 2       F

03: 39      Z Loc [:Snow Calc]

120: P95      End

121: P30      Z=F

01: 291     F

02: 41      Z Loc [:T2 291 K ]

122: P38      Z=X/Y

01: 28      X Loc Temp LC K

02: 41      Y Loc T2 291 K

03: 20      Z Loc [:Snow D mm]

123: P39      Z=SQRT(X)

01: 20      X Loc Snow D mm

02: 20      Z Loc [:Snow D mm]

124: P36      Z=X*Y

01: 42      X Loc Snow # Pu

02: 20      Y Loc Snow D mm

03: 20      Z Loc [:Snow D mm]

125: P37      Z=X*F

01: 20      X Loc Snow D mm

02: .52176  F

03: 20      Z Loc [:Snow D mm]

126: P34      Z=X+F

01: 20      X Loc Snow D mm

02: -39     F

03: 20      Z Loc [:Snow D mm]

127: P20      Set Port

01: 0       Set low

02: 4       Port Number

128: P20      Set Port

01: 0       Set low

02: 5       Port Number

129: P20      Set Port                 End of Snow Depth

01: 0       Set low

02: 6       Port Number

130: P89      If X<=>F           Five Minute Average at the top of

01: 64      X Loc Minutes    the hour for Belfort and Snow Depth

02: 1       =

03: 59      F

04: 10      Set high Flag 0 (output)

131: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 15      Array ID or location

132: P71      Average

01: 2       Reps

02: 19      Loc Belfortmm

133: P95      End

134: P95      End

135: P92      If time is

01: 0       minutes into a

02: 60      minute interval

03: 30      Then Do

136: P35      Z=X-Y

01: 15      X Loc Av Belfor

02: 59      Y Loc Prev Belf

03: 60      Z Loc [:Belf Diff]

137: P31      Z=X

01: 15      X Loc Av Belfor

02: 59      Z Loc [:Prev Belf]

138: P95      End

139: P89      If X<=>F           Two minute average of Wind Speed

01: 64      X Loc Minutes      and Direction at top of the hour

02: 3       >=

03: 58      F

04: 10      Set high Flag 0 (output)

140: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 23      Array ID or location

141: P69      Wind Vector

01: 1       Rep

02: 0       Samples per sub-interval

03: 1       Polar Sensor/(S, D1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

142: P92      If time is

01: 59      minutes into a

02: 60      minute interval

03: 10      Set high Flag 0 (output)

143: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 61      Array ID or location

144: P71      Average            One minute average of Pressure

01: 1       Rep                at top of the hour

02: 11      Loc Press KPa

145: P71      Average            One minute average of Temperature

01: 1       Rep                at top of the hour

02: 5       Loc Temp UC C

146: P71      Average            One minute average of Dewpoint

01: 1       Rep                at top of the hour

02: 22      Loc Dewpoint

147: P92      If time is            Begin writing to the array -

01: 0       minutes into a        15 minute interval

02: 15      minute interval

03: 10      Set high Flag 0 (output)

148: P80      Set Active Storage Area

01: 1       Final Storage Area

02: 6       Array ID or location

149: P70      Sample                     Sample Battery

01: 1       Rep

02: 25      Loc Battery V

150: P77      Real Time                  Year, Day, Time

01: 1110    Year,Day,Hour-Minute

151: P78      Resolution

01: 1       High Resolution

152: P72      Totalize           Totalize Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Loc Par KJ/m2

153: P78      Resolution

01: 0       Low Resolution

154: P82      Standard Deviation Std Dev Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Sample Loc Par KJ/m2

155: P71      Average           Average TempUC, TempLC, Temp10

01: 6       Reps              Temp20, Temp50, RelHum

02: 5       Loc Temp UC C

156: P78      Resolution

01: 1       High Resolution

157: P71      Average           Average Pressure

01: 1       Rep

02: 11      Loc Press KPa

158: P78      Resolution

01: 0       Low Resolution

159: P71      Average           Average IRSensor

01: 1       Rep

02: 12      Loc IRSensorC

160: P82      Standard Deviation Std Dev Temp UC, TempLC, Temp10

01: 8       Reps               Temp20, Temp50, RelHum, Pressure

02: 5       Sample Loc Temp UC C IRSensor

161: P69      Wind Vector      Average Wind Speed, Wind Direction

01: 1       Rep                   and Std Dev Wind Direction

02: 0       Samples per sub-interval

03: 0       Polar Sensor/(S, D1, SD1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

162: P82      Standard Deviation      Std Dev Wind Speed

01: 1       Rep

02: 14      Sample Loc WindS m/s

163: P70      Sample                Sample Belfort, Snow Depth

01: 2       Reps                  Average of last 5 minutes

02: 15      Loc Av Belfor         of the hour

164: P72      Totalize                Totalize Tip Bucket

01: 1       Rep

02: 18      Loc TipBuc mm

165: P33      Z=X+Y

01: 18      X Loc TipBuc mm

02: 65      Y Loc Total Tip

03: 65      Z Loc [:Total Tip]

166: P70      Sample                     Sample Soil Moisture

01: 1       Rep                       Average of minute 50

02: 17      Loc Av Soil M             of the hour

167: P78      Resolution

01: 1       High Resolution

168: P70      Sample               Sample Pressure for GTS

01: 1       Rep

02: 61      Loc Press 1hr

169: P78      Resolution

01: 0       Low Resolution

170: P70      Sample    Sample TempUC, Dewpoint for GTS

01: 2       Reps

02: 62      Loc Temp  1hr

171: P70      Sample           Sample Wind Dir for GTS

01: 1       Rep

02: 24      Loc WindD 1hr

172: P70      Sample         Sample Wind Speed for GTS

01: 1       Rep

02: 23      Loc WindS 1hr

173: P70      Sample          Sample Belfort difference from

01: 1       Rep             previous hour

02: 60      Loc Belf Diff

174: P70      Sample

01: 1       Rep

02: 65      Loc Total Tip

175: P70      Sample

01: 2       Reps

02: 73      Loc ThC 1sec

176: P96      Serial Output

01: 30      SM192/SM716/CSM1

177: P18      Time                Store end of Program time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 45      Loc [:LastTime ]

178: P35      Z=X-Y                Program Execution Time

01: 45      X Loc LastTime

02: 43      Y Loc FirstTime

03: 44      Z Loc [:Prog Time]

179: P        End Table 1

*     2       Table 2 Programs

01: 60      Sec. Execution Interval

01:  P92      If time is

01: 50      minutes into a

02: 60      minute interval

03: 30      Then Do

02:  P89      If X<=>F

01: 43      X Loc FirstTime

02: 4       <

03: 200     F

04: 30      Then Do

03:  P86      Do

01: 10      Set high Flag 0 (output)

04:  P30      Z=F

01: 0       F

02: 29      Z Loc [:OV  Pw   ]

05:  P30      Z=F

01: 2000    F

02: 66      Z Loc [:2V  Pw   ]

06:  P17      Panel Temperature

01: 67      Loc [:PanelTemp]

07:  P20      Set Port

01: 1       Set high

02: 1       Port Number

08:  P87      Beginning of Loop

01: 0       Delay

02: 2       Loop Count

09:  P20      Set Port

01: 1       Set high

02: 2       Port Number

10:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

11:  P20      Set Port

01: 0       Set low

02: 2       Port Number

12:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0.0000  mV Excitation

13:  P95      End

14:  P21      Analog Out

01: 2       CAO Chan

02: 66      mV Loc 2V  Pw

15:  P22      Excitation with Delay

01: 4       EX Chan

02: 100     Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

16:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 46      Loc [:ThC 1 sec]

07: 1       Mult

08: 0       Offset

17:  P22      Excitation with Delay

01: 4       EX Chan

02: 2000    Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

18:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 47      Loc [:ThC 21sec]

07: 1       Mult

08: 0       Offset

19:  P21      Analog Out

01: 2       CAO Chan

02: 29      mV Loc OV  Pw

20:  P20      Set Port

01: 0       Set low

02: 1       Port Number

21:  P35      Z=X-Y                   End of Soil Moisture

01: 47      X Loc ThC 21sec

02: 46      Y Loc ThC 1 sec

03: 68      Z Loc [:Soil Diff]

22:  P37      Z=X*F

01: 68      X Loc Soil Diff

02: 4.89    F

03: 69      Z Loc [:Soil Mult]

23:  P30      Z=F

01: 10      F

02: 70      Z Loc [:Soil Ten ]

24:  P47      Z=X^Y

01: 70      X Loc Soil Ten

02: 69      Y Loc Soil Mult

03: 71      Z Loc [:Soil Sub ]

25:  P37      Z=X*F

01: 71      X Loc Soil Sub

02: .00026  F

03: 72      Z Loc [:Soil Res ]

26:  P37      Z=X*F

01: 72      X Loc Soil Res

02: .1      F

03: 21      Z Loc [:Soil MPa ]

27:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 17      Array ID or location

28:  P70      Sample

01: 1       Rep

02: 21      Loc Soil MPa

29:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 73      Array ID or location

30:  P70      Sample

01: 2       Reps

02: 46      Loc ThC 1 sec

31:  P95      End

32:  P95      End

33:  P        End Table 2

*     3       Table 3 Subroutines

01:  P        End Table 3

*     4       Mode 4 Output Options

01: 0       (Tape OFF) (Printer OFF)

02: 0       Printer 300 Baud

*     A       Mode 10 Memory Allocation

01: 76      Input Locations

02: 130     Intermediate Locations

*     C       Mode 12 Security (OSX-0)

01: 00      Security Option

02: 0000    Security Code

Input Location Assignments (with comments):

Key:

T=Table Number

E=Entry Number

L=Location Number

T:  E:  L:

1:  4:  1:  Loc [:Par KJ/m2]

1:  5:  2:  Loc [:Net KJ/m2]

1:  6:  3:  Loc [:AlU KJ/m2]

1:  7:  4:  Loc [:AlD KJ/m2]

1: 70:  5:  F(X) Loc [:Temp UC C]

1: 64:  6:  F(X) Loc [:Temp LC C]

1: 51:  7:  Loc [:Soil 10cm]

1: 55:  8:  Loc [:Soil 20cm]

1: 59:  9:  Loc [:Soil 50cm]

1: 74: 10:  Loc [:Humid %RH]

1: 43: 11:  Loc [:Press KPa]

1: 33: 12:  Z Loc [:IRSensorC]

1: 35: 13:  Loc [:WindDdegT]

1: 36: 14:  Loc [:WindS m/s]

1: 37: 18:  Loc [:TipBuc mm]

1: 91: 19:  Loc [:Belfortmm]

1:122: 20:  Z Loc [:Snow D mm]

1:123: 20:  Z Loc [:Snow D mm]

1:124: 20:  Z Loc [:Snow D mm]

1:125: 20:  Z Loc [:Snow D mm]

1:126: 20:  Z Loc [:Snow D mm]

2: 26: 21:  Z Loc [:Soil MPa ]

1: 87: 22:  Z Loc [:Dewpoint ]       End of Dewpoint Calculations

1:  3: 25:  Loc [:Battery V]

1: 63: 26:  Loc [:LC Store ]

1: 69: 27:  Loc [:UC Store ]

1: 65: 28:  Z Loc [:Temp LC K]

1:  8: 29:  Z Loc [:OV  Pw   ]

2:  4: 29:  Z Loc [:OV  Pw   ]

1:  9: 30:  Z Loc [:5V  Pw   ]

1: 11: 31:  Loc [:Ed Volts ]

1: 12: 32:  Loc [:Erel Volt]

1: 28: 32:  Z Loc [:Erel Volt]

1: 14: 33:  F(X) Loc [:Td C     ]

1: 18: 33:  F(X) Loc [:Td C     ]

1: 22: 33:  Z Loc [:Td C     ]

1: 25: 33:  F(X) Loc [:Td C     ]

1: 17: 34:  Z Loc [:Temporary]

1: 20: 34:  Z Loc [:Temporary]

1: 21: 34:  Z Loc [:Temporary]

1: 24: 34:  Z Loc [:Temporary]

1: 19: 35:  Z Loc [:Six      ]

1: 29: 36:  Z Loc [:Erel Mult]

1: 30: 36:  Z Loc [:Erel Mult]

1: 31: 37:  Z Loc [:Ecrel V  ]

1: 32: 38:  F(X) Loc [:Trel C   ]

1:110: 39:  Z Loc [:Snow Calc]

1:119: 39:  Z Loc [:Snow Calc]

1:115: 40:  Loc [:Snow Data]

1:121: 41:  Z Loc [:T2 291 K ]

1:111: 42:  Z Loc [:Snow # Pu]

1:117: 42:  Z Loc [:Snow # Pu]

1:  1: 43:  Loc [:FirstTime]

1:178: 44:  Z Loc [:Prog Time]

1:177: 45:  Loc [:LastTime ]

2: 16: 46:  Loc [:ThC 1 sec]

2: 18: 47:  Loc [:ThC 21sec]

1: 76: 48:  Z Loc [:a        ]

1: 77: 49:  Z Loc [:b        ]

1: 78: 50:  Z Loc [:a*T      ]

1: 79: 51:  Z Loc [:b+T      ]

1: 80: 52:  Z Loc [:aT/b+T   ]

1: 81: 53:  Z Loc [:aT/b+T-2 ]

1: 82: 54:  Z Loc [:ln(RH)   ]

1: 83: 55:  Z Loc [:ln/log   ]

1: 84: 56:  Z Loc [:log (RH) ]

1: 85: 57:  Z Loc [:log +aT/b]

1: 86: 58:  Z Loc [:a/logRH  ]

1:137: 59:  Z Loc [:Prev Belf]

1:136: 60:  Z Loc [:Belf Diff]

1:  2: 64:  Loc [:Minutes  ]

1:165: 65:  Z Loc [:Total Tip]

2:  5: 66:  Z Loc [:2V  Pw   ]

2:  6: 67:  Loc [:PanelTemp]

2: 21: 68:  Z Loc [:Soil Diff]

2: 22: 69:  Z Loc [:Soil Mult]

2: 23: 70:  Z Loc [:Soil Ten ]

2: 24: 71:  Z Loc [:Soil Sub ]

2: 25: 72:  Z Loc [:Soil Res ]

Page 24    Input Location Labels:

1:Par KJ/m2    20:Snow D mm    39:Snow Calc    58:a/logRH

2:Net KJ/m2    21:Soil MPa     40:Snow Data    59:Prev Belf

3:AlU KJ/m2    22:Dewpoint     41:T2 291 K     60:Belf Diff

4:AlD KJ/m2    23:WindS 1hr    42:Snow # Pu    61:Press 1hr

5:Temp UC C    24:WindD 1hr    43:FirstTime    62:Temp  1hr

6:Temp LC C    25:Battery V    44:Prog Time    63:Dewpt 1hr

7:Soil 10cm    26:LC Store     45:LastTime     64:Minutes

8:Soil 20cm    27:UC Store     46:ThC 1 sec    65:Total Tip

9:Soil 50cm    28:Temp LC K    47:ThC 21sec    66:2V  Pw

10:Humid %RH    29:OV  Pw       48:a            67:PanelTemp

11:Press KPa    30:5V  Pw       49:b            68:Soil Diff

12:IRSensorC    31:Ed Volts     50:a*T          69:Soil Mult

13:WindDdegT    32:Erel Volt    51:b+T          70:Soil Ten

14:WindS m/s    33:Td C         52:aT/b+T       71:Soil Sub

15:Av Belfor    34:Temporary    53:aT/b+T-2     72:Soil Res

16:Av Snow D    35:Six          54:ln(RH)       73:ThC 1sec

17:Av Soil M    36:Erel Mult    55:ln/log       74:ThC 21sec

18:TipBuc mm    37:Ecrel V      56:log (RH)     75:_________

19:Belfortmm    38:Trel C       57:log +aT/b    76:_________

Program: Boreas  The Pas, MB  Jul 10/95

Flag Usage:

Input Channel Usage:

Excitation Channel Usage:

Continuous Analog Output Usage:

Control Port Usage:

Pulse Input Channel Usage:

Output Array Definitions:

*     1       Table 1 Programs

01: 5       Sec. Execution Interval

01:  P18      Time                 Beginning of Program Time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 43      Loc [:FirstTime]

02:  P18      Time                 Time used for Soil Moisture

01: 1       Minutes into current day (maximum 1440)

02: 60      Mod/by

03: 64      Loc [:Minutes  ]

03:  P10      Battery Voltage            Battery Voltage

01: 25      Loc [:Battery V]

04:  P2       Volt (DIFF)                PAR Sensor         KJ/m*m

01: 1       Rep

02: 2       15 mV slow Range

03: 1       IN Chan

04: 1       Loc [:Par KJ/m2]

05: .5      Mult

06: 0       Offset

05:  P2       Volt (DIFF)                Net Radiometer    KJ/m*m

01: 1       Rep

02: 4       500 mV slow Range

03: 2       IN Chan

04: 2       Loc [:Net KJ/m2]

05: .065    Mult

06: 0       Offset

06:  P2       Volt (DIFF)                Albedometer Up    KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 3       IN Chan

04: 3       Loc [:AlU KJ/m2]

05: .58824  Mult

06: 0       Offset

07:  P2       Volt (DIFF)                Albedometer Down   KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 4       IN Chan

04: 4       Loc [:AlD KJ/m2]

05: .62035  Mult

06: 0       Offset

08:  P30      Z=F                 Beginning of IR Sensor  deg C

01: 0       F

02: 29      Z Loc [:OV  Pw   ]

09:  P30      Z=F

01: 5000    F

02: 30      Z Loc [:5V  Pw   ]

10:  P21      Analog Out Set CAO channel 1 to 5000 mV

01: 1       CAO Chan

02: 30      mV Loc 5V  Pw

11:  P4       Excite,Delay,Volt(SE) Measures Ed and Erel

01: 1       Rep

02: 5       5000 mV slow Range

03: 9       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 100     Delay (units .01sec)

06: 1200    mV Excitation

07: 31      Loc [:Ed Volts ]

08: .001    Mult

09: 0       Offset

12:  P4       Excite,Delay,Volt(SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 10      IN Chan

04: 2       Excite all reps w/EXchan 2

05: 100     Delay (units .01sec)

06: 5000--  mV Excitation

07: 32      Loc [:Erel Volt]

08: .001    Mult

09: 0       Offset

13:  P89      If X<=>F

01: 31      X Loc Ed Volts

02: 3       >=

03: .42315  F

04: 30      Then Do

14:  P55      Polynomial

01: 1       Rep

02: 31      X Loc Ed Volts

03: 33      F(X) Loc [:Td C     ]

04: 48.653  C0

05: -302.29 C1

06: 658.31  C2

07: -911.19 C3

08: 660.33  C4

09: -201.44 C5

15:  P94      Else

16:  P89      If X<=>F

01: 31      X Loc Ed Volts

02: 3       >=

03: .03125  F

04: 30      Then Do

17:  P37      Z=X*F

01: 31      X Loc Ed Volts

02: 10      F

03: 34      Z Loc [:Temporary]

18:  P55      Polynomial

01: 1       Rep

02: 34      X Loc Temporary

03: 33      F(X) Loc [:Td C     ]

04: 88.341  C0

05: -140.82 C1

06: 131.86  C2

07: -74.476 C3

08: 23.529  C4

09: -3.8390 C5

19:  P30      Z=F

01: 6       F

02: 35      Z Loc [:Six      ]

20:  P47      Z=X^Y

01: 34      X Loc Temporary

02: 35      Y Loc Six

03: 34      Z Loc [:Temporary]

21:  P37      Z=X*F

01: 34      X Loc Temporary

02: .25131  F

03: 34      Z Loc [:Temporary]

22:  P33      Z=X+Y

01: 34      X Loc Temporary

02: 33      Y Loc Td C

03: 33      Z Loc [:Td C     ]

23:  P94      Else

24:  P37      Z=X*F

01: 31      X Loc Ed Volts

02: 100     F

03: 34      Z Loc [:Temporary]

25:  P55      Polynomial

01: 1       Rep

02: 34      X Loc Temporary

03: 33      F(X) Loc [:Td C     ]

04: 164.35  C0

05: -134.14 C1

06: 80.230  C2

07: -23.831 C3

08: 2.6569  C4

09: 0       C5

26:  P95      End

27:  P95      End

28:  P37      Z=X*F

01: 32      X Loc Erel Volt

02: 1       F

03: 32      Z Loc [:Erel Volt]

29:  P37      Z=X*F

01: 33      X Loc Td C

02: -.00224 F

03: 36      Z Loc [:Erel Mult]

30:  P34      Z=X+F

01: 36      X Loc Erel Mult

02: 1.0589  F

03: 36      Z Loc [:Erel Mult]

31:  P36      Z=X*Y

01: 32      X Loc Erel Volt

02: 36      Y Loc Erel Mult

03: 37      Z Loc [:Ecrel V  ]

32:  P55      Polynomial

01: 1       Rep

02: 37      X Loc Ecrel V

03: 38      F(X) Loc [:Trel C   ]

04: .0836   C0

05: 122     C1

06: -65.5   C2

07: 126.4   C3

08: -223.2  C4

09: 140.3   C5

33:  P33      Z=X+Y                    End of IR Sensor

01: 33      X Loc Td C

02: 38      Y Loc Trel C

03: 12      Z Loc [:IRSensorC]

34:  P21      Analog Out

01: 1       CAO Chan

02: 29      mV Loc OV  Pw

35:  P4       Excite,Delay,Volt(SE)    Wind Direction  degrees true

01: 1       Rep

02: 5       5000 mV slow Range

03: 11      IN Chan

04: 3       Excite all reps w/EXchan 3

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 13      Loc [:WindDdegT]

08: .071    Mult

09: 0       Offset

36:  P3       Pulse                     Wind Speed    metres/sec

01: 1       Rep

02: 2       Pulse Input Chan

03: 21      Low level AC; Output Hz.

04: 14      Loc [:WindS m/s]

05: .0980   Mult

06: 0       Offset

37:  P3       Pulse                    Tipping Bucket     mm

01: 1       Rep

02: 1       Pulse Input Chan

03: 2       Switch closure

04: 18      Loc [:TipBuc mm]

05: .05     Mult

06: 0       Offset

38:  P89      If X<=>F      On the 50th minute skip the multiplexer

01: 64      X Loc Minutes  and execute soil moisture in Table 2

02: 2       <>

03: 50      F

04: 30      Then Do

39:  P20      Set Port                  Start of Multiplexer

01: 1       Set high

02: 1       Port Number

40:  P20      Set Port

01: 1       Set high

02: 2       Port Number

41:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

42:  P20      Set Port

01: 0       Set low

02: 2       Port Number

43:  P8       Excite,Delay,Volt(DIFF)     Setra Pressure Sensor KPa

01: 1       Rep

02: 4       500 mV slow Range

03: 8       IN Chan

04: 1       Excite all reps w/EXchan 1

05: 1       Delay (units=.01sec)

06: 2500    mV Excitation

07: 11      Loc [:Press KPa]

08: .12     Mult

09: 80      Offset

44:  P20      Set Port

01: 1       Set high

02: 2       Port Number

45:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

46:  P20      Set Port

01: 0       Set low

02: 2       Port Number

47:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

48:  P20      Set Port

01: 1       Set high

02: 2       Port Number

49:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

50:  P20      Set Port

01: 0       Set low

02: 2       Port Number

51:  P11      Temp 107 Probe          Temperature at 10 cm    deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 7       Loc [:Soil 10cm]

05: 1       Mult

06: 0       Offset

52:  P20      Set Port

01: 1       Set high

02: 2       Port Number

53:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

54:  P20      Set Port

01: 0       Set low

02: 2       Port Number

55:  P11      Temp 107 Probe           Temperature at 20 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 8       Loc [:Soil 20cm]

05: 1       Mult

06: 0       Offset

56:  P20      Set Port

01: 1       Set high

02: 2       Port Number

57:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

58:  P20      Set Port

01: 0       Set low

02: 2       Port Number

59:  P11      Temp 107 Probe          Temperature at 50 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 9       Loc [:Soil 50cm]

05: 1       Mult

06: 0       Offset

60:  P20      Set Port

01: 1       Set high

02: 2       Port Number

61:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

62:  P20      Set Port

01: 0       Set low

02: 2       Port Number

63:  P4       Excite,Delay,Volt(SE)   107F Temperature LC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 26      Loc [:LC Store ]

08: .001    Mult

09: 0       Offset

64:  P55      Polynomial

01: 1       Rep

02: 26      X Loc LC Store

03: 6       F(X) Loc [:Temp LC C]

04: -74.159 C0              Coefficients for 35 foot cable -

05: 645.87  C1              lower canopy

06: -3844.6 C2

07: 16081   C3

08: -34152  C4

09: 29933   C5

65:  P34      Z=X+F

01: 6       X Loc Temp LC C

02: 273.15  F

03: 28      Z Loc [:Temp LC K]

66:  P20      Set Port

01: 1       Set high

02: 2       Port Number

67:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

68:  P20      Set Port

01: 0       Set low

02: 2       Port Number

69:  P4       Excite,Delay,Volt(SE)  HMP35CF Temperature UC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 27      Loc [:UC Store ]

08: .001    Mult

09: 0       Offset

70:  P55      Polynomial

01: 1       Rep

02: 27      X Loc UC Store

03: 5       F(X) Loc [:Temp UC C]

04: -74.168 C0              Coefficients for 50 foot cable -

05: 646.22  C1               upper canopy

06: -3848.9 C2

07: 16107   C3

08: -34225  C4

09: 30009   C5

71:  P20      Set Port

01: 1       Set high

02: 2       Port Number

72:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

73:  P20      Set Port

01: 0       Set low

02: 2       Port Number

74:  P4       Excite,Delay,Volt(SE)   HMP35CF Relative Humidity %RH

01: 1       Rep

02: 5       5000 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 15      Delay (units .01sec)

06: 5000    mV Excitation

07: 10      Loc [:Humid %RH]

08: .1      Mult

09: 0       Offset

75:  P20      Set Port

01: 0       Set low

02: 1       Port Number

76:  P30      Z=F               Beginning of Dewpoint Calculations

01: 9.5     F

02: 48      Z Loc [:a        ]

77:  P30      Z=F

01: 265.5   F

02: 49      Z Loc [:b        ]

78:  P37      Z=X*F

01: 5       X Loc Temp UC C

02: 9.5     F

03: 50      Z Loc [:a*T      ]

79:  P34      Z=X+F

01: 5       X Loc Temp UC C

02: 265.5   F

03: 51      Z Loc [:b+T      ]

80:  P38      Z=X/Y

01: 50      X Loc a*T

02: 51      Y Loc b+T

03: 52      Z Loc [:aT/b+T   ]

81:  P34      Z=X+F

01: 52      X Loc aT/b+T

02: -2      F

03: 53      Z Loc [:aT/b+T-2 ]

82:  P40      Z=LN(X)

01: 10      X Loc Humid %RH

02: 54      Z Loc [:ln(RH)   ]

83:  P30      Z=F

01: 2.303   F

02: 55      Z Loc [:ln/log   ]

84:  P38      Z=X/Y

01: 54      X Loc ln(RH)

02: 55      Y Loc ln/log

03: 56      Z Loc [:log (RH) ]

85:  P33      Z=X+Y

01: 56      X Loc log (RH)

02: 53      Y Loc aT/b+T-2

03: 57      Z Loc [:log +aT/b]

86:  P38      Z=X/Y

01: 48      X Loc a

02: 57      Y Loc log +aT/b

03: 58      Z Loc [:a/logRH  ]

87:  P38      Z=X/Y

01: 49      X Loc b

02: 58      Y Loc a/logRH

03: 22      Z Loc [:Dewpoint ]       End of Dewpoint Calculations

88:  P95      End

89:  P92      If time is

01: 0       minutes into a

02: 1       minute interval

03: 30      Then Do

90:  P89      If X<=>F

01: 64      X Loc Minutes

02: 3       >=

03: 55      F

04: 30      Then Do

91:  P4       Excite,Delay,Volt(SE)     Belfort Weighing Gauge

01: 1       Rep

02: 5       5000 mV slow Range

03: 12      IN Chan

04: 4       Excite all reps w/EXchan 4

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 19      Loc [:Belfortmm]

08: .07155  Mult

09: 0       Offset

92:  P20      Set Port                   Begin Snow Depth Sensor

01: 1       Set high

02: 6       Port Number

93:  P20      Set Port

01: 0       Set low

02: 4       Port Number

94:  P20      Set Port

01: 1       Set high

02: 5       Port Number

95:  P20      Set Port

01: 0       Set low

02: 5       Port Number

96:  P20      Set Port

01: 1       Set high

02: 4       Port Number

97:  P20      Set Port

01: 1       Set high

02: 5       Port Number

98:  P20      Set Port

01: 0       Set low

02: 5       Port Number

99:  P20      Set Port

01: 0       Set low

02: 4       Port Number

100: P87      Beginning of Loop

01: 0       Delay

02: 6       Loop Count

101: P20      Set Port

01: 1       Set high

02: 5       Port Number

102: P20      Set Port

01: 0       Set low

02: 5       Port Number

103: P95      End

104: P20      Set Port

01: 1       Set high

02: 5       Port Number

105: P22      Excitation with Delay

01: 1       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

106: P20      Set Port

01: 0       Set low

02: 6       Port Number

107: P20      Set Port

01: 1       Set high

02: 6       Port Number

108: P22      Excitation with Delay

01: 1       EX Chan

02: 8       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

109: P20      Set Port

01: 0       Set low

02: 5       Port Number

110: P30      Z=F

01: 1       F

02: 39      Z Loc [:Snow Calc]

111: P30      Z=F

01: 0       F

02: 42      Z Loc [:Snow # Pu]

112: P87      Beginning of Loop

01: 0       Delay

02: 16      Loop Count

113: P20      Set Port

01: 1       Set high

02: 5       Port Number

114: P20      Set Port

01: 0       Set low

02: 5       Port Number

115: P1       Volt (SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 13      IN Chan

04: 40      Loc [:Snow Data]

05: 1       Mult

06: 0       Offset

116: P89      If X<=>F

01: 40      X Loc Snow Data

02: 3       >=

03: 3000    F

04: 30      Then Do

117: P33      Z=X+Y

01: 39      X Loc Snow Calc

02: 42      Y Loc Snow # Pu

03: 42      Z Loc [:Snow # Pu]

118: P95      End

119: P37      Z=X*F

01: 39      X Loc Snow Calc

02: 2       F

03: 39      Z Loc [:Snow Calc]

120: P95      End

121: P30      Z=F

01: 291     F

02: 41      Z Loc [:T2 291 K ]

122: P38      Z=X/Y

01: 28      X Loc Temp LC K

02: 41      Y Loc T2 291 K

03: 20      Z Loc [:Snow D mm]

123: P39      Z=SQRT(X)

01: 20      X Loc Snow D mm

02: 20      Z Loc [:Snow D mm]

124: P36      Z=X*Y

01: 42      X Loc Snow # Pu

02: 20      Y Loc Snow D mm

03: 20      Z Loc [:Snow D mm]

125: P37      Z=X*F

01: 20      X Loc Snow D mm

02: .52176  F

03: 20      Z Loc [:Snow D mm]

126: P34      Z=X+F

01: 20      X Loc Snow D mm

02: -39     F

03: 20      Z Loc [:Snow D mm]

127: P20      Set Port

01: 0       Set low

02: 4       Port Number

128: P20      Set Port

01: 0       Set low

02: 5       Port Number

129: P20      Set Port                 End of Snow Depth

01: 0       Set low

02: 6       Port Number

130: P89      If X<=>F           Five Minute Average at the top of

01: 64      X Loc Minutes    the hour for Belfort and Snow Depth

02: 1       =

03: 59      F

04: 10      Set high Flag 0 (output)

131: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 15      Array ID or location

132: P71      Average

01: 2       Reps

02: 19      Loc Belfortmm

133: P95      End

134: P95      End

135: P92      If time is            Calculate the Belfort change

01: 0       minutes into a        from the previous hour

02: 60      minute interval

03: 30      Then Do

136: P35      Z=X-Y

01: 15      X Loc Av Belfor

02: 59      Y Loc Prev Belf

03: 60      Z Loc [:Belf Diff]

137: P31      Z=X

01: 15      X Loc Av Belfor

02: 59      Z Loc [:Prev Belf]

138: P95      End

139: P89      If X<=>F          Two minute average of Wind Speed

01: 64      X Loc Minutes     and Direction at top of the hour

02: 3       >=

03: 58      F

04: 10      Set high Flag 0 (output)

140: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 23      Array ID or location

141: P69      Wind Vector

01: 1       Rep

02: 0       Samples per sub-interval

03: 1       Polar Sensor/(S, D1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

142: P92      If time is

01: 59      minutes into a

02: 60      minute interval

03: 10      Set high Flag 0 (output)

143: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 61      Array ID or location

144: P71      Average            One minute average of Pressure

01: 1       Rep                at top of the hour

02: 11      Loc Press KPa

145: P71      Average            One minute average of Temperature

01: 1       Rep                at top of the hour

02: 5       Loc Temp UC C

146: P71      Average            One minute average of Dewpoint

01: 1       Rep                at top of the hour

02: 22      Loc Dewpoint

147: P92      If time is            Begin writing to the array -

01: 0       minutes into a        15 minute interval

02: 15      minute interval

03: 10      Set high Flag 0 (output)

148: P80      Set Active Storage Area

01: 1       Final Storage Area

02: 7       Array ID or location

149: P70      Sample                     Sample Battery

01: 1       Rep

02: 25      Loc Battery V

150: P77      Real Time                  Year, Day, Time

01: 1110    Year,Day,Hour-Minute

151: P78      Resolution

01: 1       High Resolution

152: P72      Totalize           Totalize Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Loc Par KJ/m2

153: P78      Resolution

01: 0       Low Resolution

154: P82      Standard Deviation Std Dev Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Sample Loc Par KJ/m2

155: P71      Average           Average TempUC, TempLC, Temp10

01: 6       Reps              Temp20, Temp50, RelHum

02: 5       Loc Temp UC C

156: P78      Resolution

01: 1       High Resolution

157: P71      Average           Average Pressure

01: 1       Rep

02: 11      Loc Press KPa

158: P78      Resolution

01: 0       Low Resolution

159: P71      Average           Average IRSensor

01: 1       Rep

02: 12      Loc IRSensorC

160: P82      Standard Deviation Std Dev Temp UC, TempLC, Temp10

01: 8       Reps               Temp20, Temp50, RelHum, Pressure

02: 5       Sample Loc Temp UC C IRSensor

161: P69      Wind Vector      Average Wind Speed, Wind Direction

01: 1       Rep                   and Std Dev Wind Direction

02: 0       Samples per sub-interval

03: 0       Polar Sensor/(S, D1, SD1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

162: P82      Standard Deviation      Std Dev Wind Speed

01: 1       Rep

02: 14      Sample Loc WindS m/s

163: P70      Sample                Sample Belfort, Snow Depth

01: 2       Reps                  Average of minute 50

02: 15      Loc Av Belfor         of the hour

164: P72      Totalize                Totalize Tip Bucket

01: 1       Rep

02: 18      Loc TipBuc mm

165: P33      Z=X+Y

01: 18      X Loc TipBuc mm

02: 65      Y Loc Total Tip

03: 65      Z Loc [:Total Tip]

166: P70      Sample                     Sample Soil Moisture

01: 1       Rep                       Average of last 5 minutes

02: 17      Loc Av Soil M             of the hour

167: P78      Resolution

01: 1       High Resolution

168: P70      Sample         Sample Pressure for GTS

01: 1       Rep

02: 61      Loc Press 1hr

169: P78      Resolution

01: 0       Low Resolution

170: P70      Sample   Sample TempUC, Dewpoint for GTS

01: 2       Reps

02: 62      Loc Temp  1hr

171: P70      Sample           Sample Wind Dir for GTS

01: 1       Rep

02: 24      Loc WindD 1hr

172: P70      Sample         Sample Wind Speed for GTS

01: 1       Rep

02: 23      Loc WindS 1hr

173: P70      Sample           Sample Belfort difference from

01: 1       Rep              previous hour

02: 60      Loc Belf Diff

174: P70      Sample      Sample Total Tipping Bucket for season

01: 1       Rep

02: 65      Loc Total Tip

175: P70      Sample

01: 2       Reps

02: 73      Loc ThC 1sec

176: P96      Serial Output

01: 30      SM192/SM716/CSM1

177: P18      Time                Store end of Program time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 45      Loc [:LastTime ]

178: P35      Z=X-Y                Program Execution Time

01: 45      X Loc LastTime

02: 43      Y Loc FirstTime

03: 44      Z Loc [:Prog Time]

179: P        End Table 1

*     2       Table 2 Programs

01: 60      Sec. Execution Interval

01:  P92      If time is

01: 50      minutes into a

02: 60      minute interval

03: 30      Then Do

02:  P89      If X<=>F

01: 43      X Loc FirstTime

02: 4       <

03: 200     F

04: 30      Then Do

03:  P86      Do

01: 10      Set high Flag 0 (output)

04:  P30      Z=F

01: 0       F

02: 29      Z Loc [:OV  Pw   ]

05:  P30      Z=F

01: 2000    F

02: 66      Z Loc [:2V  Pw   ]

06:  P17      Panel Temperature

01: 67      Loc [:PanelTemp]

07:  P20      Set Port

01: 1       Set high

02: 1       Port Number

08:  P87      Beginning of Loop

01: 0       Delay

02: 2       Loop Count

09:  P20      Set Port

01: 1       Set high

02: 2       Port Number

10:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

11:  P20      Set Port

01: 0       Set low

02: 2       Port Number

12:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0.0000  mV Excitation

13:  P95      End

14:  P21      Analog Out

01: 2       CAO Chan

02: 66      mV Loc 2V  Pw

15:  P22      Excitation with Delay

01: 4       EX Chan

02: 100     Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

16:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 46      Loc [:ThC 1 sec]

07: 1       Mult

08: 0       Offset

17:  P22      Excitation with Delay

01: 4       EX Chan

02: 2000    Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

18:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 47      Loc [:ThC 21sec]

07: 1       Mult

08: 0       Offset

19:  P21      Analog Out

01: 2       CAO Chan

02: 29      mV Loc OV  Pw

20:  P20      Set Port

01: 0       Set low

02: 1       Port Number

21:  P35      Z=X-Y                   End of Soil Moisture

01: 47      X Loc ThC 21sec

02: 46      Y Loc ThC 1 sec

03: 68      Z Loc [:Soil Diff]

22:  P37      Z=X*F

01: 68      X Loc Soil Diff

02: 4.89    F

03: 69      Z Loc [:Soil Mult]

23:  P30      Z=F

01: 10      F

02: 70      Z Loc [:Soil Ten ]

24:  P47      Z=X^Y

01: 70      X Loc Soil Ten

02: 69      Y Loc Soil Mult

03: 71      Z Loc [:Soil Sub ]

25:  P37      Z=X*F

01: 71      X Loc Soil Sub

02: .00026  F

03: 72      Z Loc [:Soil Res ]

26:  P37      Z=X*F

01: 72      X Loc Soil Res

02: .1      F

03: 21      Z Loc [:Soil MPa ]

27:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 17      Array ID or location

28:  P70      Sample

01: 1       Rep

02: 21      Loc Soil MPa

29:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 73      Array ID or location

30:  P70      Sample

01: 2       Reps

02: 46      Loc ThC 1 sec

31:  P95      End

32:  P95      End

33:  P        End Table 2

*     3       Table 3 Subroutines

01:  P        End Table 3

*     4       Mode 4 Output Options

01: 0       (Tape OFF) (Printer OFF)

02: 0       Printer 300 Baud

*     A       Mode 10 Memory Allocation

01: 76      Input Locations

02: 130     Intermediate Locations

*     C       Mode 12 Security (OSX-0)

01: 00      Security Option

02: 0000    Security Code

Input Location Assignments (with comments):

Key:

T=Table Number

E=Entry Number

L=Location Number

T:  E:  L:

1:  4:  1:  Loc [:Par KJ/m2]

1:  5:  2:  Loc [:Net KJ/m2]

1:  6:  3:  Loc [:AlU KJ/m2]

1:  7:  4:  Loc [:AlD KJ/m2]

1: 70:  5:  F(X) Loc [:Temp UC C]

1: 64:  6:  F(X) Loc [:Temp LC C]

1: 51:  7:  Loc [:Soil 10cm]

1: 55:  8:  Loc [:Soil 20cm]

1: 59:  9:  Loc [:Soil 50cm]

1: 74: 10:  Loc [:Humid %RH]

1: 43: 11:  Loc [:Press KPa]

1: 33: 12:  Z Loc [:IRSensorC]

1: 35: 13:  Loc [:WindDdegT]

1: 36: 14:  Loc [:WindS m/s]

1: 37: 18:  Loc [:TipBuc mm]

1: 91: 19:  Loc [:Belfortmm]

1:122: 20:  Z Loc [:Snow D mm]

1:123: 20:  Z Loc [:Snow D mm]

1:124: 20:  Z Loc [:Snow D mm]

1:125: 20:  Z Loc [:Snow D mm]

1:126: 20:  Z Loc [:Snow D mm]

2: 26: 21:  Z Loc [:Soil MPa ]

1: 87: 22:  Z Loc [:Dewpoint ]       End of Dewpoint Calculations

1:  3: 25:  Loc [:Battery V]

1: 63: 26:  Loc [:LC Store ]

1: 69: 27:  Loc [:UC Store ]

1: 65: 28:  Z Loc [:Temp LC K]

1:  8: 29:  Z Loc [:OV  Pw   ]

2:  4: 29:  Z Loc [:OV  Pw   ]

1:  9: 30:  Z Loc [:5V  Pw   ]

1: 11: 31:  Loc [:Ed Volts ]

1: 12: 32:  Loc [:Erel Volt]

1: 28: 32:  Z Loc [:Erel Volt]

1: 14: 33:  F(X) Loc [:Td C     ]

1: 18: 33:  F(X) Loc [:Td C     ]

1: 22: 33:  Z Loc [:Td C     ]

1: 25: 33:  F(X) Loc [:Td C     ]

1: 17: 34:  Z Loc [:Temporary]

1: 20: 34:  Z Loc [:Temporary]

1: 21: 34:  Z Loc [:Temporary]

1: 24: 34:  Z Loc [:Temporary]

1: 19: 35:  Z Loc [:Six      ]

1: 29: 36:  Z Loc [:Erel Mult]

1: 30: 36:  Z Loc [:Erel Mult]

1: 31: 37:  Z Loc [:Ecrel V  ]

1: 32: 38:  F(X) Loc [:Trel C   ]

1:110: 39:  Z Loc [:Snow Calc]

1:119: 39:  Z Loc [:Snow Calc]

1:115: 40:  Loc [:Snow Data]

1:121: 41:  Z Loc [:T2 291 K ]

1:111: 42:  Z Loc [:Snow # Pu]

1:117: 42:  Z Loc [:Snow # Pu]

1:  1: 43:  Loc [:FirstTime]

1:178: 44:  Z Loc [:Prog Time]

1:177: 45:  Loc [:LastTime ]

2: 16: 46:  Loc [:ThC 1 sec]

2: 18: 47:  Loc [:ThC 21sec]

1: 76: 48:  Z Loc [:a        ]

1: 77: 49:  Z Loc [:b        ]

1: 78: 50:  Z Loc [:a*T      ]

1: 79: 51:  Z Loc [:b+T      ]

1: 80: 52:  Z Loc [:aT/b+T   ]

1: 81: 53:  Z Loc [:aT/b+T-2 ]

1: 82: 54:  Z Loc [:ln(RH)   ]

1: 83: 55:  Z Loc [:ln/log   ]

1: 84: 56:  Z Loc [:log (RH) ]

1: 85: 57:  Z Loc [:log +aT/b]

1: 86: 58:  Z Loc [:a/logRH  ]

1:137: 59:  Z Loc [:Prev Belf]

1:136: 60:  Z Loc [:Belf Diff]

1:  2: 64:  Loc [:Minutes  ]

1:165: 65:  Z Loc [:Total Tip]

2:  5: 66:  Z Loc [:2V  Pw   ]

2:  6: 67:  Loc [:PanelTemp]

2: 21: 68:  Z Loc [:Soil Diff]

2: 22: 69:  Z Loc [:Soil Mult]

2: 23: 70:  Z Loc [:Soil Ten ]

2: 24: 71:  Z Loc [:Soil Sub ]

2: 25: 72:  Z Loc [:Soil Res ]

Program: Boreas  Nelson House, MB  Nov 27/95

Flag Usage:

Input Channel Usage:

Excitation Channel Usage:

Continuous Analog Output Usage:

Control Port Usage:

Pulse Input Channel Usage:

Output Array Definitions:

*     1       Table 1 Programs

01: 5       Sec. Execution Interval

01:  P18      Time                 Beginning of Program Time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 43      Loc [:FirstTime]

02:  P18      Time                 Time used for counting minutes

01: 1       Minutes into current day (maximum 1440)

02: 60      Mod/by

03: 64      Loc [:Minutes  ]

03:  P10      Battery Voltage            Battery Voltage

01: 25      Loc [:Battery V]

04:  P2       Volt (DIFF)                PAR Sensor         KJ/m*m

01: 1       Rep

02: 2       15 mV slow Range

03: 1       IN Chan

04: 1       Loc [:Par KJ/m2]

05: .5      Mult

06: 0       Offset

05:  P2       Volt (DIFF)                Net Radiometer    KJ/m*m

01: 1       Rep

02: 4       500 mV slow Range

03: 2       IN Chan

04: 2       Loc [:Net KJ/m2]

05: .0645   Mult

06: 0       Offset

06:  P2       Volt (DIFF)                Albedometer Up    KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 3       IN Chan

04: 3       Loc [:AlU KJ/m2]

05: .57537  Mult

06: 0       Offset

07:  P2       Volt (DIFF)                Albedometer Down   KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 4       IN Chan

04: 4       Loc [:AlD KJ/m2]

05: .58480  Mult

06: 0       Offset

08:  P30      Z=F                 Beginning of IR Sensor  deg C

01: 0       F

02: 29      Z Loc [:OV  Pw   ]

09:  P30      Z=F

01: 5000    F

02: 30      Z Loc [:5V  Pw   ]

10:  P21      Analog Out Set CAO channel 1 to 5000 mV

01: 1       CAO Chan

02: 30      mV Loc 5V  Pw

11:  P4       Excite,Delay,Volt(SE) Measures Ed and Erel

01: 1       Rep

02: 5       5000 mV slow Range

03: 9       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 100     Delay (units .01sec)

06: 1200    mV Excitation

07: 31      Loc [:Ed Volts ]

08: .001    Mult

09: 0       Offset

12:  P4       Excite,Delay,Volt(SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 10      IN Chan

04: 2       Excite all reps w/EXchan 2

05: 100     Delay (units .01sec)

06: 5000--  mV Excitation

07: 32      Loc [:Erel Volt]

08: .001    Mult

09: 0       Offset

13:  P89      If X<=>F

01: 31      X Loc Ed Volts

02: 3       >=

03: .42315  F

04: 30      Then Do

14:  P55      Polynomial

01: 1       Rep

02: 31      X Loc Ed Volts

03: 33      F(X) Loc [:Td C     ]

04: 48.653  C0

05: -302.29 C1

06: 658.31  C2

07: -911.19 C3

08: 660.33  C4

09: -201.44 C5

15:  P94      Else

16:  P89      If X<=>F

01: 31      X Loc Ed Volts

02: 3       >=

03: .03125  F

04: 30      Then Do

17:  P37      Z=X*F

01: 31      X Loc Ed Volts

02: 10      F

03: 34      Z Loc [:Temporary]

18:  P55      Polynomial

01: 1       Rep

02: 34      X Loc Temporary

03: 33      F(X) Loc [:Td C     ]

04: 88.341  C0

05: -140.82 C1

06: 131.86  C2

07: -74.476 C3

08: 23.529  C4

09: -3.8390 C5

19:  P30      Z=F

01: 6       F

02: 35      Z Loc [:Six      ]

20:  P47      Z=X^Y

01: 34      X Loc Temporary

02: 35      Y Loc Six

03: 34      Z Loc [:Temporary]

21:  P37      Z=X*F

01: 34      X Loc Temporary

02: .25131  F

03: 34      Z Loc [:Temporary]

22:  P33      Z=X+Y

01: 34      X Loc Temporary

02: 33      Y Loc Td C

03: 33      Z Loc [:Td C     ]

23:  P94      Else

24:  P37      Z=X*F

01: 31      X Loc Ed Volts

02: 100     F

03: 34      Z Loc [:Temporary]

25:  P55      Polynomial

01: 1       Rep

02: 34      X Loc Temporary

03: 33      F(X) Loc [:Td C     ]

04: 164.35  C0

05: -134.14 C1

06: 80.230  C2

07: -23.831 C3

08: 2.6569  C4

09: 0       C5

26:  P95      End

27:  P95      End

28:  P37      Z=X*F

01: 32      X Loc Erel Volt

02: 1       F

03: 32      Z Loc [:Erel Volt]

29:  P37      Z=X*F

01: 33      X Loc Td C

02: -.00224 F

03: 36      Z Loc [:Erel Mult]

30:  P34      Z=X+F

01: 36      X Loc Erel Mult

02: 1.0589  F

03: 36      Z Loc [:Erel Mult]

31:  P36      Z=X*Y

01: 32      X Loc Erel Volt

02: 36      Y Loc Erel Mult

03: 37      Z Loc [:Ecrel V  ]

32:  P55      Polynomial

01: 1       Rep

02: 37      X Loc Ecrel V

03: 38      F(X) Loc [:Trel C   ]

04: .0836   C0

05: 122     C1

06: -65.5   C2

07: 126.4   C3

08: -223.2  C4

09: 140.3   C5

33:  P33      Z=X+Y                    End of IR Sensor

01: 33      X Loc Td C

02: 38      Y Loc Trel C

03: 12      Z Loc [:IRSensorC]

34:  P21      Analog Out

01: 1       CAO Chan

02: 29      mV Loc OV  Pw

35:  P4       Excite,Delay,Volt(SE)    Wind Direction  degrees true

01: 1       Rep

02: 5       5000 mV slow Range

03: 11      IN Chan

04: 3       Excite all reps w/EXchan 3

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 13      Loc [:WindDdegT]

08: .071    Mult

09: 0       Offset

36:  P3       Pulse                     Wind Speed    metres/sec

01: 1       Rep

02: 2       Pulse Input Chan

03: 21      Low level AC; Output Hz.

04: 14      Loc [:WindS m/s]

05: .0980   Mult

06: 0       Offset

37:  P3       Pulse                    Tipping Bucket     mm

01: 1       Rep

02: 1       Pulse Input Chan

03: 2       Switch closure

04: 18      Loc [:TipBuc mm]

05: .025    Mult

06: 0       Offset

38:  P89      If X<=>F      On the 50th minute skip the multiplexer

01: 64      X Loc Minutes and execute soil moisture in Table 2

02: 2       <>

03: 50      F

04: 30      Then Do

39:  P20      Set Port                  Start of Multiplexer

01: 1       Set high

02: 1       Port Number

40:  P20      Set Port

01: 1       Set high

02: 2       Port Number

41:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

42:  P20      Set Port

01: 0       Set low

02: 2       Port Number

43:  P8       Excite,Delay,Volt(DIFF)     Setra Pressure Sensor KPa

01: 1       Rep

02: 4       500 mV slow Range

03: 8       IN Chan

04: 1       Excite all reps w/EXchan 1

05: 1       Delay (units=.01sec)

06: 2500    mV Excitation

07: 11      Loc [:Press KPa]

08: .12     Mult

09: 80      Offset

44:  P20      Set Port

01: 1       Set high

02: 2       Port Number

45:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

46:  P20      Set Port

01: 0       Set low

02: 2       Port Number

47:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

48:  P20      Set Port

01: 1       Set high

02: 2       Port Number

49:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

50:  P20      Set Port

01: 0       Set low

02: 2       Port Number

51:  P11      Temp 107 Probe          Temperature at 10 cm    deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 7       Loc [:Soil 10cm]

05: 1       Mult

06: 0       Offset

52:  P20      Set Port

01: 1       Set high

02: 2       Port Number

53:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

54:  P20      Set Port

01: 0       Set low

02: 2       Port Number

55:  P11      Temp 107 Probe           Temperature at 20 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 8       Loc [:Soil 20cm]

05: 1       Mult

06: 0       Offset

56:  P20      Set Port

01: 1       Set high

02: 2       Port Number

57:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

58:  P20      Set Port

01: 0       Set low

02: 2       Port Number

59:  P11      Temp 107 Probe          Temperature at 50 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 9       Loc [:Soil 50cm]

05: 1       Mult

06: 0       Offset

60:  P20      Set Port

01: 1       Set high

02: 2       Port Number

61:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

62:  P20      Set Port

01: 0       Set low

02: 2       Port Number

63:  P4       Excite,Delay,Volt(SE)   107F Temperature LC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 26      Loc [:LC Store ]

08: .001    Mult

09: 0       Offset

64:  P55      Polynomial

01: 1       Rep

02: 26      X Loc LC Store

03: 6       F(X) Loc [:Temp LC C]

04: -74.159 C0              Coefficients for 35 foot cable -

05: 645.87  C1              lower canopy

06: -3844.6 C2

07: 16081   C3

08: -34152  C4

09: 29933   C5

65:  P34      Z=X+F

01: 6       X Loc Temp LC C

02: 273.15  F

03: 28      Z Loc [:Temp LC K]

66:  P20      Set Port

01: 1       Set high

02: 2       Port Number

67:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

68:  P20      Set Port

01: 0       Set low

02: 2       Port Number

69:  P4       Excite,Delay,Volt(SE)  HMP35CF Temperature UC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 27      Loc [:UC Store ]

08: .001    Mult

09: 0       Offset

70:  P55      Polynomial

01: 1       Rep

02: 27      X Loc UC Store

03: 5       F(X) Loc [:Temp UC C]

04: -74.181 C0              Coefficients for 75 foot cable -

05: 646.76  C1               upper canopy

06: -3855.7 C2

07: 16149   C3

08: -34341  C4

09: 30134   C5

71:  P20      Set Port

01: 1       Set high

02: 2       Port Number

72:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

73:  P20      Set Port

01: 0       Set low

02: 2       Port Number

74:  P4       Excite,Delay,Volt(SE)   HMP35CF Relative Humidity %RH

01: 1       Rep

02: 5       5000 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 15      Delay (units .01sec)

06: 5000    mV Excitation

07: 10      Loc [:Humid %RH]

08: .1      Mult

09: 0       Offset

75:  P20      Set Port

01: 0       Set low

02: 1       Port Number

76:  P30      Z=F               Beginning of Dewpoint Calculations

01: 9.5     F

02: 48      Z Loc [:a        ]

77:  P30      Z=F

01: 265.5   F

02: 49      Z Loc [:b        ]

78:  P37      Z=X*F

01: 5       X Loc Temp UC C

02: 9.5     F

03: 50      Z Loc [:a*T      ]

79:  P34      Z=X+F

01: 5       X Loc Temp UC C

02: 265.5   F

03: 51      Z Loc [:b+T      ]

80:  P38      Z=X/Y

01: 50      X Loc a*T

02: 51      Y Loc b+T

03: 52      Z Loc [:aT/b+T   ]

81:  P34      Z=X+F

01: 52      X Loc aT/b+T

02: -2      F

03: 53      Z Loc [:aT/b+T-2 ]

82:  P40      Z=LN(X)

01: 10      X Loc Humid %RH

02: 54      Z Loc [:ln(RH)   ]

83:  P30      Z=F

01: 2.303   F

02: 55      Z Loc [:ln/log   ]

84:  P38      Z=X/Y

01: 54      X Loc ln(RH)

02: 55      Y Loc ln/log

03: 56      Z Loc [:log (RH) ]

85:  P33      Z=X+Y

01: 56      X Loc log (RH)

02: 53      Y Loc aT/b+T-2

03: 57      Z Loc [:log +aT/b]

86:  P38      Z=X/Y

01: 48      X Loc a

02: 57      Y Loc log +aT/b

03: 58      Z Loc [:a/logRH  ]

87:  P38      Z=X/Y

01: 49      X Loc b

02: 58      Y Loc a/logRH

03: 22      Z Loc [:Dewpoint ]       End of Dewpoint Calculations

88:  P95      End

89:  P92      If time is

01: 0       minutes into a

02: 1       minute interval

03: 30      Then Do

90:  P89      If X<=>F

01: 64      X Loc Minutes

02: 3       >=

03: 55      F

04: 30      Then Do

91:  P4       Excite,Delay,Volt(SE)     Belfort Weighing Gauge

01: 1       Rep

02: 5       5000 mV slow Range

03: 12      IN Chan

04: 4       Excite all reps w/EXchan 4

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 19      Loc [:Belfortmm]

08: .11384  Mult

09: 0       Offset

92:  P20      Set Port                   Begin Snow Depth Sensor

01: 1       Set high

02: 6       Port Number

93:  P20      Set Port

01: 0       Set low

02: 4       Port Number

94:  P20      Set Port

01: 1       Set high

02: 5       Port Number

95:  P20      Set Port

01: 0       Set low

02: 5       Port Number

96:  P20      Set Port

01: 1       Set high

02: 4       Port Number

97:  P20      Set Port

01: 1       Set high

02: 5       Port Number

98:  P20      Set Port

01: 0       Set low

02: 5       Port Number

99:  P20      Set Port

01: 0       Set low

02: 4       Port Number

100: P87      Beginning of Loop

01: 0       Delay

02: 6       Loop Count

101: P20      Set Port

01: 1       Set high

02: 5       Port Number

102: P20      Set Port

01: 0       Set low

02: 5       Port Number

103: P95      End

104: P20      Set Port

01: 1       Set high

02: 5       Port Number

105: P22      Excitation with Delay

01: 1       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

106: P20      Set Port

01: 0       Set low

02: 6       Port Number

107: P20      Set Port

01: 1       Set high

02: 6       Port Number

108: P22      Excitation with Delay

01: 1       EX Chan

02: 8       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

109: P20      Set Port

01: 0       Set low

02: 5       Port Number

110: P30      Z=F

01: 1       F

02: 39      Z Loc [:Snow Calc]

111: P30      Z=F

01: 0       F

02: 42      Z Loc [:Snow # Pu]

112: P87      Beginning of Loop

01: 0       Delay

02: 16      Loop Count

113: P20      Set Port

01: 1       Set high

02: 5       Port Number

114: P20      Set Port

01: 0       Set low

02: 5       Port Number

115: P1       Volt (SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 13      IN Chan

04: 40      Loc [:Snow Data]

05: 1       Mult

06: 0       Offset

116: P89      If X<=>F

01: 40      X Loc Snow Data

02: 3       >=

03: 3000    F

04: 30      Then Do

117: P33      Z=X+Y

01: 39      X Loc Snow Calc

02: 42      Y Loc Snow # Pu

03: 42      Z Loc [:Snow # Pu]

118: P95      End

119: P37      Z=X*F

01: 39      X Loc Snow Calc

02: 2       F

03: 39      Z Loc [:Snow Calc]

120: P95      End

121: P30      Z=F

01: 291     F

02: 41      Z Loc [:T2 291 K ]

122: P38      Z=X/Y

01: 28      X Loc Temp LC K

02: 41      Y Loc T2 291 K

03: 20      Z Loc [:Snow D mm]

123: P39      Z=SQRT(X)

01: 20      X Loc Snow D mm

02: 20      Z Loc [:Snow D mm]

124: P36      Z=X*Y

01: 42      X Loc Snow # Pu

02: 20      Y Loc Snow D mm

03: 20      Z Loc [:Snow D mm]

125: P37      Z=X*F

01: 20      X Loc Snow D mm

02: .52176  F

03: 20      Z Loc [:Snow D mm]

126: P34      Z=X+F

01: 20      X Loc Snow D mm

02: -39     F

03: 20      Z Loc [:Snow D mm]

127: P20      Set Port

01: 0       Set low

02: 4       Port Number

128: P20      Set Port

01: 0       Set low

02: 5       Port Number

129: P20      Set Port                 End of Snow Depth

01: 0       Set low

02: 6       Port Number

130: P89      If X<=>F           Five Minute Average at the top of

01: 64      X Loc Minutes    the hour for Belfort and Snow Depth

02: 1       =

03: 59      F

04: 10      Set high Flag 0 (output)

131: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 15      Array ID or location

132: P71      Average

01: 2       Reps

02: 19      Loc Belfortmm

133: P95      End

134: P95      End

135: P92      If time is

01: 0       minutes into a

02: 60      minute interval

03: 30      Then Do

136: P35      Z=X-Y

01: 15      X Loc Av Belfor

02: 59      Y Loc Prev Belf

03: 60      Z Loc [:Belf Diff]

137: P31      Z=X

01: 15      X Loc Av Belfor

02: 59      Z Loc [:Prev Belf]

138: P95      End

139: P89      If X<=>F           Two minute average of Wind Speed

01: 64      X Loc Minutes      and Direction at top of the hour

02: 3       >=

03: 58      F

04: 10      Set high Flag 0 (output)

140: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 23      Array ID or location

141: P69      Wind Vector

01: 1       Rep

02: 0       Samples per sub-interval

03: 1       Polar Sensor/(S, D1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

142: P92      If time is

01: 59      minutes into a

02: 60      minute interval

03: 10      Set high Flag 0 (output)

143: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 61      Array ID or location

144: P71      Average             One minute average of Pressure

01: 1       Rep                 at top of the hour

02: 11      Loc Press KPa

145: P71      Average             One minute average of Temperature

01: 1       Rep                 at top of the hour

02: 5       Loc Temp UC C

146: P71      Average             One minutue average of Dewpoint

01: 1       Rep                 at top of the hour

02: 22      Loc Dewpoint

147: P92      If time is            Begin writing to the array -

01: 0       minutes into a        15 minute interval

02: 15      minute interval

03: 10      Set high Flag 0 (output)

148: P80      Set Active Storage Area

01: 1       Final Storage Area

02: 8       Array ID or location

149: P70      Sample                     Sample Battery

01: 1       Rep

02: 25      Loc Battery V

150: P77      Real Time                  Year, Day, Time

01: 1110    Year,Day,Hour-Minute

151: P78      Resolution

01: 1       High Resolution

152: P72      Totalize           Totalize Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Loc Par KJ/m2

153: P78      Resolution

01: 0       Low Resolution

154: P82      Standard Deviation Std Dev Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Sample Loc Par KJ/m2

155: P71      Average           Average TempUC, TempLC, Temp10

01: 6       Reps              Temp20, Temp50, RelHum

02: 5       Loc Temp UC C

156: P78      Resolution

01: 1       High Resolution

157: P71      Average           Average Pressure

01: 1       Rep

02: 11      Loc Press KPa

158: P78      Resolution

01: 0       Low Resolution

159: P71      Average           Average IRSensor

01: 1       Rep

02: 12      Loc IRSensorC

160: P82      Standard Deviation Std Dev Temp UC, TempLC, Temp10

01: 8       Reps               Temp20, Temp50, RelHum, Pressure

02: 5       Sample Loc Temp UC C IRSensor

161: P69      Wind Vector      Average Wind Speed, Wind Direction

01: 1       Rep                   and Std Dev Wind Direction

02: 0       Samples per sub-interval

03: 0       Polar Sensor/(S, D1, SD1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

162: P82      Standard Deviation      Std Dev Wind Speed

01: 1       Rep

02: 14      Sample Loc WindS m/s

163: P70      Sample                Sample Belfort, Snow Depth

01: 2       Reps                  Average of last 5 minutes

02: 15      Loc Av Belfor         of the hour

164: P72      Totalize                Totalize Tip Bucket

01: 1       Rep

02: 18      Loc TipBuc mm

165: P33      Z=X+Y

01: 18      X Loc TipBuc mm

02: 65      Y Loc Total Tip

03: 65      Z Loc [:Total Tip]

166: P70      Sample                     Sample Soil Moisture

01: 1       Rep                        Average of minute 50

02: 17      Loc Av Soil M              of the hour

167: P78      Resolution

01: 1       High Resolution

168: P70      Sample            Sample Pressure for GTS

01: 1       Rep

02: 61      Loc Press 1hr

169: P78      Resolution

01: 0       Low Resolution

170: P70      Sample    Sample TempUC, Dewpoint for GTS

01: 2       Reps

02: 62      Loc Temp  1hr

171: P70      Sample           Sample Wind Dir for GTS

01: 1       Rep

02: 24      Loc WindD 1hr

172: P70      Sample         Sample Wind Speed for GTS

01: 1       Rep

02: 23      Loc WindS 1hr

173: P70      Sample          Sample Belfort difference from

01: 1       Rep             previous hour

02: 60      Loc Belf Diff

174: P70      Sample      Sample Total Tipping Bucket for season

01: 1       Rep

02: 65      Loc Total Tip

175: P70      Sample              Sample Soil Moisture Temps

01: 2       Reps

02: 73      Loc ThC 1sec

176: P96      Serial Output

01: 30      SM192/SM716/CSM1

177: P18      Time         Store end of Program time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 45      Loc [:LastTime ]

178: P35      Z=X-Y                Program Execution Time

01: 45      X Loc LastTime

02: 43      Y Loc FirstTime

03: 44      Z Loc [:Prog Time]

179: P92      If time is          Alcohol Injection - At 8:30 a.m.

01: 510     minutes into a      the alcohol injection system comes

02: 1440    minute interval     on three times for 1 second with

03: 11      Set high Flag 1     5 seconds between pulses

180: P91      If Flag             This calls Subroutine 1 contained

01: 11      1 is set            in Table 3

02: 30      Then Do

181: P86      Do

01: 1       Call Subroutine 1

182: P32      Z=Z+1

01: 75      Z Loc [:Counter1 ]

183: P95      End

184: P89      If X<=>F                This number controls the

01: 75      X Loc Counter1          number of pulses.

02: 3       >=

03: 3       F

04: 30      Then Do

185: P30      Z=F                     Resets the counter.

01: 0       F

02: 75      Z Loc [:Counter1 ]

186: P86      Do

01: 21      Set low Flag 1

187: P95      End

188: P        End Table 1

*     2       Table 2 Programs

01: 60      Sec. Execution Interval

01:  P92      If time is                 Soil Moisture

01: 50      minutes into a

02: 60      minute interval

03: 30      Then Do

02:  P89      If X<=>F

01: 43      X Loc FirstTime

02: 4       <

03: 200     F

04: 30      Then Do

03:  P86      Do

01: 10      Set high Flag 0 (output)

04:  P30      Z=F

01: 0       F

02: 29      Z Loc [:OV  Pw   ]

05:  P30      Z=F

01: 2000    F

02: 66      Z Loc [:2V  Pw   ]

06:  P17      Panel Temperature

01: 67      Loc [:PanelTemp]

07:  P20      Set Port

01: 1       Set high

02: 1       Port Number

08:  P87      Beginning of Loop

01: 0       Delay

02: 2       Loop Count

09:  P20      Set Port

01: 1       Set high

02: 2       Port Number

10:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

11:  P20      Set Port

01: 0       Set low

02: 2       Port Number

12:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0.0000  mV Excitation

13:  P95      End

14:  P21      Analog Out

01: 2       CAO Chan

02: 66      mV Loc 2V  Pw

15:  P22      Excitation with Delay

01: 4       EX Chan

02: 100     Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

16:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 46      Loc [:ThC 1 sec]

07: 1       Mult

08: 0       Offset

17:  P22      Excitation with Delay

01: 4       EX Chan

02: 2000    Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

18:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 47      Loc [:ThC 21sec]

07: 1       Mult

08: 0       Offset

19:  P21      Analog Out

01: 2       CAO Chan

02: 29      mV Loc OV  Pw

20:  P20      Set Port

01: 0       Set low

02: 1       Port Number

21:  P35      Z=X-Y                   End of Soil Moisture

01: 47      X Loc ThC 21sec

02: 46      Y Loc ThC 1 sec

03: 68      Z Loc [:Soil Diff]

22:  P37      Z=X*F

01: 68      X Loc Soil Diff

02: 4.89    F

03: 69      Z Loc [:Soil Mult]

23:  P30      Z=F

01: 10      F

02: 70      Z Loc [:Soil Ten ]

24:  P47      Z=X^Y

01: 70      X Loc Soil Ten

02: 69      Y Loc Soil Mult

03: 71      Z Loc [:Soil Sub ]

25:  P37      Z=X*F

01: 71      X Loc Soil Sub

02: .00026  F

03: 72      Z Loc [:Soil Res ]

26:  P37      Z=X*F

01: 72      X Loc Soil Res

02: .1      F

03: 21      Z Loc [:Soil MPa ]

27:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 17      Array ID or location

28:  P70      Sample

01: 1       Rep

02: 21      Loc Soil MPa

29:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 73      Array ID or location

30:  P70      Sample

01: 2       Reps

02: 46      Loc ThC 1 sec

31:  P95      End

32:  P95      End

33:  P        End Table 2

*     3       Table 3 Subroutines

01:  P85      Beginning of Subroutine     Alcohol Injection

01: 1       Subroutine Number

02:  P20      Set Port

01: 1       Set high

02: 3       Port Number

03:  P22      Excitation with Delay

01: 3       EX Chan

02: 0       Delay w/EX (units=.01sec)

03: 100     Delay after EX (units=.01sec)

04: 0       mV Excitation

04:  P20      Set Port

01: 0       Set low

02: 3       Port Number

05:  P95      End

06:  P        End Table 3

*     4       Mode 4 Output Options

01: 0       (Tape OFF) (Printer OFF)

02: 0       Printer 300 Baud

*     A       Mode 10 Memory Allocation

01: 76      Input Locations

02: 130     Intermediate Locations

*     C       Mode 12 Security (OSX-0)

01: 00      Security Option

02: 0000    Security Code

Input Location Assignments (with comments):

Key:

T=Table Number

E=Entry Number

L=Location Number

T:  E:  L:

1:  4:  1:  Loc [:Par KJ/m2]

1:  5:  2:  Loc [:Net KJ/m2]

1:  6:  3:  Loc [:AlU KJ/m2]

1:  7:  4:  Loc [:AlD KJ/m2]

1: 70:  5:  F(X) Loc [:Temp UC C]

1: 64:  6:  F(X) Loc [:Temp LC C]

1: 51:  7:  Loc [:Soil 10cm]

1: 55:  8:  Loc [:Soil 20cm]

1: 59:  9:  Loc [:Soil 50cm]

1: 74: 10:  Loc [:Humid %RH]

1: 43: 11:  Loc [:Press KPa]

1: 33: 12:  Z Loc [:IRSensorC]

1: 35: 13:  Loc [:WindDdegT]

1: 36: 14:  Loc [:WindS m/s]

1: 37: 18:  Loc [:TipBuc mm]

1: 91: 19:  Loc [:Belfortmm]

1:122: 20:  Z Loc [:Snow D mm]

1:123: 20:  Z Loc [:Snow D mm]

1:124: 20:  Z Loc [:Snow D mm]

1:125: 20:  Z Loc [:Snow D mm]

1:126: 20:  Z Loc [:Snow D mm]

2: 26: 21:  Z Loc [:Soil MPa ]

1: 87: 22:  Z Loc [:Dewpoint ]       End of Dewpoint Calculations

1:  3: 25:  Loc [:Battery V]

1: 63: 26:  Loc [:LC Store ]

1: 69: 27:  Loc [:UC Store ]

1: 65: 28:  Z Loc [:Temp LC K]

1:  8: 29:  Z Loc [:OV  Pw   ]

2:  4: 29:  Z Loc [:OV  Pw   ]

1:  9: 30:  Z Loc [:5V  Pw   ]

1: 11: 31:  Loc [:Ed Volts ]

1: 12: 32:  Loc [:Erel Volt]

1: 28: 32:  Z Loc [:Erel Volt]

1: 14: 33:  F(X) Loc [:Td C     ]

1: 18: 33:  F(X) Loc [:Td C     ]

1: 22: 33:  Z Loc [:Td C     ]

1: 25: 33:  F(X) Loc [:Td C     ]

1: 17: 34:  Z Loc [:Temporary]

1: 20: 34:  Z Loc [:Temporary]

1: 21: 34:  Z Loc [:Temporary]

1: 24: 34:  Z Loc [:Temporary]

1: 19: 35:  Z Loc [:Six      ]

1: 29: 36:  Z Loc [:Erel Mult]

1: 30: 36:  Z Loc [:Erel Mult]

1: 31: 37:  Z Loc [:Ecrel V  ]

1: 32: 38:  F(X) Loc [:Trel C   ]

1:110: 39:  Z Loc [:Snow Calc]

1:119: 39:  Z Loc [:Snow Calc]

1:115: 40:  Loc [:Snow Data]

1:121: 41:  Z Loc [:T2 291 K ]

1:111: 42:  Z Loc [:Snow # Pu]

1:117: 42:  Z Loc [:Snow # Pu]

1:  1: 43:  Loc [:FirstTime]

1:178: 44:  Z Loc [:Prog Time]

1:177: 45:  Loc [:LastTime ]

2: 16: 46:  Loc [:ThC 1 sec]

2: 18: 47:  Loc [:ThC 21sec]

1: 76: 48:  Z Loc [:a        ]

1: 77: 49:  Z Loc [:b        ]

1: 78: 50:  Z Loc [:a*T      ]

1: 79: 51:  Z Loc [:b+T      ]

1: 80: 52:  Z Loc [:aT/b+T   ]

1: 81: 53:  Z Loc [:aT/b+T-2 ]

1: 82: 54:  Z Loc [:ln(RH)   ]

1: 83: 55:  Z Loc [:ln/log   ]

1: 84: 56:  Z Loc [:log (RH) ]

1: 85: 57:  Z Loc [:log +aT/b]

1: 86: 58:  Z Loc [:a/logRH  ]

1:137: 59:  Z Loc [:Prev Belf]

1:136: 60:  Z Loc [:Belf Diff]

1:  2: 64:  Loc [:Minutes  ]

1:165: 65:  Z Loc [:Total Tip]

2:  5: 66:  Z Loc [:2V  Pw   ]

2:  6: 67:  Loc [:PanelTemp]

2: 21: 68:  Z Loc [:Soil Diff]

2: 22: 69:  Z Loc [:Soil Mult]

2: 23: 70:  Z Loc [:Soil Ten ]

2: 24: 71:  Z Loc [:Soil Sub ]

2: 25: 72:  Z Loc [:Soil Res ]

1:182: 75:  Z Loc [:Counter1 ]

1:185: 75:  Z Loc [:Counter1 ]

Input Location Labels:

1:Par KJ/m2    20:Snow D mm    39:Snow Calc    58:a/logRH

2:Net KJ/m2    21:Soil MPa     40:Snow Data    59:Prev Belf

3:AlU KJ/m2    22:Dewpoint     41:T2 291 K     60:Belf Diff

4:AlD KJ/m2    23:WindS 1hr    42:Snow # Pu    61:Press 1hr

5:Temp UC C    24:WindD 1hr    43:FirstTime    62:Temp  1hr

6:Temp LC C    25:Battery V    44:Prog Time    63:Dewpt 1hr

7:Soil 10cm    26:LC Store     45:LastTime     64:Minutes

8:Soil 20cm    27:UC Store     46:ThC 1 sec    65:Total Tip

9:Soil 50cm    28:Temp LC K    47:ThC 21sec    66:2V  Pw

10:Humid %RH    29:OV  Pw       48:a            67:PanelTemp

11:Press KPa    30:5V  Pw       49:b            68:Soil Diff

12:IRSensorC    31:Ed Volts     50:a*T          69:Soil Mult

13:WindDdegT    32:Erel Volt    51:b+T          70:Soil Ten

14:WindS m/s    33:Td C         52:aT/b+T       71:Soil Sub

15:Av Belfor    34:Temporary    53:aT/b+T-2     72:Soil Res

16:Av Snow D    35:Six          54:ln(RH)       73:ThC 1sec

17:Av Soil M    36:Erel Mult    55:ln/log       74:ThC 21sec

18:TipBuc mm    37:Ecrel V      56:log (RH)     75:Counter1

19:Belfortmm    38:Trel C       57:log +aT/b    76:_________

Program: Boreas Suite B Nelson House Dec 7/94

Flag Usage:

Input Channel Usage:

Excitation Channel Usage:

Continous Analog Output Usage:

Control Port Usage:

Pulse Input Channel Usage:

Output Array Definitions:

*     1       Table 1 Programs

01: 5       Sec. Execution Interval

01:  P10      Battery Voltage             Battery Voltage

01: 7       Loc [:Battery V]

02:  P22      Excitation with Delay             Signal Light

01: 3       EX Chan

02: 25      Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 2500    mV Excitation

03:  P2       Volt (DIFF)                         Pyranometer

01: 1       Rep

02: 23      25 mV 60 Hz rejection Range

03: 1       IN Chan

04: 1       Loc [:PSP kJ/m2]

05: .5848   Mult

06: 0.0000  Offset

04:  P2       Volt (DIFF)                        Pyrgeometer

01: 1       Rep

02: 23      25 mV 60 Hz rejection Range

03: 2       IN Chan

04: 2       Loc [:PIR kJ/m2]

05: 1.4620  Mult

06: 0.0000  Offset

05:  P2       Volt (DIFF)

01: 1       Rep

02: 21      2.5 mV 60 Hz rejection Range

03: 3       IN Chan

04: 3       Loc [:ThPile mV]

05: 1       Mult

06: 0.0000  Offset

06:  P89      If X<=>F

01: 1       X Loc PSP kJ/m2

02: 4       <

03: 0.0000  F

04: 30      Then Do

07:  P30      Z=F

01: 0.0000  F

02: 00      Exponent of 10

03: 1       Z Loc [:PSP kJ/m2]

08:  P95      End

09:  P89      If X<=>F

01: 2       X Loc PIR kJ/m2

02: 4       <

03: 0.0000  F

04: 30      Then Do

10:  P30      Z=F

01: 0.0000  F

02: 00      Exponent of 10

03: 2       Z Loc [:PIR kJ/m2]

11:  P95      End

YSI 44031 Thermistor Measurement

12:  P4       Excite,Delay,Volt(SE)

01: 2       Reps

02: 24      250 mV 60 Hz rejection Range

03: 7       IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0000    Delay (units .01sec)

06: 1700    mV Excitation

07: 4       Loc [:Tcase C  ]

08: .01     Mult

09: 0       Offset

YSI 44031 Linearization

13:  P87      Beginning of Loop

01: 0000    Delay

02: 2       Loop Count

14:  P89      If X<=>F

01: 4--     X Loc Tcase C

02: 4       <

03: .5      F

04: 30      Then Do

15:  P55      Polynomial

01: 1       Rep

02: 4--     X Loc Tcase C

03: 4--     F(X) Loc [:Tcase C  ]

04: -64.140 C0

05: 472.02  C1

06: -2304.8 C2

07: 7037.4  C3

08: -11140  C4

09: 7001.6  C5

16:  P94      Else

17:  P55      Polynomial

01: 1       Rep

02: 4--     X Loc Tcase C

03: 4--     F(X) Loc [:Tcase C  ]

04: -32.981 C0

05: 85.859  C1

06: -62.706 C2

07: 30.782  C3

08: -8.1108 C4

09: .87158  C5

18:  P95      End

19:  P95      End

20:  P92      If time is

01: 0       minutes into a

02: 15      minute interval

03: 10      Set high Flag 0 (output)

21:  P80      Set Active Storage Area

01: 1       Final Storage Area 1

02: 8       Array ID or location

22:  P70      Sample

01: 1       Reps

02: 7       Loc Battery V

23:  P77      Real Time

01: 1220    Year,Day,Hour-Minute

24:  P78      Resolution

01: 1       High Resolution

25:  P72      Totalize        Totalize PSP, PIR, ThPile

01: 3       Reps

02: 1       Loc PSP kJ/m2

26:  P78      Resolution

01: 0       Low Resolution

27:  P71      Average               Average Tcase, Themisph

01: 2       Reps

02: 4       Loc Tcase C

28:  P82      Standard Deviation    Std Dev PSP, PIR, ThPile,

01: 5       Reps                          Tcase, Themisph

02: 1       Sample Loc PSP kJ/m2

29:  P96      Serial Output

01: 71      SM192/SM716/CSM1

30:  P92      If time is       Alcohol Injection - At 8:30 a.m.

01: 510     minutes into a   the alcohol injection system comes

02: 1440    minute interval  on three times for 1 second with

03: 11      Set high Flag 1  5 seconds between pulses

31:  P91      If Flag/Port           This calls Subroutine 1

01: 11      Do if flag 1 is high   contained in Table 3

02: 30      Then Do

32:  P86      Do

01: 1       Call Subroutine 1

33:  P32      Z=Z+1

01: 6       Z Loc [:Counter1 ]

34:  P95      End

35:  P89      If X<=>F              This number controls the

01: 6       X Loc Counter1        number of pulses

02: 3       >=

03: 3       F

04: 30      Then Do

36:  P30      Z=F

01: 0       F

02: 0       Exponent of 10

03: 6       Z Loc [:Counter1 ]

37:  P86      Do

01: 21      Set low Flag 1

38:  P95      End

39:  P        End Table 1

*     2       Table 2 Programs

01: 0       Sec. Execution Interval

01:  P        End Table 2

*     3       Table 3 Subroutines

01:  P85      Beginning of Subroutine    Alcohol Injection

01: 1       Subroutine Number

02:  P86      Do

01: 43      Set high Port 3

03:  P22      Excitation with Delay

01: 3       EX Chan

02: 0       Delay w/EX (units=.01sec)

03: 100     Delay after EX (units=.01sec)

04: 0       mV Excitation

04:  P86      Do

01: 53      Set low Port 3

05:  P95      End

06:  P        End Table 3

*     A       Mode 10 Memory Allocation

01: 28      Input Locations

02: 64      Intermediate Locations

03: 0.0000  Final Storage Area 2

*     C       Mode 12 Security

01: 0000    LOCK 1

02: 0000    LOCK 2

03: 0000    LOCK 3

Input Location Assignments (with comments):

Key:

T=Table Number

E=Entry Number

L=Location Number

T:  E:  L:

1:  3:  1:  Loc [:PSP kJ/m2]

1:  7:  1:  Z Loc [:PSP kJ/m2]

1:  4:  2:  Loc [:PIR kJ/m2]

1: 10:  2:  Z Loc [:PIR kJ/m2]

1:  5:  3:  Loc [:ThPile mV]

1: 12:  4:  Loc [:Tcase C  ]

1: 15:  4:  F(X) Loc [:Tcase C  ]

1: 17:  4:  F(X) Loc [:Tcase C  ]

1: 33:  6:  Z Loc [:Counter1 ]

1: 36:  6:  Z Loc [:Counter1 ]

1:  1:  7:  Loc [:Battery V]

Program: Boreas  Thompson, MB December 19/95

Flag Usage:

Input Channel Usage:

Excitation Channel Usage:

Continuous Analog Output Usage:

Control Port Usage:

Pulse Input Channel Usage:

Output Array Definitions:

*     1       Table 1 Programs

01: 5       Sec. Execution Interval

01:  P18      Time                 Beginning of Program Time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 43      Loc [:FirstTime]

02:  P18      Time                 Time used for counting minutes

01: 1       Minutes into current day (maximum 1440)

02: 60      Mod/by

03: 64      Loc [:Minutes  ]

03:  P10      Battery Voltage            Battery Voltage

01: 25      Loc [:Battery V]

04:  P2       Volt (DIFF)                PAR Sensor         KJ/m*m

01: 1       Rep

02: 2       15 mV slow Range

03: 1       IN Chan

04: 1       Loc [:Par KJ/m2]

05: .5      Mult

06: 0       Offset

05:  P2       Volt (DIFF)                Net Radiometer    KJ/m*m

01: 1       Rep

02: 4       500 mV slow Range

03: 2       IN Chan

04: 2       Loc [:Net KJ/m2]

05: .0645   Mult

06: 0       Offset

06:  P2       Volt (DIFF)                Albedometer Up    KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 3       IN Chan

04: 3       Loc [:AlU KJ/m2]

05: .56883  Mult

06: 0       Offset

07:  P2       Volt (DIFF)                Albedometer Down   KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 4       IN Chan

04: 4       Loc [:AlD KJ/m2]

05: .55991  Mult

06: 0       Offset

08:  P30      Z=F                 Beginning of IR Sensor  deg C

01: 0       F

02: 29      Z Loc [:OV  Pw   ]

09:  P30      Z=F

01: 5000    F

02: 30      Z Loc [:5V  Pw   ]

10:  P21      Analog Out Set CAO channel 1 to 5000 mV

01: 1       CAO Chan

02: 30      mV Loc 5V  Pw

11:  P4       Excite,Delay,Volt(SE) Measures Ed and Erel

01: 1       Rep

02: 5       5000 mV slow Range

03: 9       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 100     Delay (units .01sec)

06: 1200    mV Excitation

07: 31      Loc [:Ed Volts ]

08: .001    Mult

09: 0       Offset

12:  P4       Excite,Delay,Volt(SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 10      IN Chan

04: 2       Excite all reps w/EXchan 2

05: 100     Delay (units .01sec)

06: 5000--  mV Excitation

07: 32      Loc [:Erel Volt]

08: .001    Mult

09: 0       Offset

13:  P89      If X<=>F

01: 31      X Loc Ed Volts

02: 3       >=

03: .42315  F

04: 30      Then Do

14:  P55      Polynomial

01: 1       Rep

02: 31      X Loc Ed Volts

03: 33      F(X) Loc [:Td C     ]

04: 48.653  C0

05: -302.29 C1

06: 658.31  C2

07: -911.19 C3

08: 660.33  C4

09: -201.44 C5

15:  P94      Else

16:  P89      If X<=>F

01: 31      X Loc Ed Volts

02: 3       >=

03: .03125  F

04: 30      Then Do

17:  P37      Z=X*F

01: 31      X Loc Ed Volts

02: 10      F

03: 34      Z Loc [:Temporary]

18:  P55      Polynomial

01: 1       Rep

02: 34      X Loc Temporary

03: 33      F(X) Loc [:Td C     ]

04: 88.341  C0

05: -140.82 C1

06: 131.86  C2

07: -74.476 C3

08: 23.529  C4

09: -3.8390 C5

19:  P30      Z=F

01: 6       F

02: 35      Z Loc [:Six      ]

20:  P47      Z=X^Y

01: 34      X Loc Temporary

02: 35      Y Loc Six

03: 34      Z Loc [:Temporary]

21:  P37      Z=X*F

01: 34      X Loc Temporary

02: .25131  F

03: 34      Z Loc [:Temporary]

22:  P33      Z=X+Y

01: 34      X Loc Temporary

02: 33      Y Loc Td C

03: 33      Z Loc [:Td C     ]

23:  P94      Else

24:  P37      Z=X*F

01: 31      X Loc Ed Volts

02: 100     F

03: 34      Z Loc [:Temporary]

25:  P55      Polynomial

01: 1       Rep

02: 34      X Loc Temporary

03: 33      F(X) Loc [:Td C     ]

04: 164.35  C0

05: -134.14 C1

06: 80.230  C2

07: -23.831 C3

08: 2.6569  C4

09: 0       C5

26:  P95      End

27:  P95      End

28:  P37      Z=X*F

01: 32      X Loc Erel Volt

02: 1       F

03: 32      Z Loc [:Erel Volt]

29:  P37      Z=X*F

01: 33      X Loc Td C

02: -.00224 F

03: 36      Z Loc [:Erel Mult]

30:  P34      Z=X+F

01: 36      X Loc Erel Mult

02: 1.0589  F

03: 36      Z Loc [:Erel Mult]

31:  P36      Z=X*Y

01: 32      X Loc Erel Volt

02: 36      Y Loc Erel Mult

03: 37      Z Loc [:Ecrel V  ]

32:  P55      Polynomial

01: 1       Rep

02: 37      X Loc Ecrel V

03: 38      F(X) Loc [:Trel C   ]

04: .0836   C0

05: 122     C1

06: -65.5   C2

07: 126.4   C3

08: -223.2  C4

09: 140.3   C5

33:  P33      Z=X+Y                    End of IR Sensor

01: 33      X Loc Td C

02: 38      Y Loc Trel C

03: 12      Z Loc [:IRSensorC]

34:  P21      Analog Out

01: 1       CAO Chan

02: 29      mV Loc OV  Pw

35:  P4       Excite,Delay,Volt(SE)    Wind Direction  degrees true

01: 1       Rep

02: 5       5000 mV slow Range

03: 11      IN Chan

04: 3       Excite all reps w/EXchan 3

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 13      Loc [:WindDdegT]

08: .071    Mult

09: 0       Offset

36:  P3       Pulse                     Wind Speed    metres/sec

01: 1       Rep

02: 2       Pulse Input Chan

03: 21      Low level AC; Output Hz.

04: 14      Loc [:WindS m/s]

05: .0980   Mult

06: 0       Offset

37:  P3       Pulse                    Tipping Bucket     mm

01: 1       Rep

02: 1       Pulse Input Chan

03: 2       Switch closure

04: 18      Loc [:TipBuc mm]

05: .025    Mult

06: 0       Offset

38:  P89      If X<=>F      On the 50th minute skip the multiplexer

01: 64      X Loc Minutes and execute soil moisture in Table 2

02: 2       <>

03: 50      F

04: 30      Then Do

39:  P20      Set Port                  Start of Multiplexer

01: 1       Set high

02: 1       Port Number

40:  P20      Set Port

01: 1       Set high

02: 2       Port Number

41:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

42:  P20      Set Port

01: 0       Set low

02: 2       Port Number

43:  P8       Excite,Delay,Volt(DIFF)     Setra Pressure Sensor KPa

01: 1       Rep

02: 4       500 mV slow Range

03: 8       IN Chan

04: 1       Excite all reps w/EXchan 1

05: 1       Delay (units=.01sec)

06: 2500    mV Excitation

07: 11      Loc [:Press KPa]

08: .12     Mult

09: 80      Offset

44:  P20      Set Port

01: 1       Set high

02: 2       Port Number

45:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

46:  P20      Set Port

01: 0       Set low

02: 2       Port Number

47:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

48:  P20      Set Port

01: 1       Set high

02: 2       Port Number

49:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

50:  P20      Set Port

01: 0       Set low

02: 2       Port Number

51:  P11      Temp 107 Probe          Temperature at 10 cm    deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 7       Loc [:Soil 10cm]

05: 1       Mult

06: 0       Offset

52:  P20      Set Port

01: 1       Set high

02: 2       Port Number

53:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

54:  P20      Set Port

01: 0       Set low

02: 2       Port Number

55:  P11      Temp 107 Probe           Temperature at 20 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 8       Loc [:Soil 20cm]

05: 1       Mult

06: 0       Offset

56:  P20      Set Port

01: 1       Set high

02: 2       Port Number

57:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

58:  P20      Set Port

01: 0       Set low

02: 2       Port Number

59:  P11      Temp 107 Probe          Temperature at 50 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 9       Loc [:Soil 50cm]

05: 1       Mult

06: 0       Offset

60:  P20      Set Port

01: 1       Set high

02: 2       Port Number

61:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

62:  P20      Set Port

01: 0       Set low

02: 2       Port Number

63:  P4       Excite,Delay,Volt(SE)   107F Temperature LC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 26      Loc [:LC Store ]

08: .001    Mult

09: 0       Offset

64:  P55      Polynomial

01: 1       Rep

02: 26      X Loc LC Store

03: 6       F(X) Loc [:Temp LC C]

04: -74.159 C0              Coefficients for 35 foot cable -

05: 645.87  C1              lower canopy

06: -3844.6 C2

07: 16081   C3

08: -34152  C4

09: 29933   C5

65:  P34      Z=X+F

01: 6       X Loc Temp LC C

02: 273.15  F

03: 28      Z Loc [:Temp LC K]

66:  P20      Set Port

01: 1       Set high

02: 2       Port Number

67:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

68:  P20      Set Port

01: 0       Set low

02: 2       Port Number

69:  P4       Excite,Delay,Volt(SE)  HMP35CF Temperature UC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 27      Loc [:UC Store ]

08: .001    Mult

09: 0       Offset

70:  P55      Polynomial

01: 1       Rep

02: 27      X Loc UC Store

03: 5       F(X) Loc [:Temp UC C]

04: -74.181 C0              Coefficients for 75 foot cable -

05: 646.76  C1               upper canopy

06: -3855.7 C2

07: 16149   C3

08: -34341  C4

09: 30134   C5

71:  P20      Set Port

01: 1       Set high

02: 2       Port Number

72:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

73:  P20      Set Port

01: 0       Set low

02: 2       Port Number

74:  P4       Excite,Delay,Volt(SE)   HMP35CF Relative Humidity %RH

01: 1       Rep

02: 5       5000 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 15      Delay (units .01sec)

06: 5000    mV Excitation

07: 10      Loc [:Humid %RH]

08: .1      Mult

09: 0       Offset

75:  P20      Set Port

01: 0       Set low

02: 1       Port Number

76:  P30      Z=F               Beginning of Dewpoint Calculations

01: 9.5     F

02: 48      Z Loc [:a        ]

77:  P30      Z=F

01: 265.5   F

02: 49      Z Loc [:b        ]

78:  P37      Z=X*F

01: 5       X Loc Temp UC C

02: 9.5     F

03: 50      Z Loc [:a*T      ]

79:  P34      Z=X+F

01: 5       X Loc Temp UC C

02: 265.5   F

03: 51      Z Loc [:b+T      ]

80:  P38      Z=X/Y

01: 50      X Loc a*T

02: 51      Y Loc b+T

03: 52      Z Loc [:aT/b+T   ]

81:  P34      Z=X+F

01: 52      X Loc aT/b+T

02: -2      F

03: 53      Z Loc [:aT/b+T-2 ]

82:  P40      Z=LN(X)

01: 10      X Loc Humid %RH

02: 54      Z Loc [:ln(RH)   ]

83:  P30      Z=F

01: 2.303   F

02: 55      Z Loc [:ln/log   ]

84:  P38      Z=X/Y

01: 54      X Loc ln(RH)

02: 55      Y Loc ln/log

03: 56      Z Loc [:log (RH) ]

85:  P33      Z=X+Y

01: 56      X Loc log (RH)

02: 53      Y Loc aT/b+T-2

03: 57      Z Loc [:log +aT/b]

86:  P38      Z=X/Y

01: 48      X Loc a

02: 57      Y Loc log +aT/b

03: 58      Z Loc [:a/logRH  ]

87:  P38      Z=X/Y

01: 49      X Loc b

02: 58      Y Loc a/logRH

03: 22      Z Loc [:Dewpoint ]       End of Dewpoint Calculations

88:  P95      End

89:  P92      If time is

01: 0       minutes into a

02: 1       minute interval

03: 30      Then Do

90:  P89      If X<=>F

01: 64      X Loc Minutes

02: 3       >=

03: 55      F

04: 30      Then Do

91:  P4       Excite,Delay,Volt(SE)     Belfort Weighing Gauge

01: 1       Rep

02: 5       5000 mV slow Range

03: 12      IN Chan

04: 4       Excite all reps w/EXchan 4

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 19      Loc [:Belfortmm]

08: .11518  Mult

09: 0       Offset

92:  P20      Set Port                   Begin Snow Depth Sensor

01: 1       Set high

02: 6       Port Number

93:  P20      Set Port

01: 0       Set low

02: 4       Port Number

94:  P20      Set Port

01: 1       Set high

02: 5       Port Number

95:  P20      Set Port

01: 0       Set low

02: 5       Port Number

96:  P20      Set Port

01: 1       Set high

02: 4       Port Number

97:  P20      Set Port

01: 1       Set high

02: 5       Port Number

98:  P20      Set Port

01: 0       Set low

02: 5       Port Number

99:  P20      Set Port

01: 0       Set low

02: 4       Port Number

100: P87      Beginning of Loop

01: 0       Delay

02: 6       Loop Count

101: P20      Set Port

01: 1       Set high

02: 5       Port Number

102: P20      Set Port

01: 0       Set low

02: 5       Port Number

103: P95      End

104: P20      Set Port

01: 1       Set high

02: 5       Port Number

105: P22      Excitation with Delay

01: 1       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

106: P20      Set Port

01: 0       Set low

02: 6       Port Number

107: P20      Set Port

01: 1       Set high

02: 6       Port Number

108: P22      Excitation with Delay

01: 1       EX Chan

02: 8       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

109: P20      Set Port

01: 0       Set low

02: 5       Port Number

110: P30      Z=F

01: 1       F

02: 39      Z Loc [:Snow Calc]

111: P30      Z=F

01: 0       F

02: 42      Z Loc [:Snow # Pu]

112: P87      Beginning of Loop

01: 0       Delay

02: 16      Loop Count

113: P20      Set Port

01: 1       Set high

02: 5       Port Number

114: P20      Set Port

01: 0       Set low

02: 5       Port Number

115: P1       Volt (SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 13      IN Chan

04: 40      Loc [:Snow Data]

05: 1       Mult

06: 0       Offset

116: P89      If X<=>F

01: 40      X Loc Snow Data

02: 3       >=

03: 3000    F

04: 30      Then Do

117: P33      Z=X+Y

01: 39      X Loc Snow Calc

02: 42      Y Loc Snow # Pu

03: 42      Z Loc [:Snow # Pu]

118: P95      End

119: P37      Z=X*F

01: 39      X Loc Snow Calc

02: 2       F

03: 39      Z Loc [:Snow Calc]

120: P95      End

121: P30      Z=F

01: 291     F

02: 41      Z Loc [:T2 291 K ]

122: P38      Z=X/Y

01: 28      X Loc Temp LC K

02: 41      Y Loc T2 291 K

03: 20      Z Loc [:Snow D mm]

123: P39      Z=SQRT(X)

01: 20      X Loc Snow D mm

02: 20      Z Loc [:Snow D mm]

124: P36      Z=X*Y

01: 42      X Loc Snow # Pu

02: 20      Y Loc Snow D mm

03: 20      Z Loc [:Snow D mm]

125: P37      Z=X*F

01: 20      X Loc Snow D mm

02: .52176  F

03: 20      Z Loc [:Snow D mm]

126: P34      Z=X+F

01: 20      X Loc Snow D mm

02: -39     F

03: 20      Z Loc [:Snow D mm]

127: P20      Set Port

01: 0       Set low

02: 4       Port Number

128: P20      Set Port

01: 0       Set low

02: 5       Port Number

129: P20      Set Port                 End of Snow Depth

01: 0       Set low

02: 6       Port Number

130: P89      If X<=>F           Five Minute Average at the top of

01: 64      X Loc Minutes    the hour for Belfort and Snow Depth

02: 1       =

03: 59      F

04: 10      Set high Flag 0 (output)

131: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 15      Array ID or location

132: P71      Average

01: 2       Reps

02: 19      Loc Belfortmm

133: P95      End

134: P95      End

135: P92      If time is

01: 0       minutes into a

02: 60      minute interval

03: 30      Then Do

136: P35      Z=X-Y

01: 15      X Loc Av Belfor

02: 59      Y Loc Prev Belf

03: 60      Z Loc [:Belf Diff]

137: P31      Z=X

01: 15      X Loc Av Belfor

02: 59      Z Loc [:Prev Belf]

138: P95      End

139: P89      If X<=>F           Two minute average of Wind Speed

01: 64      X Loc Minutes      and Direction at top of the hour

02: 3       >=

03: 58      F

04: 10      Set high Flag 0 (output)

140: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 23      Array ID or location

141: P69      Wind Vector

01: 1       Rep

02: 0       Samples per sub-interval

03: 1       Polar Sensor/(S, D1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

142: P92      If time is

01: 59      minutes into a

02: 60      minute interval

03: 10      Set high Flag 0 (output)

143: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 61      Array ID or location

144: P71      Average           One minute average of Pressure

01: 1       Rep               at top of the hour

02: 11      Loc Press KPa

145: P71      Average           One minute average of Temperature

01: 1       Rep               at top of the hour

02: 5       Loc Temp UC C

146: P71      Average           One minute average of Dewpoint

01: 1       Rep               at top of the hour

02: 22      Loc Dewpoint

147: P92      If time is            Begin writing to the array -

01: 0       minutes into a        15 minute interval

02: 15      minute interval

03: 10      Set high Flag 0 (output)

148: P80      Set Active Storage Area

01: 1       Final Storage Area

02: 9       Array ID or location

149: P70      Sample                     Sample Battery

01: 1       Rep

02: 25      Loc Battery V

150: P77      Real Time                  Year, Day, Time

01: 1110    Year,Day,Hour-Minute

151: P78      Resolution

01: 1       High Resolution

152: P72      Totalize           Totalize Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Loc Par KJ/m2

153: P78      Resolution

01: 0       Low Resolution

154: P82      Standard Deviation Std Dev Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Sample Loc Par KJ/m2

155: P71      Average           Average TempUC, TempLC, Temp10

01: 6       Reps              Temp20, Temp50, RelHum

02: 5       Loc Temp UC C

156: P78      Resolution

01: 1       High Resolution

157: P71      Average           Average Pressure

01: 1       Rep

02: 11      Loc Press KPa

158: P78      Resolution

01: 0       Low Resolution

159: P71      Average           Average IRSensor

01: 1       Rep

02: 12      Loc IRSensorC

160: P82      Standard Deviation Std Dev Temp UC, TempLC, Temp10

01: 8       Reps               Temp20, Temp50, RelHum, Pressure

02: 5       Sample Loc Temp UC C IRSensor

161: P69      Wind Vector      Average Wind Speed, Wind Direction

01: 1       Rep                   and Std Dev Wind Direction

02: 0       Samples per sub-interval

03: 0       Polar Sensor/(S, D1, SD1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

162: P82      Standard Deviation      Std Dev Wind Speed

01: 1       Rep

02: 14      Sample Loc WindS m/s

163: P70      Sample                Sample Belfort, Snow Depth

01: 2       Reps                  Average of last 5 minutes

02: 15      Loc Av Belfor         of the hour

164: P72      Totalize                Totalize Tip Bucket

01: 1       Rep

02: 18      Loc TipBuc mm

165: P33      Z=X+Y

01: 18      X Loc TipBuc mm

02: 65      Y Loc Total Tip

03: 65      Z Loc [:Total Tip]

166: P70      Sample                     Sample Soil Moisture

01: 1       Rep                       Average of minute 50

02: 17      Loc Av Soil M             of the hour

167: P78      Resolution

01: 1       High Resolution

168: P70      Sample        Sample Pressure for GTS

01: 1       Rep

02: 61      Loc Press 1hr

169: P78      Resolution

01: 0       Low Resolution

170: P70      Sample    Sample TempUC, Dewpoint for GTS

01: 2       Reps

02: 62      Loc Temp  1hr

171: P70      Sample           Sample Wind Dir for GTS

01: 1       Rep

02: 24      Loc WindD 1hr

172: P70      Sample         Sample Wind Speed for GTS

01: 1       Rep

02: 23      Loc WindS 1hr

173: P70      Sample          Sample Belfort difference from

01: 1       Rep             previous hour

02: 60      Loc Belf Diff

174: P70      Sample      Sample Total Tipping Bucket for season

01: 1       Rep

02: 65      Loc Total Tip

175: P70      Sample

01: 2       Reps

02: 73      Loc ThC 1sec

176: P96      Serial Output

01: 30      SM192/SM716/CSM1

177: P18      Time                Store end of Program time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 45      Loc [:LastTime ]

178: P35      Z=X-Y                Program Execution Time

01: 45      X Loc LastTime

02: 43      Y Loc FirstTime

03: 44      Z Loc [:Prog Time]

179: P        End Table 1

*     2       Table 2 Programs

01: 60      Sec. Execution Interval

01:  P92      If time is

01: 50      minutes into a

02: 60      minute interval

03: 30      Then Do

02:  P89      If X<=>F

01: 43      X Loc FirstTime

02: 4       <

03: 200     F

04: 30      Then Do

03:  P86      Do

01: 10      Set high Flag 0 (output)

04:  P30      Z=F

01: 0       F

02: 29      Z Loc [:OV  Pw   ]

05:  P30      Z=F

01: 2000    F

02: 66      Z Loc [:2V  Pw   ]

06:  P17      Panel Temperature

01: 67      Loc [:PanelTemp]

07:  P20      Set Port

01: 1       Set high

02: 1       Port Number

08:  P87      Beginning of Loop

01: 0       Delay

02: 2       Loop Count

09:  P20      Set Port

01: 1       Set high

02: 2       Port Number

10:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

11:  P20      Set Port

01: 0       Set low

02: 2       Port Number

12:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0.0000  mV Excitation

13:  P95      End

14:  P21      Analog Out

01: 2       CAO Chan

02: 66      mV Loc 2V  Pw

15:  P22      Excitation with Delay

01: 4       EX Chan

02: 100     Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

16:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 46      Loc [:ThC 1 sec]

07: 1       Mult

08: 0       Offset

17:  P22      Excitation with Delay

01: 4       EX Chan

02: 2000    Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

18:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 47      Loc [:ThC 21sec]

07: 1       Mult

08: 0       Offset

19:  P21      Analog Out

01: 2       CAO Chan

02: 29      mV Loc OV  Pw

20:  P20      Set Port

01: 0       Set low

02: 1       Port Number

21:  P35      Z=X-Y                   End of Soil Moisture

01: 47      X Loc ThC 21sec

02: 46      Y Loc ThC 1 sec

03: 68      Z Loc [:Soil Diff]

22:  P37      Z=X*F

01: 68      X Loc Soil Diff

02: 4.89    F

03: 69      Z Loc [:Soil Mult]

23:  P30      Z=F

01: 10      F

02: 70      Z Loc [:Soil Ten ]

24:  P47      Z=X^Y

01: 70      X Loc Soil Ten

02: 69      Y Loc Soil Mult

03: 71      Z Loc [:Soil Sub ]

25:  P37      Z=X*F

01: 71      X Loc Soil Sub

02: .00026  F

03: 72      Z Loc [:Soil Res ]

26:  P37      Z=X*F

01: 72      X Loc Soil Res

02: .1      F

03: 21      Z Loc [:Soil MPa ]

27:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 17      Array ID or location

28:  P70      Sample

01: 1       Rep

02: 21      Loc Soil MPa

29:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 73      Array ID or location

30:  P70      Sample

01: 2       Reps

02: 46      Loc ThC 1 sec

31:  P95      End

32:  P95      End

33:  P        End Table 2

*     3       Table 3 Subroutines

01:  P        End Table 3

*     4       Mode 4 Output Options

01: 0       (Tape OFF) (Printer OFF)

02: 0       Printer 300 Baud

*     A       Mode 10 Memory Allocation

01: 76      Input Locations

02: 130     Intermediate Locations

*     C       Mode 12 Security (OSX-0)

01: 00      Security Option

02: 0000    Security Code

Input Location Assignments (with comments):

Key:

T=Table Number

E=Entry Number

L=Location Number

T:  E:  L:

1:  4:  1:  Loc [:Par KJ/m2]

1:  5:  2:  Loc [:Net KJ/m2]

1:  6:  3:  Loc [:AlU KJ/m2]

1:  7:  4:  Loc [:AlD KJ/m2]

1: 70:  5:  F(X) Loc [:Temp UC C]

1: 64:  6:  F(X) Loc [:Temp LC C]

1: 51:  7:  Loc [:Soil 10cm]

1: 55:  8:  Loc [:Soil 20cm]

1: 59:  9:  Loc [:Soil 50cm]

1: 74: 10:  Loc [:Humid %RH]

1: 43: 11:  Loc [:Press KPa]

1: 33: 12:  Z Loc [:IRSensorC]

1: 35: 13:  Loc [:WindDdegT]

1: 36: 14:  Loc [:WindS m/s]

1: 37: 18:  Loc [:TipBuc mm]

1: 91: 19:  Loc [:Belfortmm]

1:122: 20:  Z Loc [:Snow D mm]

1:123: 20:  Z Loc [:Snow D mm]

1:124: 20:  Z Loc [:Snow D mm]

1:125: 20:  Z Loc [:Snow D mm]

1:126: 20:  Z Loc [:Snow D mm]

2: 26: 21:  Z Loc [:Soil MPa ]

1: 87: 22:  Z Loc [:Dewpoint ]       End of Dewpoint Calculations

1:  3: 25:  Loc [:Battery V]

1: 63: 26:  Loc [:LC Store ]

1: 69: 27:  Loc [:UC Store ]

1: 65: 28:  Z Loc [:Temp LC K]

1:  8: 29:  Z Loc [:OV  Pw   ]

2:  4: 29:  Z Loc [:OV  Pw   ]

1:  9: 30:  Z Loc [:5V  Pw   ]

1: 11: 31:  Loc [:Ed Volts ]

1: 12: 32:  Loc [:Erel Volt]

1: 28: 32:  Z Loc [:Erel Volt]

1: 14: 33:  F(X) Loc [:Td C     ]

1: 18: 33:  F(X) Loc [:Td C     ]

1: 22: 33:  Z Loc [:Td C     ]

1: 25: 33:  F(X) Loc [:Td C     ]

1: 17: 34:  Z Loc [:Temporary]

1: 20: 34:  Z Loc [:Temporary]

1: 21: 34:  Z Loc [:Temporary]

1: 24: 34:  Z Loc [:Temporary]

1: 19: 35:  Z Loc [:Six      ]

1: 29: 36:  Z Loc [:Erel Mult]

1: 30: 36:  Z Loc [:Erel Mult]

1: 31: 37:  Z Loc [:Ecrel V  ]

1: 32: 38:  F(X) Loc [:Trel C   ]

1:110: 39:  Z Loc [:Snow Calc]

1:119: 39:  Z Loc [:Snow Calc]

1:115: 40:  Loc [:Snow Data]

1:121: 41:  Z Loc [:T2 291 K ]

1:111: 42:  Z Loc [:Snow # Pu]

1:117: 42:  Z Loc [:Snow # Pu]

1:  1: 43:  Loc [:FirstTime]

1:178: 44:  Z Loc [:Prog Time]

1:177: 45:  Loc [:LastTime ]

2: 16: 46:  Loc [:ThC 1 sec]

2: 18: 47:  Loc [:ThC 21sec]

1: 76: 48:  Z Loc [:a        ]

1: 77: 49:  Z Loc [:b        ]

1: 78: 50:  Z Loc [:a*T      ]

1: 79: 51:  Z Loc [:b+T      ]

1: 80: 52:  Z Loc [:aT/b+T   ]

1: 81: 53:  Z Loc [:aT/b+T-2 ]

1: 82: 54:  Z Loc [:ln(RH)   ]

1: 83: 55:  Z Loc [:ln/log   ]

1: 84: 56:  Z Loc [:log (RH) ]

1: 85: 57:  Z Loc [:log +aT/b]

1: 86: 58:  Z Loc [:a/logRH  ]

1:137: 59:  Z Loc [:Prev Belf]

1:136: 60:  Z Loc [:Belf Diff]

1:  2: 64:  Loc [:Minutes  ]

1:165: 65:  Z Loc [:Total Tip]

2:  5: 66:  Z Loc [:2V  Pw   ]

2:  6: 67:  Loc [:PanelTemp]

2: 21: 68:  Z Loc [:Soil Diff]

2: 22: 69:  Z Loc [:Soil Mult]

2: 23: 70:  Z Loc [:Soil Ten ]

2: 24: 71:  Z Loc [:Soil Sub ]

2: 25: 72:  Z Loc [:Soil Res ]

Program: Boreas  Flin Flon, MB  November 24/95

Flag Usage:

Input Channel Usage:

Excitation Channel Usage:

Continuous Analog Output Usage:

Control Port Usage:

Pulse Input Channel Usage:

Output Array Definitions:

*     1       Table 1 Programs

01: 5       Sec. Execution Interval

01:  P18      Time                 Beginning of Program Time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 43      Loc [:FirstTime]

02:  P18      Time                 Time used for counting minutes

01: 1       Minutes into current day (maximum 1440)

02: 60      Mod/by

03: 64      Loc [:Minutes  ]

03:  P10      Battery Voltage            Battery Voltage

01: 25      Loc [:Battery V]

04:  P2       Volt (DIFF)                PAR Sensor         KJ/m*m

01: 1       Rep

02: 2       15 mV slow Range

03: 1       IN Chan

04: 1       Loc [:Par KJ/m2]

05: .5      Mult

06: 0       Offset

05:  P2       Volt (DIFF)                Net Radiometer    KJ/m*m

01: 1       Rep

02: 4       500 mV slow Range

03: 2       IN Chan

04: 2       Loc [:Net KJ/m2]

05: .0660   Mult

06: 0       Offset

06:  P2       Volt (DIFF)                Albedometer Up    KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 3       IN Chan

04: 3       Loc [:AlU KJ/m2]

05: .56243  Mult

06: 0       Offset

07:  P2       Volt (DIFF)                Albedometer Down   KJ/m*m

01: 1       Rep

02: 3       50 mV slow Range

03: 4       IN Chan

04: 4       Loc [:AlD KJ/m2]

05: .60901  Mult

06: 0       Offset

08:  P30      Z=F                 Beginning of IR Sensor  deg C

01: 0       F

02: 29      Z Loc [:OV  Pw   ]

09:  P30      Z=F

01: 5000    F

02: 30      Z Loc [:5V  Pw   ]

10:  P21      Analog Out Set CAO channel 1 to 5000 mV

01: 1       CAO Chan

02: 30      mV Loc 5V  Pw

11:  P4       Excite,Delay,Volt(SE) Measures Ed and Erel

01: 1       Rep

02: 5       5000 mV slow Range

03: 9       IN Chan

04: 2       Excite all reps w/EXchan 2

05: 100     Delay (units .01sec)

06: 1200    mV Excitation

07: 31      Loc [:Ed Volts ]

08: .001    Mult

09: 0       Offset

12:  P4       Excite,Delay,Volt(SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 10      IN Chan

04: 2       Excite all reps w/EXchan 2

05: 100     Delay (units .01sec)

06: 5000--  mV Excitation

07: 32      Loc [:Erel Volt]

08: .001    Mult

09: 0       Offset

13:  P89      If X<=>F

01: 31      X Loc Ed Volts

02: 3       >=

03: .42315  F

04: 30      Then Do

14:  P55      Polynomial

01: 1       Rep

02: 31      X Loc Ed Volts

03: 33      F(X) Loc [:Td C     ]

04: 48.653  C0

05: -302.29 C1

06: 658.31  C2

07: -911.19 C3

08: 660.33  C4

09: -201.44 C5

15:  P94      Else

16:  P89      If X<=>F

01: 31      X Loc Ed Volts

02: 3       >=

03: .03125  F

04: 30      Then Do

17:  P37      Z=X*F

01: 31      X Loc Ed Volts

02: 10      F

03: 34      Z Loc [:Temporary]

18:  P55      Polynomial

01: 1       Rep

02: 34      X Loc Temporary

03: 33      F(X) Loc [:Td C     ]

04: 88.341  C0

05: -140.82 C1

06: 131.86  C2

07: -74.476 C3

08: 23.529  C4

09: -3.8390 C5

19:  P30      Z=F

01: 6       F

02: 35      Z Loc [:Six      ]

20:  P47      Z=X^Y

01: 34      X Loc Temporary

02: 35      Y Loc Six

03: 34      Z Loc [:Temporary]

21:  P37      Z=X*F

01: 34      X Loc Temporary

02: .25131  F

03: 34      Z Loc [:Temporary]

22:  P33      Z=X+Y

01: 34      X Loc Temporary

02: 33      Y Loc Td C

03: 33      Z Loc [:Td C     ]

23:  P94      Else

24:  P37      Z=X*F

01: 31      X Loc Ed Volts

02: 100     F

03: 34      Z Loc [:Temporary]

25:  P55      Polynomial

01: 1       Rep

02: 34      X Loc Temporary

03: 33      F(X) Loc [:Td C     ]

04: 164.35  C0

05: -134.14 C1

06: 80.230  C2

07: -23.831 C3

08: 2.6569  C4

09: 0       C5

26:  P95      End

27:  P95      End

28:  P37      Z=X*F

01: 32      X Loc Erel Volt

02: 1       F

03: 32      Z Loc [:Erel Volt]

29:  P37      Z=X*F

01: 33      X Loc Td C

02: -.00224 F

03: 36      Z Loc [:Erel Mult]

30:  P34      Z=X+F

01: 36      X Loc Erel Mult

02: 1.0589  F

03: 36      Z Loc [:Erel Mult]

31:  P36      Z=X*Y

01: 32      X Loc Erel Volt

02: 36      Y Loc Erel Mult

03: 37      Z Loc [:Ecrel V  ]

32:  P55      Polynomial

01: 1       Rep

02: 37      X Loc Ecrel V

03: 38      F(X) Loc [:Trel C   ]

04: .0836   C0

05: 122     C1

06: -65.5   C2

07: 126.4   C3

08: -223.2  C4

09: 140.3   C5

33:  P33      Z=X+Y                    End of IR Sensor

01: 33      X Loc Td C

02: 38      Y Loc Trel C

03: 12      Z Loc [:IRSensorC]

34:  P21      Analog Out

01: 1       CAO Chan

02: 29      mV Loc OV  Pw

35:  P4       Excite,Delay,Volt(SE)    Wind Direction  degrees true

01: 1       Rep

02: 5       5000 mV slow Range

03: 11      IN Chan

04: 3       Excite all reps w/EXchan 3

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 13      Loc [:WindDdegT]

08: .071    Mult

09: 0       Offset

36:  P3       Pulse                     Wind Speed    metres/sec

01: 1       Rep

02: 2       Pulse Input Chan

03: 21      Low level AC; Output Hz.

04: 14      Loc [:WindS m/s]

05: .0980   Mult

06: 0       Offset

37:  P3       Pulse                    Tipping Bucket     mm

01: 1       Rep

02: 1       Pulse Input Chan

03: 2       Switch closure

04: 18      Loc [:TipBuc mm]

05: .05     Mult

06: 0       Offset

38:  P89      If X<=>F       On the 50th minute skip the multiplexer

01: 64      X Loc Minutes  and execute soil moisture in Table 2

02: 2       <>

03: 50      F

04: 30      Then Do

39:  P20      Set Port                  Start of Multiplexer

01: 1       Set high

02: 1       Port Number

40:  P20      Set Port

01: 1       Set high

02: 2       Port Number

41:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

42:  P20      Set Port

01: 0       Set low

02: 2       Port Number

43:  P8       Excite,Delay,Volt(DIFF)     Setra Pressure Sensor KPa

01: 1       Rep

02: 4       500 mV slow Range

03: 8       IN Chan

04: 1       Excite all reps w/EXchan 1

05: 1       Delay (units=.01sec)

06: 2500    mV Excitation

07: 11      Loc [:Press KPa]

08: .12     Mult

09: 80      Offset

44:  P20      Set Port

01: 1       Set high

02: 2       Port Number

45:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

46:  P20      Set Port

01: 0       Set low

02: 2       Port Number

47:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

48:  P20      Set Port

01: 1       Set high

02: 2       Port Number

49:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

50:  P20      Set Port

01: 0       Set low

02: 2       Port Number

51:  P11      Temp 107 Probe          Temperature at 10 cm    deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 7       Loc [:Soil 10cm]

05: 1       Mult

06: 0       Offset

52:  P20      Set Port

01: 1       Set high

02: 2       Port Number

53:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

54:  P20      Set Port

01: 0       Set low

02: 2       Port Number

55:  P11      Temp 107 Probe           Temperature at 20 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 8       Loc [:Soil 20cm]

05: 1       Mult

06: 0       Offset

56:  P20      Set Port

01: 1       Set high

02: 2       Port Number

57:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

58:  P20      Set Port

01: 0       Set low

02: 2       Port Number

59:  P11      Temp 107 Probe          Temperature at 50 cm   deg C

01: 1       Rep

02: 14      IN Chan

03: 1       Excite all reps w/EXchan 1

04: 9       Loc [:Soil 50cm]

05: 1       Mult

06: 0       Offset

60:  P20      Set Port

01: 1       Set high

02: 2       Port Number

61:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

62:  P20      Set Port

01: 0       Set low

02: 2       Port Number

63:  P4       Excite,Delay,Volt(SE)   107F Temperature LC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 26      Loc [:LC Store ]

08: .001    Mult

09: 0       Offset

64:  P55      Polynomial

01: 1       Rep

02: 26      X Loc LC Store

03: 6       F(X) Loc [:Temp LC C]

04: -74.159 C0              Coefficients for 35 foot cable -

05: 645.87  C1              lower canopy

06: -3844.6 C2

07: 16081   C3

08: -34152  C4

09: 29933   C5

65:  P34      Z=X+F

01: 6       X Loc Temp LC C

02: 273.15  F

03: 28      Z Loc [:Temp LC K]

66:  P20      Set Port

01: 1       Set high

02: 2       Port Number

67:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

68:  P20      Set Port

01: 0       Set low

02: 2       Port Number

69:  P4       Excite,Delay,Volt(SE)  HMP35CF Temperature UC  deg C

01: 1       Rep

02: 4       500 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0       Delay (units .01sec)

06: 500     mV Excitation

07: 27      Loc [:UC Store ]

08: .001    Mult

09: 0       Offset

70:  P55      Polynomial

01: 1       Rep

02: 27      X Loc UC Store

03: 5       F(X) Loc [:Temp UC C]

04: -74.168 C0              Coefficients for 50 foot cable -

05: 646.22  C1               upper canopy

06: -3848.9 C2

07: 16107   C3

08: -34225  C4

09: 30009   C5

71:  P20      Set Port

01: 1       Set high

02: 2       Port Number

72:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

73:  P20      Set Port

01: 0       Set low

02: 2       Port Number

74:  P4       Excite,Delay,Volt(SE)   HMP35CF Relative Humidity %RH

01: 1       Rep

02: 5       5000 mV slow Range

03: 14      IN Chan

04: 1       Excite all reps w/EXchan 1

05: 15      Delay (units .01sec)

06: 5000    mV Excitation

07: 10      Loc [:Humid %RH]

08: .1      Mult

09: 0       Offset

75:  P20      Set Port

01: 0       Set low

02: 1       Port Number

76:  P30      Z=F               Beginning of Dewpoint Calculations

01: 9.5     F

02: 48      Z Loc [:a        ]

77:  P30      Z=F

01: 265.5   F

02: 49      Z Loc [:b        ]

78:  P37      Z=X*F

01: 5       X Loc Temp UC C

02: 9.5     F

03: 50      Z Loc [:a*T      ]

79:  P34      Z=X+F

01: 5       X Loc Temp UC C

02: 265.5   F

03: 51      Z Loc [:b+T      ]

80:  P38      Z=X/Y

01: 50      X Loc a*T

02: 51      Y Loc b+T

03: 52      Z Loc [:aT/b+T   ]

81:  P34      Z=X+F

01: 52      X Loc aT/b+T

02: -2      F

03: 53      Z Loc [:aT/b+T-2 ]

82:  P40      Z=LN(X)

01: 10      X Loc Humid %RH

02: 54      Z Loc [:ln(RH)   ]

83:  P30      Z=F

01: 2.303   F

02: 55      Z Loc [:ln/log   ]

84:  P38      Z=X/Y

01: 54      X Loc ln(RH)

02: 55      Y Loc ln/log

03: 56      Z Loc [:log (RH) ]

85:  P33      Z=X+Y

01: 56      X Loc log (RH)

02: 53      Y Loc aT/b+T-2

03: 57      Z Loc [:log +aT/b]

86:  P38      Z=X/Y

01: 48      X Loc a

02: 57      Y Loc log +aT/b

03: 58      Z Loc [:a/logRH  ]

87:  P38      Z=X/Y

01: 49      X Loc b

02: 58      Y Loc a/logRH

03: 22      Z Loc [:Dewpoint ]       End of Dewpoint Calculations

88:  P95      End

89:  P92      If time is

01: 0       minutes into a

02: 1       minute interval

03: 30      Then Do

90:  P89      If X<=>F

01: 64      X Loc Minutes

02: 3       >=

03: 55      F

04: 30      Then Do

91:  P4       Excite,Delay,Volt(SE)     Belfort Weighing Gauge

01: 1       Rep

02: 5       5000 mV slow Range

03: 12      IN Chan

04: 4       Excite all reps w/EXchan 4

05: 20      Delay (units .01sec)

06: 5000    mV Excitation

07: 19      Loc [:Belfortmm]

08: .07558  Mult

09: 0       Offset

92:  P20      Set Port                   Begin Snow Depth Sensor

01: 1       Set high

02: 6       Port Number

93:  P20      Set Port

01: 0       Set low

02: 4       Port Number

94:  P20      Set Port

01: 1       Set high

02: 5       Port Number

95:  P20      Set Port

01: 0       Set low

02: 5       Port Number

96:  P20      Set Port

01: 1       Set high

02: 4       Port Number

97:  P20      Set Port

01: 1       Set high

02: 5       Port Number

98:  P20      Set Port

01: 0       Set low

02: 5       Port Number

99:  P20      Set Port

01: 0       Set low

02: 4       Port Number

100: P87      Beginning of Loop

01: 0       Delay

02: 6       Loop Count

101: P20      Set Port

01: 1       Set high

02: 5       Port Number

102: P20      Set Port

01: 0       Set low

02: 5       Port Number

103: P95      End

104: P20      Set Port

01: 1       Set high

02: 5       Port Number

105: P22      Excitation with Delay

01: 1       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

106: P20      Set Port

01: 0       Set low

02: 6       Port Number

107: P20      Set Port

01: 1       Set high

02: 6       Port Number

108: P22      Excitation with Delay

01: 1       EX Chan

02: 8       Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

109: P20      Set Port

01: 0       Set low

02: 5       Port Number

110: P30      Z=F

01: 1       F

02: 39      Z Loc [:Snow Calc]

111: P30      Z=F

01: 0       F

02: 42      Z Loc [:Snow # Pu]

112: P87      Beginning of Loop

01: 0       Delay

02: 16      Loop Count

113: P20      Set Port

01: 1       Set high

02: 5       Port Number

114: P20      Set Port

01: 0       Set low

02: 5       Port Number

115: P1       Volt (SE)

01: 1       Rep

02: 5       5000 mV slow Range

03: 13      IN Chan

04: 40      Loc [:Snow Data]

05: 1       Mult

06: 0       Offset

116: P89      If X<=>F

01: 40      X Loc Snow Data

02: 3       >=

03: 3000    F

04: 30      Then Do

117: P33      Z=X+Y

01: 39      X Loc Snow Calc

02: 42      Y Loc Snow # Pu

03: 42      Z Loc [:Snow # Pu]

118: P95      End

119: P37      Z=X*F

01: 39      X Loc Snow Calc

02: 2       F

03: 39      Z Loc [:Snow Calc]

120: P95      End

121: P30      Z=F

01: 291     F

02: 41      Z Loc [:T2 291 K ]

122: P38      Z=X/Y

01: 28      X Loc Temp LC K

02: 41      Y Loc T2 291 K

03: 20      Z Loc [:Snow D mm]

123: P39      Z=SQRT(X)

01: 20      X Loc Snow D mm

02: 20      Z Loc [:Snow D mm]

124: P36      Z=X*Y

01: 42      X Loc Snow # Pu

02: 20      Y Loc Snow D mm

03: 20      Z Loc [:Snow D mm]

125: P37      Z=X*F

01: 20      X Loc Snow D mm

02: .52176  F

03: 20      Z Loc [:Snow D mm]

126: P34      Z=X+F

01: 20      X Loc Snow D mm

02: -39     F

03: 20      Z Loc [:Snow D mm]

127: P20      Set Port

01: 0       Set low

02: 4       Port Number

128: P20      Set Port

01: 0       Set low

02: 5       Port Number

129: P20      Set Port                 End of Snow Depth

01: 0       Set low

02: 6       Port Number

130: P89      If X<=>F           Five Minute Average at the top of

01: 64      X Loc Minutes    the hour for Belfort and Snow Depth

02: 1       =

03: 59      F

04: 10      Set high Flag 0 (output)

131: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 15      Array ID or location

132: P71      Average

01: 2       Reps

02: 19      Loc Belfortmm

133: P95      End

134: P95      End

135: P92      If time is

01: 0       minutes into a

02: 60      minute interval

03: 30      Then Do

136: P35      Z=X-Y

01: 15      X Loc Av Belfor

02: 59      Y Loc Prev Belf

03: 60      Z Loc [:Belf Diff]

137: P31      Z=X

01: 15      X Loc Av Belfor

02: 59      Z Loc [:Prev Belf]

138: P95      End

139: P89      If X<=>F           Two minute average of Wind Speed

01: 64      X Loc Minutes      and Direction at top of the hour

02: 3       >=

03: 58      F

04: 10      Set high Flag 0 (output)

140: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 23      Array ID or location

141: P69      Wind Vector

01: 1       Rep

02: 0       Samples per sub-interval

03: 1       Polar Sensor/(S, D1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

142: P92      If time is

01: 59      minutes into a

02: 60      minute interval

03: 10      Set high Flag 0 (output)

143: P80      Set Active Storage Area

01: 3       Input Storage Area

02: 61      Array ID or location

144: P71      Average             One minute average of Pressure

01: 1       Rep                 at top of the hour

02: 11      Loc Press KPa

145: P71      Average             One minute average of Temperature

01: 1       Rep                 at top of the hour

02: 5       Loc Temp UC C

146: P71      Average             One minute average of Dewpoint

01: 1       Rep                 at top of the hour

02: 22      Loc Dewpoint

147: P92      If time is            Begin writing to the array -

01: 0       minutes into a        15 minute interval

02: 15      minute interval

03: 10      Set high Flag 0 (output)

148: P80      Set Active Storage Area

01: 1       Final Storage Area

02: 10      Array ID or location

149: P70      Sample                     Sample Battery

01: 1       Rep

02: 25      Loc Battery V

150: P77      Real Time                  Year, Day, Time

01: 1110    Year,Day,Hour-Minute

151: P78      Resolution

01: 1       High Resolution

152: P72      Totalize           Totalize Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Loc Par KJ/m2

153: P78      Resolution

01: 0       Low Resolution

154: P82      Standard Deviation Std Dev Par, Net, AlbUp, AlbDn

01: 4       Reps

02: 1       Sample Loc Par KJ/m2

155: P71      Average           Average TempUC, TempLC, Temp10

01: 6       Reps              Temp20, Temp50, RelHum

02: 5       Loc Temp UC C

156: P78      Resolution

01: 1       High Resolution

157: P71      Average           Average Pressure

01: 1       Rep

02: 11      Loc Press KPa

158: P78      Resolution

01: 0       Low Resolution

159: P71      Average           Average IRSensor

01: 1       Rep

02: 12      Loc IRSensorC

160: P82      Standard Deviation Std Dev Temp UC, TempLC, Temp10

01: 8       Reps               Temp20, Temp50, RelHum, Pressure

02: 5       Sample Loc Temp UC C IRSensor

161: P69      Wind Vector      Average Wind Speed, Wind Direction

01: 1       Rep                   and Std Dev Wind Direction

02: 0       Samples per sub-interval

03: 0       Polar Sensor/(S, D1, SD1)

04: 14      Wind Speed/East Loc WindS m/s

05: 13      Wind Direction/North Loc WindDdegT

162: P82      Standard Deviation      Std Dev Wind Speed

01: 1       Rep

02: 14      Sample Loc WindS m/s

163: P70      Sample                Sample Belfort, Snow Depth

01: 2       Reps                  Average of last 5 minutes

02: 15      Loc Av Belfor         of the hour

164: P72      Totalize                Totalize Tip Bucket

01: 1       Rep

02: 18      Loc TipBuc mm

165: P33      Z=X+Y

01: 18      X Loc TipBuc mm

02: 65      Y Loc Total Tip

03: 65      Z Loc [:Total Tip]

166: P70      Sample                     Sample Soil Moisture

01: 1       Rep                       Average of minute 50

02: 17      Loc Av Soil M             of the hour

167: P78      Resolution

01: 1       High Resolution

168: P70      Sample          Sample Pressure for GTS

01: 1       Rep

02: 61      Loc Press 1hr

169: P78      Resolution

01: 0       Low Resolution

170: P70      Sample    Sample TempLC, Dewpoint for GTS

01: 2       Reps

02: 62      Loc Temp  1hr

171: P70      Sample           Sample Wind Dir for GTS

01: 1       Rep

02: 24      Loc WindD 1hr

172: P70      Sample         Sample Wind Speed for GTS

01: 1       Rep

02: 23      Loc WindS 1hr

173: P70      Sample           Sample Belfort difference from

01: 1       Rep              previous hour

02: 60      Loc Belf Diff

174: P70      Sample      Sample Total Tipping Bucket for season

01: 1       Rep

02: 65      Loc Total Tip

175: P70      Sample            Sample Soil Moisture Temps

01: 2       Reps

02: 73      Loc ThC 1sec

176: P96      Serial Output

01: 30      SM192/SM716/CSM1

177: P18      Time                Store end of Program time

01: 0       Tenths of seconds into minute (maximum 600)

02: 0       Mod/by

03: 45      Loc [:LastTime ]

178: P35      Z=X-Y                Program Execution Time

01: 45      X Loc LastTime

02: 43      Y Loc FirstTime

03: 44      Z Loc [:Prog Time]

179: P92      If time is          Alcohol Injection - At 8:30 a.m.

01: 510     minutes into a      the alcohol injection system comes

02: 1440    minute interval     on three times for 1 second with

03: 11      Set high Flag 1     5 seconds between pulses

180: P91      If Flag             This calls Subroutine 1 contained

01: 11      1 is set            in Table 3

02: 30      Then Do

181: P86      Do

01: 1       Call Subroutine 1

182: P32      Z=Z+1

01: 75      Z Loc [:Counter1 ]

183: P95      End

184: P89      If X<=>F                This number controls the

01: 75      X Loc Counter1          number of pulses.

02: 3       >=

03: 3       F

04: 30      Then Do

185: P30      Z=F                     Resets the counter.

01: 0       F

02: 75      Z Loc [:Counter1 ]

186: P86      Do

01: 21      Set low Flag 1

187: P95      End

188: P        End Table 1

*     2       Table 2 Programs

01: 60      Sec. Execution Interval

01:  P92      If time is                     Soil Moisture

01: 50      minutes into a

02: 60      minute interval

03: 30      Then Do

02:  P89      If X<=>F

01: 43      X Loc FirstTime

02: 4       <

03: 200     F

04: 30      Then Do

03:  P86      Do

01: 10      Set high Flag 0 (output)

04:  P30      Z=F

01: 0       F

02: 29      Z Loc [:OV  Pw   ]

05:  P30      Z=F

01: 2000    F

02: 66      Z Loc [:2V  Pw   ]

06:  P17      Panel Temperature

01: 67      Loc [:PanelTemp]

07:  P20      Set Port

01: 1       Set high

02: 1       Port Number

08:  P87      Beginning of Loop

01: 0       Delay

02: 2       Loop Count

09:  P20      Set Port

01: 1       Set high

02: 2       Port Number

10:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0       mV Excitation

11:  P20      Set Port

01: 0       Set low

02: 2       Port Number

12:  P22      Excitation with Delay

01: 4       EX Chan

02: 1       Delay w/EX (units=.01sec)

03: 1       Delay after EX (units=.01sec)

04: 0.0000  mV Excitation

13:  P95      End

14:  P21      Analog Out

01: 2       CAO Chan

02: 66      mV Loc 2V  Pw

15:  P22      Excitation with Delay

01: 4       EX Chan

02: 100     Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

16:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 46      Loc [:ThC 1 sec]

07: 1       Mult

08: 0       Offset

17:  P22      Excitation with Delay

01: 4       EX Chan

02: 2000    Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 0       mV Excitation

18:  P14      Thermocouple Temp (DIFF)

01: 1       Rep

02: 1       5 mV slow Range

03: 8       IN Chan

04: 1       Type T (Copper-Constantan)

05: 67      Ref Temp Loc PanelTemp

06: 47      Loc [:ThC 21sec]

07: 1       Mult

08: 0       Offset

19:  P21      Analog Out

01: 2       CAO Chan

02: 29      mV Loc OV  Pw

20:  P20      Set Port

01: 0       Set low

02: 1       Port Number

21:  P35      Z=X-Y                   End of Soil Moisture

01: 47      X Loc ThC 21sec

02: 46      Y Loc ThC 1 sec

03: 68      Z Loc [:Soil Diff]

22:  P37      Z=X*F

01: 68      X Loc Soil Diff

02: 4.89    F

03: 69      Z Loc [:Soil Mult]

23:  P30      Z=F

01: 10      F

02: 70      Z Loc [:Soil Ten ]

24:  P47      Z=X^Y

01: 70      X Loc Soil Ten

02: 69      Y Loc Soil Mult

03: 71      Z Loc [:Soil Sub ]

25:  P37      Z=X*F

01: 71      X Loc Soil Sub

02: .00026  F

03: 72      Z Loc [:Soil Res ]

26:  P37      Z=X*F

01: 72      X Loc Soil Res

02: .1      F

03: 21      Z Loc [:Soil MPa ]

27:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 17      Array ID or location

28:  P70      Sample

01: 1       Rep

02: 21      Loc Soil MPa

29:  P80      Set Active Storage Area

01: 3       Input Storage Area

02: 73      Array ID or location

30:  P70      Sample

01: 2       Reps

02: 46      Loc ThC 1 sec

31:  P95      End

32:  P95      End

33:  P        End Table 2

*     3       Table 3 Subroutines

01:  P85      Beginning of Subroutine     Alcohol Injection

01: 1       Subroutine Number

02:  P20      Set Port

01: 1       Set high

02: 3       Port Number

03:  P22      Excitation with Delay

01: 3       EX Chan

02: 0       Delay w/EX (units=.01sec)

03: 100     Delay after EX (units=.01sec)

04: 0       mV Excitation

04:  P20      Set Port

01: 0       Set low

02: 3       Port Number

05:  P95      End

06:  P        End Table 3

*     4       Mode 4 Output Options

01: 0       (Tape OFF) (Printer OFF)

02: 0       Printer 300 Baud

*     A       Mode 10 Memory Allocation

01: 76      Input Locations

02: 130     Intermediate Locations

*     C       Mode 12 Security (OSX-0)

01: 00      Security Option

02: 0000    Security Code

Input Location Assignments (with comments):

Key:

T=Table Number

E=Entry Number

L=Location Number

T:  E:  L:

1:  4:  1:  Loc [:Par KJ/m2]

1:  5:  2:  Loc [:Net KJ/m2]

1:  6:  3:  Loc [:AlU KJ/m2]

1:  7:  4:  Loc [:AlD KJ/m2]

1: 70:  5:  F(X) Loc [:Temp UC C]

1: 64:  6:  F(X) Loc [:Temp LC C]

1: 51:  7:  Loc [:Soil 10cm]

1: 55:  8:  Loc [:Soil 20cm]

1: 59:  9:  Loc [:Soil 50cm]

1: 74: 10:  Loc [:Humid %RH]

1: 43: 11:  Loc [:Press KPa]

1: 33: 12:  Z Loc [:IRSensorC]

1: 35: 13:  Loc [:WindDdegT]

1: 36: 14:  Loc [:WindS m/s]

1: 37: 18:  Loc [:TipBuc mm]

1: 91: 19:  Loc [:Belfortmm]

1:122: 20:  Z Loc [:Snow D mm]

1:123: 20:  Z Loc [:Snow D mm]

1:124: 20:  Z Loc [:Snow D mm]

1:125: 20:  Z Loc [:Snow D mm]

1:126: 20:  Z Loc [:Snow D mm]

2: 26: 21:  Z Loc [:Soil MPa ]

1: 87: 22:  Z Loc [:Dewpoint ]       End of Dewpoint Calculations

1:  3: 25:  Loc [:Battery V]

1: 63: 26:  Loc [:LC Store ]

1: 69: 27:  Loc [:UC Store ]

1: 65: 28:  Z Loc [:Temp LC K]

1:  8: 29:  Z Loc [:OV  Pw   ]

2:  4: 29:  Z Loc [:OV  Pw   ]

1:  9: 30:  Z Loc [:5V  Pw   ]

1: 11: 31:  Loc [:Ed Volts ]

1: 12: 32:  Loc [:Erel Volt]

1: 28: 32:  Z Loc [:Erel Volt]

1: 14: 33:  F(X) Loc [:Td C     ]

1: 18: 33:  F(X) Loc [:Td C     ]

1: 22: 33:  Z Loc [:Td C     ]

1: 25: 33:  F(X) Loc [:Td C     ]

1: 17: 34:  Z Loc [:Temporary]

1: 20: 34:  Z Loc [:Temporary]

1: 21: 34:  Z Loc [:Temporary]

1: 24: 34:  Z Loc [:Temporary]

1: 19: 35:  Z Loc [:Six      ]

1: 29: 36:  Z Loc [:Erel Mult]

1: 30: 36:  Z Loc [:Erel Mult]

1: 31: 37:  Z Loc [:Ecrel V  ]

1: 32: 38:  F(X) Loc [:Trel C   ]

1:110: 39:  Z Loc [:Snow Calc]

1:119: 39:  Z Loc [:Snow Calc]

1:115: 40:  Loc [:Snow Data]

1:121: 41:  Z Loc [:T2 291 K ]

1:111: 42:  Z Loc [:Snow # Pu]

1:117: 42:  Z Loc [:Snow # Pu]

1:  1: 43:  Loc [:FirstTime]

1:178: 44:  Z Loc [:Prog Time]

1:177: 45:  Loc [:LastTime ]

2: 16: 46:  Loc [:ThC 1 sec]

2: 18: 47:  Loc [:ThC 21sec]

1: 76: 48:  Z Loc [:a        ]

1: 77: 49:  Z Loc [:b        ]

1: 78: 50:  Z Loc [:a*T      ]

1: 79: 51:  Z Loc [:b+T      ]

1: 80: 52:  Z Loc [:aT/b+T   ]

1: 81: 53:  Z Loc [:aT/b+T-2 ]

1: 82: 54:  Z Loc [:ln(RH)   ]

1: 83: 55:  Z Loc [:ln/log   ]

1: 84: 56:  Z Loc [:log (RH) ]

1: 85: 57:  Z Loc [:log +aT/b]

1: 86: 58:  Z Loc [:a/logRH  ]

1:137: 59:  Z Loc [:Prev Belf]

1:136: 60:  Z Loc [:Belf Diff]

1:  2: 64:  Loc [:Minutes  ]

1:165: 65:  Z Loc [:Total Tip]

2:  5: 66:  Z Loc [:2V  Pw   ]

2:  6: 67:  Loc [:PanelTemp]

2: 21: 68:  Z Loc [:Soil Diff]

2: 22: 69:  Z Loc [:Soil Mult]

2: 23: 70:  Z Loc [:Soil Ten ]

2: 24: 71:  Z Loc [:Soil Sub ]

2: 25: 72:  Z Loc [:Soil Res ]

1:182: 75:  Z Loc [:Counter1 ]

1:185: 75:  Z Loc [:Counter1 ]

Page 25    Input Location Labels:

1:Par KJ/m2    20:Snow D mm    39:Snow Calc    58:a/logRH

2:Net KJ/m2    21:Soil MPa     40:Snow Data    59:Prev Belf

3:AlU KJ/m2    22:Dewpoint     41:T2 291 K     60:Belf Diff

4:AlD KJ/m2    23:WindS 1hr    42:Snow # Pu    61:Press 1hr

5:Temp UC C    24:WindD 1hr    43:FirstTime    62:Temp  1hr

6:Temp LC C    25:Battery V    44:Prog Time    63:Dewpt 1hr

7:Soil 10cm    26:LC Store     45:LastTime     64:Minutes

8:Soil 20cm    27:UC Store     46:ThC 1 sec    65:Total Tip

9:Soil 50cm    28:Temp LC K    47:ThC 21sec    66:2V  Pw

10:Humid %RH    29:OV  Pw       48:a            67:PanelTemp

11:Press KPa    30:5V  Pw       49:b            68:Soil Diff

12:IRSensorC    31:Ed Volts     50:a*T          69:Soil Mult

13:WindDdegT    32:Erel Volt    51:b+T          70:Soil Ten

14:WindS m/s    33:Td C         52:aT/b+T       71:Soil Sub

15:Av Belfor    34:Temporary    53:aT/b+T-2     72:Soil Res

16:Av Snow D    35:Six          54:ln(RH)       73:ThC 1sec

17:Av Soil M    36:Erel Mult    55:ln/log       74:ThC 21sec

18:TipBuc mm    37:Ecrel V      56:log (RH)     75:Counter1

19:Belfortmm    38:Trel C       57:log +aT/b    76:_________

Program: Boreas Suite B Flin Flon Dec 6/94

Flag Usage:

Input Channel Usage:

Excitation Channel Usage:

Continous Analog Output Usage:

Control Port Usage:

Pulse Input Channel Usage:

Output Array Definitions:

*     1       Table 1 Programs

01: 5       Sec. Execution Interval

01:  P22      Excitation with Delay              Signal Light

01: 3       EX Chan

02: 25      Delay w/EX (units=.01sec)

03: 0       Delay after EX (units=.01sec)

04: 2500    mV Excitation

02:  P2       Volt (DIFF)                         Pyranometer

01: 1       Rep

02: 23      25 mV 60 Hz rejection Range

03: 1       IN Chan

04: 1       Loc [:PSP kJ/m2]

05: .56818  Mult

06: 0.0000  Offset

03:  P2       Volt (DIFF)                        Pyrgeometer

01: 1       Rep

02: 23      25 mV 60 Hz rejection Range

03: 2       IN Chan

04: 2       Loc [:PIR kJ/m2]

05: 1.2821  Mult

06: 0.0000  Offset

04:  P2       Volt (DIFF)

01: 1       Rep

02: 21      2.5 mV 60 Hz rejection Range

03: 3       IN Chan

04: 3       Loc [:ThPile mV]

05: 1       Mult

06: 0.0000  Offset

05:  P89      If X<=>F

01: 1       X Loc PSP kJ/m2

02: 4       <

03: 0.0000  F

04: 30      Then Do

06:  P30      Z=F

01: 0.0000  F

02: 00      Exponent of 10

03: 1       Z Loc [:PSP kJ/m2]

07:  P95      End

08:  P89      If X<=>F

01: 2       X Loc PIR kJ/m2

02: 4       <

03: 0.0000  F

04: 30      Then Do

09:  P30      Z=F

01: 0.0000  F

02: 00      Exponent of 10

03: 2       Z Loc [:PIR kJ/m2]

10:  P95      End

YSI 44031 Thermistor Measurement

11:  P4       Excite,Delay,Volt(SE)

01: 2       Reps

02: 24      250 mV 60 Hz rejection Range

03: 7       IN Chan

04: 1       Excite all reps w/EXchan 1

05: 0000    Delay (units .01sec)

06: 1700    mV Excitation

07: 4       Loc [:Tcase C  ]

08: .01     Mult

09: 0       Offset

YSI 44031 Linearization

12:  P87      Beginning of Loop

01: 0000    Delay

02: 2       Loop Count

13:  P89      If X<=>F

01: 4--     X Loc Tcase C

02: 4       <

03: .5      F

04: 30      Then Do

14:  P55      Polynomial

01: 1       Rep

02: 4--     X Loc Tcase C

03: 4--     F(X) Loc [:Tcase C  ]

04: -64.140 C0

05: 472.02  C1

06: -2304.8 C2

07: 7037.4  C3

08: -11140  C4

09: 7001.6  C5

15:  P94      Else

16:  P55      Polynomial

01: 1       Rep

02: 4--     X Loc Tcase C

03: 4--     F(X) Loc [:Tcase C  ]

04: -32.981 C0

05: 85.859  C1

06: -62.706 C2

07: 30.782  C3

08: -8.1108 C4

09: .87158  C5

17:  P95      End

18:  P95      End

19:  P92      If time is

01: 0       minutes into a

02: 15      minute interval

03: 10      Set high Flag 0 (output)

20:  P80      Set Active Storage Area

01: 1       Final Storage Area 1

02: 10      Array ID or location

21:  P77      Real Time

01: 1220    Year,Day,Hour-Minute

22:  P78      Resolution

01: 1       High Resolution

23:  P72      Totalize                Totalize PSP, PIR, ThPile

01: 3       Reps

02: 1       Loc PSP kJ/m2

24:  P78      Resolution

01: 0       Low Resolution

25:  P71      Average                Average Tcase, Themisph

01: 2       Reps

02: 4       Loc Tcase C

26:  P82      Standard Deviation     Std Dev PSP, PIR, ThPile

01: 5       Reps                           Tcase, Themisph

02: 1       Sample Loc PSP kJ/m2

27:  P96      Serial Output

01: 71      SM192/SM716/CSM1

28:  P92      If time is        Alcohol Injection - At 8:30 a.m.

01: 510     minutes into a    the alcohol injection system comes

02: 1440    minute interval   on three times for 1 second with

03: 11      Set high Flag 1   5 seconds between pulses

29:  P91      If Flag/Port             This calls Subroutine 1

01: 11      Do if flag 1 is high     contained in Table 3

02: 30      Then Do

30:  P86      Do

01: 1       Call Subroutine 1

31:  P32      Z=Z+1

01: 6       Z Loc [:Counter1 ]

32:  P95      End

33:  P89      If X<=>F              This number controls the

01: 6       X Loc Counter1        number of pulses.

02: 3       >=

03: 3       F

04: 30      Then Do

34:  P30      Z=F

01: 0       F

02: 0       Exponent of 10

03: 6       Z Loc [:Counter1 ]

35:  P86      Do

01: 21      Set low Flag 1

36:  P95      End

37:  P        End Table 1

*     2       Table 2 Programs

01: 0.0000  Sec. Execution Interval

01:  P        End Table 2

*     3       Table 3 Subroutines

01:  P85      Beginning of Subroutine     Alcohol Injection

01: 1       Subroutine Number

02:  P86      Do

01: 43      Set high Port 3

03:  P22      Excitation with Delay

01: 3       EX Chan

02: 0       Delay w/EX (units=.01sec)

03: 100     Delay after EX (units=.01sec)

04: 0       mV Excitation

04:  P86      Do

01: 53      Set low Port 3

Page 5   Table 3

05:  P95      End

06:  P        End Table 3

*     A       Mode 10 Memory Allocation

01: 28      Input Locations

02: 64      Intermediate Locations

03: 0.0000  Final Storage Area 2

*     C       Mode 12 Security

01: 0000    LOCK 1

02: 0000    LOCK 2

03: 0000    LOCK 3

Input Location Assignments (with comments):

Key:

T=Table Number

E=Entry Number

L=Location Number

T:  E:  L:

1:  2:  1:  Loc [:PSP kJ/m2]

1:  6:  1:  Z Loc [:PSP kJ/m2]

1:  3:  2:  Loc [:PIR kJ/m2]

1:  9:  2:  Z Loc [:PIR kJ/m2]

1:  4:  3:  Loc [:ThPile mV]

1: 11:  4:  Loc [:Tcase C  ]

1: 14:  4:  F(X) Loc [:Tcase C  ]

1: 16:  4:  F(X) Loc [:Tcase C  ]

1: 31:  6:  Z Loc [:Counter1 ]

1: 34:  6:  Z Loc [:Counter1 ]