BOREAS TGB-04 Water and Sediment Temperature data over the NSA-BP

Summary

The BOREAS TGB-04 team collected several data sets in support of their flux tower measurements at the NSA Beaver Pond site.  This data set contains water and sediment temperature data collected from May to September 1994.  The data are stored in tabular ASCII files.

Table of Contents

*  1. Data Set Overview

*  2. Investigator(s)

*  3. Theory of Measurements

*  4. Equipment

*  5. Data Acquisition Methods

*  6. Observations

*  7. Data Description

*  8. Data Organization

*  9. Data Manipulations

*  10. Errors

*  11. Notes

*  12. Application of the Data Set

*  13. Future Modifications and Plans

*  14. Software

*  15. Data Access

*  16. Output Products and Availability

*  17. References

*  18. Glossary of Terms

*  19. List of Acronyms

*  20. Document Information

1.	Data Set Overview

1.1 Data Set Identification

BOREAS TGB-04 Water and Sediment Temperature data over the NSA-BP

1.2 Data Set Introduction

The fluxes of heat, water and CO2 from one beaver pond were measured continuously using the energy balance Bowen ratio approach. The diffuse and bubble flux CH4 were measured several times a week using chambers. The chamber approach was used to sample CO2 and CH4 flux from 4 to 5 additional beaver ponds, once ever two weeks, and regional survey of the beaver ponds once during the IFC.  The results of the work was extrapolated from the local to regional scale in collaboration with the remote-sensing project of J. Miller (York University).

1.3 Objective/Purpose

The primary objective of the study was to quantify the exchange of water, and CH4 between boreal forest beaver ponds and the atmosphere for the ice free period of the BOReal Ecosystem-Atmosphere Study (BOREAS).

The secondary objective of the study was to study the soil climate and soil characteristics at a forest site in conjunction with the flux studies of P. Crill (UNH). Soil moisture and temperatures were measured continuously, and soil porosity was determined.

1.4 Summary of Parameters

The main parameters are daily sediment and water temperatures.

1.5 Discussion

None given.

1.6 Related Data Sets

BOREAS TGB01 CH4 Tower flux data over NSA

BOREAS TGB-01 CO2 and CH4 Chamber Flux data over the NSA

BOREAS TGB-03 NEE and air and water temperature data over the NSA Fen

BOREAS TGB-03 CO2 and CH4 Chamber Flux data over the NSA

BOREAS TGB-05 CO, CO2, and CH4 Chamber Flux data over the NSA

2.	Investigator(s)

2.1 Investigator(s) Name and Title

Dr. Nigel T. Roulet

Department of Geography

McGill University

Montreal

(514)-398-4945

(514)-398-7437 (fax)

roulet@felix.geog.mcgill.ca

2.2 Title of Investigation

Stores and Dynamics of Organic Matter in Boreal Ecosystems

2.3 Contact Information

Contact 1

Dr. Nigel T. Roulet

Department of Geography

McGill University

Montreal

(514)-398-4945

(514)-398-7437 (fax)

roulet@felix.geog.mcgill.ca

Contact 2

Jeffrey A. Newcomer

Raytheon STX Corporation

NASA/GSFC

Greenbelt, MD

(301) 286-7858

Jeffrey.Newcomer@gsfc.nasa.gov

3. Theory of Measurements

None given.

4.	Equipment

4.1 Sensor/Instrument Description

4.1.1 Collection Environment

Water and sediment temperatures were determined.

4.1.2 Source/Platform

Ground.

4.1.3 Source/Platform Mission Objectives

The mission objective was to determine the water and sediment temperatures over at the NSA-BP.

4.1.4 Key Variables

The key variables measured were the water and sediment temperatures at specific depths.

4.1.5 Principles of Operation

None given.

4.1.6 Sensor/Instrument Measurement Geometry

Not applicable.

4.1.7 Manufacturer of Sensor/Instrument

None given.

4.2 Calibration

None given.

4.2.1 Specifications

4.2.1.1 Tolerance

None given.

4.2.2 Frequency of Calibration

None given.

4.2.3 Other Calibration Information

None given.

5. Data Acquisition Methods

None given.

6.	Observations

6.1	Data Notes

BOREAS Information System (BORIS) staff compiled the information that were available to create this document.

6.2 Field Notes

None given.

7. Data Description

7.1 Spatial Characteristics

7.1.1 Spatial Coverage

The North American Datum of 1983 (NAD83) coordinates of the site are:

NSA-9BP-FLXTR:  55.84225° N, 98.02747° W

7.1.2 Spatial Coverage Map

Not available.

7.1.3 Spatial Resolution

These are point source measurements.

7.1.4 Projection

Not applicable.

7.1.5 Grid Description

Not applicable.

7.2 Temporal Characteristics

7.2.1 Temporal Coverage

The data were collected from May to September 1994.

7.2.2 Temporal Coverage Map

Not applicable.

7.2.3 Temporal Resolution

During optimal conditions, the temperatures were recorded hourly.

7.3 Data Characteristics

Sample data format shown in the companion data definition file (tgb4wsed.def).

7.4 Sample Data Record

Sample data format shown in the companion data definition file (tgb4wsed.def).

8. Data Organization

8.1 Data Granularity

All of the Water and Sediment Temperature data over the NSA-BP are contained in one data set.

8.2 Data Format(s)

The data file contains numerical and character fields of varying length separated by commas. The character fields are enclosed with single apostrophe marks. There are no spaces between the fields. Sample data format shown in the companion data definition file (tgb4wsed.def).

9. Data Manipulations

9.1 Formulae

None given.

9.1.1 Derivation Techniques and Algorithms

None given.

9.2 Data Processing Sequence

9.2.1 Processing Steps

None given.

9.2.2 Processing Changes

None given.

9.3 Calculations

9.3.1 Special Corrections/Adjustments

None given.

9.3.2 Calculated Variables

None given.

9.4 Graphs and Plots

None.

10. Errors

10.1 Sources of Error

None given.

10.2 Quality Assessment

10.2.1 Data Validation by Source

None given.

10.2.2 Confidence Level/Accuracy Judgment

None given.

10.2.3 Measurement Error for Parameters

None given.

10.2.4 Additional Quality Assessments

None given.

10.2.5 Data Verification by Data Center

Data were examined for general consistency and clarity and available information was compiled into this document.

11. Notes

11.1 Limitations of the Data

None given.

11.2 Known Problems with the Data

None given.

11.3 Usage Guidance

None given.

11.4 Other Relevant Information

None given.

12. Application of the Data Set

None given.

13. Future Modifications and Plans

This data set is in its final format.

14. Software

14.1 Software Description

None given.

14.2 Software Access

None given.

15.   Data Access

15.1  Contact for Data Center/Data Access Information

These BOREAS data are available from the Earth Observing System Data and Information System (EOS-DIS) Oak Ridge National Laboratory (ORNL) Distributed Active Archive Center (DAAC). The BOREAS contact at ORNL is:

ORNL DAAC User Services

Oak Ridge National Laboratory

(865) 241-3952

ornldaac@ornl.gov

ornl@eos.nasa.gov

15.2  Procedures for Obtaining Data

BOREAS data may be obtained through the ORNL DAAC World Wide Web site at http://www-eosdis.ornl.gov/ or users may place requests for data by telephone, electronic mail, or fax

15.3  Output Products and Availability

Requested data can be provided electronically on the ORNL DAAC's anonymous FTP site or on various media including, CD-ROMs, 8-MM tapes, or diskettes.

The complete set of BOREAS data CD-ROMs, entitled "Collected Data of the Boreal Ecosystem-Atmosphere Study", edited by Newcomer, J., et al., NASA, 1999, are also available.

16. Output Products and Availability

16.1 Tape Products

None.

16.2 Film products

None.

16.3 Other Products

Comma separated ASCII files.

17. References

17.1 Platform/Sensor/Instrument/Data Processing Documentation

None.

17.2 Journal Articles and Study Reports

Sellers, P. and F. Hall. 1994. Boreal Ecosystem-Atmosphere Study: Experiment Plan. Version 1994-3.0, NASA BOREAS Report (EXPLAN 94).

Sellers, P. and F. Hall. 1996. Boreal Ecosystem-Atmosphere Study: Experiment Plan. Version 1996-2.0, NASA BOREAS Report (EXPLAN 96).

Sellers, P., F. Hall, and K.F. Huemmrich. 1996. Boreal Ecosystem-Atmosphere Study: 1994 Operations. NASA BOREAS Report (OPS DOC 94).

Sellers, P., F. Hall, and K.F. Huemmrich. 1997. Boreal Ecosystem-Atmosphere Study: 1996 Operations. NASA BOREAS Report (OPS DOC 96).

Sellers, P.J., F.G. Hall, R.D. Kelly, A. Black, D. Baldocchi, J. Berry, M. Ryan, K.J. Ranson, P.M. Crill, D.P. Lettenmaier, H. Margolis, J. Cihlar, J. Newcomer, D. Fitzjarrald, P.G. Jarvis, S.T. Gower, D. Halliwell, D. Williams, B. Goodison, D.E. Wickland, and F.E. Guertin. 1997. BOREAS in 1997: Experiment overview, scientific results, and future directions. Journal of Geophysical Research 102(D24):28,731-28,769.

Sellers, P., F. Hall, H. Margolis, B. Kelly, D. Baldocchi, G. den Hartog, J. Cihlar, M.G. Ryan, B. Goodison, P. Crill, K.J. Ranson, D. Lettenmaier, and D.E. Wickland. 1995. The boreal ecosystem-atmosphere study (BOREAS): an overview and early results from the 1994 field year. Bulletin of the American Meteorological Society. 76(9):1549-1577.

17.3 Archive/DBMS Usage Documentation

None.

18. Glossary of Terms

None.

19. List of Acronyms

AES     - Atmospheric Environment Services

BOREAS  - BOReal Ecosystem-Atmosphere Study

BORIS   - BOREAS Information System

BP      - Beaver Pond

CMDL    - Climate Monitoring and Diagnostics Laboratory

DAAC    - Distributed Active Archive Center

ECD     - Electron Capture Detector

EOS     - Earth Observing System

EOSDIS  - EOS Data and Information System

FID     - Flame Ionization Detector

GC      - Gas Chromatograph

GSFC    - Goddard Space Flight Center

NASA    - National Aeronautics and Space Administration

NSA     - Northern Study Area

OBS     - Old Black Spruce

ORNL    - Oak Ridge National Laboratory

PANP    - Prince Albert National Park

SSA     - Southern Study Area

TE      - Terrestrial Ecology

TCD     - Thermal Conductivity Detector

TGB     - Trace Gas Biogeochemistry

URL     - Uniform Resource Locator

20. Document Information

20.1 Document Revision Date

Written:  10-Aug-1998

Last Updated:  05-May-1999

20.2 Document Review Date(s)

BORIS Review:  04-May-1999

Science Review:

20.3 Document ID

20.4 Citation

20.5 Document Curator

20.6 Document URL

Keywords

Methane flux

Carbon dioxide flux

Trace Gas

Water temperature

Sediment temperature