BOREAS HYD-08 DEM Data over the NSA-MSA and SSA-MSA in the UTM Projection

Summary

These DEMs were produced from digitized contours at a cell resolution of 100 meters.  Vector contours of the area were used as input to a software package that interpolates between contours to create a DEM representing the terrain surface.  The vector contours had a contour interval of 25 feet.  The data cover the BOREAS MSAs of the SSA and NSA and are given in a UTM map projection.  The data are stored in binary, image format files.

Note that the binary files of this data set on the BOREAS CD-ROMs have been compressed using the Gzip program.  See section 8.2 for details.

Table of Contents

*  1 Data Set Overview

*  2 Investigator(s)

*  3 Theory of Measurements

*  4 Equipment

*  5 Data Acquisition Methods

*  6 Observations

*  7 Data Description

*  8 Data Organization

*  9 Data Manipulations

*  10 Errors

*  11 Notes

*  12 Application of the Data Set

*  13 Future Modifications and Plans

*  14 Software

*  15 Data Access

*  16 Output Products and Availability

*  17 References

*  18 Glossary of Terms

*  19 List of Acronyms

*  20 Document Information

1. Data Set Overview

1.1 Data Set Identification

BOREAS HYD-08 DEM Data over the NSA-MSA and SSA-MSA in the UTM Projection

1.2 Data Set Introduction

These data are provided as part of the BOReal Ecosystem-Atmosphere Study (BOREAS) Staff Science Geographic Information System (GIS) Data Collection Program, which included the collection of pertinent map data, in both hard copy and digital form.

1.3 Objective/Purpose

The objective of these Digital Elevation Models (DEMs) is to provide the BOREAS investigators with a data product that characterizes the topography of the Northern Study Area (NSA) and Southern Study Area (SSA) Modeling Sub-Areas (MSAs).  These data are to be used for modeling purposes.

1.4 Summary of Parameters

Elevation above mean sea level in meters.

1.5 Discussion

The input vector data were acquired through the Canadian Centre for Remote Sensing (CCRS) from the National Topographical Data Base (NTDB) in Standard Interchange Format (SIF).  The vector data were digitized from 1:50,000-scale topographic maps and had a contour interval of 25 feet.  The BOREAS HYD-08 team gridded the data into a Universal Transverse Mercator (UTM) projection.

1.6 Related Data Sets

BOREAS Regional DEM in Raster Format and AEAC Projection

BOREAS DEM Data over the NSA-MSA and SSA-MSA in the AEAC Projection

2. Investigator(s)

2.1 Investigator(s) Name and Title

Dr. L.E. Band, Professor

2.2 Title of Investigation

Simulation of Boreal Ecosystem Carbon and Water Budgets: Scaling from Local to Regional Extents

2.3 Contact Information

Contact 1

-----------

Xuewen Wang

Dept. Geography, U. Toronto

Toronto, Ontario

(416) 978-5070

wangx@esker.geog.utoronto.ca

Contact 2

-----------

L.E. Band

Dept. Geography, U. Toronto

Toronto, Ontario

(416) 978-3375

lband@eos.geog.utoronto.ca

Contact 3

-----------

David Knapp

NASA/GSFC

Greenbelt, MD

(301) 286-1424

(301) 286-0239 (fax)

David.Knapp@gsfc.nasa.gov

3. Theory of Measurements

The user is referred to the NTDB to obtain information about the processes used to create the vector contour data.

4. Equipment

4.1 Sensor/Instrument Description

Unknown.

4.1.1 Collection Environment

Unknown.

4.1.2 Source/Platform

Unknown.

4.1.3 Source/Platform Mission Objectives

Unknown.

4.1.4 Key Variables

Unknown.

4.1.5 Principles of Operation

Unknown.

4.1.6 Sensor/Instrument Measurement Geometry

Unknown.

4.1.7 Manufacturer of Sensor/Instrument

Unknown.

4.2 Calibration

Unknown.

4.2.1 Specifications

Unknown.

4.2.1.1 Tolerance

Unknown.

4.2.2 Frequency of Calibration

Unknown.

4.2.3 Other Calibration Information

Unknown.

5. Data Acquisition Methods

The data were acquired from the NTDB and received from CCRS.  The data came in SIF, digitized from 1:50,000-scale topographic maps.  These vector contour data were used by the HYD-08 team to produce the DEMs in this data set.

6. Observations

6.1 Data Notes

Unknown.

6.2 Field Notes

Unknown.

7. Data Description

7.1 Spatial Characteristics

7.1.1 Spatial Coverage

NSA:

The image area that was modeled covers an area that is approximately 54 km x 37 km.  This area includes areas just northwest of Thompson, extending as far south as Nelson House, Manitoba.

The North American Datum 1927 (NAD27) corners of the data set are as follows.

The following UTM coordinates are in UTM zone 14.

UTM

Corner        Easting   Northing     Longitude   Latitude

---------------------------------------------------------------

Northwest        503100    6212100     98.95022W   56.05600N

Northeast        556900    6212100     98.08645W   56.05263N

Southwest        503100    6175500     98.95064W   55.72715N

Southeast        556900    6175500     98.09414W   55.72382N

SSA:

The image area that was modeled covers an area that is approximately 54 km x 44 km.  This area is located northeast of Prince Albert, Saskatchewan.

The NAD27 corners of the data set are as follows.

The following UTM coordinates are in UTM zone 13.

UTM

Corner        Easting   Northing     Longitude   Latitude

---------------------------------------------------------------

Northwest        484800    5993800    105.23240W   54.09410N

Northeast        538300    5993800    104.41442W   54.09290N

Southwest        484800    5949500    105.23020W   53.69594N

Southeast        538300    5949500    104.41996W   53.69475N

7.1.2 Spatial Coverage Map

Not available.

7.1.3 Spatial Resolution

These data were gridded in the UTM projection to a cell size of 100 meters in both the X and Y directions.

7.1.4 Projection

UTM zone 13 under NAD27.

7.1.5 Grid Description

The data are gridded in the UTM projection (zone 14 in the NSA, zone 13 in the SSA) at a cell size of 100 meters in both the X and Y directions.

7.2 Temporal Characteristics

7.2.1 Temporal Coverage

Most of the elevation data from which the DEM was produced were collected in the 1970s or 1980s.

7.2.2 Temporal Coverage Map

Not available.

7.2.3 Temporal Resolution

These elevations represent the state of the terrain at a point in time.  Most of the elevation data from which the DEM was produced were collected in the 1970s or 1980s.

7.3 Data Characteristics

7.3.1 Parameter/Variable

Elevation above mean sea level

7.3.2 Variable Description/Definition

Elevation above mean sea level - The vertical distance between a plane at mean sea level and a parallel plane intersecting the given location.

7.3.3 Unit of Measurement

Meters.

7.3.4 Data Source

The HYD-08 team received the original data from CCRS, who acquired them from the NTBD.

7.3.5 Data Range

Not available.

7.4 Sample Data Record

Not applicable to binary image data.

8. Data Organization

8.1 Data Granularity

The smallest amount of data that can be obtained from this data set is the entire data set.

8.2 Data Format(s)

8.2.1 Uncompressed Data Files

This data product contains the following three files:

File 1: American Standard Code for Information Interchange (ASCII) Header File listing the files that are on the tape.  The file contains 9 records of 80 bytes each.

File 2: DEM data file for the NSA.  This is a binary file containing 1,076 bytes in each of 366 records.  Each binary record is a line of the image file and contains 538 2-byte (16-bit) values stored as low-order byte first.  Each binary value is the mean elevation above sea level of the location in meters.

File 3: DEM data file for the SSA.  This is a binary file containing 1,070 bytes in each of 443 records.  Each binary record is a line of the image file and contains 535 2-byte (16-bit) values stored as low-order byte first.  Each binary value is the mean elevation above sea level of the location in meters.

8.2.2 Compressed CD-ROM Files

On the BOREAS CD-ROMs, file 1 is stored as ASCII text; however, files 2 and 3 have been compressed with the Gzip compression program (file name *.gz).  These data have been compressed using gzip version 1.2.4 and the high compression (-9) option (Copyright (C) 1992-1993 Jean-loup Gailly).  Gzip (GNU zip) uses the Lempel-Ziv algorithm (Welch, 1994) used in the zip and PKZIP programs. The compressed files may be uncompressed using gzip (-d option) or gunzip.  Gzip is available from many websites (for example, ftp site prep.ai.mit.edu/pub/gnu/gzip-*.*) for a variety of operating systems in both executable and source code form.  Versions of the decompression software for various systems are included on the CD-ROMs.

9. Data Manipulations

9.1 Formulae

9.1.1 Derivation Techniques and Algorithms

The Topog software package was used to interpolate between contours and create these DEMs.  Any details beyond this information is unknown.

9.2 Data Processing Sequence

9.2.1 Processing Steps

HYD-08 used the Topog software to interpolate elevations between the contours.

BOREAS Information System (BORIS) personnel processed the data by:

1)  Visually reviewing the data on a display system.

2)  Inventorying the data in the online data base.

3)  Documenting the data contents.

4) Copy the ASCII and compress the binary files for release on CD-ROM.

9.2.2 Processing Changes

None.

9.3 Calculations

9.3.1 Special Corrections/Adjustments

None.

9.3.2 Calculated Variables

None.

9.4 Graphs and Plots

None.

10. Errors

10.1 Sources of Error

The Topog program interpolates the values to grid cells from vector and point data (digitized contours). Errors occur where the original vector data are too sparse spatially, particularly in flat lowland areas.

10.2 Quality Assessment

10.2.1 Data Validation by Source

See Section 10.1.

10.2.2 Confidence Level/Accuracy Judgment

See Section 10.1.

10.2.3 Measurement Error for Parameters

See Section 10.1.

10.2.4 Additional Quality Assessments

See Section 10.1.

10.2.5 Data Verification by Data Center

BORIS Staff visually reviewed the images to verify that they did appear to represent DEMs without any obvious anomalies.  The only quantitative assessment made was to see that the minimum and maximum elevation values in the raster file approximated those shown on topographic maps of the area.

11. Notes

11.1 Limitations of the Data

Elevation variations exist within the lakes, especially large lakes, as explained in Section 10.1.

11.2 Known Problems with the Data

Elevation variations exist within the lakes, especially large lakes, as explained in Section 10.1.

11.3 Usage Guidance

Elevation variations exist within the lakes, especially large lakes, as explained in Section 10.1.

Before uncompressing the Gzip files on CD-ROM, be sure that you have enough disk space to hold the uncompressed data files.  Then use the appropriate decompression program provided on the CD-ROM for your specific system.

11.4 Other Relevant Information

None.

12. Application of the Data Set

The data can be used to perform analyses of terrain and related effects on hydrology and vegetation.

13. Future Modifications and Plans

None.

14. Software

14.1 Software Description

TOPOG Version 5.0

Division of Water Resources, CSIRO

Canberra, Australia

Gzip (GNU zip) uses the Lempel-Ziv algorithm (Welch, 1994) used in the zip and PKZIP commands.

14.2 Software Access

Contact Division of Water Resources, CSIRO

Canberra, Australia

Gzip is available from many websites across the net (for example) ftp site prep.ai.mit.edu/pub/gnu/gzip-*.*) for a variety of operating systems in both executable and source code form. Versions of the decompression software for various systems are included on the CD-ROMs.

15. Data Access

15.1 Contact Information

Primary contact:

Ms. Beth McCowan

BOREAS Data Manager

NASA/GSFC

Greenbelt, Maryland

(301) 286-4005

(301) 286-0239 (fax)

beth@ltpmail.gsfc.nasa.gov

15.2 Data Center Identification

See Section 15.l

.

15.3 Procedures for Obtaining Data

Users may place requests by telephone, electronic mail, or fax.

15.4 Data Center Status/Plans

The HYD-08 DEM data are available from the Earth Observing System Data and Information System (EOSIDS) Oak Ridge National Laboratory (ORNL) Distributed Active Archive Center (DAAC).

The BOREAS contact at ORNL is:

ORNL DAAC User Services

Oak Ridge National Laboratory

Oak Ridge, TN

(423) 241-3952

ornldaac@ornl.gov

ornl@eos.nasa.gov

16. Output Products and Availability

16.1 Tape Products

The DEM data can be made available on 8-mm, Digital Archive Tape (DAT), or 9-track tapes at 6250 or 1600 Bytes Per Inch (BPI).

16.2 Film Products

None.

16.3 Other Products

These data are available on the BOREAS CD-ROM series.

17. References

17.1 Platform/Sensor/Instrument/Data Processing Documentation

Topog User Guide (Version 5.0) 1994. Division of Water Resources, CSIRO. Canberra, Australia.

Welch, T.A. 1984, A Technique for High Performance Data Compression, IEEE Computer, Vol. 17, No. 6, pp. 8 - 19.

17.2 Journal Articles and Study Reports

Sellers, P. and F. Hall. 1994. Boreal Ecosystem-Atmosphere Study: Experiment Plan. Version 1994-3.0, NASA BOREAS Report (EXPLAN 94).

Sellers, P.and F. Hall. 1996. Boreal Ecosystem-Atmosphere Study: Experiment Plan. Version 1996-2.0, NASA BOREAS Report (EXPLAN 96).

Sellers, P., F. Hall and K.F. Huemmrich. 1996. Boreal Ecosystem-Atmosphere Study: 1994 Operations. NASA BOREAS Report (OPS DOC 94).

Sellers, P., F. Halland K.F. Huemmrich. 1997. Boreal Ecosystem-Atmosphere Study: 1996 Operations. NASA BOREAS Report (OPS DOC 96).

Sellers, P., F. Hall, H. Margolis, B. Kelly, D. Baldocchi, G. den Hartog, J. Cihlar, M.G. Ryan, B. Goodison, P. Crill, K.J. Ranson, D. Lettenmaier, and D.E. Wickland. 1995. The boreal ecosystem-atmosphere study (BOREAS): an overview and early results from the 1994 field year. Bulletin of the American Meteorological Society. 76(9):1549-1577.

Sellers, P. and F. Hall. 1997. BOREAS Overview Paper. JGR Special Issue (in press).

17.3 Archive/DBMS Usage Documentation

None.

18. Glossary of Terms

None.

19. List of Acronyms

ASCII   - American Standard Code for Information Interchange

BOREAS  - BOReal Ecosystem-Atmosphere Study

BORIS   - BOREAS Information System

BPI     - Bytes Per Inch

CCRS    - Canadian Centre for Remote Sensing

CD-ROM  - Compact Disk-Read-Only-Memory

DAAC    - Distributed Active Archive Center

DAT     - Digital Archive Tape

DEM     - Digital Elevation Model

EOS     - Earth Observing System

EOSDIS  - EOS Data and Information System

GSFC    - Goddard Space Flight Center

MSA     - Modeling Sub-Area

NAD27   - North American Datum of 1927

NASA    - National Aeronautics and Space Administration

NSA     - Northern Study Area

NTDB    - National Topographic Data Base

ORNL    - Oak Ridge National Laboratory

PANP    - Prince Albert National Park

SIF     - Standard Interchange Format

SSA     - Southern Study Area

URL     - Uniform Resource Locator

UTM     - Universal Transverse Mercator

20. Document Information

20.1 Document Revision Dates

Written:  03-Nov-1994

Last Updated:  26-Feb-1998

20.2 Document Review Dates

BORIS Review:    05-Jun-1997

Science Review:

20.3 Document ID

20.4 Citation

These data originated as vector data from CCRS.  This data product was gridded from the original vector data by the BOREAS Science Team HYD-8, led by Prof. L.E. Band at the University of Toronto.

20.5 Document Curator

20.6 Document URL

Keywords

GIS

DEM

ELEVATION