BOREAS RSS-20 POLDER Radiance Images from the NASA C-130

Summary

These data are a subset of images collected by the POLDER instrument over tower sites in the BOREAS study areas during the IFCs in 1994.  The POLDER images presented here from the NASA/Ames C-130 aircraft are made available for illustration purposes only.  The data are stored in binary image-format files.

Note that some of the data files on the BOREAS CD-ROMs have been compressed using the Gzip program.  See Section 8.2 for details.

Table of Contents

*  1 Data Set Overview

*  2 Investigator(s)

*  3 Theory of Measurements

*  4 Equipment

*  5 Data Acquisition Methods

*  6 Observations

*  7 Data Description

*  8 Data Organization

*  9 Data Manipulations

*  10 Errors

*  11 Notes

*  12 Application of the Data Set

*  13 Future Modifications and Plans

*  14 Software

*  15 Data Access

*  16 Output Products and Availability

*  17 References

*  18 Glossary of Terms

*  19 List of Acronyms

*  20 Document Information

1. Data Set Overview

1.1 Data Set Identification

BOREAS RSS-20 POLDER Radiance Images from the NASA C-130

1.2 Data Set Introduction

POLarization and Directionality of Earth Reflectances (POLDER) is an instrument that measures Bidirectional Reflectance Distribution Function (BRDF) and Bidirectional Polarization Distribution Function (BPDF) of terrestrial surfaces in several visible and near-infrared spectral bands.  The instrument scanned several surface types (pine, spruce, fen, and others) in the BOReal Ecosystem-Atmosphere Study (BOREAS) study areas during the various Intensive Field Campaigns (IFCs) in 1994.  Single-point BRDF measurements were acquired either from the National Aeronautics and Space Administration (NASA) C-130 aircraft or from a NASA helicopter. POLDER images acquired from the C-130 are made available for illustration purposes.

1.3 Objective/Purpose

The objective of this investigation was to characterize the bidirectional reflectance properties of different cover types in boreal forests over several seasons (IFC-1, -2, and 3). This characterization can then be used to retrieve biophysical parameters such as Leaf Area Index (LAI), chlorophyll content, and structural canopy parameters, either through the use of semiempirical relations between reflectances and biophysical parameters or through the inversion of a BRDF radiative transfer model. The overall goal is to establish methodologies of monitoring the ecological state of the boreal forest using remote sensing techniques.

1.4 Summary of Parameters

This data set contains POLDER images acquired from the C-130 at approximately 5500 m over the various tower sites.

1.5 Discussion

Warning: The C-130 POLDER images are given as a qualitative information only.  Although the measurements have been calibrated, no geometric correction has been applied.

1.6 Related Data Sets

BOREAS RSS-01 PARABOLA Surface Reflectance and Transmittance Data

BOREAS RSS-02 Level-1b ASAS Imagery: At-sensor Radiance in BSQ Format

BOREAS RSS-03 Helicopter-Mounted MMR Reflectance Data

BOREAS RSS-11 Airborne Tracking Sun Photometer Data

BOREAS RSS-20 POLDER BRDF Measurements of Tower Flux Sites

2. Investigator(s)

2.1 Investigator(s) Name and Title

Dr. Marc Leroy, Dr. François-Marie Bréon, Patrice Bicheron, Olivier Hautecoeur

2.2 Title of Investigation

Airborne Remote Sensing Measurements with the POLDER Instrument

2.3 Contact Information

Contact 1

-------------

Dr. Marc Leroy

Centre d'Etudes Spatiales de la Biosphère (CESBIO)

Toulouse, France

+33 5 61 55 85 14

+33 5 61 55 85 00 (fax)

Marc.Leroy@cesbio.cnes.fr

Contact 2

----------------

Dr. François-Marie Bréon

Laboratoire de Modélisation du climat et de l'Environnement

Gif sur Yvette, France

+33 1 69 08 94 55

+33 1 69 08 77 16 (fax)

fmbreon@cea.fr

Contact 3

--------------

Jaime Nickeson

Raytheon ITSS

NASA/GSFC

Greenbelt, MD

(301) 286-3373

(301) 286-0239 (fax)

Jaime.Nickeson@gsfc.nasa.gov

3. Theory of Measurements

POLDER is an optical sensor designed to observe the surface reflectance in visible and near-infrared bands.  Its main characteristic is that it can observe an area from various directions.  POLDER has a wide field-of-view (FOV) lens with ± 51° along-track and ± 43° cross-track viewing, and a charge-coupled device (CCD) array detector to collect images.

From the NASA Ames Research Center (ARC) C-130 aircraft at an altitude of approximately 5500 m, the surface cannot be considered homogeneous. POLDER's capacity to observe an area from various view angles is used to constitute complete BRDF with the successive images acquired along different flight axes over the experimental site.

4. Equipment

4.1 Sensor/Instrument Description

4.1.1 Collection Environment

It is mandatory to operate POLDER only under totally clear sky conditions, so that the distribution of irradiance does not change from one measurement to the next, and so that calculation of reflectances in absolute units from radiances is possible.

4.1.2 Source/Platform

During IFC-1 and IFC-2, the POLDER instrument was installed alternatively on the C-130 aircraft, or on the helicopter.  During IFC-3, the instrument flew only on the helicopter.  POLDER C-130 data were acquired only in the Southern Study Area (SSA) (Prince Albert).

4.1.3 Source/Platform Mission Objectives

The POLDER mission objective was to collect multiangle and multispectral bidirectional reflectance data over flux tower and auxiliary sites to study the boreal forest canopy.

4.1.4 Key Variables

POLDER measures multispectral radiance in the visible and near-infrared domain as a function of Sun-view geometry.

4.1.5 Principles of Operation

The POLDER optical system consists of a telecentric lens, a filter wheel, and a CCD array as a detector. The light is almost vertically incident on the filter wheel after passing the telecentric lens. The CCD array (288 x 384 elements) can collect 2-D images. The filter wheel contains 10 slots for spectral filters and polarizers. The first channel is reserved for dark current measurement, while the others allow measurements in five spectral bands (443, 550, 670, 864, and 910 nm). Two spectral bands (443 and 864 nm) are associated with three polarized filters oriented by steps of 60°. A 10-channel image, corresponding to the 10 positions of the filter wheel, is collected within 3 seconds.  Each image acquisition is repeated every 10 seconds.

The POLDER optical system was installed on the C-130 aircraft in the forward bay.  Aircraft position and attitude parameters provided by the onboard navigation system were recorded by POLDER electronics subsystem for data postprocessing.  Typical flight altitude was 5500 m.  Flight lines were designed on each site to collect images in the principal, perpendicular, and 45° solar planes.

4.1.6 Sensor/Instrument Measurement Geometry

The long axis of the CCD array was set parallel to the aircraft's longitudinal axis. An inclinometer was used to record the initial bias between the optical axis and true nadir.

4.1.7 Manufacturer of Sensor/Instrument

The instrument was designed and manufactured by Laboratoire d'Optique Atmosphérique (LOA), USTL, 59655 Villeneuve d’Ascq Cedex, France.

4.2 Calibration

Radiometric calibration data were acquired at LOA by J.-Y. Balois before and after the BOREAS experiment (11-May-1994 and 24-Oct-1994) using a calibrated integration sphere. The whole exit port of the integration sphere is used to derive the equalization coefficients  (see definition in Section 9.2.1). For absolute calibration, the exit port is reduced by a diaphragm to illuminate only a small circular area in the center of the CCD array. Readings of 15 x 15 pixel window are corrected for dark current and averaged to obtain the absolute calibration coefficients  (see Section 9.2.1).

Other calibration experiments were made during the BOREAS experiment using a 30-inch (0.76 m) diameter portable hemisphere that is owned and operated by NASA GSFC. It was made available to the Remote Sensing Science (RSS)-20 team by Brian Markham and John Schaffer from NASA GSFC. The POLDER sensor was calibrated at the airport when POLDER was installed in the C-130 aircraft on (27-May-1994 and 21-Jul-1994).

There is a good agreement between the LOA calibration and the first insitu calibration results. The second in-situ calibration shows discrepancies greater than 10% for all channels. The reasons for such discrepancies are still unknown.

4.2.1 Specifications

The general specifications of calibration accuracy were 5% absolute accuracy, 3% interband relative calibration accuracy, and 2% multitemporal relative calibration accuracy.

4.2.1.1 Tolerance

A general rise of the sensitivity was noted between the two calibration experiments made at LOA: 8% in the blue,  3.5% in the green and in the red, 5.5% for the 864-nm channel, and 5% for the 910-nm channel. For subsequent processing, mean coefficients obtained at LOA are used.

4.2.2 Frequency of Calibration

The instrument is generally calibrated once before an experimental campaign and once after the campaign.

4.2.3 Other Calibration Information

Having the spectral radiance at the outport of the sphere or the hemisphere, knowing the sensitivity of the various filters and the spectral value of the solar exoatmospheric irradiance, the normalized radiance is computed using:

[Note: Equations created in MS Word do not appear in ASCII text format.         Please refer to the MS Word formatted guide document.]

L : spectral radiance (Wm-2sr-1µm-1) as a function of wavelength (li)

S : spectral sensitivity as a function of wavelength

E : spectral exoatmospheric solar irradiance (Wm-2µm-1) as a function of

wavelength

The normalized radiance is used (see Section 9.2.1) to derive the absolute

calibration coefficient .

5. Data Acquisition Methods

For the C-130 data, the onboard navigation system gives information on the viewing geometry of each pixel.  Therefore, the location and attitude data yield an approximate position of a given surface target in all POLDER images. There is a time lag of 10 seconds between each image acquisition sequence.  For a typical C-130 flight altitude and speed, an angular resolution of approximately 10 degrees is obtained.

6. Observations

6.1 Data Notes

None.

6.2 Field Notes

None.

7. Data Description

7.1 Spatial Characteristics

7.1.1 Spatial Coverage

The POLDER images were acquired over various tower site locations.  The North American Datum of 1983 (NAD83) coordinates are:

West     North      UTM        UTM     UTM

Site        Longitude  Latitude  Easting   Northing   Zone

-----       ---------  --------  -------   --------   ----

SSA Fen     104.61797  53.80206  525190.7  5961344.0   13

SSA OA      106.19779  53.62890  420821.8  5942678.0   13

SSA OBS     105.11779  53.98718  492306.1  5981879.0   13

SSA OJP     104.69203  53.91634  520257.0  5974035.0   13

SSA YJP     104.64527  53.87581  523350.7  5969540.0   13

7.1.2 Spatial Coverage Map

Not available.

7.1.3 Spatial Resolution

The pixel size is approximately 35 meters when POLDER is on the C-130.

7.1.4 Projection

Each image is supplied in its original geometry with no geometric rectification or registration performed.  Users will need to at least rotate the images for a coarse registration.  The images are nearly centered on the tower sites.

7.1.5 Grid Description

Not applicable.

7.2 Temporal Characteristics

7.2.1 Temporal Coverage

POLDER image data exist only for C-130 acquisitions taken from 26-May-1994 to 24-July-1994.  Most experiments took place in the morning, except the following: 21-July: OJP (around noon), YJP, Fen..

7.2.2 Temporal Coverage Map

Images from the C-130 exist for the following dates:

Site            IFC-1         IFC-2

----         -----------   ------------

Fen          07/24

OA           05/26,05/31

OBS          05/31,06/01   07/21

OJP          05/31,06/01   07/21, 07/24

YJP          06/01         07/21

7.2.3 Temporal Resolution

Most sites were visited more than once in 1994.

7.3 Data Characteristics

7.3.1 Parameter/Variable

Raw radiometric POLDER image data.

7.3.2 Variable Description/Definition

They are essentially normalized radiances.

7.3.3 Unit of Measurement

Unitless digital numbers.

7.3.4 Data Source

POLDER instrument mounted on the NASA C-130 Aircraft.

7.3.5 Data Range

None given.

7.4 Sample Data Record

Not applicable to image data.

8. Data Organization

8.1 Data Granularity

The smallest unit of data tracked by BORIS is a given image file.

8.2 Data Format(s)

8.2.1 Uncompressed Data Files

The image parameter is , a digital number proportional to the observed normalized radiance for the channels without polarizers (see Section 9.2).  The image data are stored in a Band Sequential (BSQ) format (9 bands, 288 lines by 384 pixels, 16 bits per pixel).

Bytes Per	Size

Description/Name    Format       Pixel    Npixels   Nlines	Nbands	(Bytes)

SSA-FEN_940724     Raw Binary      2	  384	     288	9	1990656

SSA-OA_940526      Raw Binary      2	  384	     288	9	1990656

SSA-OA_940531      Raw Binary      2	  384	     288	9	1990656

SSA-OBS_940531     Raw Binary      2	  384	     288	9	1990656

SSA-OBS_940601     Raw Binary      2	  384	     288	9	1990656

SSA-OBS_940721     Raw Binary      2	  384	     288	9	1990656

SSA-OJP_940531     Raw Binary      2	  384	     288	9	1990656

SSA-OJP_940601     Raw Binary      2	  384	     288	9	1990656

SSA-OJP_940721     Raw Binary      2	  384	     288	9	1990656

SSA-OJP_940724     Raw Binary      2	  384	     288	9	1990656

SSA-YJP_940601     Raw Binary      2	  384	     288	9	1990656

SSA-YJP_940721     Raw Binary      2	  384	     288	9	1990656

The table of the attitude parameters for these images follows:

Mean attitude parameters           Sun position

Site   Date     Hour      roll    pitch   heading   altitude   zenith   azimuth

----   ----     ----     ----    -----   -------   --------   ------   -------

FEN   940724  15:49:07    0.7     3.0      191.0    5645.2     49.3     114.3

OA    940526  16:47:03   -0.1     1.8       82.4    5482.44    41.8     127.7

OA    940531  15:31:45    0.4     2.6      263.2    5457.75    51.0     107.0

OBS   940531  17:19:52   -0.3     1.6      209.8    5489.75    37.3     139.5

OBS   940601  14:49:48    0.0     2.5      349.1    5552.54    53.4      98.6

OBS   940721  17:39:30   -0.4     1.1       16.8    5493.41    36.8     147.3

OJP   940531  16:27:49   -0.3     1.9      329.0    5461.41    42.9     123.4

OJP   940601  15:44:48   -0.2     2.3       68.0    5601.0     48.4     111.7

OJP   940721  18:27:14   -0.2     2.2      198.9    5558.03    33.9     166.7

OJP   940724  16:48:45   -1.6     1.4      229.0    5595.21    42.0     131.0

YJP   940601  15:53:55    0.1     1.4      194.0    5630.57    47.1     114.1

YJP   940721  19:25:35    0.1     2.3      331.2    5567.78    33.7     191.4

8.2.2 Compressed CD-ROM Files

On the BOREAS CD-ROMs, each of the 12 image files been compressed with the Gzip (GNU zip) compression program (file_name.gz).  These data have been compressed using gzip version 1.2.4 and the high compression (-9) option (Copyright (C) 1992-1993 Jean-loup Gailly).  Gzip uses the Lempel-Ziv algorithm (Welch, 1994) also used in the zip and PKZIP programs.  The compressed files may be uncompressed using gzip (with the -d option) or gunzip.  Gzip is available from many WWW sites (for example, the ftp site prep.ai.mit.edu/pub/gnu/gzip-*.*) for a variety of operating systems in both executable and source code form.  Versions of the decompression software for various systems are included on the CD-ROMs.

9. Data Manipulations

9.1 Formulae

See Section 9.2.

9.1.1 Derivation Techniques and Algorithms

See Section 9.2.

9.2 Data Processing Sequence

9.2.1 Processing Steps

9.2.1.1 Level 1 Images

The raw radiometric data are digital numbers noted , where i, j are indices of pixel location on the CCD matrix, k is the wavelength, and a is the polarizer number for spectral bands comprising three polarizers. For the other spectral bands, a is meaningless.  The processing from level 0 to level 1 data consists of the transformation of raw data into data proportional to normalized radiances , according to the equation:

[Note: Equations created in MS Word do not appear in ASCII text format.         Please refer to the MS Word formatted guide document.]

0

with

t0	reference exposure time, used in calibration : 100 ms

t	exposure time during operation

average of line j of dark current

calibration coefficient

relative sensitivity (high and low frequency) of instrumental (optics + CCD) transmission. It is normalized such that the local average of   at the matrix center equals 1.

sensitivity of absolute calibration to CCD temperature

CCD temperature during calibration

T	CCD temperature in operation

is a digital number proportional to the observed normalized radiance (for the channels without polarizers),  i.e.,

with

observed radiance (Wm-2sr-1µm-1) for pixel i, j in band k

exoatmospheric solar irradiance in band k (Wm-2µm-1).

For polarized bands, the aircraft displacement between successive channel acquisition must be taken into account to obtain a normalized spectral radiance from the three polarized channels

where (x,y) are surface coordinates that refer to CCD pixels coordinates (i,j) in each of the polarized channels viewing the same ground point (x,y).

The level 1 images provide data that for each band are equal to the right-hand side of the two previous equations.  They are essentially normalized radiances.

The following table summarizes the POLDER C-130 data acquisitions and sun and atmospheric conditions:

Sun zenith angle      Aerosol optical thickness

Site          Date           degrees        at 550 nm (total/below aircraft)

----          ----       ----------------    -------------------------------

Fen          24-Jul        44.4 - 49.3                0.080/0.020

03-May        38.4 - 42.8                0.130/0.055

OJP          01-Jun        48.4 - 51.4                0.095/0.050

21-Jul        33.8 - 35.0                0.120/0.095

24-Jul        40.5 - 43.3                0.095/0.020

26-May        39.4 - 41.8                0.070/0.025

01-Jun        44.0 - 47.0                0.095/0.050

YJP          21-Jul        35.5 - 37.2                0.115/0.090

31-May        35.5 - 37.4                0.135/0.070

OBS          01-Jun        53.5 - 56.4                0.060/0.030

21-Jul        33.4 - 33.7                0.115/0.090

9.2.2 Processing Changes

None.

9.3 Calculations

9.3.1 Special Corrections/Adjustments

Not applicable.

9.3.2 Calculated Variables

Radiance, and reflectance were calculated.

9.4 Graphs and Plots

None.

10. Errors

10.1 Sources of Error

For images and BRDF data, there is some uncertainty in the absolute calibration coefficient, as illustrated by the calibration tables shown above.  For the BRDF data, an additional source of error results from image registration.  In the processing, it is assumed that the position of the site is the same for all images of the sequence, which can induce an error in the location of less than 1 pixel.  These errors are lessened with the spatial averaging procedure.  The smoothing aspect of the BRDF data tends to show that the misregistration errors are not critical.

10.2 Quality Assessment

10.2.1 Data Validation by Source

The POLDER data have been tested against the 4-scale BRDF reflectance model (Leblanc et al., 1997) as well as against the PARABOLA data and the DART 3-D BRDF model (Gastellu-Etchegorry et al., 1997).

10.2.2 Confidence Level/Accuracy Judgment

The uncertainty associated with POLDER spectral reflectances values, taking into account only error in the absolute calibration coefficient, is approximately less than 0.005 for the visible channels and 0.01 for the near-infrared channel.  The confidence level in these measurements is good because of their reproducibility for different axes during the same flight.

10.2.3 Measurement Error for Parameters

Not available.

10.2.4 Additional Quality Assessments

The directional reflectances obtained with POLDER data corrected from atmospheric effects for the flux tower or auxiliary sites can be compared to similar data made by other instruments.

10.2.5 Data Verification by Data Center

BORIS staff has looked at some of the POLDER imagery from the C-130.  It appears that there are some registration problems between bands in some of the imagery.

11. Notes

11.1 Limitations of the Data

None.

11.2 Known Problems with the Data

Based on a visual review of the images by BORIS staff, it appears that there are some registration problems between bands in the imagery.

11.3 Usage Guidance

Not applicable.

11.4 Other Relevant Information

None.

12. Application of the Data Set

Data set used for BRDF model inversion and BRDF direct models cross-check.

13. Future Modifications and Plans

None.

14. Software

14.1 Software Description

None given.

14.2 Software Access

Raw data and processing software might be available upon request.  See Section 2.3.

15. Data Access

15.1 Contact Information

For BOREAS data and documentation please contact:

ORNL DAAC User Services

Oak Ridge National Laboratory

Oak Ridge, TN

Phone:  (423) 241-3952

Fax:    (423) 574-4665

E-mail:   or

15.2 Data Center Identification

Earth Observing System Data and Information System (EOSDIS)

Oak Ridge National Laboratory (ORNL)

Distributed Active Archive Center (DAAC) for Biogeochemical Dynamics

http://www-eosdis.ornl.gov/

15.3 Procedures for Obtaining Data

Users may obtain data directly through the ORNL DAAC online search and order system [http://www-eosdis.ornl.gov/] and the anonymous FTP site [ftp://www-eosdis.ornl.gov/data/] or by contacting User Services by electronic mail, telephone, or fax.

15.4 Data Center Status/Plans

The ORNL DAAC is the primary source for BOREAS field measurement, image, GIS, and hardcopy data products. The BOREAS CD-ROM and data referenced or listed in inventories on the CD-ROM are available from the ORNL DAAC.

16. Output Products and Availability

16.1 Tape Products

The image data are stored on 8 mm media as BSQ raw images (9 bands, 288 lines by 384 pixels, 16 bits per pixel).

16.2 Film Products

None.

16.3 Other Products

None.

17. References

17.1 Platform/Sensor/Instrument/Data Processing Documentation

Welch, T.A. 1984. A Technique for High Performance Data Compression. IEEE Computer, Vol. 17, No. 6, pp. 8-19.

17.2 Journal Articles and Study Reports

Bréon, F.M., V. Vanderbilt, M. Leroy, P. Bicheron, C.L. Walthall, and J.E. Kalshoven. 1997. Evidence of hot spot directional signature from airborne POLDER measurements. IEEE Transactions on Geoscience and Remote Sensing, Vol. 35, pp. 479-484.

Bicheron, P., M. Leroy, O. Hautecoeur, and F.M. Bréon. 1997.  Enhanced discrimination of boreal forest covers from airborne directional POLDER data. Journal of Geophysical Research, 102(D24):  29,517-29,528.

Deschamps, P.Y., F.M. Bréon, M. Leroy, A. Podaire, A. Bricaud, J.C. Buriez, G. Sèze. 1994. The POLDER mission: Instrument characteristics and scientific objectives. IEEE Transactions on Geoscience and Remote Sensing, 32, pp. 598-615.

Gastellu-Etchegorry J.P., P. Guillevic, F. Zagolski, V. Demarez, V. Trichon, D. Deering, and M. Leroy. 1997. Modelling BRDF and radiation regime of boreal and tropical forest. submitted to Remote Sensing of Environment.

Leblanc, S.G., P. Bicheron, J.M. Chen, M. Leroy, and J. Cihlar. 1997. Investigation of directional reflectance in boreal forests with an improved 4-scale model and airborne POLDER data, IEEE Transactions on Geoscience and Remote Sensing, (submitted).

Leroy, M. and F.M. Bréon. 1996. Surface reflectance angular signatures from airborne POLDER data. Remote Sensing of Environment, 57, pp. 97-107.

Leroy, M., Bicheron, P., and Hautecoeur, O. 1997. An algorithm of LAI and FAPAR retrieval to be used with spaceborne POLDER/ADEOS data. In 7th International Symposium - Physical Measurements and Signatures in Remote Sensing, Courchevel, France.

Sellers, P.and F. Hall. 1994. Boreal Ecosystem-Atmosphere Study: Experiment Plan. Version 1994-3.0, NASA BOREAS Report (EXPLAN 94).

Sellers, P.and F. Hall. 1996. Boreal Ecosystem-Atmosphere Study: Experiment Plan. Version 1996-2.0, NASA BOREAS Report (EXPLAN 96).

Sellers, P., F. Hall, and K.F. Huemmrich. 1996. Boreal Ecosystem-Atmosphere Study: 1994 Operations. NASA BOREAS Report (OPS DOC 94).

Sellers, P., F. Hall, and K.F. Huemmrich. 1997. Boreal Ecosystem-Atmosphere Study: 1996 Operations. NASA BOREAS Report (OPS DOC 96).

Sellers, P., F. Hall, H. Margolis, B. Kelly, D. Baldocchi, G. den Hartog, J. Cihlar, M.G. Ryan, B. Goodison, P. Crill, K.J.Ranson, D. Lettenmaier, and D.E. Wickland. 1995. The boreal ecosystem-atmosphere study (BOREAS): an overview and early results from the 1994 field year. Bulletin of the American Meteorological Society. 76(9):1549-1577.

Sellers, P.J., F.G. Hall, R.D. Kelly, A. Black, D. Baldocchi, J. Berry, H. Margolis, M. Ryan, J. Ranson, P.M. Crill, D.P. Lettenmeier, J. Cihlar, J. Newcomer, D. Halliwell, D. Fitzjarrald, P.G. Jarvis, S.T. Gower, D. Williams, B. Goodison, D.E. Wickland, and F.E. Guertin. 1997.  BOREAS in 1997: Scientific results, experiment overview and future directions.  Journal of Geophysical Research, 102(D24): 28,731-28,770.

17.3 Archive/DBMS Usage Documentation

None.

18. Glossary of Terms

None.

19. List of Acronyms

6S      - Second Simulation of the Satellite signal in the Solar system

ARC     - Ames Research Center

BOREAS  - BOReal Ecosystem-Atmosphere Study

BORIS   - BOREAS Information System

BPDF    - Bidirectional Polarization Distribution Function

BRDF    - Bidirectional Reflectance Distribution Function

BSQ     - Band Sequential

CCD     - Change Coupled Device

DAAC    - Distributed Active Archive Center

EOS     - Earth Observing System

EOSDIS  - EOS Data and Information System

FOV     - Field-of-View

GSFC    - Goddard Space Flight Center

IFC     - Intensive field Campaign

LAI     - Leaf Area Index

LOA     - Laboratoire d'Optique Atmospherique

NAD83   - North American Datum of 1983

NASA    - National Aeronautics and Space Administration

NSA     - Northern Study Area

OA      - Old Aspen

OBS     - Old Black Spruce

OJP     - Old Jack Pine

ORNL    - Oak Ridge National Laboratory

PANP    - Prince Albert National Park

POLDER  - POLarization and Directionality of Earth’s Reflectances

RSS     - Remote Sensing Science

SSA     - Southern Study Area

URL     - Uniform Resource Locator

UTM     - Universal Transverse Mercator

YJP     - Young Jack Pine

20. Document Information

20.1 Document Revision Date

Written: 12-Sep-1996

Updated: 07-May-1999

20.2 Document Review Date(s)

BORIS Review: 06-May-1999

Science Review:

20.3 Document ID

20.4 Citation

Acknowledge Marc Leroy and Patrice Bicheron (CESBIO, Toulouse), and François-Marie Bréon (LMCE, Saclay) for providing the POLDER data. Thank LOA (Lille) for providing the POLDER instrument. Cite relevant publications (see Section 17).

If using data from the BOREAS CD-ROM series, also reference the data as:

Leroy, Marc, Bréon, F. M.,  Bicheron, P., Hautecoeur, O., "Airborne

Remote Sensing Measurements with the POLDER Instrument" in Collected

Data of The Boreal Ecosystem-Atmosphere Study.  Eds. J. Newcomer, D.

Landis, S. Conrad, S. Curd, K. Huemmrich, D. Knapp, A.Morrell, J.

Nickeson, A. Papagno, D. Rinker, R. Strub, T. Twine, F. Hall, and P.

Sellers.  CD-ROM. NASA, 2000.

Also, cite the BOREAS CD-ROM set as:

Newcomer, J., D. Landis, S. Conrad, S. Curd, K. Huemmrich, D. Knapp, A. Morrell, J. Nickeson, A. Papagno, D. Rinker, R. Strub, T. Twine, F. Hall, and P. Sellers, eds. Collected Data of The Boreal Ecosystem-Atmosphere Study. CD-ROM. NASA, 2000.

20.5 Document Curator

20.6 Document URL

Keywords:

POLDER

Bidirectional Reflectance

Aircraft Sensors