BOREAS Level-3a Landsat TM Imagery: Scaled At-sensor Radiance in BSQ Format

Summary:

For BOREAS, the level-3a Landsat TM data, along with the other remotely sensed images, were collected in order to provide spatially extensive information over the primary study areas.  This information includes radiant energy, detailed land cover, and biophysical parameter maps such as FPAR and LAI.  Although very similar in content to the level-3s Landsat TM products, the level-3a images were created to provide users with a more usable BSQ format and to provide information that permitted direct determination of per-pixel latitude and longitude coordinates.  Geographically, the level-3a images cover the BOREAS NSA and SSA.  Temporally, the images cover the period of 22-Jun-1984 to 30-Jul-1996.  The images are available in binary, image-format files.

Table of Contents

*   1 Data Set Overview

*   2 Investigator(s)

*   3 Theory of Measurements

*   4 Equipment

*   5 Data Acquisition Methods

*   6 Observations

*   7 Data Description

*   8 Data Organization

*   9 Data Manipulations

*  10 Errors

*  11 Notes

*  12 Application of the Data Set

*  13 Future Modifications and Plans

*  14 Software

*  15 Data Access

*  16 Output Products and Availability

*  17 References

*  18 Glossary of Terms

*  19 List of Acronyms

*  20 Document Information

1. Data Set Overview

1.1 Data Set Identification

BOREAS Level-3a Landsat TM Imagery: Scaled At-sensor Radiance in BSQ Format

1.2 Data Set Introduction

The BOReal Ecosystem-Atmosphere Study (BOREAS) Staff Science effort covered those activities that were BOREAS community-level activities, or required uniform data collection procedures across sites and time. These activities included the acquisition of the relevant satellite data. Data from the Landsat Thematic Mapper (TM) instruments on the Landsat satellites were acquired by the Canada Centre for Remote Sensing (CCRS) and provided for use by BOREAS researchers.  BOREAS Information System (BORIS) and CCRS personnel subsequently processed the acquired images to the level-3a products described here.

1.3 Objective/Purpose

For BOREAS, the Landsat TM imagery, along with the other remotely sensed images, was collected in order to provide spatially extensive information over the primary study areas.  This information includes detailed land cover and biophysical parameter maps such as biomass, Fraction of Photosynthetically Active Radiation (FPAR), and Leaf Area Index (LAI).

The BORIS staff processed the seven-band level-3s and level-3p Landsat TM imagery to level-3a products.

1.4 Summary of Parameters

Landsat TM level-3a data in BORIS contain the following parameters:

Original image header information, image coordinates, gains and offsets for each band for at-sensor radiance derivations, georeferencing information summary, control point coordinates used to georeference the image, and image bands 1 - 7.

1.5 Discussion

Use and distribution of the level-3a Landsat TM images are subject to copyright restrictions.  CCRS and Radarsat International (RSI) granted permission to BOREAS to place a subset of the Landsat TM images on the BOREAS CD-ROM series.  The remaining images may not be available for public access.  Please see Sections 15 and 16 for further details.

BORIS staff created the Landsat TM level-3a imagery by:

1) Extracting pertinent header information from the level-3s or 3p image product and placing it in the level-3a American Standard Code for Information Interchange (ASCII) header file,

2) Reformatting the level-3s or -3p image data into a band sequential (BSQ) file on disk,

3) Reviewing the image bands for cloud cover and band quality,

4) Selecting control points to calculate an improved set of georeferencing coordinates,

5) Appending the georeferencing information to the level-3a ASCII header file,

6) Writing the ASCII header file and seven image bands to tape.

1.6 Related Data Sets

BOREAS Level-3s Landsat TM Imagery: Scaled At-sensor Radiance in LGSOWG Format

BOREAS Level-3b Landsat TM Imagery: At-sensor Radiance in BSQ Format

BOREAS Level-3p Landsat TM Imagery: Geocoded and Scaled At-sensor Radiance

BOREAS Level-3s SPOT Imagery: Scaled At-sensor Radiance in LGSOWG Format

2. Investigator(s)

2.1 Investigator(s) Name and Title

BOREAS Staff Science

2.2 Title of Investigation

BOREAS Staff Science Satellite Data Acquisition Program

2.3 Contact Information

Contact 1

----------

Jeffrey A. Newcomer

NASA/Goddard Sp. Fl. Ctr.

Greenbelt, MD

(301) 286-785

(301) 286-0239

Jeffrey.Newcomer@gsfc.nasa.gov

Contact 2

----------

Josef Cihlar

Canada Centre for Remote Sensing

Ottawa, Ontario

Canada

(613) 947-1265

Josef.Cihlar@geocan.emr.ca

3. Theory of Measurements

The Landsat series of satellites began with the Earth Resources Technology Satellite (ERTS) launched in July 1972. This satellite was renamed Landsat 1 in 1975 to reflect its primary use as a land resource observatory. Through its onboard instruments, Landsat monitors Earth's mountain ranges, deserts, forests, and crops by measuring the light waves they reflect.

The second generation of Landsat satellites (4 and 5) marked a significant advance in remote sensing through the addition of the more sophisticated TM sensor, with higher spectral and spatial resolution, and faster data processing at a highly automated data processing facility at the National Aeronautics and Space Administration (NASA) Goddard Space Flight Center (GSFC) in Greenbelt, MD.  For BOREAS, the CCRS receiving station in Prince Albert, Saskatchewan collected the raw data.  Processing of the raw data to the imagery used as input for the BOREAS level-3a processing was performed with the Geocoded Image Correction System (GICS; Friedel, 1992) at the CCRS facility in Ottawa

As Landsat's instrument mirrors scan Earth's surface, light enters the instrument optics, where it is focused on specially calibrated detector arrays. Onboard electronics encode the detector voltage as binary digits or bits. These digital image data are then relayed back to Earth to be processed into film and Computer-Compatible Tape (CCT) products which are subsequently used for Earth resources analysis.

4. Equipment

4.1 Sensor/Instrument Description

The TM sensor system records radiation from seven bands in the electromagnetic spectrum. It has a telescope that directs the incoming radiant flux obtained along a scan line through a scan line collector to the visible and near-infrared focal plane, or to the mid-infrared and thermal-infrared cooled focal plane. The detectors for the visible and near-infrared bands (1 to 4) are four staggered linear arrays, each containing 16 silicon detectors. The two mid-infrared detectors are 16 indium-antimonide cells in a staggered linear array, and the thermal-infrared detector is a four-element array of mercury-cadmium-telluride cells. The spectral regions, band widths, and primary use of each channel are given in the following table:

Channel  Wavelength (µm)                Primary Use

-------  ---------------  ------------------------------------------

1        0.451 -  0.521      Coastal water mapping, soil vegetation

differentiation, deciduous/coniferous

differentiation.

2        0.526 -  0.615      Green reflectance by healthy vegetation.

3        0.622 -  0.699      Chlorophyll absorption for plant species

differentiation.

4        0.771 -  0.905      Biomass surveys, water body delineation.

5        1.564 -  1.790      Vegetation moisture measurement, snow and cloud

differentiation.

6       10.450 - 12.460      Plant heat stress measurement, other thermal

mapping.

7        2.083 -  2.351      Hydrothermal mapping.

4.1.1 Collection Environment

The BOREAS Landsat TM level-3s and -3p images were acquired through the CCRS.  Radiometric corrections and systematic geometric corrections are applied to produce the images in a path-oriented, systematically corrected (level-3s) or precision-corrected (level-3p) form.  A full TM image contains 6920 pixels in each of 5728 lines (see Section 11.2).  Before any geometric corrections, the ground resolution is 30 m for bands 1, 2, 3, 4, 5, and 7 and 120 m for band 6 at nadir. The pixel values of the images can range from 0 to 255. This allows each pixel to be stored in a single-byte field.  The level-3s and level-3p images were processed through the CCRS GICS.  The Landsat satellite orbits Earth at an altitude of 705 km.

4.1.2 Source/Platform

Although the majority of the BOREAS Landsat TM imagery was acquired by the instrument onboard Landsat-5, some imagery was obtained with the TM sensor on the Landsat 4 platform.

4.1.3 Source/Platform Mission Objectives

The Landsat TM is designed to respond to and measure both reflected and emitted Earth surface radiation to enable the investigation, survey, inventory, and mapping of Earth's natural resources.

4.1.4 Key Variables

Reflected radiation, emitted radiation, temperature.

4.1.5 Principles of Operation

The TM is a scanning optical sensor operating in the visible and infrared wavelengths. It contains a scan mirror assembly that directly projects the reflected Earth radiation onto detectors arrayed in two focal planes. The TM achieves better image resolution, sharper color separation, and greater in-flight geometric and radiometric accuracy for seven spectral bands simultaneously than the previous generation sensor, the MultiSpectral Scanner (MSS). Data collected by the sensor are beamed back to ground receiving stations for processing.

4.1.6 Sensor/Instrument Measurement Geometry

The TM sensor depends on the forward motion of the spacecraft for the along-track scan and uses moving mirror assembly to scan in the cross-track direction (perpendicular to the spacecraft).  The instantaneous field-of-view (IFOV) for each detector from bands 1 - 5 and band 7 is equivalent to a 30-m square when projected to the ground at nadir; band 6 (the thermal infrared band) has an IFOV equivalent to a 120-m square at nadir.

4.1.7 Manufacturer of Sensor/Instrument

NASA GSFC

Greenbelt, MD 20771

Hughes Santa Barbara Remote Sensing (SBRS)

Goleta, CA.

4.2 Calibration

The internal calibrator, a flex-pivot-mounted shutter assembly, is synchronized with the scan mirror, oscillating at the same 7-Hz frequency. During the turnaround period of the scan mirror, the shutter introduces the calibration source energy and a black direct-current restoration surface into the 100-detector field-of-view (FOV).

The calibration signals for bands 1 - 5 and 7 are derived from three regulated tungsten-filament lamps. The calibration source for band 6 is a blackbody with three temperature selections, commanded from the ground. The method for transmitting radiation to the moving calibration shutter allows the tungsten lamps to provide radiation independently and to contribute proportionately to the illumination of all detectors.

4.2.1 Specifications

Radiometric

Band              Sensitivity [NE(dP)]*

----              --------------------

1                     0.8%

2                     0.5%

3                     0.5%

4                     0.5%

5                     1.0%

6                     0.5 K [NE(dT)]

7                     2.4%

Ground IFOV             30 m (Bands 1-5, 7)

120 m (Band 6)

Avg. altitude          699.6 Km

Data rate                 85 Mbps

Quantization levels      256

Orbit angle             8.15 degrees

Orbital nodal period   98.88 minutes

Scan width               185 km

Scan angle              14.9 degrees

Image overlap            7.6%

Note:  The radiometric sensitivities are the noise-equivalent (NE) reflectance differences for the reflective channels expressed as percentages [NE(dP)] and temperature differences for the thermal-infrared bands [NE(dT)] in Kelvins.

4.2.1.1 Tolerance

The TM channels were designed for a NE differential represented by the radiometric sensitivity shown in Section 4.2.1.

4.2.2 Frequency of Calibration

The absolute radiometric calibration between bands on the TM sensor is maintained by using internal calibrators located between the telescope and the detectors that are sampled at the end of a scan.

4.2.3 Other Calibration Information

Relative within-band radiometric calibration, to reduce "striping," is provided by a scene-based procedure called histogram equalization. Because of the absolute accuracy and relative precision of this calibration scheme, it is assumed that any changes in the optics of the primary telescope or the "effective radiance" from the internal calibrator lamps are insignificant in comparison to the changes in detector sensitivity and electronic gain and bias with time and that the scene-dependent sampling is sufficiently precise for the required within-scan destriping from histogram equalization.

Each TM reflective band and the internal calibrator lamps were calibrated prior to launch using lamps in integrating spheres that were in turn calibrated against lamps traceable to calibrated National Bureau of Standards lamps. The absolute radiometric calibration constants in the "short-term" and "long-term" parameter files used for ground processing were modified after launch if there was an inconsistency within or between bands, a change in the inherent dynamic range of the sensors, or a desire to make quantized and calibrated values from one sensor match those from another.

5. Data Acquisition Methods

The BOREAS Landsat TM level-3s and -3p images were acquired through the CCRS.  Radiometric corrections and systematic or precision geometric corrections are applied to produce the images in a path-oriented form.  A full TM image contains 6920 pixels in each of 5728 lines (see Section 11.2).  Before any geometric corrections, the ground resolution is 30 m for bands 1-5 and 7 and 120 m for band 6 at nadir. The pixel values of the images can range from 0 to 255. This allows each pixel to be stored in a single-byte field.

6. Observations

6.1 Data Notes

None.

6.2 Field Notes

Not applicable.

7. Data Description

7.1 Spatial Characteristics

7.1.1 Spatial Coverage

The BOREAS level-3a Landsat TM images cover the NSA and SSA.  The SSA and the NSA are located in the southwest and northeast portions of the overall region.  A full TM scene covers approximately 31,000 square kilometers.

The North American Datum of 1983 (NAD83) corner coordinates of the SSA are:

Latitude     Longitude

--------     ---------

Northwest    54.321 N     106.228 W

Northeast    54.225 N     104.237 W

Southwest    53.515 N     106.321 W

Southeast    53.420 N     104.368 W

The NAD83 corner coordinates of the NSA are:

Latitude     Longitude

--------     ---------

Northwest    56.249 N      98.825 W

Northeast    56.083 N      97.234 W

Southwest    55.542 N      99.045 W

Southeast    55.379 N      97.489 W

7.1.2 Spatial Coverage Map

Not available.

7.1.3 Spatial Resolution

New Summary of Documentation (added January 20, 2006):

The level-3a image collection contains both level-3s images (systematic spatial corrections applied in resampling) and level-3p images (precision geometric corrections applied in resampling).  The difference being that the 3p images have had ground control added.  By definition, the 3s images are fine in their internal integrity, but require some shift and/or rotation overall to get the ground aligned (as indicated in the original documentation below).  Users should carefully check the information in the ASCII header files of the 3a images.  If the ASCII header does not show if the source image was '3s' or '3p', the user would need to look at the list of 3s and 3p images to make the connection by site and date to the level-3a image in question.  (End of January 20, 2006 addition.)

Original Documentation:

Before any geometric corrections, the spatial resolution at nadir is 30 m for bands 1-5 and 7 and 120 m for band 6.  These values increase with scan angle away from the nadir path.  The level-3s and -3p Landsat TM images have had geometric corrections applied so that the spatial resolution for all pixels is 30 m in all bands.  The level-3s images have a high level of internal spatial integrity but the actual geographic coordinates contained on the tape can be offset from their actual positions by as much as 20 km.  The level-3p images have a high level of internal spatial integrity and have had ground control added to improve the accuracy of the geographic coordinates provided on the tape.  In processing the level-3s and -3p images to level-3a products, BORIS has provided equations for calculating the latitude, longitude of any image pixel but has not performed any further geometric corrections or spatial resampling of the image data.  The image pixels retain their 30 meter spatial resolution with some leveling of the geographic accuracy of the pixel positions.

7.1.4 Projection

The level-3a Landsat TM images are in a Universal Transverse Mercator (UTM) projection based on NAD83. Detailed projection parameter information for the individual images is contained in the ASCII header file.  Ground control point locations and least squares equations to calculate the latitude and longitude of any pixel in the image were included in the ASCII header file by BORIS personnel (see Sections 9.2.1 and 9.2.2).

7.1.5 Grid Description

The pixel/grid spacing for each pixel in the level-3a Landsat TM images is 30 m in the UTM projection.

7.2 Temporal Characteristics

7.2.1 Temporal Coverage

The entire set of BOREAS Landsat TM acquisitions cover 22-Jun-1984 to 30-Jul-1996.  Imagery acquired before the BOREAS field campaigns were conducted is included in the BOREAS archive with imagery collected during the project.  Historical Landsat data have been acquired by CCRS routinely since the launch of Landsat 1 and are kept in the CCRS archive.  Since the mid-1980s, CCRS has been acquiring and archiving all Landsat data over Canada during the growing season; however during the winter, only requested data were obtained. For BOREAS, this policy was modified to obtain data throughout the year over the BOREAS region. The acquired data are archived by CCRS and can be interrogated to ascertain which scenes were archived and their characteristics.

7.2.2 Temporal Coverage Map

The following two lists provide dates for all the level-3a Landsat TM images that are available from BOREAS.

Date        Study Area

-----------     ----------

11-Jul-1984        SSA

12-Aug-1984        SSA

07-Jul-1985        SSA

11-Aug-1986        SSA

18-Aug-1986        SSA

30-Aug-1987        SSA

20-Jun-1988        SSA

06-Jul-1988        SSA

23-Aug-1988        SSA

02-Jul-1989        SSA

04-Sep-1989        SSA

06-Aug-1990        SSA

06-Aug-1990        SSA

29-Aug-1990        SSA

05-May-1991        SSA

06-Jun-1991        SSA

24-Jul-1991        SSA

09-Aug-1991        SSA

10-Sep-1991        SSA

15-Jun-1992        SSA

18-Jan-1993        SSA

29-Jul-1993        SSA

06-Feb-1994        SSA

20-Apr-1994        SSA

07-Jun-1994        SSA

29-Mar-1995        SSA

03-Jul-1995        SSA

21-Sep-1995        SSA

27-Jan-1996        SSA

02-May-1996        SSA

30-Jul-1996        SSA

Date        Study Area

-----------     ----------

22-Jun-1984        NSA

19-Aug-1985        NSA

15-Aug-1986        NSA

01-Jun-1988        NSA

20-Aug-1988        NSA

05-Sep-1988        NSA

07-Aug-1989        NSA

25-Jul-1990        NSA

28-Jul-1991        NSA

06-Aug-1992        NSA

02-Aug-1993        NSA

10-Feb-1994        NSA

09-Jun-1994        NSA

13-Feb-1995        NSA

09-Apr-1995        NSA

11-May-1995        NSA

21-Jun-1995        NSA

22-May-1996        NSA

09-Jul-1996        NSA

7.2.3 Temporal Resolution

The Landsat TM satellite revisit frequency is 16 days for each path/row; however, in the BOREAS region the overlap between adjacent scene paths is about 50%.

7.3 Data Characteristics (Need to update with CD-ROM Inv file info???)

Data characteristics are defined in the companion data definition file (ltm_ii3a.def).

7.3.1 Parameter/Variable

The main parameter contained in the image data files is scaled at-sensor radiance.

7.3.2 Variable Description/Definition

For the image data files:

Scaled at-sensor radiance - The scaled value representing the radiant energy

incident on the sensor aperture at the time of data

collection in the specific TM wavelength regions.

7.3.3 Unit of Measurement

The units for the scaled at-sensor radiance values vary by band.  To obtain at-sensor radiance values in Watts/(m2 * sr * µm) use the formula:

At-sensor Radiance = Scaled Value * Gain + Offset

where the gain and Offset values are contained in the ASCII header file.

7.3.4 Data Source

The data contained in the level-3a Landsat TM data files come from various portions of the Landsat satellite, the TM instrument, and the ground processing components.  The level-3a Landsat TM images were created by BORIS and CCRS personnel from the level-3s and level-3p images supplied by CCRS.

7.3.5 Data Range

The maximum range of scaled at-sensor radiance values in each level-3a Landsat TM image band is limited from 0 (zero) to 255 so that the values can be stored in a single 8-bit (byte) field.

7.4 Sample Data Record

Sample data format shown in the companion data definition file (ltm_ii3a.def).

8. Data Organization

8.1 Data Granularity

The smallest unit of data tracked by BORIS for the level-3a Landsat TM imagery is a full TM scene.

8.2 Data Format(s)

The data files contain numerical and character fields of varying length separated by commas. The character fields are enclosed with a single apostrophe marks. There are no spaces between the fields. Sample data records are shown in the companion data definition file (ltm_ii3a.def).

8.2.1 Uncompressed Data Files

A level-3a Landsat TM image produced by BORIS contains eight files, an ASCII header file followed by seven BSQ format image data files.

FILE 1 (90 byte ASCII text records)

- Description of level-1a product files

- Original image header information (tape values are decoded based on the

conventions outlined in the User's Guide for Landsat Thematic Mapper

Computer-Compatible Tapes, 1985; EOSAT).

- Level-3a image coordinates

- Calibration information summary (gain and offset per band)

- Georeferencing information summary (minimum and maximum latitude/longitude)

- Coordinates (pixel, line and longitude, latitude) of the control points used

to provide improved georeferencing information.

FILES 2 - 8 (A band sequential set of files containing image bands 1 to 7,

respectively.)

- Each of the 5728 records in each file contains 6920 bytes.

- Each of the 6920 byte records contains 6920 8-bit/one-byte pixel values

- Each pixel value is in units of digital counts  (See section 11.2)

- Each image is oriented so that pixel 1, line 1 is in the upper left-hand

corner (i.e., northwest) of the screen display.  Pixels and lines progress

left to right, and top to bottom so that pixel n, line n is in the lower

right-hand corner.

8.2.2 Compressed CD-ROM Files

On the BOREAS CD-ROMs, file 1 listed above is stored as ASCII text; however, files 2 - 8 have been compressed with the Gzip compression program (file name *.gz).  These data have been compressed using gzip version 1.2.4 and the high compression (-9) option (Copyright (C) 1992-1993 Jean-loup Gailly).  Gzip (GNU zip) uses the Lempel-Ziv algorithm (Welch, 1994) used in the zip and PKZIP programs. The compressed files may be uncompressed using gzip (-d option) or gunzip.  Gzip is available from many websites (for example, ftp site prep.ai.mit.edu/pub/gnu/gzip-*.*) for a variety of operating systems in both executable and source code form.  Versions of the decompression software for various systems are included on the CD-ROMs.

9. Data Manipulations

9.1 Formulae

9.1.1 Derivation Techniques and Algorithms

Not applicable.

9.2 Data Processing Sequence

9.2.1 Processing Steps

BORIS staff created the level-3a Landsat TM images by :

1) Inventorying the level-3s or level-3p image by date and time in the online

data base,

2) Extracting the seven image bands and pertinent header information to online

files from the digital tape,

3) Identifying a set of ground control points,

4) Deriving a second-degree least squares fit to calculate latitude, longitude

coordinates from pixel, line values,

5) Writing the files of information to tape.

Some cloud cover and image quality assessment information is generated when BORIS staff processed the level-3s images to level-3a products.  This information is entered into the BORIS data base but is not included with the images on tape.  To obtain this information, see the inventory file included on the CD-ROMs or see Section 15.1.

The ground control points for the SSA were selected from 1:50,000-scale National Topographic System (NTS) maps.  Different maps will tend to have different levels of accuracy; however, all of the control points that were used for each image have an error of no more than 1.5 pixels (45 meters).

The ground control points for the NSA were selected using 13 ground control points located in the field with a global positioning system (GPS).  Most of these points are road intersections within the study area that are easily identifiable on the imagery.  Because they are of such high precision, 13 points are sufficient to produce an acceptable transformation equation.  These GPS coordinates were determined and used in the NSA due to unexplainable discrepancies that resulted when points digitized from the 1:50,000-scale NTS maps over the western portion of the NSA were used.

The NSA images from Path/Row 34/21 did not cover the entire study area and only a portion of the 13 GPS points fell within these images.  For such cases, another image of the NSA  that had been georeferenced using GPS points was used to perform an image-to-image registration.  This made it possible to select enough ground control points to produce a good transformation equation.

9.2.2 Processing Changes

After processing several Landsat TM images to level-3a products, an error was discovered in the software that caused the level-3a images to contain 6930 pixels in each image line versus the correct 6920 pixels per image line.  After the software problem was discovered, the number of pixels in the subsequently processed images was set at 6920.  However, the images processed prior to the software change still contain 6930 pixels per line.  The extra 10 pixels are located at the end of each line and contain values of zero.

9.3 Calculations

9.3.1 Special Corrections/Adjustments

None.

9.3.2 Calculated Variables

None.

9.4 Graphs and Plots

None.

10. Errors

10.1 Sources of Error

Errors could arise in the acquired imagery from location inaccuracy, distortion of lengths, anisomorphism, the instrument's local coherence, and multispectral registrability. Other errors could arise from inherent radiometric imperfections of the sensors.

10.2 Quality Assessment

10.2.1 Data Validation by Source

Whatever the processing level, the geometric quality of the image depends on the accuracy of the viewing geometry and the ground control points as required to adjust the viewing model.

Spectral errors could arise from image-wide signal-to-noise ratio, saturation, cross-talk, spikes, and response normalization caused by change in gain.

10.2.2 Confidence Level/Accuracy Judgment

Assessment of accuracy of the absolute radiometric constants is difficult. The uncertainties in prelaunch and postlaunch updates of the absolute calibration constants are nominally specified to be less than 10%. A root mean square (rms) summing of known errors in the prelaunch calibration suggests that this may be a reasonable estimate of overall uncertainty in the prelaunch calibration.

There are also known, but as yet uncorrected, effects associated with temperature-dependence of the TM internal calibrator that may be contributing to apparent discontinuous changes at launch and to the continuous changes of gain while in orbit. Additional uncertainties for exoatmospheric reflectances are probably less than 2% in the visible/near-infrared and less than 5% in the shortwave infrared portion of the spectrum as judged by the current differences in estimates of the solar irradiance.

10.2.3 Measurement Error for Parameters

The rms errors for the latitude and longitude least-squares equations are listed in the ASCII header file of each image.  The rms error for the selected points was approximately 1.5 pixels (i.e. 45 meters) in the X and Y directions.  Therefore, the overall RMS error for each scene should be below this threshold.

10.2.4 Additional Quality Assessments

The ability to reproduce coincident TM and ground measurements made for five dates at White Sands, NM, to about 5% for bands 1-4 suggests a potential for monitoring sensor change for the system with time.

The images were screened for cloud cover before BORIS processing.  Each level-3a image has a minimum of cloud cover over the study areas.

10.2.5 Data Verification by Data Center

BORIS checked the image files by visually inspecting them on a display screen and reading the ASCII header files for correctness.

11. Notes

11.1 Limitations of the Data

None.

11.2 Known Problems with the Data

To date, the following discrepancies/problems have been noted in the data:

	Because of a software error, the first several level-3a Landsat TM images  created contain 6930 pixels rather than the correct 6920 pixels.  The last 10 pixel values may or may not contain spurious values but should be ignored.

	The ASCII header files for the level-3a products contain gain and offset values for the seven TM bands.  The units as given in the header files for the gain and offset values are in error.  The proper units for the offset value are watts/(m2 * sr * µm).  The proper units for the gain value are watts/(m2 * sr * µm * DN).

	Some header files refer to level-1A rather than level-3A or to L1A rather than L3A because they were created by software prior to BORIS finalization of data categories.

	Level-3a images for the BOREAS NSA (Path/Row 33/21) have ground control points in the ASCII header file numbered 601 through 629.  The updated coordinates for these points should be:

Point

Number   Longitude      Latitude

----------------------------------

601     98.82064W      55.88655N

602     98.82180W      55.88114N

603     98.78512W      55.88217N

604     97.91873W      55.81210N

605     97.85946W      55.78508N

606     98.83772W      55.77294N

607     97.83192W      55.76364N

608     97.90285W      55.69227N

609     97.89372W      55.70106N

610     97.86028W      55.73037N

611     97.85835W      55.72543N

612     98.09482W      55.51495N

613     98.05691W      55.53442N

620     98.92360W      55.70465N

621     98.85014W      55.80254N

622     98.42479W      55.91969N

623     98.08685W      55.86547N

624     98.37678W      55.68005N

625     98.45378W      55.84137N

626     98.54973W      55.70142N

627     98.35490W      55.72299N

628     98.36780W      56.13641N

629     98.36713W      56.01236N

11.3 Usage Guidance

Before uncompressing the Gzip files on CD-ROM, be sure that you have enough disk space to hold the uncompressed data files.  Then use the appropriate decompression program provided on the CD-ROM for your specific system.

11.4 Other Relevant Information

None.

12. Application of the Data Set

The level-3a Landsat TM images are useful for anyone interested in high spatial resolution imagery over the entire NSA or SSA.

13. Future Modifications and Plans

None.

14. Software

14.1 Software Description

BORIS staff developed software and command procedures to:

1) Process level-3s and -3p Landsat TM images on tape to level-3a products on

disk,

2) Write the level-3a Landsat TM products from disk to tape,

3) Extract header information from level-3a Landsat TM images on tape,

4) Copy level-3a Landsat TM images from tape to disk,

5) Log level-3a Landsat TM image products into the Oracle data base tables.

6) Convert image header coordinates between the geographic systems of (latitude,

longitude), UTM (northing, easting), and BOREAS (x,y) grid locations.

The software mentioned under items 1 to 5 is written in C and is operational on VAX 6410 and MicroVAX 3100 systems at GSFC.  The primary dependencies in the software are the tape input/output (I/O) library and the Oracle data base utility routines.

The geographic coordinate conversion utility (BOR_CORD) has been tested and used on Macintosh, IBM PC, VAX, Silicon Graphics, and Sun workstations.

Gzip (GNU zip) uses the Lempel-Ziv algorithm (Welch, 1994) used in the zip and PKZIP commands.

14.2 Software Access

All of the described software is available upon request.  BORIS staff would appreciate knowing of any problems discovered with the software, but cannot promise to fix them.

Gzip is available from many websites across the net (for example) ftp site prep.ai.mit.edu/pub/gnu/gzip-*.*) for a variety of operating systems in both executable and source code form. Versions of the decompression software for various systems are included on the CD-ROMs.

15. Data Access

15.1 Contact Information

Ms. Beth Nelson

NASA GSFC

Greenbelt, MD

(301) 286-4005

(301) 286-0239 (fax)

beth@ltpmail.gsfc.nasa.gov

15.2 Data Center Identification

See Section 15.1.

15.3 Procedures for Obtaining Data

Users may place requests by telephone, electronic mail, or fax.

15.4 Data Center Status/Plans

The level-3a Landsat TM image data are available from the Earth Observing System Data and Information System (EOS-DIS) Oak Ridge National Laboratory (ORNL) Distributed Active Archive Center (DAAC).  The BOREAS contact at ORNL is:

ORNL DAAC User Services

Oak Ridge National Laboratory

(865) 241-3952

ornldaac@ornl.gov

ornl@eos.nasa.gov

Although the BOREAS level-3a Landsat TM images are being held in a public archive, copyright restrictions limit the distribution and use of the data.  The BOREAS CD-ROM series is publicly available and the Landsat TM images on the CD-ROMs are available for unrestricted use.  However, the other images in the collection are only available to official BOREAS project personnel.  Please contact the ORNL DAAC User Services office to get the most recent information.

16. Output Products and Availability

16.1 Tape Products

The level-3a Landsat TM data can be made available on 8-mm, Digital Archive Tape (DAT), or 9-track tapes at 6250 or 1600 Bytes per Inch (BPI).

Although the BOREAS level-3a Landsat TM images are being held in a public archive, copyright restrictions limit the distribution and use of the data.  The BOREAS CD-ROM series is publicly available and the Landsat TM images on the CD-ROMs are available for unrestricted use.  However, the other images in the collection are only available to official BOREAS project personnel.  Please contact the ORNL DAAC User Services office (see Section 15.4) to get the most recent information.

16.2 Film Products

None.

16.3 Other Products

Although the entire level-3a image inventory is contained on the BOREAS CD-ROM set, only some of the images are included there.  See section 15 for information about how to obtain images not on the CD-ROMs.

17. References

17.1 Platform/Sensor/Instrument/Data Processing Documentation

Multispectral Scanner System for ERTS. 1972. HS324-5214. Hughes Aircraft Corporation. Santa Barbara, CA.

User's Guide for Landsat Thematic Mapper Computer-Compatible Tapes. 1985. Earth Observation Satellite Company. Lanham, MD.

Welch, T.A. 1984, A Technique for High Performance Data Compression, IEEE Computer, Vol. 17, No. 6, pp. 8 - 19.

17.2 Journal Articles and Study Reports

Byrne, G.F., P.F. Crapper, and K.K. Mayo. 1980. Monitoring land-cover change by principal component analysis of multitemporal Landsat data. Remote Sens. Environ. 10:175-184.

Chavez, P.C., S.C. Guptill, and J.A. Bowell. 1984. Image processing techniques for Thematic Mapper data. Technical Papers. 50th Annual Meeting of the Amer. Soc. of Photogr. 2:728-743.

Crist, E.P. and R.C. Cicone. 1984. Application of the Tasseled Cap concept to simulated Thematic Mapper data. Photogr. Engr. & Rem. Sens.50:343-352.

Engel, J.L. and O. Weinstein. 1983. The Thematic Mapper: An Overview. IEEE Transactions on Geoscience and Remote Sensing. GE-21:258-265.

Friedel, J. 1992. System description of the Geocoded Image Correction System. Report GC-MA-50-3915, MacDonald Detwiller and Associates, Richmond, B.C.

Holmes, R.A. 1984. Advanced sensor systems: Thematic Mapper and beyond. Remote Sens. Environ. 15:213-221.

Kanemasu, E.T., J.L. Heilman, J.O. Bagley, and W.L. Powers. 1977. Using Landsat data to estimate evapotranspiration of winter wheat. Environmental Management. 1:515-520.

Lulla, K. 1983. The Landsat satellites and selected aspects of Physical Geography. Progress in Phy. Geogr. 7:1-45.

Malila, W.A. 1985. Comparison of the Information Contents of Landsat TM and MSS Data. Photogrammetric Engineering and Remote Sensing. 51:1449-1457.

Pollock, R.B. and E.T. Kanemasu. 1979. Estimating leaf-area index of wheat with Landsat data. Remote Sens. Environ. 8:307-312.

Robinov, C.J. 1982. Computation with physical values from Landsat digital data. Photogr. Engr. & Rem. Sens. 48:781-784.

Salomonson, V.V. 1984. Landsat 4 and 5 status and results from Thematic Mapper data analysis. Proceedings. Machine Processing of Remotely Sensed Data Symposium. Lab. for the Applications of Remote Sensing. West Lafayette, IN. p 13-18.

Satterwhite, M.B. 1984. Discriminating vegetation and soils using Landsat MSS and Thematic Mapper bands and band ratios. Technical Papers. 50th Annual Meeting of the Amer. Soc. of Photogr. 2:479-485.

Sellers, P. and F. Hall. 1994. Boreal Ecosystem-Atmosphere Study: Experiment Plan. Version 1994-3.0, NASA BOREAS Report (EXPLAN 94).

Sellers, P. and F. Hall. 1996. Boreal Ecosystem-Atmosphere Study: Experiment Plan. Version 1996-2.0, NASA BOREAS Report (EXPLAN 96).

Sellers, P. and F. Hall. 1997. BOREAS Overview Paper. JGR Special Issue (in press).

Sellers, P., F. Hall, and K.F. Huemmrich. 1996. Boreal Ecosystem-Atmosphere Study: 1994 Operations. NASA BOREAS Report (OPS DOC 94).

Sellers, P., F. Hall, and K.F. Huemmrich. 1997. Boreal Ecosystem-Atmosphere Study: 1996 Operations. NASA BOREAS Report (OPS DOC 96).

Sellers, P., F. Hall, H. Margolis, B. Kelly, D. Baldocchi, G. den Hartog, J. Cihlar, M.G. Ryan, B. Goodison, P. Crill, K.J. Ranson, D. Lettenmaier, and D.E. Wickland. 1995. The boreal ecosystem-atmosphere study (BOREAS): an overview and early results from the 1994 field year. Bulletin of the American Meteorological Society. 76(9):1549-1577.

Singn, A.N., and R.S. Dwived, 1986. The Utility of LANDSAT Imagery as an Integral Part of the Data Base for Small Scale Soil Mapping. Int. J. Remote Sensing. 7:1099-1108.

Taranik, J.V. 1978. Characteristics of the Landsat Multispectral Data System. U.S. Dept. of the Interior. Open File Report 78-187. Sioux Falls, SD.

Thompson, D.R. and O.A. Wehmanen. 1980. Using Landsat digital data to detect moisture stress in corn-soybean growing region. Photogr. Engr. & Rem. Sens. 46:1082-1089.

Williams, D.L., J.R. Irons, B.L. Markham, R.F. Nelson, D.L. Toll, R.S.Latty, and M.L. Stauffer. 1984. A statistical evaluation of the advantages of Landsat Thematic Mapper data in comparison to Multi-spectral Scanner data. IEEE Transactions on Geoscience and Remote Sensing. GE-22.

17.3 Archive/DBMS Usage Documentation

None.

18. Glossary of Terms

None.

19. List of Acronyms

ASCII   - American Standard Code for Information Interchange

BOREAS  - BOReal Ecosystem-Atmosphere Study

BORIS   - BOREAS Information System

BPI     - Byte per inch

BSQ     - Band Sequential

CCRS    - Canada for Remote Sensing

CCT     - Computer Compatible Tape

CD-ROM  - Compact Disk-Read-Only Memory

DAAC    - Distributed Active Archive Center

DAT     - Digital Archive Tape

DN      - Digital Number

EOS     - Earth Observing System

EOSDIS  - EOS Data and Information System

ERTS    - Earth Resources Technology Satellite

FOLD    - Federally Owned Landsat Database

FOV     - Field of View

FPAR    - Fraction of Photosynthetically Active Radiation

GICS    - Geocoded Image Correction System

GPS     - Global Positioning System

GSFC    - Goddard Space Flight Center

IFOV    - Instantaneous Field-of-View

I/O     - Input/Output

LAI     - Leaf Area Index

LGSOWG  - Landsat Ground Station Operations Working Group

LTWG    - LGSOWG Technical Working Group

MSS     - Multispectral Scanner

NAD27   - North American Datum of 1927

NAD83   - North American Datum of 1983

NASA    - National Aeronautics and Space Administration

NE      - Noise Equivalent

NSA     - Northern Study Area

NTS     - National Topographic System

ORNL    - Oak Ridge National Laboratory

PANP    - Prince Albert National Park

rms     - root-mean-square

SBRC    - Santa Barbara Research Center

SSA     - Southern Study Area

TIPS    - Thematic Mapper Image Processing System

TM      - Thematic Mapper

URL     - Uniform Resource Locator

UTM     - Universal Transverse Mercator

WWW     - World Wide Web

20.  Document Information

20.1 Document Revision Dates

Written:         18-Oct-1994

Last Updated:    20-Mar-1998

20.2 Document Review Dates

BORIS Review:    20-Feb-1998

Science Review:  27-Feb-1998

20.3 Document ID

20.4 Citation

The Landsat TM level-3a images resulted from a joint development and processing effort between BOReal Ecosystem-Atmosphere Study (BOREAS) staff at the Canada Centre for Remote Sensing (CCRS) and the National Aeronautics and Space Administration (NASA) Goddard Space Flight Center (GSFC).  The original level-3s and -3p data were acquired by CCRS and processed by RADARSAT International under an agreement with CCRS.  The respective contributions of the above individuals and agencies to completing this data set are greatly appreciated.

20.5 Document Curator

20.6 Document URL

Keywords

LANDSAT

LANDSAT THEMATIC MAPPER

EMITTED RADIATION

REFLECTED RADIATION