BOREAS AES READAC Surface Meteorological Data

Summary

Canadian AES personnel collected and processed data related to surface atmospheric meteorological conditions over the BOREAS region.  This data set contains 15 minute meteorological data from one READAC meteorology station in Hudson Bay, Saskatchewan. Parameters include day, time, type of report, sky condition, visibility, mean sea level pressure, temperature, dewpoint, wind, altimeter, opacity, minimum and maximum visibility, station pressure, minimum and maximum air temperature, a wind group, precipitation, and precipitation in the last hour.  The data were collected non-continuously from 24-May-1994 to 20-Sep-1994.  The data are provided in tabular ASCII files.

Table of Contents

*  1 Data Set Overview

*  2 Investigator(s)

*  3 Theory of Measurements

*  4 Equipment

*  5 Data Acquisition Methods

*  6 Observations

*  7 Data Description

*  8 Data Organization

*  9 Data Manipulations

*  10 Errors

*  11 Notes

*  12 Application of the Data Set

*  13 Future Modifications and Plans

*  14 Software

*  15 Data Access

*  16 Output Products and Availability

*  17 References

*  18 Glossary of Terms

*  19 List of Acronyms

*  20 Document Information

1. Data Set Overview

1.1 Data Set Identification

BOREAS AES READAC Surface Meteorological Data

1.2 Data Set Introduction

This data set contains 15-minute meteorological data from one Remote Environmental Automated Data Acquisition Concept (READAC) meteorology station in the BOReal Ecosystem-Atmosphere Study (BOREAS) region in Canada.  Parameters include day, time, type of report, sky condition, visibility, mean sea level pressure, temperature, dewpoint, wind, altimeter, opacity, minimum and maximum visibility, station pressure, minimum and maximum air temperature, a wind group, precipitation, and precipitation in the last hour.

1.3 Objective/Purpose

These monitoring sites were established by Environment Canada to provide hourly weather reports, input to the operational program of forecasts and warnings, input to operational weather prediction models, and climate data.

The frequency of observation was increased to 15 minutes at the request of BOREAS.  Data collection for BOREAS occurred during IFCs 1, 2, and 3.

1.4 Summary of Parameters

Included parameters are day, time, type of report, sky condition, visibility, mean sea level pressure, temperature, dewpoint, wind, altimeter, opacity, minimum and maximum visibility, station pressure, minimum and maximum air temperature, wind group, precipitation, and precipitation in the last hour.

1.5 Discussion

This station was installed before BOREAS began in order to meet the goals of Environment Canada, and it conforms to Environment Canada's criteria for accuracy and exposure.

1.6 Related Data Sets

BOREAS AFM-07 SRC Surface Meteorological Data

BOREAS AES MARSII Surface Meteorological Data

BOREAS AES Campbell Scientific Surface Meteorological Data

2. Investigator(s)

2.1 Investigator(s) Name and Title

G. Barrie Atkinson (Retired)

BOREAS Project Scientist

2.2 Title of Investigation

Environment Canada 15-Minute Autostation Data

2.3 Contact Information

Contact 1

G. Barrie Atkinson (Retired)

BOREAS Project Scientist

Environment Canada

Winnipeg, Manitoba

Canada

(204) 983-6059

(204) 983-4884  (fax)

Contact 2

Barry Funk

Supervisor, Special Programs

Environment Canada

Winnipeg, Manitoba

Canada

(204) 983-2018

(204) 984-2072  (fax)

Barry.Funk@gc.ec.ca

Contact 3

David Knapp

Raytheon STX Corporation

NASA GSFC

Greenbelt, MD

(301) 286-0544

(301) 286-0239  (fax)

David.Knapp@gsfc.nasa.gov

3.  Theory of Measurements

None given.

4. Equipment

4.1 Sensor/Instrument Description

Parameter           Instrumentation

Pressure            Sentra 270 (2)    The two are compared for each reading.

Cloud               Model 8329A Qualimetrics laser ceilometer

Visibility          Belfort 6200

Temperature         YSI READAC thermister

Dewcel Probe        AES type E

Radiation Shield    Wooden Stevenson screen with wooden stand, Height 119 cm

Precipitation       Weighing gauge, Fisher and Porter, Height 194 cm,

Altershield    196 cm

Wind                Direction 78D, Speed detector 78D, Cupwheel height 10 m,

Tower tilting

4.1.1 Collection Environment

The instruments operated during the summer of 1994 in the environmental conditions shown in the data.

4.1.2 Source/Platform

None given.

4.1.3 Source/Platform Mission Objectives

None given.

4.1.4 Key Variables

Temperature, pressure, humidity, wind.

4.1.5 Principles of Operation

None given.

4.1.6 Sensor/Instrument Measurement Geometry

None given.

4.1.7 Manufacturer of Sensor/Instrument

None given.

4.2 Calibration

4.2.1 Specifications

None given.

4.2.1.1 Tolerance

None given.

4.2.2 Frequency of Calibration

None given.

4.2.3 Other Calibration Information

None given.

5. Data Acquisition Methods

Since there is no provision for onboard storage of observations, the station was telephoned approximately every 15 minutes from a computer in Winnipeg and downloaded.

6. Observations

6.1 Data Notes

None given.

6.2 Field Notes

ZHB Hudson Bay, Saskatchewan (SK)

Installation 21-Jun-1992

All instruments were verified after installation. The average differences from the inspection were: barometer was -0.01 mb for 10 readings; dry bulb temperature, -0.1 degrees C for 10 readings; dewpoint +0.46 degrees C for 10 readings. The Fisher and Porter weighing gauge was tested at 25-mm increments over the range

0-300 mm. The difference ranged from +1.2 mm to -0.8 mm with an average of +0.05 mm.

7. Data Description

7.1 Spatial Characteristics

7.1.1 Spatial Coverage

ZHB Hudson Bay SK

The Hudson Bay site is located at a latitude of 52 degrees, 49 minutes N; at a longitude of 102 degrees, 19 minutes W; and at an elevation of 358.1 meters.  The site is located at the Hudson Bay airport, approximately 5 km south of the town of Hudson Bay, SK.  The instruments are located in the 75 m (northwest to southeast) by 60 m (southwest to northeast) instrument area of the formerly manned weather station.  The instrument area is level and grassed, with open exposure in all directions.  The surrounding countryside is generally flat and forested.  The Red Deer River is located approximately 0.7 km to the south.  The airport is located in the shallow valley of the Red Deer River, which runs generally southwest to northeast.  The valley is paralleled to the south by the Porcupine Hills, which rise to a height of 760 m above sea level approximately 48 km southeast, and to the north by the Pasquia Hills, which achieve a height of 817 m approximately 48 km northwest.

7.1.2 Spatial Coverage Map

Not available.

7.1.3 Spatial Resolution

These data were collected at a point location.

7.1.4 Projection

Not applicable.

7.1.5 Grid Description

Not applicable.

7.2 Temporal Characteristics

7.2.1 Temporal Coverage

Data are available from 24-May-1994 to 25-Jun-1994 and from 19-Jul-1994 to

20-Sep-1994.

7.2.2 Temporal Coverage Map

Not available.

7.2.3 Temporal Resolution

Data were collected approximately every 15 minutes.

7.3 Data Characteristics

Data characteristics are defined in the companion data definition file (readac_d.def).

7.4 Sample Data Record

Sample data format shown in the companion data definition file (readac_d.def).

8. Data Organization

8.1 Data Granularity

All of the READAC Surface Meteorological Data are contained in one dataset.

8.2 Data Format(s)

The data files contain a series of numerical and character fields of varying length separated by commas.  The character fields are enclosed within single apostrophe marks.  There are no spaces between fields.  Sample data records are shown in the companion data definition file (readac_d.def).

9. Data Manipulations

9.1 Formulae

None given.

9.1.1 Derivation Techniques and Algorithms

None given.

9.2 Data Processing Sequence

9.2.1 Processing Steps

None given.

9.2.2 Processing Changes

'RAW' data have many extraneous characters, which were removed.  Each record was checked for completeness.

9.3 Calculations

No calculations were performed on the data.

9.3.1 Special Corrections/Adjustments

None given.

9.3.2 Calculated Variables

None given.

9.4 Graphs and Plots

None.

10. Errors

10.1 Sources of Error

None given.

10.2 Quality Assessment

10.2.1 Data Validation by Source

None given.

10.2.2 Confidence Level/Accuracy Judgment

None given.

10.2.3 Measurement Error for Parameters

None given.

10.2.4 Additional Quality Assessments

None given.

10.2.5 Data Verification by Data Center

Some automated quality assessment was done to identify spikes and other anomalies in the data.  These anomalies are also present in the original data and are not due to BOREAS Information System (BORIS) processing.

11. Notes

11.1 Limitations of the Data

None given.

11.2 Known Problems with the Data

Weighing gauges are known to give readings of poorer quality than tipping bucket gauges.  However, they do work in winter.

Some automated quality assessment was done to identify spikes and other anomalies in the data.  These anomalies are also present in the original data and are not due to BOREAS Information System (BORIS) processing.  The following are a few examples of some anomalies that were detected for the various columns of data.  This is not meant to be a comprehensive list.

REPORT

Because this column contains character data, no quantitative assessment was done.  The data appear to be correct.

SKY_COVER

Because this column contains character data, no quantitative assessment was done.  The data appear to be correct.

VISIBILITY

Because this column contains character data, no quantitative assessment was done.  The data appear to be correct.

AIR_TEMP_1_5_M

No problems were identified.

DEW_TEMP_1_5M

No problems were identified.

MEAN_WIND_10M_2MIN

Because this column contains character data, no quantitative assessment was done.  The data appear to be correct.

ALTIMETER

These data appear to be reasonable.

OPACITY

Because this column contains character data, no quantitative assessment was done.  The data appear to be correct.

VISIBILITY_MIN_MAX

Because this column contains character data, no quantitative assessment was done.  The data appear to be correct.

STN_PRESS

No anomalies were identified.

AIR_TEMP_MIN

No serious anomalies were identified, but some questionable values were found that could not be verified for accuracy.

AIR_TEMP_MAX

No serious anomalies were identified, but some questionable values were found that could not be verified for accuracy.

WIND_GROUP_10M

Because this column contains character data, no quantitative assessment was done.  The data appear to be correct.

ACCUM_PRECIP

No serious anomalies were identified.

PRECIP_LAST_HOUR

No serious anomalies were identified.

11.3 Usage Guidance

None given.

11.4 Other Relevant Information

None given.

12. Application of the Data Set

None given.

13. Future Modifications and Plans

None given.

14. Software

14.1 Software Description

None given.

14.2 Software Access

None given.

15. Data Access

15.1 Contact Information

Ms. Beth Nelson

BOREAS Data Manager

NASA GSFC

Greenbelt, MD

(301) 286-4005

(301) 286-0239 (fax)

Elizabeth.Nelson@gsfc.nasa.gov

15.2 Data Center Identification

See Section 15.1.

15.3 Procedures for Obtaining Data

Users may place requests by telephone, electronic mail, or fax.

15.4 Data Center Status/Plans

The AES READAC data are available from the Earth Observing System Data and Information System (EOSDIS) Oak Ridge National Laboratory (ORNL) Distributed Active Archive Center (DAAC).

The BOREAS contact at ORNL is:

ORNL DAAC User Services

Oak Ridge National Laboratory

(865) 241-3952

ornldaac@ornl.gov

ornl@eos.nasa.gov

16. Output Products and Availability

16.1 Tape Products

None.

16.2 Film Products

None.

16.3 Other Products

Tabular ASCII file.

17. References

17.1 Platform/Sensor/Instrument/Data Processing Documentation

21X Micrologger Operator's Manual, Revision 8/91. Campbell Scientific, Inc.

17.2 Journal Articles and Study Reports

Sellers, P. and F. Hall. 1994. Boreal Ecosystem-Atmosphere Study: Experiment Plan. Version 1994-3.0, NASA BOREAS Report (EXPLAN 94).

Sellers, P. and F. Hall. 1996. Boreal Ecosystem-Atmosphere Study: Experiment Plan. Version 1996-2.0, NASA BOREAS Report (EXPLAN 96).

Sellers, P. and F. Hall. 1997. BOREAS Overview Paper. JGR Special Issue.

Sellers, P., F. Hall, and K.F. Huemmrich. 1996. Boreal Ecosystem-Atmosphere Study: 1994 Operations. NASA BOREAS Report (OPS DOC 94).

Sellers, P., F. Hall, and K.F. Huemmrich. 1997. Boreal Ecosystem-Atmosphere Study: 1996 Operations. NASA BOREAS Report (OPS DOC 96).

Sellers, P., F. Hall, H. Margolis, B. Kelly, D. Baldocchi, G. den Hartog, J. Cihlar, M.G. Ryan, B. Goodison, P. Crill, K.J. Ranson, D. Lettenmaier, and D.E. Wickland. 1995. The boreal ecosystem-atmosphere study (BOREAS): an overview and early results from the 1994 field year. Bulletin of the American Meteorological Society. 76(9):1549-1577.

Sellers, P.J., F.G. Hall, R.D. Kelly, A. Black, D. Baldocchi, J. Berry, M. Ryan, K.J. Ranson, P.M. Crill, D.P. Lettenmaier, H. Margolis, J. Cihlar, J.

Newcomer, D. Fitzjarrald, P.G. Jarvis, S.T. Gower, D. Halliwell, D. Williams, B. Goodison, D.E. Wickland, and F.E. Guertin. 1997. BOREAS in 1997:

Experiment Overview, Scientific Results and Future Directions. JGR, BOREAS Special Issue, 102(D24), Dec. 1997, pp.

28731-28770.

17.3 Archive/DBMS Usage Documentation

None.

18. Glossary of Terms

None.

19. List of Acronyms

AES     - Atmospheric and Environment Service

AFM     - Airborne Fluxes and Meteorology

BOREAS  - BOReal Ecosystem-Atmosphere Study

BORIS   - BOREAS Information System

CGR     - Certified by Group

CPI     - Checked by PI

CPI-??? - CPI but questionable

DAAC    - Distributed Active Archive Center

EOS     - Earth Observing System

EOSDIS  - EOS Data and Information System

GSFC    - Goddard Space Flight Center

IFC     - Intensive Field Campaign

MARSII  - Meteorological Automatic Reporting System II

MB      - Manitoba

NASA    - National Aeronautics and Space Administration

NSA     - Northern Study Area

ORNL    - Oak Ridge National Laboratory

READAC  - Remote Environmental Automated Data Acquisition Concept

PANP    - Prince Albert National Park

PI      - Principal Investigator

PRE     - Preliminary

READAC  - Remote Environmental Automated Data Acquisition Concept

SK      - Saskatchewan

SSA     - Southern Study Area

TBRG    - Tipping Bucket Rain Gauge

T/RH    - Temperature/Relative Humidity

URL     - Uniform Resource Locator

20. Document Information

20.1 Document Revision Date

Written: 27-Jul-1995

Last Updated: 02-Jul-1998

20.2 Document Review Date(s)

BORIS Review:  02-Jul-1998

Science Review:

20.3 Document ID

20.4 Citation

These data were collected by the Atmospheric Environment Service of Environment Canada.  Their efforts to make these data available are greatly appreciated.

20.5 Document Curator

20.6 Document URL

KEYWORDS

---------

SURFACE METEOROLOGY

TEMPERATURE

RELATIVE HUMIDITY

WIND SPEED

WIND DIRECTION

ATMOSPHERIC PRESSURE

PRECIPITATION

DEWPOINT

CLOUD COVER