BOREAS TF-01 SSA-OA Tower Flux, Meteorological, and Soil Temperature Data

Summary

The BOREAS TF-01 team collected energy, carbon dioxide, and momentum flux data above the canopy along with meteorological and soils data at the BOREAS SSA-OA site from mid-April to the end of the year for 1996.  The data are available in tabular ASCII files.

Table of Contents

1 Data Set Overview

2 Investigators

3 Theory of Measurements

4 Equipment

5 Data Acquisition Methods

6 Observations

7 Data Description

8 Data Organization

9 Data Manipulations

10 Errors

11 Notes

12 Application of the Data Set

13 Future Modification and Plans

14 Software

15 Data Access

16 Output Products and Availability

17 References

18 Glossary of Terms

19 List of Acronyms

20 Document Information

1.   Data Set Overview

1.1  Data Set Identification

BOREAS TF-01 SSA-OA Tower Flux, Meteorological, and Soil Temperature Data

1.2  Data Set Introduction

The Tower Flux-01 team collected heat, carbon dioxide, and momentum fluxes along with meteorological, soil temperature, soil moisture, and tree bole temperature data measured from the BOReal Ecosystem-Atmosphere Study (BOREAS) Southern Study Area (SSA) Old Aspen (OA) tower. These data were collected between 1-April and 31-December-1996.

1.3  Objective/Purpose

The general objective was to study carbon dioxide and water vapor exchange between the forest and atmosphere at the SSA-OA site. Specific objectives were:

* To measure the fluxes of sensible heat, H2O and CO2 above the aspen stand throughout the year.

* To obtain from the CO2 flux data estimates of gross photosynthesis and respiration.

* To determine the contribution of the hazelnut understory to net ecosystem productivity (NEP).

* To determine the effects of environmental factors on stand evapotranspiration and NEP.

* To take part in the development of procedures for scaling up component fluxes to the stand level.

* To study the processes controlling turbulent transfer of H2O and CO2 within the stand.

* To take part in the evaluation of methods of estimating nocturnal CO2 in and above the stand.

1.4   Summary of Parameters

From the tower, above the canopy, the following variables were measured: latent heat flux, sensible heat flux, net radiation, CO2 flux, CO2 concentration, momentum flux, Bowen ratio, air temperature, wind speed and direction, friction velocity, incident and reflected photosynthetic photon flux density (PPFD), incident and reflected shortwave and longwave radiation, water vapor concentration, relative humidity, precipitation, and air pressure.  Under the canopy, the following measurements were collected to describe the soil and forest: soil heat flux, soil temperature, soil water potential, soil water content, and tree bole temperatures.

1.5  Discussion

In 1993 and 1994, the TF-01 group measured fluxes under the canopy at the SSA-OA site, while the TF-02 group measured above canopy fluxes and profiles at that site.  In 1996, the TF-01 group moved its equipment to the top of the 39-meter tower to measure above-canopy fluxes; this document describes the 1996 data collection effort.

The fluxes of momentum, sensible heat, latent heat (water vapor), and carbon dioxide using the eddy correlation method were measured at 39-m height on the main flux tower beginning in April 1996.  This system operated continuously through the rest of 1996.  The eddy correlation system consisted of 3-dimensional sonic anemometer (model 1012R2A (Solent) Gill Instruments, Lymington, UK) with a 15-cm path length, an infrared gas (CO2/H2O) analyzer (IRGA) (model 6262, LI-COR Inc. Lincoln, NE) and a krypton open-path hygrometer (model KH20, Campbell Scientific Inc. (CSI), Logan, UT).  Air was drawn at 8.0 L min-1 down 3.2-mm inner diameter (i.d.) sampling tubing (model Bev-a-line, Thermoplastic Processes Inc., Sterling, NJ), then through copper tubing (3 mm i.d.) coiled and sandwiched between two aluminum plates within the same housing as the analyzer, and then through the analyzer’s sample cell.  To prevent condensation in the sampling tubing, it was heated (2-3 oC above ambient) by passing an electric current through 20-AWG nichrome wire (about 15 ohms resistance) coiled around the exterior of the tubing.  The pump (model DOA-V191-AA diaphragm pump, Gast Inc., Dayton, OH) was located down stream of the sample cell resulting in the sample cell pressure being about 22 kPa less than atmospheric pressure.  The IRGA was operated in absolute mode with dry air at zero CO2 concentration flowing through the reference cell at 25 cm3 min-1.  The KH20 hygrometer was operated continuously to evaluate signal delay time and any attenuation resulting from the sample tubing (Leuning & King 1992; Lee et al. 1994).

Supporting measurements included soil heat flux at the 3-cm depth measured using nine soil heat flux plates (two, model F, Middleton Instruments, Melbourne, Australia, and seven homemade, following Fuchs and Tanner (1968)) along a 20-m transect; average temperature of the surface 3 cm of the forest floor using two integrating thermometers; a soil temperature profile at depths of 2, 5, 10, 20, 50, and 100 cm (CSI direct-burial copper-constantan thermocouples); tree bole temperatures at 0.2, 4.0, 8.0, 12.0, 15.8 cm (thermocouple wire); downward total and diffuse solar (model PSP pyranometer, The Eppley Laboratory, Inc., Newport, RI), downward longwave (Eppley model PIR pyrgeometer), and net radiation (one model S-1 net radiometer, Swissteco Instruments, Oberriet, Switzerland (belonging to University of British Columbia (UBC)) and one Middleton model CN-1 net radiometer (belonging to Atmospheric Environment Service (AES)); PPFD (LI-COR model 190-SB quantum sensor) above the forest (at 33-m height from the ground ); wind speed and direction above the overstory (model 05031 vane propeller anemometer, R.M. Young Co., Traverse City, MI); soil water content using the time-domain reflectometry (TDR) technique (Hook and Livingston, 1996) with two probes consisting of 3 stainless steel rods (3-mm diameter, 30-cm long, and 2-cm apart) were positioned horizontally at 8-cm (organic layer) and 15-cm (mineral layer) depths, five 120-cm segmented rods (two thin stainless steel strips, 1.2 cm wide and 1.5 cm apart bonded by an epoxy resin layer) were installed to measure average water content in 15 cm (0-30 cm) and 30 cm soil layers (30 - 120 cm depth); and infrared surface temperatures of the aspen and hazelnut canopies (model 4000 IR thermometer, Everest Interscience, Inc., Fullerton, CA).

1.6  Related Data Sets

BOREAS TF-01 SSA-OA Soil Characteristics Data

BOREAS TF-01 SSA-OA Understory Flux, Meteorological, and Soil Temperature Data

BOREAS TF-02 SSA-OA Tower Flux, Meteorological, and Precipitation Data

BOREAS TF-09 SSA-OBS Tower Flux, Meteorological, and Soil Temperature Data

2.   Investigator(s)

2.1  Investigator Name and Title

Prof. T. Andy Black

University of British Columbia

Department of Soil Science

2.2  Title of Investigation

Boreal Forest Atmosphere Interactions: Exchanges of Energy, Water Vapor and Trace Gases (SSA-OA)

2.3  Contact Information

Contact 1:

Mr. Zoran Nesic

University of British Columbia

Department of Soil Science

Vancouver, BC CANADA

(604) 822-3479, 822-5654(Lab)

(604) 822-8639 (fax)

NESIC@PPC.UBC.CA

Contact 2:

Prof. T. Andy Black

University of British Columbia

Department of Soil Science

Vancouver, BC CANADA

(604) 822-2730

(604) 822-8639 (fax)

ablack@unixg.ubc.ca

Contact 3:

K. Fred Huemmrich

University of Maryland

NASA/GSFC

Greenbelt, MD

(301) 286-4862

(301) 286-0239  (fax)

karl.Huemmrich@gsfc.nasa.gov

Theory Of Measurements

Note: Equations and special characters are visible only in the MSWord version of this document.

Measurements of the fluxes of momentum, sensible heat, water vapor, and CO2 were made with the eddy covariance technique.  Velocity components, air temperature, water vapor density, and CO2 concentration in the air were sampled rapidly, and calculations of relevant covariances were performed from these samples to obtain the fluxes.  For example, the flux of CO2 was determined as follows:

where  is the departure of the vertical velocity component from its mean over the averaging interval, usually 30 minute, and  is the departure of CO2 concentration from its mean.

At the overstory level, three rotations in the coordinate transformation are applied to the flux data to make the lateral component (), vertical component(), and covariance () of the wind vector equal to zero.  At the understory level, however, only the mean lateral wind velocity component was rotated to zero under the suspicion that nonzero mean vertical velocities are possible within the trunk space.  Webb, Pearman, and Leuning (1980) (WPL) corrections were made to the water vapor and carbon dioxide fluxes measured using the closed-path LI-COR 6262 infrared gas analyzer (IRGA).  Broadening correction was done, but not on-line (see Chen et al., 1998, for summary of theory).

4.   Equipment

4.1  Sensor/Instrument Description

4.1.1  Collection Environment

Measurements were collected from mid-April to the end of 1996.  Over that time period, temperature conditions from less than -30 °C to over 30 °C were experienced.

4.1.2 Source/Platform

A 37-m walk up scaffold main tower and a 6-m scaffold tower about 40 m from the main tower.

4.1.3 Source/Platform Mission Objectives

The objective of the flux tower was to support instrumentation for the study of the fluxes of CO2, energy, water vapor, and momentum between the forest and atmosphere at the SSA-OA.

4.1.4 Key Variables

Variables measured using eddy covariance: CO2 and water vapor fluxes, momentum fluxes, sensible heat fluxes, latent heat fluxes.

Supporting meteorological variables: net radiation, downward total and diffuse solar radiation, downward longwave radiation, PPFD, wind speed, wind direction, air temperature, soil temperature, soil heat flux, soil moisture, precipitation.

4.1.5 Principles of Operation

A sonic anemometer determines the wind speed by a pair of transducers acting alternately as transmitters and receivers, sending pulses of high frequency ultrasound between themselves.  The 3-D sonic has three pairs of transducers arranged in nonparallel axes.

The LI-COR 6262 CO2/H2O analyzer are based on the difference in absorption of infrared radiation passing through two gas sampling cells. The reference cell is used for a gas of known CO2 or H2O concentration, and the sample cell is used for a gas of unknown concentration. Infrared radiation is transmitted through both cell paths, and the output of the analyzer is proportional to the difference in absorption between the two.

The principles of operation of most of the supporting instruments can be found in Pearcy et al. (1991) and Fritschen and Gay (1979).

4.1.6 Sensor/Instrument Measurement Geometry

Above-canopy sensors were supported by a vertical triangular mast mounted on top of a 37-m-tall scaffold-type main tower.  The sonic anemometer was mounted at a height of 39 m.  Other above-canopy measurements included downward total and diffuse solar (model PSP pyranometer, The Eppley Laboratory, Inc., Newport, RI), downward longwave (Eppley model PIR pyrgeometer) and net radiation (one model S-1 net radiometer, Swissteco Instruments, Oberriet, Switzerland, and one Middleton model CN-1 net radiometer), PPFD (LI-COR model 190-SB quantum sensor) above the forest (at 33-m height from the ground ), wind speed and direction above the overstory (model 05031 vane propeller anemometer, R.M. Young Co., Traverse City, MI), and infrared surface temperatures of the aspen and hazelnut canopies (model 4000 IR thermometer, Everest Interscience, Inc., Fullerton, CA).

Under-canopy measurements included soil heat flux measured at the 3-cm depth using nine soil heat flux plates (two model F, Middleton Instruments, Melbourne, Australia, and seven homemade, following Fuchs and Tanner (1968)) along a 20-m transect, average temperature of the surface 3 cm of the forest floor using two integrating thermometers, a soil temperature profile at depths of 2, 5, 10, 20, 50, and 100 cm (CSI direct-burial copper-constantan thermocouples); tree bole temperatures at 0.2, 4.0, 8.0, 12.0, and 15.8 cm into the bole (thermocouple wire); and soil water content using the time-domain reflectometry (TDR) technique (Hook and Livingston, 1996), where two probes consisting of 3 stainless steel roads (3 mm diameter, 30 cm long, and 2 cm apart) were positioned horizontally at 8-cm (organic layer) and 15-cm (mineral layer) depths, and five 120-cm segmented rods (two thin stainless steel strips, 1.2 cm wide and 1.5 cm apart, bonded by an epoxy resin layer) were installed to measure average water content in 15 cm (0-30 cm) and 30 cm soil layers (30-120 cm depth).

Tree bole temperatures were measured in aspen trees using thermocouples placed in the bole at several depths determined from the north side of the tree.  The temperatures were measured at 3.12 m height for the 0.2 cm depth, 3.16 m height for the 4.0 cm depth, 3.18 m height for the 8.0 cm depth (the center of the bole), at 3.16 m height for the 12 cm depth (4 cm depth from south side), and at 3.12 m height for the 15.8 cm depth (0.2 cm depth from south side).  In addition, a measurement of the hazelnut stem temperature was made at 0.7 m height and 0.2 cm depth.

4.1.7  Manufacturer of Sensor/Instrument

Solent sonic anemometer:

Gill Instruments Limited

Solent House

Cannon Street

Lymington

Hmpshire

SO41 9BR

United Kingdom

DAT-310 sonic anemometer:

Kaijo-Denki Co., Ltd.

No 19.1 Chrome Kanda-Nishikicho

Chiyoda-Ku

Tokyo 101

Japan

Li-Cor LI-6262 IRGA, 190-SB PPFD, and LAI-2000 PCA:

LI-COR Inc.

P.O. Box 4425/4421

Superior Street

Lincoln, NE 68504

(303) 499-1701

(303) 499-1767  (fax)

KH2O krypton hygrometer:

Campbell Scientific

P.O. Box 551

Logan, UT 84321

CN-1 net radiometer:

Middleton Instruments, Inc.

P.O. Box 442

South Melbourne

Victoria, 3205

Australia

S-1 net radiometer:

Swissteco Instruments Inc.

Stegweg, Eichenwies, CH-94633 OBERRIET SG

Switzerland

PSP pyranometer and PIR pyrgeometer:

The Eppley Laboratory, Inc.

12 Shefield Ave.

P. O. Box 419

Newport, RI 02840

(401) 847-1020

(401) 847-1031 (fax)

05031 vane propeller anemometer:

R.M. Young Co.

Traverse City, MI

Distributor:

Campbell Scientific

P.O. Box 551,

Logan, UT 84321

(801) 753-234

(801) 752-3268

Soil temperature (burial) Campbell Thermocouple, Copper-constantan thermocouple:

Campbell Scientific

P.O. Box 551,

Logan, UT 84321

(801) 753-2342

(801) 752-3268  (fax)

4000 IR thermometer:

Everest Interscience, Inc.

P.O. Box 3640

Fullerton, CA  92634-3640

(714) 992-4461

M1 dewpoint hygrometer (with D2 sensor):

General Eastern Instruments Corp.

Watertown, MA

HMP-35C Vaisala humidity sensor:

Vaisala, Inc.

Woburn, MA

Distributor:

Campbell Scientific

P.O. Box 551

Logan UT 84321

(801) 753-2342

(801) 752-3268  (fax)

Soil heat flux plate (model F):

Middleton Instruments, Inc.

P.O. Box 442

South Melbourne

Victoria, 3205

Australia

Time domain reflectometry (TDR):

G.S. Gabel Corp.

Victoria, BC, Canada

CS105 Barometer:

Vaisala, Inc.

Woburn, MA

Distributor:

Campbell Scientific

P.O. Box 551

Logan, UT 84321

(801) 753-2342

(801) 752-3268  (fax)

TE525 Tipping-bucket rain gauge:

Texas Electronics

Distributor:

Campbell Scientific

P.O. Box 551

Logan, UT 84321

(801) 753-2342

(801) 752-3268  (fax)

Weighing rain gauge:

Belfort Instrument Co.

1600 S. Clinton Street

Baltimore, MD 21224

21x, CR10 Data logging system:

Campbell Scientific

P.O. Box 551,

Logan, UT 84321

(801) 753-2342

(801) 752-3268  (fax)

TD-4X2N diaphragm pump:

Brailsford Co.

670 Milton Road

Rye, NY 10580

(914) 967-1820

(914) 967-1836 (fax)

DOA-V191-AA diaphragm pump:

Gast, Inc.

P.O. Box 97

Benton Harbor, MI

(616) 926-6171

(616) 925-8288 (fax)

Bev-a-line tube:

Thermoplastic Processes, Inc.

Sterling NS

Dekoron tubing:

Wirex Controls Ltd.

9446 McLaughlin Road N. Unit #27

Brampton, ON

Canada, L6X 4H9

(905) 459-0742

(905) 450-8216

4.2 Calibration

4.2.1  Specifications

In 1996, the eddy covariance IRGA at the 33-m height was automatically calibrated by one of the eddy covariance PCs at midnight every day.  A solenoid valve was opened, permitting nitrogen gas to flow into the entrance of the sampling tube for 12 seconds.  This established the voltage signals corresponding to zero CO2 and water vapor concentrations.  A second solenoid was then opened for 12 seconds, permitting dry air with 350 mmol-1 CO2 to enter the sampling tube, thereby calibrating the analyzer.  The computer changed the calibration parameters in the control program, which ensured that CO2 concentration was accurate to within ± 1 mmol mol-1.

4.2.1.1 Tolerance

See Section 4.2.1.

4.2.2  Frequency of Calibration

See Section 4.2.1.

4.2.3  Other Calibration Information

None.

5.     Data Acquisition Methods

The eddy covariance system consisted of a 3-D sonic anemometer/thermometer (SOLENT 1012R2A) for detecting the three velocity components and air temperature, the latter being derived from the speed of sound following Kaimal and Gaynor (1991), an open-path H2O krypton gas analyzer for measuring water vapor density in the air, and a closed-path dual H2O/CO2 IRGA (LI-COR 6262) for measuring water vapor density and CO2 concentration in the air.

The Solent sampled the wind speed components at 20.83 Hz, and its analog-to digital converter sampled the LI-COR signals at 10 Hz.  Prior to sampling, the latter signals had been passed through a passive filter with a 7 Hz cut-off frequency.  Spectral analysis showed that frequencies above 1 Hz made almost no contribution to fluxes.

For the flux system, all raw data were recorded using PC systems with backup tape drives.  Half-hour fluxes were calculated online.  For other measurements, all those data were recorded by data loggers (model 21X, Campbell Scientific, Inc., Logan, UT), which were networked together, using the model MD-9 network interface, along with the main system.  Every 3 hours, this network automatically transferred (using PC ANYWHERE software, Symantec Corp.) all data from the loggers to a network computer.  This computer was accessed from our laboratory at UBC through a communication system, which comprised a modem, cellular phone, and Yagi antenna at the site, and a phone and modem in the laboratory.  The Yagi antenna was mounted above the trees, and the cellular phone was housed in a thermostatically controlled box near the antenna.  At midnight, the site computer compressed the previous 24 hours of half-hour flux data, called the laboratory, and in 3 minutes transferred (using Kermit file transfer software) the compressed data to the laboratory computer.

6.    Observations

6.1   Data Notes

None.

6.2   Field Notes

None.

7.     Data Description

7.1    Spatial Characteristics

7.1.1 Spatial Coverage

All data were collected at the BOREAS SSA-OA site in the Prince Albert National Park (PANP).  North American Datum of 1983 (NAD83) coordinates for the site are latitude 53.62889° N, longitude 106.19779° W, and elevation of 600.63 m.

7.1.2 Spatial Coverage Map

Not applicable.

7.1.3 Spatial Resolution

Although the eddy covariance measurement is made at one point, it is well known that the fluxes measured with this technique can represent fluxes averaged over a relatively large area.  An analysis of the upwind land surface area that contributes to a scalar flux measurement, often referred to as “fetch” or “footprint,” is crucial in understanding the origins of the flux and any possible influences of spatial heterogeneity.  According to Blanken’s (1997) results (using Schuepp et al., 1990, model), the cumulative flux at 39 m reached 80% of the total flux at an upwind distance of 1,200 m under neutral conditions, 900 m under typical daytime stability conditions, and 2,700 m under typical nighttime stability conditions.  The corresponding values for the 4-m height (above the understory) were 130, 80, and 300 m.  Baldocchi (1997) suggests the latter values are overestimates.

.

From the above results, there was adequate fetch at the OA site because the forest extended for at least 3 km in all directions.

7.1.4 Projection

None.

7.1.5 Grid Description

None.

7.2   Temporal Characteristics

7.2.1 Temporal Coverage

The flux data were collected from 20-April to 31-December-1996.  The supporting meteorological data were collected from 02-February-1996 to 31-December-1996.  Note that Saskatchewan Research Council (SRC) (Airborne Flux and Meteorology (AFM) 07) operated a MESONET site at the OA (70 m southeast of main tower) through the study period.

7.2.2  Temporal Coverage Map

None.

7.2.3  Temporal Resolution

The data reported are 30-minute statistical mean values.

7.3 Data Characteristics

Data characteristics are defined in the companion data definition file (tf01tflx.def).

7.4 Sample Data Record

Sample data format shown in the companion data definition file (tf01tflx.def).

8. Data Organization

8.1 Data Granularity

All of the TF-01 SSA-OA Tower Flux, Meteorological, and Soil Temperature Data are contained in one dataset.

8.2 Data Format

The data file contains numerical and character fields of varying length separated by commas. The character fields are enclosed with single apostrophe marks. There are no spaces between the fields. Sample data records are shown in the companion data definition file (tf01tflx.def).

9. Data Manipulations

9.1  Formulae

9.1.1 Derivation Techniques and Algorithms

There are many equations and formulae used in the calculations of fluxes from the raw voltage signals. Readers are referred to the relevant references for details.

9.2  Data Processing Sequence

9.2.1  Processing Steps

Averages, variances, and covariances are calculated in real time, and coordinate rotation is applied on the half-hourly covariances and variances.  WPL corrections were made to the water vapor and carbon dioxide fluxes measured using the closed-path LI-COR 6262 IRGA.

BORIS staff processed these data by:

1) Reviewing the initial data files and loading them online for BOREAS team access.

2) Designing relational data base tables to inventory and store the data.

3) Loading the data into the relational data base tables.

4) Working with the team to document the data set.

5) Extracting the data into logical files.

9.2.2  Processing Changes

None.

9.3  Calculations

9.3.1  Special Corrections/Adjustments

WPL corrections were made to the water vapor and carbon dioxide fluxes measured using the closed-path LI-COR 6262 IRGA.  Broadening correction was done, but not online (see Chen et al., 1998, for summary of theory).

9.3.2  Calculated Variables

The Bowen ratio is the ratio of the sensible to latent heat flux.

9.4  Graphs and Plots

See Black et al., 1996; Chen et al., 1998; Blanken, 1997; and Yang, 1998.

10.   Errors

10.1  Sources of Error

None given.

10.2  Quality Assessment

10.2.1 Data Validation by Source

Data were checked and flagged for various conditions in the original data base at UBC (Z. Nesic). Relatively little data were missing in 4 m measurements in 1994 and 39 m in 1996.

10.2.2 Confidence Level/Accuracy Judgment

None given.

10.2.3 Measurement Error for Parameters

None given.

10.2.4 Additional Quality Assessments

None.

10.2.5 Data Verification by Data Center

Data were examined to check for spikes, values that are four standard deviations from the mean, long periods of constant values, and missing data.

11.   Notes

11.1  Limitations of the Data

None given.

11.2  Known Problems with the Data

The soil heat flux plates at plots 2, 3, and 5 did not collect any usable data.

11.3  Usage Guidance

Read this document carefully or contact Drs. T.A. Black and Z. Chen.

11.4 Other Relevant Information

None.

12.   Application of the Data Set

These data are useful for the study of water, energy, and carbon exchange in a mature aspen forest.

13.   Future Modifications and Plans

Data collection from the SSA-OA tower continued after 1996.  Contact Dr. T.A. Black for information about these data.

14.   Software

14.1 Software Description

None given.

14.2 Software Access

None given.

15.   Data Access

15.1  Contact for Data Center/Data Access Information

These BOREAS data are available from the Earth Observing System Data and Information System (EOS-DIS) Oak Ridge National Laboratory (ORNL) Distributed Active Archive Center (DAAC). The BOREAS contact at ORNL is:

ORNL DAAC User Services

Oak Ridge National Laboratory

(865) 241-3952

ornldaac@ornl.gov

ornl@eos.nasa.gov

15.2  Procedures for Obtaining Data

BOREAS data may be obtained through the ORNL DAAC World Wide Web site at http://www-eosdis.ornl.gov/ or users may place requests for data by telephone, electronic mail, or fax.

15.3  Output Products and Availability

Requested data can be provided electronically on the ORNL DAAC's anonymous FTP site or on various media including, CD-ROMs, 8-MM tapes, or diskettes.

The complete set of BOREAS data CD-ROMs, entitled "Collected Data of the Boreal Ecosystem-Atmosphere Study", edited by Newcomer, J., et al., NASA, 1999, are also available.

16. Output Products and Availability

16.1 Tape Products

None.

16.2 Film Products

None.

16.3 Other Products

These data are available on the BOREAS CD-ROM series.

17. References

17.1 Platform/Sensor/Instrument/Data Processing Documentation

None.

17.2 Journal Articles and Study Reports

Baldocchi, D.D. 1997. Flux footprints within and over forest canopy. Boundary-Layer Meteorology, 85, 273-292.

Black T.A., G. den Hartog, H.H. Neumann, P.D. Blanken, P.C. Yang, C. Russell, and Z. Nesic. 1996. Annual cycle of water vapor and carbon dioxide fluxes in and above a boreal aspen forest. Global Change Biology, 2, 101-111.

Blanken, P.D. 1997. Evaporation within and above a boreal aspen forest. Ph.D. Thesis of UBC , 79-84.

Chen, W.J., T.A. Black, P.C. Yang, A.G. Barr, H.H. Neumann, Z. Nesic, P.D. Blanken, M.D. Novak, J. Eley, R.J. Ketler, and R. Cuenca. 1998. Effects of climatic variability on the annual carbon sequestration by a boreal aspen forest. Global Change Biology (in press).

Fritschen, L.J. and L.W. Gay. 1979. Environmental Instrumentation. Springer-Verlag, Berlin, New York and Heidelberg.

Fuchs, M. and C.B. Tanner. 1968. Calibration and field tests of soil heat flux plates. Soil Science Society of America Proceedings, 32, 326-328.

Hook, W.R. and N.J.Livingston. 1996. Errors in converting time domain reflectometry measurements of propagation velocity to estimated of soil water content. Soil Sci. Soc. Amer. J., 59, 35-41.

Kaimal, J.C. and J.E. Gaynor. 1991. Another look at sonic thermometry. Boundary-Layer Meteorology, 56, 401-410.

Lee X., T.A. Black, and M.D. Novak. 1994. Comparison of flux measurements with open-and closed-path gas analyzers above an agricultural field and a forest floor. Boundary-Layer Meteorology, 67, 1995-202.

Leuning R. and K.M. King. 1992. Comparison of eddy covariance measurements of CO2 fluxes by open- and closed-path CO2 analyzers. Boundary-Layer Meteorology, 59, 297-311.

Pearcy, R.W., J. Ehleringer, H.A. Mooney, and P.W. Rundel. 1991. Plant physiological ecology: Field methods and instrumentation. Chapman and Hall, London and New York.

Schuepp P.H., M.Y. Leclerc, J.I. MacPerson, and R.L. Desjardins. 1990. Footprint prediction of scalar fluxes from analytical solutions of the diffusion equation. Boundary-Layer Meteorology, 50, 355-373.

Sellers, P. and F. Hall. 1994. Boreal Ecosystem-Atmosphere Study: Experiment Plan. Version 1994-3.0, NASA BOREAS Report (EXPLAN 94).

Sellers, P. and F. Hall. 1996. Boreal Ecosystem-Atmosphere Study: Experiment Plan. Version 1996-2.0, NASA BOREAS Report (EXPLAN 96).

Sellers, P., F. Hall, and K.F. Huemmrich. 1996. Boreal Ecosystem-Atmosphere Study: 1994 Operations. NASA BOREAS Report (OPS DOC 94).

Sellers, P., F. Hall, and K.F. Huemmrich. 1997. Boreal Ecosystem-Atmosphere Study: 1996 Operations. NASA BOREAS Report (OPS DOC 96).

Sellers, P., F. Hall, H. Margolis, B. Kelly, D. Baldocchi, G. den Hartog, J. Cihlar, M.G. Ryan, B. Goodison, P. Crill, K.J. Ranson, D. Lettenmaier, and D.E. Wickland. 1995. The boreal ecosystem-atmosphere study (BOREAS): an overview and early results from the 1994 field year. Bulletin of the American Meteorological Society. 76(9):1549-1577.

Sellers, P.J., F.G. Hall, R.D. Kelly, A. Black, D. Baldocchi, J. Berry, M. Ryan, K.J. Ranson, P.M. Crill, D.P. Lettenmaier, H. Margolis, J. Cihlar, J. Newcomer, D. Fitzjarrald, P.G. Jarvis, S.T. Gower, D. Halliwell, D. Williams, B. Goodison, D.E. Wickland, and F.E. Guertin. 1997. BOREAS in 1997: Experiment overview, scientific results, and future directions. Journal of Geophysical Research 102(D24):28,731-28,769.

Webb, E.K., G.I. Pearman, and R. Leuning. 1980. Correction of flux measurements for density effects due to heat and water vapor transfer. Quarterly Journal of the Royal Meteorological Society, 106, 85-100.

Yang, P.C. 1998. Carbon dioxide flux within and above a boreal aspen forest. Ph.D. thesis, University of British Columbia, Vancouver, Canada.

17.3  Archive/DBMS Usage Documentation

None.

18.   Glossary of Terms

None.

19.   List Of Acronyms

AES     - Atmospheric Environment Service

AFM     - Aircraft Flux and Meteorology

ASCII   - American Standard Code for Information Interchange

ATD     - Atmospheric Technology Division

ATI     - Applied Technologies, Inc.

BOREAS  - BOReal Ecosystem-Atmosphere Study

BORIS   - BOREAS Information System

CD-ROM  - Compact Disk-Read-Only Memory

DAAC    - Distributed Active Archive Center

EOS     - Earth Observing System

EOSDIS  - EOS Data and Information System

GMT     - Greenwich Mean Time

GSFC    - Goddard Space Flight Center

HTML    - Hyper-text Markup Language

i.d.    - inner diameter

IFC     - Intensive Field Campaign

IR      - Infrared

IRGA    - Infrared Gas Analyzer

LAI     - Leaf Area Index

NAD83   - North American Datum of 1983

NASA    - National Aeronautics and Space Administration

NEP     - Net Ecosystem Productivity

NSA     - Northern Study Area

OA      - Old Aspen

ORNL    - Oak Ridge National Laboratory

PANP    - Prince Albert National Park

PAR     - Photosynthetically Active Radiation

PC      - Personal Computer

PPFD    - Photosynthetic Photon Flux Density

SRC     - Saskatchewan Research Council

SSA     - Southern Study Area

TDR     - Time Domain Reflectometry

TF      - Tower Flux

UBC     - University of British Columbia

URL     - Uniform Resource Locator

20.  Document Information

20.1 Document Revision Date

Written:      04-Sep-1998

Last Updated: 20-Sep-1999

20.2 Document Review Date(s)

BORIS Review: 04-May-1999

Science Review:

20.3 Document ID

20.4  Citation

When using these data, please include the following acknowledgment:

Data were collected and processed by T. A. Black, Z. Nesic of the University of British Columbia.

If using data from the BOREAS CD-ROMs please also reference the data as:

Black, T.A., Nesic, Z., "Boreal Forest Atmosphere Interactions: Exchanges of Energy, Water Vapor and Trace Gases." In Collected Data of The Boreal Ecosystem-Atmosphere Study. Eds. J. Newcomer, D. Landis, S. Conrad, S. Curd, K. Huemmrich, D. Knapp, A. Morrell, J. Nickeson, A. Papagno, D. Rinker, R. Strub, T. Twine, F. Hall, and P. Sellers.  CD-ROM. NASA, 1999.

To cite the BOREAS CD-ROM set as a published volume, use:

J. Newcomer, D. Landis, S. Conrad, S. Curd, K. Huemmrich, D. Knapp, A. Morrell, J. Nickeson, A. Papagno, D. Rinker, R. Strub, T. Twine, F. Hall, and P. Sellers, eds. Collected Data of The Boreal Ecosystem-Atmosphere Study.  CD-ROM. NASA, 1999.

20.5 Document Curator

20.6 Document URL

Keywords

AIR TEMPERATURE

ASPEN

CARBON DIOXIDE CONCENTRATION

CARBON DIOXIDE FLUX

LATENT HEAT FLUX

METEOROLOGY

MOMENTUM FLUX

NET RADIATION

PAR

PHOTOSYNTHETIC PHOTON FLUX DENSITY

PHOTOSYNTHETICALLY ACTIVE RADIATION

PPFD

RAINFALL

SENSIBLE HEAT FLUX

SOIL HEAT FLUX

SOIL TEMPERATURE

SOIL WATER POTENTIAL

TOWER FLUX

VAPOR PRESSURE

WIND SPEED