BOREAS TF-04 SSA-YJP Tower Flux, Meteorological, and Canopy Condition Data

Summary

The BOREAS TF-04 team collected energy, carbon dioxide, and water vapor flux data at the BOREAS SSA-YJP site during the growing season of 1994.  In addition, meteorological data were collected both above and within the canopy.  The data are available in tabular ASCII files.

Table of Contents

*  1 Data Set Overview

*  2 Investigator(s)

*  3 Theory of Measurements

*  4 Equipment

*  5 Data Acquisition Methods

*  6 Observations

*  7 Data Description

*  8 Data Organization

*  9 Data Manipulations

*  10 Errors

*  11 Notes

*  12 Application of the Data Set

*  13 Future Modifications and Plans

*  14 Software

*  15 Data Access

*  16 Output Products and Availability

*  17 References

*  18 Glossary of Terms

*  19 List of Acronyms

*  20 Document Information

1. Data Set Overview

1.1 Data Set Identification

BOREAS TF-04 SSA-YJP Tower Flux, Meteorological, and Canopy Condition Data

1.2 Data Set Introduction

Measurements of CO2 and latent and sensible heat flux were made both above and within the BOReal Ecosystem-Atmosphere Study (BOREAS) Southern Study Area (SSA) Young Jack Pine (YJP) canopy during a growing season.  Combined with soil gas effluxes of CO2 and CH4, the data were used to determine daily and seasonal patterns in carbon fluxes, evapotranspiration, and environmental controls regulating the partitioning of available energy and net ecosystem productivity (NEP).  Comparisons were made between young and mature jack pine stands in proximity to one another in terms of NEP and water use.

1.3 Objective/Purpose

The objectives of this study were to investigate carbon, water, and energy fluxes in boreal forests through an integrated approach involving flux estimates across the atmosphere-forest and soil-atmosphere boundaries.  Eddy correlation measurements of CO2, latent and sensible heat fluxes, and momentum were made above the SSA-YJP stand.  Concentration profiles of CH4, 12CO2, and 13CO2 were determined within the canopy during one Intensive Field Campaign (IFC).  Soil-atmosphere flux studies employed soil depth vs. gas concentration measurements, flux chambers, and diffusion modeling to determine source and movement of CH4, 12CO2, and 13CO2 in the air-soil-water continuum.  The distribution and storage of carbon species in the soil profile were also determined.  Long-term carbon accumulation was evaluated by 14C decay of soil carbon.  Net, incoming, and Photosynthetically Active Radiation (PAR); leaf photosynthesis; and certain soil parameters (heat flux, thermal profile) were also measured at the site.

1.4 Summary of Parameters and Variables

Types of Data Collected:

Above-canopy fluxes: CO2, latent heat, sensible heat

Forest floor fluxes: CO2, sensible heat, latent heat

Radiation: Net, PAR, and shortwave

Profiles: CO2, air temperature, vapor pressure

Tree: Tree bole temperatures

Other Mean Variables:

Above-canopy: Wind direction and speed, air temperature, vapor pressure

Below-canopy: Wind speed, temperature, vapor pressure

1.5 Discussion

Flux data were collected from a 12-m tower in an 11- to 16-year old jack pine stand.  The trees were about 4 to 5 meters tall.  Flux and meteorological data were collected from mid-May through mid-September 1994.

1.6 Related Data Sets

BOREAS TF-04 CO2 and CH4 Chamber Flux Data from the SSA

BOREAS TF-05 SSA-OJP Tower Flux, Meteorological, and Soil Temperature Data

BOREAS TF-10 NSA-YJP Tower Flux, Meteorological, and Porometry Data

BOREAS TF-11 SSA Fen Tower Flux, Meteorological, and Soil Temperature Data

2. Investigator(s)

2.1 Investigator(s) Name and Title

Dr. Dean Anderson

United States Geological Survey

Dr. Rob Striegl

Hydrologist, USGS

Dr. Kimberly Wickland

Hydrologist, USGS

2.2 Title of Investigation

Exchange of Trace Gases, Water, and Energy in Disturbed and Undisturbed Boreal Forests

2.3 Contact Information

Contact 1

Dr. Rob Striegl

Hydrologist, USGS

Denver, CO

rstriegl@usgs.gov

Contact 2

Dr. Kimberly P. Wickland

Hydrologist, USGS

Denver, CO

Contact 3

K. Fred Huemmrich

University of Maryland

NASA GSFC

Greenbelt, MD

(301) 286-4862

(301) 286-0239 (fax)

Karl.Huemmrich@gsfc.nasa.gov

3. Theory of Measurements

The sonic anemometer/thermometer is designed to measure wind velocity components by transmitting and receiving sonic signals along fixed orthogonal directions.  The microcomputer electronics then processes this information and calculates the wind speed in three axes.  Since there are no moving parts to come into dynamic equilibrium with the air flow, the sonic anemometer/thermometer responds rapidly to wind velocity fluctuations.  It responds linearly to wind velocity and is free from contamination from pressure, temperature, and relative humidity.  The calibration of the sensor is established by its design parameters and therefore can be used as an absolute instrument.  The probe array is designed to minimize flow distortion created by the supporting base and to permit a very wide unobstructed coverage of the vertical component.

4. Equipment

4.1 Sensor/Instrument Description

4.1.1 Collection Environment

Measurements were collected from mid-May through mid-September 1994 in an 11- to 16-year-old jack pine stand.  Over that time period, temperature conditions went from slightly below freezing up to 29 °C.

4.1.2 Source/Platform

Instruments were mounted on a 12-m-tall Rohn tower.

4.1.3 Source/Platform Mission Objectives

The purpose of the tower was to suspend instruments to measure trace gas, energy fluxes, and meteorological variables above a young jack pine stand.

4.1.4 Key Variables

Sensible and latent heat fluxes were measured both above and below the tree canopies.  CO2 flux and concentration were measured above the canopy.  Measurements of radiation included net radiation, PAR, and shortwave radiation.  Meteorological measurements included wind speed and direction, friction velocity, air temperature, vapor pressure, air pressure, and rainfall.  Under the canopy, data on air temperature, vapor pressure, and wind speed were collected.  Bole temperature and leaf wetness data were collected.  Within the canopy, air temperature, vapor pressure, and air pressure were measured.

4.1.5 Principles of Operation

Heat, water, and CO2 fluxes were measured using eddy correlation techniques.  Meteorological measurements were collected using standard instruments and methods.

4.1.6 Sensor/Instrument Measurement Geometry

The placement of instruments on the tower was at the following heights above the ground:

Solar Radiation, LI-COR LI200S, at 12.9 m.

PAR sensor, LI-COR LI190SZ, at 12.9 m.

Air temperature and vapor pressure, Campbell Scientific, Inc., HMP35C, at 1.1, 9.1, and 12.2 m.  Used an unaspirated, white plastic 12-plate Gill radiation shield, Campbell Scientific, Inc., model 41002.

Wind speed and direction, R.M. Young 03001-5, at 1.1, 10.0, and 11.0 m.

Net Radiation at 9.1 m

Sonic anemometer, both Applied Technologies, Inc. (ATI), and Campbell, at 1.1 and 9.1 m.

LI-COR CO2 sensor at 9.1 m.

National Center for Atmospheric Research (NCAR)/Atmospheric Technology Division (ATD) CO2 sensor at 1.1 m.

Bole temperatures were measured in two trees.  In each tree, thermocouples were inserted into the north, east, south, and west sides of the bole, to approximately one half the radius of the trunk, at four heights.  The first tree was 4.6 m tall; about average for the canopy.  For that tree, the four heights were 0.58 m, 1.73 m, 2.79 m, and 3.68 m; the corresponding trunk diameters at those heights were 5.7 cm, 5.1 cm, 3.8 cm, and 2.9 cm. The second tree was about 3.6 m tall.  The four heights were 0.46 m, 1.35 m, 2.24 m, and 2.74 m; the corresponding diameters were 3.3 cm, 2.9 cm, 2.2 cm, and 1.1 cm.

Within-canopy air temperature and vapor pressure were measured with the Campbell Scientific, Inc., HMP35C, at 1.2 m above ground level.  An unaspirated, white plastic 12-plate Gill radiation shield (Campbell Scientific, Inc. model 41002) was also used.  Within-canopy atmospheric pressure was measured using the Setra 270, at 1.7 m

Leaf wetness sensors (Campbell Scientific, Inc., 237) were placed at heights of 1.6 m and 1.4 m.  The first leaf wetness sensor was deployed in a small opening in the trees, sloping about 40° to the northeast.  The second sensor was placed about 10 cm from a tree trunk, sloping about 40° to the west.

Rainfall was measured using a tipping bucket rain gauge (Weathertronics 6010) in a clearing approximately 10 m in diameter at 0.6 m height.  The 45°-angle cone above the rain gauge may have been slightly encroached upon by treetops as the average tree height was about 4.6 m.

4.1.7 Manufacturer of Sensor/Instrument

Sonic anemometer:

Applied Technologies, Inc.

1120 Delaware Ave.

Longmont, C)  80501

(303) 684-8722

(303) 684-8773 (fax)

sales@apptech.com

Sonic anemometer, CO2 sensor:

NCAR/ATD

P.O. Box 3000, 1850 Table Mesa Drive

Boulder, CO 80307  USA

(303) 497-8833,

(303) 497-8770 (fax)

atd_info@atd.ucar.edu

Sonic anemometer, temperature/humidity sensor HMP35C, Campbell 21X data logger, Gill radiation shield model 41002, leaf wetness sensor model 237, AM416 multiplexer, AM-ENCT insulating enclosure, CO2 sensor:

Campbell Scientific, Inc.

815 West 1800 North

Logan, UT 84321-1784

(435) 753-2342

(435) 750-9540 (fax)

info@campbellsci.com

LI-COR LI200S, LI190SZN, CO2 sensor:

LI-COR Environmental Division

4421 Superior Street

Lincoln, NE 68504

(800) 447-3576

(402) 467-3576

(402) 467-2819 (fax)

Wind direction and speed 03001-5:

R.M. Young Company

2801 Aero Park Drive

Traverse City, MI 49686

(616) 946-3980

(616) 946-4772 (fax)

met.sales@youngusa.com

Rain Gauge Weathertronics 6010:

WeatherMeasure Weathertronics

Qualimetrics, Inc.

1165 National Drive

Sacramento, CA 95834

(916) 928-1000

(916) 928-1165 (fax)

4.2 Calibration

None.

4.2.1 Specifications

Two problems remain, to one degree or another, with all existing sonic anemometers: distortion of the measured flow field by the anemometer array itself and reliable detection of the transmitted sound pulses by the anemometer electronics over a wide range of environmental conditions.

4.2.1.1 Tolerance

None.

4.2.2 Frequency of Calibration

None.

4.2.3 Other Calibration Information

None.

5. Data Acquisition Methods

The tower meteorological data were collected using a Campbell 21X data logger.  All sensors except the rain gauge were located on the flux tower.  Sensors were scanned every 5 s, and half-hour averages were recorded.  Vapor pressure was calculated as the product of saturated vapor pressure at air temperature and relative humidity (100% = 1).  Saturated vapor pressure was calculated using the Lowe (1977) equation.  The tipping bucket rain gauge (one tip = 0.25 mm of rain) was deployed in a clearing approximately 10 m in diameter.  The 45° cone above the rain gauge may have been slightly encroached upon by treetops.

The canopy meteorological data were collected using a Campbell 21X data logger.  Sensors were scanned every 60 s, and half-hour averages were recorded.  Vapor pressure was calculated as described above.  The reported air pressure was atmospheric (i.e., not corrected to sea level) rather than barometric pressure.  Air pressure was recorded to the nearest mb until day of year 215 at 2000 Greenwich Mean Time (GMT), and to the nearest hundredth of a mb thereafter.  The leaf wetness sensors were artificial leaf electrical resistance types, with interlacing gold plated copper fingers.  Water droplets that bridge between fingers lower the resistance.  These sensors were not painted or coated.  The manufacturer suggests that the transition from "wet" to "dry" for an uncoated sensor occurs between 50 and 200 kohms.  The first leaf wetness sensor was deployed in a small opening in the trees, sloping about 40° to the northeast.  The second leaf wetness sensor was deployed about 10 cm from a tree trunk, sloping about 40° to the west.

Tree bole temperatures were collected using a Campbell 21X data logger.  Copper-constantan thermocouples were glued into tree boles to make all of these temperature measurements.  A Campbell AM416 multiplexer was used to route the thermocouples to the logger.  An extra thermocouple reference junction was glued to the AM416 surface, and the AM416 was enclosed in a Campbell AM-ENCT insulating enclosure to minimize temperature gradients in the AM416.  Sensors were scanned every 5 s  during the last minute of each half-hour, and averages of the 13 readings were recorded.

Two trees were chosen to instrument.  The first was 4.6 m tall about average for the canopy.  Thermocouples were inserted into the north, east, south, and west sides, to approximately one half the radius of the trunk, at four heights.  The four heights were 0.58 m, 1.73 m, 2.79 m, and 3.68 m; the corresponding trunk diameters at those heights were 5.7 cm, 5.1 cm, 3.8 cm, and 2.9 cm.  The second tree was about 3.6 m tall.  The four heights were 0.46 m, 1.35 m, 2.24 m, and 2.74 m; the corresponding diameters were 3.3 cm, 2.9 cm, 2.2 cm, and 1.1 cm.  In the reported data set, the 16 temperatures from each tree were averaged together for each half-hour, and the mean temperature was reported.

6. Observations

6.1 Data Notes

Measurements began during IFC-1 and ended a day after IFC-3.  Equipment operated almost continuously.  Notable was the lack of CO2 data following a lightning strike and a malfunction of the CO2 sensor 16-Jun to 20-Jun and 10-Jul to 19-Jul-1994.  CO2 profile instruments were not operational until IFC-2.  Forest floor sensible and latent heat flux record had numerous lapses due to equipment problems.  Considering all measurements, IFC-3 had the most complete record.

6.2 Field Notes

None.

7. Data Description

7.1 Spatial Characteristics

7.1.1 Spatial Coverage

All data were collected at the BOREAS SSA-YJP site.  North American Datum of 1983 (NAD83) coordinates for the site are latitude 53.87581° N, longitude 104.64529° W, and elevation of 533.54 m.

7.1.2 Spatial Coverage Map

Not applicable.

7.1.3 Spatial Resolution

Data collected from flux towers are often thought of as point data.  However, particularly in terms of the eddy flux data, they actually represent an integrated upwind source region.  The size of the region being sampled is related to factors such as the height of the tower, the roughness of the canopy, and the wind speed.  An estimate of the upwind distance for the YJP site is 20 to 400 m upwind.

7.1.4 Projection

Not applicable.

7.1.5 Grid Description

Not applicable.

7.2 Temporal Characteristics

7.2.1 Temporal Coverage

Meteorological data were collected from 02- to 06-Sep-1993, and during 1994 from 15-May to 20-Sep.  Within-canopy meteorological data were collected continuously during 1994 from 3-June to 20-September, except for a gap from 04- to 07-Aug.  Tree bole temperature data were collected continuously from 10-Jun to 20-Sep-1994, except for a gap from 14-Jun to 21-Jun.  Flux data were collected from 26-May to 20-September, 1994.  There were gaps in CO2 data following a lightning strike and a malfunction of the CO2 sensor 16-Jun to 20-Jun and 10-Jul to 19-Jul-1994.  CO2 profile instruments were not operational until IFC-2.  The forest floor sensible and latent heat flux record had numerous lapses due to equipment problems.

7.2.2 Temporal Coverage Map

None.

7.2.3 Temporal Resolution

Meteorological and radiation sensors were scanned every 5 s, and half-hour averages were recorded.  Within-canopy meteorology data sensors were scanned every 60 s, and half-hour averages were recorded.  Tree bole temperature sensors were scanned every 5 s during the last minute of each half-hour, and averages of the 13 readings were recorded.

7.3 Data Characteristics

Data characteristics are defined in the companion data definition file (tf04flux.def)

7.4 Sample Data Record

Sample data format shown in the companion data definition file (tf04flux.def).

8. Data Organization

8.1 Data Granularity

All of the SSA-YJP Tower Flux, Meteorological, and Canopy Condition Data are contained in one dataset.

8.2 Data Format

The data file contains numerical and character fields of varying length separated by commas. The character fields are enclosed with single apostrophe marks. There are no spaces between the fields. Sample data records are shown in the companion data definition file (tf04flux.def).

9. Data Manipulations

9.1 Formulae

9.1.1 Derivation Techniques and Algorithms

Vapor pressure was calculated as product of saturated vapor pressure at air temperature and relative humidity.  Saturated vapor pressure was calculated using the Lowe (1977) equation.

Tree bole temperatures were scanned every 5 s during the last minute of each half-hour, and averages of the 13 readings were recorded.  Thermocouples were inserted into the boles of two trees on the north, east, south, and west sides, to approximately one half the radius of the trunk, at four heights.  In the reported data set the 16 temperatures from each tree were averaged together for each half-hour, and the mean temperature was reported.

9.2 Data Processing Sequence

9.2.1 Processing Steps

BORIS staff processed these data by:

1) Reviewing the initial data files and loading them online for BOREAS team access.

2) Designing relational data base tables to inventory and store the data.

3) Loading the data into the relational data base tables.

4) Working with the team to document the data set.

5) Extracting the data into logical files.

9.2.2 Processing Changes

None.

9.3 Calculations

9.3.1 Special Corrections/Adjustments

Air pressure was recorded to the nearest mb until day of year 215 at 2000 GMT, and to the nearest hundredth of a mb thereafter.

9.3.2 Calculated Variables

See Section 9.1.1.

9.4 Graphs and Plots

None.

10. Errors

10.1 Sources of Error

None given.

10.2 Quality Assessment

10.2.1 Data Validation by Source

None given.

10.2.2 Confidence Level/Accuracy Judgment

None given.

10.2.3 Measurement Error for Parameters

None given.

10.2.4 Additional Quality Assessments

None given.

10.2.5 Data Verification by Data Center

Data were examined to check for spikes, values that are four standard deviations from the mean, long periods of constant values, and missing data.

11. Notes

11.1 Limitations of the Data

These data were collected during the growing season; thus, there was little data collected under cold conditions.

11.2 Known Problems with the Data

The tipping bucket rain gauge was deployed in clearing about 10 m in diameter.  The 45° cone above the rain gauge may have been slightly encroached upon by treetops.

There is a gap in the CO2 data following a lightning strike and a malfunction of the CO2 sensor 16-Jun to 20-Jun and 10-Jul to 19-Jul-1994.  CO2 profile instruments were not operational until IFC-2.  The forest floor sensible and latent heat flux record had numerous lapses due to equipment problems.

11.3 Usage Guidance

None given.

11.4 Other Relevant Information

None.

12. Application of the Data Set

These data are useful for the study of water, energy, and carbon exchange in a young jack pine forest.

13. Future Modifications and Plans

None.

14. Software

14.1 Software Description

None given.

14.2 Software Access

None given.

15.   Data Access

15.1  Contact for Data Center/Data Access Information

These BOREAS data are available from the Earth Observing System Data and Information System (EOS-DIS) Oak Ridge National Laboratory (ORNL) Distributed Active Archive Center (DAAC). The BOREAS contact at ORNL is:

ORNL DAAC User Services

Oak Ridge National Laboratory

(865) 241-3952

ornldaac@ornl.gov

ornl@eos.nasa.gov

15.2  Procedures for Obtaining Data

BOREAS data may be obtained through the ORNL DAAC World Wide Web site at http://www-eosdis.ornl.gov/ or users may place requests for data by telephone, electronic mail, or fax.

15.3  Output Products and Availability

Requested data can be provided electronically on the ORNL DAAC's anonymous FTP site or on various media including, CD-ROMs, 8-MM tapes, or diskettes.

The complete set of BOREAS data CD-ROMs, entitled "Collected Data of the Boreal Ecosystem-Atmosphere Study", edited by Newcomer, J., et al., NASA, 1999, are also available.

16. Output Products and Availability

16.1 Tape Products

None.

16.2 Film Products

None.

16.3 Other Products

These data are available on the BOREAS CD-ROM series.

17. References

17.1 Platform/Sensor/Instrument/Data Processing Documentation

None.

17.2 Journal Articles and Study Reports

Lowe, P.R. 1977. An approximating polynomial for the computation of saturation vapor pressure. Journal of Applied Meteorology, 16(1): 100-103.

Sellers, P. and F. Hall. 1994. Boreal Ecosystem-Atmosphere Study: Experiment Plan. Version 1994-3.0, NASA BOREAS Report (EXPLAN 94).

Sellers, P. and F. Hall. 1996. Boreal Ecosystem-Atmosphere Study: Experiment Plan. Version 1996-2.0, NASA BOREAS Report (EXPLAN 96).

Sellers, P., F. Hall, and K.F. Huemmrich. 1996. Boreal Ecosystem-Atmosphere Study: 1994 Operations. NASA BOREAS Report (OPS DOC 94).

Sellers, P., F. Hall, and K.F. Huemmrich. 1997. Boreal Ecosystem-Atmosphere Study: 1996 Operations. NASA BOREAS Report (OPS DOC 96).

Sellers, P., F. Hall, H. Margolis, B. Kelly, D. Baldocchi, G. den Hartog, J. Cihlar, M.G. Ryan, B. Goodison, P. Crill, K.J. Ranson, D. Lettenmaier, and D.E. Wickland. 1995. The boreal ecosystem-atmosphere study (BOREAS): an overview and early results from the 1994 field year. Bulletin of the American Meteorological Society. 76(9):1549-1577.

Sellers, P.J., F.G. Hall, R.D. Kelly, A. Black, D. Baldocchi, J. Berry, M. Ryan, K.J. Ranson, P.M. Crill, D.P. Lettenmaier, H. Margolis, J. Cihlar, J. Newcomer, D. Fitzjarrald, P.G. Jarvis, S.T. Gower, D. Halliwell, D. Williams, B. Goodison, D.E. Wickland, and F.E. Guertin. 1997. BOREAS in 1997: Experiment overview, scientific results, and future directions. Journal of Geophysical Research 102(D24):28,731-28,769.

17.3 Archive/DBMS Usage Documentation

None.

18. Glossary of Terms

None.

19. List of Acronyms

ASCII   - American Standard Code for Information Interchange

ATD     - Atmospheric Technology Division

ATI     - Applied Technologies, Inc.

BOREAS  - BOReal Ecosystem-Atmosphere Study

BORIS   - BOREAS Information System

CD-ROM  - Compact Disk-Read-Only Memory

DAAC    - Distributed Active Archive Center

EOS     - Earth Observing System

EOSDIS  - EOS Data and Information System

GMT     - Greenwich Mean Time

GSFC    - Goddard Space Flight Center

HTML    - Hyper-text Markup Language

IFC     - Intensive Field Campaign

NAD83   - North American Datum of 1983

NASA    - National Aeronautics and Space Administration

NCAR    - National Center for Atmospheric Research

NEP     - Net Ecosystem Productivity

NSA     - Northern Study Area

ORNL    - Oak Ridge National Laboratory

PANP    - Prince Albert National Park

PAR     - Photosynthetically Active Radiation

SSA     - Southern Study Area

TF      - Tower Flux

URL     - Uniform Resource Locator

USGS    - United States Geological Survey

YJP     - Young Jack Pine

20. Document Information

20.1 Document Revision Date

Written: 22-April-1999

Revised: 25-May-1999

20.2 Document Review Date(s)

BORIS Review: 04-May-1999

Science Review:

20.3 Document ID

20.4  Citation

When using these data, please include the following acknowledgment:

Data were collected and processed by Dean Anderson, Rob Striegl, and Kimberly Wickland of the United States Geological Survey.

If using data from the BOREAS CD-ROMs please also reference the data as:

Anderson, D., R. Striegl, and K. Wickland, "Exchange of Trace Gases, Water, and Energy in Disturbed and Undisturbed Boreal Forests." In Collected Data of The Boreal Ecosystem-Atmosphere Study. Eds. J. Newcomer, D. Landis, S. Conrad, S. Curd, K. Huemmrich, D. Knapp, A. Morrell, J. Nickeson, A. Papagno, D. Rinker, R. Strub, T. Twine, F. Hall, and P. Sellers.  CD-ROM. NASA, 1999.

To cite the BOREAS CD-ROM set as a published volume, use:

J. Newcomer, D. Landis, S. Conrad, S. Curd, K. Huemmrich, D. Knapp, A. Morrell, J. Nickeson, A. Papagno, D. Rinker, R. Strub, T. Twine, F. Hall, and P. Sellers, eds. Collected Data of The Boreal Ecosystem-Atmosphere Study.  CD-ROM. NASA, 1999.

20.5 Document Curator

20.6 Document URL

Keywords

AIR TEMPERATURE

CARBON DIOXIDE CONCENTRATION

CARBON DIOXIDE FLUX

JACK PINE

LATENT HEAT FLUX

METEOROLOGY

NET RADIATION

PAR

PHOTOSYNTHETIC PHOTON FLUX DENSITY

PHOTOSYNTHETICALLY ACTIVE RADIATION

PPFD

RAINFALL

SENSIBLE HEAT FLUX

TOWER FLUX

VAPOR PRESSURE

WIND SPEED