1.  TITLE

1.1  Data Set Identification.

     Quick Look Boundary Layer Height.

1.2  Data Base Table Name.

     LIDAR_HEIGHT_DATA.

1.3  CD-ROM File Name.

      \DATA\ATMOS\LIDAR_HT\yyyyMULT.LHD

     Note: capital letters indicate fixed values that appear on the CD-ROM 
     exactly as shown here, lower case indicates characters (values) that 
     change for each path and file.

     The format used for the filenames is: yyyyMULT.sfx, where yyyy are the
     four digits of the century and year (e.g. 1987 and 1989). The filename 
     extension (.sfx), identifies the data set content for the file (see 
     Section 8.2) and is equal to .LHD for this data set.

1.4  Revision Date Of This Document.

     May 4, 1994.
 
     Warning:  This document has not been checked for technical or editorial
               accuracy by the FIFE Information Scientist. There may be 
               inconsistencies with other documents, technical or editorial 
               errors that were inadvertently introduced when the document was 
               compiled or references to preliminary data that were not 
               included on the final CD-ROM.

               Previous versions of this document have been reviewed by the 
               Principal Investigator, the person who transmitted the data to 
               FIS, a FIS staff member, or a FIFE scientist generally familiar 
               with the data.

                         2.  INVESTIGATOR(S)

2.1  Investigator(s) Name And Title.

     Dr. Edwin W. Eloranta
     University of Wisconsin-Madison

2.2  Title Of Investigation.

     LIDAR Measurements of Boundary Layer, Aerosol Scattering and Clouds.

2.3  Contacts (For Data Production Information).

      ________________________________________________________________________
     |              |         Contact 1       |       Contact 2               |
     |______________|_________________________|_______________________________|
     |2.3.1 Name    |George Vassiliou         |Dr. Edwin W. Eloranta          |
     |2.3.2 Address |Dept. of Meteorology     |Dept. of Meteorology           |
     |              |University of Wisconsin  |University of Wisconsin        |
     |      City/St.|Madison, WI              |Madison, WI                    |
     |      Zip Code|53706                    |53706                          |
     |2.3.3 Tel.    |(608) 262-0792           |(608) 262-7327                 |
     |2.3.4 Email   |                         |eloranta@lidar.meteor.wisc.edu |
     |______________|_________________________|_______________________________|

2.4  Requested Form of Acknowledgment.

     The Quick Look Boundary Layer Height data were produced by E.W. Eloranta.
     The contribution of these data is appreciated.

                            3.  INTRODUCTION

3.1  Objective/Purpose.

     The goals were to measure wind and turbulence profiles, convective 
     boundary layer depth, and optical depth of mixed layer haze.

3.2  Summary of Parameters.

     Mixed layer height above ground level.

3.3  Discussion.

     The Volume Imaging LIDAR (VIL) system of the University of Wisconsin,
     operated during FIFE and all LIDAR return signals measured at a 90 degree 
     elevation angle were averaged and stored in a file. From plots of those 
     profiles, clouds up to 15 km AGL can be identified.

     By choosing appropriate reflectivity levels, the data from the University
     of Wisconsin LIDAR have been used to derive unique 2-D and 3-D views of 
     the Atmospheric Boundary Layer (ABL) structure, and the variations in 
     that structure with time. some of these views are available in the GRABBAG 
     directory on FIFE CD-ROM Volume 1. Color videos were also produced and are
     available from the Archive listed in Section 13.1. These views and videos
     provide important insights into many problems facing investigators in 
    all aspects of FIFE, including scaling and the representativeness of point 
     and line samples.

                        4.  THEORY OF MEASUREMENTS

Volume Imaging LIDAR measures the radial (along-beam) velocity as a function of
range using light-scattering particles in the air as tracers. When the LIDAR
beam is directed straight upward and the backscattered return as function of
height is recorded, vertical aerosol profiles may be determined. Various point-
ing and scanning schemes permit measurement of a variety of mean and turbulent
quantities based on often-met assumptions about the flow.

The remote-sensing character of LIDAR offers the ability to measure flow
parameters simultaneously at all the heights in a profile. Alternatively, the
LIDAR scanning at lower elevation angles can probe flow characteristics over a
large area or volume. The vertical profiles of momentum flux and turbulent
intensity have been the object of experimental measurements to understand and
model the dynamics of the atmosphere.

Aerosol backscattering from the convective boundary layer shows spatial variat-
ions due to non-uniform mixing of the naturally occurring aerosol. The motion
of this spatial structure can be observed with the VIL and used to derive wind
speed and direction. Winds are derived by computing 2-dimensional cross correl-
ations between successive VIL Constant Altitude Plan Position Indicator (CAPPI)
images. Because these measurements are averaged over the VIL scan area, it is
possible to avoid the variations due to local wind gusts. Very stable estimates
of the area averaged wind can be obtained within approximately 3 minute period
required to obtain a pair of CAPPI images.

                            5.  EQUIPMENT

5.1  Instrument Description.

     The Volume Imaging LIDAR (VIL) is an elastic backscatter LIDAR designed to
     image the 4-dimensional structure of the atmosphere. This system couples
     an energetic, relatively high pulse repetition rate laser with a sensitive
     receiver, and a fast computer controlled angular scanning system.

     This energy is directed through a germanium wedged plate that acts as a
     transmit/receive (T/R) switch and into a ZnSe Fresnel rhomb, which changes
     the polarization to circular. The beam then enters a 27.94 cm parabolic-
     parabolic off-axis telescope which provides excellent decoupling between
     transmitter and detector. The telescope output is directed either 
     vertically through the roof (of the semi-trailer) to an azimuth/elevation 
     scanner or horizontally through a window by a 39.2 cm flat mirror.

     5.1.1  Platform.

            The LIDAR is mounted on the roof of a semi-trailer.

     5.1.2  Mission Objectives.

            The University of Wisconsin developed a semi-trailer-mounted Volume
            Imaging LIDAR system for making atmospheric measurements of winds,
            turbulence, and backscatter, using aerosols as tracers.

     5.1.3  Key Variables.

            Mixed layer height above ground level.

     5.1.4  Principles of Operation.

            Return signals pass through the system on a precise reverse path,
            and are changed to p-polarization on emerging from the Fresnel
            rhomb. These signals are then reflected from the T/R switch onto 
            the detector where heterodyne mixing with the local oscillator 
            occurs. The 20 MHz offset in the local oscillator frequency permits 
            discrimination between receding and approaching velocity components 
            of scatterers.

            The volume imaging LIDAR measures the radial component of the air
            velocity (positive toward the LIDAR) as a function of range along
            the beam. The LIDAR performed a conical scan through a full circle
            in azimuth at constant elevation angle, to obtain the radial
            component of the air velocity. Azimuth is measured clockwise from
            north at a specified time. The scan was repeated many times within
            a period long enough (typically 1 h) to sample a number of 
            advecting eddies up to the largest scale of interest in the 
            turbulent spectrum.

     5.1.5  Instrument Measurement Geometry.

            The system scanning capability through the roof:
                Elevation -5 deg. to 90 deg., Azimuth 0 deg. to 360 deg.,
                           1 deg. accuracy.
            The system scanning capability through the window:
                Elevation +/-10 deg., Azimuth +/-10 deg.,
                           0.001 deg. accuracy.

     5.1.6  Manufacturer of Instrument.

            University of Wisconsin
            Madison, Wisconsin.

5.2  Calibration.

     Among the first data taken were returns from a 2.1 m diameter disc located
     at 2400 m range. The disc was covered with sandpaper of known reflectance.
     Scattered energy from 1000 pulses was averaged and the result was compared
     with expected signal levels, adjusted for such things as measured 2-way
     efficiency of system optics (35%, determined by auto-collimation), carbon
     dioxide and water atmospheric absorption, truncation losses, shot noise
     level, etc.

     5.2.1  Specifications.

            Transmitter:
              Average power                  20 W
              Repetition rate                30 Hz
              Wavelength                     106.4 nm

            Receiver:
              Diameter                       0.5 m
              Angular scan rate              25 deg. s^-1
              APD quantum efficiency         35%
              Range resolution               7.5 m
              Optical bandwidth              1.0 nm
              Average data rate              0.5 GB h^-1 (approx.)

            Data Processing/storage:
              Control computer               DEC VAX/750 with CSPI array
                                               processor
              Realtime display computer      Stardent GS 1000
              Realtime acquisition computer  DEC LSI 11/72
              Data storage device            2.6 GB Hitachi optical disk

            5.2.1.1  Tolerance.

                Due primarily to pressure changes within the TEA gas over the
                pulse generation time, the frequency of the pulse changes over
                its lifetime, leading the frequency modulation or chirp on the
                order of several hundred KHz to several MHz. High chirps are
                clearly unacceptable for Doppler systems trying to achieve
                measurement accuracies of 1 to 2 ms^1 (190-380 kHz).

     5.2.2  Frequency of Calibration.

            Calibration is performed before each data collection.

     5.2.3  Other Calibration Information.

            While performing the calibration, it became clear that at least 50
            pulses were needed in order to get meaningful data. Single pulse
            return particularly for spinning targets, appear extremely noisy
            due to the Rayleigh phasor fluctuations of many sandpaper 
            scattering centers, while averaging provides good absolute levels 
            for calibrating and clarifies the output pulse shape.

            To corroborate this pulsed calibration, a CW calibration was
            performed using only the 0.6 W output hybrid laser, a small disc
            covered with the same sandpaper at 160 m, and the telescope focused
            at 160 m instead of 2.4 km. Observed signal/noise ratio was 43 dB
            while the expected was 50 dB, confirming the 7 dB discrepancy.

                             6.  PROCEDURE

6.1  Data Acquisition Methods.

     The volume imaging LIDAR operated with a carbon dioxide laser
     transmitting at 106.4 nanometer wavelength. The transmitted energy is
     collimated by an off-axis paraboloid telescope and directed into the 
     atmosphere through a scanner mounted on the roof of the semi-trailer that 
     houses the system. The same telescope collects radiation backscattered 
     from aerosol particles that are carried with the air motions. The 
     telescope focuses the light on a HgCdTe detector, where the atmospheric 
     signal mixes coherently with a beam from the local oscillator, which is 
     another continuous wave laser held at constant offset frequency from the 
     injection laser.

     High bandwidth data acquisition is sustained during extended experiments
     by using a 7 gigabyte write once optical disk for data storage. A Stellar
     GS-1000 graphics computer provides 1280 x 1024 pixel resolution color 
     LIDAR images.

     Because cirrus level winds are typically 20-40 ms^-1, clouds move before
     the cloud volume could be completely scanned. In order to generate 3-
     dimensional images of fast moving cirrus, the LIDAR repeatedly scans a
     plane perpendicular to the mean cloud layer wind. Three-dimensional scenes
     are displayed with the third spatial dimension computed from the time
     between images multiplied by the wind speed.

6.2  Spatial Characteristics.

     The FIFE study area, with areal extent of 15 km by 15 km, is located south 
     of the Tuttle Reservoir and Kansas River, and about 10 km from Manhattan, 
     Kansas, USA. The northwest corner of the area has UTM coordinates of 
     4,334,000 Northing and 705,000 Easting in UTM Zone 14.

     6.2.1  Spatial Coverage.

            The LIDAR operated from a relatively high vantage point in an area
            of gently rolling terrain approximately 12 km south of Manhattan,
            Kansas within the FIFE study area.

            SITEGRID_ID  STATION_ID NORTHING  EASTING LATITUDE  LONGITUDE
            ------------ ---------- -------- -------- --------- ----------
            3539-LIW            113  4326922   712836 39 04 02  -96 32 24
            3639-LIW            123  4326848   712850 39 04 00  -96 32 23

            ELEVATION
            ----------

            447

     6.2.2  Spatial Resolution.

            These are point data. However, the full width at half maximum of
            the laser power was 0.37 microseconds, which is equivalent to 55-m
            spatial resolution. The processor's minimum gate size was consider-
            ably larger, so the along-beam resolution of the LIDAR was slightly
            more than 150 m.

            For boundary layer observations the LIDAR is typically programmed 
            to repeatedly scan an atmospheric volume consisting of the 
            elevation angles between the horizon and 20 degrees inside an 
            azimuthal sector of 30 to 60 degrees. Clear air aerosol structure 
            is typically recorded with 7.5 or 15 meter resolution at ranges 
            between the LIDAR and 15 km.

            The VIL also provides high spatial resolution depictions of cirrus
            cloud structure. Cirrus clouds are easily detected at ranges of 100
            km. Detailed cirrus images showing a 120 km horizontal extent with
            60 m resolution are routinely obtained.

6.3  Temporal Characteristics.

     6.3.1  Temporal Coverage.

            The overall time period of data acquisition was from June 30, 1987
            through July 9, 1987 and July 28, 1989 through August 11, 1989.
            During that period, data were collected on the following 23 days:

                   OBS_DATE             OBS_DATE             OBS_DATE 
                   ---------            ---------            ---------
                   30-JUN-87            28-JUL-89            05-AUG-89
                   01-JUL-87            29-JUL-89            06-AUG-89
                   02-JUL-87            30-JUL-89            07-AUG-89
                   05-JUL-87            31-JUL-89            08-AUG-89
                   06-JUL-87            01-AUG-89            09-AUG-89
                   07-JUL-87            02-AUG-89            10-AUG-89
                   08-JUL-87            03-AUG-89            11-AUG-89
                   09-JUL-87            04-AUG-89

     6.3.2  Temporal Resolution.

            The pulse repetition rate for the measurements was 30 Hz. Scans are
            repeated at intervals between 2.5 and 5 minutes. Each volume scan
            consists of between ~4500 and ~9000 LIDAR profiles; producing 5-10
            million independent measurements of LIDAR backscattering in the
            scanned volume.

                           7.  OBSERVATIONS

7.1  Field Notes.

     None.

                         8.  DATA DESCRIPTION

8.1  Table Definition With Comments.

     The SQL definition for this table is found in the LIDAR_HT.TDF file found 
     on the FIFE CD-ROM Volume 1.

8.2  Type of Data.

--------------------------------------------------------------------------------
|                 8.2.1                  |               |          |          |
|Parameter/Variable Name                 |               |          |          |
--------------------------------------------------------------------------------
|    |               8.2.2               |     8.2.3     |  8.2.4   |  8.2.5   |
|    |Parameter/Variable Description     |Range          |Units     |Source    |
--------------------------------------------------------------------------------
|SITEGRID_ID                             |               |          |          |
|    |This is a FIS grid location code.  |               |          |FIS       |
|    |Site grid codes (SSEE-III) give    |               |          |          |
|    |the south (SS) and east (EE) cell  |               |          |          |
|    |number in a 100x100 array of 200m  |               |          |          |
|    |square cells.  The last 3          |               |          |          |
|    |characters (III) are an instrument |               |          |          |
|    |identifier.                        |               |          |          |
--------------------------------------------------------------------------------
|STATION_ID                              |               |          |          |
|    |The staton ID designating the      |min = 113,     |          |UNIVERSITY|
|    |location of the observations.      |max = 123      |          |OF WISCON |
|    |                                   |               |          |SIN       |
--------------------------------------------------------------------------------
|OBS_DATE                                |               |          |          |
|    |The date of the observations.      |min = 30-JUN-87|          |UNIVERSITY|
|    |                                   |,              |          |OF WISCON |
|    |                                   |max = 11-AUG-89|          |SIN       |
--------------------------------------------------------------------------------
|OBS_TIME                                |               |          |          |
|    |The time that the osbservation     |min = 4,       |[GMT]     |UNIVERSITY|
|    |was taken.                         |max = 2353     |          |OF WISCON |
|    |                                   |               |          |SIN       |
--------------------------------------------------------------------------------
|MIXED_LAYER_HEIGHT                      |               |          |          |
|    |The height of the mixed layer      |min = 65,      |[meters]  |VOLUME IMA|
|    |above the ground.                  |max = 2250,    |          |GING LIDAR|
|    |                                   |missing = -9999|          |          |
--------------------------------------------------------------------------------
|FIFE_DATA_CRTFCN_CODE                   |     **        |          |          |
|    |The FIFE Certification Code for    |CPI=checked by |          |FIS       |
|    |the data, in the following format: |principal inves|          |          |
|    |CPI (Certified by PI), CPI-???     |tigator,       |          |          |
|    |(CPI - questionable data).         |CPI-MRG=merged |          |          |
|    |                                   |data,          |          |          |
|    |                                   |CPI-???= CPI-qu|          |          |
|    |                                   |estionable data|          |          |
--------------------------------------------------------------------------------
|LAST_REVISION_DATE                      |               |          |          |
|    |The last revision date for the     |min = 24-AUG-89|          |FIS       |
|    |data, in the format (DD-MMM-YY).   |,              |          |          |
|    |                                   |max = 28-AUG-89|          |          |
--------------------------------------------------------------------------------
Footnote:

   ** Decode the FIFE_DATA_CRTFCN_CODE field as follows:

      The primary certification codes are:

      EXM - Example or Test data (not for release)
      PRE - Preliminary (unchecked, use at your own risk)
      CPI - Checked by Principal Investigator (reviewed for quality)
      CGR - Checked by a group and reconciled (data comparisons and
            cross checks)

      The certification code modifiers are:

      PRE-NFP  - Preliminary - Not for publication, at the request of
                 investigator.
      CPI-MRG  - PAMS data which is "merged" from two separate receiving
                 stations to eliminate transmission errors.
      CPI-???  - Investigator thinks data item may be questionable.

8.3  Sample Data Base Data Record.

     SITEGRID_ID STATION_ID OBS_DATE  OBS_TIME MIXED_LAYER_HEIGHT
     ----------- ---------- --------- -------- ------------------
     3539-LIW           113 30-JUN-87     2353               1238
     3539-LIW           113 01-JUL-87        4               1151
     3539-LIW           113 01-JUL-87        9               1148
     3539-LIW           113 01-JUL-87     1450                519

     FIFE_DATA_CRTFCN_CODE LAST_REVISION_DATE
     --------------------- ------------------
     CPI                   24-AUG-89
     CPI                   24-AUG-89
     CPI                   24-AUG-89
     CPI                   24-AUG-89

8.4  Data Format.

     The CD-ROM file format consists of numerical and character fields of 
     varying length separated by commas. The character fields are enclosed with 
     a single apostrophe. There are no spaces between the fields.  Each file 
     begins with five header records.  Header records contain the following 
     information:

     Record 1    Name of this file, its table name, number of records in
                 this file, path and name of the document that describes 
                 the data in this file, and name of principal investigator 
                 for these data.
     Record 2    Path and filename of the previous data set, and path and 
                 filename of the next data set.  (Path and filenames for files 
                 that contain another set of data taken at the same site on 
                 the same day.)
     Record 3    Path and filename of the previous site, and path and filename 
                 of the next site.  (Path and filenames for files of the same 
                 data set taken on the same day for the previous and next 
                 sites (sequentially numbered by SITEGRID_ID)).
     Record 4    Path and filename of the previous date, and path and filename 
                 of the next date.  (Path and filenames for files of the same 
                 data set taken at the same site for the previous and next 
                 date.)
     Record 5    Column names for the data within the file, delimited by 
                 commas.
     Record 6    Data records begin.

     Each field represents one of the attributes listed in the chart in 
     section 8.2 and described in detail in the TDF file (see Section 8.1). 
     These fields are in the same order as in the chart.

8.5  Related Data Sets.

     NOAA Wind Profiles Using LIDAR.
     FIFE Radiosonde Wind Profiles.
     NOAA Radiosonde Observations.
     FIFE Radiosonde Data.

                         9.  DATA MANIPULATIONS

9.1  Formulas.

     9.1.1  Derivation Techniques/Algorithms.

            A data analysis and real time control of the system are facilitated
            by 2-dimensional and 3-dimensional displays of data.

9.2  Data Processing Sequence.

     9.2.1  Processing Steps and Data Sets.

            Not available at this revision.

     9.2.2  Processing Changes.

            None.

9.3  Calculations.

     9.3.1  Special Corrections/Adjustments.

            The energy and frequency of the outgoing pulse were monitored by
            mixing on a second detector a reflection of the transmitted pulse
            from an optical element with a beam split from the local 
            oscillator. The processor acquired data from this pulse monitor 
            during the first two range gates and then switched to the signal 
            detector. Atmospheric velocities were corrected by any frequency 
            offset detected by the pulse monitor.

9.4  Graphs and Plots.

     None.

                          10.  ERRORS

10.1  Sources of Error.

      The LIDAR measurements are subject to errors that should be considered.
      Any constant bias is inconsequential in the turbulence analysis because
      the turbulence quantities are computed relative to the measured average
      coefficients: A(0), which includes the effects of vertical wind and
      divergence; A(1), which is the northerly component of horizontal wind
      multiplied by the constant elevation angle.

      The LIDAR measurements also suffer from random errors, partly caused by
      imperfect frequency control, and partly in common with all coherent
      systems using many randomly moving scatterers as targets.

10.2  Quality Assessment.

      10.2.1  Data Validation by Source.

              An unsolved issue was the stability of the reference frequency
              (against which the frequency of the returned pulse must be
              compared). This can lead to biases which at present, can be
              partially corrected by manual inspection of the data and the
              detection of "outliers".

      10.2.2  Confidence Level/Accuracy Judgment.

              The accuracy of individual radial velocity measurements is +/-
              0.25 m^-1. This should result in experimental errors in the 
              momentum flux of the order of 6.25 x 10^-2[m^2][s^-2], well below 
              the typical values which lie in the range of -0.2[m^2][s^-2] to 
              -2.5[m^2][s^-2].

      10.2.3  Measurement Error for Parameters and Variables.

              Although the LIDAR suffered non-trivial instrumental error in the
              velocity measurements (approximately 0.4[m^2][s^-2] variance), 
              the self-cancellation inherent in the method made the effect on 
              the flux parameters negligible.

      10.2.4  Additional Quality Assessment Applied.

              Not available at this revision.

                             11.  NOTES

11.1  Known Problems With The Data.

      o  A small fraction of the data was lost due to offset in recording
         position angles.

11.2  Usage Guidance.

      The variance due to instrumental error must be subtracted to determine
      wind vectors, so the LIDAR error must be determined accurately to avoid
      bias in the intensities. The main source of uncertainty in all turbulence
      parameters was the limited number of samples of the large eddies. This 
      was the case in spite of averaging for 1 h, covering an area by scanning 
      in azimuth, and having rapid advection of eddies by 15 [m][s^-1] average 
      winds. Dopplar radars using this Velocity Azimuth Display technique can 
      also apply this method to estimate the uncertainty in their flux and 
      turbulence measurements.

11.3  Other Relevant Information.

     The winds were obtained with the VAD (Velocity Azimuth Display)
     technique, which is explained in most books treating Doppler radar,
     (Battan 19xx). The LIDAR directly measures the radial (along-beam
     component of the wind as a function of range. When scanning 360 
     degrees in azimuth at constant elevation angle in a horizontally 
     homogeneous wind field, the radial component at a single
     range varies sinusoidally with azimuth. The phase of the sinusoid
     gives the wind direction, and the amplitude reveals the speed
     (modified by the known elevation angle). We performed a least squares
     fit of a sinusoid to the data to average out the effects of turbulence
     and random instrument uncertainties over the VAD circle.

     The profiles were obtained at irregular intervals. The LIDAR site
     was at 39 degrees 4 minutes 5 seconds north latitude and 96 degrees 32
     minutes 21 seconds west longitude, which is near the intersection of
     highways I-70 and K-177; elevation was 446 m AGL. Winds are given in
     meteorological convention: 0 degrees from north  and 90 degrees from
     east. Heights are in meters MSL. The LIDAR cannot operate within a
     minimum range of 500 m, so the wind profile begins somewhat above the
     surface. The vertical spacing depends on range gate spacing and
     elevation angle, which the operators varied from one VAD to another.
     Maximum height was set by signal/noise limitations or blockage by
     clouds. Data were edited to remove spurious values. Data in the
     planetary boundary layer are usually continuous, but gaps appear
     occasionally in profiles extending to several km. Profiles are
     unsmoothed, and the LIDAR's short pulse made adjacent data points
     almost independent.

     Wind profiles can also be supplied on request for other times
     (between mid-morning and late afternoon) when the LIDAR engaged in
     intensive scanning for turbulence properties. These data sets are
     temporally intensive, typically with one wind profile per minute.

     Some of the lost data were recoverable, and were restored and
     processed.

                           12.  REFERENCES

12.1  Satellite/Instrument/Data Processing Documentation.

      Hall, F.F. Jr., R.E. Cupp, R.M. Hardesty, T.R. Lawrence, M.J. Post,
         R.A. Richter, and B.F. Weber. 1987. "Six Years of Pulsed-Doppler LIDAR
         Field Experiments at NOAA/WPL" in Preprint Vol. 6th Symp. on Meteor.
         Observations and Instrumentation. Amer. Meteor. Soc. Boston. 11-14.
      Post, M.J., R.A. Richter, R.M. Hardesty, T.R. Lawrence, and F.F. Hall,
         Jr. 1982. National Oceanic and Atmospheric Administration's (NOAA)
         pulsed, coherent, infrared Doppler LIDAR -- characteristics and data.
         SPIE Vol. 300 Physics and Technology of Coherent Infrared Radar. 
         (1981). Soc. Photo-Opt. Instrumentation Engr. Bellingham, Washington. 
         60-65.

12.2  Journal Articles and Study Reports.

      Battan, L.J. 19xx. Radar Observation of the Atmosphere. University
         of Chicago. Press. 324pp.
      Eberhard, W.L., R.E. Cupp, and K.R. Healy. 1989. Doppler LIDAR 
         measurement of profiles of turbulence and momentum flux. J. Atmos. 
         Oceanic Technol. 6:809-819.
      Hall, F.F. Jr., R.M. Huffaker, R.M. Hardesty, M.E. Jackson, T.R.
         Lawrence, M.J. Post, R.A. Richter, and B.F. Weber. "Wind Measurement
         Accuracy of the NOAA Pulsed Infrared Doppler LIDAR" Applied Optics.
         Vol. 23 (1984). 2503-2506.
      Gal-Chen, T., and R.A. Kropfli. 1984. Buoyancy and pressure perturbations
         derived from dual-Doppler radar observations of the planetary boundary
         layer: applications for matching models with observations. J. Atmos.
         Sci. 41:3007-3020.
      Kunkel, K.E., E.W. Eloranta, and J.A. Weinman. 1980. Remote determination
         of winds, turbulence spectra and energy dissipation rates in the
         boundary layer from LIDAR measurements. J. Atmos. Sci. 37:978-985.
      Sellers, P.J., F.G. Hall, G. Asrar, D.E. Strebel, and R.E. Murphy. 1988.
         The First ISLSCP Field Experiment (FIFE). Bull. Am. Meteor. Soc.
         69:22-27.
      Sugita, M., and W. Brutsaert. 1990. Wind velocity measurements in the
         neutral boundary layer above hilly prairie. J. Geophys. Res.
         95:7617-7624.

12.3  Archive/DBMS Usage Documentation. 

      The Collected Data of the First ISLSCP Field Experiment is archived at
      the EOS Distributed Active Archive Center (DAAC) at Oak Ridge National
      Laboratory (ORNL), Oak Ridge, Tennessee (Section 13 below).  
      Documentation about using the archive and/or online access to the data 
      at the ORNL DAAC is not available at this revision.

                             13.  DATA ACCESS

13.1  Contacts for Archive/Data Access Information. 

      ORNL DAAC User Services
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      (615) 241-3952

13.2  Archive Identification. 

      EOSDIS Distributed Active Archive Center
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      USA

      Telephone:       (615) 241-3952
      FAX:             (615) 574-4665
      Internet Email:   ornldaac@onrl.gov

13.3  Procedures for Obtaining Data.

      Users may place requests by letter, telephone, electronic mail, FAX, or 
      personal visit. 

13.4  ORNL DAAC Status/Plans. 

      FIFE data will be available from the ORNL DAAC. Please contact the 
      ORNL DAAC User Services Office for the most current information about 
      these data.


                 14.  OUTPUT PRODUCTS AND AVAILABILITY

14.1  Tape Products.

      None.

14.2  Film Products.

      None.

14.3  Other Products.

      The Quick Look Boundary Layer Height data are available on FIFE CD-ROM 
      Volume 1.

                        15.  GLOSSARY OF ACRONYMS

ABL               Atmospheric Boundary Layer
AGL               Above Ground Level
CAPPI             Constant Altitude Plan Position Indicator
CD-ROM            Compact Disk (optical), Read-Only Memory
DAAC              Distributed Active Archive Center
DEC               Digital Equipment Corporation
EOSDIS            Earth Observing System Data and Information System
FIFE              First ISLSCP Field Experiment
FIS               FIFE Information System
ISLSCP            International Satellite Land Surface Climatology Project
LIDAR             Light Detection and Range
ORNL              Oak Ridge National Laboratory
T/R               Transmit/Receive
UTM               Universal Transverse Mercator
VAD               Velocity Azimuth Display
VIL               Volume Image LIDAR