1.  TITLE

1.1  Data Set Identification. 

     NOAA Radiosonde Observations.

1.2  FIS Data Base Table Name. 

     NOAA_RADIOSONDE_DATA.

1.3  CD-ROM File Name. 

     \DATA\ATMOS\NOAA_SON\GRIDxxx\YyyMmm\ydddgrid.NOR

     Where xxxx is the four digit code for the location within the FIFE site 
     grid, yy is the last two digits of the year (e.g. Y87=1987), mm is the
     month of the year (e.g. M12=December), and ddd is the day of the year,
     (e.g. 061=sixty-first day in the year). Note: capital letters 
     indicate fixed values that appear on the CD-ROM exactly as shown here, 
     lower case indicates characters (values) that change for each path
     and file.

     The format used for the filenames is: ydddgrid.sfx, where grid is the 
     four-number code for the location within the FIFE site grid, y is the 
     last digit of the year (e.g. 7=1987, and 9=1989), and ddd is the day of 
     the year.  The filename extension (.sfx), identifies the data set content
     for the file (see Section 8.2) and is equal to .NOR for this data set. 

1.4  Revision Date Of This Document. 

     April 28, 1994. 

     This document has been reviewed to eliminate technical and editorial
     inaccuracies by the FIFE Information Scientist. Previous versions of this
     document have been reviewed by the Principal Investigator, the person who
     transmitted the data to FIS, a FIS staff member, or a FIFE scientist 
     generally familiar with the data. It is believed that the document 
     accurately describes the data as collected and as archived on the FIFE
     CD-ROM series.

                         2.  INVESTIGATOR(S)

2.1  Investigator(s) Name And Title. 

     Staff Science.

2.2  Title Of Investigation. 

     Staff Science Meteorological Data Acquisition Program.

2.3  Contacts (For Data Production Information). 

      ___________________________________
     |              |   Contact 1        |
     |______________|____________________|
     |2.3.1 Name    |Dan Tarpley         |
     |2.3.2 Address |NOAA/NESDIS, Rm 712 |
     |              |World Weather Bldg. |
     |      City/St.|Washington, DC      |
     |      Zip Code|20233               |
     |2.3.3 Tel.    |(301) 763-8042      |
     |2.3.4 Email   |dtarpley@omnet      |
     |______________|____________________|

2.4  Requested Form of Acknowledgement.

     The NOAA radiosonde observation were obtained from Dr. Dan Tarpley of the
     National Oceanic and Atmospheric Administration (NOAA)/National
     Environmental Satellite Data and Information Service (NESDIS.) His
     assistance is greatly appreciated.

                            3.  INTRODUCTION

3.1  Objective/Purpose. 

     The FIFE Staff Science effort covered those activities which were FIFE
     community level activities, or required uniform data collection 
     procedures across sites and time. These activities included the 
     acquisition, processing and archiving of meteorological parameters of the 
     atmosphere above the FIFE site. These data can be used as input to
     numerical models, as well as, verification data for simulation studies.

3.2  Summary of Parameters. 

     Atmospheric pressure, geopotential height, and temperature.

3.3  Discussion. 

     The radiosonde data were extracted from the NOAA operational analysis 
     system and transmitted to the FIS. Data are available from July 1985 to 
     October 1988, there are 1123 days of data during this period with data at 
     twelve hour intervals. Unlike the radiosonde data collected at the FIFE
     study area (see FIFE Radiosonde Data (Brutsaert)), these data were 
     collected using sondes released in Dodge City and Topeka, Kansas, 
     337 km and 68 km, respectively, from the FIFE site.

                        4.  THEORY OF MEASUREMENTS

Radiosonde observations are made to determine the pressure, temperature, and 
humidity from the surface to the point where the sounding is terminated. 

                            5.  EQUIPMENT

5.1  Instrument Description. 

     The radiosonde is a balloon-borne, battery-powered instrument used 
     together with the ground-receiving equipment to delineate the vertical 
     profile of the atmosphere. The radiosonde consists of meteorological 
     measuring elements coupled to a radio transmitter and assembled into a 
     small lightweight box. The device is carried aloft by a balloon filled 
     with hydrogen, natural gas, or helium gas. Included in the train is a 
     small parachute to slow the descent of the instrument after the balloon 
     bursts, thereby minimizing the danger of injury to life and property.

     5.1.1  Platform.

            Balloon filled with hydrogen.

     5.1.2  Mission Objectives. 

            To measure pressure, and temperature profiles in the 
            atmosphere.

     5.1.3  Key Variables. 

            Pressure level, height, and temperature.

     5.1.4  Principles of Operation. 

            Pressure is measured by means of a baroswitch which employs an 
            expanding aneroid pressure cell to move a contact arm across a 
            commutator bar as the pressure decreases. Temperature is measured 
            by a thermistor. The electrical resistance of the thermistor is a 
            function of temperature. 

            As the radiosonde ascends, the thermistor and hygristor are 
            switched sequentially into the modulator circuit by the 
            baroswitch. The amplitude of the received signal, therefore, is 
            alternately a function of temperature or humidity. Because of the
            translation done by the modulator circuit the signal may be any 
            value from 0 to 200 Hz. Periodically, the thermistor and hygristor
            are bypassed in the modulator circuit. Reference circuits using 
            fixed resistors are then used to modulate the carrier frequency 
            to known values, 95, 190, or 195 Hz (47.5, 95, or 97.5 
            recorder divisions). Any changes that may be occurring in 
            the modulator circuit can then be evaluated.

     5.1.5  Instrument Measurement Geometry. 

            The radiosonde consists of meteorological measuring elements 
            coupled to a radio transmitter and assembled into a small 
            lightweight box.

     5.1.6  Manufacturer of Instrument. 

            Not available at this revision.

5.2  Calibration. 

     5.2.1  Specifications. 

            Not available at this revision.

            5.2.1.1  Tolerance. 

                     Not available at this revision.

     5.2.2  Frequency of Calibration. 

            Calibration is performed at the beginning of each sounding.

     5.2.3  Other Calibration Information.

            Calibration charts are provided by the manufacturer of the 
            radiosonde. The serial numbers affixed to the baroswitch assembly 
            are checked to make sure that they agree with those printed on the 
            calibration chart and on the instrument. If the baroswitch numbers
            disagree, the radiosonde is rejected. 

                          6.  PROCEDURE

6.1  Data Acquisition Methods. 

     The radiosonde transmits meteorological information consisting of 
     pressure obtained from an aneroid cell, temperature, and relative 
     humidity. The telemetered meteorological information from the radiosonde 
     is detected, amplified, and shaped by a receiver, and the processed 
     information is printed in graphic form on a strip chart recorder or 
     stored on computer disc. 

     Dan Tarpley, of NOAA's National Environmental Satellite Data and 
     Information Service, acquired the NOAA radiosonde data from the reporting 
     NOAA stations. These data were then sent to the FIFE Information System.

6.2  Spatial Characteristics. 

     6.2.1  Spatial Coverage. 

            NOAA radiosonde data for FIFE were obtained from two stations  
            in Kansas. The names, locations, and approximate distance from the 
            FIFE site of these stations are listed below:

                               UTM        UTM    
            LOCATION         NORTHING   EASTING  LATITUDE  LONGITUDE  DISTANCE
            ------------------------------------------------------------------
            Dodge City, KS   4180534    414568   37 46 12  99 58 12   337 km
            Topeka, KS       4327629    272466   39 04 12  95 37 48   68  km

            The FIFE STATION_ID and SITEGRID_ID for these locations are:

            STATION_ID SITEGRID_ID
            ---------- -----------
            451        XRSD-RDN
            456        XRST-RDN

            The horizontal coverage of an individual sonde varies depending 
            upon the track the sonde takes as it ascends. The data were 
            collected 400 km apart.

     6.2.2  Spatial Resolution. 
            
            The horizontal resolution varies with the rate and angle of the 
            ascent. The specific values are not available at this revision.

            The vertical resolution will vary as the sonde ascends.

6.3  Temporal Characteristics. 

     6.3.1  Temporal Coverage. 

            The overall time period of data acquisition was from July 2, 1985 
            through October 23, 1988. There are 1123 days of data, distributed 
            as follows over this period:

            YEAR         DAYS
            -----------------
            1985         160
            1986         321
            1987         350
            1988         292

     6.3.2  Temporal Resolution. 

            Observations are made at 12 hour intervals.

                           7.  OBSERVATIONS

7.1  Field Notes.

     None.

                         8.  DATA DESCRIPTION

8.1  Table Definition With Comments. 

     The SQL definition for this table is found in the NOAA_SON.TDF File
     found on CD_ROM Volume 1.

8.2  Type of Data. 

--------------------------------------------------------------------------------
|                 8.2.1                  |               |          |          |
|Parameter/Variable Name                 |               |          |          |
--------------------------------------------------------------------------------
|    |               8.2.2               |     8.2.3     |  8.2.4   |  8.2.5   |
|    |Parameter/Variable Description     |Range          |Units     |Source    |
--------------------------------------------------------------------------------
|SITEGRID_ID                             |               |          |          |
|    |This is a FIS grid location code.  |               |          |FIS       |
|    |Site grid codes (SSEE-III) give    |               |          |          |
|    |the south (SS) and east (EE) cell  |               |          |          |
|    |number in a 100x100 array of 200m  |               |          |          |
|    |square cells.  The last 3          |               |          |          |
|    |characters (III) are an instrument |               |          |          |
|    |identifier.                        |               |          |          |
--------------------------------------------------------------------------------
|STATION_ID                              |               |          |          |
|    |The FIS site identifier used to    |min = 451,     |          |FIS       |
|    |designate this site.               |max = 456      |          |          |
--------------------------------------------------------------------------------
|OBS_DATE                                |               |          |          |
|    |The date of the observations.      |min = 02-JUL-85|          |NOAA      |
|    |                                   |,              |          |          |
|    |                                   |max = 23-OCT-88|          |          |
--------------------------------------------------------------------------------
|OBS_TIME                                |               |          |          |
|    |The time that the observation was  |min = 0,       |[GMT]     |NOAA      |
|    |taken.                             |max = 1200     |          |          |
--------------------------------------------------------------------------------
|ATMOSPHERIC_PRESS                       |               |          |          |
|    |The atmospheric pressure, one of   |min = 10,      |[millibars|ANEROID SE|
|    |the 15 manditory pressure levels   |max = 1000     |]         |NSOR      |
|    |used by NOAA.                      |               |          |          |
--------------------------------------------------------------------------------
|GEOPTNTL_HEIGHT                         |               |          |          |
|    |The measured geopotential height.  |min = 264,     |[meters]  |NOAA      |
|    |                                   |max = 32000,   |          |          |
|    |                                   |missing = 99999|          |          |
--------------------------------------------------------------------------------
|ATMOSPHERIC_TEMP                        |               |          |          |
|    |The measured atmospheric           |min = -88.9,   |[degrees C|THERMISTOR|
|    |temperature, at a given pressure.  |max = 34.2,    |elsius]   |          |
|    |                                   |missing = 99999|          |          |
--------------------------------------------------------------------------------
|DEWPNT_DEPRSSN                          |               |          |          |
|    |The measured Dewpoint Depression.  |               |          |          |
--------------------------------------------------------------------------------
|FIFE_DATA_CRTFCN_CODE                   |       *       |          |          |
|    |The FIFE Certification Code for    |CPI=checked by |          |FIS       |
|    |the data, in the following format: |principal inves|          |          |
|    |CPI (Certified by PI), CPI-???     |tigator,       |          |          |
|    |(CPI - questionable data).         |CPI-MRG=merged |          |          |
|    |                                   |data           |          |          |
--------------------------------------------------------------------------------
|LAST_REVISION_DATE                      |               |          |          |
|    |The last revision date for the     |min = 20-JUN-87|          |FIS       |
|    |data, in the format (DD-MMM-YY).   |,              |          |          |
|    |                                   |max = 11-FEB-91|          |          |
--------------------------------------------------------------------------------

Footnote:

    * Valid levels 

      The primary certification codes are:

      EXM - Example or Test data (not for release)
      PRE - Preliminary (unchecked, use at your own risk)
      CPI - Checked by Principal Investigator (reviewed for quality)
      CGR - Checked by a group and reconciled (data comparisons and 
            cross checks)

      The certification code modifiers are:

      PRE-NFP  - Preliminary - Not for publication, at the request of 
                 investigator.
      CPI-MRG  - PAMS data that is "merged" from two separate receiving 
                 stations to eliminate transmission errors.
      CPI-???  - Investigator thinks data item may be questionable.

8.3  Sample Data Base Data Record. 

      SITEGRID STATION_ID OBS_DATE    OBS_TIME ATMOSPHERIC_PRESS
      -------- ---------- --------- ---------- -----------------
      XRSD-RSN        451 15-AUG-87          0              1000
      XRSD-RSN        451 15-AUG-87          0               850
      XRSD-RSN        451 15-AUG-87          0               700
      XRSD-RSN        451 15-AUG-87          0               500
      XRSD-RSN        451 15-AUG-87          0               400
      XRSD-RSN        451 15-AUG-87          0               300
      XRSD-RSN        451 15-AUG-87          0               250
      XRSD-RSN        451 15-AUG-87          0               200
      XRSD-RSN        451 15-AUG-87       1200              1000
      XRSD-RSN        451 15-AUG-87          0               150
      XRSD-RSN        451 15-AUG-87       1200               100   
      
      
      GEOPTNTL_HEIGHT ATMOSPHERIC_TEMP DEWPNT_DEPRSSN FIFE_DATA_CRTFCN_CODE
      --------------- ---------------- -------------- ---------------------
                99999            99999          -9999 CPI    
                 1456             25.6              8 CPI    
                 3131               13             10 CPI    
                 5860             -7.1             30 CPI    
                 7570            -15.7             30 CPI    
                 9690            -28.5             30 CPI    
                10970            -38.3             30 CPI    
                12470            -49.1          -9999 CPI    
                99999            99999          -9999 CPI    
                14300            -62.5          -9999 CPI    
                16670            -68.9          -9999 CPI    
      
      
      LAST_REVISION_DATE
      ------------------
      10-NOV-93
      10-NOV-93
      10-NOV-93
      10-NOV-93
      10-NOV-93
      10-NOV-93
      10-NOV-93
      10-NOV-93
      10-NOV-93
      10-NOV-93
      10-NOV-93

8.4  Data Format.

     The CD-ROM file format consists of numerical and character fields of 
     varying length separated by commas. The character fields are enclosed 
     with a single apostrophe. There are no spaces between the fields.  Each 
     file begin with five header records.  Header records contain the 
     following information:

     Record 1    Name of this file, its table name, number of records in
                 this file, and principal investigator name.
     Record 2    Path and filename of the previous data set, and path and 
                 filename of the next data set. (Path and filenames for files 
                 that contain another set of data taken at the same site on 
                 the same day.)
     Record 3    Path and filename of the previous site, and path and filename 
                 of the next site. (Path and filenames for files of the same 
                 data set taken on the same day for the previous and next 
                 sites, sequentially numbered by SITEGRID.)
     Record 4    Path and filename of the previous date, and path and filename 
                 of the next date. (Path and filenames for files of the same 
                 data set taken at the same site for the previous and next 
                 date.)
     Record 5    Column names for the data within the file, delimited by 
                 commas.
     Record 6    Data records begin.

     Each field represents one of the attributes listed in the chart in 
     Section 8.2 and described in detail in the TDF file (see Section 8.1). 
     These fields are in the same order as in the chart.

8.5  Related Data Sets. 

     NOAA Radiosonde Observations-1989 (NCDC).
     Upper Air Derivative Data from NMC.
     NOAA Regional Surface Data - 1989 (NCDC).
     NOAA Regional Surface Data.
     FIFE Radiosonde Data.
     Automated Meteorological Stations (AMS).

                         9.  DATA MANIPULATIONS

9.1  Formulas.

     Not available at this revision.

     9.1.1  Derivation Techniques/Algorithms.

            Not available at this revision.

9.2  Data Processing Sequence. 

     9.2.1  Processing Steps and Data Sets.

               1. Unpack 9-track tape data sent to FIFE by D. Tarpley.
                  A progam was run that unpacked each file and created three 
                  files (e.g., FILES1_RADIO, FILE1_UPPERAIR, and 
                  FILE1_SURFACE). The 9-track tape contained the 
                  NOAA Radiosonde Observation described here, the Upper Air 
                  Derivation Data from NMC and the NOAA Regional Surface
                  Data. All files were ASCII text files. In addition to the 
                  above files the program created a log file to flag problems
                  (e.g., missing data or year). A message indicates any 
                  problems, which should be corrected before continuing.

               2. Load data into FIS data base.
                  A program was run, which uses ORACLE, that adds data to the 
                  data base in tables for each of these data sets (i.e., NOAA
                  Radiosonde Observations described here, the Upper Air 
                  Derivation Data from NMC and the NOAA Regional Surface Data).
                  ORACLE was then used to systematically check these data 
                  tables for data inconsistencies.

     9.2.2  Processing Changes.

            Not available at this revision.

9.3  Calculations.

     9.3.1  Special Corrections/Adjustments.

            The original NOAA radiosonde data contained pressure levels, not 
            atmospheric pressure. The FIFE Information System staff, converted 
            pressure levels to atmospheric pressure. The relationship between 
            the original pressure levels and the current atmospheric pressures 
            are listed below.

            Pressure Level        Atmospheric Pressure
            --------------        --------------------
             1                                 1000 mb
             2                                  850 mb
             3                                  700 mb
             4                                  500 mb
             5                                  400 mb
             6                                  300 mb
             7                                  250 mb
             8                                  200 mb
             9                                  150 mb
            10                                  100 mb
            11                                   70 mb
            12                                   50 mb
            13                                   30 mb
            14                                   20 mb
            15                                   10 mb

9.4  Graphs and Plots. 

     None.

                          10.  ERRORS

10.1  Sources of Error. 

      The sources of error are as follows:  1) insufficient recorder
      sensitivity, 2) fading or weak signals, 3) unstable temperature 
      traces, 4) leaking pressure cell, 5) sticking contact arm, 
      6) electrical leakage in the baseline check box, or 7) repeated 
      contacts caused by faulty baroswitch assembly.
      
10.2  Quality Assessment. 

      10.2.1  Data Validation by Source. 

              Not available at this revision. 
        
      10.2.2  Confidence Level/Accuracy Judgement. 

              Not available at this revision.

      10.2.3  Measurement Error for Parameters and Variables. 

              Not available at this revision.

      10.2.4  Additional Quality Assessment Applied. 

              Occasionally soundings terminate abnormally, (e.g., balloon 
              burst, leaking or floating balloon, weak or fading signal, 
              radiosonde failure, etc.) When possible, another release 
              is made close to the allotted time, and a complete explanation 
              of the problems that caused the unsuccessful flight are 
              documented.

                             11.  NOTES

11.1  Known Problems With The Data.

      Not available at this revision.

11.2  Usage Guidance. 

      When the types of ground and flight equipment used to collect these data
      malfunction they exhibit little or no obvious abnormalities in the 
      record. These cases, however, do show certain patterns in the record, 
      a knowledge of these is very helpful in the classification of the data.

11.3  Other Relevant Information.

      Not available at this revision.

                           12.  REFERENCES

12.1  Satellite/Instrument/Data Processing Documentation. 

      Federal Meteorological Handbook No. 3
      Radiosonde Observations
      U.S. Department of Commerce, National Oceanic and Atmospheric 
      Administration
      Washington, D. C.

      Federal Meteorological Handbook No. 4
      Radiosonde Code
      Second Edition-1976
      U.S. Department of Commerce, National Oceanic and Atmospheric 
      Administration
      Washington, D. C.

12.2  Journal Articles and Study Reports. 

      Brutsaert, W., M. Sugita, and L.J. Fritschen. 1990. Inner region 
         humidity characteristics of the neutral boundary layer over prairie 
         terrain. Water Resour. Res. 26:2931-2936.
      Sugita, M., and W. Brutsaert. 1990. Wind velocity measurements in the 
         neutral boundary layer above hilly prairie. J. Geophys. Res. 
         95:7617-7624.
      Sugita, M. and W. Brutsaert. 1991. Daily evaporation over a region from
         lower boundary layer profiles measured with radiosondes. Water Resour.
         Res. 27:747-752.
      Sellers, P.J., F.G. Hall, G. Asrar, D.E. Strebel, and R.E. Murphy. 1988. 
         The first ISLSCP field experiment (FIFE). Bull. Am. Meteorol. Soc. 
         69:22-27.

12.3  Archive/DBMS Usage Documentation. 

      Contact the EOS Distributed Active Archive Center (DAAC) at Oak Ridge 
      National Laboratory (ORNL), Oak Ridge, Tennessee (Section 13 below).  
      Documentation about using the archive and/or online access to the data 
      at the ORNL DAAC is not available at this revision.

                             13.  DATA ACCESS

13.1  Contacts for Archive/Data Access Information. 

      ORNL DAAC User Services
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      (615) 574-7817

13.2  Archive Identification. 

      EOSDIS Distributed Active Archive Center
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      USA

      Telephone:       (615) 574-7817
      FAX:             (615) 574-4665
      Internet Email:   ornldaac@onrl.gov

13.3  Procedures for Obtaining Data

      Users may place requests by letter, telephone, electronic mail, FAX, or 
      personal visit. 

13.4  ORNL DAAC Status/Plans. 

      FIFE data will be available from the ORNL DAAC. Please contact the 
      ORNL DAAC User Services Office for the most current information about 
      these data.

                 14.  OUTPUT PRODUCTS AND AVAILABILITY 

14.1  Tape Products. 

      None. 

14.2  Film Products. 

      None.

14.3  Other Products.

      NOAA Radiosonde Observation data is available on FIFE CD-ROM Volume 1.

                        15.  GLOSSARY OF ACRONYMS

BPI            Byte per inch
CD-ROM         Compact Disk (optical), Read-Only Memory
CCT            Computer Compatible Tape
DAAC           Distributed Active Archive Center
EOSDIS         Earth Observing System Data and Information System
FIS            FIFE Information System
IFOV           Instantaneous Field of View
ISLSCP         International Satellite Cloud Climatology Project
Mbps           Megabyte per second
NESDIS         National Environmental Satellite Data and Information Service
NOAA           National Oceanic and Atmospheric Administration
ORNL           Oak Ridge National Laboratory
UTM            Universal Transverse Mercator