1.  TITLE

1.1  Data Set Identification. 

     TIROS Operational Vertical Sounder (TOVS).

1.2  FIS Data Base Table Name. 

     NOAA_TOVS_DATA.

1.3  CD-ROM File Name. 

     \DATA\SAT_OBS\NOAA_TOV\YyyMmm\yyddd\ydddhhmm.NTV

     Where yy is the last two digits of the year (e.g., Y87=1987, or 87=1987),
     and mm is the month of the year (e.g., M12=December). Note: capital 
     letters indicate fixed values that appear on the CD-ROM exactly as shown 
     here, lower case indicates characters (values) that change for each path
     and file.

     The format used for the filenames is: ydddhhmm.sfx, y is the 
     last digit of the year (e.g., 7=1987, and 9=1989), ddd is the day of 
     the year (e.g., 061=sixty-first day in the year), hh is the GMT hour 
     (e.g., 13=1300), and mm is the minutes. The filename extension (.sfx), 
     identifies the data set content for the file (see Section 8.2) and is 
     equal to .NTV for this data set. 

1.4  Revision Date Of This Document. 

     May 11, 1994.

     Warning:  This document has not been checked for technical or editorial
               accuracy by the FIFE Information Scientist. There may be 
               inconsistencies with other documents, technical or editorial 
               errors that were inadvertently introduced when the document was 
               compiled or references to preliminary data that were not included 
               on the final CD-ROM.

               Previous versions of this document have been reviewed by the 
               Principal Investigator, the person who transmitted the data to 
               FIS, a FIS staff member, or a FIFE scientist generally familiar 
               with the data.

                         2.  INVESTIGATOR(S)

2.1  Investigator(s) Name And Title. 

     Staff Science.

2.2  Title Of Investigation. 

     Staff Science Satellite Data Acquisition Program.

2.3  Contacts (For Data Production Information). 

      __________________________________________________________________
     |              |      Contact 1     |          Contact 2           |
     |______________|____________________|______________________________|
     |2.3.1 Name    |Michael P. Chalfant |Dr. Robert Frouin             |
     |2.3.2 Address |NOAA/NESDIS         |California Space Inst.        |
     |              |World Weather Bldg. |Scripps Inst. of Oceanography |
     |              |                    |Univ. of California, San Diego|
     |      City/St.|Washington, DC      |La Jolla, CA                  |
     |      Zip Code|20233               |92093                         |
     |2.3.3 Tel.    |(301) 763-4380      |(619) 534-6243                |
     |2.3.4 Email   |                    |rfrouin@ucsd.edu              |
     |______________|____________________|______________________________|

2.4  Requested Form of Acknowledgment.

     The TIROS Operational Vertical Sounder (TOVS) data were obtained by the 
     FIFE Information System (FIS) from the National Oceanic and Atmospheric 
     Administration (NOAA)/National Environmental Satellite Data and 
     Information Service (NESDIS).

                            3.  INTRODUCTION

3.1  Objective/Purpose.

     The TOVS data were acquired from NOAA/NESDIS to monitor atmospheric 
     conditions that occurred over the FIFE study area during 1987. 

3.2  Summary of Parameters.

     Layer mean temperature, pressure at lower and upper boundary, layer 
     precipitable water, tropopause parameters, ozone, cloud cover, brightness 
     temperatures and radiances, sounding quality, and methods used to derive 
     some of the quantities.

3.3  Discussion.

     The TOVS data were obtained from NESDIS in the standard TOVS 
     sounding product format on magnetic tapes that contained atmospheric
     sounding data for NOAA-9 and -10 satellites over the FIFE study area.
     This data set contains the temperature, water, and brightness temperatures 
     collected over the given latitude and longitude location.

                        4.  THEORY OF MEASUREMENTS

The TOVS sounding products information is derived from the three instruments, 
namely HIRS/2, MSU, and SSU sensors, which measure the intensity of upwelling 
radiation in the various spectral intervals that occur at maxima over broad 
layers and depths of the atmosphere. These radiances measurements are processed 
into Earth-located, calibrated radiances values, "clear" radiances (radiances 
corrected for cloud effects and angle-of-view), estimates of water vapor in 
three atmospheric layers (converted to precipitable water in these layers), 
mean temperatures for selected atmospheric layers, tropopause height and 
temperature estimates, and geopotential thickness of selected atmospheric 
layers. The basic retrieval technique is statistical: eigenvector regression 
(Smith and Woolf 1976) is employed for water vapor and temperature below 
100 mb, while multiple linear regression is used for temperature above 100 mb
and total ozone. A combination of eigenvector and linear regression is utilized 
in the retrieval of cloud altitude and amount. The regression coefficients are 
derived from a dependent sample of measured radiances and quasi-coincident 
radiosonde observations.

The HIRS/2, using 19 infrared and 1 visible channel, provides temperature and 
water vapor soundings, surface temperature, and cloud detection. The MSU, with 
four microwave channels, provides temperature soundings under all sky 
conditions except rain, and also determines surface emissivity and cloud 
attenuation. The SSU provides temperature soundings using carbon dioxide gas 
cells and pressure modulation to observe thermal emissions for the 
stratosphere.

                            5.  EQUIPMENT

5.1  Instrument Description.

     The TOVS system consists of three separate sensors: High Resolution 
     Infrared Radiometer Sounder/2 (HIRS/2), Stratospheric Sounding Unit (SSU), 
     and Microwave Sounding Unit (MSU). Each of these sensors is a multi-
     channel radiometer. The HIRS/2 measures incident radiation, primarily in 
     the infrared region of the spectrum (19 channels) including both longwave 
     (15 micrometers) and shortwave (4.3 micrometers) regions, as well as one 
     channel in the visible spectrum. The SSU, a pressure-modulated radiometer 
     provided by the British Meteorological Office, observes thermal emissions 
     from the stratosphere. This instrument measures the radiation with 3 
     channels in the 15-micrometer carbon dioxide absorption band. The MSU is a 
     passive scanning microwave spectrometer with 4 channels in the 5.5-
     micrometer oxygen region.

     5.1.1  Platform.

            NOAA-9 and NOAA-10 polar orbiting satellites.

     5.1.2  Mission Objectives. 

            The TOVS instruments were designed to provide combined atmospheric 
            soundings from the Earth's surface to the stratosphere, with a 
            nominal ground resolution of about 250 by 250 km.

     5.1.3  Key Variables.

            Layered temperature, layered water vapor, cloud cover, tropopause 
            pressure and temperature, total ozone, and equivalent blackbody 
            temperatures for 20 HIRS/2, 4 MSU, and 3 SSU channels. 

     5.1.4  Principle of Operation.

            The HIRS/2 measuring scheme is based on the rotating mirror 
            providing 56 measurements per scan in 6.4 seconds. This cross-track 
            scan, combined with the satellite motion in orbit, provides 
            coverage of a major portion of the Earth's surface. There are two 
            modes of operation known as normal earth scan and calibration mode. 
            The instrument automatically operates in the calibration mode every 
            256 seconds and measures the calibration parameters. The total 
            calibration sequence is equivalent to three scan lines during which 
            no Earth data are obtained. The analog data is digitized onboard 
            spacecraft at a rate of 2880 bits per second. At this rate, there 
            are 288 bits per step (step time = 100 milliseconds) for all  
            20 channels. This data is digitized to 13 bits precision.

            SSU principle of operation is based on the selective chopper 
            radiometers flown on Nimbus 4 & 5, and the pressure modulator 
            radiometer flown on Nimbus 6. The three SSU channels have the same 
            frequency, but different cell pressures. This instrument consists 
            of a single telescope with a 10 degree IFOV which is step-scanned 
            perpendicular to the satellite subpoint track. Data is sampled at 
            the rate of 40 samples per second, and is digitized to 12-bit 
            precision. Therefore, the SSU data rate is 480 bits per second.

            MSU is a passive scanning microwave spectrometer with four channels 
            in the 5.5 micrometer oxygen region. This instrument measures an 
            apparent brightness temperature after a 1.84 second integration 
            period per step. The data is quantized to 12-bit precision and 
            combined with telemetry and step position information to produce an 
            effective output data rate of 320 bits per second.

     5.1.5  Instrument Measurement Geometry. 

            The HIRS/2 cross-track scan, combined with the satellite's motion 
            in orbit, provides coverage of a major portion of the Earth's 
            surface. The width of cross-track scan is 90 degrees or 2240 km 
            and consists of 56 steps. The mirror is stepped from home position 
            in 55 steps of 1.8 degrees. At the end of the scan (at position 
            56) the mirror rapidly returns to the home position and repeats 
            the scanning pattern. Each scan takes 6.4 seconds to complete (100 
            milliseconds per step) and there are 42 km between IFOV'S along the 
            sub-orbital track. The optical FOV is 1.25 degrees which gives a 
            ground IFOV of 17.4 km diameter at the nadir. At the end of the 
            scan, the ground IFOV is 58.5 km cross-track by 29.9 along-track.

            The SSU consists of a single primary telescope with a 10 degree 
            IFOV which is step-scanned perpendicular to the satellite subpoint 
            track. Each scan line is composed of eight individual 4.0 second 
            steps, and requires a total of 32 seconds, including time for the 
            mirror retrace. The 10 degree IFOV gives a resolution of 147 km at 
            the satellite subpoint and the stepping produces a gap 
            between adjacent scan lines of approximately 62 km at nadir. 

            The MSU sensors consist of two four-inch diameter antennas, each 
            having an IFOV of 7.5 degrees. The antennas are step-scanned 
            through eleven individual 1.84-second Earth viewing steps,
            taking a total of 25.6 seconds to complete. The 109-km IFOV 
            resolution at the subpoint creates a gap of approximately 
            115 km between adjacent scan lines.

     5.1.6  Manufacturer of Instrument. 

            HIRS/2    Aerospace/Optical Division
                      International Telephone and Telegraph Corp.
                      Fort Wayne, Indiana.

            MSU       NASA Goddard Space Flight Center
                      Greenbelt, Maryland.

            SSU       British Meteorological Office
                      United Kingdom.

5.2  Calibration. 

     HIRS/2 can be commanded to automatically enter a calibration mode every 
     256 seconds. When the instrument is in the calibration mode, the mirror 
     (starting from the beginning of a scan line) rapidly slews to a space 
     view and samples all channels for the equivalent time of one complete 
     scan line of 56 scan steps. Next, the mirror is moved to a position where 
     it views a cold calibration target and data is taken for the equivalent 
     of 56 scan steps. The mirror is then stepped to view an internal warm 
     target for another 56 scan steps. Upon completion of the calibration
     mode, the mirror continues its motion to the home position where it
     begins normal Earth scan.

     For the SSU, a calibration sequence is initiated every 256 seconds (8 
     scans) during which the radiometer is, in turn, stepped to a position to 
     view unobstructed space and an internal blackbody at a known temperature. 
     This calibration mode is synchronized with the HIRS/2 instrument.

     Unlike the HIRS/2 and SSU instruments, the MSU has no special calibration 
     sequence that interrupts normal scanning. The calibration data is 
     included in a scan line of data. From the last Earth view position, the 
     reflector rapidly moves 4 steps to view space, 10 additional steps to 
     view the housing, and then returns to the home position to begin another 
     scan line. Since each scan line requires 25.6 seconds, synchronization of 
     MSU within the other two TOVS instruments occurs every 128 seconds (5    
     scan lines).

     5.2.1  Specifications. 
                               HIRS/2    SSU      MSU      Units
                               ______    _____    _____    __________
            IFOV (nadir)        17.4     147.3    109.3    km (diameter)
            ANGULAR FOV          1.25     10.0      7.5    deg.
            ALTITUDE           833       833      833      km
            SCAN RATE            9.4       1.9      2.3    scans/min.
            STEP ANGLE           1.8      10.0      9.47   deg.
            STEP TIME            0.1       4.0      1.84   sec.
            DATA RATE         2880       480      320      bits/sec.
            DATA PRECISION      13        12       12      bits

            5.2.1.1  Tolerance. 

                     Typical values of the noise equivalent differential 
                     radiance for the HIRS/2, SSU, and MSU range from 0.001 to 
                     3.00 [mW][m^-2][steradian^-1][cm^-1], 0.30 to 1.00 [mW] 
                     [m^-2][steradian^-1][cm^-1], and about 0.3 degrees K, 
                     respectively.

                     Expected tolerance for retrieved layered temperature is 
                     of the order of 3.0 degrees K. Tropopause pressure and 
                     temperature are defined within 50 mb and 2.5 degrees K. 
                     Total ozone can be determined within 15% in the tropics 
                     and within 50% in the polar region. Cloud cover is 
                     estimated within 20% mb and tropopause.

     5.2.2  Frequency of Calibration. 

            A special calibration sequence is initiated every 256 seconds in
            the HIRS/2 and SSU sensors, whereas, a calibration target is
            observed every 25.6 seconds in the MSU sensor (i.e., once per scan
            line).

     5.2.3  Other Calibration Information. 

            See NOAA Polar Orbiter Data Users Guide, revised December 1991, 
            pages 4-1 through 4-35.

                          6.  PROCEDURE

6.1  Data Acquisition Methods.

     As part of the FIFE staff science data collection effort, the FIFE
     Information System (FIS) received and archived Television and
     Infrared Observational Satellite (TIROS) Operational Vertical Sounder
     (TOVS) data. The data were acquired by the NOAA-9 and NOAA-10 satellites
     during 1987. The data were obtained from NESDIS in the standard TOVS
     sounding product format on magnetic tape (see NOAA Polar Orbiter Data
     Users Guide, revised December 1991, pages 5-1 through 5-14).

6.2  Spatial Characteristics.

     The FIFE study area, with areal extent of 15 km by 15 km, is located south 
     of the Tuttle Reservoir and Kansas River, and near Manhattan, Kansas, USA. 
     The northwest corner of the area has UTM coordinates of 4,334,000 
     Northing and 705,000 Easting in UTM Zone 14.

     6.2.1  Spatial Coverage. 

            The NOAA TOVS sounding product acquired for FIFE centered on 39 
            deg. 03 min. N, 96 deg. 30 min. W, with a specified target area of 
            +/-250 km in all directions (approximately +/-2.5 deg. latitude,
            +/-4 deg. longitude).

     6.2.2  Spatial Resolution. 

            The three sensors, namely HIRS/2, SSU, and MSU have +/-49.5, 
            +/-40.0, and +/-47.35 degrees cross-track scan angle (degrees 
            from nadir). These scans equate to swaths +/-1120 , +/-737, and 
            +/-1174 km. This produces a ground IFOV at nadir (diameter) of 
            17.4, 147.3, and 109.3 km for the three sensors respectively. 
            Hence, the ground IFOV at the end of scan results in 58.5 km 
            cross-track by 29.9 km along-track for the HIRS/2, 244 km cross-
            track by 186.1 km along-track for the SSU, and 323.1 km cross-
            track by 178.8 km along-track for the MSU.

            The layered temperature are obtained for 15 layers: surface to
            850 mb, 850 to 700 mb, 700 to 500 mb, 500 to 400 mb, 400 to 300 
            mb, 300 to 200 mb, 200 to 100 mb, 100 to 70 mb, 70 to 50 mb, 50 
            to 30 mb, 30 to 10 mb, 10 to 5 mb, 5 to 2 mb, 2 to 1 mb, and 1 to 
            0.4 mb.

            The layered precipitable water are obtained for the layers:
            surface to 700 mb, 700 to 500 mb, and 500 to 100 mb.

6.3  Temporal Characteristics.

     6.3.1  Temporal Coverage.
 
            The overall time period of data acquisition was from January 1, 
            1987 through December 31, 1987 with some missing data due to
            processing problems. There was no NOAA-9 TOVS data available at 
            NESDIS for the period of March, 1987 to August, 1987.

     6.3.2  Temporal Resolution.  

            There are generally 2 overpasses per day per satellite at approx-
            imate times of 0130, 0820, 1330, and 2020 GMT at the equator. 
            However, not all of these data are processed and distributed due to 
            cloud cover and other data problems. North or south of the equator, 
            adjacent orbits can cause double coverage at an interval of 90 
            minutes increasing the number of scenes on some days.

                           7.  OBSERVATIONS

7.1  Field Notes. 

     Not Applicable.

                           8.  DATA DESCRIPTION

8.1  Table Definition With Comments.

     The SQL definition for this table is found in the NOAA_TOV.TDF file found
     on FIFE CD-ROM Volume 1.

8.2  Type of Data. 

--------------------------------------------------------------------------------
|                 8.2.1                  |               |          |          |
|Parameter/Variable Name                 |               |          |          |
--------------------------------------------------------------------------------
|    |               8.2.2               |     8.2.3     |  8.2.4   |  8.2.5   |
|    |Parameter/Variable Description     |Range          |Units     |Source    |
--------------------------------------------------------------------------------
|OBS_DATE                                |               |          |          |
|    |The date the data were collected,  |               |          |          |
|    |in the format (DD-mmm-YY).         |               |          |          |
--------------------------------------------------------------------------------
|OBS_TIME                                |               |          |          |
|    |The time of day that the data      |               |[GMT]     |          |
|    |were collected, in the format HHMM.|               |          |          |
--------------------------------------------------------------------------------
|PLATFORM                                |               |          |          |
|    |The NOAA platform that collected   |               |          |          |
|    |the data (NOAA-9 or NOAA-10).      |               |          |          |
--------------------------------------------------------------------------------
|LATITUDE                                |               |          |          |
|    |The latitude (DD MM SS.SS) of the  |               |          |          |
|    |data location.                     |               |          |          |
--------------------------------------------------------------------------------
|LONGITUDE                               |               |          |          |
|    |The longitude (DDD MM SS.SS) of    |               |          |          |
|    |the data location.                 |               |          |          |
--------------------------------------------------------------------------------
|OBS_TYPE                                |               |          |          |
|    |The type of observation recorded   |               |          |          |
|    |in this record.                    |               |          |          |
--------------------------------------------------------------------------------
|LOWER_PRESS                             |               |          |          |
|    |The lower pressure boundary for    |               |[millibars|          |
|    |the reading.                       |               |]         |          |
--------------------------------------------------------------------------------
|UPPER_PRESS                             |               |          |          |
|    |The upper pressure for the reading.|               |[millibars|          |
|    |                                   |               |]         |          |
--------------------------------------------------------------------------------
|OBS_VALUE                               |               |          |          |
|    |The observed parameter value.      |               |          |          |
--------------------------------------------------------------------------------
|OBS_UNITS                               |               |          |          |
|    |The units of the observed          |               |          |          |
|    |parameter.                         |               |          |          |
--------------------------------------------------------------------------------
|VALUE_QUALITY                           |               |          |          |
|    |The quality of the observed value. |               |          |          |
--------------------------------------------------------------------------------
|SOLAR_ZEN_ANG                           |               |          |          |
|    |The solar zenith angles at the     |               |[degrees] |          |
|    |time of data collection.           |               |          |          |
--------------------------------------------------------------------------------
|SURF_ELEV                               |               |          |          |
|    |The elevation of the surface       |               |[meters]  |          |
|    |location over which the data were  |               |          |          |
|    |collected.                         |               |          |          |
--------------------------------------------------------------------------------
|SURF_TEMP                               |               |          |          |
|    |The temperature of the surface     |               |[degrees K|          |
|    |over which the data were collected.|               |]         |          |
--------------------------------------------------------------------------------
|SURF_PRESS                              |               |          |          |
|    |The surface pressure over which    |               |[millibars|          |
|    |the data were collected.           |               |]         |          |
--------------------------------------------------------------------------------
|UPPER_TEMP_METHOD                       |               |          |          |
|    |The instrument and channel combin- |               |          |          |
|    |ations used to derive the          |               |          |          |
|    |temperatures of the atmospheric    |               |          |          |
|    |layers with pressures less than or |               |          |          |
|    |equal to 100 millibars.            |               |          |          |
--------------------------------------------------------------------------------
|LOWER_TEMP_METHOD                       |               |          |          |
|    |The instrument and channel combin- |               |          |          |
|    |ations used to derive the          |               |          |          |
|    |temperatures of the atmospheric    |               |          |          |
|    |layers with pressures from the     |               |          |          |
|    |surface to 100 millibars.          |               |          |          |
--------------------------------------------------------------------------------
|PRECIP_METHOD                           |               |          |          |
|    |The method used to derive the      |               |          |          |
|    |precipitable water estimates.      |               |          |          |
--------------------------------------------------------------------------------
|RETRIEVAL_METHOD                        |      $        |          |          |
|    |The method used in the retrieval.  |               |          |          |
--------------------------------------------------------------------------------
|SD_LOW                                  |               |          |          |
|    |The standard deviation of the      |               |          |          |
|    |low-level HIRS/2 channel (7)       |               |          |          |
|    |giving a measure of the            |               |          |          |
|    |atmospheric clarity for the        |               |          |          |
|    |sounding.                          |               |          |          |
--------------------------------------------------------------------------------
|SD_MID                                  |               |          |          |
|    |The standard deviation of the      |               |          |          |
|    |mid-level HIRS/2 channel (5)       |               |          |          |
|    |giving a measure of the            |               |          |          |
|    |atmospheric clarity for the        |               |          |          |
|    |sounding.                          |               |          |          |
--------------------------------------------------------------------------------
|N_STAR                                  |               |          |          |
|    |The average value of N*            |               |          |          |
|    |indicating clarity of the          |               |          |          |
|    |atmosphere in calculating the      |               |          |          |
|    |radiance values.                   |               |          |          |
--------------------------------------------------------------------------------
|SOUNDING_QUALITY                        |               |          |          |
|    |The quality of the sounding        |               |          |          |
|    |values (good, redundant,           |               |          |          |
|    |questionable, bad).                |               |          |          |
--------------------------------------------------------------------------------
|TROPO_PRESS                             |               |          |          |
|    |The pressure at the troposphere    |               |[millibars|          |
|    |level.                             |               |]         |          |
--------------------------------------------------------------------------------
|TROPO_TEMP                              |               |          |          |
|    |The temperature at the troposphere.|               |[degrees K|          |
|    |                                   |               |]         |          |
--------------------------------------------------------------------------------
|TROPO_QUALITY                           |               |          |          |
|    |The quality of the troposphere     |               |[millibars|          |
|    |values.                            |               |]         |          |
--------------------------------------------------------------------------------
|TROPO_PARM_METHOD                       |               |          |          |
|    |The method used to derive the      |               |          |          |
|    |troposphere temperature and        |               |          |          |
|    |pressure values.                   |               |          |          |
--------------------------------------------------------------------------------
|TOTAL_OZONE                             |               |          |          |
|    |The total ozone.                   |               |[Dobson un|          |
|    |                                   |               |its]      |          |
--------------------------------------------------------------------------------
|OZONE_QUALITY                           |               |          |          |
|    |The quality of the ozone amount.   |               |[percent] |          |
--------------------------------------------------------------------------------
|OZONE_METHOD                            |               |          |          |
|    |The method used to derive the      |               |          |          |
|    |total ozone amount.                |               |          |          |
--------------------------------------------------------------------------------
|CLOUD_LEVEL                             |               |          |          |
|    |The pressure level where any       |               |[millibars|          |
|    |cloud cover was located.           |               |]         |          |
--------------------------------------------------------------------------------
|CLOUD_PERCENT                           |               |          |          |
|    |The percent of the area covered    |               |[percent] |          |
|    |by clouds.                         |               |          |          |
--------------------------------------------------------------------------------

Footnotes:

          $ This is an encoded field. See Section 9.1.1 for a translation of 
            these codes.

          * Decode the FIFE_DATA_CRTFCN_CODE field as follows:

            The primary certification codes are:

            EXM - Example or Test data (not for release).
            PRE - Preliminary (unchecked, use at your own risk).
            CPI - Checked by Principal Investigator (reviewed for quality).
            CGR - Checked by a group and reconciled (data comparisons and 
                  cross-checks).

            The certification code modifiers are:

            PRE-NFP  - Preliminary - Not for publication, at the request of 
                       investigator.
            CPI-MRG  - PAMS data that are "merged" from two separate receiving 
                       stations to eliminate transmission errors.
            CPI-???  - Investigator thinks data item may be questionable.

8.3  Sample Data Base Data Record.
     
    OBS_DATE    OBS_TIME PLATFORM LATITUDE     LONGITUDE     OBS_TYPE
    --------- ---------- -------- ------------ ------------- ------------
    01-JAN-87        403 NOAA-9    38 01 12.00 -096 52 47.99 LAYER_TEMP
    01-JAN-87        403 NOAA-9    38 01 12.00 -096 52 47.99 LAYER_TEMP
    01-JAN-87        403 NOAA-9    38 01 12.00 -096 52 47.99 LAYER_TEMP
    01-JAN-87        403 NOAA-9    38 01 12.00 -096 52 47.99 LAYER_TEMP
    
    
    LOWER_PRESS UPPER_PRESS  OBS_VALUE OBS_UNITS VALUE_QUALITY SOLAR_ZEN_ANG
    ----------- ----------- ---------- --------- ------------- -------------
            950         850      276.4 DEG K              9999            90
            850         700      272.2 DEG K              9999            90
            500         400      247.1 DEG K              9999            90
            700         500      261.1 DEG K              9999            90
    
    
     SURF_ELEV  SURF_TEMP SURF_PRESS UPPER_TEMP_METHOD
    ---------- ---------- ---------- ------------------------
           401      263.9        950 HIRS + SSU + MSU (3,4)
           401      263.9        950 HIRS + SSU + MSU (3,4)
           401      263.9        950 HIRS + SSU + MSU (3,4)
           401      263.9        950 HIRS + SSU + MSU (3,4)
    
    
    LOWER_TEMP_METHOD    PRECIP_METHOD RETRIEVAL_METHOD     SD_LOW
    -------------------- ------------- ---------------- ----------
    HIRS + MSU           NO RETRIEVAL               544       9999
    HIRS + MSU           NO RETRIEVAL               544       9999
    HIRS + MSU           NO RETRIEVAL               544       9999
    HIRS + MSU           NO RETRIEVAL               544       9999
    
    
    
        SD_MID     N_STAR SOUNDING_QUALITY TROPO_PRESS TROPO_TEMP
    ---------- ---------- ---------------- ----------- ----------
          9999      9.999 GOOD                     224        218
          9999      9.999 GOOD                     224        218
          9999      9.999 GOOD                     224        218
          9999      9.999 GOOD                     224        218
    
    
    TROPO_QUALITY TROPO_PARM_METHO TOTAL_OZONE OZONE_QUALITY
    ------------- ---------------- ----------- -------------
             9999 HIRS + MSU        9999          9999
             9999 HIRS + MSU        9999          9999
             9999 HIRS + MSU        9999          9999
             9999 HIRS + MSU        9999          9999
                              
    OZONE_METHOD                             CLOUD_LEVEL CLOUD_PERCENT
    ---------------------------------------- ----------- -------------
    NO RETRIEVAL                                    9999          9999
    NO RETRIEVAL                                    9999          9999
    NO RETRIEVAL                                    9999          9999
    NO RETRIEVAL                                    9999          9999

8.4  Data Format.

     The CD-ROM file format consists of numerical and character fields of 
     varying length separated by commas. The character fields are enclosed with 
     a single apostrophe. There are no spaces between the fields.  Each file 
     begins with five header records.  Header records contain the following 
     information:

     Record 1    Name of this file, its table name, number of records in
                 this file, path and name of the document that describes 
                 the data in this file, and name of principal investigator 
                 for these data.
     Record 2    Path and filename of the previous data set, and path and 
                 filename of the next data set.  (Path and filenames for files 
                 that contain another set of data taken at the same site on 
                 the same day.)
     Record 3    Path and filename of the previous site, and path and filename 
                 of the next site.  (Path and filenames for files of the same 
                 data set taken on the same day for the previous and next 
                 sites (sequentially numbered by SITEGRID_ID)).
     Record 4    Path and filename of the previous date, and path and filename 
                 of the next date.  (Path and filenames for files of the same 
                 data set taken at the same site for the previous and next 
                 date.)
     Record 5    Column names for the data within the file, delimited by 
                 commas.
     Record 6    Data records begin.

     Each field represents one of the attributes listed in the chart in 
     Section 8.2 and described in detail in the TDF file (see Section 8.1). 
     These fields are in the same order as in the chart.

8.5  Related Data Sets. 

     NOAA Radiosonde Observations.
     NOAA Radiosonde Observations - 1989 (NCDC).
     Upper Air Derivative Data from NMC.
     NOAA Regional Surface Data.
     NOAA Regional Surface Data - 1989(NCDC).
     FIFE Radiosonde Data.
     Automatic Micrometeorological Observations.

                         9.  DATA MANIPULATIONS

9.1  Formulas. 

     9.1.1  Derivation Techniques/Algorithms. 

            Retrieval of the meteorological data from the multichannel 
            soundings of the instruments is accomplished by NOAA using 
            algorithms developed by Smith and Woolf (1976) and later modified 
            by McMillin and Dean (1982). The basic retrieval technique was
            statistical: eigenvector regression was employed for water vapor
            and temperature below 100 mb, while multiple linear regression was 
            used for temperature above 100 mb and total ozone. A combination 
            of eigenvector and linear regression was utilized in the retrieval 
            of cloud altitude and amount. The regression coefficients were 
            derived from a dependent sample of measured radiances and quasi-
            coincident radiosonde observations. These coefficients were 
            updated on a weekly basis. 

            The retrieval_method (Adolf Werbowetzki 1981) is encoded within a
            two byte field within the document portion of the NMC/NESDIS data 
            format for these data (Kidwell 1991, p 5-15). This code is also in
            the RETRIEVAL_METHOD field within this data set (see chart in 
            Section 8.2).

            This value is encoded as follows:

            RETRIEVAL_METHOD = 256 (A) + 16 (B) + C

                 where valid values for A are:

                        0 = no HIRS/2 data
                        1 = clear radiances are derived from completely clear 
                               spots
                        2 = Clear radiances derived from N* approach

                 where valid values for B are:
                        
                        0 = no HIRS/2 data
                        1 = all HIRS/2 channels are used in the retrieval
                        2 = the tropopause HIRS/2 channels were unusable due
                               to clouds and only stratospheric channels were 
                               used in the retrieval

                 where valid values for C are:

                       0 = a statistical retrieval method was used
                       1 = the minimum information retrieval was used
                       2 = the minimum information retrieval was attempted but
                              the statistical retrieval was used


9.2  Data Processing Sequence. 

     9.2.1  Processing Steps and Data Sets. 

            FIS processed the TOVS data as follows:

            1) The information about original tape and files were loaded into 
               the on-line inventory.

            2) The information contained in the Category 1 (Layer 
               temperatures), 2 (Layer Precipitable Water), 3 (Tropopause 
               Parameters), 4 (Ozone), 5 (Cloud Cover), and 6 (Sounding 
               Radiances) areas of the NMC/NESDIS Sounding 
               Products/Information portion of the TOVS tape entries were read   
               from the tape, unpacked and translated into an ASCII text file 
               using the information from the NOAA Polar Orbiter Data Users 
               Guide (Kidwell 1991).

             3) The data in these files were then loaded into the data base.

     9.2.2  Processing Changes.

            None.

9.3  Calculations. 

     9.3.1  Special Corrections/Adjustments.

            None.

9.4  Graphs and Plots.

     None.

                          10.  ERRORS

10.1  Sources of Error.

      Users of TOVS data should be aware that the satellite's onboard clock
      experiences a small drift in time over a period of several months.
      Specifically, that time drift may be defined by dt, where dt is the
      spacecraft clock time minus the actual GMT time. Satellite Operations
      Control Center (SOCC) monitors this time error and corrects dt to +0.5
      second when it reaches -0.5 second. The Earth data which is appended to
      the level-0 data is based on the spacecraft clock time. Therefore, an
      error in dt will be reflected as an error in Earth location. The error
      in Earth location due to this timing error could be as much as 4 kilo-
      meters at the satellite subpoint. SOCC applies the correction to dt just
      before an orbital recording begins, so, a user would never see a jump in
      the Earth location of a particular data set.

10.2  Quality Assessment. 

      10.2.1  Data Validation by Source. 

              The following tests are performed for quality assessment on the
              data by NESDIS (as given in NOAA Technical Report NESS 65):

              A superadiabatic temperature lapse rate test is performed on the
              tropospheric pressure layers bounded by the mandatory and 
              significant pressure levels to insure a stable profile;

              A gross error or "neighbor" check is performed on the difference 
              between the NMC forecast first guess heights and the retrieved 
              heights for all constant pressure levels. Values of this 
              difference are calculated for all points in the neighborhood 
              (within 500 Km). A sounding is required to have at least one 
              neighbor or it is automatically rejected. The value of the 
              height difference for the point is required to agree with the 
              average of the height differences for the other points in the 
              neighborhood to within: +/- 200 m with one neighbor, +/- 100 m 
              with two neighbors, or +/- 75 m with more than two neighbors.

              When retrievals are extended to land areas on an operational
              basis, further location tests are performed to insure that a 
              proper adjustment has been made for the terrain elevation in the
              field-of-view.

              Additional checks are generated over selected areas or at 
              selected times to monitor the performance of each channel, the 
              communication links from the data acquisition stations, and the 
              individual programs used to generate a sounding. Some 
              retrieved sounding are compared with standard radiosonde 
              reports, the NMC analyses, and the scanning radiometer data to
              test for meteorological reasonableness.
 
      10.2.2  Confidence Level/Accuracy Judgment.
 
              Not available at this revision.
             
      10.2.3  Measurement Error for Parameters and Variables. 

              The probable errors in TOVS-derived meteorological parameters 
              are estimated (Kidwell 1991) with layer mean temperatures from 
              the surface to 850 mb being +/-2.5 K, and 850 mb to tropopause 
              being +/-2.25 K. Those for layer precipitable water, cloud 
              cover, and cloud base pressure are +/-30%, +/-20%, and +/-100 mb 
              respectively. Total ozone concentrations could have an error of 
              about +/-15% for tropical regions, to +/-50% for polar regions.

      10.2.4  Additional Quality Assessment Applied. 

              Not available at this revision. 

                             11.  NOTES

11.1  Known Problems With The Data. 

      To date (July 13, 1992) the following discrepancies/problems have been
      noted in the data:

      For March 1987 through August 1987, only NOAA-10 TOVS data were 
      acquired. 

11.2  Usage Guidance. 

      A problem with operationally produced soundings occurs where retrievals 
      based on microwave and infrared radiances are mixed. In many instances, 
      pronounced differences between the two types persist over large 
      geographical areas. These large-scale, systematic differences must be 
      eliminated in order to achieve a proper representation of thermal 
      gradients from a mixture of the two types of soundings.

      One solution has been employed in the interactive processing. For every 
      spot where an infrared retrieval is made, a microwave retrieval is also 
      produced. Differences between the retrievals are calculated and mapped 
      across those areas where only microwave retrievals exist. The mapped 
      differences are then added to the microwave retrievals to make them 
      horizontally consistent with surrounding infrared soundings. 
      Unfortunately the current "operational" system is designed to process 
      soundings sequentially, so that major modifications are required to 
      implement such a retrieval-type normalization procedure. However, a 
      similar procedure could be implemented as part of a data analysis system 
      by any user of the TOVS data.

11.3  Other Relevant Information. 

      NESDIS keeps a detailed log of events associated with these data, a
      selection from that log follows. See the appendix-D of NOAA POLAR 
      ORBITER DATA USERS GUIDE for the complete list.

      1/8-12/87 Increase in number of cloudy retrievals believed due to noisy
                HIRS for NOAA-9. On 1/12 new HIRS calibration limits were
                applied. Percent cloudy retrievals reduced possibly because of
                drop in HIRS channel 1 noise.
      
      2/3/87    NOAA-9 MSU channel 3 performance significantly deteriorated,
                resulting in large temperature biases above 250 mb.

      2/20/87   NOAA-9 HIRS noise level is unstable and generally increasing
                since about 1/5/87. Increased noise induced by SSU and AVHRR
                instruments resulting in retrieval accuracy.

      2/26/87   NOAA-9 HIRS noise high again. 

      3/18/87   NOAA-10 quality problem above 30 mb. Sounding for NOAA-10
                above 100 mb will be discontinued.

      6/18/87   Processing modified to accept SSU data up to 24 hours old for 
                TRET processing.

                           12.  REFERENCES

12.1  Satellite/Instrument/Data Processing Documentation. 

      Adolf, Werbowetzki 1981. NOAA Technical Report NESS 83: Atmospheric 
         Sounding User's Guide.
      Kidwell, K.B. 1991. NOAA polar orbiter Data (TIROS-N, NOAA-6, NOAA-7, 
         NOAA-8, NOAA-9, NOAA-10, NOAA-11 and NOAA-12) User's Guide. National
         Environmental Satellite Data, and Information Service. NOAA. 141 p
         (revised).
      McMillin, L.M., and C. Dean. 1982. Evaluation of a new operational 
         technique for producing clear radiances. J. Appl. Meteor. 21:1005-
         1014. 
      McMillin, L.M., D.Q. Wark, et al. 1973. NOAA Technical Report NESS 65:
         Satellite Infrared Soundings From NOAA Spacecraft.     
      Smith, W.L., H.M. Woolf, C.M. Hayden, D.Q. Wark, and L.M. McMillin. 
         1979. The TIROS-N operational vertical sounder. Bull. Am. Meteor. 
         Soc. 60:1177-1187.

12.2  Journal Articles and Study Reports. 

      Smith, W.L., and H.M. Woolf. 1976. The use of eigenvectors of 
         statistical covariance matrices for interpreting satellite sounding 
         radiometer observations. J. Atmos. Sci. 33:1127-1140. 69:22-27.

12.3  Archive/DBMS Usage Documentation. 

      The Collected Data of the First ISLSCP Field Experiment is archived at
      the EOS Distributed Active Archive Center (DAAC) at Oak Ridge National
      Laboratory (ORNL), Oak Ridge, Tennessee (Section 13 below).  
      Documentation about using the archive and/or online access to the data 
      at the ORNL DAAC is not available at this revision.

                             13.  DATA ACCESS

13.1  Contacts for Archive/Data Access Information. 

      ORNL DAAC User Services
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      (615) 241-3952

13.2  Archive Identification. 

      EOSDIS Distributed Active Archive Center
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      USA

      Telephone:       (615) 241-3952
      FAX:             (615) 574-4665
      Internet Email:   ornldaac@onrl.gov

13.3  Procedures for Obtaining Data.

      Users may place requests by letter, telephone, electronic mail, FAX, or 
      personal visit. 

13.4  ORNL DAAC Status/Plans. 

      FIFE data will be available from the ORNL DAAC. Please contact the 
      ORNL DAAC User Services Office for the most current information about 
      these data.

                 14.  OUTPUT PRODUCTS AND AVAILABILITY 

14.1  Tape Products. 

      None. 

14.2  Film Products. 

      None.

14.3  Other Products.

      The TIROS Operational Vertical Sounder (TOVS) data are available on FIFE 
      CD-ROM Volume 1.

                        15.  GLOSSARY OF ACRONYMS

CD-ROM       Compact Disk (optical), Read-Only Memory
DAAC         Distributed Active Archive Center
EOSDIS       Earth Observing System Data and Information System
FIFE         First ISLSCP Field Experiment
FIS          FIFE Information System
FOV          Field-of-View
HIRS-2       High Resolution Infrared Sounder-Version 2
IFOV         Instantaneous Field-of-View
ISLSCP       International Satellite Land Surface Climatology Project
MSU          Microwave Sounding Unit
NESDIS       National Environmental Satellite Data and Information Service
NOAA         National Oceanic and Atmospheric Administration
ORNL         Oak Ridge National Laboratory
SSU          Stratospheric Sounding Unit
TOVS         Tiros Operational Vertical Sounder
UTM          Universal Transverse Mercator