1.  TITLE

1.1  Data Set Identification.

     Boundary Layer Heights Using SODAR.

1.2  FIS Data Base Table Name.

     SODAR_DATA.

1.3  CD-ROM File Name.

      \DATA\ATMOS\SODAR\YyyMmm\ydddgrid.SOD.

     Where yy is the last two digits of the year (e.g., Y87=1987) and mm is 
     the month of the year (e.g., M12=December). Note: capital letters indicate
     fixed values that appear on the CD-ROM exactly as shown here, lower case
     indicates characters (values) that change for each path and file.

     The format used for the filenames is: ydddgrid.sfx, where grid is the
     four number code for the location within the FIFE site grid, y is the
     last digit of the year (e.g. 7=1987, and 9=1989), and ddd is the day of
     the year (e.g., 061=sixty-first day in the year). The filename extension 
     (.sfx), identifies the data set content for the file (see Section 8.2) and 
     is equal to .SOD for this data set.

1.4  Revision Date Of This Document.

     May 6, 1994.

     Warning:  This document has not been checked for technical or editorial
               accuracy by the FIFE Information Scientist. There may be 
               inconsistencies with other documents, technical or editorial 
               errors that were inadvertently introduced when the document was 
               compiled or references to preliminary data that were not 
               included on the final CD-ROM.

               Previous versions of this document have been reviewed by the 
               Principal Investigator, the person who transmitted the data to 
               FIS, a FIS staff member, or a FIFE scientist generally familiar 
               with the data.

                             2.  INVESTIGATOR(S)

2.1  Investigator(s) Name And Title.

     Dr. Marvin L. Wesely
     Argonne National Laboratory

2.2  Title Of Investigation.

     Measurements of Boundary-Layer Inversion Heights with a SODAR.

2.3  Contacts (For Data Production Information).

        ____________________________________________________________
       |              |     Contact 1         |       Contact 2     |
       |______________|_______________________|_____________________|
       |2.3.1 Name    |Dr. Marvin L. Wesely   |Mr. David R. Cook    |
       |2.3.2 Address |Bldg. 203, ER          |Bldg. 203, ER        |
       |              |Argonne National Lab   |Argonne National Lab.|
       |      City/St.|Argonne, IL            |Argonne, IL          |
       |      Zip Code|60439                  |60439                |
       |2.3.3 Tel.    |(708) 252-5827         |(708) 252-5840       |
       |2.3.4 Email   |wesely@anler.er.anl.gov|cook@anler.er.anl.gov|
       |______________|_______________________|_____________________|

2.4  Requested Form of Acknowledgment.

     The Boundary Layer Heights Using SODAR data were obtained by M. L. Wesely,
     R. L. Coulter, and associates at Argonne National Laboratory.

                             3.  INTRODUCTION

3.1  Objective/Purpose.

     The aim of acoustic sounder (SODAR) measurements was to provide estimates
     of the height of the mixed layer and the vertical dimensions of inversions
     within the lower kilometer of the atmosphere.

3.2  Summary of Parameters.

     Ground-based inversion height, elevated inversion top, and elevated 
     inversion bottom.

3.3  Discussion.

     The thickness of an elevated inversion as seen by the SODAR is often
     smaller than the difference between the heights of the inversion top and
     bottom, because of oscillations in the heights that occur. The heights 
     were estimated only for the inversions that were clearly associated with 
     the active mixed layer. These data were collected at one location in the
     northwest quadrant of the FIFE study area during the first three Intensive
     Field Campaigns held in 1987.

                             4.  THEORY OF MEASUREMENTS

The signal detected with the SODAR is the amplitude of the backscatter of
acoustic pulses transmitted vertically. This backscatter is caused mostly by 
the rapid temperature fluctuations associated with thermal inversions coupled 
with mechanical mixing in the atmosphere. With appropriate range gating, 
vertical profiles of the acoustic refractive index structure function can be 
plotted versus height, thus mapping inversion heights.

                             5.  EQUIPMENT

5.1  Instrument Description.

     A single, vertically pointing, conventional SODAR was operated at an
     acoustic frequency near 1500 Hz to detect the amplitude (uncalibrated) of
     backscattered acoustic energy. The primary components in the field were a
     1.5-m diameter parabolic dish and transducer that serves as both the 
     transmitter and receiver, a switchbox and field amplifier, sound baffling 
     around the antenna to suppress sidelobes, and electronic cabling to go to 
     the electronics. The electronics were located in a trailer and consisted 
     of an analog signal processor, a digital microprocessor, and a psuedo-
     facsimile display.

     5.1.1  Platform.

            The transmit-receive antenna was located on the ground, and the
            electronics were located in a nearby trailer. The antenna was 
            placed approximately 100 m from the trailer and other equipment so 
            that the antenna would be in a location where the background 
            acoustic noise was small.

     5.1.2  Mission Objectives.

            The purpose of the SODAR system developed at Argonne National 
            Laboratory was to measure atmospheric refraction of sound. This 
            refraction is then used to derive atmospheric temperature and wind
            profiles.

     5.1.3  Key Parameters.

            Key parameters are heights of the mixed layer (ground-based invers-
            ion) and the top and bottom of thermal inversions in the lower
            one kilometer of the atmosphere.

     5.1.4  Principles of Operation.

            The SODAR maps the amplitude of backscattered acoustic energy asso-
            ciated with temperature fluctuations and thus thermal inversions in
            the atmosphere.

     5.1.5  Instrument Measurement Geometry.

            The SODAR system measures vertical profiles from the surface to
            heights of approximately one kilometer. The beam width was 
            typically 10 degrees between half-power points. Energy is both 
            transmitted from and received at the same point, i.e., within the 
            parabolic antenna.

     5.1.6  Manufacturer of Instrument.

            The SODAR was designed and assembled by R.L. Coulter and T.J.
            Martin of Argonne National Laboratory.

5.2  Calibration.

     No calibrations were necessary.

     5.2.1  Specifications.

            Not applicable.

            5.2.1.1  Tolerance.

                     Not applicable.

     5.2.2  Frequency of Calibration.

            Not applicable.

     5.2.3  Other Calibration Information.

            Not applicable.

                             6.  PROCEDURE

6.1  Data Acquisition Methods.

     The SODAR system pointed vertically and sampled acoustic backscatter
     intensity from the measured signal amplitude at 0.8 m height intervals. 
     The amplitude information received was digitized and stored using a 
     computer system that was also used for performing the data analysis. 
     Sampled at the rate of 68 pulses per second, the data within each pulse 
     were averaged by twos or fours and were subsequently averaged in a pulse-
     to-pulse manner for 100 pulses (30 min.) before being stored in memory 
     (Coulter and Wesely 1980).

     The data indicating the magnitude of high-frequency temperature fluctuat-
     ions, were displayed on a pseudo-facsimile chart, and plotted as a 
     function of height with time. Some of the regions of greatest signal can  
     be readily identified as being portions of temperature inversions. The 
     data were extracted by visual inspection of the facsimile charts and 
     entered manually into a data file.

6.2  Spatial Characteristics.

     The FIFE study area, with areal extent of 15 km by 15 km, is located south 
     of the Tuttle Reservoir and Kansas River, and about 10 km from Manhattan, 
     Kansas, USA. The northwest corner of the area has UTM coordinates of 
     4,334,000 Northing and 705,000 Easting in UTM Zone 14.

     6.2.1  Spatial Coverage.

            Horizontal location of data collection occurred at specific fixed
            locations.

            In 1987, the acoustic antenna was located at station 114
            (sitegrid_ID=2731-SOD), which was approximately 100 meters west of
            station 4 (sitegrid_ID=2731-ECA), where the 10-m walkup tower
            for eddy correlation had been placed.

            SITEGRID_ID STN_ID NORTHING EASTING LATITUDE  LONGITUDE   ELEV
            ----------- ------ -------- ------- --------  ---------   ----
            2731-SOD       114  4328678  711110 39 05 01  -96 33 34   446



     6.2.2  Spatial Resolution.

            These are point data; however, vertical resolution of the heights
            was approximately 25 m.

            Horizontal resolution is within 1.5 m which is the diameter of the
            dish containing both the receiver and the transmitter.

6.3  Temporal Characteristics.

     6.3.1  Temporal Coverage.

            Measurements were taken during IFC's 1, 2, and 3. Data were 
            collected between May 28 and June 6, 1987 (IFC-1), June 25 and July 
            11, 1987 (IFC-2), and August 5 and 21, 1987 (IFC-3).

     6.3.2  Temporal Resolution.

            Measurements were recorded as heights of the inversion layers
            averaged over 30-minute intervals.

                             7.  OBSERVATIONS

7.1  Field Notes.

     Usually inversions heights up to one kilometer above the ground can be
     detected. The maximum setting for the range of the facsimile chart varied
     from 0.6 to 1.5 km. Because of noise associated with wind and insects at
     the SODAR antenna, the maximum practical range was typically limited to
     about 1.0 km even though the maximum range displayed on the facsimile was
     usually 1.5 km. During the first few days of both IFC-1 and IFC-5, the
     maximum range of the SODAR was less than one kilometer because the sound
     baffling had not been completed and the insect problem was significant.

                             8.  DATA DESCRIPTION

8.1  Table Definition With Comments.

     The SQL definition for this table is found in the SODAR.TDF file found on
     FIFE CD-ROM Volume 1.

8.2  Type of Data.

--------------------------------------------------------------------------------
|                 8.2.1                  |               |          |          |
|Parameter/Variable Name                 |               |          |          |
--------------------------------------------------------------------------------
|    |               8.2.2               |     8.2.3     |  8.2.4   |  8.2.5   |
|    |Parameter/Variable Description     |Range          |Units     |Source    |
--------------------------------------------------------------------------------
|SITEGRID_ID                             |               |          |          |
|    |This is a FIS grid location code.  |               |          |FIS       |
|    |Site grid codes (SSEE-III) give    |               |          |          |
|    |the south (SS) and east (EE) cell  |               |          |          |
|    |number in a 100x100 array of 200m  |               |          |          |
|    |square cells.  The last 3          |               |          |          |
|    |characters (III) are an instrument |               |          |          |
|    |identifier.                        |               |          |          |
--------------------------------------------------------------------------------
|STATION_ID                              |               |          |          |
|    |The ID number of the station       |min = 114,     |          |FIS       |
|    |where the observations were made.  |max = 114      |          |          |
--------------------------------------------------------------------------------
|OBS_DATE                                |               |          |          |
|    |The date that the observation was  |min = 26-MAY-87|          |ANL       |
|    |made on.                           |,              |          |          |
|    |                                   |max = 22-AUG-89|          |          |
--------------------------------------------------------------------------------
|OBS_TIME                                |               |          |          |
|    |The time of the observation.       |min = 15.  max |[GMT]     |ANL       |
|    |                                   |= 2345         |          |          |
--------------------------------------------------------------------------------
|GRND_INVERSION_HEIGHT                   |         *     |          |          |
|    |The height of the initiation of    |min = 50,      |[meters]  |SODAR     |
|    |the mixed layer as measured from   |max = 600,     |          |          |
|    |the ground.  If 9999 then no       |missing = 9999 |          |          |
|    |inversion found at this SCALE      |               |          |          |
|    |setting.                           |               |          |          |
--------------------------------------------------------------------------------
|ELEVTD_INVERSION_TOP                    |         *     |          |          |
|    |The top of thermal inversion       |min = 100,     |[meters]  |SODAR     |
|    |zone.  If 9999 then no inversion   |max = 1500,    |          |          |
|    |found at this SCALE setting.       |missing = 9999 |          |          |
--------------------------------------------------------------------------------
|ELEVTD_INVERSION_BOTTOM                 |         *     |          |          |
|    |The bottom of thermal inversion    |min = 50,      |[meters]  |SODAR     |
|    |zone.  If 9999 then no inversion   |max = 1450,    |          |          |
|    |found at this SCALE setting.       |missing = 9999 |          |          |
--------------------------------------------------------------------------------
|SODAR_MAX_HEIGHT_SCALE                  |         *     |          |          |
|    |The maximum height on setting on   |min = 600,     |[meters]  |SODAR     |
|    |the SODAR chart.  If this is 9999  |max = 1500,    |          |          |
|    |then no readings were taken.       |missing = 9999 |          |          |
--------------------------------------------------------------------------------
|COMMENT1                                |        **     |          |          |
|    |A comment describing any           |               |          |ANL       |
|    |inversion found.                   |               |          |          |
--------------------------------------------------------------------------------
|COMMENT2                                |        **     |          |          |
|    |A comment describing any           |               |          |ANL       |
|    |inversion found.                   |               |          |          |
--------------------------------------------------------------------------------
|COMMENT3                                |        **     |          |          |
|    |A comment describing any           |               |          |ANL       |
|    |inversion found.                   |               |          |          |
--------------------------------------------------------------------------------
|FIFE_DATA_CRTFCN_CODE                   |       ***     |          |          |
|    |The FIFE Certification Code for    |               |          |FIS       |
|    |the data, in the following format: |               |          |          |
|    |CPI (Certified by PI), CPI-???     |               |          |          |
|    |(CPI - questionable data).         |               |          |          |
--------------------------------------------------------------------------------
|LAST_REVISION_DATE                      |               |          |          |
|    |The last revision date for the     |min = 07-DEC-88|          |FIS       |
|    |data, in the format (DD-MMM-YY).   |,              |          |          |
|    |                                   |max = 22-APR-89|          |          |
--------------------------------------------------------------------------------

Footnotes:

    *  For these parameters, 9999 means no data were collected, when the
       SODAR_MAX_HEIGHT_SCALE = 9999.

   **  Valid Comments are:

       Additional layer(s) existed above the active mixed layer.
       Disturbance was obvious, usually with multiple layers.
       Elevated inversions merged during half hour.
       Ground-based inversion became elevated during the half hour.
       Inversion weakened, no longer distinguishable from noise.
       Precipitation occurred during the half hour.
       The SODAR chart maximum height scale was changed during half hour.
       The elevated inversion bottom appears to be near cloud base.
       The elevated inversion top and/or elevated inversion bottom height was
           greater than the SODAR chart maximum height scale.
       The ground-based inversion height top was lower than detectable (below
           50 m).

  *** Decode the FIFE_DATA_CRTFCN_CODE field as follows:

      The primary certification codes are:

      EXM - Example or Test data (not for release)
      PRE - Preliminary (unchecked, use at your own risk)
      CPI - Checked by Principal Investigator (reviewed for quality)
      CGR - Checked by a group and reconciled (data comparisons and
            cross checks)

      The certification code modifiers are:

      PRE-NFP  - Preliminary - Not for publication, at the request of
                 investigator.
      CPI-MRG  - PAMS data which is "merged" from two separate receiving
                 stations to eliminate transmission errors.
      CPI-???  - Investigator thinks data item may be questionable.

8.3  Sample Data Record.


     SITEGRID_ID STATION_ID OBS_DATE  OBS_TIME GRND_INVERSION_HEIGHT
     ----------- ---------- --------- -------- ---------------------
     2731-SOD           114 26-MAY-87      515                  9999
     2731-SOD           114 26-MAY-87      545                  9999
     2731-SOD           114 26-MAY-87      615                  9999
     2731-SOD           114 26-MAY-87      645                  9999
     
     ELEVTD_INVERSION_TOP ELEVTD_INVERSION_BOTTOM SODAR_MAX_HEIGHT_SCALE
     -------------------- ----------------------- ----------------------
                     9999                    9999                   9999
                     9999                    9999                   9999
                     9999                    9999                   9999
                     9999                    9999                   9999
     
     COMMENT1
     ------------------------------------------------------------
     
     
     
     
     
     COMMENT2
     ------------------------------------------------------------
     
     
     
     
     
     COMMENT3
     ------------------------------------------------------------
     
     
     
     
     
     FIFE_DATA_CRTFCN_CODE LAST_REVISION_DATE
     --------------------- ------------------
     CPI                   07-DEC-88
     CPI                   07-DEC-88
     CPI                   07-DEC-88
     CPI                   07-DEC-88

8.4  Data Format.

     The CD-ROM file format consists of numerical and character fields of 
     varying length separated by commas. The character fields are enclosed with 
     a single apostrophe. There are no spaces between the fields.  Each file 
     begins with five header records.  Header records contain the following 
     information:

     Record 1    Name of this file, its table name, number of records in
                 this file, path and name of the document that describes 
                 the data in this file, and name of principal investigator 
                 for these data.
     Record 2    Path and filename of the previous data set, and path and 
                 filename of the next data set.  (Path and filenames for files 
                 that contain another set of data taken at the same site on 
                 the same day.)
     Record 3    Path and filename of the previous site, and path and filename 
                 of the next site.  (Path and filenames for files of the same 
                 data set taken on the same day for the previous and next 
                 sites (sequentially numbered by SITEGRID_ID)).
     Record 4    Path and filename of the previous date, and path and filename 
                 of the next date.  (Path and filenames for files of the same 
                 data set taken at the same site for the previous and next 
                 date.)
     Record 5    Column names for the data within the file, delimited by 
                 commas.
     Record 6    Data records begin.

     Each field represents one of the attributes listed in the chart in 
     section 8.2 and described in detail in the TDF file (see Section 8.1). 
     These fields are in the same order as in the chart.

8.5  Related Data Sets.

     FIFE Radiosonde Data.
     Quick Look Boundary Layer Height.
     FIFE Temperature and Humidity Profiles.
     FIFE Radiosonde Wind Profiles.
     Atmospheric Turbulence Data from the NCAR King Air.

                             9.  DATA MANIPULATIONS

9.1  Formulas.

     9.1.1  Derivation Techniques/Algorithms.

            The heights were calculated by range gating according to trans-
            mission times and estimates of the speed of sound. For this 
            purpose, no calibrations were necessary. Occasional spot checks on 
            the height of the mixed layer were made by comparison to the 
            results of radiosonde launches a few kilometers away.

            Ambient mean surface temperature was recorded and incorporated into
            the calculations of heights. Data were analyzed by visual 
            inspection of the psuedo-facsimile charts and manual recording of 
            the heights.

            Heights were derived from the SODAR pseudo-facsimile charts by
            direct visual inspection and consideration of the time and height
            scales on the charts.

9.2  Data Processing Sequence.

     9.2.1  Processing Steps and Data Sets.

            After each IFC, the processing of the pseudo-facsimile charts were
            done at Argonne National Laboratory.

            The values were recorded in a notebook and then typed into a
            computer data file.

     9.2.2  Processing Changes.

            None.

9.3  Calculations.

     9.3.1  Special Corrections/Adjustments.

            Heights were read directly from the SODAR pseudo-facsimile charts.
            Because the acoustic pulse lengths were finite, the height derived
            was altered by one-half the pulse length from the edge of the
            inversion seen on the chart.

9.4  Graphs and Plots.

     None.

                             10.  ERRORS

10.1  Sources of Error.

      Errors in the heights can occur as a result of misreading the charts.
      Experimental factors that could cause underestimation of the parameters
      include volume averaging of the signals backscattered from the acoustic
      beam, short averaging time (finite acoustic pulse lengths) used in the
      SODAR computations, and excessive filtering of the acoustic backscatter
      signals by the SODAR system.

10.2  Quality Assessment.

      10.2.1  Data Validation by Source.

              The 1987 SODAR data was checked by Drs. Coulter and Wesely of 
              ANL. Sorbjan et al. (1991) analyzed the FIFE SODAR data obtained 
              during the second IFC in 1987 using local similarity theory, and 
              concluded that the data seem to produce temperature profiles that 
              agree qualitatively with predictions and with results of Fairall 
              (1987).

      10.2.2  Confidence Level/Accuracy Judgment.

              There is some uncertainty in the height measurements. Because of
              the smearing associated with a finite height, the transmission
              beam pulse length, and typical variations that occur within each
              half-hour measurement period, the heights have an uncertainty of
              +/-25 m.

      10.2.3  Measurement Error for Parameters and Variables.

              The uncertainty of the height measurements for the elevated 
              inversion top, elevated inversion bottom, and ground-based 
              inversion height were typically plus-or-minus 25 m.

              Other errors mentioned in Section 10.1 above were not quantified.

       10.2.4  Additional Quality Assessment Applied.

               FIS staff applied a general QA procedure to the data to identify
               inconsistencies and problems for potential users. As a general
               procedure, the FIS QA consisted of examining the maximum, mini-
               mum, average, and standard deviations that appeared inconsistent
               with the mean. In some cases, histograms were examined to deter-
               mine whether outliers were consistent with the shape of the data
               distribution.

               The discrepancies, that were identified, are reported
               as problems in Section 11.1.

                             11.  NOTES

11.1  Known Problems With The Data.

      As of the revision date of this document, the following
      discrepancies or errors in the data have been reported:

      Results of the FIS staff quality assessment:

      *  Investigators data document suggests that there is data from 22-AUG-87
         to 22-AUG-89, but no 1989 data exists in the FIFE data base.

      *  90% of the data is -999.

11.2  Usage Guidance.

      Data on the heights of inversions were obtained by other investigators
      during the FIFE campaigns. For example, radiosonde data collected by 
      Brutsaert (FIFE Radiosonde Data) can be used to infer inversion heights; 
      LIDAR Quick Look Boundary Layer Height data collected by Eloranta, and 
      NOAA Wind Profiles Using LIDAR data collected by Gal-Chen provide 
      other measures of the mixing layer depth; and Atmospheric Turbulence Data
      from the NCAR King Air obtained by Grossman and Sinclair often can be 
      used to infer information on inversions. These data set and documents 
      describing them are included on FIFE CD-ROM Volume 1.

11.3  Other Relevant Information.

      None.

                          12.  REFERENCES

12.1  Satellite/Instrument/Data Processing Documentation.

      Culter, R.L., and M.L. Wesely. 1980. Estimates of surface heat flux from
         SODAR and Laser Scintillation measurements in the unstable boundary 
         layer. J. Appl. Meteorol. 19:1209-1222.
      Greenfield, R.J., M. Teufel, D.W. Thomson, and R.L. Coulter. 1974. A
         method for measurement of temperature profiles in inversions from 
         refractive transmission of sound. J. Geophys. Res. 79:5551-5554.

12.2  Journal Articles and Study Reports.

      Brutsaert, W., M. Sugita, and L.J. Fritschen. 1990. Inner region humidity
         characteristics of the neutral boundary layer over prairie terrain.
         Water Resour. Res. 26:2931-2936.
      Coulter, R.L. 1979. A comparison of three methods for measuring mixing-
         layer height. J. Appl. Meteorol. 18:1495-1499.
      Eberhard, W.L., R.E. Cupp, and K.R. Healy. 1989. Doppler LIDAR 
         measurement of profiles of turbulence and momentum flux. J. Atmos. 
         Oceanic Technol. 6:809-819.
      Fairall, C.W. 1987. A top-down and bottom-up diffusion model of C[(T)E-2]
         and C[(Q)E-2] in the entraining convective boundary layer. J. Atmos.
         Sci. 44:1009-1017.
      Gal-Chen, T., and R.A. Kropfli. 1984. Bouyancy and pressure perturbations
         derived from dual-Doppler radar observations of the planetary boundary
         layer: applications for matching models with observations. J. Atmos.
         Sci. 41:3007-3020.
      Kunkel, K.E., E.W. Eloranta, and J.A. Weinman. 1980. Remote determination
         of winds, turbulence spectra and energy dissipation rates in the 
         boundary layer from LIDAR measurements. J. Atmos. Sci. 37:978-985.
      Sellers, P.J., F.G. Hall, G. Asrar, D.E. Strebel, and R.E. Murphy. 1988.
         The first ISLSCP field experiment (FIFE). Bull. Am. Meteorol. Soc.
         69:22-27.
      Sorbjan, Z., R.L. Coulter, and M.L. Wesely. 1991. Similarity scaling
         applied to SODAR observations of the convective boundary layer above 
         an irregular hill. Boundary-layer Meteorol. 56:33-50.
      Sugita, M., and W. Brutsaert. 1990. Wind velocity measurements in the
         neutral boundary layer above hilly prairie. J. Geophys. Res.
         95:7617-7624.

12.3  Archive/DBMS Usage Documentation. 

      The Collected Data of the First ISLSCP Field Experiment is archived at
      the EOS Distributed Active Archive Center (DAAC) at Oak Ridge National
      Laboratory (ORNL), Oak Ridge, Tennessee (Section 13 below).  
      Documentation about using the archive and/or online access to the data 
      at the ORNL DAAC is not available at this revision.

                             13.  DATA ACCESS

13.1  Contacts for Archive/Data Access Information. 

      ORNL DAAC User Services
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      (615) 241-3952

13.2  Archive Identification. 

      EOSDIS Distributed Active Archive Center
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      USA

      Telephone:       (615) 241-3952
      FAX:             (615) 574-4665
      Internet Email:   ornldaac@onrl.gov

13.3  Procedures for Obtaining Data.

      Users may place requests by letter, telephone, electronic mail, FAX, or 
      personal visit. 

13.4  ORNL DAAC Status/Plans. 

      FIFE data will be available from the ORNL DAAC. Please contact the 
      ORNL DAAC User Services Office for the most current information about 
      these data.

                 14.  OUTPUT PRODUCTS AND AVAILABILITY

14.1  Tape Products.

      None.

14.2  Film Products.

      None.

14.3  Other Products.

      The Boundary Layer Heights Using SODAR data are available on FIFE CD-ROM 
      Volume 1.

                        15.  GLOSSARY OF ACRONYMS

CD-ROM            Compact Disk (optical), Read-Only Memory
DAAC              Distributed Active Archive Center
EOSDIS            Earth Observing System Data and Information System
FIFE              First ISLSCP Field Experiment
FIS               FIFE Information System
ISLSCP            International Satellite Land Surface Climatology Project
ORNL              Oak Ridge National Laboratory
UTM               Universal Transverse Mercator