1.  TITLE

1.1  Data Set Identification. 

     FIFE Radiosonde Wind Profiles.

1.2  FIS Data Base Table Name. 

     WIND_PROFILE_SONDE_DATA

1.3  CD-ROM File Name. 

      \DATA\ATMOS\WIND_SON\YyyMmm\ydddNnnn.WPS

     Where yy is the last two digits of the year (e.g. Y87=1987), mm is the
     month of the year (e.g. M12=December), and ddd is the day of the year,
     (e.g. 061=sixty-first day in the year). Note: capital letters indicate 
     fixed values that appear on the CD-ROM exactly as shown here, lower case 
     indicates characters (values) that change for each path and file.

     The format used for the filenames is: ydddNnnn.sfx, y is the 
     last digit of the year (e.g. 7=1987, and 9=1989), ddd is the day of 
     the year, and nnn is the flight number (002 - 450). The file extension, 
     (.sfx), identifies the data set content for the file and is equal to 
     .WPS for this data set. 

1.4  Revision Date Of This Document. 
  
     April 22, 1994.

     Warning:  This document has not been checked for technical or editorial
               accuracy by the FIFE Information Scientist. There may be 
               inconsistencies with other documents, technical or editorial 
               errors that were inadvertently introduced when the document was 
               compiled or references to preliminary data that were not 
               included on the final CD-ROM.

               Previous versions of this document have been reviewed by the 
               Principal Investigator, the person who transmitted the data to 
               FIS, a FIS staff member, or a FIFE scientist generally familiar 
               with the data.

                         2.  INVESTIGATOR(S)

2.1  Investigator(s) Name And Title. 

     Dr. Wilfred H. Brutsaert
     School of Civil and Environmental Engineering

2.2  Title Of Investigation. 

     Radiosonde analysis of wind velocity measurements in the boundary layer 
     above a hilly prairie.

2.3  Contacts (For Data Production Information).
      ______________________________________________________
     |              |      Contact 1                        |
     |______________|_______________________________________|
     |2.3.1 Name    |Dr. Wilfred H. Brutsaert               |
     |2.3.2 Address |School of Civil and                    |
     |              |Environmental Eng.                     |
     |              |Hollister Hall                         |
     |              |Cornell University                     |
     |      City/St |Ithaca, NY                             |
     |      Zip Code|14853-3501                             |
     |2.3.3 Tel.    |(607) 255-3676                         |
     |2.3.4 Email   |WBH@CORNELLA.BITNET                    |
     |              |WHB@CORNELLA.CIT.CORNELL.EDU (Internet)|
     |______________|_______________________________________|

2.4  Requested Form of Acknowledgment.

     The FIFE Radiosonde Wind Profiles were collected by a team from Cornell 
     University, directed by Prof. W. Brutsaert.

                            3.  INTRODUCTION

3.1  Objective/Purpose. 

     The objective of this study was to calculate wind velocity and wind 
     direction from successive horizontal positions of a radiosonde.

3.2  Summary of Parameters. 

     Wind velocity and direction.

3.3  Discussion. 

     Intensive radiosonde flights, carried out by Dr. Wilfred H. Brutsaert 
     during the summer and fall of 1987 and the late summer of 1989 have 
     allowed the measurement of the atmospheric profiles of wind velocity 
     and direction. The wind profile data described in this document was 
     derived (corrected for algorithm inconsistencies) from the raw radiosonde 
     data (FIFE Radiosonde Data) collected during FIFE by Dr. Wilfred H. 
     Brutsaert. The raw data have also been corrected for sensor delays 
     (FIFE Temperature and Humidity Profiles) and have been interpolated to 
     a set standard pressure level (FIFE Standard Pressure Level Radiosonde 
     Data). These other data sets are described separately.

                        4.  THEORY OF MEASUREMENTS

The wind velocity data in the FIFE Radiosonde Data were calculated 
by means of an algorithm (developed by the manufacturer) involving 
the radius of the Earth, the curvature of the surface, etc. This algorithm is 
correct but produces wind speeds and directions with a large degree of noise 
and scatter. Therefore, Dr. Brutsaert decided to re-calculated Average wind 
velocity and direction in a simpler way for a flat Earth. This new method used 
successive horizontal positions of the radiosonde balloon in relation to it's 
release point to calculate average wind speed and direction. The variables 
used to make these calculations were obtained from the FIFE Radiosonde Data.

                            5.  EQUIPMENT

5.1  Instrument Description. 

     See the document entitled FIFE Radiosonde Data for details on the 
     instrumentation used to collect the original data used here.

     5.1.1  Platform.

            See Section 5.1 for details.

     5.1.2  Mission Objectives. 

            See Section 5.1 for details.

     5.1.3  Key Variables. 

            See Section 5.1 for details.

     5.1.4  Principles of Operation.

            See Section 5.1 for details.

     5.1.5  Instrument Measurement Geometry. 

            See Section 5.1 for details.

     5.1.6  Manufacturer of Instrument. 

            See Section 5.1 for details.

5.2  Calibration. 

     See the document entitled FIFE Radiosonde Data for details on the 
     calibration of the original data used to generate the data set described 
     here.

     5.2.1  Specifications. 

            See Section 5.2 for details.

            5.2.1.1  Tolerance. 

            See Section 5.2 for details.

     5.2.2  Frequency of Calibration. 

            See Section 5.2 for details.

     5.2.3  Other Calibration Information. 

            See Section 5.2 for details.

                          6.  PROCEDURE

6.1  Data Acquisition Methods. 

     The Wind Profile Sonde data was calculated from the FIFE Radiosonde
     Data on FIFE CD-ROM Volume 1.

6.2  Spatial Characteristics. 

     The FIFE study area, with areal extent of 15 km by 15 km, is located south 
     of the Tuttle Reservoir and Kansas River, and about 10 km from Manhattan, 
     Kansas, USA. The northwest corner of the area has UTM coordinates of 
     4,334,000 Northing and 705,000 Easting in UTM Zone 14.

     6.2.1  Spatial Coverage. 

            The Wind profile sonde data were calculated from radiosonde data 
            collected from balloon releases at the FIFE site listed below:

            SITEGRID_ID  SN_ID  NORTHING  EASTING  LATITUDE  LONGITUDE  ELEV
            -----------  -----  --------  -------  --------  ---------  ----
            0928-RSB     102    4332188   710674   39 06 55  -96 33 48  342

            The spatial coverage varies with the flight. It depends upon the 
            horizontal distance and direction the sonde has traveled from the 
            launch site.

     6.2.2  Spatial Resolution. 

            Resolution for the measurements are about 15 to 20 meter.

6.3  Temporal Characteristics. 

     6.3.1  Temporal Coverage

            The data were collected during the five IFC's, covering the
            period from May 25, 1987 through August 12, 1989.

                         IFC              Dates
                        -----      -------------------
                        IFC-1      05/26/87 - 06/06/87
                        IFC-2      06/25/87 - 07/11/87
                        IFC-3      08/06/87 - 08/21/87
                        IFC-4      10/05/87 - 10/16/87
                        IFC-5      07/24/89 - 08/12/89

     6.3.2  Temporal Resolution.

            The soundings were made at 2 to 3 hour intervals, depending on
            weather conditions.

                           7.  OBSERVATIONS

7.1  Field Notes.

     Not applicable.

                         8.  DATA DESCRIPTION

8.1  Table Definition With Comments. 

     The SQL definition for this table is found in the WIND_SON.TDF 
     file found on FIFE CD-ROM Volume 1.

8.2  Type of Data. 

--------------------------------------------------------------------------------
|                 8.2.1                  |               |          |          |
|Parameter/Variable Name                 |               |          |          |
--------------------------------------------------------------------------------
|    |               8.2.2               |     8.2.3     |  8.2.4   |  8.2.5   |
|    |Parameter/Variable Description     |Range          |Units     |Source    |
--------------------------------------------------------------------------------
|SITEGRID_ID                             |               |          |          |
|    |This is a FIS grid location code.  |               |          |FIS       |
|    |Site grid codes (SSEE-III) give    |               |          |          |
|    |the south (SS) and east (EE) cell  |               |          |          |
|    |number in a 100x100 array of 200m  |               |          |          |
|    |square cells.  The last 3          |               |          |          |
|    |characters (III) are an instrument |               |          |          |
|    |identifier.                        |               |          |          |
--------------------------------------------------------------------------------
|STATION_ID                              |               |          |          |
|    |The station ID designating the     |min = 102,     |          |FIS       |
|    |location of the observations.      |max = 103      |          |          |
--------------------------------------------------------------------------------
|OBS_DATE                                |               |          |          |
|    |The date of the observations.      |min = 25-MAY-87|          |FIS       |
|    |                                   |,              |          |          |
|    |                                   |max = 12-AUG-89|          |          |
--------------------------------------------------------------------------------
|START_TIME                              |               |          |          |
|    |The time that this radiosonde      |min = 30,      |[GMT]     |FIS       |
|    |flight was started.                |max = 2355,    |          |          |
|    |                                   |missing = -9999|          |          |
--------------------------------------------------------------------------------
|FLIGHT_NUM                              |               |          |          |
|    |This is the flight number of the   |               |          |FIS       |
|    |radiosonde balloon flight where    |               |          |          |
|    |the data was recorded.             |               |          |          |
--------------------------------------------------------------------------------
|EAST_WEST_OFFSET                        |               |          |          |
|    |The east/west offset from the      |min = -6142,   |[meters]  |FIS       |
|    |starting location.  East is        |max = 17730    |          |          |
|    |positive.  West is negative.       |               |          |          |
--------------------------------------------------------------------------------
|NORTH_SOUTH_OFFSET                      |               |          |          |
|    |The north/south offset from the    |min = -9969,   |[meters]  |FIS       |
|    |starting location.  North is       |max = 15087    |          |          |
|    |positive, South is negative.       |               |          |          |
--------------------------------------------------------------------------------
|HEIGHT_ABV_MEAN_SEA_LVL                 |               |          |          |
|    |The height above mean sea level    |min = 340,     |[meters]  |FIS       |
|    |for each observation.              |max = 11397.32 |          |          |
--------------------------------------------------------------------------------
|WIND_SPEED                              |               |          |          |
|    |The average speed of the wind in   |min = 0,       |[meters][s|FIS       |
|    |this 30 minutes.                   |max = 360      |ec^-1]    |          |
--------------------------------------------------------------------------------
|WIND_DIR                                |               |          |          |
|    |The direction from which the wind  |min = .026,    |[degrees] |FIS       |
|    |is blowing, measured in degrees    |max = 359.924  |          |          |
|    |from north.                        |               |          |          |
--------------------------------------------------------------------------------
|FIFE_DATA_CRTFCN_CODE                   |      *        |          |          |
|    |The FIFE Certification Code for    |CPI - checked b|          |FIS       |
|    |the data, in the following format: |y primary inves|          |          |
|    |CPI (Certified by PI), CPI-???     |tigator        |          |          |
|    |(CPI - questionable data).         |               |          |          |
--------------------------------------------------------------------------------
|LAST_REVISION_DATE                      |               |          |          |
|    |The last revision date for the     |min = 24-MAY-90|          |FIS       |
|    |data, in the format (DD-MMM-YY).   |,              |          |          |
|    |                                   |max = 26-JUL-90|          |          |
-------------------------------------------------------------------------------- 

Footnote:

    * Valid levels 

      The primary certification codes are:

      EXM - Example or Test data (not for release)
      PRE - Preliminary (unchecked, use at your own risk)
      CPI - Checked by Principal Investigator (reviewed for quality)
      CGR - Checked by a group and reconciled (data comparisons and 
            cross checks)

      The certification code modifiers are:

      PRE-NFP  - Preliminary - Not for publication, at the request of 
                 investigator.
      CPI-MRG  - PAMS data that is "merged" from two separate receiving 
                 stations to eliminate transmission errors.
      CPI-???  - Investigator thinks data item may be questionable.

8.3  Sample Data Base Data Record.

     SITEGRID_ID STATION_ID OBS_DATE   START_TIME FLIGHT_NUM EAST_WEST_OFFSET
     ----------- ---------- ---------- ---------- ---------- ----------------
     0928-RSB           102 25-MAY-87        2354          1                3
     0928-RSB           102 25-MAY-87        2354          1
     0928-RSB           102 25-MAY-87        2354          1                6
     0928-RSB           102 25-MAY-87        2354          1               10

     NORTH_SOUTH_OFFSET HEIGHT_ABV_MEAN_SEA_LVL WIND_SPEED   WIND_DIR
     ------------------ ----------------------- ---------- ----------
                    134                375.5000      .0000   181.2000
                    167                415.0000     6.7000   175.3000
                    215                443.0000    12.1000   187.1000
                    271                471.0000    11.2000   183.8000

     FIFE_DATA_CRTFCN_CODE LAST_REVISION_DATE
     --------------------- ------------------
     CPI                   04-JUN-90
     CPI                   04-JUN-90
     CPI                   04-JUN-90
     CPI                   04-JUN-90 

8.4  Data Format.

     The CD-ROM file format consists of numerical and character fields of 
     varying length separated by commas. The character fields are enclosed with 
     a single apostrophe. There are no spaces between the fields.  Each file 
     begins with five header records.  Header records contain the following 
     information:

     Record 1    Name of this file, its table name, number of records in
                 this file, path and name of the document that describes 
                 the data in this file, and name of principal investigator 
                 for these data.
     Record 2    Path and filename of the previous data set, and path and 
                 filename of the next data set.  (Path and filenames for files 
                 that contain another set of data taken at the same site on 
                 the same day.)
     Record 3    Path and filename of the previous site, and path and filename 
                 of the next site.  (Path and filenames for files of the same 
                 data set taken on the same day for the previous and next 
                 sites (sequentially numbered by SITEGRID_ID)).
     Record 4    Path and filename of the previous date, and path and filename 
                 of the next date.  (Path and filenames for files of the same 
                 data set taken at the same site for the previous and next 
                 date.)
     Record 5    Column names for the data within the file, delimited by 
                 commas.
     Record 6    Data records begin.

     Each field represents one of the attributes listed in the chart in 
     Section 8.2 and described in detail in the TDF file (see section 8.1). 
     These fields are in the same order as in the chart.


8.5  Related Data Sets. 

     FIFE Radiosonde Data.
     This data set contains Dr. Brutsaert's actual (raw) radiosonde 
     observations.

     FIFE Standard Pressure Level Radiosonde Data.
     This data set contains temperature and humidity values at standard levels 
     (5 mb intervals) derived from Dr. Brutsaert's raw radiosonde data.

     FIFE Temperature and Humidity Profiles.
     This data set contains corrected temperature and humidity profile data 
     derived from Dr. Brutsaert's radiosonde measurements.

                         9.  DATA MANIPULATIONS

9.1  Formulas. 

     9.1.1  Derivation Techniques/Algorithms.

            Dr. Brutsaert calculated wind velocity and direction by obtaining 
            horizontal distance between the sonde and the release point. This 
            distance was obtained from the elevation angle measured by the 
            optical theodolite and from the balloon height. Dr. Brutsaert, 
            recalculated the height, and humidity (see Special 
            Corrections/Adjustments Section 9.3.1 for details) for details. 
            The balloon height was calculated by adding 10 m (the length of 
            the string) to the height of the sonde. The horizontal distance of 
            the sonde, together with the measured azimuth angle (also obtained 
            from the FIFE Radiosonde Data), produced the horizontal position of 
            the sonde. Finally, successive horizontal positions allowed the 
            calculation of average wind velocity and direction over the 
            interval. Note as a result of this addition of 10 m for most 
            flights, the height of the wind measurements in this data set 
            is 10 meters higher than the companion values in the original 
            FIFE Radiosonde Data.

9.2  Data Processing Sequence. 

     9.2.1  Processing Steps and Data Sets. 

            1) Obtained pressure, temperature, dry-bulb temperature and wet-
               bulb temperature data from FIFE Radiosonde Data set.
            2) Made corrections for sensor delays (see the 
               FIFE Radiosonde Data document for details)
            3) Re-calculated height of radiosonde instrument (see section 
               9.3.1 for details)
            4) Calculated balloon height.
            5) Obtained elevation angle and azimuth angle (of balloon) from the
               original FIFE Radiosonde Data set.
            6) Calculated horizontal distance of balloon from release point,
               using elevation angle and balloon height.
            7) Calculated horizontal position of balloon using horizontal 
               distance and azimuth angle.
            8) Calculated wind velocity and direction from successive 
               horizontal positions.

     9.2.2  Processing Changes. 

            None.

9.3  Calculations. 

     9.3.1  Special Corrections/Adjustments. 

            The height of the sonde was re-calculated from the pressure, 
            temperature (obtained from the FIFE Radiosonde Data) and 
            humidity (derived from the time shifted dry-bulb temperature and 
            wet-bulb temperature data, see the FIFE Radiosonde Wind Profiles 
            document for details). It should be noted that these "improved" 
            heights, as listed in the FIFE Temperature and Humidity Profiles,
            are not very different (except for the conversion from height above 
            ground level to height above sea level) from those listed in the 
            FIFE Radiosonde Data so that it should be easy to recover the 
            original pressures (which are not listed here) from the FIFE 
            Radiosonde Data.

9.4  Graphs and Plots. 

     None.

                          10.  ERRORS

10.1  Sources of Error. 

      Not available at this revision.

10.2  Quality Assessment. 

      10.2.1  Data Validation by Source. 

              Not available at this revision.

      10.2.2  Confidence Level/Accuracy Judgment. 

              Not available at this revision.

      10.2.3  Measurement Error for Parameters and Variables. 

              Not available at this revision.

      10.2.4  Additional Quality Assessment Applied. 

              FIS staff applied a general QA procedure to the data to identify 
              inconsistencies and problems for potential users. As a general 
              procedure, the FIS QA consisted of examining the maximum, 
              minimum, average, and standard deviation for each numerical 
              field in the data table. In some cases, histograms were examined 
              to determine whether outliers were consistent with the shape of 
              the data distribution. Inconsistencies and problems found in the 
              QA check are described is section 11.1 (Known Problems With The 
              Data).

                             11.  NOTES

11.1  Known Problems With The Data. 

      As of the revision data of this document, the following discrepancies or 
      errors in the data have been reported:

      1)  On June 27, 1987 some observation times are missing (encoded as 
          -9999). The FIS staff did not receive observation time, so a missing 
          flag was entered.
  
      2)  For more information on known problems with the data see the 
          document which describes the FIFE Radiosonde Data.

11.2  Usage Guidance. 

      These data are useful for the study of the atmospheric boundary layer.

11.3  Other Relevant Information. 

      Not available at this revision.

                           12.  REFERENCES

12.1  Satellite/Instrument/Data Processing Documentation. 

      ADAS Operating Manual, AIR, Inc. Boulder CO.

12.2  Journal Articles and Study Reports. 

      Brutsaert, W. and M. Sugita. 1991. A bulk similarity approach in the 
         atmospheric boundary layer using radiometric skin temperature to 
         determine regional surface fluxes. Boundary-Layer Meteor. 55:1-23.
      Brutsaert, W. and M. Sugita. 1992. Self-preservation in the diurnal 
         evolution of the surface energy budget to determine daily 
         evaporation. Jour. Geophys. Res. 97:18,377-18,382.
      Brutsaert, W. and M. Sugita. 1992. Regional surface fluxes under non-
         uniform and patchy soil moisture conditions during drying. Water 
         Resour. Res. 28:1669-1674. 
      Sugita, M. and W. Brutsaert. 1990. Wind velocity measurements in the 
         neutral boundary layer above hilly prairie. Jour. Geophys. Res. 
         (Atmos.). 95(D6):7617-7624.
      Sugita, M. and W. Brutsaert. 1990. Regional surface fluxes from remotely 
         sensed skin temperature and lower boundary layer measurements. Water 
         Resour. Res. 26:2937-2944.
      Sugita, M. and W. Brutsaert. 1991. Daily evaporation over a region from 
         lower boundary layer profiles measured with radiosonde. Water Resour. 
         Res. 27:747-752.
      Sugita, M. and W. Brutsaert. 1992. Landsat surface temperatures and 
         radiosoundings to obtain regional surface fluxes of heat and water 
         vapor. Water Resour. Res. 28:1675-1679.
      Sugita, M. and W. Brutsaert. 1992. The stability functions in the bulk 
         similarity formulation for the unstable boundary layer. Boundary-
         Layer Meteor. 61:65-80.

12.3  Archive/DBMS Usage Documentation. 

      The Collected Data of the First ISLSCP Field Experiment is archived at
      the EOS Distributed Active Archive Center (DAAC) at Oak Ridge National
      Laboratory (ORNL), Oak Ridge, Tennessee (section 13 below).  
      Documentation about using the archive and/or online access to the data 
      at the ORNL DAAC is not available at this revision.

                             13.  DATA ACCESS

13.1  Contacts for Archive/Data Access Information. 

      ORNL DAAC User Services
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      (615) 241-3952

13.2  Archive Identification. 

      EOSDIS Distributed Active Archive Center
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      USA

      Telephone:       (615) 241-3952
      FAX:             (615) 574-4665
      Internet Email:   ornldaac@onrl.gov

13.3  Procedures for Obtaining Data.

      Users may place requests by letter, telephone, electronic mail, FAX, or 
      personal visit. 

13.4  ORNL DAAC Status/Plans. 

      FIFE data will be available from the ORNL DAAC.  Please contact the 
      ORNL DAAC User Services Office for the most current information about 
      these data.

                      14.  OUTPUT PRODUCTS AND AVAILABILITY

14.1  Tape Products. 

      None

14.2  Film Products. 

      None.

14.3  Other Products.

      FIFE Radiosonde Wind Profiles are available on FIFE CD-ROM Volume 1.

                        15.  GLOSSARY OF ACRONYMS

ABL           Atmospheric Boundary Layer
ASL           Above Sea Level
AGL           Above Ground Level
CD-ROM        Compact Disk (optical), Read-Only Memory
DAAC          Distributed Active Archive Center
EOS           Earth Observing System
EOSDIS        EOS Data and Information System.
FIFE          First ISLSCP Field Experiment
FIS           FIFE Information System
GMT           Greenwich Mean Time
IFC           Intensive Field Campaign
IFOV          Instantaneous Field of View
ISLSCP        International Satellite Land Surface Climatology Project
Mbps          Megabyte per second
NESDIS        National Environmental Satellite Data and Information Service
NOAA          National Oceanic and Atmospheric Administration
ORNL          Oak Ridge National Laboratory
TDF           Table Definition File
UTM           Universal Transverse Mercator