1.  TITLE

1.1  Data Set Identification.

     Fifteen-minute Stream Flow Data from USGS.

1.2  FIS Data Base Table Name.

     STREAM_FLOW_15MIN_DATA.

1.3  CD-ROM File Name.

     \DATA\HYDROLGY\STRM_15M\Yyyyy\ydddgrid.S15

     Where yyyy are the four digits of the century and year (e.g., Y1987=1987).
     Note: capital letters indicate fixed values that appear on the CD-
     ROM exactly as shown here, lower case indicates characters (values) that 
     change for each path and file.

     The format used for the filenames is: ydddgrid.sfx, where grid is the
     four number code for the location within the FIFE site grid, y is the
     last digit of the year (e.g., 7=1987), and ddd is the day of the year
     (e.g., 061=sixty-first day of the year). The filename extension (.sfx),
     identifies the data set content for the file (see Section 8.2) and is 
     equal to .S15 for this data set.

1.4  Revision Date Of This Document.

     May 11, 1994.
 
     Warning:  This document has not been checked for technical or editorial
               accuracy by the FIFE Information Scientist. There may be 
               inconsistencies with other documents, technical or editorial 
               errors that were inadvertently introduced when the document was 
               compiled or references to preliminary data that were not 
               included on the final CD-ROM.

               Previous versions of this document have been reviewed by the 
               Principal Investigator, the person who transmitted the data to 
               FIS, a FIS staff member, or a FIFE scientist generally familiar 
               with the data.

                         2.  INVESTIGATOR(S)

2.1  Investigator(s) Name And Title.

     Staff Science.

2.2  Title Of Investigation.

     Staff Science Soil Moisture and Hydrology Data Acquisition Program.

2.3  Contacts (For Data Production Information).

      __________________________________________
     |              |         Contact 1         |
     |______________|___________________________|
     |2.3.1 Name    |Dr. Eric Wood              |
     |2.3.2 Address |Dept. of Civil Engineering |
     |              |Princeton University       |
     |      City/St.|Princeton, NJ.             |
     |      Zip Code|08544                      |
     |2.3.3 Tel.    |(609) 258-4675             |
     |2.3.4 Email   |efwood@pucc.princeton.edu  |
     |______________|___________________________|

2.4  Requested Form of Acknowledgment.

     The Fifteen-minute Stream Flow Rates from USGS were provided to the FIFE
     Information System staff courtesy of the U.S. Geological Survey,
     Water Resources Division, Lawrence, Kansas.

                              3.  INTRODUCTION

3.1  Objective/Purpose.

     The purpose of this data set was to provide accurate measurements of
     the stream flow from Kings Creek so that a water budget analysis for the 
     northwest quadrant of the FIFE study area could be performed.

3.2  Summary of Parameters.

     Water flow.

3.3  Discussion.

     This data set contains 15 minute stream flow data from the USGS station
     located 2.9 miles upstream from the mouth of Kings Creek. The record
     extends from April 1, 1979 through September 2, 1988.

                       4.  THEORY OF MEASUREMENTS

The stilling pipe installed at the USGS station operates on the principle
that the water level in a standpipe at a specific location within
a stream bed can be converted to a volume of water in the stream bed. The 
tracking of the change in stream height with time then enables the calculation 
of stream flow.

                            5.  EQUIPMENT

5.1  Instrument Description.

     The stilling well consisted of a vertical pipe connected to the stream by
     intake pipes. The well was placed in one side of the stream. A
     float was used to detect the height of the water within the well.

     An analog or digital recorder was used to track the stage height of the
     water in the stilling well. The analog recorder (strip-chart) produces a
     graphic record of the rise and fall of the water surface with time, while
     the battery-powered, paper-punch recorder is actuated by a cam on a
     battery-driven mechanical clock which punchs stage height every 15
     minutes. Both recorders run unattended for 60-90 days.

     A manual reference gauge was also used in Kings Creek to make direct
     measurements of stream height.

     5.1.1  Platform.

            The stilling pipe intake at the USGS station is built into the
            bottom of the stream bed.

     5.1.2  Mission Objectives.

            To measure the volume of stream flow.

     5.1.3  Key Parameters.

            Water flow rate.

     5.1.4  Principles of Operation.

            The water stage recorder measures height of the water surface above
            an established base plane for that stream. The stage is sensed by
            a float in a stilling well that is connected to the stream by
            intake pipes. The stilling well protects the float and dampens the
            fluctuation in the stream caused by wind and turbulence. The
            stilling well was placed on one side of the stream with the base
            of the well placed at the bottom of the stream and its top above
            the maximum recorded stage. The intake was designed to prevent lag
            during periods of rapid change in stage and to prevent velocity-
            head effects at its end.

            The height of the water in the still is converted to stream flow
            using a discharge rating which was determined for Kings Creek.
            This discharge rating may be a simple relation between stage and
            discharge or a more complex relation in which discharge is a
            function of stage, slope, rate of change of stage or other factors
            such as channel shape, debris, and vegetation in the stream bed.


     5.1.5  Instrument Measurement Geometry .

            Not available at this revision.


     5.1.6  Manufacturer of Instrument.

            Digital stage recorder: Fischer-Porter

            Analog stage recorder: Stevens A-35

            Stilling Well & Weir:   United States Geological Survey
                                    Manhattan, Kansas.

5.2  Calibration.
 
     Stage height in the stilling well is checked periodically when an engineer
     visits the gauge and at a minimum every (2-3 years). The stage height
     inside the still is compared with that of a direct, manual stage height
     measurement using a non-recording gauge.

     Discharge measurements were made to define the discharge rating for
     Kings Creek. The measurements were initially made at various stages
     (stream heights) to define the relation between stage and discharge.
     After the initial measurements, discharge measurements were made
     monthly to verify the stage-discharge relationship or to define any
     change in the relationship.

     The discharge measurements are normally made using a pygmy current meter.
     This meter is individually calibrated in the rating flume at the National
     Institute for Standards and Technology. Measurements with the current
     meter are made in a cross-section of the stream that is divided into
     20-30 partial sections. The area and mean velocity in each of these
     sections is determined separately. Indirect methods are used to
     determine peak flood discharges (see Carter and Davidian 1968
     for details).

     The stage-discharge relationship is not stable. Frequent measurement
     of stream discharge is required, especially when the features which
     control the discharge are not permanent and when various discharge
     measurements represent different positions of the stage-discharge curve.

     5.2.1  Specifications.

            Not available at this revision.

            5.2.1.1  Tolerance.

                     Accuracy of the stilling well is about + or - 0.3048
                     E-3 meters

     5.2.2  Frequency of Calibration.

            Discharge measurements are checked monthly.

            Stage height is checked when the station is visited by an engineer
            or at a minimum every 2-3 years.

     5.2.3  Other Calibration Information.

            Not available at this revision.

                          6.  PROCEDURE

6.1  Data Acquisition Methods.

     The stream flow station measurements were made in a stilling well located
     to the side of the open channel of Kings Creek. The data were recorded on
     to paper tape or a strip chart continuous recorder. It is not known which
     of these two standard USGS methods was used.

     These data were supplied to the FIFE Information System by Eric Wood who
     obtained them from the Lawrence, Kansas, District Office of USGS.

6.2  Spatial Characteristics.

     The FIFE study area, with areal extent of 15 km by 15 km, is located south 
     of the Tuttle Reservoir and Kansas River, and about 10 km from Manhattan, 
     Kansas, USA. The northwest corner of the area has UTM coordinates of 
     4,334,000 Northing and 705,000 Easting in UTM Zone 14.

     6.2.1  Spatial Coverage.

            Measurements were made at the USGS Kings Creek station (USGS ID
            number 06879650) located 2.9 miles from the mouth of Kings Creek.

            SITEGRID_ID  STATION_ID  STATION_NAME  NORTHING  EASTING
            -----------  ----------  ------------  --------  -------
            1715-STG     650         KINGS CREEK   4330650   707973

            LATITUDE  LONGITUDE
            --------  ---------
            39 06 07  -96 35 42

     6.2.2  Spatial Resolution.

            These are point data, however, they represent the total water flow 
            from the watershed upstream from the location of the stilling well.

6.3  Temporal Characteristics.

     6.3.1  Temporal Coverage.

            The USGS Kings Creek stream flow data covers the period of
            December 25, 1984 through March 3, 1988.

     6.3.2  Temporal Resolution.

            The USGS Kings Creek stream flow station data was recorded at
            15-minute intervals when there was a flow rate greater than
            2.837 E-4 [m^3][sec^-1].  When the flow rate was less, no data
            were reported until this rate was exceeded or 24 hours had elapsed.

                           7.  OBSERVATIONS

7.1  Field Notes.

     None available at this revision.

                         8.  DATA DESCRIPTION

8.1  Table Definition With Comments.

     The SQL definition for this table is found in the STRM_15M.TDF file
     found on FIFE CD-ROM Volume 1.

8.2  Type of Data.


--------------------------------------------------------------------------------
|                 8.2.1                  |               |          |          |
|Parameter/Variable Name                 |               |          |          |
--------------------------------------------------------------------------------
|    |               8.2.2               |     8.2.3     |  8.2.4   |  8.2.5   |
|    |Parameter/Variable Description     |Range          |Units     |Source    |
--------------------------------------------------------------------------------
|SITEGRID_ID                             |               |          |          |
|    |This is a FIS grid location code.  |               |          |FIS       |
|    |Site grid codes (SSEE-III) give    |               |          |          |
|    |the south (SS) and east (EE) cell  |               |          |          |
|    |number in a 100x100 array of 200m  |               |          |          |
|    |square cells.  The last 3          |               |          |          |
|    |characters (III) are an instrument |               |          |          |
|    |identifier.                        |               |          |          |
--------------------------------------------------------------------------------
|STATION_ID                              |               |          |          |
|    |The station ID designating the     |min = 650,     |          |FIS       |
|    |location of the observations.      |max = 650      |          |          |
--------------------------------------------------------------------------------
|OBS_DATE                                |               |          |          |
|    |The date of the observations.      |min = 25-DEC-84|          |USGS      |
|    |                                   |,              |          |          |
|    |                                   |max = 03-MAR-88|          |          |
--------------------------------------------------------------------------------
|START_TIME                              |               |          |          |
|    |The starting time of the           |min = 15,      |[GMT]     |USGS      |
|    |observations, converted from CST.  |max = 2400     |          |          |
--------------------------------------------------------------------------------
|END_TIME                                |               |          |          |
|    |The ending time of the             |min = 15,      |[GMT]     |USGS      |
|    |observations, converted from CST.  |max = 2400     |          |          |
--------------------------------------------------------------------------------
|AVG_FLOW                                |               |          |          |
|    |The stream flow rate between the   |min = 0,       |[meters^3]|USGS      |
|    |times listed in START_TIME and     |max = 10.2507  |[sec^-1]  |          |
|    |END_TIME.                          |               |          |          |
--------------------------------------------------------------------------------
|FIFE_DATA_CRTFCN_CODE                   |      *        |          |          |
|    |The FIFE Certification Code for    |CPI=checked by |          |FIS       |
|    |the data, in the following format: |principal inves|          |          |
|    |CPI (Certified by PI), CPI-???     |tigator,       |          |          |
|    |(CPI - questionable data).         |CPI-MRG=merged |          |          |
|    |                                   |data,          |          |          |
|    |                                   |CPI-???= CPI-qu|          |          |
|    |                                   |estionable data|          |          |
--------------------------------------------------------------------------------
|LAST_REVISION_DATE                      |               |          |          |
|    |The last revision date for the     |min = 29-SEP-89|          |FIS       |
|    |data, in the format (DD-MMM-YY).   |,              |          |          |
|    |                                   |max = 29-SEP-89|          |          |
--------------------------------------------------------------------------------

Footnote:

        * Decode the FIFE_DATA_CRTFCN_CODE field as follows:

          The primary certification codes are:

          EXM - Example or Test data (not for release)
          PRE - Preliminary (unchecked, use at your own risk)
          CPI - Checked by Principal Investigator (reviewed for quality)
          CGR - Checked by a group and reconciled (data comparisons and
                cross checks)

          The certification code modifiers are:

          PRE-NFP  - Preliminary - Not for publication, at the request of
                     investigator.
          CPI-MRG  - PAMS data which is "merged" from two separate receiving
                     stations to eliminate transmission errors.
          CPI-???  - Investigator thinks data item may be questionable.

8.3  Sample Data Base Data Record.

     SITEGRID_ID STATION_ID OBS_DATE  START_TIME END_TIME  AVG_FLOW
     ----------- ---------- --------- ---------- -------- ---------
     1715-STG           650 25-DEC-84        615     2400    .00000
     1715-STG           650 26-DEC-84         15     2400    .00000
     1715-STG           650 27-DEC-84         15     2400    .00000
     1715-STG           650 28-DEC-84         15      815    .03400

     FIFE_DATA_CRTFCN_CODE LAST_REVISION_DATE
     --------------------- ------------------
     CPI                   29-SEP-89
     CPI                   29-SEP-89
     CPI                   29-SEP-89
     CPI                   29-SEP-89

8.4  Data Format.

     The CD-ROM file format consists of numerical and character fields of 
     varying length separated by commas. The character fields are enclosed with 
     a single apostrophe. There are no spaces between the fields.  Each file 
     begins with five header records.  Header records contain the following 
     information:

     Record 1    Name of this file, its table name, number of records in
                 this file, path and name of the document that describes 
                 the data in this file, and name of principal investigator 
                 for these data.
     Record 2    Path and filename of the previous data set, and path and 
                 filename of the next data set.  (Path and filenames for files 
                 that contain another set of data taken at the same site on 
                 the same day.)
     Record 3    Path and filename of the previous site, and path and filename 
                 of the next site.  (Path and filenames for files of the same 
                 data set taken on the same day for the previous and next 
                 sites (sequentially numbered by SITEGRID_ID)).
     Record 4    Path and filename of the previous date, and path and filename 
                 of the next date.  (Path and filenames for files of the same 
                 data set taken at the same site for the previous and next 
                 date.)
     Record 5    Column names for the data within the file, delimited by 
                 commas.
     Record 6    Data records begin.

     Each field represents one of the attributes listed in the chart in 
     Section 8.2 and described in detail in the TDF file (see Section 8.1). 
     These fields are in the same order as in the chart.

8.5  Related Data Sets.

     Storm Event Stream Flow.
     Daily Stream Flow Amounts.

                         9.  DATA MANIPULATIONS

9.1  Formulas.

     9.1.1  Derivation Techniques/Algorithms.

            Section Discharge = (Mean Velocity) x (depth at vertical) x 
                                (sum 1/2 distance to adjacent vertical)

            Total Stream Discharge = Sum of Section Discharges for the stream.

            The equation used to relate stream stage to discharge is not known.

9.2  Data Processing Sequence.

     9.2.1  Processing Steps and Data Sets.

            The processing steps for these data depend upon whether the data is
            written to a strip-chart recorder or to paper tape. Since it is
            not known which was used at the Kings Creek station both
            will be described here. If the stage height is recorded on a
            strip-chart all computations are performed manually in the
            following order:

                1)  Determination and application of gauge height and time
                    corrections to the gauge height chart.
                2)  Computation of the mean gauge height for each 15 minute
                    interval point.
                3)  Computation of discharge for each period from mean values 
                    of stage and discharge rating, including any strip chart 
                    corrections.
                4)  Computation of peak values of gauge height and discharge.

            If the stage height is recorded to paper tape the data is read from
            the paper tape by a paper tape reader attached to a computer. The
            discharge is then computed using these data, the stage-discharge
            rating, the list of any corrections to the basic discharge rating,
            and a list of corrections to the data.

     9.2.2  Processing Changes.

            None.

9.3  Calculations.

     9.3.1  Special Corrections/Adjustments.

            None known at this revision.

9.4  Graphs and Plots.

     None.

                          10.  ERRORS

10.1  Sources of Error.

      Errors originate from the instability of the relationship between stage
      height and discharge. This relationship varies temporally. It is
      affected by changes in the stream bed which result from the flow of
      water over the bed, such as scour and fill, aquatic growth, ice,
      debris, or bed roughness.

      The intakes to the stilling well can become plugged with debris or
      overgrown with plant or animal material, and the float can malfunction.

10.2  Quality Assessment.

      10.2.1  Data Validation by Source.

              The discharge curves are routinely checked for accuracy. The
              stage height within the stilling well is routinely checked
              against that measured using a manual gauge.

      10.2.2  Confidence Level/Accuracy Judgment.

              The overall accuracy of these data for each year is as listed
              below:

                     Year              Accuracy Judgment
                    --------         ----------------------
                    1984                     Good
                    1985                     Good
                    1986                     Good
                    1987                 Not available
                    1988                     Good

      10.2.3  Measurement Error for Parameters and Variables.

              Records for 1984, 1985, 1986 and 1988 are within 5% of the
              reported daily discharges. The error rate for 1987 is unknown.

      10.2.4  Additional Quality Assessment Applied.

              FIS staff applied a general Quality Assessment (QA) procedure to
              the data to identify inconsistencies and problems for potential
              users. As a general procedure, the FIS QA consisted of examining
              the maximum, minimum, average, and standard deviation for each
              numerical field in the data table. An attempt was made to find an
              explanation for unexpected high or low values, values outside of
              the normal physical range for a variable, or standard deviations
              that appeared inconsistent with the mean. In some cases, histog-
              rams were examined to determine whether outliers were consistent
              with the shape of the data distribution.

              The discrepancies, which were identified, are reported as
              problems in Section 11.1.

                                  11.  NOTES

11.1  Known Problems With The Data.

      The mean flow values for July 6, 1987 through July 11, 1987 are
      questionable. An independent comparison of the data here and these
      same data acquired directly from USGS by another group shows a
      discrepancy between the mean flow values for these dates. The data
      here shows a mean flow of zero for these dates while the same USGS
      data set acquired by the second group shows the mean flow rates for
      these dates to be .08211 [m^3][sec^-1] for July 6, 1987 and to range
      from .05390 to .05958 [m^3][sec^-1] for July 10, 1987. The USGS
      regional office in Lawrence, Kansas, should be contacted if you wish
      to resolve this discrepancy.

      Unusually high mean flow values were recorded on the days,
      listed below:

                                                       Mean Flow
                     Date        Description         [m^3][sec^-1]
               --------------    ------------       ---------------
               April 27, 1985     5 values         greater than 6.0
               June 22, 1985      3 values         greater than 6.0
               October 9, 1985    3 values         greater than 6.0
               May 17, 1986       3 values         greater than 6.0
               October 4, 1986    3 values         greater than 6.0
               April 14, 1987     3 values         greater than 6.0

11.2  Usage Guidance.

      None available at this revision.

11.3  Other Relevant Information.

      None.

                           12.  REFERENCES

12.1  Satellite/Instrument/Data Processing Documentation.

      Beven, K.J. 1986. Hillslope runoff processes and flood frequency
         characteristics. In: Hillslope Processes. A.D. Abrahams (ed.). George
         Allen and Unwin.
      Anonymous. 1980. U.S Geological Survey Water-Data Report KS-79-1 Through 
         KS-89-1. Water Resources Data Kansas. Water Year 1979-. Prepared in 
         cooperation with the State of Kansas and with other agencies.
      Carter, R.W., and J. Davidian. 1968.  Techniques of Water-Resources
         Investigations of the United States Geological Survey.  Book 3:
         Applications of Hydraulics. Chapter A6: General Procedure for Gaging
         Streams. 13 pgs.

12.2  Journal Articles and Study Reports.

      Wood, E.F. 1990. Water balance model for Kings Creek. AMS Symposium on 
         the First ISLSCP Field Experiment (FIFE). Anaheim, California. p 163-
         167.
      Wood, E.F., M. Sivapalan, K.J. Beven, and L. Band. 1989. Effects of
         spatial variability and scale with implications to hydrologic 
         modeling. J. Hydrol. 102:29-47.
      Sivapalan, M., K.J. Beven, and E.F. Wood. 1987. On hydrological similar-
         ity: 2. A scaled model of storm runoff production. Water Resources 
         Res. 23:2266-2278.
      Famiglietti, J.S., E.F. Wood, M. Sivapalan, and D.J. Thongs. 1992. A
         catchment Scale Water Balance for FIFE. J. Geophysical Res.
      Famiglietti, J.S. 1991. Aggregation and scaling of spatially-variable
         hydrological processes: local, catchment-scale and macroscale models
         of water and energy balance. PhD Dissertation. Dept. of Civil
         Engineering. Princeton University. Princeton, NJ.

12.3  Archive/DBMS Usage Documentation. 

      The Collected Data of the First ISLSCP Field Experiment is archived at
      the EOS Distributed Active Archive Center (DAAC) at Oak Ridge National
      Laboratory (ORNL), Oak Ridge, Tennessee (Section 13 below).  
      Documentation about using the archive and/or online access to the data 
      at the ORNL DAAC is not available at this revision.

                             13.  DATA ACCESS

13.1  Contacts for Archive/Data Access Information. 

      ORNL DAAC User Services
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      (615) 241-3952

13.2  Archive Identification. 

      EOSDIS Distributed Active Archive Center
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      USA

      Telephone:       (615) 241-3952
      FAX:             (615) 574-4665
      Internet Email:   ornldaac@onrl.gov

13.3  Procedures for Obtaining Data.

      Users may place requests by letter, telephone, electronic mail, FAX, or 
      personal visit. 

13.4  ORNL DAAC Status/Plans. 

      FIFE data will be available from the ORNL DAAC. Please contact the 
      ORNL DAAC User Services Office for the most current information about 
      these data.

                 14.  OUTPUT PRODUCTS AND AVAILABILITY

14.1  Tape Products.

      None.

14.2  Film Products.

      None.

14.3  Other Products.

      The Daily Stream Flow Amounts are available on FIFE CD-ROM Volume 1.

                        15.  GLOSSARY OF ACRONYMS

CD-ROM            Compact Disk-Read Only Memory
DAAC              Distributed Active Archive Center
EOSDIS            Earth Observing System Data and Information System
FIFE              First ISLSCP Field Experiment
FIS               FIFE Information System
ISLSCP            International Satellite Land Surface Climatology Project
ORNL              Oak Ridge National Laboratory
USGS              United States Geological Survey
UTM               Universal Transverse Mercator