1.  TITLE

1.1  Data Set Identification.

     Optical Thickness Calibration.

1.2  FIS Data Base Table Name.

     OPTICAL_THICK_CALIB_REF.

1.3  CD-ROM File Name. 

     \DATA\OPTCAL\OT_CALIB\ydddMULT.OT

     Note: capital letters indicate fixed values that appear on the CD-ROM 
     exactly as shown here, lowercase indicates characters (values) that 
     change for each path and file.

     The format used for the filenames is: ydddMULT.sfx, where y is the 
     last digit of the year (e.g., 7=1987, and 9=1989), and ddd is the day of 
     the year (e.g., 061=sixty-first day in the year).  The filename 
     extension (.sfx), identifies the data set content for the file (see 
     Section 8.2) and is equal to .OT for this data set. 

1.4  Revision Date Of This Document.

     May 10, 1994.

     Warning:  This document has not been checked for technical or editorial
               accuracy by the FIFE Information Scientist. There may be 
               inconsistencies with other documents, technical or editorial 
               errors that were inadvertently introduced when the document was 
               compiled or references to preliminary data that were not 
               included on the final CD-ROM.

               Previous versions of this document have been reviewed by the 
               Principal Investigator, the person who transmitted the data to 
               FIS, a FIS staff member, or a FIFE scientist generally familiar 
               with the data.

                            2.  INVESTIGATOR(S)

2.1  Investigator(s) Name And Title.

     Dr. Carol J. Bruegge
     Jet Propulsion Laboratory

     Dr. Rangasayi N. Halthore
     NASA Goddard Space Flight Center/Hughes STX Corp.

     Mr. Brian L. Markham
     NASA Goddard Space Flight Center     

     Dr. Michael A. Spanner
     NASA Ames Research Center

2.2  Title Of Investigation.

     Aerosol Optical Thickness Calibration. 

2.3  Contacts (For Data Production Information).

 ____________________________________________________________________________
|              |     Contact 1      |      Contact 2      |     Contact 3    |
|______________|____________________|_____________________|__________________|
|2.3.1 Name    |Dr. R.N. Halthore   |Dr. C.J. Bruegge     |Dr. M.A. Spanner  |
|2.3.2 Address |Code 923            |Mail Stop 169-237    |MS 242-4          |
|              |NASA/GSFC           |Jet Propulsion Lab.  |NASA/Ames Res. Ctr|
|      City/St.|Greenbelt, MD       |Pasadena, CA         |Moffett Field     |
|      Zip Code|20771               |91109                |CA 94035          |
|2.3.3 Tel.    |(301) 286-1094      |(818) 354-4956       |(415) 604-3620    |
|2.3.4 Email   |halthore@ltpsun.gsfc|cjb@scn1.jpl.nasa.gov|spanner@eco.arc   |
|              |.nasa.gov           |                     |.nasa.gov         |
|______________|____________________|_____________________|__________________|

2.4  Requested Form of Acknowledgment.

     The Optical Thickness Calibration data were obtained by C.J. Bruegge, 
     R.N. Halthore, B.L. Markham, and M.A. Spanner.

                               3.  INTRODUCTION

3.1  Objective/Purpose.

     During the 1989 field campaign for FIFE there were three independent 
     groups measuring atmospheric transmission, in particular, the 
     aerosol optical thickness, using at least three different instruments 
     and three different analysis procedures. The objective of this study 
     was to collocate the instruments in space and time so that a comparison 
     could be made of the aerosol optical thickness derived by the three 
     groups.

3.2  Summary of Parameters.

     Rayleigh, aerosol, ozone, and total optical thickness.

3.3  Discussion.

     These data enable the intercalibration of the sunphotometers used in 1989 
     and therefore, the direct comparison of the data collected by these 
     instruments. Measurements were taken with three instruments (Solar 
     transmissometer SXM-2, Reagan sunphotometer, and Airborne Tracking 
     Sunphotometer) positioned side by side on August 4, 1989. Only the 
     SMX-2 and Reagan sunphotometer were used for measurements on 
     August 6, 1989. Optical thickness was measured with each of the 
     instruments. 
     
     Bruegge et al. (1992a) reported on the comparison study involving data 
     acquired in the early afternoon of August 4, 1989 using the Reagan, 
     SXM-2, and Airborne Tracking Sunphotometers (ATSP) at Manhattan Airport.  
     When the data at 440 nm were compared for a 1-hour period, the 
     aerosol optical depth was found to drop by about 0.01.  All instruments 
     followed the same temporal profile during periods of simultaneous 
     measurements.  Generally, the data were in agreement to within 0.005.

                          4.  THEORY OF MEASUREMENTS

Sunphotometers or solar transmissometers have long been used to measure 
atmospheric transmission. The basic idea is that since for time scales in order
of a day, solar radiance I_o outside the atmosphere is a constant in narrow 
bands (approx. 10 nm) in the visible and near-infrared wavelengths, changes in 
radiance I measured at the ground by the sunphotometer are the result of 
changes in atmospheric radiance, and more importantly, transmission. Thus, 
applying Bouger's law of attenuation,

    I = (I_o/r^2) * exp(-(m*tau)_R -(m*tau)_oz -(m*tau)_aer)             (1)

where 

     I_o = solar radiance at one AU in a given band (the underscore refers 
           to a subscript and a '^' refers to a superscript), 
       r = Earth-Sun distance at the time of observation in Astronomical 
           Units (AU), 
       m = airmass of observation, 
     tau = optical thickness, and 
       R = Rayleigh scattering as cause of attenuation
      oz = ozone absorption as cause of attenuation
     aer = aerosol absorption and scattering as cause of attenuation 

Note: water vapor is not included in this analysis, which refers to channels 
that avoid water bands. If the sunphotometer responds with a voltage V for an 
incident radiance I as in I = KV, where K is a constant, thus implying 
linearity in the instrument response, equation (1) becomes, after some 
manipulation, 

     (m*tau)_aer = -lnV - (m*tau)_oz - (m*tau)_R + ln(V_o/r^2).           (2)

For a measurement of voltage V at a known airmass of m (= sec(theta), approx- 
imately where theta is the solar zenith angle), all the terms on the right-hand 
side of equation (2) are known, and therefore, aerosol optical thickness can be 
estimated. Note that V_o is the calibration coefficient to be discussed in 
Section 5.2, and Rayleigh and ozone optical thickness are calculated thus:

     tau_R = (P/P_o) * (0.008569*Lambda^(-4)*
             (1 + 0.0113*Lambda^-2 + 0.00013*Lambda^-4)).                 (3)

with p as the measured surface pressure and P_o is the sea level pressure of 
1.013 bars. The wavelength of observation lambda is in micrometers or microns. 
Ozone optical thickness is estimated by multiplying the ozone column abundance 
in Dobson units (DU or matm-cm) obtained from climatological charts (i.e., the 
standard relation between ozone abundance, latitude and time of year) by the 
absorption coefficient tabulated below:

                     ________________________________
                     Wavelength     Ozone Absorption
                        (nm)         Coefficient in
                                    [matm^-1][cm^-1]
                     ________________________________
                      441               3.36E-6
                      522               4.8E-5
                      557               9.73E-5
                      613               1.19E-5
                      671               4.55E-5
                      781               4.61E-6
                      872               6.17E-7
                     1030               0.0
                    _________________________________

For a description of the theory involved in water column abundance measurements
in channels that include the 940 nm water vapor band, the reader should consult 
Bruegge et al. (1992b).            
    
                                5.  EQUIPMENT

5.1  Instrument Description. 

     The SXM-2 (Solar transmissometer), Reagan, and Airborne Tracking
     Sunphotometers (ATSP) used to collect the original data from which 
     this data set was produced have been described in detail in the 
     Transmissometer Aerosol Optical Thickness, the NIPS and Reagan 
     Sunphotometer Optical Thickness, and the Sunphotometer Optical Thickness 
     Data from C130 Aircraft documents found on FIFE CD-ROM Volume 1.  The 
     three principal investigators, R.N. Halthore, C.J. Bruegge, and 
     M.A. Spanner, used the SXM-2, Reagan, and ATSP, respectively, for 
     these measurements.

     5.1.1  Platform.

            SXM-2 and Reagan sunphotometers were located on the ground, while
            the ATSP was in its usual location atop the C-130 aircraft parked
            nearby.

     5.1.2  Mission Objectives. 

            The objective was to compare the measured aerosol or total optical 
            thickness as measured by different groups.

     5.1.3  Key Parameters. 

            Aerosol optical thickness, pressure, total optical thickness,
            and optical thickness due to ozone absorption.

     5.1.4  Principles of Operation. 

            Sunphotometers used in this study typically employ a 
            silicon photodiode detector, which may be temperature controlled. A 
            filter wheel having 6 - 10 bands throughout the visible and near-IR
            at preselected wavelengths that usually avoid water band
            absorption. Sometimes bands are specifically chosen to include
            water absorption to monitor water column abundance.

     5.1.5  Instrument Measurement Geometry. 

            Sunphotometers are designed to measure solar radiance at the ground
            surface, in a narrow viewing angle as determined by a baffled long
            tube. The narrow viewing angle, typically 1-2 degrees field of view 
            ensures full coverage of the solar disk, while eliminating much of
            the sky radiance.

     5.1.6  Manufacturer of Instrument. 

            See the documents listed in Section 5.1.

5.2  Calibration. 

     Equation (2) in Section 4 can be written as

         lnV + (m*tau)_oz + (m*tau)_R = ln(V_o/R^2) -tau_aer*m_aer.  (4)

     In the above equation, the terms on the left-hand side can be 
     plotted against m_aer, the aerosol airmass. If the aerosol optical 
     thickness does not change during portions of the day when the airmass 
     is changing the most (sunrise and sunset), such a plot would yield a 
     straight line whose y-intercept would be a function of the required 
     calibration coefficient:

         ln(V_o/R^2), and whose slope is -tau_aer.

     This is known as the Langley plot method of calibration. The requirement 
     that tau_aer not change during measurements is most easily met at mountain 
     sites, which are above the boundary layer and in the morning when convect-
     ive motions have had not enough time set in. For a further discussion, see
     Halthore and Markham (1992).

     In 1987 and 1989, all of the sunphotometers were calibrated using the 
     Langley plot method (or a minor variant on the theme). The present effort,
     however, was conducted to perform another method of calibration -- the 
     intercomparison method. In this method, if there are two instruments 
     (e.g., 1 and 2) of identical bands, situated side by side and measuring 
     the aerosol optical thickness at the same time, the calibration 
     coefficient of one of the instruments (e.g., 2) can be computed from 
     equation (2) as:

         (V_o)_2 = (V_o)_1 * (V_2/V_1)                             (5)

     Where the subscripts _1 and _2 refer to the instruments 1 and 2 
     respectively. Instrument 1 is the reference instrument in this case. 
     If the bands do not overlap, appropriate extrapolation/interpolation 
     in wavelength for the optical thickness must be done and with the help 
     of equation (2), V_o is determined.

     The advantage of having three instruments is obvious. Aerosol 
     optical thickness derived from three independent calibrations can be 
     compared to have the following outcomes:

     1.  All three values agree. No correction for calibration is 
         required.

     2.  Two values agree. The third instrument's calibration is 
         adjusted to make its aerosol optical thickness agree with the other 
         two.

     3.  None of the values agree. There is no positive outcome. 
         Further intercomparisons with other instruments better calibrated than 
         the three used here must be done to resolve the differences.

     In the data reported here, it can be seen that the aerosol optical 
     thickness derived from the three instruments agreed to within the 
     uncertainties of any one instrument.

     5.2.1  Specifications. 

            Not available at this revision.

            5.2.1.1  Tolerance. 

                     Not available at this revision.
        
     5.2.2  Frequency of Calibration. 

            The Langley plot method of calibration was performed at 
            mountain sites before and after the 1989 IFC. Calibration check
            using the intercomparison method was done once during the 1989 IFC.

     5.2.3  Other Calibration Information. 

            None.

                            6.  PROCEDURE 

6.1  Data Acquisition Methods. 

     Optical thickness data were collected simultaneously by the SXM-2, Reagan,
     and ATSP sunphotometers at the same site and times during the 1989 IFC.
     Surface pressure was measured with a high-accuracy barometer made 
     by Atmospheric Instrumentation Research, Inc.

6.2  Spatial Characteristics. 

     The FIFE study area, with areal extent of 15 km by 15 km, is located south 
     of the Tuttle Reservoir and Kansas River, and about 10 km from Manhattan, 
     Kansas, USA. The northwest corner of the area has UTM coordinates of 
     4,334,000 Northing and 705,000 Easting in UTM Zone 14.

     6.2.1  Spatial Coverage.

            All the data were acquired at a single location in Manhattan 
            airport near the tarmac where the C130 aircraft was parked. 
            The sitegrid is XMH2-SPS with coordinates as follows:

            LATITUDE     LONGITUDE
            --------     ---------
            39 13 00     -96 67 00

     6.2.2  Spatial Resolution.

            This is point data.  However, the data represent the optical 
            thickness for distances of about 0.5 km from the instrument 
            collecting the data. 

6.3  Temporal Characteristics.

     6.3.1  Temporal Coverage

            Data were collected on 2 days during the IFC. Measurements were 
            made by all three investigators on August 4, 1989, but only two of
            the investigators collected data on August 6, 1989. Below are the 
            dates, times, and investigators for the measurements:

            Investigators                Date      
            -------------                --------  
            Halthore, Bruegge, Spanner   AUG-04-89  
            Halthore, Bruegge            AUG-06-89   


     6.3.2  Temporal Resolution.

            The spectra were taken by Spanner every minute on August 4, 
            by Bruegge about every minute on the August 4 and 6 August, 
            and by Halthore every minute on the August 4 , and three 
            measurements on the August 6. There are 10 spectra on 
            August 4 between 1843 and 1852 GMT which coincide in time for 
            all three instruments.

                               7.  OBSERVATIONS
7.1  Field Notes.

     None.

                            8.  DATA DESCRIPTION

8.1  Table Definition With Comments. 

     The SQL definition for this table is found in the OT_CALIB.TDF file 
     found on the CD-ROM Volume 1.

8.2  Type of Data.

--------------------------------------------------------------------------------
|                 8.2.1                  |               |          |          |
|Parameter/Variable Name                 |               |          |          |
--------------------------------------------------------------------------------
|    |               8.2.2               |     8.2.3     |  8.2.4   |  8.2.5   |
|    |Parameter/Variable Description     |Range          |Units     |Source    |
--------------------------------------------------------------------------------
|SITEGRID_ID                             |               |          |          |
|    |This is a FIS grid location code.  |               |          |          |
|    |Site grid codes (SSEE-III) give    |               |          |          |
|    |the south (SS) and the east (EE)   |               |          |          |
|    |cell number in a 100x100 array of  |               |          |          |
|    |200m square cells.  The last 3     |               |          |          |
|    |characters (III) are an instrument |               |          |          |
--------------------------------------------------------------------------------
|STATION_ID                              |               |          |          |
|    |The station ID designating the     |               |          |          |
|    |location of the observations.      |               |          |          |
--------------------------------------------------------------------------------
|OBS_DATE                                |               |          |          |
|    |The date of the observations, in   |               |          |          |
|    |the format (DD-MMM-YY).            |               |          |          |
--------------------------------------------------------------------------------
|OBS_TIME                                |               |          |          |
|    |The time that the observation was  |               |[GMT]     |          |
|    |taken, in GMT.  The format is HHMM.|               |          |          |
--------------------------------------------------------------------------------
|INSTR_ID                                |               |          |          |
|    |The code name for the instrument   |               |          |          |
|    |used to make the observations.     |               |          |          |
--------------------------------------------------------------------------------
|SURFACE_PRESS                           |               |          |          |
|    |The surface pressure at the time   |               |[millibars|          |
|    |of the observation.                |               |]         |          |
--------------------------------------------------------------------------------
|SURFACE_TEMP                            |               |          |          |
|    |The surface temperature during     |               |[degrees C|          |
|    |the observation.                   |               |elsius]   |          |
--------------------------------------------------------------------------------
|SOLAR_ZEN_ANG                           |               |          |          |
|    |The Solar Zenith Angle for this    |               |[degrees] |          |
|    |observation.                       |               |          |          |
--------------------------------------------------------------------------------
|WAVLEN                                  |               |          |          |
|    |The wavelength at which the        |               |[nm]      |          |
|    |observation was made.              |               |          |          |
--------------------------------------------------------------------------------
|OZONE_OPTCL_THICK                       |               |          |          |
|    |The Ozone Optical Thickness of     |               |          |          |
|    |the atmosphere due to Ozone        |               |          |          |
|    |molecules in the air.              |               |          |          |
--------------------------------------------------------------------------------
|RAYLEIGH_OPTCL_THICK                    |               |          |          |
|    |The Rayleigh Optical Thickness,    |               |          |          |
|    |caused by molecular scattering.    |               |          |          |
--------------------------------------------------------------------------------
|AEROSOL_OPTCL_THICK                     |               |          |          |
|    |The Aerosol Optical Thickness, of  |               |          |          |
|    |colloidal particles suspended in   |               |          |          |
|    |the atmospheric column.            |               |          |          |
--------------------------------------------------------------------------------
|TOTAL_OPTCL_THICK                       |               |          |          |
|    |The Total Optical Thickness, on a  |               |          |          |
|    |vertical path from surface to      |               |          |          |
|    |space.                             |               |          |          |
--------------------------------------------------------------------------------
|MIE_CONSTANT_1                          |               |          |          |
|    |MIE_1 and MIE_2 are used to        |               |          |          |
|    |compute AEROSOL_OPTCL_THICK at     |               |          |          |
|    |arbitrary wavelengths.             |               |          |          |
--------------------------------------------------------------------------------
|MIE_CONSTANT_2                          |               |          |          |
|    |MIE_1 and MIE_2 are used to        |               |          |          |
|    |compute AEROSOL_OPTICAL_THICK at   |               |          |          |
|    |arbitrary wavelengths.             |               |          |          |
--------------------------------------------------------------------------------
|ABUNDANCE_OF_OZONE                      |               |          |          |
|    |The column abundance of ozone, at  |               |          |          |
|    |standard temperature and pressure. |               |          |          |
--------------------------------------------------------------------------------
|WEATHER                                 |               |          |          |
|    |A comment on the weather           |               |          |          |
|    |conditions at the time of the      |               |          |          |
|    |observation.                       |               |          |          |
--------------------------------------------------------------------------------
|FIFE_DATA_CRTFCN_CODE                   |               |          |          |
|    |The FIFE Certification Code for    |       *       |          |          |
|    |the data, in the following format: |               |          |          |
|    |CPI (Certified by PI), CPI-???     |               |          |          |
|    |(CPI - questionable data).         |               |          |          |
--------------------------------------------------------------------------------
|LAST_REVISION_DATE                      |               |          |          |
|    |The last revision date for the     |               |          |          |
|    |data, in the format (DD-MMM-YY).   |               |          |          |
--------------------------------------------------------------------------------

Footnote:

      * Valid levels

      The primary certification codes are:

      EXM - Example or Test data (not for release).
      PRE - Preliminary (unchecked, use at your own risk).
      CPI - Checked by Principal Investigator (reviewed for quality).
      CGR - Checked by a group and reconciled (data comparisons and 
            cross-checks).

      The certification code modifiers are:

      PRE-NFP  - Preliminary - Not for publication, at the request of 
                 investigator.
      CPI-MRG  - PAMS data that are "merged" from two separate receiving 
                 stations to eliminate transmission errors.
      CPI-???  - Investigator thinks data item may be questionable.
 
8.3  Sample Data Record.

     SITEGRID_ID STATION_ID OBS_DATE   OBS_TIME INSTR_ID SURFACE_PRESS
     ----------- ---------- ---------- -------- -------- -------------
     XMH2-SPH           417 04-AUG-89      1841 SMX-2           963.60
     XMH2-SPH           417 04-AUG-89      1841 SMX-2           963.60
     XMH2-SPH           417 04-AUG-89      1841 SMX-2           963.60
     XMH2-SPH           417 04-AUG-89      1841 SMX-2           963.60
     
     SURFACE_TEMP SOLAR_ZEN_ANG  WAVLEN OZONE_OPTCL_THICK RAYLEIGH_OPTCL_THICK
     ------------ ------------- ------- ----------------- --------------------
                                  440.0
                                  552.0
                                  557.0
                                  612.0
     
     AEROSOL_OPTCL_THICK TOTAL_OPTCL_THICK MIE_CONSTANT_1 MIE_CONSTANT_2
     ------------------- ----------------- -------------- --------------
                   .1580
                   .1340
                   .1170
                   .1020
     
     ABUNDANCE_OF_OZONE WEATHER                        FIFE_DATA_CRTFCN_CODE
     ------------------ ------------------------------ ---------------------
                 300.00                                CPI
                 300.00                                CPI
                 300.00                                CPI
                 300.00                                CPI
     
     LAST_REVISION_DATE
     ------------------
     14-JUL-93
     14-JUL-93
     14-JUL-93
     14-JUL-93

8.4  Data Format.

     The CD-ROM file format consists of numerical and character fields of 
     varying length separated by commas. The character fields are enclosed with 
     a single apostrophe. There are no spaces between the fields.  Each file 
     begins with five header records.  Header records contain the following 
     information:

     Record 1    Name of this file, its table name, number of records in
                 this file, path and name of the document that describes 
                 the data in this file, and name of principal investigator 
                 for these data.
     Record 2    Path and filename of the previous data set, and path and 
                 filename of the next data set.  (Path and filenames for files 
                 that contain another set of data taken at the same site on 
                 the same day.)
     Record 3    Path and filename of the previous site, and path and filename 
                 of the next site.  (Path and filenames for files of the same 
                 data set taken on the same day for the previous and next 
                 sites (sequentially numbered by SITEGRID_ID)).
     Record 4    Path and filename of the previous date, and path and filename 
                 of the next date.  (Path and filenames for files of the same 
                 data set taken at the same site for the previous and next 
                 date.)
     Record 5    Column names for the data within the file, delimited by 
                 commas.
     Record 6    Data records begin.

     Each field represents one of the attributes listed in the chart in 
     section 8.2 and described in detail in the TDF file (see section 8.1). 
     These fields are in the same order as in the chart.

8.5  Related Data Sets.

     Sunphotometer Optical Thickness Data from C130 Aircraft.
     Solar Transmissometer Aerosol Optical Thickness.
     NIPS and Reagan Sunphotometer Optical Thickness.
     Aerosol Optical Thickness from GSFC.

                           9.  DATA MANIPULATIONS

9.1  Formulas.

     9.1.1  Derivation Techniques/Algorithms.

            The voltage response of the instrument V to a radiance L at the 
            ground can be written as a function of the exoatmospheric solar 
            radiance response V_o through the Bouger's Law:

                V = (V_o/R^2)*e^(-m*tau)

            where,
                tau = the total optical thickness
                  m = the air mass

            If changes in tau are negligible during an air mass change, such as
            during mornings at a mountain site, a plot of ln V versus m gives 
            as the y-intercept the required exoatmospheric radiance response 
            ln V_o. The latter is the well-known Langley plot method of 
            calibration. 

            The aerosol optical thickness derived from a voltage measurement 
            using the above equation is compared for each instrument. Of the 
            three instruments, if data from two agreed and the other did not, 
            the latter could be calibrated using:

                V_o = (V*R^2)*e^(m*tau)

            where all the quantities on the right-hand side of the equation are
            known and tau is derived from the other instruments. This is the 
            intercomparison method. If none of the instruments agreed, then, 
            aerosol optical thickness derived from the most reliable 
            instrument/calibration is used to calibrate the other two.  In 
            the data set presented here, the derived aerosol optical thickness 
            values all agreed to within the uncertainties of the measurements 
            (see Section 10.2.2).

9.2  Data Processing Sequence.

     9.2.1  Processing Steps and Data Sets.

            Morning data runs were used to produce Langley plots.

     9.2.2  Processing Changes.

            None.

9.3  Calculations.

     9.3.1  Special Corrections/Adjustments.

            None.

9.4  Graphs and Plots.

     None.

                                 10.  ERRORS

10.1  Sources of Error.

      Errors can arise during measurement or calibration.  During 
      calibration, a requirement of the Langley plot method is that
      the atmospheric optical thickness remains constant during the period
      of maximum airmass change. At mountain sites, this requirement is 
      usually met on clear days, but not always. The effect of varying 
      atmospheric conditions is reflected in the quality of the Langley
      plots (see Halthore and Markham, 1992). The calibration coefficient,
      which is the y-intercept in Langley plots, can be obtained to a 
      consistency better than 1% and we take this as the uncertainty in
      our measurements. A 1% uncertainty in V_o translates to an uncertainty
      in the aerosol optical thickness of 0.01 at airmass of 1. The 
      equation is:

          Delta(tau_aerosol) = (1/m)((Delta V_o)/V_o).

      Uncertainties in the Rayleigh optical thickness and ozone optical
      thickness are negligible for the conditions encountered in FIFE.

      For sunphotometers that do not employ constant temperature 
      detectors, a major source of variation and hence uncertainty
      arises due to inadequate temperature compensation for the response.
      Furthermore, for sunphotometer that do not employ auto-tracking
      or peak hold features, another major source of uncertainty
      arises due to imperfect pointing. For measurements reported here,
      these are not expected to contribute to absolute errors in
      the measurements of aerosol optical thickness.

10.2  Quality Assessment.

      10.2.1  Data Validation by Source.

              Not available at this revision.

      10.2.2  Confidence Level/Accuracy Judgment.

              All the data submitted to FIFE have an uncertainty of 1% in the 
              calibration which translates to an absolute uncertainty in 
              aerosol optical thickness of (0.01) per airmass. 

      10.2.3  Measurement Error for Parameters and Variables.

              See Section 10.2.2.

      10.2.4  Additional Quality Assessment Applied.

              FIS staff applied a general Quality Assessment (QA) procedure to 
              these data to identify inconsistencies and problems for potential 
              users. As a general procedure, the FIS QA consisted of examining 
              the maximum, minimum, average, and standard deviation for each 
              numerical field in the data table. An attempt was made to find an 
              explanation for unexpected high or low values, values outside of 
              the normal physical range for a variable, or standard deviations 
              that appeared inconsistent with the mean. In some cases, histog- 
              rams were examined to determine whether outliers were consistent 
              with the shape of the data distribution.

              The discrepancies, which were identified, are reported as
              problems in Section 11.1.

                                  11.  NOTES

11.1  Known Problems With The Data.

      As of the revision date of this document, the following discrepancies or
      errors in the data have been reported:

        Parameter  Sitegrid  Stn  Date    Instrmnt  Description of problem
        ---------  --------  --- -------- -------- ----------------------------

        SURFACE_PRESS
                   XMH2-SPH  417 4-AUG-89  SMX-2    272 values have 0.96

        SURFACE_TEMP        
                   XMH2-SPB  416 4-AUG-89  REAGAN   Only 2 values, 40 & 28

         SOLAR_ZEN_ANG                     C-130    Only records for C-130

         OZONE_OPTCL_THICK 
                   XMH2-SPB  416 6-AUG-89  REAGAN   6 values greater than 0.041

         AEROSOL_OPTCL_THICK  
                   XMH2-SPB  416 4-AUG-89  REAGAN   4 values greater than 0.55
                                 6-AUG-89  REAGAN   6 values greater than 0.597

         TOTAL_OPTCL_THICK       4-AUG-89  C-130    274 values greater than 1.4


11.2  Usage Guidance.

      The purpose of the data in this data set is to give an idea of the 
      discrepancies between the values of different instruments when they are 
      collocated in space and time. This hopefully will assist an investigator 
      in assessing the quality of the measurements during the rest of the IFCs.

11.3  Other Relevant Information. 

      None.

                          12.  REFERENCES

12.1  Satellite/Instrument/Data Processing Documentation.

      Bruegge, C.J., R.N. Halthore, B.L. Markham, M. Spanner and R. Wrigley.
         1992a. Aerosol optical depth retrievals over the Konza Prairie. J. 
         Geophys. Res., 97:18743-18758. 

12.2  Journal Articles and Study Reports.

      Bruegge, C.J., J.E. Conel, R.O. Green, J.S. Margolis, G. Toon and R.G. 
         Holm. 1992b. Water-vapor column abundance retrievals. J. Geophys. 
         Res., 97:18759-18768.
      Fraser, R.S., R.A. Ferrare, Y.J. Kaufman, S. Mattoo. 1989. Algorithm for
         atmospheric corrections of aircraft and satellite imagery. J. Int. 
         Remote Sens., 13:541-557.
      Halthore, R.N., and B.L. Markham. 1992. Overview of Atmospheric 
         Correction and radiometric calibration efforts during FIFE. 
         J. Geophys. Res., 97:18731-18742.
      Halthore, R.N., B.L. Markham, R. Ferrare and O. Aro. 1992. Aerosol 
         optical properties over the mid-continental United States. 
         J. Geophys. Res., 97:18769-18778. 
      King, M.D., and D.M. Bryne. 1976. A method for inferring total ozone
         content from spectral variation of total optical depth obtained with a
         solar  radiometer. J. Atmos. Sci., 33:2242-2251.
      King, M., D. Bryne, B. Herman, and J. Reagan. 1978. Aerosol size distri- 
         butions obtained by inversion of spectral optical depth measurements. 
         J. Atmos. Sci., 35:2153-2167.
      Shaw, G.E., J.A. Reagan, and B.M. Herman. 1973. Investigations of atmos-
         pheric extinction using direct solar radiation measurements made with 
         a multiple wavelength radiometer. J. Appl. Meteorol., 12:374-380.

12.3  Archive/DBMS Usage Documentation. 

      The Collected Data of the First ISLSCP Field Experiment is archived at
      the EOS Distributed Active Archive Center (DAAC) at Oak Ridge National
      Laboratory (ORNL), Oak Ridge, Tennessee (Section 13 below).  
      Documentation about using the archive and/or online access to the data 
      at the ORNL DAAC is not available at this revision.

                             13.  DATA ACCESS

13.1  Contacts for Archive/Data Access Information. 

      ORNL DAAC User Services
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      (615) 241-3952

13.2  Archive Identification. 

      EOSDIS Distributed Active Archive Center
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      USA

      Telephone:       (615) 241-3952
      FAX:             (615) 574-4665
      Internet Email:   ornldaac@onrl.gov

13.3  Procedures for Obtaining Data.

      Users may place requests by letter, telephone, electronic mail, FAX, or 
      personal visit. 

13.4  ORNL DAAC Status/Plans. 

      FIFE data will be available from the ORNL DAAC.  Please contact the 
      ORNL DAAC User Services Office for the most current information about 
      these data.

                 14.  OUTPUT PRODUCTS AND AVAILABILITY 

14.1  Tape Products. 

      None. 

14.2  Film Products. 

      None.

14.3  Other Products.

      Optical Thickness Calibration data are available on FIFE CD-ROM 
      Volume 1.

                        15.  GLOSSARY OF ACRONYMS

ATSP              Airborne Tracking Sunphotometer
CD-ROM            Compact Disk-Read Only Memory
DAAC              Distributed Active Archive Center
EOSDIS            Earth Observing System-Data and Information System
FIFE              First ISLSCP Field Experiment
FIS               FIFE Information System
ISLSCP            International Satellite Land Surface Climatology Project
ORNL              Oak Ridge National Laboratory
UTM               Universal Transverse Mercator