1.  TITLE

1.1  Data Set Identification.

     Solar Transmissometer Aerosol Optical Thickness.

1.2  FIS Data Base Table Name.

     OPTICAL_THICK_FRASER_DATA.

1.3  CD-ROM File Name. 

      \DATA\OPTICAL\OT_FRASR\GRIDxxxx\YyyMmm\ydddgrid.OTF

     Where xxxx is the four digit code for the location within the FIFE site 
     grid, yy is the last two digits of the year (e.g., Y87=1987), mm is the
     month of the year (e.g., M12=December), and ddd is the day of the year,
     (e.g., 061=sixty-first day in the year). Note: capital letters 
     indicate fixed values that appear on the CD-ROM exactly as shown here, 
     lower case indicates characters (values) that change for each path
     and file.

     The format used for the filenames is: ydddgrid.sfx, where grid is the 
     four-number code for the location within the FIFE site grid, y is the 
     last digit of the year (e.g., 7=1987, and 9=1989), and ddd is the day of 
     the year.  The filename extension (.sfx), identifies the data set content
     for the file (see Section 8.2) and is equal to .OTF for this data set. 

1.4  Revision Date Of This Document.

     May 10,1994.

     This document has been reviewed to eliminate technical and editorial 
     inaccuracies by the FIFE Information Scientist. Previous versions of this
     document have been reviewed by the Principal Investigator, the person who
     transmitted the data to FIS, a FIS staff member, or a FIFE scientist 
     generally familiar with the data. It is believed that the document 
     accurately describes the data as collected and as archived on the FIFE
     CD-ROM series.

                            2.  INVESTIGATOR(S)

2.1  Investigator(s) Name And Title.

     Staff Science.

2.2  Title Of Investigation.

     Aerosol Optical Thickness Measurements During FIFE.

2.3  Contacts (For Data Production Information).

 
_____________________________________________________________________________
|              |           Contact 1          |       Contact 2              |
|______________|______________________________|______________________________|
|2.3.1 Name    |Dr. R.N. Halthore             |Mr. Brian L. Markham          |
|2.3.2 Address |Code 923                      |Code 923                      |
|              |NASA Goddard Sp. Fl. Ctr.     |NASA Goddard Sp. Fl. Ctr.     |
|      City/St.|Greenbelt                     |Greenbelt                     |
|      Zip Code|MD 20771                      |MD 20771                      |
|2.3.3 Tel.    |(301) 286-1094                |(301) 286-5240                |
|2.3.4 Email   |halthore@ltpsun.gsfc.nasa.gov |Markham@highwire.gsfc.nasa.gov|
|______________|______________________________|______________________________|

2.4  Requested Form of Acknowledgement.

     The aerosol optical thickness data were collected under the direction of
     the FIFE calibration scientist B. Markham and his staff at GSFC. The
     dedicated efforts of B. Markham and R. Halthore in the collection analysis
     and preparation of these data is greatly appreciated. Please cite the
     following papers in any work or publication using these data:

     Halthore, R.N., B.L. Markham, R. Ferrare, and T.O. Aro. 1992. 
        Aerosol optical properties over the mid-continental United States. J. 
        Geophys. Res. 97:18,769-18,778.

     Bruegge, C.J., R.N. Halthore. B.L. Markham, M. Spanner, and R. 
        Wrigley. 1992a. Aerosol optical depth retrievals over the Konza 
        Prairie. J. Geophys. Res. 97:18,743-18,758.

                               3.  INTRODUCTION

3.1  Objective/Purpose.

     The focus of these measurements of aerosol optical thickness was 
     to enable an estimation of atmospheric effects on transmitted and 
     reflected radiation. These estimates can then be used to develop 
     correction schemes for aircraft and satellite radiometric data.
    
3.2  Summary of Parameters.

     Atmospheric pressure, ozone content, and aerosol optical thickness 
     at 8 wavelengths from 440 to 1030 nanometers (nm).

3.3  Discussion.

     These optical thickness data provide a measure of the effect of aerosols
     on the attenuation of radiation through the atmosphere at 8 descrete wave- 
     length bands throughout the visible and near IR portion of the electro- 
     magnetic spectrum. These data are used to provide atmospheric correction 
     of remotely sensed data using radiative transfer models and to study
     aerosol particle size distribution (see Halthore and Markham 1992; King
     et al. 1978). These data are also used to infer the optical clarity of
     the atmosphere. These data were collected using a ground-based solar
     transmissometer in June and July of 1987, and July and August of 1989, at
     two stations in the FIFE study area. 
     
                          4.  THEORY OF MEASUREMENTS

Aerosol optical thickness is highly variable in space and time, and an accurate 
estimate is made by measuring the direct solar radiance at the ground by the
use of a calibrated sunphotometer. Solar radiation reaching the ground is
attenuated by absorption and scattering by atmospheric molecules, as well as
particles. Molecular scattering (Rayleigh scattering) is estimated by measuring
the pressure. Molecular absorption is avoided by an appropriate choice of band
passes. 

If I is the solar radiance at the surface, 

    I = (I_o/r^2) exp ((-m*tau)_R+(-m tau)_oz+(-m*tau)_aer) * T_w

where I_o is the exo-atmospheric solar radiance, r is the Sun-Earth distance in
Astronomical Units, m is the airmass, tau is the optical thickness, and sub- 
scripts R, oz, and aer refer to Rayleigh, ozone, and aerosol components of the 
total attenuation. Tw is the transmission due to water vapor attenuation. Since 
the instruments used by this group avoided the water absorption bands, T_w is 
assumed to be 1. The form of the above equation then becomes what is commonly 
known as the Beer-Lambert-Bouger law.

If V is voltage response of the sunphotometer,

    ln(V) + (m*tau)_R + (m*tau)_oz = ln (V_o/R^2) -(m*tau)_aer.

Here, V_o is the calibration coefficient and is the fictitious response of the 
sunphotometer to exo-atmospheric solar radiance. By measuring surface pressure, 
tau_R can be accurately calculated. From climatology or from the TOMS
(Total Ozone Mapping Spectrometer) aboard the Nimbus satellite, ozone column
abundance can be obtained from which tau_oz can be calculated. Thus, in the
above equation, all terms except tau_aer are known for each measurement of V. 

                                5.  EQUIPMENT

5.1  Instrument Description.

     The eight-channel sunphotometer, named SXM-2 (Spinhirne, 1983), is a
     table-mounted automatic Sun-tracking transmissometer having wavelengths of
     440, 522, 557, 613, 672, 781, 871, and 1030 nm with 10 nm full width 
     at half maximum (FWHM). It was used on the ground. SXM-3 is identical to
     SXM-2 except that it is hand-held. SXM-3 was used in 1987, and SXM-2 was
     used in 1989.

     5.1.1  Platform.

            Ground.
 
     5.1.2  Mission Objectives.

            The primary reasons for collecting these data were two fold,
            1) to measure atmospheric attenuation and hence estimate the 
               aerosol optical thickness, and 2) to then use the aerosol 
               optical thickness values in radiative transfer algorithms 
               to estimate components of the radiation field at the 
               ground or at the sensor.

     5.1.3  Key Parameters.

            Aerosol optical thickness, surface atmospheric pressure, and ozone 
            abundance.

     5.1.4  Principles of Operation.

            The SXM-3 is a hand-held sunphotometer used only in the 
            1987 field campaign. It has a peak hold feature, which enables
            the instrument to measure and hold the maximum voltage as the
            instrument is pointed toward the Sun. The detector is a silicon 
            photodiode detector, which is kept at a constant temperature 
            of 20 degrees C. It employs multiple gain settings allowing gain
            factors of 1, 10, 1000, and 10,000, thus enabling solar radiance,
            as well as sky radiance measurements with  a viewing angle of
            approximately 1.3 degrees (Spinhirne and King, 1985). 

            In 1989, SXM-2, an automatic version of SXM-3, was used. SXM-2 has
            the same eight channels as SXM-3, but unlike SXM-3, it tracks the
            Sun automatically. The frequency of sampling for the SXM-2 can be
            varied from once every 0.5 min to once every 4 min. The SXM-3
            detector is kept at a constant temperature of 25 degrees C.

     5.1.5  Instrument Measurement Geometry.

            The field-of-view (FOV) for SXM-2 and SXM-3 are 0.8 and 
            1.3 degrees, respectively. 

     5.1.6  Manufacturer of Instruments.

            SXM-2 and SXM-3 were built at Goddard Space Flight Center, 
            Greenbelt, Maryland. 

5.2  Calibration.

     Calibration was performed using the Langley plot method. This method has 
     been discussed extensively in the literature (Shaw et al. 1973; See also 
     Section 5.2 in the document Optical Thickness Calibration.) In 1987, 
     Langley plots were obtained for the SXM-3 on two relatively clear 
     and stable days. In 1987, the derived optical thickness values 
     did not agree with the instrument readings from the JPL Reagan 
     sunphotometer. For that reason, the calibration obtained using 
     the Langley plots was supplemented with the information obtained 
     from the instrument intercomparisons performed in 1989. In 1989, 
     the SXM-2 instrument was calibrated before and after the FIFE IFC 
     in August at mountain sites. These data and the data from the 
     intercomparisons of this instrument, the Reagan Sunphotometer 
     (see NIPS and Reagan Sunphotometer Optical Thickness) and the 
     C-130 airborne tracking sunphotometer (see Sunphotometer Optical 
     Thickness Data from c130 Aircraft) were used to create a calibration 
     for the SXM-2 in 1989.

     5.2.1  Specifications.

            See Section 5.1.
           
            5.2.1.1  Tolerance.

                     The precision of SXM-2 and SXM-3 is quite good at 
                     4 x 10E-4 in some channels. The accuracy is determined 
                     by the accuracy in calibration, which is estimated 
                     to be 1% translating to +/- 0.01 in aerosol optical 
                     thickness at 1 airmass.

     5.2.2  Frequency of Calibration.

            The responses of the instrument were monitored during the 
            experiment period in 1989 by instrument intercomparison 
            (see the Optical Thickness Calibration and Aerosol 
            Optical Thickness from GSFC documents) and calibration 
            at Mountain top sites before and after FIFE. In 1987, 
            Langley calibration was performed on 2 days and checked 
            with prior calibrations. In the period between the 1987 
            and 89 field campaigns, Langley plots used for calibration 
            were obtained on 3 days. Finally, in 1989, instrument 
            calibration was performed both before and after the August 
            IFC at a mountain site and during the IFC via a comparison 
            of the three instruments used to measure aerosol optical 
            thickness.

     5.2.3  Other Calibration Information.

            None.

                              6.  PROCEDURE

6.1  Data Acquisition Methods.

     In 1987, data were acquired from the manual SXM-3 sunphotometer with the
     aid of an electronic data logger. Data were written to a cassette tape
     within the data logger. Of the 20 days of data, 11 days were
     either clouded or rained out.
  
     In 1989, data were acquired throughout the day using a SXM-2. Date were
     logged directly on to a computer and then down-loaded for analysis. 
     On some days, cloud cover did not allow continuous measurement 
     of solar transmission.

6.2  Spatial Characteristics. 

     The FIFE study area, with areal extent of 15 km by 15 km, is located south
     of the Tuttle Reservoir and Kansas River, and about 10 km from Manhattan,
     Kansas, USA. The northwest corner of the area has UTM coordinates of
     4,334,000 Northing and 705,000 Easting in UTM Zone 14.

     6.2.1  Spatial Coverage.

            In 1987, measurements were made at station 100 (sitegrid 1609-SPF) 
            with SXM-3. In 1989, measurements were made at station 415
            (sitegrid 3639-SPH) with SXM-2.

     6.2.2  Spatial Resolution.

            These are point data. However, single measurement represents the 
            area of the FIFE study area.

6.3  Temporal Characteristics.

     6.3.1  Temporal Coverage.

            Measurements were made during daylight hours on 10 days from June
            25, 1987 to July 14, 1987, and on 13 days from July 25, 1989 to
            August 12, 1989. 

     6.3.2  Temporal Resolution.

            The SXM-2 instrument cycles through a set of eight filters in about
            20 seconds and the frequency of sampling can be varied from once
            every 4 minutes to once every .5 minutes. In 1987, the SXM-3 
            obtained data when possible approximately every 5 minutes. 
            The number of spectra obtained each day ranges from 5 to 376. 

                               7.  OBSERVATIONS
7.1  Field Notes.

     Contact R.N. Halthore (see Section 2.3), if you wish to examine the field 
     notes. 

                            8.  DATA DESCRIPTION

8.1  Table Definition With Comments. 

     The SQL definition for this table is found in the OT_FRASR.TDF file 
     found on the CD-ROM Volume 1.

8.2  Type of Data.

--------------------------------------------------------------------------------
|                 8.2.1                  |               |          |          |
|Parameter/Variable Name                 |               |          |          |
--------------------------------------------------------------------------------
|    |               8.2.2               |     8.2.3     |  8.2.4   |  8.2.5   |
|    |Parameter/Variable Description     |Range          |Units     |Source    |
--------------------------------------------------------------------------------
|SITEGRID_ID                             |               |          |          |
|    |This is a FIS grid location code.  |               |          |          |
|    |Site grid codes (SSEE-III) give    |               |          |          |
|    |the south (SS) and east (EE) cell  |               |          |          |
|    |number in a 100x100 array of 200m  |               |          |          |
|    |square cells.  The last 3          |               |          |          |
|    |characters (III) are an instrument |               |          |          |
|    |identifier.                        |               |          |          |
--------------------------------------------------------------------------------
|STATION_ID                              |               |          |          |
|    |The Station ID number for the      |               |          |          |
|    |location of the observations.      |               |          |          |
--------------------------------------------------------------------------------
|OBS_DATE                                |               |          |          |
|    |The date on which the observation  |min = 25-JUN-87|          |GSFC      |
|    |was made.                          |,              |          |          |
|    |                                   |max = 12-AUG-89|          |          |
--------------------------------------------------------------------------------
|OBS_TIME                                |               |          |          |
|    |The time when the observation was  |min = 4,       |[GMT]     |GSFC      |
|    |made.                              |max = 2356     |          |          |
--------------------------------------------------------------------------------
|INSTR_ID                                |               |          |          |
|    |The instrument which collected     |               |          |          |
|    |the image data.                    |               |          |          |
--------------------------------------------------------------------------------
|SURFACE_PRESS                           |               |          |          |
|    |The surface pressure.              |min = 1,       |[millibars|ANEROID SE|
|    |                                   |max = 1        |]         |NSOR      |
--------------------------------------------------------------------------------
|ABUNDANCE_OF_OZONE                      |               |          |          |
|    |The column abundance of ozone,     |min = 297,     |[Dobson Un|SUNPHOTOME|
|    |reduced to STP.                    |max = 348      |its]      |TER       |
--------------------------------------------------------------------------------
|AEROSOL_OPTCL_THICK_440                 |               |          |          |
|    |The aerosol optical thickness for  |min = .059,    |          |SUNPHOTOME|
|    |a wavelength of 440.8 nm.          |max = .697     |          |TER       |
--------------------------------------------------------------------------------
|AEROSOL_OPTCL_THICK_552                 |               |          |          |
|    |The aerosol optical thickness for  |min = .051,    |          |SUNPHOTOME|
|    |a wavelength of 552.2 nm.          |max = .564     |          |TER       |
--------------------------------------------------------------------------------
|AEROSOL_OPTCL_THICK_557                 |               |          |          |
|    |The aerosol optical thickness for  |min = .043,    |          |SUNPHOTOME|
|    |a wavelength of 557.9 nm.          |max = .512,    |          |TER       |
|    |                                   |missing = -9.99|          |          |
|    |                                   |9              |          |          |
--------------------------------------------------------------------------------
|AEROSOL_OPTCL_THICK_612                 |               |          |          |
|    |The aerosol optical thickness for  |min = .038,    |          |SUNPHOTOME|
|    |a wavelength of 612.7 nm.          |max = .471,    |          |TER       |
|    |                                   |missing = -9.99|          |          |
|    |                                   |9              |          |          |
--------------------------------------------------------------------------------
|AEROSOL_OPTCL_THICK_672                 |               |          |          |
|    |The aerosol optical thickness for  |min = .034,    |          |SUNPHOTOME|
|    |a wavelength of 672.3 nm.          |max = .443,    |          |TER       |
|    |                                   |missing = -9.99|          |          |
|    |                                   |9              |          |          |
--------------------------------------------------------------------------------
|AEROSOL_OPTCL_THICK_781                 |               |          |          |
|    |The aerosol optical thickness for  |min = .027,    |          |SUNPHOTOME|
|    |a wavelength of 781.2 nm.          |max = .389,    |          |TER       |
|    |                                   |missing = -9.99|          |          |
|    |                                   |9              |          |          |
--------------------------------------------------------------------------------
|AEROSOL_OPTCL_THICK_872                 |               |          |          |
|    |The aerosol optical thickness for  |min = .022,    |          |SUNPHOTOME|
|    |a wavelength of 872.4 nm.          |max = .351,    |          |TER       |
|    |                                   |missing = -9.99|          |          |
|    |                                   |9              |          |          |
--------------------------------------------------------------------------------
|AEROSOL_OPTCL_THICK_1030                |               |          |          |
|    |The aerosol optical thickness for  |min = .021,    |          |SUNPHOTOME|
|    |a wavelength of 1030.0 nm.         |max = .485,    |          |TER       |
|    |                                   |missing = -9.99|          |          |
|    |                                   |9              |          |          |
--------------------------------------------------------------------------------
|FIFE_DATA_CRTFCN_CODE                   |       **      |          |          |
|    |The FIFE Certification Code for    |min = D,       |          |FIS       |
|    |the data, in the following format: |max = E        |          |          |
|    |CPI (Certified by PI), CPI-???     |               |          |          |
|    |(CPI - questionable data).         |               |          |          |
--------------------------------------------------------------------------------
|LAST_REVISION_DATE                      |               |          |          |
|    |The last revision date for the     |min = 09-MAY-88|          |FIS       |
|    |data, in the format (DD-MMM-YY).   |,              |          |          |
|    |                                   |max = 16-NOV-89|          |          |
--------------------------------------------------------------------------------

Footnote:

      ** Valid levels.

      The primary certification codes are:

      EXM - Example or Test data (not for release).
      PRE - Preliminary (unchecked, use at your own risk).
      CPI - Checked by Principal Investigator (reviewed for quality).
      CGR - Checked by a group and reconciled (data comparisons and 
            cross-checks).

      The certification code modifiers are:

      PRE-NFP  - Preliminary - Not for publication, at the request of 
                 investigator.
      CPI-MRG  - PAMS data that are "merged" from two separate receiving 
                 stations to eliminate transmission errors.
      CPI-???  - Investigator thinks data item may be questionable.
 
8.3  Sample Data Record.

     SITEGRID STATION_ID OBS_DATE    OBS_TIME INSTR_ID     SURFACE_PRESS
     -------- ---------- --------- ---------- ------------ -------------
     3639-SPH        415 25-JUL-89       1403 SXM-2                963.6
     3639-SPH        415 25-JUL-89       1403 SXM-2                963.6
     3639-SPH        415 25-JUL-89       1404 SXM-2                963.6
     3639-SPH        415 25-JUL-89       1404 SXM-2                963.6
     3639-SPH        415 25-JUL-89       1404 SXM-2                963.6
     3639-SPH        415 25-JUL-89       1405 SXM-2                963.6

     ABUNDANCE_OF_OZONE AEROSOL_OPTCL_THICK_440 AEROSOL_OPTCL_THICK_552
     ------------------ ----------------------- -----------------------
                    300                    .438                    .372
                    300                    .428                    .362
                    300                    .428                    .363
                    300                     .43                     .36
                    300                    .422                    .355
                    300                    .422                    .355

     AEROSOL_OPTCL_THICK_557 AEROSOL_OPTCL_THICK_612 AEROSOL_OPTCL_THICK_672
     ----------------------- ----------------------- -----------------------
                        .329                    .285                    .247
                        .321                    .281                    .242
                        .325                    .284                    .247
                        .319                    .279                    .241
                        .314                    .273                    .238
                        .316                    .278                    .241

     AEROSOL_OPTCL_THICK_781 AEROSOL_OPTCL_THICK_872 AEROSOL_OPTCL_THICK_1030 
     ----------------------- ----------------------- ------------------------ 
                        .193                    .158                     .118 
                        .187                    .155                     .117 
                        .191                    .158                      .12 
                        .187                    .153                     .117 
                        .187                    .154                     .118 
                        .186                    .152                     .117 


     FIFE_DATA_CRTFCN_CODE     LAST_REVISION_DATE
     ---------------------     ------------------
     CPI                       16-NOV-89
     CPI                       16-NOV-89
     CPI                       16-NOV-89
     CPI                       16-NOV-89
     CPI                       16-NOV-89
     CPI                       16-NOV-89

                                                                             
8.4  Data Format.

     The CD-ROM file format consists of numerical and character fields of 
     varying length separated by commas. The character fields are enclosed with 
     a single apostrophe. There are no spaces between the fields.  Each file 
     begins with five header records. Header records contain the following 
     information:

     Record 1    Name of this file, its table name, number of records in
                 this file, and principal investigator name.
     Record 2    Path and filename of the previous data set, and path and 
                 filename of the next data set. (Path and filenames for files 
                 that contain another set of data taken at the same site on 
                 the same day.)
     Record 3    Path and filename of the previous site, and path and filename 
                 of the next site. (Path and filenames for files of the same 
                 data set taken on the same day for the previous and next 
                 sites, sequentially numbered by SITEGRID.)
     Record 4    Path and filename of the previous date, and path and filename 
                 of the next date. (Path and filenames for files of the same 
                 data set taken at the same site for the previous and next 
                 date.)
     Record 5    Column names for the data within the file, delimited by 
                 commas.
     Record 6    Data records begin.

     Each field represents one of the attributes listed in the chart in 
     Section 8.2 and described in detail in the TDF file (see Section 8.1). 
     These fields are in the same order as in the chart.

8.5  Related Data Sets.

     NIPS and Reagan Sunphotometer Optical Thickness (Bruegge).
     Sunphotometer Optical Thickness Data from C130 Aircraft.
     Optical Thickness Calibration.
     Aerosol Optical Thickness from GSFC.

                           9.  DATA MANIPULATIONS

9.1  Formulas.

     9.1.1  Derivation Techniques/Algorithms.

            From pressure values, obtain the Rayleigh optical thickness:
            (Hansen and Travis, 1974)

                tau_R = (p/p0) (0.008569/L^4) (1-0.0113/L^2-0.00013/L^4)

            where, p is the measured surface pressure, p0 is pressure
            at sea level, and L is the wavelength in micrometers.

            The ozone optical thickness is obtained by multiplying the column 
            abundance in Dobson units ([matm][cm]) with the absorption coeff- 
            icient given in the following table for a particular wavelength and
            dividing by 1000.

                     Ozone Absorption Coefficients

             _____________________________________________________

              Wavelength                  Absorption Coefficient
                 [nm]                        [atm^-1][cm^-1]

             _____________________________________________________

                 368                          6.18 E-4
                 380                          3.22 E-4
                 441                          3.36 E-3
                 500                          3.28 E-2
                 522                          4.80 E-2
                 551                          9.73 E-2
                 613                          1.19 E-1
                 640                          2.89 E-2
                 671                          4.55 E-2
                 781                          4.61 E-3
                 872                          6.17 E-4
                 945                          0.00 E-0
                1030                          0.00 E-0
             _____________________________________________________

9.2  Data Processing Sequence.

     9.2.1  Processing Steps and Data Sets.

            To get the total optical thickness, first, the formulae given in
            the above section is used to compute the Rayleigh optical
            thickness. Second, compute the ozone optical thickness (if any),
            and third, add them to the aerosol optical thickness.

     9.2.2  Processing Changes.

            None.

9.3  Calculations.

     9.3.1  Special Corrections/Adjustments.

            None.

9.4  Graphs and Plots.

     None.

                                 10.  ERRORS

10.1  Sources of Error.

      Errors can arise (i) while calibrating and (ii) while measuring.
      During calibration, a requirement of the Langley plot method is that
      the atmospheric optical thickness remains constant during the period
      of maximum airmass change. At mountain sites, this requirement is 
      usually met on clear days, but not always. The effect of varying 
      atmospheric conditions is reflected in the quality of the Langley
      plots (see Halthore and Markham 1992). The calibration coefficient,
      which is the y-intercept in Langley plots, can be obtained to a 
      consistency better than 1% and we take this as the uncertainty in
      our measurements. A 1% uncertainty in V_o (calibration coefficient) 
      translates to an absolute uncertainty in the aerosol optical thickness of
      0.01 at airmass of 1. The equation is:

          Delta(tau_aerosol) = (1/m)((Delta V_o)/V_o)

      Uncertainties in the Rayleigh optical thickness and ozone optical
      thickness are negligible for the conditions encountered in FIFE.

      For sunphotometers that do not employ constant temperature 
      detectors, a major source of variation and hence uncertainty may
      arise due to inadequate temperature compensation for the response.
      Furthermore, for sunphotometers that do not employ auto-tracking
      or peak hold features, another major source of uncertainty
      arises due to imperfect pointing. Neither of these two sources 
      of error are applicable in this case.

10.2  Quality Assessment.

      10.2.1  Data Validation by Source.

              The FIFE calibration scientist (B. Markham) and staff at GSFC 
              believe their data to be of good quality.

      10.2.2  Confidence Level/Accuracy Judgement.

              All these data submitted to FIFE have an uncertainty
              of 1% in the calibration, which translates to an     
              absolute uncertainty in aerosol optical thickness
              of (0.01)/m where m is the airmass. 

      10.2.3  Measurement Error for Parameters and Variables.

              Not applicable.

      10.2.4  Additional Quality Assessment Applied.

              FIS staff applied a general Quality Assessment (QA) procedure to 
              these data to identify inconsistencies and problems for potential 
              users. As a general procedure, the FIS QA consisted of examining 
              the maximum, minimum, average, and standard deviation for each 
              numerical field in the data table. An attempt was made to find an 
              explanation for unexpected high or low values, values outside of 
              the normal physical range for a variable, or standard deviations 
              that appeared inconsistent with the mean. In some cases, histog- 
              rams were examined to determine whether outliers were consistent 
              with the shape of the data distribution.

              The discrepancies, which were identified, are reported as
              problems in Section 11.1.

                                  11.  NOTES

11.1  Known Problems With The Data.

      As of the revision date of this document, the following discrepancies or
      errors in the data have been reported:

      *  All values for SURFACE_PRESSURE hover around 1.
     
      *  All values for aerosol optical thickness on August 12, 1989 are
         suspicious and should be used with caution.

      *  Values for the ABUNDANCE_OF_OZONE are constant throughout the day and 
         were higher than expected on 3 days, July 1, 1987, July 13, 1987
         and July 14, 1987 (ozone values of 324, 325 and, 348 respectively.)

      For 1987 data, the optical thickness for the 1030-nm channel did 
      not agree with similar measurements using the sunphotometer (see NIPS
      and Reagan Sunphotometer Optical Thickness (Bruegge)). The problem may be
      with either instrument.

11.2  Usage Guidance.

      The derived aerosol optical thicknesses can be used to correct
      remotely sensed data for atmospheric effect in conjunction with a
      reliable radiative transfer model, and they can be used to derive aerosol
      size distribution (Halthore et al. 1992; Markham et al. 1992).
     
11.3  Other Relevant Information. 

      None.

                          12.  REFERENCES

12.1  Satellite/Instrument/Data Processing Documentation.

      Spinhirne, J.D. 1983. El Chichon eruption cloud: Latitudinal variation of
         the spectral optical thickness for October 1982. Geophys. Lett. 
         10:881-884.

      Bruegge, C.J., R.N. Halthore, B.L. Markham, M. Spanner and R. Wrigley.
         1992a. Aerosol optical depth retrievals over the Konza Prairie. J. 
         Geophys. Res. 97:18,743-18,758. 

12.2  Journal Articles and Study Reports.

      Bruegge, C.J., J.E. Conel, R.O. Green, J.S. Margolis, G. Toon and R.G. 
         Holm. 1992b. Water-vapor column abundance retrievals. J. Geophys. 
         Res. 97:18,759-18,768.
      Fraser, R.S., R.A. Ferrare, Y.J. Kaufman, S. Mattoo. 1989. Algorithm for
         atmospheric corrections of aircraft and satellite imagery. J. Int. 
         Remote Sens. 13:541-557.
      Halthore, R.N., and B.L. Markham. 1992. Overview of Atmospheric
         Correction and radiometric calibration efforts during FIFE. J.
         Geophys. Res. 97:18,731-18,742.
      Halthore,R.N., B.L.Markham, R.Ferrare and O.Aro. 1992. Aerosol optical 
         properties over the mid-continental United States. J. Geophy. Res. 
         97:18,769-18,778. 
      King, M.D., and D.M. Bryne. 1976. A method for inferring total ozone
         content from spectral variation of total optical depth obtained with a
         solar radiometer. J. Atmos. Sci. 33:2242-2251.
      King, M., D. Bryne, B. Herman, and J. Reagan. 1978. Aerosol size distri- 
         butions obtained by inversion of spectral optical depth measurements. 
         J. Atmos. Sci. 35:2153-2167.
      Markham, B.L., R.N. Halthore, and S.J. Goetz. 1992. Surface reflectance 
         retrieval from satellite and aircraft sensors during FIFE. J. Geophys.
         Res. 97:18,785-18,795. 
      Shaw, G.E., J.A. Reagan, and B.M. Herman. 1973. Investigations of atmos-
         pheric extinction using direct solar radiation measurements made with 
         a multiple wavelength radiometer. J. Appl. Meteorol. 12:374-380.
      Spinhirn, J.D., and M.D. King. 1985. Latitudinal variation of spectral 
         optical thickness and columnar size distribution of the El Chichon 
         stratospheric aerosol layer. J. Geophys. Res. 90:10,607-10,619.

12.3  Archive/DBMS Usage Documentation. 

      The Collected Data of the First ISLSCP Field Experiment are archived at
      the EOS Distributed Active Archive Center (DAAC) at Oak Ridge National
      Laboratory (ORNL), Oak Ridge, Tennessee (see Section 13 below).  
      Documentation about using the archive and/or online access to 
      these data at the ORNL DAAC is not available at this revision.

                             13.  DATA ACCESS

13.1  Contacts for Archive/Data Access Information. 

      ORNL DAAC User Services Office
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      (615) 241-3952

13.2  Archive Identification. 

      EOSDIS Distributed Active Archive Center
      P.O. Box 2008, 
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      USA

      Telephone:       (615) 241-3952
      FAX:             (615) 574-4665
      Internet Email:   ornldaac@onrl.gov

13.3  Procedures for Obtaining Data.

      Users may place requests by letter, telephone, electronic mail, FAX, or 
      personal visit. 

13.4  ORNL DAAC Status/Plans. 

      FIFE data will be available from the ORNL DAAC.  Please contact the 
      ORNL DAAC User Services Office for the most current information about 
      these data.

                 14.  OUTPUT PRODUCTS AND AVAILABILITY 

14.1  Tape Products. 

      None.

14.2  Film Products. 

      None.

14.3  Other Products.

      Solar Transmissometer Aerosol Optical Thickness data are available
      on FIFE CD-Rom Volume 1.

                        15.  GLOSSARY OF ACRONYMS

BPI               Byte per inch
CCT               Computer Compatible Tape
CD-ROM            Compact Disk-Read Only Memory
DAAC              Distributed Active Archive Center
EOSDIS            Earth Observing System Data and Information System
FIFE              First ISLSCP Field Experiment
FIS               FIFE Information System
FOV               Field of View
FWHM              Full Width Half Maximum
IFC               Intensive Field Campaign
ISLSCP            International Satellite Land Surface Climatology Project
JPL               Jet Propulsion Laboratory
ORNL              Oak Ridge National Laboratory
PAMS              Portable Automatic Mesonet Station
TOMS              Total Ozone Mapping Spectrometer
UTM               Universal Transverse Mercator