1.  TITLE

1.1  Data Set Identification.

     High Spectral Resolution Measurements from the Russian Gemma Instrument.

1.2  FIS Data Base Table Name.

     GEMMA_HELO_DATA.

1.3  CD-ROM File Name.

     \DATA\SUR_REFL\GEM_HELO\GRIDxxxx\ydddgrid.GHs 

     Where xxxx is the four digit code for the location within the FIFE site
     grid. Note: capital letters indicate fixed values that appear on the CD-
     ROM exactly as shown here, lower case indicates characters (values) that 
     change for each path and file. 

     The format used for the filenames is: ydddgrid.sfx, where grid is the four 
     number code for the location within the FIFE site grid, y is the last 
     digit of the year (e.g., 7=1987, and 9=1989), and ddd is the day of the 
     year (e.g., 061=sixty-first day in the year), and s is the sequential
     number of this spectra for that date and location. There are one to five
     spectra. The filename extension (.sfx), identifies the data set content 
     for the file (see Section 8.2) and is equal to .GH1, .GH2, .GH3, .GH4, 
     or .GH5 for this data set. 

1.4  Revision Date Of This Document.

     May 5, 1994.
 
     Warning:  This document has not been checked for technical or editorial
               accuracy by the FIFE Information Scientist. There may be 
               inconsistencies with other documents, technical or editorial 
               errors that were inadvertently introduced when the document was 
               compiled or references to preliminary data that were not 
               included on the final CD-ROM.

               Previous versions of this document have been reviewed by the 
               Principal Investigator, the person who transmitted the data to 
               FIS, a FIS staff member, or a FIFE scientist generally familiar 
               with the data.

                                  2.  INVESTIGATOR(S)

2.1  Investigator(s) Name And Title.

     Boris I. Belyaev
     Byelorussian State University 

     Igor K. Gorankov
     Academy of Sciences of the USSR

2.2  Title Of Investigation.

     Spectropolarimetry Using Gemma Instrument.

2.3  Contacts (For Data Production Information). 

     ____________________________________________________________
     |              |      Contact 1                             |
     |______________|____________________________________________| 
     |2.3.1 Name    |Charles L. Walthall                         |
     |2.3.2 Address |Laboratory for Global Remote Sensing Studies| 
     |              |Dept. of Geography, Univ. of MD             |
     |      City/St.|College Park, MD                            |
     |      Zip Code|20742                                       |
     |2.3.3 Tel.    |(301) 405-4058                              |
     |2.3.4 Email   |cw7@umail.umd.edu                           |
     |______________|____________________________________________| 

2.4  Requested Form of Acknowledgment.

     The High Spectral Resolution Measurements from the Russian Gemma 
     Instrument were collected by the FIFE helicopter crew for B.I. Belyaev 
     and I.K. Gorankov of Byelorussian State University and Academy of 
     Sciences of the USSR, respectively.  The dedicated efforts of this 
     team of pilots, mechanics, photographers and scientists are especially 
     appreciated.  The efforts of the following individuals are notable:  
     Helicopter crew: Charles Walthall, mission scientist; William Dykes, 
     pilot; Charles Smith, mechanic and observer; Ed Bohles, mechanic and 
     observer; Richard Huey, photographer; David Pierce, engineer; Douglas 
     Young, engineer; Moon Kim, software development and data processing; 
     Frank Wood, system integration; US Army 82nd Medical Helicopter Unit, 
     Ft. Riley, Kansas for on-site hanger space and helicopter technical 
     support.

                                 3.  INTRODUCTION

3.1  Objective/Purpose.

     The acquisition of multispectral radiometer data from FIFE sites using a 
     helicopter platform.

3.2  Summary of Parameters.

     Reflected radiance. 

3.3  Discussion.

     During the 1989 Intensive Field Campaign a Russian spectroradiometer, the 
     Gemma, was used to collect visible and near infrared spectra of a 
     variety of FIFE sites from a helicopter. Gemma measurements of 
     selected study sites and laboratory measurements of a portable calibration 
     light sphere were made. 

                              4.  THEORY OF MEASUREMENTS

The helicopter missions were designed to provide 1) a rapid means of 
intensively, spectrally characterizing each FIFE site while providing FIFE 
study area coverage, and 2) to provide an intermediate scale of sampling 
between that of the surface measurements and the higher altitude aircraft and 
spacecraft multispectral imaging devices. The Gemma spectroradiometer was 
mounted on the helicopter to allow a comparison between it and the SE-590 
spectroradiometer and Modular Multiband Radiometer (MMR) over a number of 
sites.

                                    5.  EQUIPMENT

5.1  Instrument Description.

     Gemma is a portable spectroradiometer based on a scanning monochrometer 
     with optional provisions for measurement of polarization. The optical 
     system module (MS-03) includes a polarization device that is placed in 
     front of the monochrometer lens (designated as the MS- 02 STOKS module). A 
     gap in the spectral data exists at 626 nm +/-1nm due to an absorption line 
     from the configuration of the monochrometer and therefore data is 
     unavailable at this wavelength. The system has 396 channels in the 
     spectral range of 0.409 to 0.804 micrometers and takes less than 1 second 
     to complete a spectral scan. The gain is pre-set to accommodate radiance 
     levels commonly found under field conditions. The focus of the lens system 
     is variable between 80-200 mm yielding a field-of-view between 3.6 x 0.3 
     and 1.5 x 0.1 degrees. A microcomputer system (ACC-2) serves as the 
     control unit and as the data logger for Gemma. This microcomputer system 
     is also used to process the data. Data storage is via cassette tape.

     5.1.1  Platform. 

            During 1989 the Gemma was mounted on a plate on the port side of 
            the NASA Bell UH-1B "Huey" helicopter (NASA 415). The instrument   
            was fixed in a nadir-looking attitude for all of the helicopter 
            flights. Because of logistical limitations and time restrictions, 
            it was not possible to accurately adjust the optical alignment of 
            Gemma to that of the SE-590 and the MMR.

     5.1.2  Mission Objectives.

            There were two type of helicopter optical system missions: H-1a and 
            H-1b. The objective of the H-1a missions was to acquire spectral 
            data of specific FIFE sites coincident with surface, atmospheric 
            and satellite measurements. The objective for the H-1b missions was 
            to acquire multispectral data of as many FIFE sites during the 
            available flight time. All regular FIFE sites were measured from a 
            hover. Some special sites were flown in a slow-flight transect 
            mode.

            The area for observations within a site differed for the three 
            primary sites (906, 916 and 928) from the other FIFE sites. For the 
            primary sites the area upwind of the flux tower or "WAB" area was 
            outlined by crews on the surface with flags: the two edges and a 
            center line directly into the wind were marked. Using these lines 
            as guides, slow flight transects with an average of 8 observations 
            per line were flown. Sampling of the other FIFE sites followed the 
            1987-type pattern of sampling. The sample area for these sites was 
            a doughnut-like ring around the automated weather stations or over 
            areas where surface radiance and biology measurements were being 
            conducted. The ring around the weather stations was 2-3 times the 
            width of the weather station areas (the instruments were normally 
            bounded by fences).

     5.1.3  Key Parameters.

            Reflected spectral radiance and wavelength.

     5.1.4  Principles of Operation.

            The Gemma spectroradiometer based on a scanning monochrometer The 
            system has 396 channels in the spectral range of 0.409 to 0.804 
            micrometers and takes less than 1 second to complete a spectral 
            scan. A gap in the spectral data exists at 0.626 micrometers +/- 
            0.01 micrometers due to an absorption line from the configuration 
            of the monochrometer and therefore data is unavailable at this 
            wavelength.

     5.1.5  Instrument Measurement Geometry.

            The Gemma was mounted on a plate on the port side of the helicopter 
            and fixed at a nadir view. The focus of the lens system is variable 
            between 80-200 mm yielding a field-of-view between 3.6 x 0.3 and 
            1.5 x 0.1 degrees. The helicopter collected data at an altitude of 
            330 m.

     5.1.6  Manufacturer of Instrument.

            Built by engineers at White Russian State University, Minsk, CIS.

5.2  Calibration.

     Spectral and radiometric calibration of Gemma is done at the Meteorol-
     ogical Complex for Spectrophotometric Testing at Byelorussian State 
     University, Minsk, CIS (Antonov et al. 1989). A 600 mm illuminated 
     integrating sphere that is calibrated in absolute values of radiance is 
     used for radiometric calibration. A linear relationship between the 
     instrument response and the radiance from the sphere is determined (Green 
     et al. 1991).

     The spectral and polarization features are calibrated using linear 
     polarized light streams of equal intensity. One source is parallel, the 
     other is perpendicular to the input slit. The total error of the system is 
     less than 10 percent (Green et al. 1991). Processing of the spectra 
     includes conversion of digital counts to radiance using equations from the 
     radiometric calibration and the use of a non-linear median filter 
     procedure for noise suppression (Huang 1981). When calculation of 
     reflectance factors are desired, a well-characterized white "milk glass" 
     reflectance standard is used as a target to provide estimates of 
     irradiance.

     The Gemma and SE-590 spectroradiometers were compared under controlled 
     conditions through viewing the laboratory-based 30 cm integrating sphere. 
     At the completion of the flight measurements, the SE-590 and Gemma were  
     dismounted from the helicopter and taken to the laboratory where the 
     integrating sphere was located. The inside of the sphere is coated with 
     barium sulfate and is illuminated by four quartz-halogen lamps that are 
     powered with a regulated power supply. This sphere was used to provide a 
     controlled source of illumination for periodic comparisons of MMRs during 
     FIFE (Markham et al. 1988). Measurements of the different lamp levels 
     were made using the two spectroradiometers by placing each instrument on a 
     pedestal in front of the 12 cm sphere aperture and triggering the devices 
     as the number of lamps were varied. 

     5.2.1  Specifications.

            Observations of the four lamp levels from the laboratory-based 
            portable integrating sphere provided an increase in overall 
            radiance with an increase in lamp levels. The SE-590 spectra showed 
            less noise, while the Gemma data had a noticeable amount of detail 
            that increased with increasing lamp levels. The standard deviation 
            of the SE-590 was small, while the standard deviation for Gemma 
            increased from lamp levels 1 to 3 and then decreased at lamp level 
            4, suggesting that the Gemma had saturated at that light level. The 
            SE-590 uses a procedure to determine an appropriate gain setting 
            for every observation, while the gain setting on Gemma is fixed for 
            the expected range of illumination conditions. For the illuminating 
            sphere lamp comparisons, it was determined later that the radiance 
            level from the integrating sphere lamps would seldom, if ever, be 
            encountered under field conditions. This created problems with 
            Gemma as the gain settings were for field conditions. Some error in 
            comparing the Gemma and SE-590 was also introduced from the 
            different physical configuration of the devices as they sit in the 
            port, as each instrument has a different view into the sphere of 
            which a part is then re-reflected to the sensor.

            5.2.1.1  Tolerance.

                     The sensitivity of Gemma appears to be somewhat higher
                     than that of the SE-590 in the visible wavelengths while
                     the SE-590 appears to provide a signal with lower noise.
                     The SE-590 uses a procedure to determine an appropriate
                     gain setting for a target, while the gain setting on
                     Gemma is fixed for an expected range of field conditions.
                     The differences in sensitivity between the two devices
                     is such that reflectances calculated from the two
                     different devices (using each device for its
                     corresponding irradiance measurement), may be similar
                     as the amplitude differences would cancel each other out.

     5.2.2  Frequency of Calibration.

            At the completion of the flight measurements, the SE-590 and Gemma 
            were dismounted from the helicopter and taken to the laboratory 
            where the integrating sphere was located. This sphere was used to 
            provide a controlled source of illumination for periodic 
            comparisons of MMRs during FIFE (Markham et al. 1988).

     5.2.3  Other Calibration Information.

            Not available at this revision.

                                   6.  PROCEDURE

6.1  Data Acquisition Methods.

     The NASA Bell UH-1B helicopter optical remote sensing system for 1989 
     supported a data acquisition system consisting of a SE-590, MMR, Everest 
     infrared thermometer, Gemma, a color video camera, and one 35 mm flight 
     research camera loaded with color film. Controller units for all the 
     optical devices are rack-mounted inside the helicopter and are wired such 
     that a single switch closure triggers all devices except Gemma, which was 
     operated independently. Coordination of simultaneous triggering of the 
     spectroradiometers was executed by verbal and visual signals between 
     operators. The switch closure also activates an audible tone which is 
     recorded on one of the two audio tracks of a Beta-format video recording 
     system. The other audio track of the VCR was used to record cabin intercom 
     conversations among the helicopter crew. Note that the 35 mm camera and 
     Gemma were secured in a nadir-looking configuration. The video camera was 
     mounted on the pointable platform with the other radiometric instruments. 

6.2  Spatial Characteristics.

     The FIFE study area with areal extent of 15 km by 15 km, is located south 
     of the Tuttle Reservoir and Kansas River, and about 10 km from Manhattan, 
     Kansas, USA. The northwest corner of the area has UTM coordinates of 
     4,334,000 Northing and 705,000 Easting in UTM Zone 14. 

     6.2.1  Spatial Coverage.

            The number and spatial distribution of the sites covered on each  
            mission varied. The purpose of the helicopter mission was to 
            collect data over many of the sites. These data were collected from 
            the 13 locations listed below. The three primary sites 
            (2133-GEM, 4439-GEM, 8739-GEM) were measured on every mission to 
            assure continuity.

            SITEGRID STN NORTHING EASTING  LATITUDE  LONGITUDE ELEV 
            -------- --- -------- -------  --------  --------- ---- 
            1478-BRS 938  4331223  720664  39 06 15  -96 26 53  375 
            1916-BRK 902  4330282  708259  39 05 55  -96 35 30  351 
            1942-BRL 944  4330133  713414  39 05 46  -96 31 56  422 
            2123-SAM 905  4329866  709506  39 05 41  -96 34 39  405 
            2133-ECA 906  4329726  711604  39 05 34  -96 33 12  443 
            2330-BRK 908  4329314  711066  39 05 22  -96 33 35  424 
            2655-BRL 936  4328787  716070  39 05 00  -96 30 07  367 
            3317-BRK 910  4327395  708485  39 04 22  -96 35 24  427 
            4439-ECV 916  4325193  712773  39 03 06  -96 32 28  443 
            6735-BRL 913  4320652  712073  39 00 40  -96 33 03  385 
            6912-BRL 924  4320111  707336  39 00 26  -96 36 20  397 
            8739-ECB 926  4316699  712845  38 58 31  -96 32 35  442 
            XETL-SPH 999  4340743  708712  39 11 34  -96 35 00  325

            SITEGRID SLOPE ASPECT
            -------- ----- ------
            1478-BRS     2 N
            1916-BRK     2 N
            1942-BRL     1 TOP
            2123-SAM     1 TOP
            2133-ECA     1 TOP
            2330-BRK     5 E
            2655-BRL     4 E
            3317-BRK    15 W
            4439-ECV     2 N
            6735-BRL     1 BOTTOM
            6912-BRL     2 N
            8739-ECB     1 TOP
            XETL-SPH 

     6.2.2  Spatial Resolution.

            The focus of the lens system is variable between 80-200 mm yielding 
            a field-of-view between 3.6 x 0.3 and 1.5 x 0.1 degrees. The 
            helicopter collected data at an altitude of 330 m.

6.3  Temporal Characteristics.

     Missions were dependent on the availability of clear sky conditions. Every 
     site was not observed on every flight. 

     6.3.1  Temporal Coverage.

            Missions were dependent on the availability of clear sky 
            conditions. Data were collected on August 4, 8 and 12, 1989.
            Measurements were made between 1400 and 2102 GMT.

     6.3.2  Temporal Resolution.

            Observation time over each site was 2 to 5 minutes during which an 
            average of 20 measurements were made.

                                7. OBSERVATIONS

7.1  Field Notes.

     No atmospheric corrections have been made. 

                           8.  DATA DESCRIPTION

8.1  Table Definition With Comments.

     The SQL definition for this table is found in the GEM_HELO.TDF file found
     on FIFE CD-ROM Volume 1.

8.2 Type of Data.

--------------------------------------------------------------------------------
|                 8.2.1                  |               |          |          |
|Parameter/Variable Name                 |               |          |          |
--------------------------------------------------------------------------------
|    |               8.2.2               |     8.2.3     |  8.2.4   |  8.2.5   |
|    |Parameter/Variable Description     |Range          |Units     |Source    |
--------------------------------------------------------------------------------
|SITEGRID_ID                             |               |          |          |
|    |This is a FIS grid location code.  |               |          |          |
|    |Site grid codes (EESS-III) give    |               |          |          |
|    |the east (EE) and south (SS) cell  |               |          |          |
|    |number in a 100x100 array of 200m  |               |          |          |
|    |square cells.  The last 3          |               |          |          |
|    |characters (III) are an instrument |               |          |          |
|    |identifer.                         |               |          |          |
--------------------------------------------------------------------------------
|STATION_ID                              |               |          |          |
|    |The station ID designating the     |               |          |          |
|    |location of the observations.      |               |          |          |
--------------------------------------------------------------------------------
|OBS_DATE                                |               |          |          |
|    |The date of the observations, in   |               |          |          |
|    |the format (DD-MMM-YY).            |               |          |          |
--------------------------------------------------------------------------------
|OBS_TIME                                |               |          |          |
|    |The start time of the observation  |               |          |          |
|    |in GMT.  The format is (HHMM).     |               |          |          |
--------------------------------------------------------------------------------
|NUM_OBS                                 |               |          |          |
|    |The number of observations         |               |          |          |
|    |averaged together.                 |               |          |          |
--------------------------------------------------------------------------------
|VIEW_AZIM_ANG                           |               |          |          |
|    |The view azimuth angle (With       |               |[degrees f|          |
|    |North=0, East=90).                 |               |rom North]|          |
--------------------------------------------------------------------------------
|VIEW_ZEN_ANG                            |               |          |          |
|    |The view zenith angle of the       |               |[degrees] |          |
|    |observations.  With a nadir view=0 |               |          |          |
--------------------------------------------------------------------------------
|SOLAR_AZIM_ANG                          |               |          |          |
|    |The solar azimuth angle (With      |               |[degrees f|          |
|    |North=0, East=90).                 |               |rom North]|          |
--------------------------------------------------------------------------------
|SOLAR_ZEN_ANG                           |               |          |          |
|    |The solar zenith angle.            |               |[degrees] |          |
--------------------------------------------------------------------------------
|ALTITUDE                                |               |          |          |
|    |The helicopter altitude above      |               |[meters]  |          |
|    |ground level.                      |               |          |          |
--------------------------------------------------------------------------------
|OBS_TYPE                                |               |          |          |
|    |A description of the area          |               |          |          |
|    |observed, FULL is the entire site, |               |          |          |
|    |SRB is the same area as the        |               |          |          |
|    |ground surface radiance            |               |          |          |
|    |observations, WAB is the area      |               |          |          |
|    |upwind of the flux tower, SMT is   |               |          |          |
|    |a transect.                        |               |          |          |
--------------------------------------------------------------------------------
|MISSION_ID                              |               |          |          |
|    |The mission identification for     |               |          |          |
|    |the helicopter flight.             |               |          |          |
--------------------------------------------------------------------------------
|WAVLEN                                  |               |          |          |
|    |The wavelength at which the        |               |[micromete|          |
|    |observation was made.              |               |rs]       |          |
--------------------------------------------------------------------------------
|RADNC                                   |               |          |          |
|    |The average reflected spectral     |               |[Watts][me|          |
|    |radiance.                          |               |ter^-2][st|          |
|    |                                   |               |er^-1][mic|          |
|    |                                   |               |rometer^-1|          |
|    |                                   |               |]         |          |
--------------------------------------------------------------------------------
|RADNC_SDEV                              |               |          |          |
|    |The standard deviation of the      |               |[Watts][me|          |
|    |radiance.                          |               |ter^-2][st|          |
|    |                                   |               |er^-1][mic|          |
|    |                                   |               |rometer^-1|          |
|    |                                   |               |]         |          |
--------------------------------------------------------------------------------
|COMMENTS                                |               |          |          |
|    |The comments provide information   |               |          |          |
|    |on the field-of-view of the        |               |          |          |
|    |GEMMA in meters on the ground.     |               |          |          |
|    |The field of view varies with the  |               |          |          |
|    |use of different optics in the     |               |          |          |
|    |instrument.                        |               |          |          |
--------------------------------------------------------------------------------
|FIFE_DATA_CRTFCN_CODE                   |       *       |          |          |
|    |The FIFE Data Certification Code   |               |          |          |
|    |for the data, in the following     |               |          |          |
|    |format: CPI (Certified by PI),     |               |          |          |
|    |CPI-??? (CPI - questionable data). |               |          |          |
--------------------------------------------------------------------------------
|LAST_REVISION_DATE                      |               |          |          |
|    |The last revision date for the     |               |          |          |
|    |data, in the format (DD-MMM-YY).   |               |          |          |
--------------------------------------------------------------------------------

Footnote:

      * Decode the FIFE_DATA_CRTFCND_CODE field as follows:

        The primary certification codes are:

        EXM - Example or Test data (not for release).
        PRE - Preliminary (unchecked, use at your own risk).
        CPI - Checked by Principal Investigator (reviewed for quality).
        CGR - Checked by a group and reconciled (data comparisons and 
              cross-checks).

        The certification code modifiers are:

        PRE-NFP  - Preliminary - Not for publication, at the request of 
                   investigator.
        CPI-MRG  - PAMS data that are "merged" from two separate receiving 
                   stations to eliminate transmission errors.
        CPI-???  - Investigator thinks data item may be questionable.

8.3  Sample Data Base Data Record.

     SITEGRID_ID STATION_ID OBS_DATE  OBS_TIME NUM_OBS VIEW_AZIM_ANG
     ----------- ---------- --------- -------- ------- -------------
     1478-GEM           938 08-AUG-89     2034      11             0
     1478-GEM           938 08-AUG-89     2034      11             0
     1478-GEM           938 08-AUG-89     2034      11             0
     1478-GEM           938 08-AUG-89     2034      11             0
     
     VIEW_ZEN_ANG SOLAR_AZIM_ANG SOLAR_ZEN_ANG   ALTITUDE OBS_TYPE
     ------------ -------------- ------------- ---------- --------
                0         237.95          35.1        305 FULL
                0         237.95          35.1        305 FULL
                0         237.95          35.1        305 FULL
                0         237.95          35.1        305 FULL
     
     MISSION_ID     WAVLEN      RADNC RADNC_SDEV
     ---------- ---------- ---------- ----------
     890616B          .409      6.346      4.885
     890616B           .41      9.946      3.915
     890616B          .411     10.196      3.964
     890616B          .412      9.127      3.517

     COMMENTS                                 FIFE_DATA_CRTFCN_CODE
     ---------------------------------------- ---------------------
     FOV=19 X 1.5 M                           CPI
     FOV=19 X 1.5 M                           CPI
     FOV=19 X 1.5 M                           CPI
     FOV=19 X 1.5 M                           CPI
     
     LAST_REVISION_DATE
     ------------------
     04-OCT-90
     04-OCT-90
     04-OCT-90
     04-OCT-90 

8.4  Data Format.

     The CD-ROM file format consists of numerical and character fields of 
     varying length separated by commas. The character fields are enclosed with 
     a single apostrophe. There are no spaces between the fields.  Each file 
     begins with five header records.  Header records contain the following 
     information:

     Record 1    Name of this file, its table name, number of records in
                 this file, path and name of the document that describes 
                 the data in this file, and name of principal investigator 
                 for these data.
     Record 2    Path and filename of the previous data set, and path and 
                 filename of the next data set.  (Path and filenames for files 
                 that contain another set of data taken at the same site on 
                 the same day.)
     Record 3    Path and filename of the previous site, and path and filename 
                 of the next site.  (Path and filenames for files of the same 
                 data set taken on the same day for the previous and next 
                 sites (sequentially numbered by SITEGRID_ID)).
     Record 4    Path and filename of the previous date, and path and filename 
                 of the next date.  (Path and filenames for files of the same 
                 data set taken at the same site for the previous and next 
                 date.)
     Record 5    Column names for the data within the file, delimited by 
                 commas.
     Record 6    Data records begin.

     Each field represents one of the attributes listed in the chart in 
     section 8.2 and described in detail in the TDF file (see Section 8.1). 
     These fields are in the same order as in the chart.

8.5  Related Data Sets.

     SE-590 Reflectance Factors and Radiances Measured from a Helicopter.
     This data set contains SE-590 spectrometer reflectances measured in 
     conjunction with the Gemma.

     SE-590 Reflectance Factors and Radiances from UNL.
     This data set contains nadir and off-nadir SE-590 spectrometer 
     reflectances measurements from the University of Nebraska group. 

     SE-590 Spectroradiometer Reflectance Factors from GSFC.
     This data set contains nadir SE-590 spectrometer reflectances measurements 
     from the Elizabeth Middleton at NASA Goddard Space Flight Center. 

     Surface Reflectance Measured with a Helicopter-borne MMR.
     This data set contains site averaged reflected radiance and reflectance 
     values from a Barnes MMR taken from a helicopter. 

     Surface Radiant Temperature Measured with a Helicopter-borne Infrared 
     Thermometer.
     This data set contains data from the Everest Infrared thermometer mounted 
     on the helicopter.

                               9.  DATA MANIPULATIONS

9.1  Formulas.

     9.1.1  Derivation Techniques/Algorithms.

            For a discussion of the Algorithms used to analyze these data
            refer to Markham et al. (1988) and Markham (1989).

9.2  Data Processing Sequence.

     Processing of the spectra includes conversion of digital counts to 
     radiance using equations from the radiometric calibration and the use of a 
     non-linear median filter procedure for noise suppression (Huang 1981).

     9.2.1  Processing Steps and Data Sets.

            See references in Section 9.1.1.

     9.2.2  Processing Changes.

            Not applicable.

9.3  Calculations.

     9.3.1  Special Corrections/Adjustments.

            Not applicable.

9.4  Graphs and Plots.

     None.

                                       10.  ERRORS

10.1  Sources of Error.

      There is some debate on the amount of atmosphere in the pathlength 
      between the helicopter and the surface. Recent inquiries have revealed 
      absolute reflectance differences of up to 1 percent in the visible bands 
      when at-sensor helicopter MMR radiances were corrected for atmospheric 
      path length (of 300 m AGL) and processed for reflectance when using an 
      atmospheric model. This has not been fully investigated and is still 
      under investigation at the time of this writing. 

      The heterogeneity of the study site can also affect the measurements. 
      This has been shown to be a potential problem when comparing airborne 
      radiometric measurements to surface radiometric measurements. 

10.2  Quality Assessment.

      Gemma data were compared with SE-590 and MMR data. Differences between 
      data from the two spectroradiometers can be attributed to several 
      factors: spectral bandwidths, gain/sensitivity, and calibration sources. 
      Greater standard deviations are commonly found in data reported from high 
      spectral resolution systems. Fewer photons reach the sensor during the 
      integration time for each wavelength resulting in a higher noise level. 
      Degradation of the finer resolution Gemma data to that of the MMR 
      provided more comparable values than that of the SE-590 because of 
      reduced integration errors inherent in the use of finer resolution data .

      The sensitivity of Gemma appears to be somewhat higher than that of the
      SE-590 in the visible wavelengths while the SE-590 appears to provide a 
      signal with lower noise.

      10.2.1  Data Validation by Source.

              The spectra from the Gemma and SE-590 spectroradiometers were 
              qualitatively similar and when integrated to broader band 
              channels quantitatively compared well with radiances obtained 
              with the broad band measurements of the well characterized MMR. 
              The sensitivity of Gemma appears to be greater than that of the 
              SE-590 and produces a higher value for a given level of field 
              target radiance. The SE-590 produces a signal containing a lower 
              level of noise and therefore spectra more consistent with data 
              found in the literature.

      10.2.2  Confidence Level/Accuracy Judgment. 

              Not available at this revision.

      10.2.3  Measurement Error for Parameters and Variables. 

              Not available at this revision.

      10.2.4  Additional Quality Assessment Applied. 

              Not available at this revision.

                                 11.  NOTES

11.1  Known Problems With The Data.

      Due to differences in alignment and field-of-view, the Gemma was not 
      viewing exactly the same area as the other instruments on the helicopter. 
      It is assumed that the averaging of several observations has minimized 
      these differences. Precise locations of the observations used to 
      calculate a site average may not coincide with the exact locations of 
      surface-based measurements. 

11.2  Usage Guidance.

      Note that the Gemma data provides radiance values only. The data has not 
      been corrected for the effects of the atmosphere beneath the helicopter.

                                12.  REFERENCES

12.1  Satellite/Instrument/Data Processing Documentation. 

      None available.

12.2  Journal Articles and Study Reports. 

      Antonov, B.S., B.I. Belyaev, A.A. Bogdanov, L.I. Kiselevsky and 
         P.V. Komar. 1989. The metrological complex for spectrophotometric  
         apparatus testing in diapason 0.35-2.5 mcm (in Russian). Proceedings 
         From Statistical Methods and Data Processing Methods for Remote 
         Sensing of the Environment. (Minsk Univ.). pp. 75-76. 
      Green, A.M., E.A. Mikhalenko, S.N. Migalin, B.I. Belyaev, S.A. Kapanik, 
         A.V. Tehumakov. 1991. The ground and helicopter observations. Report 
         by the Russian scientists participating in the FIFE-89 Intensive Field 
         Campaign translated from Russian. Institute of Geography. Russian 
         Academy of Sciences.
      Huang, T.S. (ed.). 1981. Two-Dimensional Digital Signal Processing: 
         VII Transformation and Median Filters. (Berlin, Heidelberg, New York: 
         Springer-Verlag).
      Markham, B.L. 1987. FIFE MMR Calibration Report. GSFC/NASA. 
         Greenbelt, MD 20771.
      Markham, B.L., F.M. Wood, and S.P. Ahmad. 1988. Radiometric calibration 
         of the reflective bands of NS001 Thematic Mapper Simulator (TMS) and 
         Modular Multispectral Radiometers (MMR). Society of Photo-Optical 
         Instrumentation Engineers Recent Advances in Sensors, Radiometers, and 
         Data Processing for Remote Sensing. 924:96-108.
      Markham, B.L. 1989. MMR Calibration data for FIFE 89 and related studies. 
         GSFC/NASA. Greenbelt, MD 20771. 
      Sellers, P.J. and F.G. Hall. 1989. FIFE-89 Experiment Plan. GSFC/NASA. 
         Greenbelt, MD 20771.
      Sellers, P.J., F.G. Hall, D.E. Strebel, R.D. Kelly, S.B. Verma, B.L. 
         Markham, B.L. Blad, D.S. Schimel, J.R. Wang, and E. Kanemasu. 1990. 
         FIFE Interim Report. GSFC/NASA. Greenbelt, MD 20771. 
      Walthall, C.L. 1989. The FIFE Helicopter Mission: Summary. Laboratory 
         for Global Remote Sensing Studies. Univ. of Maryland. College Park, 
         MD.   
      Walthall, C.L. and E.M. Middleton. 1992. Assessing spatial and grasslands
         with the use of a helicopter platform. J. Geophys. Res. FIFE issue (in 
         press).
      Williams, D.L., C.L. Walthall and S.N. Goward, 1984. Collection of in- 
         situ forest canopy spectra using a helicopter: A discussion of 
         methodology and preliminary results. Proced. of 1984 Symp. on Machine 
         Processing of Remotely Sensed Data. Purdue Univ. West Lafayette, 
         Indiana. p. 94-106.

12.3  Archive/DBMS Usage Documentation. 

      The Collected Data of the First ISLSCP Field Experiment is archived at
      the EOS Distributed Active Archive Center (DAAC) at Oak Ridge National
      Laboratory (ORNL), Oak Ridge, Tennessee (Section 13 below).  
      Documentation about using the archive and/or online access to the data 
      at the ORNL DAAC is not available at this revision.

                             13.  DATA ACCESS

13.1  Contacts for Archive/Data Access Information. 

      ORNL DAAC User Services
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      (615) 241-3952

13.2  Archive Identification. 

      EOSDIS Distributed Active Archive Center
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      USA

      Telephone:       (615) 241-3952
      FAX:             (615) 574-4665
      Internet Email:   ornldaac@onrl.gov

13.3  Procedures for Obtaining Data.

      Users may place requests by letter, telephone, electronic mail, FAX, or 
      personal visit. 

13.4  ORNL DAAC Status/Plans. 

      FIFE data will be available from the ORNL DAAC. Please contact the 
      ORNL DAAC User Services Office for the most current information about 
      these data.

                       14.  OUTPUT PRODUCTS AND AVAILABILITY

14.1  Tape Products.

      None.

14.2  Film Products.

      None.

14.3 Other Products.

      The High Spectral Resolution Measurements from the Russian Gemma
      Instrument data are available on FIFE CD-ROM Volume 1. 

                           15.  GLOSSARY OF ACRONYMS

AGL               Above Ground Level
DAAC              Distributed Active Archive Center
EOSDIS            Earth Observing System Data and Information System
FIFE              First ISLSCP Field Experiment
FIS               FIFE Information System
IFC               Intensive Field Campaign
ISLSCP            International Satellite Land Surface Climatolgoy Project
MMR               Modular Multiband Radiometer (8 channel radiometer)
ORNL              Oak Ridge National Laboratory
SE-590            Spectron Engineering 590 spectroradiometer
WAB               Wind Aligned Blob
CIS               Commonwealth of Independant States