1.  TITLE 
 
1.1  Data Set Identification.  
 
     Surface Reflectance Measured with a Helicopter-borne MMR. 
 
1.2  FIS Data Base Table Name.  
 
     MMR_HELO_DATA. 
 
1.3  CD-ROM File Name.  
 
     DATA\SUR_REFL\MMR_HELO\Yyyyy\ydddMULT.MRH

     Where yyyy are the four digits of the century and year (Y1987=1987). Note:
     capital letters indicate fixed values that appear on the CD-ROM exactly as 
     shown here, lower case indicates characters (values) that change for each 
     path and file.

     The format used for the filenames is: ydddMULT.sfx, where y is the last 
     digit of the year (e.g., 7=1987, and 9=1989), and ddd is the day of the 
     year (e.g., 061=sixty-first day in the year). The filename extension 
     (.sfx), identifies the data set content for the file (see Section 8.2) and 
     is equal to .MRH for this data set.
 
 
1.4  Revision Date Of This Document.  
 
     April 26, 1994. 
 
     This document has been reviewed to eliminate technical and editorial
     inaccuracies by the FIFE Information Scientist. Previous versions of this 
     document have been reviewed by the Principal Investigator, the person who
     transmitted the data to FIS, a FIS staff member, or a FIFE scientist 
     generally familiar with the data. It is believed that the document 
     accurately describes the data as collected and as archived on the FIFE
     CD-ROM series.

                         2.  INVESTIGATOR(S) 
 
2.1  Investigator(s) Name And Title.  
 
     Staff Science. 
 
2.2  Title Of Investigation.  
 
     Staff Science Helicopter Data Acquisition Program. 
 
2.3  Contacts (For Data Production Information).  
 
      _______________________________________________________________________
     |              |      Contact 1        |           Contact 2            |
     |______________|_______________________|________________________________|
     |2.3.1 Name    |Charles L. Walthall    |Mr. K. Fred Huemmrich           |
     |2.3.2 Address |Dept. of Geography     |Code 923                        |
     |              |University of Maryland |NASA/Goddard Space Flight Center|
     |      City/St.|College Park, MD       |Greenbelt, MD                   |
     |      Zip Code|20742                  |20771                           |
     |2.3.3 Tel.    |(301) 405-4058         |(301) 286-4862                  |
     |2.3.4 Email   |cw7@umail.umd.edu      |fred@ltpsun.gsfc.nasa.gov       |
     |______________|_______________________|________________________________|

2.4  Requested Form of Acknowledgment. 
 
     The helicopter MMR data was processed by K. Fred Huemmrich of the FIFE 
     Information System. Thanks for collecting the data must also be given to 
     the NASA Helicopter crew: Charles Walthall, mission scientist; William 
     Dykes, pilot; Charles Smith, mechanic and observer; Ed Bohles, mechanic 
     and observer; Richard Huey, photographer; Wayne Dulaney, calibration 
     panel and instrument operator; David Pierce, engineer; Douglas Young, 
     engineer; and to the US Army 82nd Medical Helicopter Unit, Ft. Riley, 
     Kansas, for on-site hanger space and helicopter technical support.
 
                            3.  INTRODUCTION 
 
3.1  Objective/Purpose.  
 
     The FIFE Staff Science effort covered those activities which were 
     community level activities, or which required uniform data collection 
     procedures  across sites and time. Hence, these activities were more 
     appropriate for a  team under the direction of a single scientist who 
     would respond to the needs of the Science Steering Group of the 
     experiment. This included the acquisition of the multispectral radiometer 
     data from FIFE sites using a helicopter platform.  
 
3.2  Summary of Parameters.  
 
     Helicopter-borne MMR radiances and reflectances in the 8 MMR bands.
 
3.3  Discussion.  
 
     The helicopter-borne MMR provides surface reflectance measurements in 
     Landsat-TM bands at low to intermediate altitudes. The helicopter 
     operated during all Intensive Field Campaigns (IFCs) and was 
     available to support all satellite overpasses. During IFC-1 through 
     IFC-4; 11, 10, 16, and 10 'clear day' missions were flown, respectively. 
     The average flight time was 2 hours, during which an average of 11 FIFE 
     sites plus one special target were covered. During IFC-5 10 missions were 
     flown on 6 days in late July and early August 1989.
 
     The helicopter missions were designed to provide 1) a rapid means of
     intensively spectrally characterizing each FIFE site while providing 
     FIFE study area coverage, and 2) to provide an intermediate scale of 
     sampling between that of the surface measurements and the higher altitude 
     aircraft and spacecraft multispectral imaging devices. The MMR 
     instrumentation was chosen to provide compatibility with surface-based 
     radiometers and TM spacecraft sensors. Off-nadir measurements were made 
     as a means of providing more accurate estimates of hemispherical 
     reflectance and for use with bidirectional reflectance models.

                        4.  THEORY OF MEASUREMENTS 
 
Not available at this revision.

                            5.  EQUIPMENT 
 
5.1  Instrument Description.  
 
     The Barnes Modular Multiband Radiometer (MMR) was designed to acquire
     multispectral radiance data over the visible, near infrared, middle 
     infrared and thermal regions of the electromagnetic spectrum. It produces 
     analog voltage responses to scene radiance in 8 spectral bands. Voltages 
     from thermistors attached to the instrument chopper and detectors are 
     recorded to provide a means of compensating for thermal effects on sensor 
     response and for calculation of target surface temperatures.  The 8 bands 
     are approximately 0.45-0.52,0.52-0.60, 0.63-0.69, 0.76-0.90, 1.15-1.30, 
     1.55-1.75, 2.08-2.35, 10.4-12.5 um.  Bands 1-4 have silicon detectors and 
     bands 5-7 have lead sulfide detectors and waveband 8 has a Lithium 
     Tantalum trioxide detector. The MMR's dimensions are 26.4 cm by 20.5 cm 
     by 22.2 cm and the device weighs 6.4 kg.

     5.1.1  Platform.  
 
            The MMR (serial number 117) was mounted on a hinged plate on the 
            nose of a NASA Bell UH-1B "Huey" helicopter. This system was 
            developed for prior experiments over forested areas (Williams et 
            al., 1984).
 
     5.1.2  Mission Objectives. 
 
            There were two type of helicopter optical system missions: H-1a 
            and H-1b. The objective of the H-1a missions was to acquire 
            spectral data at specific FIFE sites coincident with surface, 
            atmospheric and satellite measurements. The objective for the H-1b 
            missions was to acquire multispectral data of as many FIFE sites 
            as possible during the available flight time. All regular FIFE 
            sites were measured from a hover. Some special sites were flown in 
            a slow-flight transect mode.

            The area for observations was a doughnut-like ring around the 
            automated weather stations or over areas where surface radiance 
            and biology measurements were being conducted. The ring around the 
            weather stations was 2-3 times the width of the weather station 
            areas (the instruments were normally bounded by fences). During 
            1989 transects designed to follow the wind-aligned-blob or WABs 
            were flown. 
 
     5.1.3  Key Parameters. 
 
            Reflected radiation, emitted radiation, surface temperature. 
 
     5.1.4  Principles of Operation. 
 
            The MMR is a multi-sensor optical device operating in the visible, 
            near infrared, middle infrared and thermal wavelengths. A 
            mechanical chopper is used and the temperatures of the sensors and 
            the chopper are monitored and stored with each 8-channel 
            observation. Analog voltages from each sensor, detector 
            thermistor, and chopper thermistor are converted to digital 
            numbers and stored in the data logger. 
 
     5.1.5  Instrument Measurement Geometry. 
 
            When mounted on the helicopter the optical head is equipped with 
            lenses having a 1 degree FOV. Given a nominal data acquisition 
            altitude of 300 m, spectral irradiance from the ground surface 
            area of approximately 5 m in  diameter is recorded. Prior to the 
            FIFE mission the instrument pallet was modified to accommodate 
            both nadir and a range (15, 30, 45, 60 degrees) of off-nadir view 
            angles. 

            During 1989 missions a pointable pallet mounted on the side of the 
            helicopter cabin was used. An altitude of 330 m above ground level 
            was used during data collection.
 
     5.1.6  Manufacturer of Instrument. 
 
            Barnes Engineering Company 
            30 Commerce Road 
            Stamford, Connecticut  07904 
            (203) 348-5381 
 
            Note that this instrument was designed and produced to meet NASA
            specifications for a field radiometer in the late 1970s. Since 
            that time the MMR has been considered the industry standard for 
            broad band field measurements. It is currently out of production.

5.2  Calibration.  
 
     With the exception of IFC-1, detector and chopper temperature voltages 
     were recorded on the Omnidata Polycorder. Without these data during IFC-1 
     it is not possible to calculate reflectance in the lead sulfide channels 
     during the period. Calibration of the MMR for absolute radiance and 
     compensation for thermal effects (lead sulfide channels) was carried out 
     by Staff/GSFC. Estimates of irradiance were derived from the use of a 
     separate MMR (serial number 102) located on the surface mounted over a 
     horizontal BaSO4 reflectance panel using a 15 degree field of view lens. 
     During IFC-1 the BaSO4 panel was located near the FIFE headquarters 
     building on the Konza (northwest corner of the study area). Due to 
     concerns raised by FIFE investigators over the influence of diffuse 
     radiation from this location, the panel was moved to site 16(4439-HLM) 
     (centrally located) for the remainder of the FIFE 1987. To minimize any 
     background effects, the MMR was suspended over the panel using an 
     extendible boom mounted on the back of a pick-up truck. The panel itself 
     was placed on a raised platform above the cab of the truck. In addition 
     to use in calculating downwelling irradiance for reflectance  
     calculations, the MMR data from the calibration panel can be used to 
     examine each day for cloudiness. These measurements were corrected for 
     the spectral and non-lambertian characteristics of the panel according to 
     the procedures of Jackson et al., 1983. Reflectance factors were 
     calculated for all but the thermal band by dividing the helicopter-borne 
     MMR target radiances by the corrected reflectance panel radiances. Data 
     consists of means and standard deviations of radiance for each band and 
     means and standard deviations of reflectance and surface temperature by 
     band. Five minute running averages of the reflectance panel data were 
     used to calculate reflectance factors. 

     5.2.1  Specifications. 

            Not available at this revision. 
 
            5.2.1.1  Tolerance. 
 
                     The absolute error in calibration is estimated to be 
                     approximately 5% in wavebands 1-4 and approximately 10% 
                     in wavebands 5-7 (Sellers et al., 1990). The error in the 
                     thermal waveband is + or - 0.5 degrees Centigrade (Markham 
                     1987).
  
    5.2.2  Frequency of Calibration.  
 
           1987:  Pre- and post-season calibrations were supplemented by daily 
           stability checks using a 30 cm integrating sphere (for the first 7 
           wavebands) and an Everest Model 1000 calibration source (for the 
           thermal waveband). The optical and thermal detectors are known to 
           be temperature sensitive. The calibration procedures and specifics 
           can be found in Jackson et al., 1983; Markham 1987; and Markham et 
           al., 1988. BaSO4 measurements were made at one minute intervals 
           beginning 30 minutes prior to the first helicopter mission and 
           ending 30 minutes after the last helicopter mission of the day.
 
    5.2.3  Other Calibration Information.  
 
           The MMR instruments used during FIFE showed good stability over the 
           study period, changing a maximum of 5% between calibrations 
           (Markham et al., 1988). 
 
            Changing the field-of-view will change the gains and offsets but 
            will not change the temperature sensitivity coefficients. 

                          6.  PROCEDURE 
 
6.1  Data Acquisition Methods.  
 
     The NASA Bell UH-1B helicopter optical remote sensing system for 1987
     supported a data acquisition system consisting of a foresighted MMR; a 
     color video camera; and two 35 mm flight research cameras loaded with 
     color film (one with a 1 inch focal length and the other with a 6 inch 
     focal length). Controller units for all the optical devices were rack-
     mounted inside the helicopter and were wired such that a single switch 
     closure triggered all devices. The switch closure also activates an 
     audible tone which was recorded on one of the two audio tracks of a Beta-
     format video recording system. The other audio track of the VCR was used 
     to record cabin intercom conversations among the helicopter crew. If one 
     desires to examine site conditions in greater detail, the higher 
     resolution 35 mm still photography can be reviewed. [Video tapes and 35 mm 
     files are in the permanent FIFE archive]
 
     During the 1987 FIFE campaigns, the radiometric instruments were placed 
     on a moveable mount located on the nose of the helicopter so that the 
     instruments could be pointed nadir or at preselected angles of up to 55 
     degrees off-nadir. Coincident surface-based measurements of the 
     calibrated reference panel were supplemented with occasional data 
     collection from the helicopter instrumentation while hovering over a 
     calibrated 6 m by 6 m canvas panel on the surface.

6.2  Spatial Characteristics. 
 
     The FIFE study area, with areal extent of 15 km by 15 km, is located south 
     of the Tuttle Reservoir and Kansas River, and about 10 km from Manhattan, 
     Kansas, USA. The northwest corner of the area has UTM coordinates of 
     4,334,000 Northing and 705,000 Easting in UTM Zone 14.

     6.2.1  Spatial Coverage. 

            Measurements were scattered throughout the FIFE study area. 
            They were made in the following 32 sitegrids.
 
            SITEGRID  NORTHING  EASTING  LATITUDE  LONGITUDE  ELEV  SLOPE
            --------  -------- -------- ---------  --------- ----- -------
            0847-HLM  4332344   714439  39 06 57  -96 31 11   418   1 TOP
            1246-HLM  4331625   714200  39 06 34  -96 31 22   410  12 S  
            1445-HLM  4331160   714090  39 06 19  -96 31 27   400        
            1478-HLM  4331223   720664  39 06 15  -96 26 53   375   2 N  
            1511-HLM  4331080   707287  39 06 22  -96 36 10              
            1544-HLM  4330975   713795  39 06 13  -96 31 39              
            1916-HLM  4330282   708259  39 05 55  -96 35 30   351   2 N  
            1942-HLM  4330121   713402  39 05 46  -96 31 57   420   1 TOP
            2043-HLM  4330003   713536  39 05 42  -96 31 51   415        
            2123-HLM  4329866   709506  39 05 41  -96 34 39   405   1 TOP
            2132-HLM  4329774   711336  39 05 36  -96 33 23   405        
            2133-HLM  4329706   711577  39 05 34  -96 33 13   443   1 TOP
            2330-HLM  4329314   711066  39 05 22  -96 33 35   424   5 E  
            2516-HLM  4328956   708102  39 05 12  -96 35 38   405        
            2619-HLM  4328874   708868  39 05 09  -96 35 07              
            2655-HLM  4328787   716070  39 05 00  -96 30 07   367   4 E  
            2731-HLM  4328678   711110  39 05 01  -96 33 34   446
            2915-HLM  4328167   708028  39 04 47  -96 35 42   415
            2929-HLM  4328244   710726  39 04 47  -96 33 50   440
            3129-HLM  4327822   710820  39 04 33  -96 33 47   431  14 E  
            3317-HLM  4327395   708485  39 04 22  -96 35 24   427  15 W  
            3414-HLM  4327286   707854  39 04 19  -96 35 51   410
            3479-HLM  4327134   720890  39 04 02  -96 26 49   420
            4268-HLM  4325633   718582  39 03 16  -96 28 26   420   1 TOP
            4439-HLM  4325219   712795  39 03 07  -96 32 27   445   2 N  
            4609-HLM  4324766   706700  39 02 58  -96 36 41   398        
            4631-HLM  4324830   711253  39 02 56  -96 33 32   405        
            6340-HLM  4321500   713000  39 01 07  -96 32 23   410   4 SW 
            6735-HLM  4320652   712073  39 00 40  -96 33 03   385   1 BOTTOM
            6912-HLM  4320178   707307  39 00 29  -96 36 21   385   2 N   
            6943-HLM  4320147   713500  39 00 22  -96 32 04   415        
            8739-HLM  4316699   712845  38 58 31  -96 32 35   442   1 TOP

     6.2.2  Spatial Resolution. 
 
            The ground resolution of the Helicopter MMR is 12.7 square meters 
            at nadir and changed with view-zenith angle. The values in this 
            data set are averaged values over a larger area of 10 to 100 
            square meters.
 
6.3  Temporal Characteristics. 
 
     Missions were dependent on the availability of clear sky conditions. 
     Every site was not observed on every flight. 
 
     6.3.1  Temporal Coverage. 
 
            Helicopter-borne MMR observations were obtained in 1987 and 1989 
            during the FIFE IFCs.

                IFC#              Dates
              -------     -------------------
               IFC-1      05/26/87 - 06/06/87
               IFC-2      06/25/87 - 07/11/87
               IFC-3      08/06/87 - 08/21/87
               IFC-4      10/05/87 - 10/16/87
               IFC-5      07/24/89 - 08/12/89

     6.3.2  Temporal Resolution. 
 
            Observation time over each site was 2 to 5 minutes during which an 
            average of 20 measurements were made (maximum of 150). Only 
            averages of each site visit are reported in the FIFE data set. In 
            general, sites were visited every couple of days.

                           7.  OBSERVATIONS 
 
7.1  Field Notes.  
 
     Special targets include tree stands northeast of the HQ building and east 
     of Highway I-77. Transects for Dr. David Schimel include ones west of 
     site 40, southwest of site 8, east of site 4, and west of site 4.  
     Correction/calibration targets for Dr. Carol Bruegge include the oil spill 
     at site 30/32, bare soil near the HQ building, ponds near site 6, 2 ponds 
     near the road and a tarp in the road west of site 16, and the blacktop at 
     the entrance to site 16.

     Off-nadir data is limited to backscatter measurements, and is limited in
     quantity.  Data quality checks have not been made.

                         8.  DATA DESCRIPTION 
 
8.1  Table Definition With Comments. 

     The SQL definition for this table is found in the MMR_HELO.TDF file found
     on FIFE CD-ROM Volume 1.
 
8.2  Type of Data. 
 
--------------------------------------------------------------------------------
|                 8.2.1                  |               |          |          |
|Parameter/Variable Name                 |               |          |          |
--------------------------------------------------------------------------------
|    |               8.2.2               |     8.2.3     |  8.2.4   |  8.2.5   |
|    |Parameter/Variable Description     |Range          |Units     |Source    |
--------------------------------------------------------------------------------
|SITEGRID_ID                             |               |          |          |
|    |This is a FIS grid location code.  |               |          |          |
|    |Site grid codes (SSEE-III) give    |               |          |          |
|    |the south (SS) and the east (EE)   |               |          |          |
|    |cell number in a 100x100 array of  |               |          |          |
|    |200m square cells.  The last 3     |               |          |          |
|    |characters (III) are an instrument |               |          |          |
--------------------------------------------------------------------------------
|STATION_ID                              |               |          |          |
|    |The station ID designating the     |               |          |          |
|    |location of the observations.      |               |          |          |
--------------------------------------------------------------------------------
|OBS_DATE                                |               |          |          |
|    |The date of the observations, in   |               |          |          |
|    |the format (DD-mmm-YY).            |               |          |          |
--------------------------------------------------------------------------------
|OBS_TIME                                |               |          |          |
|    |The time that the observation was  |               |          |          |
|    |taken in GMT.  The format is       |               |          |          |
|    |(HHMM).                            |               |          |          |
--------------------------------------------------------------------------------
|DURATION                                |               |          |          |
|    |The length of time over which the  |               |[seconds] |          |
|    |observations were made.            |               |          |          |
--------------------------------------------------------------------------------
|MISSION_ID                              |               |          |          |
|    |The FIFE mission id number for     |               |          |          |
|    |this helicopter flight.            |               |          |          |
--------------------------------------------------------------------------------
|OBS_TYPE                                |               |          |          |
|    |This is the area of the site       |               |          |          |
|    |observed.  FULL is the entire site,|               |          |          |
|    |WAB is only the WAB area, UNL      |               |          |          |
|    |is the area where the ground       |               |          |          |
|    |reflectance measurements were      |               |          |          |
|    |made, and PARA is at the Parabola  |               |          |          |
|    |site.                              |               |          |          |
--------------------------------------------------------------------------------
|NUM_OBS                                 |               |          |          |
|    |The number of observations made    |               |          |          |
|    |at the site.                       |               |          |          |
--------------------------------------------------------------------------------
|SOLAR_ZEN_ANG                           |               |          |          |
|    |The solar zenith angle.            |               |[degrees] |          |
--------------------------------------------------------------------------------
|SOLAR_AZIM_ANG                          |               |          |          |
|    |The solar azimuth angle, where     |               |[degrees f|          |
|    |0=north, 90=east, 180=south and    |               |rom North]|          |
|    |270=west.                          |               |          |          |
--------------------------------------------------------------------------------
|VIEW_ZEN_ANG                            |               |          |          |
|    |The view zenith angle.             |               |[degrees] |          |
--------------------------------------------------------------------------------
|VIEW_AZIM_ANG                           |               |          |          |
|    |The view azimuth angle.            |               |[degrees f|          |
|    |                                   |               |rom North]|          |
--------------------------------------------------------------------------------
|HEIGHT_ABV_GRND_LVL                     |               |          |          |
|    |The height of the radiometer       |               |[meters]  |          |
|    |above ground level.                |               |          |          |
--------------------------------------------------------------------------------
|BAND1_RADNC                             |               |          |          |
|    |The average reflected radiance at  |               |[Watts][me|          |
|    |this site from the Barnes MMR      |               |ter^-2][st|          |
|    |channel 1 (.45 - .52 microns).     |               |er^-1][mic|          |
--------------------------------------------------------------------------------
|BAND2_RADNC                             |               |          |          |
|    |The average reflected radiance at  |               |[Watts][me|          |
|    |this site from the Barnes MMR      |               |ter^-2][st|          |
|    |channel 2 (.51 - .60 microns).     |               |er^-1][mic|          |
--------------------------------------------------------------------------------
|BAND3_RADNC                             |               |          |          |
|    |The average reflected radiance at  |               |[Watts][me|          |
|    |this site from the Barnes MMR      |               |ter^-2][st|          |
|    |channel 3 (.63 - .68 microns).     |               |er^-1][mic|          |
--------------------------------------------------------------------------------
|BAND4_RADNC                             |               |          |          |
|    |The average reflected radiance at  |               |[Watts][me|          |
|    |this site from the Barnes MMR      |               |ter^-2][st|          |
|    |channel 4 (.75 - .88 microns).     |               |er^-1][mic|          |
--------------------------------------------------------------------------------
|BAND5_RADNC                             |               |          |          |
|    |The average reflected radiance at  |               |[Watts][me|          |
|    |this site from the Barnes MMR      |               |ter^-2][st|          |
|    |channel 5 (1.17 - 1.33 microns).   |               |er^-1][mic|          |
--------------------------------------------------------------------------------
|BAND6_RADNC                             |               |          |          |
|    |The average reflected radiance at  |               |[Watts][me|          |
|    |this site from the Barnes MMR      |               |ter^-2][st|          |
|    |channel 6 (1.57 - 1.80 microns).   |               |er^-1][mic|          |
--------------------------------------------------------------------------------
|BAND7_RADNC                             |               |          |          |
|    |The average reflected radiance at  |               |[Watts][me|          |
|    |this site from the Barnes MMR      |               |ter^-2][st|          |
|    |channel 7 (2.08 - 2.37 microns).   |               |er^-1][mic|          |
--------------------------------------------------------------------------------
|BAND8_RADNC                             |               |          |          |
|    |The average reflected radiance at  |               |[Watts][me|          |
|    |this site from the Barnes MMR      |               |ter^-2][st|          |
|    |channel 8 (10.4 -12.3 microns).    |               |er^-1][mic|          |
--------------------------------------------------------------------------------
|TARGET_TEMP                             |               |          |          |
|    |The average radiant temperature    |               |[degrees C|          |
|    |of the site.                       |               |elsius]   |          |
--------------------------------------------------------------------------------
|CHOPPER_TEMP                            |               |          |          |
|    |The average radiometer chopper     |               |[degrees C|          |
|    |temperature.                       |               |elsius]   |          |
--------------------------------------------------------------------------------
|DETECTOR_TEMP                           |               |          |          |
|    |The average temperature of the     |               |[degrees C|          |
|    |detector.                          |               |elsius]   |          |
--------------------------------------------------------------------------------
|BAND1_REFL                              |               |          |          |
|    |The average reflectance factor at  |               |[percent] |          |
|    |this site for the Barnes MMR       |               |          |          |
|    |channel 1 (.45 - .52 microns).     |               |          |          |
--------------------------------------------------------------------------------
|BAND2_REFL                              |               |          |          |
|    |The average reflectance factor at  |               |[percent] |          |
|    |this site for the Barnes MMR       |               |          |          |
|    |channel 2 (.51 - .60 microns).     |               |          |          |
--------------------------------------------------------------------------------
|BAND3_REFL                              |               |          |          |
|    |The average reflectance factor at  |               |[percent] |          |
|    |this site for the Barnes MMR       |               |          |          |
|    |channel 3 (.63 - .68 microns).     |               |          |          |
--------------------------------------------------------------------------------
|BAND4_REFL                              |               |          |          |
|    |The average reflectance factor at  |               |[percent] |          |
|    |this site for the Barnes MMR       |               |          |          |
|    |channel 4 (.75 - .88 microns).     |               |          |          |
--------------------------------------------------------------------------------
|BAND5_REFL                              |               |          |          |
|    |The average reflectance factor at  |               |[percent] |          |
|    |this site for the Barnes MMR       |               |          |          |
|    |channel 5 (1.17 - 1.33 microns).   |               |          |          |
--------------------------------------------------------------------------------
|BAND6_REFL                              |               |          |          |
|    |The average reflectance factor at  |               |[percent] |          |
|    |this site for the Barnes MMR       |               |          |          |
|    |channel 6 (1.57 - 1.80 microns).   |               |          |          |
--------------------------------------------------------------------------------
|BAND7_REFL                              |               |          |          |
|    |The average reflectance factor at  |               |[percent] |          |
|    |this site for the Barnes MMR       |               |          |          |
|    |channel 7 (2.08 - 2.37 microns).   |               |          |          |
--------------------------------------------------------------------------------
|BAND1_RADNC_SDEV                        |               |          |          |
|    |The standard deviation of the      |               |[percent] |          |
|    |reflected radiances (expressed as  |               |          |          |
|    |percent of the mean) for MMR       |               |          |          |
|    |channel 1 (.45 - .52 microns).     |               |          |          |
--------------------------------------------------------------------------------
|BAND2_RADNC_SDEV                        |               |          |          |
|    |The standard deviation of the      |               |[percent] |          |
|    |reflected radiances (expressed as  |               |          |          |
|    |percent of the mean) for MMR       |               |          |          |
|    |channel 2 (.51 - .60 microns).     |               |          |          |
--------------------------------------------------------------------------------
|BAND3_RADNC_SDEV                        |               |          |          |
|    |The standard deviation of the      |               |[percent] |          |
|    |reflected radiances (expressed as  |               |          |          |
|    |percent of the mean) for MMR       |               |          |          |
|    |channel 3 (.63 - .68 microns).     |               |          |          |
--------------------------------------------------------------------------------
|BAND4_RADNC_SDEV                        |               |          |          |
|    |The standard deviation of the      |               |[percent] |          |
|    |reflected radiances (expressed as  |               |          |          |
|    |percent of the mean) for MMR       |               |          |          |
|    |channel 4 (.75 - .88 microns).     |               |          |          |
--------------------------------------------------------------------------------
|BAND5_RADNC_SDEV                        |               |          |          |
|    |The standard deviation of the      |               |[percent] |          |
|    |reflected radiances (expressed as  |               |          |          |
|    |percent of the mean) for MMR       |               |          |          |
|    |channel 5 (1.17 - 1.33 microns).   |               |          |          |
--------------------------------------------------------------------------------
|BAND6_RADNC_SDEV                        |               |          |          |
|    |The standard deviation of the      |               |[percent] |          |
|    |reflected radiances (expressed as  |               |          |          |
|    |percent of the mean) for MMR       |               |          |          |
|    |channel 6 (1.57 - 1.80 microns).   |               |          |          |
--------------------------------------------------------------------------------
|BAND7_RADNC_SDEV                        |               |          |          |
|    |The standard deviation of the      |               |[percent] |          |
|    |reflected radiances (expressed as  |               |          |          |
|    |percent of the mean) for MMR       |               |          |          |
|    |channel 7 (2.08 - 2.37 microns).   |               |          |          |
--------------------------------------------------------------------------------
|BAND8_RADNC_SDEV                        |               |          |          |
|    |The standard deviation of the      |               |[percent] |          |
|    |reflected radiances (expressed as  |               |          |          |
|    |percent of the mean) for MMR       |               |          |          |
|    |channel 8 (10.4 -12.3 microns).    |               |          |          |
--------------------------------------------------------------------------------
|TARGET_TEMP_SDEV                        |               |          |          |
|    |The standard deviation of the      |               |[percent] |          |
|    |radiant temperatures (expressed as |               |          |          |
|    |percent of the mean) of the site.  |               |          |          |
--------------------------------------------------------------------------------
|CHOPPER_TEMP_SDEV                       |               |          |          |
|    |The standard deviation of the      |               |[percent] |          |
|    |radiometer chopper temperatures    |               |          |          |
|    |(expressed as percent of the mean).|               |          |          |
--------------------------------------------------------------------------------
|DETECTOR_TEMP_SDEV                      |               |          |          |
|    |The standard deviation of the      |               |[percent] |          |
|    |detector temperatures (expressed   |               |          |          |
|    |as percent of the mean).           |               |          |          |
--------------------------------------------------------------------------------
|BAND1_REFL_ATM_COR                      |               |          |          |
|    |The atmospherically corrected      |               |[percent] |          |
|    |reflectance at this site for the   |               |          |          |
|    |Barnes MMR channel 1 (.45 - .52    |               |          |          |
|    |microns).                          |               |          |          |
--------------------------------------------------------------------------------
|BAND2_REFL_ATM_COR                      |               |          |          |
|    |The atmospherically corrected      |               |[percent] |          |
|    |reflectance at this site for the   |               |          |          |
|    |Barnes MMR channel 2 (.51 - .60    |               |          |          |
|    |microns).                          |               |          |          |
--------------------------------------------------------------------------------
|BAND3_REFL_ATM_COR                      |               |          |          |
|    |The atmospherically corrected      |               |[percent] |          |
|    |reflectance at this site for the   |               |          |          |
|    |Barnes MMR channel 3 (.63 - .68    |               |          |          |
|    |microns).                          |               |          |          |
--------------------------------------------------------------------------------
|BAND4_REFL_ATM_COR                      |               |          |          |
|    |The atmospherically corrected      |               |[percent] |          |
|    |reflectance at this site for the   |               |          |          |
|    |Barnes MMR channel 4 (.75 - .88    |               |          |          |
|    |microns).                          |               |          |          |
--------------------------------------------------------------------------------
|BAND5_REFL_ATM_COR                      |               |          |          |
|    |The atmospherically corrected      |               |[percent] |          |
|    |reflectance at this site for the   |               |          |          |
|    |Barnes MMR channel 5 (1.17 - 1.33  |               |          |          |
|    |microns).                          |               |          |          |
--------------------------------------------------------------------------------
|BAND6_REFL_ATM_COR                      |               |          |          |
|    |The atmospherically corrected      |               |[percent] |          |
|    |reflectance at this site for the   |               |          |          |
|    |Barnes MMR channel 6 (1.57 - 1.80  |               |          |          |
|    |microns).                          |               |          |          |
--------------------------------------------------------------------------------
|BAND7_REFL_ATM_COR                      |               |          |          |
|    |The atmospherically corrected      |               |[percent] |          |
|    |reflectance at this site for the   |               |          |          |
|    |Barnes MMR channel 7 (2.08 - 2.37  |               |          |          |
|    |microns).                          |               |          |          |
--------------------------------------------------------------------------------
|DATASET_ID                              |               |          |          |
|    |This field contains an             |               |          |          |
|    |identification code for this group |               |          |          |
|    |of data to link it to other        |               |          |          |
|    |information in the inventory table.|               |          |          |
--------------------------------------------------------------------------------
|FIFE_DATA_CRTFCN_CODE                   |       *       |          |          |
|    |The FIFE Certification Code for    |               |          |          |
|    |the data, in the following format: |               |          |          |
|    |CPI (Certified by PI), CPI-???     |               |          |          |
|    |(CPI - questionable data).         |               |          |          |
--------------------------------------------------------------------------------
|LAST_REVISION_DATE                      |               |          |          |
|    |The last revision date for the     |               |          |          |
|    |data, in the format (DD-mmm-YY).   |               |          |          |
--------------------------------------------------------------------------------

Footnote:

    * Valid levels 

      The primary certification codes are:

      EXM - Example or Test data (not for release)
      PRE - Preliminary (unchecked, use at your own risk)
      CPI - Checked by Principal Investigator (reviewed for quality)
      CGR - Checked by a group and reconciled (data comparisons and 
            cross checks)

      The certification code modifiers are:

      PRE-NFP  - Preliminary - Not for publication, at the request of 
                 investigator.
      CPI-MRG  - PAMS data that is "merged" from two separate receiving 
                 stations to eliminate transmission errors.
      CPI-???  - Investigator thinks data item may be questionable.

8.3  Sample Data Base Data Record.  

     SITEGRID_ID STATION_ID OBS_DATE   OBS_TIME DURATION MISSION_ID OBS_TYPE
     ----------- ---------- ---------- -------- -------- ---------- --------
     0847-HLM            29 06-JUN-87      1641      161 870412A    FULL
     1445-HLM            42 06-JUN-87      1645      105 870412A    FULL
     2043-HLM            44 06-JUN-87      1654      108 870412A    FULL
     2655-HLM            36 06-JUN-87      1650      121 870412A    FULL
     
     NUM_OBS SOLAR_ZEN_ANG SOLAR_AZIM_ANG VIEW_ZEN_ANG VIEW_AZIM_ANG
     ------- ------------- -------------- ------------ -------------
          40        27.400        119.210         .000          .000
          41        26.660        120.740         .000          .000
          40        25.280        123.860         .000          .000
          40        25.940        122.330         .000          .000
     
     HEIGHT_ABV_GRND_LVL BAND1_RADNC BAND2_RADNC BAND3_RADNC BAND4_RADNC
     ------------------- ----------- ----------- ----------- -----------
                     229       22.81       32.82       26.47       90.33
                     229       18.24       28.23       18.15      100.52
                     229       21.37       31.55       23.18       94.60
                     229       22.87       33.27       26.44       89.29

     BAND5_RADNC BAND6_RADNC BAND7_RADNC BAND8_RADNC TARGET_TEMP CHOPPER_TEMP
     ----------- ----------- ----------- ----------- ----------- ------------
           39.46       14.29       2.618      10.009      31.724       22.998
           37.77       11.21       1.680       9.719      29.635       23.046
           38.73       12.95       2.261      10.027      31.842       22.983
           40.48       14.85       2.779      10.235      33.331       22.975
     
     DETECTOR_TEMP BAND1_REFL BAND2_REFL BAND3_REFL BAND4_REFL BAND5_REFL
     ------------- ---------- ---------- ---------- ---------- ----------
            24.960       5.65       7.35       6.79      32.28      -9.99
            24.436       4.49       6.28       4.63      35.73      -9.99
            24.273       5.18       6.91       5.82      33.15      -9.99
            24.263       5.58       7.33       6.68      31.47      -9.99
     
     BAND6_REFL BAND7_REFL BAND1_RADNC_SDEV BAND2_RADNC_SDEV BAND3_RADNC_SDEV
     ---------- ---------- ---------------- ---------------- ----------------
          -9.99      -9.99            11.40             9.38            17.26
          -9.99      -9.99             6.77             5.46            10.40
          -9.99      -9.99             4.50             3.70             6.60
          -9.99      -9.99             2.78             2.19             3.15
     
     BAND4_RADNC_SDEV BAND5_RADNC_SDEV BAND6_RADNC_SDEV BAND7_RADNC_SDEV
     ---------------- ---------------- ---------------- ----------------
                 2.72             3.60             6.48             8.51
                 5.64             3.12             3.68             6.66
                 8.88             3.31             3.34             7.83
                 2.91             1.36             1.96             3.78
     
     BAND8_RADNC_SDEV TARGET_TEMP_SDEV CHOPPER_TEMP_SDEV DETECTOR_TEMP_SDEV
     ---------------- ---------------- ----------------- ------------------
                 1.03             2.32               .13                .83
                  .92             2.20              1.75                .19
                 2.19             4.93               .06                .04
                 1.04             2.25              1.65                .12
     
     BAND1_REFL_ATM_COR BAND2_REFL_ATM_COR BAND3_REFL_ATM_COR
     ------------------ ------------------ ------------------
                   4.51               7.08               6.63
                   3.53               6.02               4.47
                   4.11               6.66               5.68
                   4.45               7.07               6.54
     
     BAND4_REFL_ATM_COR BAND5_REFL_ATM_COR BAND6_REFL_ATM_COR
     ------------------ ------------------ ------------------
                  34.35                                 28.58
                  37.91                                 22.25
                  35.24                                 25.36
                  33.48                                 29.27
     
     BAND7_REFL_ATM_COR DATASET_ID       FIFE_DATA_CRTFCN_CODE 
     ------------------ ---------------- --------------------- 
                  15.62 HEL157A          CPI                   
                   9.94 HEL157A          CPI                   
                  13.20 HEL157A          CPI                   
                  16.34 HEL157A          CPI                   


     LAST_REVISION_DATE
     ------------------
     20-SEP-88
     20-SEP-88
     20-SEP-88
     20-SEP-88
 
8.4  Data Format. 
 
     The CD-ROM file format consists of numerical and character fields of 
     varying length separated by commas. The character fields are enclosed with 
     a single apostrophe. There are no spaces between the fields.  Each file 
     begins with five header records.  Header records contain the following 
     information:

     Record 1    Name of this file, its table name, number of records in
                 this file, path and name of the document that describes 
                 the data in this file, and name of principal investigator 
                 for these data.
     Record 2    Path and filename of the previous data set, and path and 
                 filename of the next data set. (Path and filenames for files 
                 that contain another set of data taken at the same site on 
                 the same day.)
     Record 3    Path and filename of the previous site, and path and filename 
                 of the next site. (Path and filenames for files of the same 
                 data set taken on the same day for the previous and next 
                 sites (sequentially numbered by SITEGRID_ID)).
     Record 4    Path and filename of the previous date, and path and filename 
                 of the next date. (Path and filenames for files of the same 
                 data set taken at the same site for the previous and next 
                 date.)
     Record 5    Column names for the data within the file, delimited by 
                 commas.
     Record 6    Data records begin.

     Each field represents one of the attributes listed in the chart in 
     Section 8.2 and described in detail in the TDF file (see Section 8.1). 
     These fields are in the same order as in the chart.
 
8.5  Related Data Sets. 

     Surface Reflectance Measured with Mast-borne MMR.
     Leaf Optical Properties from UNL.
     SE590 Spectroradiometer Reflectance Factors from GSFC.
     SE590 Reflectance Factors and Radiances from UNL.
     SE590 Reflectance Factors and Radiances Measured from a Helicopter (1989).
     SE590 Leaf Level Spectral Observations from GSFC.
     Surface Temperatures from UNL.
     Surface Temperature Measured with a Helicopter-borne Infrared Thermometer 
        (1989 only).
     Vegetation Species and Cover Abundance.
     Vegetation Species Reference.
     Biophysical Properties of Vegetation.

     Color 35 mm aerial photographs and video records were made during 1987 MMR 
     data collection. The video record includes helicopter crew cabin intercom
     conversations and an audible tone that was initiated each time the MMR 
     was triggered.
  
     Surface-based MMR measurements collected by the University of Nebraska 
     were frequently obtained coincident with helicopter MMR data collection 
     from the same site. 

     During 1989 only a video record was made during the helicopter missions 
     (i.e., no photographs were taken).
 
                        9.  DATA MANIPULATIONS 
 
9.1  Formulas. 

     See references in Section 9.2.1.

     9.1.1  Derivation Techniques/Algorithms. 

            See Section 9.2.1.

9.2  Data Processing Sequence. 

     9.2.1  Processing Steps and Data Sets. 

            An MMR was mounted to continually view a Barium Sulfate panel (the 
            Kansas State University #3 panel in 1987 and the University of 
            Nebraska at Lincoln #2 panel in 1989). A measurement was 
            automatically collected every minute during the helicopter 
            flights. In the data processing the MMR voltage values from both 
            the helicopter and calibration panel site were corrected to 
            radiances. If detector voltages were recorded then the detector 
            temperature (Td) was determined from the channel 10 voltage (V10)

            Td = (LOG(V10)-1.9316)/(-.04446).                           (1)

            For each channel (k) the voltage (Vk) is adjusted for temperature 
            effects

            V'k = ((Ck+Tc)/(Ck+Td))*Vk                                  (2)

            where V'k is the adjusted voltage for channel k, Ck is the 
            temperature adjustment coefficient for channel k, and Tc is the 
            calibration temperture.  The radiance for channel k (Rk) in [Watts] 
            [m^-2][sr^-1][micron^-1] is calculated using the calibration gains 
            (Gk) and offsets (Ok): 

            Rk = ((V'k-Ok)/Gk)*100.                                      (3)

            If the detector temperature was not available the voltage (Vk) was 
            used in equation 3 instead of the temperature adjusted voltage 
            (V'k).

            Calibration coefficients for channels 1 through 7 were determined 
            using the Goddard Space Flight Center calibration hemisphere and 
            thermal calibration from the United States Department of 
            Agriculture at Phoenix.

            MMR SN #102 with a 15 degree field-of-view lens (this MMR was used 
            for the calibration panel observations):

            Optical calibration done July 1987, thermal calibration done May 
            1987

                k       Gk       Ok         Ck
               ---  --------  -------   ----------  
                1     .6730   -.0027       558
                2     .7030   -.0069       2280
                3     .7560   -.0124       -805
                4    1.033    -.0217        388
                5    2.122    -.0083        -68.7
                6    4.524    -.0081        -67.7
                7   13.416    -.0239        -61.3

            Calibration temperature (Tc) = 25.8 degrees Centigrade

            Temperature calibration parameters:

              Ac     Bc     Ka          Kb           Aa            Ab
            .2332  14.98  3.9767e-04  1.14575e-06  -7.91868e-04  -3.08147e-06

            MMR SN #102 with a 15 degree field-of-view lens 
            Optical calibration done December 1987, thermal calibration done 
            November 1987

                k        Gk       Ok          Ck
               ---   --------   -------    ---------
                1       .6590   -.0024        558
                2       .6920   -.0070       2280
                3       .7430   -.0134       -805
                4      1.009    -.0185        388
                5      2.133    -.0110        -68.7
                6      4.718    -.0072        -67.7
                7      14.121   -.0269        -61.3

            Calibration temperature (Tc) = 25.8 degrees Centigrade

            Temperature calibration parameters:

              Ac     Bc     Ka          Kb           Aa            Ab
            .1780  14.39  3.9741e-04  1.2111e-06  -8.1345e-04  -2.3683e-06

            MMR SN #117 with a 1 degree field-of-view lens (this MMR was used 
            on the helicopter):

            Optical calibration done December 1987, thermal calibration done 
            November 1987

                k        Gk        Ok          Ck
               ---   ---------  -------    ---------
                1       .617    -.0054       4370
                2       .6560   -.0081        872
                3       .7100   -.0122      -1073
                4       .9450   -.0177        382
                5      2.615     .0263        -72.7
                6      5.437     .0300        -84.0
                7     15.407    -.0069        -70.4

            Calibration temperature (Tc) = 25.8 degrees Centigrade

            Temperature calibration parameters:

              Ac     Bc     Ka           Kb            Aa             Ab
            .1433  14.25  3.87660E-04  1.52420E-06  -7.515800E-04  -2.5883E-06

            MMR SN #117 with a 1 degree field-of-view lens
            Optical calibration done May 1989, thermal calibration done June 
            1989

                k         Gk       Ok         Ck
               ---    --------  -------    --------
                1       .563    -.0032       1175
                2       .644    -.0037       1196
                3       .685    -.0046      -1217
                4       .927    -.0065        356
                5      2.418     .0484        -71.9
                6      4.858     .0523        -85.0
                7     14.167     .0250        -69.6

            Calibration temperature (Tc) = 28.5 degrees Centigrade

            Temperature calibration parameters:

              Ac     Bc     Ka           Kb            Aa             Ab
            .1975  14.76  3.96060e-04  1.25000e-06  -7.35310e-04   -3.5036e-06

            The calibration panel radiances were then corrected for the 
            anisotropy of the calibration panel

            R'k = Rk/(A1k + A2k*SZA + A3k*SZA^2 + A4k*SZA^3)           (4)

            Where R'k is the radiance for channel k corrected or the 
            anisotropy of the calibration panel; A1k, A2k, A3k, and A4k are 
            the coefficients for channel k for a specific panel, and SZA is 
            the solar zenith angle.

            Kansas State University #3 panel coefficients (this panel was used 
            in 1987)

                k      A1          A2            A3            A4
               --- --------  ------------  -------------  -------------
                1  .9290196  2.306627e-04  -4.65592e-05   2.59352e-07
                2  .9195879  5.812958e-04  -5.164272e-05  2.977609e-07
                3  .911211   5.37265e-04   -4.971094e-05  2.935253e-07
                4  .9055673  3.424218e-04  -3.873801e-05  1.908786e-07
                5  .8883391  2.91882e-04   -2.947789e-05  1.204603e-07
                6  .8733857  6.246419e-04  -3.213795e-05  1.273971e-07
                7  .8247155  1.075296e-03  -3.702393e-05  1.485077e-07

            University of Nebraska at Lincoln #2 panel coefficients (this 
            panel was used in 1989)

                k      A1          A2            A3            A4
               --- ---------  -------------  ------------  -------------
                1  1.024066   -7.996049e-04  5.068796e-06  -3.423062e-07
                2  1.022361   -8.242803e-04  1.107736e-05  -4.046916e-07
                3  1.028746   -1.375718e-03  2.305963e-05  -4.769363e-07
                4  1.027821   -1.352304e-03  2.514470e-05  -4.980858e-07
                5  1.017411   -2.097449e-03  4.728492e-05  -6.302641e-07
                6   .9879391  -1.605808e-03  3.859259e-05  -5.455406e-07
                7   .9251772  -1.235733e-03  3.302859e-05  -4.998493e-07

            The corrected radiance values are described in the MMR Calibration
            document on FIFE CD-ROM Volume 1.

            Radiance values from the helicopter MMR were calculated from 
            voltages the same way as the calibration panel MMR radiances were
            determined, by using equations 1 through 3 and the coefficients 
            for instrument #117. To calculate reflectance factors for bands 1
            through 7 the helicopter and calibration panel radiances must be 
            combined. First, the calibration panel radiances were smoothed 
            using a five minute running average and the data were visually 
            examined to detect the presence of clouds. Intermittent clouds 
            caused noticeable fluctuations in the calibration panel radiance 
            data and these data were removed. The smoothed calibration panel 
            radiances were matched by times and the reflectance factor for 
            channel k (Rflk) were calculated

            Rflk = (Rhk/Rpk)*100.                                      (5)

            Where Rhk is the radiance from the helicopter for channel k, Rpk 
            is the radiance from the calibration panel for channel k, and the 
            factor of 100 is to express the reflectance factor as a percent.

            The radiant temperature of the site was calculated from the 
            helicopter MMR channel 8 radiance and the instrument temperature.  
            The instrument temperature (Ti) was determined using the channel 9 
            voltage (V9) and the temperature calibration parameters Ac and Bc 
            and the instrument temperature was used to calculate the 
            instrument radiance (Ri):

            Ti = (V9-Ac)*Bc.                                           (6)
            Ri =.11927/(EXP(1278.88/(Ti + 273)) -1).                   (7)

            The radiance from the ground (Rg) was calculated from the 
            instrument temperature and radiance, the channel 8 voltage (V8) 
            and the temperature calibration parameters Ka, Kb, Aa, and Ab

            Rg = Ri + (Ka+Kb*Ti)*V8 + (Aa+Ab*Ti)                        (8)


            The ground radiance was expressed as a radiant temperature (Tg) 
            using the Stephan-Boltzmann equation


            Tg = 1278.88/LOG(.11927/Rg+1)-273.                          (9)

            Finally, the individual radiance, reflectance, and temperature 
            values were grouped for each site overpass and an average and 
            standard deviation were calculated. The standard deviation was 
            expressed as a percent of the mean. Also in that grouping the 
            duration of the site overpass and the midpoint time were 
            determined.

     9.2.2  Processing Changes. 
 
            Not applicable. 
 
9.3  Calculations. 
 
     9.3.1  Special Corrections/Adjustments. 
 
            Not applicable. 
 
9.4  Graphs and Plots. 
 
     None. 
                                10.  ERRORS 
 
10.1  Sources of Error. 
 
      Errors associated with the measurements can occur due to orientation of 
      the MMR. The angle of attack of the helicopter varies during flight. The 
      motion of the helicopter cabin beneath the main rotor blades is 
      analogous to a pendulum swinging. "Swings" resulting in off-nadir views 
      up to 8 degrees off-nadir are possible. There has been no quantitative 
      inquiry into this effect as only very small (estimated at 1 to 2 
      degrees) off-nadir-induced errors have been estimated in extreme cases. 
      The instrument operator can normally wait for this motion to stop or can 
      anticipate the position of the helicopter before triggering the 
      instruments. The helicopter roll, pitch and yaw are dependent on 
      atmospheric conditions, engine performance and aircrew fatigue. Off-
      nadir observations are especially questionable under less-than-optimal 
      atmospheric conditions.

      The shadowing caused by the MMR and the helicopter in measuring the "hot 
      spot" area is another source of error. Variable cloud cover could be an 
      error source with reflectance factors since the incoming radiation 
      measurements were not made simultaneously with the surface measurements. 
      Differences in irradiance between the reference panel location and the 
      site being measured are an additional source of error (spatial 
      distribution of atmospheric properties affecting irradiance).

      There is also some debate on the amount of atmosphere in the pathlength
      between the helicopter and the surface. This has not been resolved and 
      is under investigation at the time of this writing.

10.2  Quality Assessment. 
 
      10.2.1  Data Validation by Source. 
 
              Comparisons have been made with Surface Reflectances Measured by   
              the PARABOLA, Surface Reflectances Measured with Mast-borne MMR
              and SE590 measurements (e.g., SE590 Spectroradiometer Reflectance 
              Factors from GSFC, SE590 Reflectance Factor and Radiances 
              Measured from a Helicopter, etc.). Plots of all helicopter MMR 
              observations used in calculations of site averages have been made 
              and examined for selected cases. The video tapes for these 
              flights were reviewed as well. No obvious errors were detected.
 
      10.2.2  Confidence Level/Accuracy Judgment. 
 
              On days with variable cloud conditions the data should be used 
              with caution. The AMS incoming solar radiation data at the site 
              or nearby site should be consulted. On clear days the 
              measurements fall within the precision of the instrument and 
              errors that were discussed in previous sections. 
 
      10.2.3  Measurement Error for Parameters and Variables. 
 
              Not provided by the Principal Investigator. 
 
      10.2.4  Additional Quality Assessment Applied. 
 
              FIS staff applied a general QA procedure to the data to identify 
              inconsistencies and problems for potential users. As a general 
              procedure, the FIS QA consisted of examining the maximum, 
              minimum, average, and standard deviation for each numerical 
              field in the data table. Inconsistencies and problems found in 
              the QA check are described is Section 11.1 (Known Problems With 
              The Data).

                          11.  NOTES

11.1  Known problems With the Data.

      Actual locations of the observations used to calculate a site average 
      may not coincide exactly with locations of surface-based radiance 
      measurements.
 
11.2  Usage Guidance. 
 
      Before using reflectance factors the incoming radiation from the AMS 
      station at the site or nearby site should be checked for possible cloud-
      induced error in reflectance factors. 
 
11.3  Other Relevant Information.

      Not available at this revision.

                           12.  REFERENCES 
 
12.1  Satellite/Instrument/Data Processing Documentation.  
 
      Barnes Engineering. 1982. Calibration and data book: Multispectral 8- 
         channel radiometer. Barnes Engineering Company. Stamford, CT. 
      Jackson, R.D., D.A. Dusek, and E.E. Ezra. 1983. Calibration of the 
         thermal channel on four Barnes model 12-1000 multi-modular 
         radiometers. U.S. Water Conservation Laboratory Report 12. Phoenix, 
         Arizona. 
      Jackson, R.D., S.M. Moran, P.N. Slater, and S.F. Biggar. 1987. Field 
         calibration of reference reflectance panels. Remote Sensing of 
         Environment. 17:103-108. 
      Markham, B.L. 1987. Memo on review of Phoenix calibration of MMR Channel  
         8. GSFC/NASA, Greenbelt, MD  20771. 
      Markham, B.L. 1987. FIFE MMR Calibration Report. GSFC/NASA, Greenbelt, 
         MD 20771. 
      Markham, B.L. 1989. MMR Calibration data for FIFE 89 and related 
         studies. GSFC/NASA, Greenbelt, MD  20771. 
      Robinson, B.F., M.E. Bauer, D.P. DeWitt, L.F. Silva and V.C. Vanderbilt.
         1979. Multiband radiometer for field research.  Measurements of 
         Optical Radiation. Proceedings of the Society of Photo-Optical 
         Instrumentation Engineers. 196:8-15.
      Robinson, B.F., and L.L. Biehl. 1979. Calibration procedures for 
         measurement of reflectance factor in remote sensing field research. 
         Measurements of Optical Radiation. Proceedings of the Society of 
         Photo-Optical Instrumentation Engineers. 196:16-26.

12.2  Journal Articles and Study Reports.  
 
      Bauer, M.E., B.F. Robinson, C. Daughtry, and L.L. Biehl. 1981. Field
         Measurement Workshop. Oct. 14-16, Laboratory for application of 
         Remote Sensing. Purdue University. Lafayette, Indiana.
      Blad, B.L., E.A. Walter Shea, C.J. Hays, and M.A. Mesarch. 1990. 
         Calibration of field reference panel and radiometers used in FIFE 
         1989. AgMet Progress Report 90-3. Department of Agricultural 
         Meteorology. Univ. of Nebraska-Lincoln. Lincoln, Nebraska. 68583-
         0728. 
      Markham, B.L., F.M. Wood, and S.P. Ahmad. 1988. Radiometric calibration  
         of the reflective bands of NS001 Thematic Mapper Simulator (TMS) and 
         Modular Multispectral Radiometers (MMR). Society of Photo-Optical 
         Instrumentation Engineers Recent Advances in Sensors, Radiometers, 
         and Data Processing for Remote Sensing. 924:96-108. 
      Sellers, P.J. and F.G. Hall. 1989. FIFE-89 Experiment Plan. GSFC/NASA, 
         Greenbelt, MD 20771. 
      Sellers, P.J., F.G. Hall, D.E. Strebel, R.D. Kelly, S.B. Verma, B.L. 
         Markham, B.L. Blad, D.S. Schimel, J.R. Wang, and E. Kanemasu. 1990. 
         FIFE Interim Report. GSFC/NASA, Greenbelt, MD 20771. 
      Walthall, C.L., 1989. The FIFE Helicopter Mission: Summary. Laboratory 
         for Global Remote Sensing Studies. Univ. of Maryland. College Park, 
         MD.
      Walthall, C.L. and E.M. Middleton. 1992. Assessing spatial and spectral 
         variations in grasslands with the use of a helicopter platform. J. 
         Geophys. Res. FIFE issue. (in press).
      Williams, D.L., C.L. Walthall and S.N. Goward. 1984. Collection of in-
         situ forest canopy spectra using a helicopter: A discussion of 
         methodology and preliminary results. Proced. of 1984 Symp. on Machine 
         Processing of Remotely Sensed Data. Purdue Univ. West Lafayette 
         Indiana. p. 94-106.
     
12.3  Archive/DBMS Usage Documentation.  
 
      The Collected Data of the First ISLSCP Field Experiment is archived at
      the EOS Distributed Active Archive Center (DAAC) at Oak Ridge National
      Laboratory (ORNL), Oak Ridge, Tennessee (Section 13 below).  
      Documentation about using the archive and/or online access to the data 
      at the ORNL DAAC is not available at this revision.

                             13.  DATA ACCESS

13.1  Contacts for Archive/Data Access Information. 

      ORNL DAAC User Services
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      (615) 241-3952

13.2  Archive Identification. 

      EOSDIS Distributed Active Archive Center
      P.O. Box 2008
      Mail Stop 6490
      Oak Ridge National Laboratory
      Oak Ridge, TN 37831-6490
      USA

      Telephone:       (615) 241-3952
      FAX:             (615) 574-4665
      Internet Email:   ornldaac@onrl.gov

13.3  Procedures for Obtaining Data.

      Users may place requests by letter, telephone, electronic mail, FAX, or 
      personal visit. 

13.4  ORNL DAAC Status/Plans. 

      FIFE data will be available from the ORNL DAAC.  Please contact the 
      ORNL DAAC User Services Office for the most current information about 
      these data.
 
                   14.  OUTPUT PRODUCTS AND AVAILABILITY 
 
14.1  Tape Products.  
 
      Video tapes of the flights are available from the ORNL DAAC. 
 
14.2  Film Products.  
 
      35 mm film products from some of the flights in 1987 are available 
      from the ORNL DAAC. 
 
14.3  Other Products.  
 
      Surface Reflectance Measured with a Helicopter-borne MMR data are 
      available on FIFE CD-ROM Volume 1. 
 
                       15.  GLOSSARY OF ACRONYMS

AMS               Automatic Meteorological Station
CD-ROM            Compact Disk - Read Only Memory
DAAC              Distributed Active Archive Center
EOSDIS            Earth Observing System Data and Information System
FIFE              First ISLSCP Field Experiment
FIS               FIFE Information System
IFC               Intensive Field Campaign
IFOV              Instantaneous Field-of-View
ISLSCP            International Satellite Land Surface Climatology Project
Mbps              Megabyte per second
MMR               Modular Multiband Radiometer
ORNL              Oak Ridge National Laboratory
WAB               Wind Aligned Blob
UTM               Universal Transverse Mercator